CLOCK

                                     Version 3.44



                            CLOCK is a shareware program.
                     See Appendix A for registration information.
                          $10 (or $25 for full source code)
                                   Ronald Q. Smith
                                  11 Black Oak Road
                              North Oaks, MN 55127-6204





                       (c) Copyright 1991-1993 Ronald Q. Smith































          CLOCK Version 3.44                                  March 9, 1993


                                       CONTENTS


          1  INTRODUCTION . . . . . . . . . . . . . . . . . . . . . . .   1

          1  CLOCK.SYS - Replacement Device Driver  . . . . . . . . . .   3
               1.1  Unique Clock Hardware Support . . . . . . . . . . .   3
               1.2  Installing CLOCK.SYS  . . . . . . . . . . . . . . .   4
               1.3  Clock Type  . . . . . . . . . . . . . . . . . . . .   8
               1.4  Examples  . . . . . . . . . . . . . . . . . . . . .  11
               1.5  Future Enhancements . . . . . . . . . . . . . . . .  11

          2  CLK.EXE - Clock Control Program  . . . . . . . . . . . . .  12
               2.1  CLK Command . . . . . . . . . . . . . . . . . . . .  12
               2.2  Format of TZ= Function  . . . . . . . . . . . . . .  24
               2.3  Using CLK . . . . . . . . . . . . . . . . . . . . .  27
               2.4  Examples  . . . . . . . . . . . . . . . . . . . . .  30
               2.5  Errors  . . . . . . . . . . . . . . . . . . . . . .  31
               2.6  Future Enhancements . . . . . . . . . . . . . . . .  31

          3  CLKDEMO.EXE  . . . . . . . . . . . . . . . . . . . . . . .  32
               3.1  CLKDEMO Command Line  . . . . . . . . . . . . . . .  32

          4  IOCTL - API TO CLOCK.SYS . . . . . . . . . . . . . . . . .  33
               4.1  Data Structures . . . . . . . . . . . . . . . . . .  33
               4.2  clksta  . . . . . . . . . . . . . . . . . . . . . .  36
               4.3  setpw . . . . . . . . . . . . . . . . . . . . . . .  39
               4.4  connec  . . . . . . . . . . . . . . . . . . . . . .  40
               4.5  newpw . . . . . . . . . . . . . . . . . . . . . . .  42
               4.6  rstrct  . . . . . . . . . . . . . . . . . . . . . .  43
               4.7  stmode  . . . . . . . . . . . . . . . . . . . . . .  46
               4.8  stzone  . . . . . . . . . . . . . . . . . . . . . .  47
               4.9  tdisp . . . . . . . . . . . . . . . . . . . . . . .  50

          5  CLOCK.SYS - ASSEMBLY LANGUAGE API  . . . . . . . . . . . .  54
               5.1  Opening the CLOCK$ Device . . . . . . . . . . . . .  54
               5.2  Sending New Values to CLOCK.SYS . . . . . . . . . .  54
               5.3  Getting Current Status of CLOCK.SYS . . . . . . . .  56

          APPENDIX A:  DEFINITION OF SHAREWARE  . . . . . . . . . . . .  57

          APPENDIX B:  CLOCK TYPES  . . . . . . . . . . . . . . . . . .  59
               B.1  Type 0 - PC/AT  . . . . . . . . . . . . . . . . . .  59
               B.2  Type 1 - Zenith Z-18x portables, Supersport 20  . .  60
               B.3  Type 2 - Various Zenith Data System PCs.  . . . . .  60
               B.4  Type 3 - Memory-Mapped Clocks . . . . . . . . . . .  61
               B.5  Type 4 - Direct Register I/O Bus Clock  . . . . . .  62
               B.6  Type 5 - Mitsubishi 8088 PCs  . . . . . . . . . . .  63


                                          ii












          CLOCK Version 3.44                                  March 9, 1993


               B.7  Type 6 - Indirect Register I/O Bus Clock  . . . . .  65
               B.8  Type 7 - Complex I/O Bus Clock  . . . . . . . . . .  66
               B.9  Type 8 - Generic I/O Bus Clock  . . . . . . . . . .  67
               B.10 Type 9 - Quadram I/O Bus Clock  . . . . . . . . . .  67
               B.11 Type A - AT&T 6300, 6300 PLUS, 6300 WGS . . . . . .  68
               B.12 Type B - Hyundai 8088 clock . . . . . . . . . . . .  69

          APPENDIX C:  REVISION HISTORY . . . . . . . . . . . . . . . .  70










































                                         iii












          CLOCK Version 3.44                                  March 9, 1993


          1  INTRODUCTION

          CLOCK consists  of two programs  that give  you complete  control
          over the operation of your calendar (battery-protected) clock and
          your DOS/BIOS internal  timer.  The normal DOS  mode of operation
          is  to read the calendar  clock when you boot  the system and set
          the internal timer.  Thereafter all read operations refer only to
          the internal timer  while time setting  operations write to  both
          clocks.  In levels of DOS prior to 3.3,  even time setting opera-
          tions only  wrote to  the internal  timer.  In  order to  set the
          calendar clock you had to run the SETUP program.

          Some of the drawbacks  to the standard  DOS clock operation  that
          the CLOCK programs address are:

               ù    There  is no  provision  to switch  time zones  without
                    resetting the system time.

               ù    DOS does not handle automatic  changes between daylight
                    savings time and standard time.

               ù    The DOS/BIOS internal timer  often drifts quite rapidly
                    away  from the  time  maintained by  the more  accurate
                    calendar clock.

               ù    Even  the calendar  clock drifts  slowly away  from the
                    accurate time.   DOS  provides no way  to automatically
                    adjust for that drift.

               ù    If your  battery is failing  or some other  hardware or
                    software problem  messes up  the time in  your calendar
                    clock, there is no way to detect that except by manual-
                    ly displaying the time and checking it.

               ù    If you have to run a program that occasionally  changes
                    the time incorrectly, there  is no way to protect  your
                    clock  from those  changes.   You  can  also have  this
                    problem  if  you are  a parent  whose children  set the
                    clock when you don't want them to, an  instructor whose
                    students  reset the time, or an expert young user whose
                    parents mess up your clock.

               ù    If you need to experiment with special  times and dates
                    but don't want to have to reset your clock  afterwards,
                    DOS has no mechanism to help.  In order to test end-of-
                    month processing for your  application, you have to set
                    the date  and time,  run your tests,  and then  set the
                    time and date back.


                                          1












          CLOCK Version 3.44                                  March 9, 1993


               ù    The standard DOS and BIOS software on some PCs can miss
                    the change to  a new day  when the PC  is left on  over
                    midnight.

               ù    Your clock might  not handle automatic changes to a new
                    year or may not understand leap years.

               ù    You may have an  older PC from  before the PC/AT  clock
                    standardization and your vendor no longer releases  new
                    versions of DOS for that PC.   You are stuck on DOS 3.2
                    or earlier or you have to give up your calendar clock.


          If any of  those circumstances cause problems for  you, CLOCK can
          help.  The  two primary programs are  CLOCK.SYS and CLK.EXE.   In
          addition, if you are a software developer, CLKDEMO is provided in
          source code to show you how to  program the extended clock opera-
          tions into your own applications.


               CLOCK.SYS is a clock device driver (CLOCK$ device).  It
               replaces the DOS internal clock driver.  CLOCK.SYS pro-
               vides  for automatic  time  zone conversion.   It  also
               allows you to periodically or continuously get the time
               from the  calendar clock.   This can  totally eliminate
               problems with missing  day changes and realtime  clocks
               that are  inaccurate.   CLOCK.SYS provides support  for
               many  types of  calendar clocks  including many  of the
               original add-in clocks of the 8088 era.  If your  clock
               is not currently supported, I want to hear from you.  I
               will be happy to add it to the software.
              
               CLK.EXE  is a  program  that allows  you to  separately
               control your  DOS/BIOS internal clock  and battery-pro-
               tected calendar clock.  Most importantly,  CLK.EXE will
               handle time zones and will automatically switch between
               standard and  daylight savings time  for you.   It also
               supports automatic adjustment for calendar clock drift,
               checks  for incorrect  or unlikely  times, and  can re-
               strict time changes.

               CLKDEMO.EXE is a small part of CLK.EXE that is provided
               in source code (C  language) form so  that you can  see
               how to add clock control to your own applications.






                                          2












          CLOCK Version 3.44                                  March 9, 1993


          1  CLOCK.SYS - Replacement Device Driver

          CLOCK.SYS is  a device driver  that replaces the  built-in CLOCK$
          device driver in DOS levels 2.1  and above.  CLOCK.SYS adds  many
          functions not provided  in the standard DOS CLOCK$ device driver.
          You won't see mention of the DOS CLOCK$ device driver in your DOS
          user's guides.   You will see a  very small mention of  it in the
          system's  programmers reference  manuals if  you are  an assembly
          language developer.   It  is there and  DOS was  specifically de-
          signed to  let you replace  it with one  of your own  even if the
          manual doesn't tell you that.


          1.1  Unique Clock Hardware Support

          CLOCK.SYS  was originally  written  especially for  those  people
          whose  clocks  are not  supported  by new  levels of  DOS.   This
          usually occurs  because your vendor stopped  providing new levels
          of DOS adapted  for your computer model.  Before  the days of the
          PC/AT and standard clock interfaces, DOS was usually sold direct-
          ly to  hardware vendors  who customized it  for their  system and
          delivered it  with the system.   In  addition, many of  the early
          clocks were provided by third-party, after-market vendors who had
          no idea what system it would be used in.  Since those systems and
          clocks have been  out of production for a long  time, most of the
          vendors have stopped  providing upgrades.  Yet most  of those PCs
          will happily run  DOS 3.3 or above and especially  DOS 5.0 except
          that you have to give up your calendar clock.

          CLOCK.SYS supports a wide variety of different clock hardware and
          BIOS interfaces.  As far as possible, CLOCK.SYS will automatical-
          ly  determine what  clock interface  to  use.   If the  automatic
          determination  does  not  work  for your  system,  you  may  tell
          CLOCK.SYS specifically what interface type to use.   CLOCK.SYS is
          also required  by anyone  who  wants to  use CLK  as it  provides
          functions not  provided by the  normal DOS CLOCK$  device driver.
          CLOCK.SYS is fully  compatible with the DOS device  driver on all
          modern PCs and many older ones.

          If your PC clock is not currently supported but you would like to
          remove the  restrictions on  what versions  of DOS  you can  use,
          please  contact me by mail or on  CompuServe.  I will be happy to
          add support for your  clock.  I will need some technical informa-
          tion and help from you in getting it to work so I will give you a
          $0 usage license for your help.   Please see section 1.3 for  the
          current list of supported clocks and Appendix B for a description
          of those clocks.



                                          3












          CLOCK Version 3.44                                  March 9, 1993


          1.2  Installing CLOCK.SYS

          To install the  device driver include the following  line in your
          CONFIG.SYS file.

          Syntax    device=[d:][path\]clock.sys [type][,io_addr] [/N]

                                          or

                    device=[d:][path\]clock.sys 3[,segment[,write0,
                         write1,read]] [/N]

                                          or

                    device=[d:][path\]clock.sys A[,base_year] [/N]


          Parameters     d:
                         Identifies the drive containing CLOCK.SYS.   If d:
                         is not provided, the boot drive is assumed.

                    path\
                         Specifies the directory containing  CLOCK.SYS.  If
                         path\ is not given, the root directory is assumed.

                    CLOCK.SYS
                         Is the name of the CLOCK.SYS file.  You may change
                         the name  if you  wish, but you  must not  use the
                         .COM or .EXE extensions.

                    type
                         Is the kind of calendar clock on your system.   If
                         you do not provide type, CLOCK.SYS will probe your
                         system   to  determine   which  clock   you  have.
                         CLOCK.SYS is  usually able  to detect the  type of
                         calendar clock  without trouble.  It  is possible,
                         however, that you have some other hardware in your
                         system that  could fool CLOCK.SYS.   For that rea-
                         son, you might need to provide the type  of clock.
                         See section  1.3 and Appendix B  for more informa-
                         tion about the clock types.

                    io_addr
                         Is  the I/O  bus address  of your  clock hardware.
                         Some  of the  types of  clocks that  are supported
                         were set  up at a  wide variety of  I/O addresses.
                         CLOCK.SYS  probes  all the  commonly used  I/O ad-
                         dresses for  these clocks.   However, you  or your


                                          4












          CLOCK Version 3.44                                  March 9, 1993


                         vendor may have installed your clock at an address
                         that CLOCK.SYS  doesn't know about.   By providing
                         the  address, you  make it  much more  likely that
                         CLOCK.SYS will correctly find your clock.  Even if
                         you  don't know what type  of clock you have, pro-
                         viding the I/O address may be enough for CLOCK.SYS
                         to determine which one it is.  io_addr is current-
                         ly  used with clock  types 4, 6,  7, 8, 9,  and B.
                         Normally this is 240, 2C0, or 340 for types 4,  6,
                         and 7.  It is 210 or 310 for type 9.  And it is E0
                         for type B.  All numbers are in hex.  For example,
                         an AST Research clock might be:

                         device=[d:][path\]clock.sys 4,2C0

                         If  you do  not  specify the  "io_addr", CLOCK.SYS
                         will try to determine the correct address by prob-
                         ing.

                         If you are sure that you have an I/O clock but you
                         are not sure  which one it is, specify  type 8 and
                         supply the io_addr  if possible.  Type 8  does not
                         represent a specific clock.  Rather it attempts to
                         determine whether your clock is a type 4, 6, 7, 9,
                         or  B using a  sequence of tests  similar to those
                         used by some  of the I/O  clock vendors to  figure
                         out what kind of clock you have.

                    If you  have a  memory mapped  clock, you  may use  the
                    second format to specify the addresses to be used.   If
                    you don't know the addresses, CLOCK.SYS will attempt to
                    determine them by probing.

                    segment
                         Is  the base  address  used to  access the  clock.
                         Usually your  documentation will give  the segment
                         address as four  hex digits such as  FE00 or F000.
                         Some addresses may be less than four digits (e.g.,
                         70).   Other  documentation may show  addresses in
                         the  form aaaa:bbbb.    In this  case the  segment
                         address is  the aaaa  value.  Sometimes  these ad-
                         dresses  are written as  0xaaaa, aaaah,  aaaaH, or
                         0Xaaaa.  In all of these forms there is a 2- to 4-
                         digit hex number that is the segment address.

                    write0
                         Is  the offset used to write 0 bits.  It must also
                         be a hex  address and may be 0,  F002, or anything


                                          5












          CLOCK Version 3.44                                  March 9, 1993


                         else the vendor chose.  If the addresses are given
                         in the aaaa:bbbb form,  use the bbbb.   With these
                         clocks, you  read and  write the clock  by reading
                         the  memory addresses.   For example,  reading ad-
                         dress segment:write0 results in writing a zero bit
                         to the  clock.  Writing an  appropriate length se-
                         quence of zero and one bits sets the clock.

                    write1
                         Is the offset used to write 1 bits.

                    read
                         Is the offset used to read bits.

                         If your  documentation gives  the segment  address
                         but isn't  clear about the  offsets, just  specify
                         the  segment address  and CLOCK.SYS  will try  all
                         offset combinations that it knows about.

                         If you specify one of the offsets, you must speci-
                         fy them all.

                    The third format is used with the AT&T 6300 clocks.

                    base_year
                         Is used for the AT&T 6300 clocks (type=A).   Dates
                         prior to that year or more than 7 years after that
                         year will  not be handled  correctly.  If  no base
                         year is specified, 1992  will be used.   Dates be-
                         tween the start of  the base year  and the end  of
                         the seventh year later are handled (e.g., 1992-1-1
                         until 1999-12-31).

                    /N
                         Indicates that  you do  not want CLOCK.SYS  to at-
                         tempt  to detect  missed date  changes.   Normally
                         CLOCK.SYS  will  try to  detect  when  a date  has
                         changed that was not  reported by the BIOS.   This
                         usually happens  when a  program  is running  past
                         midnight and calls the BIOS to read the time rath-
                         er than calling  DOS.  That program sees the date-
                         change  indication   from   the   BIOS   and   DOS
                         (CLOCK.SYS) never gets a chance to change the day.
                         However,  the logic  that  CLOCK.SYS uses  can  be
                         fooled by  programs that change the  time with di-
                         rect calls  on the BIOS  and may advance  the date
                         incorrectly.  This is very rare,  but if your date



                                          6












          CLOCK Version 3.44                                  March 9, 1993


                         advances unexpectedly or by more than one day, you
                         may want to use this option.

          Notes     DOS interfaces                    ______________
                    All DOS  DATE and  TIME commands and  all DOS  date and
                    time system calls will  operate with no apparent change
                    to you  or any program.   Unless you  have used  CLK to
                    change the time handling,  your clocks are handled just
                    as DOS would handle them.

                    Dates and leap years                    ____________________
                    CLOCK.SYS supports all valid DOS dates from 1980-1-1 to
                    2079-12-31.   It supports dates to  2099-12-31 for many
                    of the clocks.  CLOCK.SYS also handles year changes and
                    leap years automatically for  clock types that don't do
                    it themselves.

                    Time zones and daylight savings time                    ____________________________________
                    CLOCK.SYS in conjunction  with CLK.EXE provides support
                    for multiple  time zones  and automatic conversion  be-
                    tween daylight  savings time  and standard time  at the
                    appropriate  times  of  the  year.   For  this  reason,
                    CLOCK.SYS  may be  of great  use  to you  even if  your
                    version of DOS already supports your clock correctly.

                    Clock synchronization                    _____________________
                    Normally,  CLOCK.SYS operates  identically  to the  DOS
                    CLOCK$ device driver.   At boot it  sets the DOS  clock
                    from the calendar clock.  Any time you change the  date
                    or time it writes to both clocks.

                    With CLK.EXE you  have several other  options.  If  you
                    have  specified a  time zone  and offset  with CLK.EXE,
                    CLOCK.SYS will  adjust all times read  from and written
                    to the calendar clock by the time zone offset.  You can
                    also set it to read the calendar clock rather than  the
                    DOS  clock for  some  or all  time  requests to  ensure
                    continued synchronization  of the two clocks.   You can
                    also  totally separate the two clocks  so that DOS time
                    and  date functions  only read  and write  the DOS/BIOS
                    internal clock.

                    Time setting limits                    ___________________
                    CLK.EXE can tell CLOCK.SYS to apply limits to the  time
                    changes  that it  will  accept or  stop accepting  time
                    changes at all.  For example, you can tell CLOCK.SYS to
                    accept no  changes that  would set the  clock backward.
                    You can also inhibit all changes.


                                          7












          CLOCK Version 3.44                                  March 9, 1993


                    Password Protection                    ___________________
                    CLK.EXE  can establish  a  password to  control  future
                    changes to the time  zone, connection, and time setting
                    limits.   Once  the password  is  set, all  attempts to
                    change those  values will simply be  ignored unless the
                    correct  password  is supplied.    You  may change  the
                    daylight  versus standard time  flag and the continuous
                    time display without knowing the password.

                    Continuous Time Display                    _______________________
                    CLK.EXE can tell CLOCK.SYS to display the time continu-
                    ously at any position on your screen.  You specify  the
                    cursor coordinates, display  attributes, and 12-hour or
                    24-hour mode  and  CLOCK.SYS will  update  the  display
                    every second.

                    Saving Settings Across Boots                    ____________________________
                    With  CLK.EXE  you  can   save  the  current  state  of
                    CLOCK.SYS  at any time  in a form  that can be  used on
                    your next boot.  You can set up your time zone, setting
                    limits, connection mode, continuous display, and  pass-
                    word and then save  a new version  of CLOCK.SYS.   This
                    new  version  will  automatically  start  running  with
                    without having to scan for your clock type and with all
                    your standard state automatically in effect.


          1.3  Clock Type

          There  are almost as many different  implementations of PC clocks
          as there are different types of PCs.  Until the PC/AT came along,
          there  was no standard for  battery-protected clocks, and each PC
          and add-in vendor was likely to implement them differently.  With
          the PC/AT a standard and documented interface for such clocks was
          provided.   Since that  time, most  PCs have  followed the  PC/AT
          standard.   It is  earlier PCs, especially  8088 PCs,  that don't
          follow the standard.  Since these  are early PCs, there is also a
          high probability that the vendor is  no longer providing modified
          versions of  DOS with  built-in support for  their clocks.   Most
          add-in clock vendors never did provide a modified DOS and you had
          to manage  your clock  with utility  programs.   This leaves  you
          faced with the choice  between staying with  an early version  of
          DOS or giving up your clock.

          CLOCK.SYS is  intended to  free you from  those limitations.   It
          will work with  all versions of  DOS from 2.10  through 5.00  and
          undoubtedly beyond.  It  also attempts to automatically determine
          what kind of clock you have  and install the correct support  for


                                          8












          CLOCK Version 3.44                                  March 9, 1993


          it.  However, there are often enough differences between PCs that
          the automatic determination  may not  find anything  or may  even
          make  the wrong choice.   To give you more  control of the situa-
          tion, you may specify the clock interface by giving an  interface
          number.

          It will  not always be  easy to decide  what interface  number to
          use.  You will  at least need  some technical information on  how
          your  clock works or on  the BIOS calls used  to control the bat-
          tery-protected clock.  If you find a description below that seems
          to  match, give it a try.  The  most that should go wrong is that
          your time and date will be set incorrectly,  but then they proba-
          bly weren't working anyhow.

          If you aren't sure what interface to use or if you are  sure that
          your clock is not  supported, LET ME KNOW.  I WOULD LIKE TO HELP.
          You can help me make CLOCK.SYS better for everyone.  I would even
          like to  hear from you  if CLOCK.SYS  did work  for you and  your
          clock isn't  currently listed.   I would like  to be able  to add
          your PC manufacturer and  model number to  the supported list  so
          others know what to use.  If CLOCK.SYS did not work for you, I am
          interested in  making the changes so  that it does work.   If you
          can  provide me with the  necessary technical information, I will
          make the changes.

          Usually,  a technical  reference  manual with  hardware and  BIOS
          interfaces is the best source.  Even if you  don't have one, your
          original  hardware  vendor may  be  willing  to send  you  enough
          information  to allow  you  to program  the clock.   If  all else
          fails, we may even  be able to use an old copy of  DOS or a clock
          setting utility to  figure out how it works.   Before we do that,
          check  your license to be sure that it is not forbidden to disas-
          semble the software to see how the clock works.  
          The following table shows the  systems that have been  determined
          to  work with existing  clock types.   If your  system is  in the
          list,  try the clock type indicated.  If not, look through Appen-
          dix B which tells you about  the characteristics of each type  of
          clock and see if anything seems to match your system type.












                                          9












          CLOCK Version 3.44                                  March 9, 1993


                   ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÑÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
                   º     SYSTEM                ³  BLOCK TYPE              º
                   ÇÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¶
                   º     Amstrad PC1521DD      ³  0                       º
                   ÇÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¶
                   º     AST Research          ³  8 (4, 6, or 7) See dis- º
                   º       Six-Pack            ³  cussion above and in    º
                   º       I/O Plus            ³  Appendix B              º
                   º       etc.                ³                          º
                   ÇÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¶
                   º     AT&T 6300             ³  A                       º
                   ÇÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¶
                   º     Hyundai 8088          ³  B                       º
                   ÇÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¶
                   º     IBM PC/AT and most    ³  0                       º
                   º     PCs since then.       ³                          º
                   ÇÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¶
                   º     Leading Edge Model D  ³  5                       º
                   ÇÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¶
                   º     Mitsubishi 8088       ³  5                       º
                   ÇÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¶
                   º     Quadram Corp.         ³  9                       º
                   º       QuadCard            ³                          º
                   º       QuadCard II         ³                          º
                   º       QuadCard 512+       ³                          º
                   ÇÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¶
                   º     SMT No-Slot Clock     ³  3                       º
                   ÇÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¶
                   º     Sperry PC-1           ³  5                       º
                   ÇÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¶
                   º     Sperry PC/HT          ³  5                       º
                   ÇÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¶
                   º     Tandy 1200HD          ³  4                       º
                   ÇÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¶
                   º     Vendex Turbo-888-XT   ³  4                       º
                   ÇÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¶
                   º     Zenith Supersport 20  ³  1                       º
                   ÇÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¶
                   º     Zenith Z-18x          ³  1                       º
                   ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÏÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼










                                          10












          CLOCK Version 3.44                                  March 9, 1993


          1.4  Examples

          For almost everyone, the only format you ever need to use is:
               device=[d:][path\]clock.sys

          If CLOCK.SYS is in  the root directory of your boot  device, this
          is:
               device=clock.sys

          CLOCK.SYS will  quite happily load  into the upper  memory blocks
          (UMBs)  provided by DOS 5.0 and by other software.  With DOS 5.0,
          you might use:
               devicehigh=clock.sys

          With some memory managers you can even load CLOCK.SYS into  upper
          memory blocks on earlier levels of  DOS.  See your manual for the
          commands to use.  Some of these  memory managers will create UMBs
          on 8088  and 80286 systems.   CLOCK.SYS  loads and  runs high  on
          those systems as well.

          With a memory mapped clock that uses an address combination  that
          CLOCK.SYS doesn't search automatically  and with CLOCK.SYS stored
          in the C:\UTILITY directory, you might use:
               device=c:\utility\clock.sys 3,ffff,f000,f004,f008
          Please note that the memory addresses chosen for this example are
          not likely to match those of your clock and you should substitute
          the addresses appropriate to your clock.

          If you have an  I/O clock with the same interface  as the Quadram
          Corp. clock but a different I/O address, you might use:
               device=clock.sys 9,3fc
          if your I/O base address were 3fc.

          If you have one of the AT&T 6300 system types and you occasional-
          ly need to set your clock prior to 1992-1-1, you might use:
               device=clock.sys a,1988

          1.5  Future Enhancements

          Of course,  I hope  to add  more clocks as  people ask  for them.
          Those old PCs are still good for a lot of what we do even if they
          are sometimes relegated to a secondary status.

          There are no other outstanding enhancements currently planned for
          CLOCK.SYS.





                                          11












          CLOCK Version 3.44                                  March 9, 1993


          2  CLK.EXE - Clock Control Program

          CLK gives you complete control over the operation of the calendar
          clock and  DOS/BIOS clock.   You can  operate them  separately or
          together.  You  can establish time  zones, daylight savings  time
          rules, automatic adjustment, synchronization rules, and more.


          2.1  CLK Command

          Syntax    clk [function] [function ...] [/I[file]] [/?]

                              or in full form

                    clk [A=ñsss.cc] [C=A|D|R|W] [D=[N][x,y,a[,12|,24]]
                         [L=...] [M=...] [R=A|B-hh:mm:ss|F+hh:mm:ss|N|R]
                         [S=C|D]    [TZ=...]    [W=-back,+forward]     [/B]
                         [/I[file][,C]]  [/M[file][,C]] [/P[N]]  [/S[file]]
                         [/?]

          Parameters     function
                         There  are many  functions that  may be  used with
                         CLK.EXE and  they are discussed  in the  following
                         paragraphs.   You may use any  number of functions
                         on  a single command  line and  they will  be pro-
                         cessed  in  the order  in  which  you enter  them.
                         However, if  any error is discovered in any of the
                         functions, none of them are processed.  Thus, 
                              clk c=r tz=:est
                         is the same as the two command lines:
                              clk c=r
                              clk tz=:est
                         except that an error in either of the functions in
                         the first  example cause  the whole command  to be
                         ignored.

                         The case (upper  or lower) of any  of the function
                         names, options,  or values  is ignored  except for
                         the TZ  function's time  zone names.   Even there,
                         the case is not used.  It is simply preserved  for
                         later display.

                         You can display a  help message about any function
                         or option  by immediately  following the  function
                         letter or  option letter with ?.  Thus M? displays
                         help about  the M= function and  /I? displays help
                         about the I  option.  /?  displays a help  message
                         about the CLK command line.


                                          12












          CLOCK Version 3.44                                  March 9, 1993


                    none
                         If no function or option is provided, CLK displays
                         the current  state of  operation of  CLOCK.SYS and
                         the current time from  both the calendar clock and
                         the DOS/BIOS clock.

                         If you have used CLK to set a time  zone (TZ func-
                         tion), the current time zone name and offset value
                         are  displayed.     These  values   are  saved  in
                         CLOCK.SYS so that they may  be used for time func-
                         tions.

                         The connection state of the clocks (C function) is
                         displayed as is the current restrictions  (R func-
                         tion) on clock changes.

                         All uses  of CLK  (except  errors and  /?) end  by
                         displaying  the same information.  You always know
                         the state of your two clocks after execution.

                    A=ñsss.cc
                         The Adjust function is used to set a daily adjust-
                         ment factor in seconds and 100ths of seconds.

                         This function assumes that you have some knowledge
                         of the  rate at  which your calendar  clock drifts
                         with respect to "real"  time.  Presumably you have
                         periodically  set your clock  using a program that
                         calls the Naval Observatory  or NIST and noted the
                         difference  over time.    Some such  programs will
                         help you to calculate the drift rate.  You can get
                         a very good adjustment from a decent quartz watch.

                         The value may be a positive or  negative number in
                         the range  -326.99 to +326.99 seconds  per day but
                         reasonable values are likely to be a fraction of a
                         second.

                         The first time  you use A=, your clock  is not ad-
                         justed.  The  value of A and the  current time are
                         saved in  a file  for later  use.   Later you  can
                         choose to run CLK with the /I option to invoke the
                         file.  The elapsed  time since the last adjustment
                         (or the time you last changed A) in days and frac-
                         tions is multiplied by  A to calculate any adjust-
                         ment that needs to be applied.  Only whole seconds
                         of adjustment are applied.



                                          13












          CLOCK Version 3.44                                  March 9, 1993


                         The A=  function only sets the  adjustment factor.
                         The  actual adjustment  is carried  out by  the L=
                         function.   You don't have  to enter the  L= func-
                         tion.  CLK will do that for you the first time you
                         use A=  and will keep  it up  to date as  it later
                         makes adjustments.

                         NOTE:  Do not  use the A=  function with the  AT&T
                         6300 clocks  (Type A) or the  Quadram clocks (Type
                         9).  They only  permit the time to  be set to  the
                         nearest minute.

                    C=A
                         Connects the  two clocks for All  operations.  All
                         read operations go directly to the calendar clock.
                         The calendard clock is  read, the time is adjusted
                         for any time zone offset, and the adjusted time is
                         written to the DOS clock and returned to the call-
                         er.   With this function, your  calendar clock es-
                         sentially becomes  the only  clock.  However,  the
                         DOS clock is set each time so that any application
                         reading the clock  directly (without going through
                         DOS) sees the  same time that DOS reports.   It is
                         unwise to use this function  if your clock is slow
                         (some I/O clocks and some memory-mapped clocks) or
                         if it  only increments  in units of  seconds (most
                         clocks).  Any time zone offset is applied to reads
                         and writes.

                    C=D
                         Disconnects  the two  clocks.   Any change  of the
                         date  and time  will  affect the  DOS clock  only.
                         Reads also use the DOS  clock only.  This function
                         allows you  to perform  any operation on  the time
                         without affecting  your  calendar clock.    It  is
                         useful for dealing with ill-behaved programs  that
                         need to  change the time and  for testing programs
                         at different dates and  times.  You can  later use
                         the C=R, C=A,  or other functions  to re-establish
                         the  value in  your  DOS clock  from the  calendar
                         clock.

                    C=R
                         Connects the  two clocks for  writing and periodic
                         Reading.   This  function  may be  used when  your
                         clocks  drift slowly  with respect to  each other.
                         If the time has  not been read  for about 10  sec-
                         onds, the calendar clock will be read, adjusted by


                                          14












          CLOCK Version 3.44                                  March 9, 1993


                         the offset  if any, and the  adjusted time written
                         to the DOS clock and returned to the caller.  This
                         periodic Read  assures you  that the  clocks never
                         get  very  far out  of  synchronization with  each
                         other.    Some calendar  clocks take  a relatively
                         long time  to read and  most don't have  100ths of
                         seconds.  By only  reading the calendar clock when
                         no other time request has occurred in the last  10
                         seconds,  we minimize  both  the overhead  and any
                         visibility of time jumps.

                    C=W
                         Connects  the two clocks for Writing.  This is the
                         default  mode of  operation and  is the  same mode
                         that the DOS CLOCK$  device driver supports as its
                         only mode.  Reading the time is served by the  DOS
                         clock.  Writing  the time sets both clocks.   If a
                         time zone  offset has  previously been  specified,
                         all writes to  the clock are adjusted  so that the
                         calendar  clock remains  on  the base  time.   For
                         example,  if the calendar clock is  set to UTC and
                         you specify that you want to use CST which has  an
                         offset of 6 hours from UTC, all writes of the time
                         will have 6 hours added  to them before writing to
                         the  calendar clock.   Thus the DOS  clock and the
                         calendar clock remain at a constant time offset.

                    D=N
                         The D=  function controls  a continuous  time dis-
                         play.  D=N turns off the continuous display.

                    D=x,y,a[,12|,24]
                         Starts a continuous  time display at cursor  posi-
                         tion x,y  with display attribute a.   Cursor posi-
                         tion 0,0  is the upper left corner  of the screen.
                         The typical screen format  runs from 0,0 to 79,24.
                         The display  attribute is a  two-digit hex  number
                         that gives the  background and foreground  colors.
                         The high-order digit is the background color (0 to
                         7 usually)  and the  low-order digit is  the fore-
                         ground  or character color (0  to F).  The default
                         display is  a 24-hour clock in  the form HH:MM:SS.
                         If you add  the ",12", the display will  use a 12-
                         hour clock.  No AM or PM indication is given.

                         D=72,24,79,12  will place the display at the right
                         edge of the  last line of most screens.   The text



                                          15












          CLOCK Version 3.44                                  March 9, 1993


                         will be in  bright blue on a  white background and
                         the hours will run from 12 through 11.

                         The  D= functions  should not  be  used if  CLK is
                         executed from within  Windows.  If  you try to  do
                         so,  you will  received  an error  message.   This
                         avoids  a hung  system  which would  occur if  CLK
                         didn't check.

                    L=YYYY-MM-DD,hh:mm:ss,ñsss.cc

                         The L= function is not intended to be used on  the
                         command line, but will  be accepted if you provide
                         it.  The  L= function is  normally created by  CLK
                         and saved  in the  CLK.INI file  for later  use in
                         processing adjustments.  The  date and time of the
                         last adjustment (or the  most recent time you gave
                         an A= function on  the command line) are given  by
                         the YYYY-MM-DD,hh:mm:ss.   Any non-digit  except a
                         space may  separate the sub-fields.   The date and
                         time  must be followed by a  comma and any adjust-
                         ment remainder.   The  adjustment remainder  is in
                         the same form as the value for the A= function but
                         will usually be a fraction of a second.  It is the
                         adjustment  that was  left over  the last  time an
                         adjustment  was  actually  made  since only  whole
                         seconds of changes are made to the clock.

                         The L= function triggers  an adjustment if needed.
                         Generally,  it will  follow  the A=  function that
                         sets the  adjustment factor.  Both  of these func-
                         tions normally appear in the CLK.INI file.

                         The L= function  may also be used by  itself to do
                         simple arithmetic on  the clocks.   Use it on  the
                         command line with any earlier date and time and an
                         adjustment of  the number of  seconds (positive or
                         negative) that you want  added to the clock.   The
                         change will  be made and the  last adjustment time
                         set to the current time.  For example, 
                              clk l=1990-1-1,0:0:0,-4
                         will subtract 4 seconds from the clocks.

                    M=ñsss.cc,YYYY-MM-DD,hh:mm:ss
                         The M=  function is used to help you calculate the
                         automatic  adjustment A=  value for  your calendar
                         clock.  The M= function is used to enter the manu-
                         al adjustments that you make to the clock in addi-


                                          16












          CLOCK Version 3.44                                  March 9, 1993


                         tion to the automatic adjustments.  The ñsss.cc is
                         the  amount of  manual  adjustment that  you  have
                         made.  This may be adjustments made by setting the
                         clock with the  DOS DATE and TIME commands  or ad-
                         justments  made by  a time  setting program.   The
                         YYYY-MM-DD,hh:mm:ss is  the date and time at which
                         the  adjustment was  made.   It is  very important
                         that the date  and time be  given with respect  to
                         the calendar  clock and not the DOS clock, if dif-
                         ferent.  If  you do not supply the  date and time,
                         the  current  date and  time will  be used.   This
                         should be sufficiently  accurate if you just  com-
                         pleted making the adjustement.

                         The first M= value that you enter is used only  to
                         set a base date and time.  Then as you enter addi-
                         tional values in the  future, CLK will calculate a
                         new value  for the A= function by adding the aver-
                         age manual  adjustment per  day to the  current A=
                         value.  Up to  8 values are  saved in the  CLK.INI
                         file  (or other file that you  specify).  The more
                         values you provide and the longer the time period,
                         the  more accurate  the adjustment  will be.   For
                         example, if you can  only determine the adjustment
                         to the  nearest second  (likely), you may  want to
                         have a week  or more  between manual  adjustments.
                         The only  restriction is  that the first  and last
                         manual adjustement must be within one year of each
                         other.  If  you enter more than 8,  the oldest two
                         adjustement  values are  collapsed  into a  single
                         value.

                         Supplying a new A=  value, presumably based on the
                         calculations from CLK, deletes  all the M=  values
                         from the file.  You may either specify a /I option
                         to specify  the file and read all the functions in
                         the file, a /M option to specify the file and only
                         read the  M= functions, or CLK  will automatically
                         specify the  /M option for  you (but it  will only
                         know to look for CLK.INI in the directory contain-
                         ing CLK.EXE).   You may also edit the M= functions
                         in the file and use  the /M option to force  a re-
                         calculation.

                         When  CLK calculates  a new  adjustment value,  it
                         tries to determine if any of the M= values are out
                         of line  with the  rest of  the values.   It  will
                         ignore, but  provide an  error message, if  any of


                                          17












          CLOCK Version 3.44                                  March 9, 1993


                         the values are  too far away from all  of the oth-
                         ers.  CLK calculates an average and standard devi-
                         ation and  ignores all  values (of  adjustment per
                         day) that are more than 2 standard deviations from
                         the average.

                    R=A
                         The R= function sets restrictions on time changes.
                         R=A inhibits  All time changes.  When this mode is
                         set, all  attempts to change the  time are ignored
                         by  CLOCK.SYS.  This includes time changes attemp-
                         ted by CLK including time adjustments.  See R=N.

                    R=B-hh:mm:ss
                         This function limits the amount of Backward change
                         of the time.   Any change of more  than the speci-
                         fied time is ignored.  The "-" is optional as  are
                         the offset fields.
                              clk r=b
                         inhibits all backward changes.
                              CLK R=B::2
                         only  allows backward  changes of  two seconds  or
                         less This might permit CLK to perform  adjustments
                         but effectively stop other backward changes.

                    R=F+hh:mm:ss
                         This function  limits the amount of Forward change
                         of the time.   Any change of more  than the speci-
                         fied time is ignored.  The "+" is optional as  are
                         the offset fields.
                              CLK R=F+1:00:02
                         limits forward  changes to  1 hour and  2 seconds.
                         The R=B and  R=F limits do not apply  to the auto-
                         matic  conversions between  standard and  daylight
                         savings  time as these  don't actually  change the
                         time.  The R=B and R=F functions are also indepen-
                         dent of the R=A function.

                    R=N
                         This function reverses the R=A function and inhib-
                         its  No clock changes.   The R=A is independent of
                         the R=B and R=F.  You can set backward and forward
                         limits  with R=B and  R=F.  Later  you can inhibit
                         all changes with R=A.  When you do R=N, the previ-
                         ously set R=B and R=F limits again have an effect.





                                          18












          CLOCK Version 3.44                                  March 9, 1993


                    R=R
                         This function Resets the limits established by R=B
                         and R=F.  No limits are in effect  after executing
                         this function.  It has no effect on the R=A mode.

                    S=C
                         Sets  both clocks  to  the current  time from  the
                         calendar clock.   You  can  use this  even if  the
                         clocks  are disconnected  to  make the  DOS  clock
                         equal to the calendar clock.  The time zone offset
                         is set to  00:00:00 and the time zone  name is set
                         to UTC to indicate that both clocks are set to the
                         base time.

                    S=D
                         Sets both clocks to the current time  from the DOS
                         clock.  The value from the DOS clock is written to
                         the calendar clock.   The time zone offset is  set
                         to 00:00:00  and the zone  name is not  changed to
                         indicate that  both clocks  are set to  your local
                         time.

                    TZ=...
                         Sets the DOS clock to the correct local time based
                         on the value of  the expression following the TZ=.
                         This  expression  conforms  exactly  to the  POSIX
                         1003.1 standard  for time zone handling.   CLK as-
                         sumes that  the calendar clock  currently contains
                         UTC  (also known  as GMT,  Greenwich, ZULU,  and Z
                         time).   UTC  ("Universal  Time,  Coordinated"  is
                         usually spoken as "coordinated universal time") is
                         the name of  the international standard  time that
                         is provided by  WWV, WWVH, the Naval  Observatory,
                         and NIST as well as many other services around the
                         world.    Most  Unix(r)  systems  also support  TZ
                         although  many only  partially  support the  POSIX
                         standard.   See  the  notes later  for a  complete
                         description of the TZ= function.

                         You  can  put  the  CLK  TZ=...  command  in  your
                         AUTOEXEC.BAT file.  You should put it prior to any
                         other  statements that may  create or update files
                         or you run the risk  of having confusing times  in
                         your  file  directory (MAKE  could  get especially
                         confused.).   If you provide a  TZ= function, your

                                        ____________________

          Unix is a registered trademark of Unix Systems Laboratories.

                                          19












          CLOCK Version 3.44                                  March 9, 1993


                         system  will automatically  adjust to  the correct
                         time zone every  time you boot.  Note  that no at-
                         tempt is made to change between daylight and stan-
                         dard time  except  when  you  execute  CLK  TZ=...
                         Adjusting on the fly is very dangerous.  Many pro-
                         grams can produce incorrect  results or even  cor-
                         rupt  your data if  time takes a  big step forward
                         and are  even more  likely to do  so if  time runs
                         backward.  See section  ? for a discussion of  the
                         TZ= format.

                    W=-back,+forward
                         The W= function is  used to establish Warning lim-
                         its on  the time.   Each time  the W=  function is
                         processed  (usually from  the  CLK.INI file),  the
                         current time  and the previous  time are compared.
                         If the current time  is outside the -back,+forward
                         range  around the previous time, a warning message
                         is displayed  requiring you to  press a key.   The
                         program will  also exit  with an ERRORLEVEL  of 1.
                         The full form of the W= function is:
                         W=N-days/hh:mm:ss,+days/hh:mm:ss,
                              YYYY-MM-DD,hh:mm:ss

                         The days sub-field is a value from 0 to 250  days.
                         The  days  sub-field combined  with the  time sub-
                         fields gives  the maximum interval around the pre-
                         vious time  within  which the  current  time  must
                         fall.  The previous date and  time follow the sec-
                         ond comma.  For example,
                              clk w=-0/00:00:02,+91
                         will  establish a  range of  minus two  seconds to
                         plus 91 days.   The first time you  use this func-
                         tion nothing will happen  except that CLK will add
                         the current date and time to the command and store
                         it  in the CLK.INI file.  The next time you use if
                         from  the CLK.INI  file  with CLK /I,  the current
                         date  and time  will be  compared to  the previous
                         date and time and the range.  If the current  time
                         is outside  the range, a message  is displayed and
                         CLK pauses.

                         The sign characters and  all of the sub-fields are
                         optional.  Missing sub-fields are treated as zero.
                         The particular separators are not important except
                         for the  commas.   Any non-digit character  can be
                         used for the other separators.   The time and date
                         fields are  appended to  the function by  CLK when


                                          20












          CLOCK Version 3.44                                  March 9, 1993


                         the CLK.INI  file is written and  are the previous
                         time to which the next comparison will be made.  A
                         typical  function might  be W=,31.   This  command
                         will display  a warning  whenever  time has  moved
                         backwards  at all  or has  moved forwards  by more
                         than 31 days since the last time you used CLK  /I.
                         If you use CLK /I (see below) in your AUTOEXEC.BAT
                         file,  this is  very likely  to detect  a miss-set
                         clock or bad clock battery.  Yet it won't generate
                         a  message on  every boot.  You will  only get  an
                         "unnecessary" message  if it has been  more than a
                         month since you last used the PC.

                         If the "N" character (or "n")  appears immediately
                         after the "=", CLK does not pause and wait for you
                         to press a key after printing the warning message.
                         The "N" allows you  to use CLK in a .BAT  file and
                         check for the warning  with the IF ERRORLEVEL com-
                         mand.

                    /B
                         The B option  tells CLK to remain in  command mode
                         even if no other functions or options are present.
                         The  /B in  itself performs  no operation,  but it
                         avoids CLK going into  full-screen mode if all you
                         want to do is display the current status (e.g., in
                         a .BAT file).

                    /I[,C]
                    or
                    /Ifile[,C]
                         The I option  tells CLK to  read the CLK.INI  file
                         (or "file" if that  is given) for additional func-
                         tions.  These functions are usually A=, L=, and W=
                         functions that were previously written to the file
                         by CLK.   You may add any other  functions (but no
                         options) to the file and they will be processed as
                         if you had entered them at the end of the  command
                         line.   If you don't  specify "file" or  you don't
                         give a path as  part of "file",  CLK will use  the
                         directory which  contains CLK.EXE.   Thus the  de-
                         fault  is to  use  CLK.INI in  the directory  that
                         contains CLK.EXE.  

                         If you enter an A=, L=, M=, or  W= function or CLK
                         finds them in  the file, the file  will be updated
                         with  the new  values  for the  current time  when
                         appropriate.   If  an adjustment  is made,  the L=


                                          21












          CLOCK Version 3.44                                  March 9, 1993


                         function  will reflect  the date  and time  of the
                         latest adjustment.   CLK  will update or  create a
                         CLK.INI  file even if you don't  use the /I option
                         if you use  the A=, L=, M=, or W= functions on the
                         command line.

                         It is very useful to store your  standard TZ=, C=,
                         and R=  functions in the CLK.INI file.   Then your
                         AUTOEXEC.BAT  file can  simply  contain a  CLK  /I
                         command  to set  your clocks  into their  standard
                         modes, adjust  the time,  and check for  bad clock
                         values.  You  can also  reestablish your  standard
                         modes after  changes with the same command entered
                         from the DOS prompt or a .BAT file.

                         The file may be hidden and still  be updated with-
                         out error.   However, to update  a read-only file,
                         you must  add ,C to  the end of the  option.  This
                         indicates that CLK  may Change  the attributes  of
                         the file in order to update it.  CLK will  restore
                         the original attributes.   System files may not be
                         updated.

                    /M[,C]
                    or
                    /Mfile[,C]
                         The M option is  identical to the I option  except
                         that only the M= function  lines are read from the
                         file.  Its  primary use  is internal  to CLK  when
                         processing an  M= function from  the command line.
                         You may also use /Mfile to specify the location of
                         the file when  entering M= values.   You may  also
                         use  the M  option to  cause recalculation  of the
                         adjustment factor at any time (e.g., after editing
                         the file).

                    /P
                    or
                    /PN
                         Controls the use  of password  protection of  mode
                         changes.  When you use /P, CLK will ask you for  a
                         new password.  It will then ask you to repeat  the
                         password to ensure that you entered what you want.
                         It does not display the password as you enter  it.
                         The password is then passed to CLOCK.SYS and pass-
                         word protection  is enabled.   On future  calls to
                         CLOCK.SYS, you  will be asked for  the password if
                         protection is enabled.  You may use /PN to disable


                                          22












          CLOCK Version 3.44                                  March 9, 1993


                         password protection, but you  will have to provide
                         the current password  to do so.  If  used with the
                         /S feature, the password protection will remain in
                         effect even across reboots.  /P should be the last
                         field on a CLK command line.

                    /S
                    or
                    /Sfile
                         Saves the current copy  of CLOCK.SYS as it resides
                         in memory.  If  you do not  specify the file,  the
                         memory version is written to file CLOCK.NEW in the
                         same directory that contains  CLK.EXE.  While  you
                         may  directly  overwrite the  file  CLOCK.SYS, you
                         should be  very careful doing so  as whatever your
                         current  state is  will  take effect  on the  next
                         boot.

                         PLEASE  MAKE  A  BACKUP  COPY   of  your  original
                         CLOCK.SYS before replacing it  with a saved  file.
                         The saved  file does not  do any  probing at  boot
                         time as  it already knows exactly  what your clock
                         is.  It does  not need any  parameters on the  de-
                         vice= line in CONFIG.SYS.

                         The /S  option may be extremely  useful for anyone
                         with multiple  similar systems  to maintain.   You
                         can set  up all  of your options  once on  one ma-
                         chine, save those with the /S option, and then use
                         the  saved file  to  directly install  on all  the
                         other machines.   If you use  password protection,
                         no  one can  change  the other  systems except  by
                         modifying CONFIG.SYS  to  remove  the  loading  of
                         CLOCK.SYS.

                         You will still need  to run CLK  as part of  every
                         boot operation  (e.g., in AUTOEXEC.BAT)  to do any
                         automatic adjustment (A= and  L= functions), check
                         for clock failures (W= function), and check to see
                         whether the clock should  use the standard or day-
                         light offsets (TZ= function).  These functions are
                         not processed  automatically by  CLOCK.SYS because
                         they would increase the  size of the device driver
                         to an unacceptable limit.






                                          23












          CLOCK Version 3.44                                  March 9, 1993


                    /?
                         "/?" or any  error will cause  CLK to display  the
                         usage format.  If you have an error in any  field,
                         CLK first displays that field.

                    TZ=:?
                         "TZ=:?" or any error in a TZ= function that refers
                         to a  pre-defined time zone causes  CLK to display
                         all the  current pre-defined time  zone names  and
                         their associated values.


          2.2  Format of TZ= Function

          The format of TZ=... can get quite complicated as the standard is
          trying to  deal with  all time  zones and  daylight savings  time
          rules around the world.  The full format is:

               TZ=:zone
               or
               TZ=STD[offset][DAY[offset][,start[/time],end[/time]]]

          Parameters     zone
                         The form TZ=:zone  is the one you  are most likely
                         to need.  CLK knows the offsets  and daylight sav-
                         ings time rules  for most of the U.S.  and all you
                         have to supply is the name of your time zone.  The
                         time zones currently known to CLK are:
                         EST  Eastern U.S. with automatic daylight
                         CST  Central U.S. with automatic daylight
                         MST  Mountain U.S. with automatic daylight
                         PST  Pacific U.S. with automatic daylight
                         HST  Hawaiian with no daylight savings time

                         You can use CLK TZ=:? to display the list of  pre-
                         defined zone names and their values.

                         If you would like your favorite time added, please
                         send  me the names, offset from  UTC, and any day-
                         light savings time  rules that are different  from
                         the U.S.  NOTE:  The names can be composed of  any
                         characters except digits, plus, minus, and  comma.
                         They can  be up  to 32 characters  long.   Case is
                         preserved in  the names only for  later display by
                         CLK.  You can call your zone MyZone.





                                          24












          CLOCK Version 3.44                                  March 9, 1993


                         Case is not important  in matching the zone names.
                         tz=:cst is  the equivalent of TZ=:CST.   Both will
                         find the definition of CST.
                                  
                    You don't have to wait for me to modify CLK in order to
                    use your local rules or just try something out.  That's
                    what the long form is for.

                    STD
                         is any time  zone name for standard  time that you
                         want to use.  See the note above for the rules.


                    offset
                         is the difference between  your local time and UTC
                         and is expressed as hh[:mm[:ss]] with an  optional
                         leading + or -.  Offsets for times West of  Green-
                         wich are  positive and those East are negative.  A
                         24-hour  clock  is used  with  times  running from
                         00:00:00  to  23:59:59.    Mountain Standard  time
                         would be expressed as:
                              TZ=MST+07:00:00
                                   or
                              TZ=MST7
                         and that's what you would use if you live in  Ari-
                         zona  and  don't want  any  daylight  savings time
                         adjustments.

                    DAY
                         is the  time zone name for  daylight savings time.
                         If  you don't  use daylight  savings time  in your
                         location, you should not supply this or any of the
                         following fields.

                         The offset  for daylight time is in  the same form
                         as for  standard time.   If  you  don't give  this
                         offset, it  is assumed to  be one hour  later than
                         standard time.  Thus a more complete specification
                         of the Eastern time zone would be:
                              TZ=EST+05:00:00EDT+04:00:00
                                   or
                              TZ=EST5EDT4
                                   or
                              TZ=EST5EDT     (since  daylight  is one  hour
                                             later by default)





                                          25












          CLOCK Version 3.44                                  March 9, 1993


                    start
                         is the day of  the year on which  daylight savings
                         time starts.  There are three formats that you can
                         use to give this day.  They are given below.

                    end
                         is the  day  of the  year on  which standard  time
                         starts  again.   Note that  in the  Southern hemi-
                         sphere it is quite possible for "end" to be earli-
                         er in  the year  than "start" as  daylight savings
                         time will include December and January.  end is in
                         the same  format as start.   Note from  the syntax
                         above  that you  must provide  end if  you provide
                         start.

                    time
                         is the time  of day that  the change takes  place.
                         It is  in exactly the same format as offset except
                         that leading + and  - signs are  not allowed.   If
                         you do not specify  the time, 02:00:00 is  used as
                         the default.

          The day of the year form for start and end may be any of:

                    Jn
                         where n is a Julian day of the year from 1 to 365.
                         This form  does not allow you to refer to February
                         29.  Day  59 is always February  28 and Day 60  is
                         always March 1.  This is  most useful in locations
                         where  a particular  calendar  date is  used every
                         year.

                    n
                         where n is a Julian day of the year from 0 to 365.
                         This form does allow you to refer to February  29.
                         January 1  is day  0, February 28  is day  58, and
                         either February 29 or March  1 is day 59 depending
                         on whether it is a leap year or not.  Not the most
                         useful of  forms but  it does deal  with locations
                         that might  specify February  29 as the  date that
                         time changes.

                    Mm.w.d
                         is used in places like the U.S. that do not speci-
                         fy  a date, but  rather specify a rule.   m is the
                         month  (1  to 12).    d is  the  day  of the  week
                         (0=Sunday, 1=Monday, ...  6=Saturday).   w is  the
                         week of the  month (1 to 5).  Week 1 indicates the


                                          26












          CLOCK Version 3.44                                  March 9, 1993


                         first time that day d occurs in that month.   Week
                         5 indicates the  last time  that day  d occurs  in
                         that  month whether  it  is the  4th or  5th time.
                         Thus the U.S. rule is
                              M4.1.0/02:00:00,M10.5.0/02:00:00
                         or the first Sunday in April at 2AM until the last
                         Sunday in October at 2AM.

          The long form for Central U.S. time is:

               TZ=CST+06:00:00CDT+05:00:00,M4.1.0/02:00:00,M10.5.0/02:00:00
                         or
               TZ=CST6CDT5,M4.1.0/2,M10.5.0/2     (just leaving out zeros)
                         or
               TZ=CST6CDT,M4.1.0,M10.5.0          (since 2AM is default)
                         or
               TZ=CST6CDT                         (since  the U.S.  rule is
                                                  the default)


          2.3  Using CLK

          The most common  use of CLK will be to handle  your time zone and
          daylight savings time changes.  You need only do the following:

          1.   Set your clocks to UTC.

          2.   Include the following line in your AUTOEXEC.BAT file.
                    CLK TZ=:zone   (where you  use one  of the  pre-defined
                                   zones)
                         or
                    CLK TZ=...     (where you define your own rules)

          That's it.  Everything else will take care of itself.  

          The only other time you will need to do anything is if you decide
          to correct your calendar clock to a more accurate time.  You will
          probably use TIMESET  or one of the other programs  that call the
          Naval Observatory or NIST or maybe just  your watch that you have
          set accurately.

          If you don't want to have to change the configuration of the time
          setting program,  you may want  to have it  always set UTC  or at
          least your local standard  time.  If you want to have  it set UTC
          time, do the following:

               CLK S=C C=W
               run your time set program


                                          27












          CLOCK Version 3.44                                  March 9, 1993


               CLK TZ=...     (your normal TZ value)

          The  C=W in the first  line is only required  if you normally run
          with the clocks disconnected.

          Note that if you tell the time set program what your current time
          zone is, you don't have to do anything unless you have the clocks
          disconnected.

          Notes     Leaving your clock on local time                    ________________________________
                    If you  don't want  to be bothered  with UTC,  CLK will
                    quite happily work with your calendar clock set  to its
                    current  value.   For  example, let's  assume that  you
                    currently have both clocks set to Pacific Standard Time
                    and you  don't really want  to be bothered  changing to
                    UTC, but you would like future changes between standard
                    and daylight  time to  be handled automatically.   Just
                    use the following statement in AUTOEXEC.BAT:
                         CLK TZ=PST0PDT

                    CLK believes whatever you tell it and will quite happi-
                    ly operate  assuming that  PST is  equal to  UTC.   You
                    could  even use  CLK with  your calendar  clock  set to
                    Pacific Daylight Time by using:
                         CLK TZ=PST1PDT

                    Avoiding missed days when your PC stays on all night,
                    and missed years and leap days on type 4 and 6 clocks                    _____________________________________________________
                    If your PC is often left on over midnight  and seems to
                    miss the change to a new day, use:
                         CLK C=R TZ=...
                    in your AUTOEXEC.BAT file to have CLOCK.SYS periodical-
                    ly read the time and date  from the calendar clock.  If
                    your clock is a type  4 or 6 clock that doesn't  update
                    years automatically and doesn't handle leap  days, then
                    this setting  also ensures that leaving your PC on over
                    the end of  a year or across February  29 doesn't cause
                    you to get the wrong date.

                    Using CLK.INI to simplify your commands                    _______________________________________
                    If you always  use the same functions, you  may want to
                    edit the CLK.INI file that is included in this release.
                    You can include  your TZ=, C=, and R=  functions in the
                    file and just use:
                         CLK /I
                    in your AUTOEXEC.BAT file.

                    Adding and subtracting time                    ___________________________


                                          28












          CLOCK Version 3.44                                  March 9, 1993


                    You can pretty much do anything including simple arith-
                    metic  on  your clocks  by using  the functions  in the
                    correct sequence.  Let's  say that you  want to add  12
                    hours  to the current  time in both  clocks because you
                    inadvertently  set AM  time instead  of PM  time.   The
                    following function sequence will do that:
                         CLK TZ=Igoofed-12 S=D TZ=:pst

                    The TZ=Igoofed-12  (or use any other name for the zone)
                    sets your DOS clock to 12 hours later than the calendar
                    clock.  (Yes, I know that time zone offsets seem  back-
                    wards  since you subtract them from  the base time, but
                    that's the way the official standards have them.)

                    The S=D sets  both clocks to the value in the DOS clock
                    with a zero offset.

                    The TZ=:pst should be  replaced by whatever your normal
                    TZ function is  or even by a /I to  pull in your normal
                    settings.

                    If you normally have your clocks disconnected, insert a
                    C=W function as the first function.

                    Correcting inadvertent problems                    _______________________________
                    Just remember that except for the S=D function, CLK and
                    CLOCK.SYS  always start  with the  assumption  that the
                    calendar clock  is the base  and do all  their calcula-
                    tions  from that point.  Thus  you can play with TZ and
                    other functions as much as you want and always get back
                    to your normal local time just by using your normal  TZ
                    command.  The calendar clock will not have been affect-
                    ed unless you did  something to set  the time or  date.
                    You can  avoid even that problem  by disconnecting your
                    clocks  (C=D) or  restricting time  changes (R=A).   In
                    fact, if  you have trouble with some program messing up
                    your clocks, try the following:

                         CLK C=D
                         execute program
                         CLK S=C C=W (or C=R) TZ=...  (your normal)

                    If you  have your  standard C= and  TZ= functions  in a
                    file, you can simplify this as:

                         CLK C=D
                         execute program
                         CLK S=C /I


                                          29












          CLOCK Version 3.44                                  March 9, 1993


                    You may  even want  to make  up batch  files containing
                    this sequence to run  those troublesome programs.  Some
                    games are major causes of problems because they set the
                    DOS  clock  running faster  or  slower  than normal  to
                    control the pace of the game.   As long as they restore
                    the normal rate when they exit, the above sequence will
                    eliminate any clock drift problems.

                    Fast DOS clock drift                    ____________________
                    Some high-speed communication  programs will also cause
                    the DOS clock  to run slow by causing the  BIOS to miss
                    clock interrupts.   Fortunately, a C=R function  should
                    virtually eliminate problems of this type.


          2.4  Examples

               clk A=0.34
                    sets an adjustment factor of 0.34 seconds per day.  The
                    A=0.34  function will  be written  to the  CLK.INI file
                    along with an  L= function with the current  time and a
                    zero remaining adjustment.  Every time thereafter, that
                    CLK  is run with the /I option, it will check to see if
                    it is  time to  adjust the clocks.   About  every third
                    day, it will add 1 second to both clocks.

               clk s=c /i
                    sets the DOS  clock to the current  calendar clock time
                    without any time  zone adjustment.   The /i causes  all
                    functions in the  CLK.INI file to be added.   If one of
                    them is a tz function, we have corrected the DOS  clock
                    for any changes  made to it and re-established our time
                    zone.  This is a good command line to use following a 
                         clk c=d
                    and other operations that may have led to an  incorrect
                    time in the DOS clock.

               clk c=r tz=:est r=b-00:00:02 r=f+00:00:02
                    sets CLOCK.SYS  to read the calendar  clock about every
                    10 seconds  and re-synchronize  the DOS clock  with it;
                    applies the  appropriate Eastern time zone (standard or
                    daylight  depending on date);  and prohibits changes to
                    the clock of more than 2 seconds in either direction.







                                          30












          CLOCK Version 3.44                                  March 9, 1993


          2.5  Errors

          When errors are detected, CLK prints a message.  It also sets the
          ERRORLEVEL on each program termination as follows:

          0    Normal termination or only warning messages.

          1    Time outside warning range.  Warning issued.

          2    Error in command line or CLK.INI file functions.  The  func-
               tion with the error is displayed followed by the appropriate
               usage rules.

          3    Internal error or  system error (e.g., unable to open handle
               to CLOCK.SYS).


          2.6  Future Enhancements

          Several enhancements are planned for future releases of CLK.

               -    Full screen interface that  displays the current status
                    of all the things that CLK and CLOCK.SYS know and  lets
                    you change them just by editing the screen.  The rather
                    clunky command  line interface  needs to remain  as its
                    compact  function definitions  are what  you want  in a
                    .BAT file.

               -    Direct dialing of the Naval Observatory  or NIST to get
                    the correct  time with  automatic creation of  M= func-
                    tions from the results.



















                                          31












          CLOCK Version 3.44                                  March 9, 1993


          3  CLKDEMO.EXE

          A simple version of the CLK program, called CLKDEMO, is  provided
          in both executable  and source code form.   CLKDEMO only provides
          support for the C= functions and displaying the clock status.  It
          is included  to show you  how to add  clock handling to  your own
          applications.   CLKDEMO  is written  in  C and  is compiled  with
          Microsoft C 5.1.


          3.1  CLKDEMO Command Line

          Syntax    CLKDEMO [C=A|D|R|W] [/?]

          The functions provided work exactly as  they do in CLK.   CLKDEMO
          also displays the status and the current times.

          Since CLKDEMO.EXE is merely a subset of CLK.EXE, it isn't  terri-
          bly useful as a utility in its own  right.  Its value is that the
          source  code is  provided.   There  are three  source code  files
          provided.   CLKDEMO.C is the  main program  and performs  command
          interpretation and execution.  IOCTL.C is a set of functions that
          read  and write  the CLOCK$  device  driver using  the DOS  IOCTL
          functions.  IOCTL.H  is a set  of definitions which  are used  by
          CLKDEMO and  IOCTL.C.   CLKTYP.H is  a  list of  the clock  types
          currently supported by these programs.  It is used to display the
          type.























                                          32












          CLOCK Version 3.44                                  March 9, 1993


          4  IOCTL - API TO CLOCK.SYS

          IOCTL  is provided to allow you to build your own applications to
          use  the additional functions that CLOCK.SYS provides.  There are
          several  APIs  (Application Programming  Interfaces)  provided as
          part of IOCTL.  These  APIs  are sufficient to perform all of the
          extended functions.

          All of  the APIs  are defined  to be directly  callable from  all
          Microsoft compatible  languages including MASM,  FORTRAN, Pascal,
          and  BASIC.  Languages  other than  C refer to  the API  names as
          upper case characters.  Object code versions are provided for the
          small, medium,  and large  memory models.   These  may be  linked
          directly with your  applications.  The  object code versions  are
          SIOCTL.OBJ, MIOCTL.OBJ, and LIOCTL.OBJ for the small, medium, and
          large models respectively.


          4.1  Data Structures

          Data structures are defined in ioctl.h that are used in the calls
          to the IOCTL functions.


          /* "modes" holds flags that control the operation of CLOCK.SYS */

          struct modes {
              unsigned : 9;
              unsigned day_light: 1;
              unsigned disp_24 : 1;
              unsigned disp_tim : 1;
              unsigned pw_ena : 1;
              unsigned disabl : 1;
              unsigned chk_forw : 1;
              unsigned chk_back : 1;
          };

          /* "off" holds a time offset in hours, minutes, and seconds. */

          struct off {
              int hour;
              int minute;
              int second;
          };






                                          33












          CLOCK Version 3.44                                  March 9, 1993


          /* "date_time" is a structure that holds a date and time.    */

          struct date_time {
              int year;
              int month;
              int day;
              struct off time;
              int hsecond;
          };

          /* "time_zone" holds a time zone name and offset.   */

          struct time_zone {
              struct off offs;
              unsigned char zone[32];
          };

          /* "limit"  is used to  hold the data  that sets time  limits for
          changes.    */

          struct limit {
              struct off back;
              struct off forward;
          };
          /*  "disp" is used to  hold the data  that specifies the location
          and attributes of the continuous time display.   */

          struct disp {
              int x;
              int y;
              int attribute;
          };


















                                          34












          CLOCK Version 3.44                                  March 9, 1993


          /* CLOCK_DATA is the  CLOCK.SYS data that  is returned by  clksta
          (AKA CLKSTA for FORTRAN,  Pascal, and BASIC languages).   Because
          we  need to  be language  independent, all of  the data  is word-
          aligned.  Only  the data types int and character  are used.  Some
          of the int data is encoded bits or addresses.  */

          struct CLOCK_DATA {
              int connected;               /* Connection state          */
              struct modes mode;           /* Mode bits                 */
              struct date_time cal_time;   /* Current date and time     */
              struct time_zone standard;   /* Offset of standard UTC    */
              struct time_zone daylight;   /* Daylight offset           */
              struct limit rules;          /* Maximum clock movement    */
              struct disp display;         /* Time display loc and attr */
              unsigned char vers[6];       /* CLOCK.SYS version nnn.nn  */
              int clock_type;              /* Type of clock installed   */
              int ct_1;                    /* Data for clock type       */
              int ct_2;
              int ct_3;
              int ct_4;
              unsigned int clock_seg;      /* Segment CLOCK.SYS loaded at*/
              unsigned int clock_long;     /* Size of CLOCK.SYS          */
          };

          This data structure is treated as the following integer array  in
          the FORTRAN and BASIC languages.

          BASIC          _____
               OPTION BASE 1
               DIM CDATA(66)

          FORTRAN          _______
               INTEGER*2 CDATA(66)

          ARRAY INDEX         CONTENTS                 STRUCTURE ELEMENT          ___________         ________                 _________________

          CDATA(1)       =    Connection state         connected
          CDATA(2)       =    Mode bits                mode
          CDATA(3)       =    Year from calendar clock cal_time.year
          CDATA(4)       =    Month                    cal_time.month
          CDATA(5)       =    Day                      cal_time.day
          CDATA(6)       =    Hour                     cal_time.offs.hour
          CDATA(7)       =    Minute                   cal_time.offs.minute
          CDATA(8)       =    Second                   cal_time.offs.second
          CDATA(9)       =    100th of second          cal_time.hsecond
          CDATA(10)      =    Standard hours from UTC  standard.offs.hour
          CDATA(11)      =    Standard minutes         standard.offs.minute
          CDATA(12)      =    Standard seconds         standard.offs.second


                                          35












          CLOCK Version 3.44                                  March 9, 1993


          CDATA(13) -                                  standard.zone
          CDATA(28)      =    Standard time zone LJSF
          CDATA(29)      =    Daylight hours from UTC  daylight.offs.hour
          CDATA(30)      =    Daylight minutes         daylight.offs.minute
          CDATA(31)      =    Daylight seconds         daylight.offs.second
          CDATA(32) -                                  daylight.zone
          CDATA(47)      =    Daylight time zone LJSF
          CDATA(48)      =    Maximum hours backward   rules.back.hour
          CDATA(49)      =    Maximum minutes backward rules.back.minute
          CDATA(50)      =    Maximum seconds backward rules.back.second
          CDATA(51)      =    Maximum hours forward    rules.forward.hour
          CDATA(52)      =    Maximum minutes forward  rules.forward.minute
          CDATA(53)      =    Maximum seconds forward  rules.forward.second
          CDATA(54)      =    x cursor position        display.x
          CDATA(55)      =    y cursor position        display.y
          CDATA(56)      =    attribute                display.attribute
          CDATA(57) -                                  vers
          CDATA(59)      =    CLOCK.SYS version LJSF
          CDATA(60)      =    Clock type               clock_type
          CDATA(61)      =    I/O address, base memory ct_1
                              segment, or base year
          CDATA(62)      =    Read memory offset       ct_2
          CDATA(63)      =    Write-0 memory offset    ct_3
          CDATA(64)      =    Write-1 memory offset    ct_4
          CDATA(65)      =    Segment address          clock_seg
                              where CLOCK.SYS is loaded
          CDATA(66)      =    Length of CLOCK.SYS      clock_long


          4.2  clksta

          þ  Summary

          C          _

          #include <ioctl.h>

          extern int pascal far clksta(struct CLOCK_DATA *cdata);

          BASIC          _____

          OPTION BASE 1
          DIM CDATA(66)

          DECLARE FUNCTION CLKSTA%(BYVAL Addr AS INTEGER)

          STATUS% = CLKSTA(VARPTR(CDATA(1)))



                                          36












          CLOCK Version 3.44                                  March 9, 1993


          FORTRAN          _______

          INTEGER*2 CDATA(66)
          INTEGER*2 STATUS
          INTEGER*2 CLKSTA

          STATUS = CLKSTA(CDATA)

          þ  Description

          clksta  returns  all  of the  information  about  CLOCK.SYS in  a
          structure.  In FORTRAN and  BASIC the structure appears to be  an
          integer  array.  The above structure declarations can be approxi-
          mated  in Pascal.  For  a description of the  values of each ele-
          ment, see the individual APIs below.  The elements not  described
          as part of the input to other functions are:

          unsigned char vers[6];      /* CLOCK.SYS version nnn.nn     */
          int clock_type;             /* Type of clock installed      */
          int ct_1;                   /* Data for clock type          */
          int ct_2;
          int ct_3;
          int ct_4;
          unsigned int clock_seg;     /* Segment CLOCK.SYS loaded at  */
          unsigned int clock_long;    /* Size of CLOCK.SYS            */

          CDATA(57) -
          CDATA(59)      =    CLOCK.SYS version LJSF characters
          CDATA(60)      =    Clock type (see type numbers in appendix B)
          CDATA(61)      =    I/O  address, base  memory  segment, or  base
                              year
          CDATA(62)      =    Read memory offset
          CDATA(63)      =    Write-0 memory offset
          CDATA(64)      =    Write-1 memory offset
          CDATA(65)      =    Segment address at which CLOCK.SYS is loaded
          CDATA(66)      =    Length in bytes of CLOCK.SYS

               vers or CDATA(57) - CDATA(59)
                    Is  the version  number  of the  CLOCK.SYS that  is in-
                    stalled.   This  is  returned as  a 6-character,  left-
                    justified, space-filled (LJSF)  character string.   For
                    example, "3.49  ".

               clock_type or CDATA(60)
                    Is the type number of the clock being used.  See Appen-
                    dix B for the type numbers.




                                          37












          CLOCK Version 3.44                                  March 9, 1993


               ct_1 or CDATA(61)
                    Is the value of the first clock parameter.  This is the
                    base I/O  address for I/O  bus clocks, the  base memory
                    segment address for  memory-mapped clocks, or  the base
                    year for the AT&T clocks.

               ct_2 or CDATA(62)
                    Is the read offset for memory-mapped clocks.

               ct_3 or CDATA(63)
                    Is the write 0-bits offset for memory-mapped clocks.

               ct_4 or CDATA(64)
                    Is the write 1-bits offset for memory-mapped clocks.

               clock_seg or CDATA(65)
                    Is the  segment address  at which CLOCK.SYS  is loaded.
                    CLOCK.SYS always starts at offset zero in this segment.

               clock_long or CDATA(66)
                    Is the length of CLOCK.SYS in bytes.

          þ Arguments         cdata
                                   is a pointer to  a location to place the
                                   current    state     information    from
                                   CLOCK.SYS.

          þ  Return Value

          If clksta is  successful, the function returns 0.   Otherwise, it
          returns a non-zero value and _doserrno is set to the  correspond-
          ing error code.  Possible values are:

               0001h     Invalid  function.    This  should  indicate  that
                         CLOCK.SYS is not installed.  It is the error  that
                         the DOS clock device  driver would return since it
                         doesn't handle these functions.

               0005h     Access denied.  Indicates  that DOS would not open
                         a handle for read access.  You may not have enough
                         handles available.

               0006h     Invalid handle.  Should not happen.

               000Dh     Invalid data.  CLOCK.SYS reported a bad byte count
                         or otherwise  did not  process the request.   This
                         should not happen.



                                          38












          CLOCK Version 3.44                                  March 9, 1993


          4.3  setpw

          þ Summary

          C          _

          #include <ioctl.h>

          extern void pascal far setpw(unsigned char *pw);

          BASIC          _____

          DECLARE SUB SETPW(BYVAL S AS INTEGER)

          A$ = "MyPasswd"
          CALL SETPW(SADD(A$))

          Note  that A$ must be at least 8 characters long.  Only the first
          8 characters will be used.

          FORTRAN          _______

          CHARACTER*8 PW

          PW = "MyPasswd"
          CALL SETPW(PW)

          þ  Description

          The setpw  function sets  the password to  be used  on subsequent
          calls to any  of the following functions.   These functions auto-
          matically  supply  the  most   recent  password  when  they  call
          CLOCK.SYS.   You need not  ever call setpw  if you are  not using
          password protection.  CLOCK.SYS will  only check the password  if
          password protection is enabled through the stmode function.

          þ Arguments         pw
                                   is  a  pointer to  the  password string.
                                   This string should be exactly 8  charac-
                                   ters long and must be at least 8 charac-
                                   ters long.   The password should also be
                                   LJSF as every  character is significant.
                                   Case is significant in passwords.







                                          39












          CLOCK Version 3.44                                  March 9, 1993


          þ  Example

          #include <ioctl.h>

          main()

          {
                  unsigned char pw[9] = "MyPasswd";

          /* Set password to use on subsequent function calls.  */

                  setpw(pw);

          }


          4.4  connec

          þ  Summary

          C          _

          #include <ioctl.h>

          extern int pascal far connec(int *conn);

          BASIC          _____

          DECLARE FUNCTION CONNEC%(CONN AS INTEGER)

          STATUS% = CONNEC(CONN)

          FORTRAN          _______

          INTEGER*2 CONN, STATUS, CONNEC

          STATUS = CONNEC(CONN)

          þ  Description

          The connec function  provides a means  of setting the  connection
          state of CLOCK.SYS.








                                          40












          CLOCK Version 3.44                                  March 9, 1993


          þ  Arguments   conn
                              specifies the new connection mode.  The  val-
                              ues are:
                              0 = disconnected (C=D)
                              1 = connected for writes only (C=W)
                              2 = connected for  writes and periodic  reads
                              (C=R)
                              3 = connected for all operations (C=A)


          þ Return Value

          If  the return  value is zero,  the function  succeeded.   If the
          return value is non-zero, an error has occurred and _doserrno  is
          set to the corresponding error code.  Possible values are:

               0001h     Invalid  function.    This  should  indicate  that
                         CLOCK.SYS is  not installed.  It is the error that
                         the DOS clock device  driver would return since it
                         doesn't handle these functions.

               0005h     Access denied.  Indicates  that DOS would not open
                         a handle for read access.  You may not have enough
                         handles available.

               0006h     Invalid handle.  Should not happen.

               000Dh     Invalid data.  CLOCK.SYS reported a bad byte count
                         or otherwise  did not  process the request.   This
                         should not happen.

          þ  Example

          #include <stdio.h>
          #include <ioctl.h>

          main()
          {
               int conn_write = 1;
               int status;

          /* Set clock to connected for writes */

               status = connec(&conn_write);
               if (status)
                    printf("Error %X in connec\n", status);
          }



                                          41












          CLOCK Version 3.44                                  March 9, 1993


          4.5  newpw

          þ  Summary

          C          _

          #include <ioctl.h>

          extern int pascal far newpw(unsigned char *pw);

          BASIC          _____

          DECLARE FUNCTION NEWPW%(BYVAL S AS INTEGER)

          A$ = "MyPasswd"
          STATUS% = NEWPW(SADD(A$))

          Note  that A$ must be at least 8 characters long.  Only the first
          8 characters will be used.

          FORTRAN          _______

          CHARACTER*8 PW
          INTEGER*2 STATUS, NEWPW

          PW = "MyPasswd"
          STATUS = NEWPW(PW)

          þ  Description

          The  newpw function  sets a  new  password for  CLOCK.SYS.   This
          function is not  sufficient to enable  password protection.   You
          must  also use stmode to  turn on password checking.   BE SURE to
          use newpw before you use stmode to turn on password checking.  If
          you turn on password checking without first setting the  password
          to something  that you know,  you will never  be able to  use the
          CLOCK.SYS functions again until you reboot.

          þ Arguments         pw
                                   is  a pointer  to  the password  string.
                                   This string should be  exactly 8 charac-
                                   ters long and must be at least 8 charac-
                                   ters long.  The  password should also be
                                   LJSF as every  character is significant.
                                   Case is significant in passwords.

          þ Return Value



                                          42












          CLOCK Version 3.44                                  March 9, 1993


          If  the return value  is zero,  the function  succeeded.   If the
          return value is non-zero, an error has occurred and _doserrno  is
          set to the corresponding error code.  Possible values are:

               0001h     Invalid  function.    This  should  indicate  that
                         CLOCK.SYS is not installed.   It is the error that
                         the DOS clock device  driver would return since it
                         doesn't handle these functions.

               0005h     Access denied.  Indicates  that DOS would not open
                         a handle for read access.  You may not have enough
                         handles available.

               0006h     Invalid handle.  Should not happen.

               000Dh     Invalid data.  CLOCK.SYS reported a bad byte count
                         or otherwise  did not  process the request.   This
                         should not happen.


          þ  Example

          #include <stdio.h>
          #include <ioctl.h>

          main()

          {
                  unsigned char pw[9] = "MyPasswd";
                 int status;

          /* Set new password for CLOCK.SYS  */

                  status = setpw(pw);
                 if (status)
                    printf("Error %X in setpw\n", status);

          }


          4.6  rstrct









                                          43












          CLOCK Version 3.44                                  March 9, 1993


          þ  Summary

          C          _

          #include <ioctl.h>

          extern int pascal far rstrct(int *bhour, int *bmin, int *bsec,
              int *fhour, int *fmin, int *fsec);

          BASIC          _____

          DECLARE  FUNCTION RSTRCT%(BHOUR%,  BMIN%,  BSEC%, FHOUR%,  FMIN%,
          FSEC%)

          FORTRAN          _______

          INTEGER*2 BHOUR, BMIN, BSEC, FHOUR, FMIN, FSEC
          INTEGER*2 RSTRCT

          STATUS = RSTRCT(BHOUR, BMIN, BSEC, FHOUR, FMIN, FSEC)

          þ  Description

          The rstrct  function sets backwards  and forwards limits  on time
          changes.   Any  time changes  that  exceed these  limits will  be
          ignored.  For example,  if a backward limit of 2  seconds is set,
          no change that would move the clock backwards more than 2 seconds
          will be processed.  Setting the limits protects you agains keying
          in a  bad time and  agains programs that may  incorrectly set the
          time.  Yet you  can still change  the time within the  prescribed
          limits.  For  example, you may set a backward  limit of 2 seconds
          to permit CLK to adjust the time  by up to 2 seconds while inhib-
          iting any other  backwards changes.  These limits  have no effect
          on changing between standard  and daylight times  as that is  not
          really a change in the "time".

          þ Arguments         bhour:bmin:bsec
                                   is the backward limit  in hours, minutes
                                   and seconds.

                              fhour:fmin:fsec
                                   is the forward limit in hours,  minutes,
                                   and seconds.

          þ Return Value





                                          44












          CLOCK Version 3.44                                  March 9, 1993


          If  the return value  is zero,  the function  succeeded.   If the
          return value is non-zero, an error has occurred and _doserrno  is
          set to the corresponding error code.  Possible values are:

               0001h     Invalid  function.    This  should  indicate  that
                         CLOCK.SYS is not installed.   It is the error that
                         the DOS clock device  driver would return since it
                         doesn't handle these functions.

               0005h     Access denied.  Indicates  that DOS would not open
                         a handle for read access.  You may not have enough
                         handles available.

               0006h     Invalid handle.  Should not happen.

               000Dh     Invalid data.  CLOCK.SYS reported a bad byte count
                         or otherwise  did not  process the request.   This
                         should not happen.


          þ  Example

          #include <stdio.h>
          #include <ioctl.h>

          main()

          {
               int bhour = 0;
               int bmin = 0;
               int bsec = 2;
               int fhour = 1;
               int fmin = 0;
               int fsec = 0;
               int status;

          /* Set  time change  limits to  2 seconds  backwards  and 1  hour
          forwards  */

               status = rstrct(&bhour, &bmin, &bsec, &fhour, &fmin, &fsec);
               if (status)
                    printf("Error %X in rstrct\n", status);
               else
                    printf("Time limits set to "
                         "-%.2d:%.2d:%.2d,+%.2d:%.2d:%.2d\n",
                         bhour, bmin, bsec, fhour, fmin, fsec);
          }



                                          45












          CLOCK Version 3.44                                  March 9, 1993


          4.7  stmode

          þ  Summary

          C          _

          #include <ioctl.h>

          extern int pascal far stmode(struct modes *mode);

          BASIC          _____

          DECLARE FUNCTION STMODE%(MODES%)

          FORTRAN          _______

          INTEGER*2 MODES
          INTEGER*2 STMODE

          STATUS = STMODE(MODES)

          þ  Description

          The  stmode function  sets a  variety  of operating  modes.   The
          argument is  actually a  structure of bits.   Each  bit specifies
          whether an operating mode is on (1) or off (0).

          þ Arguments         modes
                                   is set  of bits  that specify  operating
                                   modes.  The bit values are:

                                   unsigned : 9;            Unused
                                   unsigned day_light: 1;   0x0200 (512)
                                   unsigned disp_24 : 1;    0x0400 (1024)
                                   unsigned disp_tim : 1;   0x0800 (2048)
                                   unsigned pw_ena : 1;     0x1000 (4096)
                                   unsigned disabl : 1;     0x2000 (8192)
                                   unsigned chk_forw : 1;   0x4000 (16384)
                                   unsigned chk_back : 1;   0x8000 (32768)

          þ Return Value

          If the  return value  is zero,  the function  succeeded.  If  the
          return value is non-zero, an error has occurred and _doserrno  is
          set to the corresponding error code.  Possible values are:

               0001h     Invalid  function.    This  should  indicate  that
                         CLOCK.SYS is not installed.  It is the  error that


                                          46












          CLOCK Version 3.44                                  March 9, 1993


                         the DOS clock device  driver would return since it
                         doesn't handle these functions.

               0005h     Access denied.  Indicates  that DOS would not open
                         a handle for read access.  You may not have enough
                         handles available.

               0006h     Invalid handle.  Should not happen.

               000Dh     Invalid data.  CLOCK.SYS reported a bad byte count
                         or otherwise  did not  process the request.   This
                         should not happen.


          þ  Example

          #include <ioctl.h>

          main()

          {
               struct CLOCK_DATA cdata;

          /* Set daylight savings time.  */

               clksta(&cdata);            /* Get current mode settings. */

               cdata.mode.day_light = 1;  /* Turn on daylight */

               stmode(&cdata.modes);
          }


          4.8  stzone

          þ  Summary

          C          _

          #include <ioctl.h>

          extern int pascal far stzone(int *shour, int *smin, int *ssec,
              unsigned char sname[32], int *dhour, int *dmin,
              int *dsec, unsigned char dname[32]);






                                          47












          CLOCK Version 3.44                                  March 9, 1993


          BASIC          _____

          DECLARE  FUNCTION  STZONE%(SHOUR%,  SMIN%,  SSEC%,  BYVAL  SN  AS
          INTEGER, DHOUR%, DMIN%, DSEC%, BYVAL DN AS INTEGER)

          SNAME$ = "32-CHARACTER STANDARD ZONE NAME "
          DNAME$ = "Daylight savings time zone name "

          STATUS% = STZONE(6,0,0,SADD(SNAME$),5,0,0,SADD(DNAME$))

          FORTRAN          _______

          CHARACTER*32 SNAME, DNAME
          INTEGER*2 STZONE, STATUS

          SNAME = "CST"
          DNAME = "CDT"
          STATUS = STZONE(6, 0, 0, SNAME, 5, 0, 0, DNAME)

          þ  Description

          The stzone function  sets the standard time and  daylight savings
          time offsets from the  calendar clock and  the standard and  day-
          light time zone  names or mnemonics.   Note that the  offsets are
          subtracted from the calendar  clock to get the local  time.  Thus
          the standard time offset from UTC to EST is 5:0:0.

          þ Arguments         SHOUR:SMIN:SSEC
                                   is the time difference  between the cal-
                                   endar clock and local standard time.  It
                                   may be a positive of negative value.  If
                                   negative, all three values must be nega-
                                   tive.

                              SNAME
                                   is the  standard time zone name  or mne-
                                   monic.   It must be  a 32-character LJSF
                                   character  string.   As  with  all other
                                   character  strings used  by these  func-
                                   tions,  there  is  no  terminating  NULL
                                   character as  is usual in C.   The other
                                   languages  do  not readily  handle  NULL
                                   terminated strings.   In  C applications
                                   you may  define the  character array  to
                                   contain  33  characters,  but  you  must
                                   ensure that the  NULL character does not
                                   occur in the first 32 characters.



                                          48












          CLOCK Version 3.44                                  March 9, 1993


                              DHOUR:DMIN:DSEC
                                   is the time difference  between the cal-
                                   endar clock  and local  daylight savings
                                   time.   Whether  the standard  offset or
                                   the daylight offset is currently used by
                                   CLOCK.SYS is  controlled by  the setting
                                   of the day_light mode bit (see stmode).

                              DNAME
                                   is the  daylight savings time  zone name
                                   or  mnemonic.  It must be a 32-character
                                   LJSF character string.

          þ Return Value

          If the  return value  is zero,  the function  succeeded.   If the
          return value is non-zero, an error has occurred and _doserrno  is
          set to the corresponding error code.  Possible values are:

               0001h     Invalid  function.    This  should  indicate  that
                         CLOCK.SYS is not installed.  It is the  error that
                         the DOS clock device  driver would return since it
                         doesn't handle these functions.

               0005h     Access denied.  Indicates  that DOS would not open
                         a handle for read access.  You may not have enough
                         handles available.

               0006h     Invalid handle.  Should not happen.

               000Dh     Invalid data.  CLOCK.SYS reported a bad byte count
                         or otherwise  did not  process the request.   This
                         should not happen.

















                                          49












          CLOCK Version 3.44                                  March 9, 1993


          þ  Example

          #include <stdio.h>
          #include <ioctl.h>

          main()

          {
               unsigned char sname[33] = "PST                    ";
               unsigned char dname[33] = "PDT                    ";
               int shour = 8;
               int smin = 0;
               int ssec = 0;
               int dhour = 7;
               int dmin = 0;
               int dsec = 0;
               struct CLOCK_DATA cdata;

          /* Get current status.   */

               clksta(&cdata);

          /* Set time zone to U.S. Pacific time.  */

               stzone(&shour, &smin, &ssec, sname, &dhour, &dmin, &dsec,
                   dname);

          /* Select daylight savings time.  */

               cdata.mode.day_light = 1;
               stmode(&cdata.mode);
          }


          4.9  tdisp

          þ  Summary

          C          _

          #include <ioctl.h>

          extern int pascal far tdisp(int *dispx, int *dispy, int *attr);







                                          50












          CLOCK Version 3.44                                  March 9, 1993


          BASIC          _____

          DECLARE FUNCTION TDISP%(DISPX%, DISPY%, ATTR%)

          STATUS% = TDISP(72, 0, &H79)

          FORTRAN          _______

          INTEGER*2 TDISP, STATUS

          STATUS = TDISP(0, 72, 0x79)

          þ  Description

          The tdisp  function sets  the coordinates  and attribute  for the
          continuous time  display.   tdisp  does  not start  or  stop  the
          continuous display nor  does it set the 12-hour  or 24-hour mode.
          Those are all provided by the stmode function.

          þ Arguments         DISPX
                                   is the x  (horizontal) cursor coordinate
                                   for  the continuous  time display.   The
                                   rightmost character on a line is at x=0.
                                   Be sure to leave enough space at the end
                                   of the line to accommodate the entire 8-
                                   chararacter time display.   For example,
                                   x=72 is  the last position to specify on
                                   an 80-character line.

                              DISPY
                                   is  the y  (vertical) cursor  coordinate
                                   for the  continuous time  display.   The
                                   top line on the display is y=0.

                              ATTR
                                   is the display attribute  to use for the
                                   continuous time display.  ATTR is usual-
                                   ly  expressed as  two hex  digits.   The
                                   first  (high-order) digit  is the  back-
                                   ground  color  (0 to  7) and  the second
                                   digit is the text or foreground color (0
                                   to  F).  For  example, 0A  would display
                                   bright  green letters  on a  black back-
                                   ground.   Background  colors usually  do
                                   not include  the  bright  colors.    The
                                   color numbers are:




                                          51












          CLOCK Version 3.44                                  March 9, 1993


                                        0    Black
                                        1    Blue
                                        2    Green
                                        3    Cyan
                                        4    Red
                                        5    Magenta
                                        6    Brown
                                        7    White
                                        8    Grey
                                        9    Bright blue
                                        A    Bright green
                                        B    Brigth cyan
                                        C    Bright red
                                        D    Bright magenta
                                        E    Yellow
                                        F    Bright White

          þ Return Value

          If the  return value  is zero,  the function succeeded.   If  the
          return value is non-zero, an error has occurred and _doserrno  is
          set to the corresponding error code.  Possible values are:

               0001h     Invalid  function.    This  should  indicate  that
                         CLOCK.SYS is not installed.  It is  the error that
                         the DOS clock device  driver would return since it
                         doesn't handle these functions.

               0005h     Access denied.  Indicates  that DOS would not open
                         a handle for read access.  You may not have enough
                         handles available.

               0006h     Invalid handle.  Should not happen.

               000Dh     Invalid data.  CLOCK.SYS reported a bad byte count
                         or otherwise  did not  process the request.   This
                         should not happen.













                                          52












          CLOCK Version 3.44                                  March 9, 1993


          þ  Example

          #include <stdio.h>
          #include <ioctl.h>

          main()

          {
               struct CLOCK_DATA cdata;
               int dispx = 72;
               int dispy = 0;
               int attr = 0x79;

          /* Get current CLOCK.SYS modes.  */

               clksta(&cdata);

          /* Turn on 12-hour display at end of top line of screen. 
             Use bright blue text on a white backgroun.          */

               tdisp(&dispx, &dispy, &attr);
               cdata.mode.disp_tim = 1;
               cdata.mode.disp_24 = 0;
               stmode(&cdata.mode);

          }
























                                          53












          CLOCK Version 3.44                                  March 9, 1993


          5  CLOCK.SYS - ASSEMBLY LANGUAGE API

          CLOCK.SYS has  a couple of additional  APIs (Application Program-
          ming Interfaces) that are  not present in  the normal DOS  CLOCK$
          device driver.  These  interfaces are provided  by the DOS  IOCTL
          (Input/Output  of ConTroL  data) functions.   The  Output Control
          Data to Character Device  function is used  to set new  operating
          values for CLOCK.SYS  for the C=, D=, R=,  TZ=, and /P functions.
          The Input Control Data from Character Device function is used  to
          get the current status  and the date and  time from the  calendar
          clock.


          5.1  Opening the CLOCK$ Device

          In order  to use  the additional APIs  provided by  CLOCK.SYS you
          must  open a handle  to the  CLOCK$ device driver.   You  do this
          using the  DOS  INT 21H  Open  File with  Handle  (3DH)  function
          specifying read-write access.  You then use the handle to  invoke
          the other functions.  Sample assembly language is:
               MOV  AX,3D00H            ; Open with read and write access
               MOV  DX,OFFSET filename  ; Pointer to "CLOCK$" ASCIIZ string
                                        ; DS:DX must point to the string
               INT  21H                 ; Call DOS function handler
          ;    AX contains the handle on return if carry flag is not set.


          5.2  Sending New Values to CLOCK.SYS

          To change the  state of CLOCK.SYS, you use  the Send Control Data
          to  Character Device  (4403H) DOS  function.   You  send data  to
          specify the connection  type, modes, time zone offsets and names,
          restrictions, continuous display information, and  password.  You
          may send any combination of these  in any order.  You must always
          send  the current  password as the  first 8  bytes.   If password
          checking  is not  enabled, it  doesn't  matter what  the 8  bytes
          contain, but you must still send the 8 bytes.

          The data  stream  that you  send  to CLOCK.SYS  consists  of  the
          current password followed by a selection index, the data for that
          selection, another selection index, its data, and so on.









                                          54












          CLOCK Version 3.44                                  March 9, 1993


          The selection  indices and the  data stream associated  with each
          one are:

          INDEX     DATA ITEMS     COMMENTS          _____     __________     ________

          1         connected      two  byte   integer  (0 : C=D,  1 : C=W,
                                   2 : C=R, 3 : C=A)

          2         mode           two byte  integer (see stmode  for a de-
                                   scription of the bits)

          3         standard       time_zone structure for standard time
                    daylight       time_zone structure for daylight time

          4         rules          limits structure

          5         display        disp structure

          6         password       8 bytes LJSF of new password

          Sample assembly language to send new information to CLOCK.SYS:

          curpw     DB   8 dup(?)       ; Current password
                    DW   1              ; Change connection
                    DW   2              ;  to C=R
                    DW   4              ; Change limits
                    DW   0,0,2,1,0,0    ;  to R=B-::2,F+1
                    DW   6              ; Set new password
                    DB   "MyPasswd"     ;  to MyPasswd (case is important)
                    DW   2              ; Change modes
                    DW   0D000H         ;  to enable limits and password
                                        ;  also sets standard time and 
                                        ;  no display
          count     equ $-curpw         ; Length to send
               ...
                    MOV  AX,4403H       ; Send control data function
                    MOV  BX,handle      ; Value returned from open
                    MOV  CX,count       ; Value = number of bytes to send
                    MOV  DX,OFFSET curpw ; Location of bytes to be sent
                                        ; DS:DX must point to the buffer
                    INT  21H            ;
          ; OK if carry not set.  CX will equal bytes actually taken.








                                          55












          CLOCK Version 3.44                                  March 9, 1993


          5.3  Getting Current Status of CLOCK.SYS

          To get the current  status and time, you use  the Receive Control
          Data from Character Device (4402H) function.  You can read all of
          the CLOCK_DATA  structure or  any smaller amount  of it  that you
          need, but you can only read starting at the beginning

          Sample assembly language for reading the clock status is:

               MOV  AX,440CH            ; Read control data function
               MOV  BX,handle           ; Value returned from open
               MOV  CX,count            ; Number of bytes to read
               MOV  DX,OFFSET buffer    ; Location to store the data
                                        ; DS:DX must point to the buffer
               INT  21H                 ; Call DOS
          ; Data returned if carry not set.
          ; CX will contain the actual number of bytes transferred.

































                                          56












          CLOCK Version 3.44                                  March 9, 1993


          APPENDIX A:  DEFINITION OF SHAREWARE

          Shareware  distribution  gives users  a  chance  to try  software
          before buying  it. If  you try a  Shareware program  and continue
          using  it,  you are  expected  to  register. Individual  programs
          differ  on  details --  some  request  registration while  others
          require it, some specify a maximum trial period.  With  registra-
          tion, you get anything  from the simple  right to continue  using
          the software to an updated program with printed manual.

          Copyright laws  apply to both Shareware  and commercial software,
          and the copyright holder retains all rights, with a few  specific
          exceptions as  stated below.  Shareware authors are  accomplished
          programmers, just  like commercial authors, and  the programs are
          of comparable  quality. (In both  cases, there are  good programs
          and bad ones!) The main difference  is in the method of distribu-
          tion.  The author  specifically  grants  the  right to  copy  and
          distribute the software, either to all and sundry or to a specif-
          ic group.  For example,  some authors require  written permission
          before a commercial disk vendor may copy their Shareware.

          Shareware is a  distribution method, not a type  of software. You
          should  find  software  that  suits your  needs  and  pocketbook,
          whether it's commercial or  Shareware. The Shareware system makes
          fitting your needs easier,  because you can  try before you  buy.
          And because the  overhead is low, prices are  low also. Shareware
          has the  ultimate money-back  guarantee -- if  you don't  use the
          product, you don't pay for it.

          DISCLAIMER - AGREEMENT

          Users of CLOCK  must accept this disclaimer of  warranty:  "CLOCK
          is supplied  as is.   The  author disclaims  all warranties,  ex-
          pressed or implied, including, without limitation, the warranties
          of merchantability and of  fitness for any  purpose.  The  author
          assumes no liability for  damages, direct or consequential, which
          may result from the use of CLOCK."

          CLOCK is a  "shareware program" and is  provided at no charge  to
          the  user for  evaluation.   Feel  free  to  share it  with  your
          friends, but please  do not give  it away altered  or as part  of
          another system.   The essence of "user-supported"  software is to
          provide  personal computer  users with  quality software  without
          high prices,  and yet  to  provide incentive  for programmers  to
          continue  to develop  new products.    If you  find this  program
          useful  and find  that you are  using CLOCK  and continue  to use
          CLOCK after a reasonable trial period, you must make a  registra-
          tion payment of $10 to Ronald Q. Smith.  The $10 registration fee


                                          57












          CLOCK Version 3.44                                  March 9, 1993


          will license  one copy  for use  on any one  computer at  any one
          time.  For a registration fee of $25, I will immediately send you
          the latest version of  CLOCK including the  source code and  this
          document as a WordPerfect 5.1 file.   You may use the source code
          for your own maintenance  of CLOCK or as a learning  tool for any
          software that you  develop.  You may  not use all or  part of the
          source code in any software that you develop or release to others
          without the permission of Ronald Q. Smith.

          You must  treat this software  just like a  book.  An  example is
          that this software may be used by any number of people and may be
          freely moved from one  computer location to  another, so long  as
          there is no  possibility of it  being used at one  location while
          it's being used at another.  Just as a book cannot be read by two
          different persons at the same time.

          Commercial users of CLOCK must register and pay for their  copies
          of  CLOCK within 30 days  of first use or  their license is with-
          drawn.    Site-License arrangements  may  be  made by  contacting
          Ronald Q. Smith.

          Anyone distributing CLOCK for any kind of remuneration must first
          contact Ronald Q. Smith at the address below for authorization.

          You are encouraged to pass a  copy of CLOCK along to your friends
          for evaluation.  Please encourage them to register their copy  if
          they  find that  they  can use  it.   All  registered users  will
          receive a copy of the latest version of the CLOCK system.

          Send the fees and any inquiries to:

                         Ronald Q. Smith
                         11 Black Oak Road
                         North Oaks, MN 55127-6204

          You may also contact me via CompuServe mail at userid  71620,514.
          I will be  happy to respond to  any problems and  suggestions for
          future capabilities.

          You may register CLOCK through the CompuServe Shareware Registra-
          tion program.  CLOCK.SYS is found under registration ID 104.  The
          fee for  registering through  CompuServe is  $12 (to  cover their
          charge) and will be added directly to your CompuServe bill.







                                          58












          CLOCK Version 3.44                                  March 9, 1993


          APPENDIX B:  CLOCK TYPES


          B.1  Type 0 - PC/AT

          IBM PC/AT and  all fully compatible  PCs.   Most versions of  DOS
          fully  support this  clock interface  without a  separate driver.
          Use CLOCK.SYS to provide support for CLK.EXE and CLKDEMO.EXE.  If
          you don't  need the  extra functions of  CLK, you  probably don't
          need CLOCK.SYS.  However,  there were a couple  of late 8088  PCs
          that adopted  the PC/AT  clock standard but  did not  provide the
          PC/AT recognition  sentinel.   DOS will not  find the  clock, but
          CLOCK.SYS will.

          Amstrad PC1521DD systems use this type of clock.
                          
          Automatic  determination checks  location F000:FFFE  for the  hex
          value FC.

          BIOS  calls are used to read and write the clock values which are
          usually stored  in the CMOS  RAM along  with other  configuration
          information.  The primary interfaces are:
                          
               Get Date: MOV  AH,4
                         INT  1AH
                              Returns the  year in CX and month  and day in
                              DX in  BCD format (e.g., a  hex display would
                              show:  CX=1991, DX=1009 for October 9, 1991).

               Set Date: MOV  AH,5
                              Load CX and DX as above for Get Date
                         INT  1AH

               Get Time: MOV  AH,2
                         INT  1AH
                              Returns hours  and minutes in CX  and seconds
                              in DH in BCD format.   May also return 100ths
                              of seconds in DL  (e.g., CX=2359, DX=5900 for
                              1 second before midnight).

               Set Time: MOV  AH,3
                              Load CX and DX as for Get Time
                         INT  1AH







                                          59












          CLOCK Version 3.44                                  March 9, 1993


          B.2  Type 1 - Zenith Z-18x portables, Supersport 20

          Automatic determination  checks location  F000:FFFA for  the two-
          byte hex value 4D32 ("M2").

          BIOS calls are used to read and write the clock.

               Get Date: MOV  AH,2
                         INT  1AH
                              Returns CX=year  (1980 - 2079) in  binary and
                              DH=month, DL=day.  All  values are binary.  A
                              hex display of the above date would look like
                              CX=7C7, DX=A09.

               Set Date: MOV  AH,3
                              Load CX and DX as for Get Date.
                         INT  1AH

               Get Time: MOV  AH,4
                         INT  1AH
                              Returns CH=hours, CL=minutes,  DH=seconds.  A
                              hex display would show: CX=173B, DX=3B00.

               Set Time: MOV  AH,5
                              Load CX and DX as for Get Time.
                         INT  1AH


          B.3  Type 2 - Various Zenith Data System PCs.

          Automatic  determination  looks  at location  F000:800A  for  the
          pattern 00,F0,"ZDS".

               Get Date: MOV  AH,2AH
                         INT  1AH
                              Returns CX and DX as for type 1.

               Set Date: MOV  AH,2BH
                              Load CX and DX as for type 1.
                         INT  1AH

               Get Time: MOV  AH,2CH
                         INT  1AH
                              Returns CX and DX as for type 1.

               Set Time: MOV  AH,2DH
                              Load CX and DX as for type 1.
                         INT  1AH


                                          60












          CLOCK Version 3.44                                  March 9, 1993



          B.4  Type 3 - Memory-Mapped Clocks

          Memory-mapped  clock used  on some  Zenith  Data Systems  PCs and
          other similar clocks including  many slot-less or no-slot clocks.
          The  SMT (Systems  Manufacturing Technology)  No-Slot  clocks are
          supported by this type.

          Automatic determination  is to  attempt to  read the  clock.   If
          values other than all 0FFH or  0 are obtained, this clock type is
          chosen.  All known segments and offsets are tried.

          Several  different memory  mapping approaches  are used  and many
          different  address possibilities  are  supported.   In general  a
          segment address in the ROM region (C800H through FFFFH) is  used.
          Offsets from that segment  address are used  to read bits,  write
          zero bits, and  write one bits.  Documentation  may specify those
          segments and  addresses in several  forms.  For  example, segment
          F000 with offset F002 is the same as segment FF00 with offset 2.

          Each memory reference reads  or writes a single bit.  Read opera-
          tions are  used  for all  references  with separate  offsets  for
          reading a bit, writing a zero bit, and writing a one bit.

          Clock segments and addresses currently probed include:

              ÉÍÍÍÍÍÍÍÑÍÍÍÍÍÍÍÍÍÑÍÍÍÍÍÍÍÍÑÍÍÍÍÍÑÍÍÍÍÍÑÍÍÍÍÍÑÍÍÍÍÍÍÍÍ»
              ºSEGMENT³WRITE 0  ³WRITE 1 ³READ ³DECR ³LAST ³VENDOR  º
              ÇÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÅÄÄÄÄÄÅÄÄÄÄÄÅÄÄÄÄÄÅÄÄÄÄÄÄÄÄ¶
              ºF000   ³ F002    ³F003    ³F004 ³0000 ³F000 ³(Zenith)º
              ÇÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÅÄÄÄÄÄÅÄÄÄÄÄÅÄÄÄÄÄÅÄÄÄÄÄÄÄÄ¶
              ºFE00   ³    2    ³   3    ³   5 ³0080 ³C800 ³SMT     º
              ÇÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÅÄÄÄÄÄÅÄÄÄÄÄÅÄÄÄÄÄÅÄÄÄÄÄÄÄÄ¶
              ºFE00   ³    0    ³   2    ³   8 ³0080 ³C800 ³SMT     º
              ÈÍÍÍÍÍÍÍÏÍÍÍÍÍÍÍÍÍÏÍÍÍÍÍÍÍÍÏÍÍÍÍÍÏÍÍÍÍÍÏÍÍÍÍÍÏÍÍÍÍÍÍÍÍ¼

          Multiple address  combinations may be  tried for each  clock pat-
          tern.   The DECR value is  subtracted from the SEGMENT  value for
          another attempt  at probing  until the value  equals LAST.   Note
          that like  the SEGMENT address,  DECR and  LAST are  in units  of
          paragraphs (16-bytes).  Thus DECR of 80 is equivalent to 800H  or
          2048 bytes.

          When the  addresses used by a memory-mapped  clock are determined
          by  probing, the segment  and read address is  displayed.  As the
          read  address varies  the  most from  one  clock manufacturer  to
          another it is a good indication of the type of clock found.



                                          61












          CLOCK Version 3.44                                  March 9, 1993


          Data is stored in BCD in  bytes that you construct by shifting in
          the bits.  The most important data bytes are: 
               0 = Hundredths of seconds
               1 = Seconds
               2 = Minutes
               3 = hours
               5 = days
               6 = months
               7 = years mod 1980


          B.5  Type 4 - Direct Register I/O Bus Clock

          Many add-in clocks on  expansion boards use  this type of  clock.
          Some built-in clocks in  PCs are also  accessed similarly.   This
          clock was used on many AST  Research I/O boards for 8088 PCs such
          as  the Six-Pack Plus,  IO Plus,  etc.  Also  used on  some Tandy
          systems (e.g., 1200HD) and the Vendex Turbo-888-XT.

          Automatic determination is to attempt to read, complement, write,
          re-read, and re-complement one  of the registers.   If the  first
          value  read and the  re-complemented second value  are equal, the
          register exists and is presumed to be the clock.

          See also the description for types 6  and 7.  If you aren't  sure
          which variant you have, specify type 8 and automatic probing will
          determine if it  is really a type 4,  6, or 7.   For the greatest
          chance of detecting  the correct clock type, supply  the base I/O
          address if at all possible.

          NOTE:   If the clock is not correctly initialized (e.g., you have
          just replaced the  battery), CLOCK.SYS must initialize it so that
          the counters will  start working.  CLOCK.SYS  determines that the
          clock has been previously initialized by looking  at register 14H
          (see  B below).  If register B contains the value 0DEH, the clock
          is  presumed to be initialized.  If not, CLOCK.SYS will clear all
          the registers to zero and start the counters running.  While this
          form  of  checking for  initialization  was  commonly used,  your
          previous software may have  used a different method.  If  so, the
          first time  you run CLOCK.SYS  your date and  time may be  set to
          zero (1980-1-1 00:00:00).   If that happens, just  enter the date
          and time.  It should work OK after that without resetting to zero
          on further boots.

          Each clock register is implemented as a separate I/O register ad-
          dress.  Clock  base I/O addresses  of 240H, 2C0H, 300H,  and 340H
          are supported by automatic probing.  Similar clocks at other base
          I/O addresses  are supported  by specifying type  4 and  the base


                                          62












          CLOCK Version 3.44                                  March 9, 1993


          address.  The address range  used is the base  plus 0 through 1FH
          (e.g., 2C0H through 2DFH).
                          
          Important registers are (using 2C0 as the example):
                          
               2C1  =  100ths of seconds 
               2C2  =  seconds 
               2C3  =  minutes 
               2C4  =  hours 
               2C6  =  days
               2C7  =  months
               2C9  =  month last time clock was read/set 
               2CA  =  years
               2CB  =  initialized flag (0DEH if initialized)
               2D4  =  Status
                              
          All values are in BCD.  That means that each register consists of
          two 4-bit nybbles (a nybble is to a nibble as a byte is to a bite
          - I haven't seen this used recently,  but as a bit of trivia, the
          first IBM 360 principles of operation manuals used that term  and
          that spelling -  at least in a  draft copy that we got  in 1965).
          Each nybble contains  one decimal digit of the value.   Years are
          mod 1980 (i.e., 0 means 1980, 99 means 2079).

          Since these  clocks do not keep  the year and do  not handle leap
          years for you, CLOCK.SYS does the necessary calculations to  keep
          the year  correctly maintained  and to adjust  the date  for leap
          days.  The  clocks do  provide a  couple of  memory locations  in
          which CLOCK.SYS maintains  the year and previous month.   As long
          as you boot your system before a full year has passed,  CLOCK.SYS
          will correctly maintain the date.


          B.6  Type 5 - Mitsubishi 8088 PCs

          These were sold by Sperry as the PC-1 and  PC/HT, by Leading Edge
          as the Model D, by Mitsubishi, and others.

          Automatic  determination checks location F000:FFB3 for the string
          "MITSUBISHI".   Later Mitsubishi PCs which used a different clock
          had the same string  at a different location.  We  hope all early
          versions had it at this location.








                                          63












          CLOCK Version 3.44                                  March 9, 1993


          BIOS functions are used to access the clock.

               Get Date: MOV  AH,4
                         INT  1AH
                              Returns  CL=year  mod   1980,  DH=month,  and
                              DL=day all  in binary.  Also  sets AL=0FFH if
                              the clock  is busy and the  request should be
                              retried.

               Set Date: MOV  AH,5
                              Load CL, DX as for Get Date.
                         INT  1AH
                              Returns AL=0FFH if busy.

               Get Time: MOV  AH,2
                         INT  1AH
                              Returns  CH=hour,  CL=minute, DH=second,  and
                              AL=status.  AL=0FFH  means busy.   AL=0 means
                              24-hour mode.   AL=1 means AM  and AL=3 means
                              PM.

               Set Time: MOV  AH,3
                              Load AL, CX, DH as for Get Time.
                         INT  1AH
                              Returns AL=0FFH if busy.

          NOTE:  Some early Mitsubishi PCs came with fixed disk controllers
          that were not DOS compatible.  In addition to the clock modifica-
          tions, the DOS for those systems also handled the disk controller
          variant.  If you have such  a PC, CLOCK.SYS is not sufficient  to
          enable  you to go  above DOS  level 3.2.   You will  also need to
          replace your fixed disk controller.  I strongly suggest that  you
          create a boot floppy for your current DOS level before you try to
          install your new DOS level.  Then boot your new DOS from a floppy
          disk, do SYS C: and copy COMMAND.COM to C:, then try a disk boot.
          If the disk boot fails, boot the floppy you just created and do a
          SYS C:  and copy COMMAND.COM to  C: to restore your  old DOS ver-
          sion.  At that point, your best bet is to simply give up and stay
          with DOS 3.2. If you want to proceed, you must replace your fixed
          disk controller.

          If  SYS C:  gives you an  error status that  indicates that there
          isn't room  for the  new DOS version  (very possible  when moving
          from 3.2 to 3.3 or above), you must backup your entire fixed disk
          and use FORMAT C:/S to place the  new version of DOS on the disk.
          While  this is a hassle, at least if  your PC won't boot from the
          disk, the fall-back approach is identical.  There will be room to
          put DOS 3.2 or earlier back on the fixed disk.


                                          64












          CLOCK Version 3.44                                  March 9, 1993



          B.7  Type 6 - Indirect Register I/O Bus Clock

          Used on AST  Research boards and others.  Typically uses the same
          I/O base  address as  type 4.   However  the clock  registers are
          selected by sending the register address to the base I/O  address
          and then  reading or writing  data at the  base I/O address  + 1.
          The internal register numbers and their contents are the same  as
          for type 4.

          Automatic determination by probing the address  register.  If the
          low-order bit is one, it may be this type of clock or type 7.  We
          then look  further to determine if  it is type 7.   If you aren't
          sure which  type of clock you have but believe it is type 4, 6 or
          7, specify type 8 and automatic probing will detect which variant
          it  is.  If at all possible  specify the base I/O address as that
          will increase  the likelihood  that the correct  determination is
          made.

          I/O  addresses used  are (again  using  2C0 as  the example  base
          address):

               2C0    =  Address register.  Writing a value to this address
                         selects the internal register to read or write.
               2C1    =  Data register.   Reading or writing  this address,
                         reads or writes  the internal register  previously
                         selected by writing 2C0.

          The internal register numbers are (the values to write to 2C0):

                1  =  100ths of seconds
                2  =  seconds
                3  =  minutes
                4  =  hours
                6  =  days
                7  =  months
                9  =  month last time date was read or written
                A  =  year
                B  =  initialization flag
               14  =  status
                          
          Other processing is the same as type 4.








                                          65












          CLOCK Version 3.44                                  March 9, 1993


          B.8  Type 7 - Complex I/O Bus Clock

          Used  on AST Research boards and others.  Typically uses the same
          base I/O address as  types 4 and 6.   Type 7 uses a more  complex
          register  access sequence than type 6.  Type 7 can be detected by
          looking to see if the value in register D has bit 1 (value=2) set
          which type  6 will not.  If  you aren't sure which  type of clock
          you have  but believe it is  type 4, 6  or 7, specify type  8 and
          automatic  probing will  detect which variant  it is.   If at all
          possible specify the  base I/O address as that  will increase the
          likelihood that the correct determination is made.

          The base I/O address is used  as an address register and the base
          + 1 as  a data register.  This  is the same as for  clock type 6.
          However, the internal  registers and the form of  the commands is
          quite  different.  The  primary difference  is that  the internal
          registers only hold four  bits of data each.  Thus  each internal
          register represents a single decimal digit.

          The I/O addresses are used as follows (using 2C0 as an example):

               2C0     = Address register.  The  number of an internal reg-
                         ister  plus 80H is written  to this I/O address to
                         select an internal register.

               2C1     = Data register.   Four  bits  of data  are read  or
                         written  using this  I/O  address from  or to  the
                         internal register  previously selected  by writing
                         to 2C0.

          The internal registers are:

               0  =  Units digit of seconds
               1  =  Tens digit of seconds
               2  =  Units digit of minutes
               3  =  Tens digit of minutes
               4  =  Units digit of hours
               5  =  Tens digit of hours
               6  =  Day of week
               7  =  Units digit of day of month
               8  =  Tens digit of day of month
               9  =  Units digit of month
               A  =  Tens digit of month
               B  =  Units digit of year
               C  =  Tens digit of year
               D  =  Function register
               E  =  Function register
               F  =  Function register


                                          66












          CLOCK Version 3.44                                  March 9, 1993



          B.9  Type 8 - Generic I/O Bus Clock

          Type unknown.  Probe only for types 4, 6, 7, 9, and B.   Use type
          8 if you are sure that you have an I/O bus clock (i.e., the clock
          is on an add-in card) but aren't sure whether it is type 4, 6, 7,
          9, or  B.  If at all possible, supply the base I/O address of the
          clock as this will greatly increase the likelihood of the correct
          handling method being chosen.


          B.10 Type 9 - Quadram I/O Bus Clock

          This type  was  used  by Quadram  Corporation  on  the  QuadCard,
          QuadCard II, and QuadCard 512+.  It may have  been used on others
          as well.

          Automatic determination checks to see that I/O registers exist at
          310H or 210H.

          This clock  used four I/O  control registers and  twelve internal
          registers.  The I/O registers (using 310H as the example) are:

               310  =  Data register (used to move data values)
               311  =  Address register (used to select internal register)
               312  =  Function register (Read, write, hold counter)
               313  =  Control register (Enables read or write function)























                                          67












          CLOCK Version 3.44                                  March 9, 1993


          The internal registers are:

                0 = Units digit of seconds
                1 = Tens digit of seconds
                2 = Units digit of minutes
                3 = Tens digit of minutes
                4 = Units digit of hours
                5 = Tens digit of hours - Also uses bit 2 (=4) to  indicate
                    PM if  in 12-hour mode and bit 3 (=8) to select 24-hour
                    mode
                6 = Day of week (we don't use this)
                7 = Units digit of days
                8 = Tens digit  of days - Also uses  bit 3 (=8) to indicate
                    that  this is a  leap year.   This bit  must be  set by
                    software whenever there is less than 366 days until the
                    next leap day.  If you  do not boot within that period,
                    leap day will not be taken.
                9 = Units digit of months
               10 = Tens digit of months
               11 = Units digit of year mod 1980
               12 = Tens digit of year mod 1980

          NOTE:  If you have this type of clock, you  can only set the time
          to the nearest minute.  Whenever the time is set, the seconds are
          always  set to  zero.   You  should set  the time  as the  minute
          changes.  For that reason, you will not want to use the automatic
          adjustment capability of  CLK with this type of clock  as it will
          try to set the time to the nearest second.


          B.11 Type A - AT&T 6300, 6300 PLUS, 6300 WGS

          Automatic probing  is accomplished by  trying to read  the clock.
          If the read attempt using the BIOS is  successful (carry flag not
          set) and the values returned look like a valid time, the clock is
          assumed to be present.

          NOTE:  AT&T clocks  do not advance the year on January  1.  It is
          necessary  to change  the date  at  the beginning  of each  year.
          Also, AT&T clocks always clear the seconds to zero  when the time
          is changed.  For  this reason you should always set  the date and
          time  at the beginning of a minute.   You should also not use the
          automatic adjustment feature of CLK with these clocks.

          A base year may be specified on the DEVICE= line.  If it is  not,
          1992 will be  used.  This  base will be  good for all dates  from
          1992-1-1 till 1999-12-31.



                                          68












          CLOCK Version 3.44                                  March 9, 1993


          BIOS functions are used with this clock.

               Get Date: MOV  AH,0FEH
                         INT  1AH
                              Returns BX =  Days since base, CH = Hours, CL
                              = Minutes, DH = Seconds,  DL = 100ths of sec-
                              onds

               Set Date: MOV  AH,0FFH
                         MOV  BX,Days since base
                         MOV  CH,Hours
                         MOV  CL,Minutes
                         MOV  DH,0
                         MOV  DL,0
                         INT  1AH


          B.12 Type B - Hyundai 8088 clock

          Automatic determination  probes the control registers.   If they,
          appear to be present, CLOCK tries to read the  clock.  Legal time
          and date values will select this clock.

          This clock uses I/O addresses E0H through EFH as follows:
               E0  =  Units digit of seconds
               E1  =  Tens digit of seconds
               E2  =  Units digit of minutes
               E3  =  Tens digit of minutes
               E4  =  Units digit of hours
               E5  =  Tens digit of hours
               E6  =  Day of week
               E7  =  Units digit of days
               E8  =  Tens digit of days
               E9  =  Units digit of month
               EA  =  Tens digit of month
               EB  =  Units digit of year
               EC  =  Tens digit of year
               ED  =  Control
               EE  =  Control
               EF  =  Control










                                          69












          CLOCK Version 3.44                                  March 9, 1993


          APPENDIX C:  REVISION HISTORY

          930309 -  Version 3.44: Modified M= to automatically set the date
                    and time on the L= to the same as the last M= if the L=
                    is  earlier.  It also  sets any remaining adjustment to
                    zero.  This  is because the clock  was adjusted exactly
                    at the point represented by the M=.

          930306 -  Version 3.43:  Fixed bug with M= function not forcing a
                    read of the  A= functions in CLK.INI and  thus not cor-
                    rectly displaying the previous and new adjustment.

          930304 -  Version 3.42:  Changed time  moving backwards logic  to
                    only look  for earlier  hours.  At  least one  case has
                    been seen of a program that set the time backward a few
                    ticks by  direct  calls on  the  BIOS and  resulted  in
                    CLOCK.SYS advanceing the day.  Now we only advance  the
                    day if the time moves backwards an hour or  more.  Also
                    added the /N  option for CLOCK.SYS that  shuts off this
                    logic  completely  if the  date  advances unexpectedly.
                    Also fixed a bug in locating the CLK.INI file when  the
                    A= function is used by itself.

          930220 -  Version 3.41: Changed timing window prevention logic in
                    CLOCK.SYS to  control another possible case  of the day
                    advancing twice over midnight.

          930212 -  Version 3.40:  Added the M=  function and /M  option to
                    provide calculation  of the  adjmustment value.   Added
                    help for all functions and options. Added the /B option
                    in anticipation  of later support of  full-screen mode.
                    Added the ,C  flag on  the /I and  /M options to  allow
                    updating a  read-only file.   Added error  messages for
                    I/O errors when updating the file.  Fixed timing window
                    in  CLOCK.SYS  that  could  occur  when the  continuous
                    display  is operational  that could  cause the  date to
                    advance unpredictably.

          930204 -  Version 3.31:  Fixed bug  in CLOCK.SYS with  some clock
                    types  causing system  lockups or  bad  data to  be re-
                    turned.

          930130 -  Version  3.30: Added  support  for a  password and  for
                    saving  the current  CLOCK.SYS state as  a new  copy of
                    CLOCK.SYS for  future booting.   Added  continuous time
                    display.   Changed  API  to support  direct calls  from
                    BASIC,  FORTRAN,  and Pascal  as  well as  C  and MASM.
                    Changed status display to be easier to read.


                                          70












          CLOCK Version 3.44                                  March 9, 1993


          930115 -  Version 3.24: Converted document to WordPerfect 5.1 and
                    rewrote  much  of it.    Provide  document in  standard
                    release that can either be viewed on-line or printed.

          930110 -  Version  3.23: Added  support for  R= and  W= commands.
                    Fixed handling of CLK.INI file so that we don't try  to
                    update  it if  it  is read  only or  is in  a read-only
                    sub-directory.   We  also don't update  it if  we can't
                    find the  [clk] section  as it  may  be someone  else's
                    file.

          930106 -  Version 3.22:  Fixed bug in  CLK.EXE that caused  it to
                    move the CLK.INI file to the root directory.

          930104 -  Version 3.21: Fixed bug in CLOCK.SYS expecting zero for
                    100ths of seconds from CMOS clock but  some BIOSs don't
                    zero the register.  Fixed bug in CLK with  synchroniza-
                    tion algorithm not correctly waiting for a new second.

          930102 -  Version 3.20:  Add support for a command file, automat-
                    ic adjustment, and improved synchronization.  My thanks
                    to Eric Smith for the ideas that lead to these enhance-
                    ments.

          921230 -  Version 3.11:  Simplified logic in CLOCK.SYS for check-
                    ing if calendar clock should be read.

          921229 -  Version 3.10: Add  support for constant synchronization
                    with calendar clock.  Fix bug in calculating dates near
                    the end of leap years.

          921226 -  Version 3.02: Recompile CLK.EXE and CLKDEMO.EXE to only
                    use 8088 instructions.  Version 3.01 inadvertently com-
                    piled with  80286 instructions  which can lock  up 8088
                    systems.

          921221 -  Version  3.01: Fixed  a  couple of  bugs  in beta  test
                    version 3.00 with non-PC/AT clocks.  Added logic to CLK
                    to  display the  pre-defined  time zones  on errors  or
                    request.

          921219 -  Version 3.00: Added support for automatic time zone and
                    daylight savings  time adjustment.   CLOCK.SYS  now has
                    the ability to  manage the DOS real time  clock and the
                    battery-protected clock separately.  CLK.EXE is used to
                    convert a base value  in the battery-protected clock to
                    a correct local time in the DOS clock.



                                          71












          CLOCK Version 3.44                                  March 9, 1993


          920614 -  Version 2.24: Fixed bug in probing of AT&T 6300 clocks.
                    Some of the  clocks do not set AL  on successful opera-
                    tion.

          920604 -  Version  2.23:  Fixed  bug  causing fall  through  into
                    memory probing when only I/O probing was wanted.

          920411 -  Version 2.22: Changed order of probing to probe memory-
                    mapped clocks  last as they are  being spuriously found
                    on some Tandy systems.

          920401 -  Version 2.21:   Changed pattern of  I/O address probing
                    to probe all possible I/O addresses for one type (e.g.,
                    4) before trying any  for another type.   Try to  avoid
                    finding the wrong  type.  Added the type B clock to the
                    type 8 probe.

          920328 -  Version 2.20:  Changed order of I/O address probing for
                    clock  types 4,  6,  and 7  to  avoid, where  possible,
                    accessing other  boards.  Most commonly  used I/O clock
                    addresses, I hope, are now probed first.

          920322 -  Version 2.19:  Improved probing for I/O clocks to check
                    that legal values are found  in all the data registers.
                    Several of  the I/O  clocks use operation  sequences so
                    much like each other that it is possible to choose  the
                    wrong one if  we don't actually read the  time and date
                    and see  if the  values are  legal.   This approach  to
                    probing may possibly result in not finding a clock that
                    is present  but that  has been totally  reset.   Such a
                    clock should  be found  on a  second try  to boot  with
                    CLOCK.SYS as the counters will have advanced by then.

          920320 -  Version  2.18:   Added probing  for generic  PC/AT type
                    clock on systems that don't have the PC/AT signature in
                    the BIOS.

          920307 -  Version 2.17:  Added Hyundai 8088 clock.

          920112 -  Version 2.16:  Added AT&T 6300 clock.

          920111 -  Version 2.15:  Fixed memory address used by one type of
                    SMT No-Slot clock.

          920105 -  Version  2.14:   Added support  for a wider  variety of
                    memory mapped clocks  including the SMT  (Systems Manu-
                    facturing Technology) No-Slot clocks.



                                          72












          CLOCK Version 3.44                                  March 9, 1993


          911208 -  Version 2.13:  Add  probing for Vendex Headstart Turbo-
                    888-XT system and any other I/O clock at 300H.   Change
                    I/O clock probing logic to make it less likely to  find
                    the wrong type by accident.

          911129 -  Version 2.12:  Fix handling of Quadram clocks (type 9).
                    They can only set seconds to zero so generate an  error
                    if anyone tries to set the seconds to any other value.

          911128 -  Version  2.11:   Fix  bug  in  handling clock  type  9,
                    Quadram clocks that left  clock turned off after opera-
                    tions.   Also fix bug  in busy determination  for clock
                    types 4 and 6 that could result in a decision  that the
                    clock was not operational.

          911121 -  Version 2.10:  Add  clock types 6 ,7 and 9.  Add type 8
                    to do specific  probing for the  various I/O bus  clock
                    types.

          911109 -  Version 2.05:   Fix  bug in leap  day handling  for I/O
                    clocks.  Fix bug that caused hung systems  when setting
                    the date or time on Z-18x portables.

          911026 -  Version 2.04:  Add support  for I/O clocks at addresses
                    240H  and 340H.    Reduce resident  memory required  by
                    clock driver  to only that required  for specific clock
                    type.

          911021 -  Version 2.03:   Change handling  of new  day flag  from
                    BIOS to  accommodate BIOSs that  indicate multiple days
                    have passed.

          911020 -  Version 2.02:  Fix bug in returning date on clock  read
                    functions.  Added message in automatic determination to
                    indicate type found.

          911010  - Version  2.01:     Added  automatic   determination  of
                    Mitsubishi 8088 PC clocks.   Fixed handler to  keep the
                    BIOS  counter set  properly for  programs that  read it
                    directly.    Also  returns  a finer  granularity  value
                    (100ths of seconds) on reads.

          911009  - Version 2.00:   Modified clock driver  to support addi-
                    tional clock types.  Thanks to Eric Smith (no relation)
                    for help in finding out how the Zenith PC clock worked.

          911005  - Version 1.20:  Changed prologue and epilogue to conform
                    to DOS 5.00  documentation.  Seems to work  OK with DOS


                                          73












          CLOCK Version 3.44                                  March 9, 1993


                    5.0 without the  changes, but we might as  well be con-
                    sistent to save problems later.

          910903  - Version 1.10:   Added display of current date  and time
                    when initializing.

          910518  - CLOCK version  1.00.  Initial version  developed at the
                    request of a  friend with a Sperry PC/HT  who wanted to
                    move to DOS 4.01.

          1984    - Write clock device driver  for AST clock for  IBM PC-1.
                    This serves as the  introduction to what device drivers
                    and especially the CLOCK$ driver are all about.





































                                          74