Using LENSCAD:

LENSCAD is a stand alone program which will calculate the focal 
lengths of a lens system with up to three variable parameters and 
three wavelengths of light.  The only limit to the number of elements 
is the memory capacity of your computer and the stack size, which has 
been set at 3000.  

To start LENSCAD type lc <enter>.  You will be asked if you want to 
use your old data.  If you enter 'n' you will be asked how many 
elements in the system you want to design.  If at any time you need to 
change the number of elements you must restart the program.  Once you 
tell the program how many elements in your design you will be asked 
how many wavelengths of light you want to test the system for and you 
will enter those wavelengths.  The red, yellow and blue menu choices 
enter hydrogen red, sodium yellow, and hydrogen blue spectral line 
wavelengths, respectively.  You will then be in the main menu. Select 
the parameters to enter for the system.  You will be prompted for 
element and surface numbers, etc.

CONVENTIONS:

The element the ray goes through first is element #1 and the first 
surface the ray passes through is surface #1.  The space between 
elements is identified by the greatest element number of the elements 
adjoining the space. Thus the greatest number of the elements 
adjoining the space between elements #1 and #2 is #2.  Rays are 
considered to be coming from the left.  The radius of curvature of an 
element is negative if the center of the curve is to the left of the 
element.  Thus a biconvex lens will have a positive radius of 
curvature for surface #1 and a negative radius of curvature for 
surface #2.

No space between lenses may be set at zero.  For elements in contact 
set the space to a very small number such as .000001. Note that mks 
units are used for all entries (distances in meters).  For a plane 
surface where the radius of curvature is effectively infinity, use a 
large number such as 1000000000 for the radius of curvature.  

Any of the three parameters curvature, distance, and element thickness 
may be made a variable.  You name which curvature, etc. you want to 
vary, and give the range.  Depending on the number of variables, the 
program will calculate over either 11 or 101 points over each range.  
If you have one variable parameter the program will divide the range 
into one hundred regions and will calculate the focal distance over 
101 points.  For two or three variable parameters the program divides 
the ranges into ten regions and calcualates the focal distance over 11 
points.  The focal distance given is the distance from the last 
surface.

You may review the parameters you have entered by choosing selection 5 
in the menu.  It is recommended that you save the data for the system 
you design prior to calculating the focal length(s) for the system. 
Use the SAVE DESIGN PARAMETERS option.  Then if you crash the program 
you can restart it and use the old data. This is quite handy with a 
very large system!

You may choose from a list of standard glass types to establish the 
indices of refraction for the elements in your system or you may enter 
the indices of refraction for the different wavelengths you are 
testing your system for. You must also enter the index of refraction 
for the media between elements.

In order to calculate the focal distance of the system you must set 
the input to the system.  If you forget to do this the program will 
prompt you for the information prior to doing the calculations.  The 
input information for the system consists of the angle the input ray 
subtends with the optical axis of the system (in radians) and the 
height above the axis the ray enters the system.

If you want to change the number of variable paramters or the 
parameter(s) to vary select CHANGE OPTIONS from the menu.  You will 
then be asked which parameters to vary and the variable ranges.

The MAKE REPORT option will create an ascii text file with a summary 
of the design information on your system.  You will be prompted for 
the filename under which to save the report.  


TIPS FOR USING LENSCAD:

Always review the paramaeters of the system you are designing prior to 
calculating the focal distance.  This will avoid a system crash should 
you forget to enter a value for a parameter.  Always save your design 
parameters before making the focal distance calculation.  

The output of LENSCAD consists of the wavelength and variable values 
for each variable parameter, and the associated focal distance for 
that set of variable values.  This format is repeated for all the 
wavelengths the system is being tested for.  LENSCAD makes all 
calculations for one wavelength before making calculations for the 
next wavelength.  The output for one variable and two wavelengths 
would have all the results for the first wavelength in the first half 
of the file and all the results for the second wavelength in the last 
half of the file,  making it very easy to extract the data.

The output for a three variable paramater system with two or more 
wavelengths of light is in excess of 360 kilobytes, therefore the data 
must be written to a hard disk or a high capacity floppy disk if you 
choose this option. If you have only 360kb drives you might run the 
program once for each wavelength.

LENSCAD displays the elements of the system matrix during the 
calculation of the focal distances.  You may see the system matrix for 
a particular system by changing options to make all the parameters 
constant.  The system matrix contains four elements:

     SYSTEM(1,1) is the angular magnification of the system.

     SYSTEM(1,2) is the equivalent power of the system.  Its 
     reciprocal is the equivalent focal length.

     SYSTEM(2,1) is the negative, reduced thickness of the lens.

     SYSTEM(2,2), along with (1,1) and (1,2), give the front vertex 
     length:

     a1=        SYSTEM(1,1)*n
                SYSTEM(1,2)

     and the back vertex focal length:

     a2=       SYSTEM(2,2)*n
               SYSTEM(1,2)

The algorithm used by the program was derived from the matrix method
outlined by Jurgen R. Meyer-Arendt, M.D in the 2nd ed. of Introduction
to Classical and Modern Optics (pp.78-89). It is my understanding he 
dropped the technique in the 3rd ed. which is a real shame because it
lends itself well to computer approaches to lens design.


****************************************************************************
INTERESTED IN NEURAL NETWORKS? NNET IS A THREE LAYER BACKPROPAGATION NEURAL
NETWORK SHELL DEVELOPED FOR RESEARCHING NEURAL NETWORKS. INCLUDED WITH NNET
IS A VERSION COMPATIBLE WITH THE HP95LX PALMTOP COMPUTER FOR TRULY PORTABLE
NEURAL NETWORKING. SEND $54 FOR EXPRESS SHIPMENT TO J. MICHAEL, BOX 941124,
ATLANTA, GA 3O341.
****************************************************************************