SOURCE.DOC Copyright (C) 1992, 1993 Douglas Herr þ all rights reserved

ASMLIB uses a number of subroutines which are not applicable to general
programming.  These subroutines include "$" in their names.  All "$"
subroutines require a near call, so the calling program must be in the same
segment as the called subroutine.  The segment names used by ASMLIB are:

asmtiny:  _TEXT   (assumes CS:DGROUP,  DS:DGROUP)
asmsmall: _TEXT   (assumes CS:_TEXT,   DS:DGROUP)
asmlib:   _MEDIUM (assumes CS:_MEDIUM, DS:DGROUP)
asmhuge:  _HUGE   (assumes CS:_HUGE,   DS:DGROUP)


°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

$clip:        clip a line to fit within graphics view area
Source:       $clip.asm ($graph.asm)

Call with:    call from ASMLIB line drawing subroutines
              assumes DS:@data
Returns:      x & y coordinates in DRAWLINE data area within view area
Uses:         AX, BX, CX, DX, DI, flags


°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

$ega16:       update EGA/VGA/SVGA registers for given drawmode & color
Source:       $ega16.asm ($graph.asm)

Call with:    no parameters
              call $graph before calling $ega16
              drawmode & gcolor must be current
Returns:      DX = 3CEh (Graphics Controller data register address)
Uses:         DX, flags


°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

$emspage:    position logical EMS page at page 0 of page frame
source:      $emspage.asm

Call with:   DS:[BX] pointing to 4-byte offset into allocated EMS block
             DX = EMS handle
Returns:     if CF = 0, no error; AL = logical page
             if CF = 1, AH = error code
Uses:        AX, flags

°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

$enter:       entry code for ASMLIB graphics subroutines
Source:       $enter.asm ($graph.asm)

Call with:    no parameters
Returns:      calls $graph
              pushes flags, BX, CX, DX, DI, SI, ES, BP
              BP = SP
              DF = 0
Uses:         AX, SP, DF


°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

$exit:        exit code for ASMLIB graphics subroutines
Source:       $exit.asm

Call with:    BP = stack frame pointer
              AX, flags, BX, CX, DX, DI, SI, ES, BP pushed on stack
Returns:      returns to program calling the primary subroutine
Uses:         flags, all registers except DS


°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

$fget:       read more data into file buffer
Source:      $fget.asm

Call with:   BX = file handle
             ES = buffer segment address
Returns:     DF = 0
             if CF = 0, AX = bytes read from file
             if CF = 1, AX = DOS error code
Uses:        AX, DX, SI, DS, flags

°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

$gbytes:      calculate byte size of graphics screen
Source:       $gbytes.asm ($graph.asm)

Call with:    no parameters
              $graph must be called before calling $gbytes
Returns:      DX:AX = byte size of screen
Uses:         AX, DX


°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

$getdot:      determines pixel status (graphics modes)
Source:       $getdot.asm ($graph.asm)

Call with:    AX = x-coordinate, BX = y-coordinate
              ES = segment address of screen buffer
              all $graph data must be current
Returns:      AX = pixel value
Uses:         AX, flags


°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

$gp00, $gp02, $gp06, $gp08, $gp10: GPrint/GPrintX code for various dottypes
Source:       $gp00.asm, $gp02.asm, $gp06.asm $gp08.asm, $gp10.asm
                   (banks.asm, $ytable.asm)

Call with:    called from GPrint or GPrintX subroutines
              DS:[SI] -> character font definition
              ES = segment address of screen buffer
Returns:      nothing
              prints a character on graphics screen
Uses:         AX, BX, CX, DX, DI, SI, flags


°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

$gpick:      select string from fixed-field string block; graph mode
Source:      $gpick.asm (heap.asm, strncpy.asm, drawbox.asm, fillbox.asm,
               gprint.asm, dosalloc.asm, bitblock.asm, bbbytes.asm,
               strlen.asm, gcolor.asm, a$menu.asm, $graph.asm, m$input.asm,
               v$extkey.asm, m$chrn.asm, m$nkey.asm)

Call with:   ES = segment address of string list
             AX = number of strings
             CX = field size
             BX = initial choice
             DS:[DX] pointing to upper left screen coordinates
             assumes DS:DGROUP
Returns:     AX = returning keycode
             BX = returned selection number
Uses:        AX, BX, CX, DX, SI, DI, flags


°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

$graph:       set up screen parameters for all ASMLIB graphics modes
Source:       $graph.asm (gcolor.asm, $ytable.asm)

Call with:    no parameters
              system must be in graphics mode you intend to use
Returns:      nothing
              updates $graph data: view coordinates
                                   x-limit
                                   y-limit
                                   base segment address
                                   page size
                                   byte width of screen
                                   maximum page number
                                   dot type:  0 = CGA 4-color
                                              2 = monochrome
                                                  (CGA, Herc, ATT, mode 11h)
                                              4 = Hercules InColor
                                              6 = EGA/VGA 16-color & monochrome
                                                  SVGA16 (up to 800x600)
                                              8 = mode 13h 256-color
                                             10 = VGA13X
                                             12 = SVGA16 (over 800x600)
                                             14 = SVGA256


°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

$h8x8:       copies standard 8x8 character definition to 0B400:0000
             for Hercules RamFont modes
Source:      $h8x8.asm (f8x8.asm)

Call with:   no parameters; assumes Hercules RamFont card is installed
Returns:     nothing
Uses:        nothing; all registers and flags are saved
Used by:     HRam9043, HRam8043


°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

$h8x12:      copies standard 8x12 character definition to 0B400:0000
             for Hercules RamFont modes
Source:      $h8x12.asm ($rld.asm, f8x12rle.asm)

Call with:   no parameters; assumes Hercules RamFont card is installed
Returns:     nothing
Uses:        nothing; all registers and flags are saved
Used by:     HRam9029, HRam8029


°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

$handle:     verify handle for buffered file I/O
Source:      fopen.asm

Call with:   BX = file handle
             ASSUMES DS:DGROUP
Returns:     if CF = 0, SI points to file handle in ASMLIB buffer data area
                        segment address of buffer associated with this handle
                        at 2[SI]
             if CF = 1, handle in BX not managed by ASMLIB buffer system
Uses:        SI, flags

°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

$herc:       detects Hercules-compatible equipment; does not determine
             if Hercules equipment is the default monitor (see IsHerc)
Source:      $herc.asm

Call with:   no parameters
             Assumes DS:@data
Returns:     if CF = 1, no Hercules-compatible equipment installed
             if CF = 0, AX = Hercules model
                       128 = Hercules Graphics Card or compatible
                       144 = Hercules Graphics Card Plus
                       208 = Hercules InColor card
Uses:        AX, flags


°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

$herc16:      update InColor registers for given drawmode & color
              used only by dottype 4 in graphics modes
Source:       $herc16.asm ($graph.asm)

Call with:    no parameters
              call $graph before calling $herc16
              drawmode & gcolor must be current
Returns:      BX = ABS(drawmode) shl 1
Uses:         BX, flags


°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

$hislope:     draw a high-slope line
Source:       $hislope.asm ($ega16.asm, $herc16.asm, $vga256.asm,
                          $hipatrn.asm, banks.asm, $graph.asm, dotmask.asm)

Call with:    DS:@data
              ES = screen buffer segment
              x0 = [BP-2]
              y0 = [BP-4]
              x1 = [BP-6]
              y1 = [BP-8]
Returns:      nothing
Uses:         AX, BX, CX, DX, DI, SI, flags


°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

$horiz:       draw horizontal line
Source:       $horiz.asm ($ega16.asm, $herc16.asm, $vga256.asm, $hvpatrn.asm
                          banks.asm, $graph.asm, dotmask.asm)

Call with:    DS:@data
              ES = screen buffer segment
              x0 = [BP-2]
              y0 = [BP-4]
              x1 = [BP-6]
              y1 = [BP-8]
Returns:      nothing
Uses:         AX, BX, CX, DX, DI, SI, flags


°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

$hipatrn:     draw a high-slope line with pattern
              called from $hislope
Source:       $hipatrn.asm

$hpattern:    draw a horizontal line with pattern
              called from $horiz
Source:       $hvpatrn.asm

°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

a$putw:      module used by several ASMLIB text subroutines to copy
             a character/attribute pair to a window of the screen;
             includes snow control logic for CGA systems.
Source:      a$putw.asm

Call with:   CX = column width of window
             DX = 0 to disable snow control
                = 3DAh to enable snow control (COLOR monitors only!!)
             SI = row height of window
             ES:[DI] points to video buffer
             AL = character
             AH = color attribute
             BX = bytes per screen row (80-column screen has 160 bytes per row)
             DF = 0 (clear direction flag with CLD)
Uses:        DI, SI, flags


°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

a$paint:     used to change color of the screen; used by Paint and
             WPaint subroutines.  Includes snow control logic for CGA
             systems.
Source:      a$paint.asm

Call with:   ES:[DI] pointing to screen
             CX = number of columns
             SI = number of rows
             AH = color attribute
             DX = 3DAh for CGA snow control, 0 otherwise
             BP = bytes per screen row


°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

a$recolor:   replaces selected screen color; used by ReColor and
             WReColor subroutines.  Includes snow control logic for CGA
             systems.
Source:      a$recolor.asm

Call with:   ES:[DI] pointing to screen
             AL = oldcolor
             AH = newcolor
             DX = 0 or 3DAh for snow control
             SI = number of rows
             CX = number of columns
             BP = bytes per screen row


°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

a$wdata:     parameter manager for ASMLIB's Window subroutines.
Source:      a$wdata.asm (crtinfo.asm)

Call with:   DS:[BX] pointing to widow corner data
             requires 2 bytes available at [bp-2]
             row0  equ  [bx]
             col0  equ 2[bx]
             row1  equ 4[bx]
             col1  equ 6[bx]
Returns:     SI = number of rows
             CX = number of columns
             DX = 0 if no CGA, 3DAh if CGA and "snow" control not disabled
             [bp-2] = bytes per screen row
             ES:[DI] -> [row0, col0] on screen
Uses:        CX, DX, DI, SI, ES, [BP-2], flags


°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

$rlbytes:    calculates bytes required to decode run-length encoded data
Source:      $rlbytes.asm

Call with:   DS:[SI] pointing to encoded data
             CX = size of encoded data block
Returns:     AX = bytes required to decode data block
Uses:        AX


°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

$rld:        decodes run-length encoded data
Source:      $rld.asm

Call with:   DS:[SI] pointing to encoded source data
             ES:[DI] pointing to destination buffer
             CX = number of encoded bytes
             assumes destination buffer is large enough for decoded data
Returns:     nothing
Uses:        nothing


°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

$rle:        run-length encoding data compression
Source:      $rle.asm

Call with:   DS:[SI] pointing to data to be encoded
             ES:[DI] pointing to output buffer
             CX = number of bytes to encode
             assumes output buffer is at least the same size as input data
Returns:     DF = 0
             if CF = 0, AX = encoded data size
             if CF = 1, run-length encoding will not compress file
                        data in output buffer is incomplete
Uses:        AX, flags

°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

$strstr:     string search module used by several ASMLIB subroutines
Source:      $strstr.asm

Call with:   ES:[DI] -> search string, DS:[SI] -> pattern string
             BX = pattern string length, DX = search string length
             $strstr searches for the first occurrance of the pattern
             string in the search string
Returns:     if CF = 1, no match
             if CF = 0, AX = match offset from ES:[DI]
Uses:        AX, BX, CX, DX, SI, DI, flags


°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

$wcopy:      copies word data from one portion of memory to another;
             intended for copying to/from video memory in text mode
             includes snow control logic for CGA systems.
Source:      $wcopy.asm

Call with:   CX = words to copy
             DS:[SI] -> source
             ES:[DI] -> destination
             DX = CRTC status port if CGA, else 0
             DF = 0 or 1
Returns:     ES:[DI] pointing past end of destination
             DS:[SI] pointing past end of block
             CX = 0
Uses:        AX, CX, DI, SI, flags
Called by:   WSave, WRestore, GetScreen, PutScreen, TCopy, VScroll, HScroll




°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

m$putwindow:  save screen, clear window & print window frame
Source:       m$putw.asm (wsize.asm, wsave.asm, dosalloc.asm, wframe.asm,
                          wclear.asm)

Call with:    DS:[BX] pointing to window corner data
Returns:      ES = segment address of saved screen area
Uses:         ES, flags
Called by:    PICKSTR


°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

$strlist:     copy group of ASCIIZ strings to block of fixed-length strings
source:       $strlist.asm (dosalloc.asm, strlen.asm, m$count.asm)

Call with:    DS:[SI] pointing to first string to copy
              CX = minimum field size
              string group terminated with double NUL
              requires sufficient free DOS memory

Returns:      if CF = 1, insufficient DOS memory available
              if CF = 0:
               ES = base segment address of string block
               AX = number of strings
               CX = string field size
Uses:         AX, CX, ES, flags
Called by:    PICKSTR, GPICKSTR


°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

m$count:      counts a group of ASCIIZ strings
Source:       m$count.asm (strlen.asm)

Call with:    DS:[BX] pointing to first string
              string group terminated with double NUL
Returns:      AX = number of strings
              CX = length of longest string in group
Uses:         AX, BX, CX, flags
Called by:    PICKSTR, PULLDOWN




°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

m$nkey:       process normal keystroke for menu subroutines
Source:       m$nkey.asm (isupper.asm, m$chr.asm)

Call with:    AL = key code
              BX = initial cursor position
              CX = field width
              DX = number of menu choices
              ES:[DI] pointing to first menu choice
Returns:      BX = output position
               if CF = 0, found matching character
               if CF = 1, no match
Uses:         AX, BX, CX, DX, DI, flags
Called by:    $pick


°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

m$chr:        determines if a keycode is the first uppercase character
              in a string
Source:       m$chr.asm (strlen.asm)

Call with:    AX = keycode
              DS:[BX] pointing to string
Returns:      if CF = 1, string length = 0
              if CF = 0:
                CX = 0 if no upper case characters in the string
                if CX <> 0, AH = first UCASE character
                ZF = 1 if character is first ucase in string
                DS:[BX] points to first ucase character
Uses:         AX, BX, CX, flags
Called by:    $pick, PULLDOWN


°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

$listwindow:  calculates window dimensions for input list; adjusts
              upper left corner coordinates if required to fit on screen
Source:       $listw.asm (crtinfo.asm)

Call with:    DS:[BX] pointing to 8-byte data area for window corner data
              AX = number of choices in list
              CX = list field width
              DH = desired first screen row for list
              DL = desired first column for list
              $listwindow assumes that DH < total screen rows
Returns:      DH = adjusted first row for $pick
              DL = adjusted first column for $pick
              8 bytes at DS:[BX] are updated with window corner coordinates
              for WSave, WFrame, WRestore, etc.
Uses:         DX; all other registers and flags are saved
Called by:    PICKSTR, PICKFILE



°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

$pick:        select one string from a list of fixed-length strings
              used in text-mode menu subroutines
Source:       $pick.asm (crtinfo.asm, str2vbuf.asm, a$putw.asm, m$input.asm,
                         m$chr.asm, m$nkey.asm, a$menu.asm, v$extkey.asm)

Call with:    ES:[DI] pointing to list of choices
              AX = number of menu choices
              CX = field width
              BX = initial cursor position
              DH = top screen row
              DL = left screen column
              Returns to calling program when Esc, Enter or ^C pressed

Returns:      if BreakTrap enabled:
               if CF = 1, ^C or ^Break was pressed
              AX = last key pressed (AX = 3 if ^C pressed)
              BX = string number selected (first string = 0)
Uses:         AX, BX, CF
Called by:    PICKSTR, PICKFILE

°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

v$extkey:     extended keycode processor for ASMLIB vertical list menus
              (text and graph modes)
Source:       v$extkey.asm

Call with:    AL = low word of ASMLIB extended key code
              [bp-2] = field width of string list
              [bp-4] = number of choices
              [bp-6] = current choice
              [bp-8] = first string to print (for scrolling if required)
              [bp-10] = number of strings to print 
                        ( = number of choices if no scrolling required)

Returns:      if CF = 0, modifies [bp-6] and [bp-8]
              if CF = 1, keycode not a valid cursor movement key
              valid keys: Up, Down, Home, End, PgUp, PgDown

Uses:         AX, flags
Called by:    $pick, $gpick

°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

FIND_CGA:     determine if color monitor is installed
FIND_MDA:     determine if monochrome monitor is installed
Source:       $6845.asm

Call with:    no parameters
Returns:      if CF = 0, monitor is installed
              if CF = 1, monitor is not installed
Uses:         flags




°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

$ytable:      calculate buffer offset for each row of screen
              used to set up for dottype 0 - 4 graphics modes
Source:       $ytable.asm ($herc.asm)

Call with:    AX = 0
              ES:[DI] pointing to YTABLE data area
              CX = ylimit+1
              DF = 0
Returns:      nothing
Uses:         AX, BX, CX, DX, DI




°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

a$mname:      return month or day name to calling program
              used by MONTHNAME and DAYNAME
Source:       a$mname.asm

Returns:      ES:[BX] -> month name string
              CX = string length
Uses:         ES, BX, CX


°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

$vga256:      determine color & machine code for given drawmode
Source:       $vga256.asm ($graph.asm)

Call with:    no parameters
              call $graph before calling $vga256
              drawmode & gcolor must be current
Returns:      AL = color
              DL = machine code
              DH = ABS(drawmode)
Uses:         AX, DX, flags




°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

$reset:       restores default hardware settings for graphics modes
              used as part of exit code from ASMLIB graphics subroutines
Source:       $reset.asm ($graph.asm)

Call with:    no parameters
Returns:      nothing
Uses:         nothing


°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

$putdot:      updates a pixel on graphics screen
Source:       $putdot.asm ($graph.asm, $herc16.asm, banks.asm, dotmask.asm)

Call with:    AX = x-coordinate, BX = y-coordinate
              ES = segment address of screen buffer
              all $graph data must be current
Returns:      nothing
Uses:         flags




°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

$rotate:      rotates character font for GPrint & GPrintX
Source:       $gp.asm

Call with:    DS:[SI] pointing to unrotated font
Returns:      DS:[SI] pointing to new charcter font on stack
              DS:@data
Uses:         DS, SI, flags




°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

$vert:        draw vertical line
Source:       $vert.asm ($ega16.asm, $herc16.asm, $vga256.asm, $hvpatrn.asm
                          banks.asm, $graph.asm, dotmask.asm)

Call with:    DS:@data
              ES = screen buffer segment
              x0 = [BP-2]
              y0 = [BP-4]
              x1 = [BP-6]
              y1 = [BP-8]
Returns:      nothing
Uses:         AX, BX, CX, DX, DI, SI, flags


°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

$loslope:     draw a low-slope line
Source:       $loslope.asm ($ega16.asm, $herc16.asm, $vga256.asm,
                          $lopatrn.asm, banks.asm, $graph.asm, dotmask.asm)

Call with:    DS:@data
              ES = screen buffer segment
              x0 = [BP-2]
              y0 = [BP-4]
              x1 = [BP-6]
              y1 = [BP-8]
Returns:      nothing
Uses:         AX, BX, CX, DX, DI, SI, flags




°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

m$input:      input module for ASMLIB menu subroutines
Source:       m$input.asm (kifwait.asm, asmflags.asm)

Call with:    DS:@data
Returns:      AX = keycode
              BX = mouse buttons pressed
               mouse motion is returned as a Left, Right, Up or Down
               keycode.  IsMouse must be called before the menu subroutine
               to enable mouse functions.
Uses:         AX, BX, flags


°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

$lopatrn:     draw a low-slope line with pattern
              called from $loslope
Source:       $lopatrn.asm

$vpattern:    draw a vertical line with pattern
              called from $vert
Source:       $hvpatrn.asm