Notes on Animation
                          04/19/93 -med


Image Animation:

Full color animation requires fast operation of the code to be 
done flicker free. With the standard BGI driver, the speed of the 
PutImage and GetImage functions is not fast enough to properly 
perform the task. An XorPut method can be used to get the job 
done (see the Turbo Pascal BGIDemo), but the problem with that 
method is that as the object moves over a background, the object 
will change colors because of the xoring. The flicker is reduced 
with XorPut, but at the cost of the object colors being changed. 

For true full color animation, color shifts are not acceptable. 
That means an additional Mask step must be added to the process. 
To animate a full color object requires a four step procedure. 
First the background must be saved, then the background must be 
masked to black for all areas of the object that will appear on 
the screen. Next the object itself is drawn. Finally, to move the 
animation object, we restore the old image that we saved, then 
move to the new location and start the process all over again. 

In the BGI, this is done with four procedures:

  while true do
  begin
    GetImage()   {get background}
    PutImage()   {mask background}
    PutImage()   {draw object}
    ----------   {wait for change}
    PutImage()   {restore background} 
  end; 

The problem with this is that the three PutImage routines take a 
lot of time and for anything other than very small objects, 
flicker is readily noticeable. This is especially caused by the 
extra step to mask the background. In a normal animation library 
package, the extra Mask step is included as a part of the object 
draw. This is done by having a foreground only drawing routine. 

The BGI256 driver provides this ability with a special PutImage 
command that allows for a foreground only PutImage. 

This reduces the number of steps down to three from four. That 
reduces the flicker somewhat, but not completely. It would be 
nice to reduce it further. It so happens that we can merge 
another of the steps into the object draw step. 

Before we draw the new object, we first must save the old 
background. It takes time to perform that action, and it must be 
done after we restored the old background from the previous 
object position. The longer we delay from restoring the old 
background to drawing the new object position, the more flicker 
we see. We need to minimize this time period. 

The simplest way to minimize the time period is to read the 
background as we are drawing the object. The standard BGI 
mechanism does not provide for this ability, however the BGI256 
driver has provided a hook to perform this function. A special 
WriteMode command can be given to tell the BGI256 driver to 
change the operation of the GetImage function. 

Ideally it would be desirable to have two pointers passed to the 
function so as to allow the read/write to occur to two separate 
places in memory. That is not possible if we are to keep within 
the calling convention of the standard BGI library. So instead, 
BGI256 uses the same pointer. What happens is that the object to 
be drawn is passed in the Image pointer, and the old screen image 
is passed back in the same memory when the drawing is finished. 
Actually, it is updated on the fly. Before each pixel is written, 
the background is read and saved to the image memory. 

We have now reduced the animation sequence down to two steps:

  while true do
  begin
    GetImage()   {get background / put image}
    ----------   {wait for change}
    PutImage()   {restore background} 
  end; 

From an algorithm standpoint, we now have an optimal animation 
routine. The update time period is limited to how fast we can get 
the new image on the screen after restoring the old background. 
About the only thing that could be done to improve things is to 
make the basic GetImage/PutImage code faster. The BGI256 driver 
has code that is as fast as it can be given the design 
constraints. There are faster animation methods, but they require 
different techniques than is used with GetImage/PutImage.

There is actually more code involved than is indicated above, 
particularly, two memory moves must be done which are not shown. 
However, these moves can be done outside the critical time 
window, so they do not play a part in the flicker process. See 
the ANISUB.PAS file for an example of implementing the BGIDEMO 
flying saucer using the new method. (The DEMO256.PAS program uses 
the ANISUB.PAS unit.)

Additionally, a separate command must be given before the 
GetImage function to specify that a foreground only write is to 
be done while drawing the object. This is required because there 
is no way to specify the drawing mode in the GetImage function as 
there is in the PutImage function, so a special call to the 
SetWriteMode function must be made.


For an example of the difference in animation, run the DEMO256 
program. Try it with the Borland VESA16 driver (DEMO256 0 4) then 
with the BGI256 driver (DEMO256 3 0). This assumes you have a 
super VGA display that is VESA compliant. Notice the substantial 
reduction in flicker when using the BGI256 animation method. 

You can see the saucer completely disappear and then reappear 
when using the standard BGI animation method. But there is only a 
slight flicker with the BGI256 animation method. Actually, the 
amount of flicker will depend on the speed of the computer and 
display. 

Ideally, flicker is eliminated by utilizing the integration 
capabilities of the brain. Flicker is eliminated by keeping the 
period of time that the object is off the display to a minimum. 
The off time should be less than 10ms, and the ratio should be 
better than 3:1.  That is, if the image is off the screen for 
10Ms, it should be on the screen for 30ms or more. The longer the 
on screen time, the less the flicker. However, it is important 
not keep the off screen time in mind as well. The object should 
not be off the screen for longer than 1/2 screen refresh time. At 
60Hz, this is 1/120 second, or 8ms which we can round up to 10ms. 

There are some tricks that can be used to reduce the flicker 
further. Screens are generally painted from top to bottom. By 
observing where the object is in the screen, and keeping the 
update time to less than 1/2 the refresh rate, you can delay the 
object update until the refresh scan has just passed the point on 
the screen where the object is. This can effectively eliminate 
flicker because the object is never actually off the display. 

Unfortunately, for large objects that technique is not always 
possible. Consider on the best display card available, the Video 
Seven VRAM card which can update the display at full PC bus 
speed. If we operate in the 800x600x256 mode, a line is 800 
pixels long. It takes 1.5us to update each pixel if we use a 
MOVSB instruction. That comes out to 1.2ms to update a single 
scan line, or 720ms for the full screen. This is absolute best 
case. In actuality it is much slower because of code overhead. 
Especially if we are using a foreground write which cannot use 
the MOVSB type instruction. 

There are other mechanisms that can be used to reduce the 
flicker. some of them are subjective. By reducing the contrast 
ratio of the background to the object being displayed, flicker 
can be reduced. An ideal contrast ratio would be around 3:1. 
A gray or pastel background reduces the contrast to the object. 
ie avoid black backgrounds if you want to reduce flicker. 

Only update the object if it has moved. Movement causes flicker 
to be much less objectionable compared to an object that is being 
continually updated in the same location. Keep in mind that the 
update time will be affected by computer type and speed as well 
as the display card being used. An old XT with a VGA card would 
be a horrible combination. A 66MHz 486 with a Video7 VRAM card 
would be an ideal solution. 

On simpler displays, a trick could be used of drawing to a 
separate undisplayed video memory location, then switching the 
display pointer to the new location. Unfortunately with most 
SuperVGA boards the address requires more than then 16bit defined 
display start address, and most SuperVGA manufacturers 
implemented the extended display address bits in different ways
(for those who even bothered to implement the extended 
addressing).

Neither has VESA defined a BIOS call to set this value. The end 
result is that either a special display card specific call must 
be done, or the function must be ignored. Since keeping up with 
SuperVGA manufacturers is a nearly impossible task, most BGI 
designers have opted to ignore the paging feature in the SuperVGA 
modes. Since this action is not available, so we are stuck with 
using the other more difficult (time critical) methods.

Warning: just because a display card claims to be fast, it does 
not make it fast for bitmap updates. As an example, the Diamond 
Stealth card is claimed to be speedy in Windows. For doing things 
like drawing windows with the special Windows software, it is 
indeed speedy, but for drawing bitmaps, it is still slower than 
the aging Video7 VRAM card which can transfer bitmaps at the 
speed of the CPU bus. There is an excellent video benchmark 
program available in the IBM forum on Compuserve called 3DBench 
from SuperScape. It will tell you how fast your display card and 
computer combination truly is. For reference purposes, my 33MHz 
486 with a Video7 VRAM display card has a benchmark of 20.0 
frames per second. 


P.S. You may notice a difference between how the Borland VESA16 
driver and the BGI256 driver handle the saucer as it passes over 
the background. Specifically, the filled area of the saucer is 
transparent with the BGI256 driver, and is not transparent with 
the VESA16 driver. This is caused by the differences in the 
floodfill routines which is what is used to fill the area. The 
Borland floodfill is a simple fast fill algorithm which is very 
speedy for solid fills, but does not do well with complex fills. 
The BGI256 floodfill handles complex fills properly which is why 
the filled saucer area is transparent. 



Pixel Animation:

There is no GetLine or GetEllipse function calls, but there is a 
GetPixel function call, so to create animated full color lines 
or elipses, you can use the modified GetPixel function and build 
your own line or ellipse routine. By using the Modified GetPixel 
instead of a GetPixel/PutPixel combination, you can reduce the 
animated linedraw time in half. 



Example ANIMATE program:

See the program ANIMATE.PAS for an example of animated line, 
rectangle, and ellipse routines. The program draws the lines, 
ellipses, and rectangles while saving the background in an array. 

You can control the object by pressing the up/down/left/right 
arrow keys. To select a line, press "L" to select a rectangle, 
press "R", to select an ellipse, press "E". To change the control 
point that the arrows change, press "T". To change the color, 
press "C". Toe see the automatic demo, press "A". To change the 
speed of the automatic demo, press a number (0-9). To quit, press 
"Q" or ESCape. 


<eof>