CMOS - Complimentary Metal Oxide Semiconductor - 

        CMOS non-volatile static RAM (SRAM) is used to store the configuration
    information for a computer system. It stores hardware information like
    drive type, memory size, floppy type(s), etc.  The system battery is

        CMOS Memory Size Mismatch will occur whenever the memory size is 
    changed. This simply indicates that the memory size is different than 
    the value stored in CMOS. To clear this error, turn on or reboot the 
    system and go into CMOS setup. DO NOT make any changes. Simply exit
    and save CMOS values. This will rewrite the CMOS values, including
    the new memory size.

        In older AMIBIOS dated 1990 and before, extended CMOS settings can
    be reset to default values by holding down the INSert key when the system 
is 
    powered up.