WILDMAIL! v3.01

                         Echomail Processor for WILDCAT! v3+



                (c) Copyright 1991, 1993 by Online Computer Resources


                    2036 Columbus Parkway #450  Benicia, CA 94510
                     Voice: (707) 552-1122  BBS: (707) 552-0602

                                 All Rights Reserved
                                  Revised: 06/25/93



          WILDMAIL! v3.01                                 TABLE OF CONTENTS
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

          INTRODUCTION  . . . . . . . . . . . . . . . . . . . . . . . .   1

          WHAT IS WILDMAIL! . . . . . . . . . . . . . . . . . . . . . .   1
               Multiline Operation  . . . . . . . . . . . . . . . . . .   2
               Single Line Systems  . . . . . . . . . . . . . . . . . .   2

          FEATURES LIST . . . . . . . . . . . . . . . . . . . . . . . .   3
               WMCONFIG! Features . . . . . . . . . . . . . . . . . . .   3
               WILDMAIL! Features . . . . . . . . . . . . . . . . . . .   4
                    GENERAL . . . . . . . . . . . . . . . . . . . . . .   4
                    NODE SPECIFIC . . . . . . . . . . . . . . . . . . .   4
                    CONFERENCE SPECIFIC . . . . . . . . . . . . . . . .   4

          FREDMAIL AND MAIL GATING  . . . . . . . . . . . . . . . . . .   5

          DEVELOPMENTAL CYCLE WITH v3.00  . . . . . . . . . . . . . . .   6
               CONFIGURATION PROGRAM  . . . . . . . . . . . . . . . . .   6
               MAIL TOSSER  . . . . . . . . . . . . . . . . . . . . . .   7
               CONCLUSION . . . . . . . . . . . . . . . . . . . . . . .   7

          REGISTRATION/ORDERING INFORMATION . . . . . . . . . . . . . .   8
               REGISTRATION FEE . . . . . . . . . . . . . . . . . . . .   8
               PAYMENT METHOD . . . . . . . . . . . . . . . . . . . . .   8
               KEY GENERATION . . . . . . . . . . . . . . . . . . . . .   8
               UPGRADE FROM PREVIOUS v1.xx/v2.xx  . . . . . . . . . . .   9

          FILES INCLUDED  . . . . . . . . . . . . . . . . . . . . . .    10

          UPGRADE FROM PREVIOUS RELEASES  . . . . . . . . . . . . . .    11
               UPGRADE PROCESS  . . . . . . . . . . . . . . . . . . .    11
               D'BRIDGE USERS . . . . . . . . . . . . . . . . . . . .    13
               DUPLICATE CHECKING . . . . . . . . . . . . . . . . . .    13
               KEY FILE CHANGES . . . . . . . . . . . . . . . . . . .    13

          COMMAND LINE PARAMETER CHANGES  . . . . . . . . . . . . . .    14
               TOSS . . . . . . . . . . . . . . . . . . . . . . . . .    14
               SCAN . . . . . . . . . . . . . . . . . . . . . . . . .    14
               MAILIN . . . . . . . . . . . . . . . . . . . . . . . .    14
               MAILOUT  . . . . . . . . . . . . . . . . . . . . . . .    14
               NETMAIL  . . . . . . . . . . . . . . . . . . . . . . .    14

          NECESSARY BATCH FILE CHANGES  . . . . . . . . . . . . . . .    15
               WILDMAIL! Directory  . . . . . . . . . . . . . . . . .    15
               Command Line Parameters  . . . . . . . . . . . . . . .    15
               WILDMAIL! File Name  . . . . . . . . . . . . . . . . .    15
               AreaFix Deactivation . . . . . . . . . . . . . . . . .    16

          POST UPGRADE CLEANUP  . . . . . . . . . . . . . . . . . . .    17



          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                         Page  i



          WILDMAIL! v3.01                                 TABLE OF CONTENTS
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

               WILDMAIL! Directory  . . . . . . . . . . . . . . . . .    17
               Old Origin Lines . . . . . . . . . . . . . . . . . . .    17
               AreaFix Directory  . . . . . . . . . . . . . . . . . .    18
               WMINSTAL!  . . . . . . . . . . . . . . . . . . . . . .    18

          FIRST TIME INSTALLATION . . . . . . . . . . . . . . . . . .    19
               CONVERTING OVER FROM A NON-WILDMAIL! TOSSER  . . . . .    20
               BATCH FILE ENTRIES . . . . . . . . . . . . . . . . . .    20

          COMMAND LINE USAGE  . . . . . . . . . . . . . . . . . . . .    22
               ?  . . . . . . . . . . . . . . . . . . . . . . . . . .    22
               TOSS . . . . . . . . . . . . . . . . . . . . . . . . .    22
               SCAN . . . . . . . . . . . . . . . . . . . . . . . . .    23
               PRETOSS  . . . . . . . . . . . . . . . . . . . . . . .    23
               MAILIN . . . . . . . . . . . . . . . . . . . . . . . .    23
               MAILOUT  . . . . . . . . . . . . . . . . . . . . . . .    23
               NETMAIL  . . . . . . . . . . . . . . . . . . . . . . .    23
               PACK . . . . . . . . . . . . . . . . . . . . . . . . .    24
               PURGE  . . . . . . . . . . . . . . . . . . . . . . . .    24
               AREAMGR  . . . . . . . . . . . . . . . . . . . . . . .    24
               NOTIFY . . . . . . . . . . . . . . . . . . . . . . . .    25
               -O . . . . . . . . . . . . . . . . . . . . . . . . . .    25
               -R<conf #>,<zone:net/node.point>,<starting msg #>  . .    25
               -T<conf #>,<last extracted msg #>  . . . . . . . . . .    26
               -Q . . . . . . . . . . . . . . . . . . . . . . . . . .    26
               -A . . . . . . . . . . . . . . . . . . . . . . . . . .    27
               LOADING THE OVERLAY FILE . . . . . . . . . . . . . . .    27
                    -XO . . . . . . . . . . . . . . . . . . . . . . .    28
                    -EO . . . . . . . . . . . . . . . . . . . . . . .    28
                    -DO . . . . . . . . . . . . . . . . . . . . . . .    28

          USER INTERFACE  . . . . . . . . . . . . . . . . . . . . . .    29
               Context Sensitive Help . . . . . . . . . . . . . . . .    29
               CRT Display Modes  . . . . . . . . . . . . . . . . . .    29
               Status Bar . . . . . . . . . . . . . . . . . . . . . .    30
               DOS Shell  . . . . . . . . . . . . . . . . . . . . . .    30
               Protected Mode . . . . . . . . . . . . . . . . . . . .    30
               Configuration Checking on Exit . . . . . . . . . . . .    31
               Database Formats . . . . . . . . . . . . . . . . . . .    31

          WMCONFIG! SETUP AND CONFIGURATION . . . . . . . . . . . . .    32
               DATA FILES USED  . . . . . . . . . . . . . . . . . . .    32
                    WMCONFIG.DAT  . . . . . . . . . . . . . . . . . .    32
                    WMAREAS.DAT/IX  . . . . . . . . . . . . . . . . .    32
                    WMNODES.DAT/IX  . . . . . . . . . . . . . . . . .    32
                    WMORIGIN.DAT  . . . . . . . . . . . . . . . . . .    32
                    WMAMGR.DAT  . . . . . . . . . . . . . . . . . . .    32
                    WMCONFIG.HLP  . . . . . . . . . . . . . . . . . .    32



          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                        Page  ii



          WILDMAIL! v3.01                                 TABLE OF CONTENTS
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

               CONFIGURATION CHECKING ON EXIT . . . . . . . . . . . .    32
               SYSTEM GENERATED ERROR FILES . . . . . . . . . . . . .    33
                    WMCONFIG.ERR  . . . . . . . . . . . . . . . . . .    33
                    WMORIGIN.ERR  . . . . . . . . . . . . . . . . . .    33
               MENU SELECTIONS  . . . . . . . . . . . . . . . . . . .    33

          SYSTEM INFORMATION  . . . . . . . . . . . . . . . . . . . .    34
               System Operator Name . . . . . . . . . . . . . . . . .    34
               Bulletin Board Name  . . . . . . . . . . . . . . . . .    34
               Primary Address  . . . . . . . . . . . . . . . . . . .    34
                    Zone  . . . . . . . . . . . . . . . . . . . . . .    35
                    Net . . . . . . . . . . . . . . . . . . . . . . .    35
                    Node  . . . . . . . . . . . . . . . . . . . . . .    35
                    Point . . . . . . . . . . . . . . . . . . . . . .    35
               AKA Addresses  . . . . . . . . . . . . . . . . . . . .    36
                    Create a New AKA  . . . . . . . . . . . . . . . .    36
                    Delete an AKA . . . . . . . . . . . . . . . . . .    37
                    Edit an AKA . . . . . . . . . . . . . . . . . . .    37
               Primary Origin Line  . . . . . . . . . . . . . . . . .    37
               Mailer Type  . . . . . . . . . . . . . . . . . . . . .    38
                    FrontDoor . . . . . . . . . . . . . . . . . . . .    38
                    D'Bridge  . . . . . . . . . . . . . . . . . . . .    38
                    LYNXMAIL! . . . . . . . . . . . . . . . . . . . .    38
                    Binkley . . . . . . . . . . . . . . . . . . . . .    39
               Mailer specific options  . . . . . . . . . . . . . . .    39
                    Program name  . . . . . . . . . . . . . . . . . .    39
                    Parameters  . . . . . . . . . . . . . . . . . . .    40
               BBS Type . . . . . . . . . . . . . . . . . . . . . . .    40
                    WILDCAT!  . . . . . . . . . . . . . . . . . . . .    40
                    FIDO  . . . . . . . . . . . . . . . . . . . . . .    40
               BBS Specific Options . . . . . . . . . . . . . . . . .    40
               WILDCAT! BBS System  . . . . . . . . . . . . . . . . .    41
                    Home directory/path . . . . . . . . . . . . . . .    41
                    Pre-process echomail  . . . . . . . . . . . . . .    41
                    Pre-processing path . . . . . . . . . . . . . . .    43
                    File attach path  . . . . . . . . . . . . . . . .    43
                    Netmail conference number . . . . . . . . . . . .    44
                    Notify users of personal mail . . . . . . . . . .    44
                    Maintain message levels . . . . . . . . . . . . .    45
                    Import Netmail as .MSG  . . . . . . . . . . . . .    46
                    Delete Netmail after extraction . . . . . . . . .    46
                    Allow CRASHMAIL support . . . . . . . . . . . . .    47
                    Valid CRASHMAIL users . . . . . . . . . . . . . .    47
                    Selecting a Crash User  . . . . . . . . . . . . .    48
                    Access Tip  . . . . . . . . . . . . . . . . . . .    48
               FIDO . . . . . . . . . . . . . . . . . . . . . . . . .    48
               Inbound Path . . . . . . . . . . . . . . . . . . . . .    48
               Outbound Path  . . . . . . . . . . . . . . . . . . . .    49



          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                       Page  iii



          WILDMAIL! v3.01                                 TABLE OF CONTENTS
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

                    FrontDoor . . . . . . . . . . . . . . . . . . . .    49
                    LYNXMAIL! . . . . . . . . . . . . . . . . . . . .    49
                    D'Bridge  . . . . . . . . . . . . . . . . . . . .    49
               Netmail Path . . . . . . . . . . . . . . . . . . . . .    50
               Bad Messages Path  . . . . . . . . . . . . . . . . . .    50
                    Stray Messages  . . . . . . . . . . . . . . . . .    51
               WILDMAIL! Log File Name/Path . . . . . . . . . . . . .    51
                    ALT-V  View File  . . . . . . . . . . . . . . . .    51
               Log File Options . . . . . . . . . . . . . . . . . . .    52
                    General . . . . . . . . . . . . . . . . . . . . .    52
                    Accounting  . . . . . . . . . . . . . . . . . . .    52
                    Conference  . . . . . . . . . . . . . . . . . . .    52
                    Errors  . . . . . . . . . . . . . . . . . . . . .    52
                    Select All  . . . . . . . . . . . . . . . . . . .    52

          MISCELLANEOUS INFORMATION . . . . . . . . . . . . . . . . .    54
               Duplicates to maintain . . . . . . . . . . . . . . . .    54
               Maximum messages per .PKT  . . . . . . . . . . . . . .    54
               Max .PKT size  . . . . . . . . . . . . . . . . . . . .    55
               Check SEEN-BYs . . . . . . . . . . . . . . . . . . . .    55
               Kill null messages . . . . . . . . . . . . . . . . . .    56
               Flag NetMail as KILL/SENT  . . . . . . . . . . . . . .    56
               Always use INTL kludge line  . . . . . . . . . . . . .    57
               Use XMS/EMS for swap file  . . . . . . . . . . . . . .    58
               Swap file path . . . . . . . . . . . . . . . . . . . .    58
               Use EMS for database access  . . . . . . . . . . . . .    58
               Database lock count  . . . . . . . . . . . . . . . . .    59
               Delete archives after tossing  . . . . . . . . . . . .    60
               Forward mail .PKTs . . . . . . . . . . . . . . . . . .    61
               Enable quiet archiving . . . . . . . . . . . . . . . .    62
               Process exclude names  . . . . . . . . . . . . . . . .    63
               Exclude names  . . . . . . . . . . . . . . . . . . . .    63
                    Create an exclude name  . . . . . . . . . . . . .    63
                    Delete an exclude name  . . . . . . . . . . . . .    64
                    Edit an exclude name  . . . . . . . . . . . . . .    64
               Save duplicate messages  . . . . . . . . . . . . . . .    64
               Duplicate message path . . . . . . . . . . . . . . . .    64
               Program to run after unpacking . . . . . . . . . . . .    64

          MULTI NETWORK/ZONE CONFIGURATION  . . . . . . . . . . . . .    66
               Assign a zone to an address  . . . . . . . . . . . . .    66
                    Create a Zone Assignment  . . . . . . . . . . . .    66
                         Zone . . . . . . . . . . . . . . . . . . . .    67
                         Net  . . . . . . . . . . . . . . . . . . . .    67
                         Node . . . . . . . . . . . . . . . . . . . .    67
                         Point  . . . . . . . . . . . . . . . . . . .    67
                    Delete an Assignment  . . . . . . . . . . . . . .    67
                    Edit an Assignment  . . . . . . . . . . . . . . .    67



          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                        Page  iv



          WILDMAIL! v3.01                                 TABLE OF CONTENTS
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

               Outbound zone matching . . . . . . . . . . . . . . . .    68

          MAIL ARCHIVE DEFINITIONS  . . . . . . . . . . . . . . . . .    70
               InUse Flag . . . . . . . . . . . . . . . . . . . . . .    70
               Type . . . . . . . . . . . . . . . . . . . . . . . . .    70
                    Special Format - NONE . . . . . . . . . . . . . .    71
               Method . . . . . . . . . . . . . . . . . . . . . . . .    71
               Program  . . . . . . . . . . . . . . . . . . . . . . .    72
               Parameters . . . . . . . . . . . . . . . . . . . . . .    72
               Archival Process . . . . . . . . . . . . . . . . . . .    72

          ORIGIN LINE MAINTENANCE . . . . . . . . . . . . . . . . . .    73
               Active Keystrokes  . . . . . . . . . . . . . . . . . .    73
                    Up/Dn Arrow Keys  . . . . . . . . . . . . . . . .    74
                    [SPACEBAR]  . . . . . . . . . . . . . . . . . . .    74
                    [CTRL-ENTER]  . . . . . . . . . . . . . . . . . .    74
               Create a new Origin line . . . . . . . . . . . . . . .    74
               Delete an Origin line(s) . . . . . . . . . . . . . . .    74
               Edit an existing Origin line . . . . . . . . . . . . .    75
               What is an Origin/Tear line  . . . . . . . . . . . . .    76
               What are Tag lines . . . . . . . . . . . . . . . . . .    76

          NETWORK ACCOUNTING  . . . . . . . . . . . . . . . . . . . .    77
               Cost/Msg . . . . . . . . . . . . . . . . . . . . . . .    77
               Cost/Byte  . . . . . . . . . . . . . . . . . . . . . .    77

          DEFAULT DEFINITIONS . . . . . . . . . . . . . . . . . . . .    78
               Default Node Settings  . . . . . . . . . . . . . . . .    78
               Default Area Settings  . . . . . . . . . . . . . . . .    79
                    Area name . . . . . . . . . . . . . . . . . . . .    79
                    WILDCAT! conference . . . . . . . . . . . . . . .    79
                    Origin line . . . . . . . . . . . . . . . . . . .    79
                    Add to SEENBYs  . . . . . . . . . . . . . . . . .    80

          NODE MANAGEMENT . . . . . . . . . . . . . . . . . . . . . .    81
               Add a new Node Address . . . . . . . . . . . . . . . .    81
               Delete a Node Address  . . . . . . . . . . . . . . . .    81
               Edit a Node Address  . . . . . . . . . . . . . . . . .    81
               Global Change/Modify . . . . . . . . . . . . . . . . .    81
               View Accounting/General information  . . . . . . . . .    83

          NODE SPECIFIC SETTINGS  . . . . . . . . . . . . . . . . . .    84
               Node's address . . . . . . . . . . . . . . . . . . . .    84
               SysOp name . . . . . . . . . . . . . . . . . . . . . .    84
               Active node  . . . . . . . . . . . . . . . . . . . . .    84
               Mail type  . . . . . . . . . . . . . . . . . . . . . .    85
                    Type 2  . . . . . . . . . . . . . . . . . . . . .    85
                    Type 2.2  . . . . . . . . . . . . . . . . . . . .    85



          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                         Page  v



          WILDMAIL! v3.01                                 TABLE OF CONTENTS
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

                    Type 2+ . . . . . . . . . . . . . . . . . . . . .    85
               Fakenet ID . . . . . . . . . . . . . . . . . . . . . .    86
               Tiny SEEN-BY:'s  . . . . . . . . . . . . . . . . . . .    87
               Mail Status  . . . . . . . . . . . . . . . . . . . . .    88
                    None  . . . . . . . . . . . . . . . . . . . . . .    88
                    Hold  . . . . . . . . . . . . . . . . . . . . . .    88
                    Crash . . . . . . . . . . . . . . . . . . . . . .    88
               Selected conferences . . . . . . . . . . . . . . . . .    88
                    Select  . . . . . . . . . . . . . . . . . . . . .    89
                    Deselect  . . . . . . . . . . . . . . . . . . . .    89
                    Filter  . . . . . . . . . . . . . . . . . . . . .    89
               Mail archive format  . . . . . . . . . . . . . . . . .    89
                    FrEdMail and Mail Gating  . . . . . . . . . . . .    90
                    PKT Path  . . . . . . . . . . . . . . . . . . . .    90
                    Standard naming . . . . . . . . . . . . . . . . .    90
               PKT password . . . . . . . . . . . . . . . . . . . . .    91
               AreaRequest password . . . . . . . . . . . . . . . . .    92
               AreaRequest security . . . . . . . . . . . . . . . . .    93
               AreaRequest flags  . . . . . . . . . . . . . . . . . .    94
               Comment  . . . . . . . . . . . . . . . . . . . . . . .    95
               Activation date  . . . . . . . . . . . . . . . . . . .    95
               Deactivation date  . . . . . . . . . . . . . . . . . .    95
               Message count in . . . . . . . . . . . . . . . . . . .    95
               Message count out  . . . . . . . . . . . . . . . . . .    96
               Byte count in  . . . . . . . . . . . . . . . . . . . .    96
               Byte count out . . . . . . . . . . . . . . . . . . . .    96
               PKT count in . . . . . . . . . . . . . . . . . . . . .    96
               PKT count out  . . . . . . . . . . . . . . . . . . . .    97

          CONFERENCE AREA MANAGEMENT  . . . . . . . . . . . . . . . .    98
               Add a new Conference . . . . . . . . . . . . . . . . .    98
               Delete a Conference  . . . . . . . . . . . . . . . . .    98
               Edit a Conference  . . . . . . . . . . . . . . . . . .    98
               Global Change/Modify . . . . . . . . . . . . . . . . .    98
               Forward-To Nodes . . . . . . . . . . . . . . . . . . .   100
               Find Conference Area . . . . . . . . . . . . . . . . .   100
                    Find via: . . . . . . . . . . . . . . . . . . . .   101
                         Number:  . . . . . . . . . . . . . . . . . .   101
                         Area name: . . . . . . . . . . . . . . . . .   101
                    Initiating the Search . . . . . . . . . . . . . .   101

          CONFERENCE SPECIFIC SETTINGS  . . . . . . . . . . . . . . .   102
               Area name  . . . . . . . . . . . . . . . . . . . . . .   102
                    [F2] - Area Pick  . . . . . . . . . . . . . . . .   103
               Long Description . . . . . . . . . . . . . . . . . . .   103
               Passthru area  . . . . . . . . . . . . . . . . . . . .   103
               WILDCAT! conference  . . . . . . . . . . . . . . . . .   104
               Origin address . . . . . . . . . . . . . . . . . . . .   105



          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                        Page  vi



          WILDMAIL! v3.01                                 TABLE OF CONTENTS
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

               Origin line  . . . . . . . . . . . . . . . . . . . . .   106
               Originating node . . . . . . . . . . . . . . . . . . .   106
               Uplink/Feed Address  . . . . . . . . . . . . . . . . .   106
               Extract private mail . . . . . . . . . . . . . . . . .   107
               Active area  . . . . . . . . . . . . . . . . . . . . .   107
               Restrict import  . . . . . . . . . . . . . . . . . . .   108
               Extract file attaches  . . . . . . . . . . . . . . . .   108
               AreaRequest security . . . . . . . . . . . . . . . . .   109
               AreaRequest flags  . . . . . . . . . . . . . . . . . .   111
               SEEN-BY: line processing . . . . . . . . . . . . . . .   112
                    Hidden  . . . . . . . . . . . . . . . . . . . . .   113
                    Display . . . . . . . . . . . . . . . . . . . . .   113
                    Delete  . . . . . . . . . . . . . . . . . . . . .   113
               Add to SEEN-BYs  . . . . . . . . . . . . . . . . . . .   114

          AREAREQUEST MANAGER . . . . . . . . . . . . . . . . . . . .   115
               SECURITY LEVELS  . . . . . . . . . . . . . . . . . . .   115
               AREAREQUEST FLAGS  . . . . . . . . . . . . . . . . . .   116
               AREAREQUEST OPTION ACTIVATION  . . . . . . . . . . . .   117
                    TO: Name  . . . . . . . . . . . . . . . . . . . .   117
                    FROM: Name  . . . . . . . . . . . . . . . . . . .   117
                    SUBJECT line: . . . . . . . . . . . . . . . . . .   117
                         -Q . . . . . . . . . . . . . . . . . . . . .   117
                         -L . . . . . . . . . . . . . . . . . . . . .   118
                         -R . . . . . . . . . . . . . . . . . . . . .   118
               MESSAGE BODY . . . . . . . . . . . . . . . . . . . . .   119
                    TEAR LINE . . . . . . . . . . . . . . . . . . . .   119
                    AREA Activation/De-activation . . . . . . . . . .   119
                    Rescanning Conferences  . . . . . . . . . . . . .   119

          AREAREQUEST CONFIGURATION OPTIONS . . . . . . . . . . . . .   121
               Process AreaRequest Msgs . . . . . . . . . . . . . . .   121
               Area Manager aliases . . . . . . . . . . . . . . . . .   121
                    Add an Alias Name . . . . . . . . . . . . . . . .   121
                    Delete an Alias Name  . . . . . . . . . . . . . .   122
                    Edit an Alias Name  . . . . . . . . . . . . . . .   122
               Purge areas  . . . . . . . . . . . . . . . . . . . . .   122
               ALT-V  View File . . . . . . . . . . . . . . . . . . .   123
               Purge file . . . . . . . . . . . . . . . . . . . . . .   123
               Master Conference List . . . . . . . . . . . . . . . .   124
               Allow area rescan  . . . . . . . . . . . . . . . . . .   125
               Allow area query . . . . . . . . . . . . . . . . . . .   126
               Show feeds . . . . . . . . . . . . . . . . . . . . . .   126
               Kill processed messages  . . . . . . . . . . . . . . .   126
               Notify with Echo List  . . . . . . . . . . . . . . . .   126
               Notify exclude . . . . . . . . . . . . . . . . . . . .   127
                    Add a New Flag  . . . . . . . . . . . . . . . . .   128
                    Delete a Flag . . . . . . . . . . . . . . . . . .   128



          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                       Page  vii



          WILDMAIL! v3.01                                 TABLE OF CONTENTS
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

                    Edit a Flag . . . . . . . . . . . . . . . . . . .   129
               Forward Lists  . . . . . . . . . . . . . . . . . . . .   129
                    Create a New List . . . . . . . . . . . . . . . .   129
                    Delete a List . . . . . . . . . . . . . . . . . .   130
                    Edit a List . . . . . . . . . . . . . . . . . . .   130
               Forward List Definitions . . . . . . . . . . . . . . .   130
                    Echo List . . . . . . . . . . . . . . . . . . . .   130
                         ALT-V  View File . . . . . . . . . . . . . .   131
                    Originating Node  . . . . . . . . . . . . . . . .   131
                    Uplink Address  . . . . . . . . . . . . . . . . .   132
                    Password  . . . . . . . . . . . . . . . . . . . .   132
                    From AKA  . . . . . . . . . . . . . . . . . . . .   132
                    AreaRequest Flags . . . . . . . . . . . . . . . .   133
                    Add Nodes . . . . . . . . . . . . . . . . . . . .   133

          WHAT ARE POINT ADDRESSES? . . . . . . . . . . . . . . . . .   135
               BOSS NODE  . . . . . . . . . . . . . . . . . . . . . .   135
               ADDRESSING SCHEMES . . . . . . . . . . . . . . . . . .   136

          POINT DESCRIPTIONS  . . . . . . . . . . . . . . . . . . . .   136
               3D POINT ADDRESSES . . . . . . . . . . . . . . . . . .   136
               FAKENET ADDRESS  . . . . . . . . . . . . . . . . . . .   137
               DESIGN CHANGE  . . . . . . . . . . . . . . . . . . . .   137
               4D ADDRESSING  . . . . . . . . . . . . . . . . . . . .   138

          POINT CONFIGURATIONS  . . . . . . . . . . . . . . . . . . .   139

          USING 3D ADDRESSING FOR POINTS  . . . . . . . . . . . . . .   139
               IF YOU'RE A BOSS NODE  . . . . . . . . . . . . . . . .   139
               IF YOU'RE A 3D POINT . . . . . . . . . . . . . . . . .   140

          USING 4D ADDRESSING FOR POINTS  . . . . . . . . . . . . . .   142
               IF YOU'RE A BOSS NODE  . . . . . . . . . . . . . . . .   142
               IF YOU'RE A 4D POINT . . . . . . . . . . . . . . . . .   142

          TROUBLESHOOTING . . . . . . . . . . . . . . . . . . . . . .   144
               COMMON QUESTIONS/PROBLEMS  . . . . . . . . . . . . . .   144
               LOGGING INFORMATION  . . . . . . . . . . . . . . . . .   150
               WILDCAT! ERROR.LOG FILE  . . . . . . . . . . . . . . .   150

          LICENSING AND DISTRIBUTION AGREEMENT  . . . . . . . . . . .   151

          NO WARRANTY . . . . . . . . . . . . . . . . . . . . . . . .   153

          TECHNICAL SUPPORT . . . . . . . . . . . . . . . . . . . . .   154

          30 DAY EVALUATION COPY  . . . . . . . . . . . . . . . . . .   154




          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                      Page  viii



          WILDMAIL! v3.01                                 TABLE OF CONTENTS
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

          TECHNICAL SPECIFICATIONS  . . . . . . . . . . . . . . . . .   155
               Memory Requirements  . . . . . . . . . . . . . . . . .   155
               Conference Areas Supported . . . . . . . . . . . . . .   155
               Node Addresses . . . . . . . . . . . . . . . . . . . .   156
               Downlink Nodes per Conference  . . . . . . . . . . . .   156
               Tossing Mail in Date/Time Order  . . . . . . . . . . .   156
               Large Messages . . . . . . . . . . . . . . . . . . . .   156
               Message Size Limitation  . . . . . . . . . . . . . . .   157
               No Content/Null Messages . . . . . . . . . . . . . . .   157
               Maximum AKA Addresses  . . . . . . . . . . . . . . . .   157
               Maximum Forward Lists  . . . . . . . . . . . . . . . .   157
               Maximum Area Manager Aliases . . . . . . . . . . . . .   157
               Maximum AreaRequest Flags  . . . . . . . . . . . . . .   157
               Maximum Zone Assignments . . . . . . . . . . . . . . .   157

          APPENDIX A - PACKER/UNPACKER PARAMETERS . . . . . . . . . .   158
               ARCA v1.28 . . . . . . . . . . . . . . . . . . . . . .   158
               ARCE v3.1b . . . . . . . . . . . . . . . . . . . . . .   158
               PKARC v3.5 . . . . . . . . . . . . . . . . . . . . . .   159
               PKXARC v3.5  . . . . . . . . . . . . . . . . . . . . .   159
               PKPAK Version 3.61 . . . . . . . . . . . . . . . . . .   160
               PKUNPAK Version 3.61 . . . . . . . . . . . . . . . . .   161
               ARJ 2.30 . . . . . . . . . . . . . . . . . . . . . . .   162
               LHARC  v1.13c  . . . . . . . . . . . . . . . . . . . .   163
               LHA version 2.13 . . . . . . . . . . . . . . . . . . .   164
               PAK  . . . . . . . . . . . . . . . . . . . . . . . . .   165
               PKZIP (R) v1.10  . . . . . . . . . . . . . . . . . . .   166
               PKUNZIP (R) v1.10  . . . . . . . . . . . . . . . . . .   167
               ZOO archiver v2.00 . . . . . . . . . . . . . . . . . .   168

          APPENDIX B - FRONTDOOR/INTERMAIL SYSTEMS  . . . . . . . . .   169

          ASSOCIATED BATCH FILES  . . . . . . . . . . . . . . . . . .   169
               CAT.BAT  . . . . . . . . . . . . . . . . . . . . . . .   169
               DOBBS.BAT  . . . . . . . . . . . . . . . . . . . . . .   169
               EXEBBS.BAT . . . . . . . . . . . . . . . . . . . . . .   169

          SYSTEM FLOW . . . . . . . . . . . . . . . . . . . . . . . .   170
               CAT.BAT FILE . . . . . . . . . . . . . . . . . . . . .   172
               DOBBS.BAT FILE . . . . . . . . . . . . . . . . . . . .   175
               EXEBBS.BAT FILE  . . . . . . . . . . . . . . . . . . .   176
                    InterMail Systems . . . . . . . . . . . . . . . .   176

          APPENDIX C - WHAT IS NETMAIL/ECHOMAIL?  . . . . . . . . . .   179
               System Addressing  . . . . . . . . . . . . . . . . . .   179
               File Attachments . . . . . . . . . . . . . . . . . . .   179
               Sharing Message Bases  . . . . . . . . . . . . . . . .   179
               Hub Creation . . . . . . . . . . . . . . . . . . . . .   181



          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                        Page  ix



          WILDMAIL! v3.01                                 TABLE OF CONTENTS
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

               Netmail Definition . . . . . . . . . . . . . . . . . .   182
               Echomail Definition  . . . . . . . . . . . . . . . . .   182
               Summary  . . . . . . . . . . . . . . . . . . . . . . .   183

          APPENDIX D - OBTAINING A NODE NUMBER  . . . . . . . . . . .   184
               Which Network to Join  . . . . . . . . . . . . . . . .   184
               What's a Nodelist  . . . . . . . . . . . . . . . . . .   184
               Obtaining a Nodelist . . . . . . . . . . . . . . . . .   184
               Locating the Closest Hub . . . . . . . . . . . . . . .   185
               Contacting the Hub SysOp . . . . . . . . . . . . . . .   185
               Netmail Transfer Capability  . . . . . . . . . . . . .   186
               Receiving Your Node Address  . . . . . . . . . . . . .   186

          APPENDIX E - PERFORMANCE TUNING . . . . . . . . . . . . . .   187
               Disk Caching Software  . . . . . . . . . . . . . . . .   187
               DOS File Count Limitation  . . . . . . . . . . . . . .   188
               Database Safety Mode . . . . . . . . . . . . . . . . .   190
               Maintain Message Level Limits  . . . . . . . . . . . .   192
               Preprocessing Mail Deliveries  . . . . . . . . . . . .   193
               Summary  . . . . . . . . . . . . . . . . . . . . . . .   193

          APPENDIX F - ERRORS UNCOMPRESSING MAIL  . . . . . . . . . .   195
               Errorlevel Checking  . . . . . . . . . . . . . . . . .   195
               Logfile Entries  . . . . . . . . . . . . . . . . . . .   195

          APPENDIX G - PATH: AND SEEN-BY: LINES . . . . . . . . . . .   196

          MASTER INDEX LISTING  . . . . . . . . . . . . . . . . . . .   198























          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                         Page  x



          WILDMAIL! v3.01                                      INTRODUCTION
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

          INTRODUCTION

          Online Computer Resources is a third party software developer for
          WILDCAT! BBS systems.  We have been producing utility programs
          for over 5 years now and have been running Bulletin Boards since
          early '87.  Over that period of time we've accumulated a vast
          amount of experience in the management and implementation side of
          BBSing.  We bring forward that experience in the software that we
          develop by offering ease of use and powerful features.

          WILDMAIL! was born out of a need from Mustang Software Inc., the
          authors of WILDCAT! BBS software, to have echomail messages
          tossed into and out of their message databases for WILDCAT! v3.0. 
          At first we were a bit reluctant because of the magnitude of the
          project, but having been involved in the early beginnings of
          echomail, we knew we could produce an all in one package that
          would greatly simplify the old archaic methods of the past.

          In the early days of WILDMAIL!, we attended the school of hard
          knocks, and learned probably more than we wanted to about the
          echomail arena and the people that use it, and have applied what
          we've learned to this release.  We think you'll find that v3.00
          far exceeds your expectations, and will provide you with many
          pleasurable hours of trouble free echomail use.


          WHAT IS WILDMAIL!

          WILDMAIL! v3.01 is an echomail processor for WILDCAT! v3.xx BBS
          systems and BBS's that support the .MSG format.  WILDMAIL!
          processes standard Fidonet compatible mail for transmission by
          FrontDoor, D'Bridge, InterMail or BinkleyTerm.  It also processes
          specially formatted Netmail messages used by your downlink nodes
          to automatically activate and or deactivate message conferences.

          After unpacking, WILDMAIL! processes the .PKT files and tosses
          the messages contained within them into either .MSG files or
          directly into the corresponding message conferences.  It also
          forwards messages to the Uplink and Downlink Node addresses
          specified in the configuration.  

          WILDMAIL! will also extract new messages from the WILDCAT!
          message databases and output them into the Fidonet standard .PKT
          format.  It will then bundle up the PKT files creating a standard
          Fidonet mail archive and pass that to the front end mailer to
          process as outbound mail.

          A new feature for v3.00 is AreaRequest.  This is a powerful



          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                         Page  1



          WILDMAIL! v3.01                                      INTRODUCTION
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

          feature allowing your downlink node addresses to turn on/off
          conferences to their system automatically by the use of Netmail
          messages.  This relieves you from having to manually toggle these
          conferences on or off.  When a request comes in for a conference
          that you don't carry on your system, WILDMAIL! will automatically
          generate a message to your Uplink address requesting the new
          conference.  Once it's received, it will be activated for the
          requesting node.


          Multiline Operation

          As with all previous releases, you may execute WILDMAIL! while
          your multiline copy of WILDCAT! is up and running.  Notice the
          key word here is multiline.  You MUST have the multiline copy of
          WILDCAT! otherwise you run the risk of corrupting your message
          databases.

          WILDMAIL! fully supports file locking/sharing in the WILDCAT!
          environment.  It obtains the necessary information about the type
          of multiline environment like DOS Share, Novell and so on from
          the WILDCAT! configuration files.

          Currently only one copy of WILDMAIL! may be executing at any
          time.  The key word here is executing!  If you attempt to run
          another copy of WILDMAIL! while the first is running, a message
          is displayed stating so and the second copy's execution is
          aborted.  This also holds true for WMUTIL! and WMCONFIG! which
          use the same configuration and database files.  The bottom line
          here is simple, only one program may access WILDMAIL!'s data
          files at any given time.


          Single Line Systems

          If you have the single line version of WILDCAT!, before executing
          WILDMAIL!, you must bring your WILDCAT! system down and then
          start the mail process.  There are *no* exceptions to this.













          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                         Page  2



          WILDMAIL! v3.01                                     FEATURES LIST
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

          FEATURES LIST

          WILDMAIL! v3.00 can easily be considered a feature rich mail
          processor that performs many functions that most systems will
          never use.  It does so in a manner that won't get you lost in all
          the technical mumbo jumbo of todays high tech world of echomail. 
          For those systems that need these advanced features, you'll
          appreciate the clarity of presentation and usefulness of the
          power that is available to you.

          Shown below is a partial list of the features of both WMCONFIG!,
          the configuration program, and WILDMAIL!, the actual mail tosser.


               WMCONFIG! Features

                    o    Protected operating mode, prevents changes
                    o    25/43/50 line CRT video modes
                    o    Context sensitive online help
                    o    User friendly interface
                    o    Shell to DOS
                    o    Automatic configuration verification
                    o    Global change for Nodes/Conferences
                    o    Extracts conference info from WILDCAT!
                    o    Automatic Origin line length checking
                    o    After edit, automatic Origin line updating
                    o    Network specific accounting definition
                    o    User defined defaults for Node/Conferences
                    o    Protected fields dictated by configuration


          Due to the fact that multiline systems are becoming more and more
          popular, when WMCONFIG! obtains and/or saves information into the
          various databases, it fully supports file locking and sharing. 
          So you may safely execute WMCONFIG! when your multiline WILDCAT!
          BBS is up and running.  However, you may not execute WMCONFIG! or
          WMUTIL! when WILDMAIL! is processing mail.














          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                         Page  3



          WILDMAIL! v3.01                                     FEATURES LIST
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

          WILDMAIL! Features

          GENERAL

               o    Significantly increased performance
               o    Separate Echomail and Netmail processing
               o    PreTossing for significant speed gains
               o    True four dimensional addressing (4D)
               o    Outbound PKT size definition
               o    FredMail and Multi-Zone Gating support
               o    Packer/parameters definition for Binkley
               o    Exclude specific names from Netmail importation
               o    Direct D'Bridge outbound queue support
               o    Swap file path definition
               o    Inbound/Outbound zone matching
               o    Conference level manager for Origin lines
               o    Primary origin line definition
               o    Default Node and Conference definitions
               o    Automatic conference activation/deactivation
               o    Disable conference activation/deactivation

          NODE SPECIFIC

               o    Active/Inactive status
               o    Type 2 and Type 2+ PKT output formats
               o    Mail status flag - Hold, Crash, None
               o    PKT level password assignment
               o    AreaRequest security and flag assignments
               o    Zone gating output path definition
               o    Complete accounting information
               o    Strip SEENBY line information
               o    Selectable archive naming convention

          CONFERENCE SPECIFIC

               o    Active/Inactive status
               o    Long descriptions (can be read from WILDCAT!)
               o    Origin address definition
               o    Origin line selection
               o    Originating Node or Uplink/Feed address
               o    Extract private echomail
               o    Restrict import of mail from undefined addresses
               o    Extract echomail file attachments
               o    AreaRequest Security and Flag assignments
               o    SEEN-BY: line processing - Display, Hide or Delete
               o    Add selected addresses to SEEN-BY: lines





          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                         Page  4



          WILDMAIL! v3.01                                 30 DAY EVALUATION
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

          30 DAY EVALUATION KEY FILE

          WILDMAIL! utilizes a special file to activate its usage for a
          period of 30 days.  This method allows the program to be fully
          utilized with all options enabled for the duration of the
          evaluation period.  If the product hasn't been registered after
          the thirty days, WILDMAIL! will inform you it has expired and
          will simply cease to run. 

          Since the current method of distribution prevents a "dated" key
          file from being included in the distribution archive files, you
          must dial up the support board (listed below) and create this
          special key file.  The Main Menu option "Create Evaluation Keys"
          initiates this process and you simply enter in the required
          information and then follow the instructions for downloading.

          The WILDMAIL! support board may reached by dialing:

                         (707) 552-0602 - USR HST (2 lines)
                         (707) 552-0636 - v32bis  (3 lines)
                         (707) 552-2344 - USR DS  (2 lines)

          Only one key per person/registration number will be allowed. 



          FREDMAIL AND MAIL GATING

          In todays complex world of mail transfers, it's common for
          systems to gate mail from one network to another.  This means
          messages from one network could be sent to another network.  This
          process involves some very special handling in order to operate
          properly.  

          WILDMAIL! now permits you to create outbound mail in raw,
          uncompressed PKT file format in any directory you specify on a
          node by node basis.  This feature coupled with the Tiny SEENBYs
          option (this strips out all the SEENBY information from the
          messages and only puts the Origin and Destination address in the
          SEENBY lines) allows you quite a bit of control in this area. 
          Since this is performed on a node basis, you may have as many
          gates as you need limited only by available disk space.

          For those systems running FrEdMail, this provides an incredibly
          easy way of tying your system into the Internet.  Simply create a
          fake node address, specify mail type as NONE and enter the path
          to FrEdMails inbound directory and you're off and running.




          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                         Page  5



          WILDMAIL! v3.01                    DEVELOPMENTAL CYCLE WITH v3.00
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

          DEVELOPMENTAL CYCLE WITH v3.00

          With the initial release in August of 1991, WILDMAIL! has always
          strived for reliable performance with more and more features. 
          Over the course of its existence, quite a number of people have
          become more and more dependant on its capabilities and have
          constantly pushed for its further development.  For almost two
          years this product has been growing at a steady pace and has
          finally outlived its original design specifications.  

          Ever since v1.00 was released, we've been keeping track of all
          the features that people have been asking for and making notes
          for future reference.  A lot of the requested features could only
          be implemented with a complete redesign of the product but we
          kept the ideas anyway.  Well that time had come upon us a bit
          faster than we expected.

          Being the company that we are, we couldn't sit on our hands and
          just be happy with the status quo.  We decided back in March of
          1992 to start the major rewrite of the program.  We knew when we
          first released v1.00 that the ASCII text file configuration
          formats would have to go.  They were the single most important
          source of all the support calls.  We, along with our customers,
          absolutely hated them!  


          CONFIGURATION PROGRAM

          Because of the complexities of echomail, we were committed to
          creating a configuration program that would be smart enough to
          know the requirements of echomail plus ensure that the user
          entered in the correct information.  This would eliminate much of
          the misconfiguration problems that we'd experienced in the v1-v2
          releases.  

          So, as with any development project, we all rolled up our sleeves
          and went to work.  We sent Eric off with a brand new PC and the
          BP v7.0 compiler loaded and he went to work on the configuration
          program.  He started off by adding in all the current features of
          WILDMAIL! and built upon that.  Once that was accomplished, we
          wanted to really have some fun, so we grabbed that big wish list
          of features we've been keeping all this time, and started
          dreaming and planning.  

          As luck would have it, reality settled in and we realized we
          couldn't do the things we wanted to with the original design
          plans.  So back to the drawing board and this time, we thought it
          out much more thoroughly and came up with a very flexible



          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                         Page  6



          WILDMAIL! v3.01                    DEVELOPMENTAL CYCLE WITH v3.00
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

          platform that took kindly to new features.  So we picked up that
          wish list again and went back to work.

          Now things were starting to happen.  More and more features
          started to appear, some working and some sort of.  There were
          several times where complete sections of the configuration
          program were continually changing and being rewritten because of
          the constant birth of new and more useful features.  An
          incredible amount of time was spent running around in circles
          until we got it just right.  After all the dust had settled, we
          realized we had come up with an incredible package worthy of the
          most critical of scrutiny.  But that was only the configuration
          program!


          MAIL TOSSER

          Work then began on getting WILDMAIL! to actually do all of this. 
          But we had faith in Derek (the mastermind behind WILDMAIL!).  If
          we could keep him pinned down behind his PC long enough, we knew
          he could do it.  After much mental brow beating, and even a brand
          new 486 machine with a 17" SVGA monitor, we got him started.  He
          struggled, complained, moaned and groaned but continued to hammer
          away (and he really liked the 17" monitor).  Finally, after a
          couple of days had gone by he said, "here try this!".  We said
          great, but what if we do this, then we could add that!  

          One thing led to another and we realized we needed to add a bit
          more to the configuration program, so Eric was back at it again
          adding more features.  Then there finally came a point where we
          said "This has to end, we're having way too much fun here!".  So
          we decided to save the rest of the ideas for future releases of
          WILDMAIL! and began work on all the support utilities and
          accompanying documentation needed for this release. 


          CONCLUSION

          WILDMAIL! v3.01 represents what we think a mail tosser should be. 
          It has taken over a year to complete and incorporates some
          features and innovations that no other tosser on the market has
          (or has even thought of) and provides a degree of configurability
          second to none.  We're extremely proud of this release and are
          confident that you'll be too!

          As part of any professionally written package, we've attempted to
          be as thorough as possible with the documentation.  We've tried
          to target the novice user as much as possible because echomail is



          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                         Page  7



          WILDMAIL! v3.01                    DEVELOPMENTAL CYCLE WITH v3.00
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

          such a complex world, and we felt it necessary to put down in
          paper what a lot of experienced echomail users have known for
          years.  Hopefully, this will make it easier for those folks that
          are just now getting into this fascinating field.


          REGISTRATION/ORDERING INFORMATION

          International and USA orders are handled by us at Online Computer
          Resources.  Please see the enclosed REGISTER.DOC file for full
          ordering information.


          REGISTRATION FEE

          Registration price for WILDMAIL! v3.01 is $65 plus $5 shipping
          and handling.  California orders MUST include 7.25% on the $65
          portion for local taxes.


          PAYMENT METHOD

          You may register the product several ways.  You can call up the
          support BBS and use the online questionnaire, you can fill out
          the enclosed registration form and mail it in.  Or you may call
          us directly Monday through Friday 9am-6pm PST and place a credit
          card order.  We presently accept VISA, MasterCard and Discover. 
          For those people that pay by check, there is a 10 day hold period
          to allow sufficient time for your check to clear the bank.


          KEY GENERATION

          For those people that register over the phone using a credit
          card, we can usually generate your registered key file on the
          spot and have it up for download on our BBS before 5pm (PST) the
          same day.

          If you send in your registration making payment via check and
          your evaluation period is about the expire, we can put up another
          30 day key to allow you to continue to toss mail until the 10 day
          hold period on your check is up.

          For all orders, in addition to putting up your registered key
          file for download, we'll create a diskette and put the most
          current release on it along with your registered key file and
          mail it off to you.




          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                         Page  8



          WILDMAIL! v3.01                    DEVELOPMENTAL CYCLE WITH v3.00
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

          UPGRADE FROM PREVIOUS v1.xx/v2.xx to v3.01

          Registered WILDMAIL! users can upgrade their current release for
          $15 plus $5 shipping and handling.  CA residents must add 7.25%. 
          Simply send in the UPGRADE.DOC form enclosing your payment.














































          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                         Page  9



          WILDMAIL! v3.01                                    FILES INCLUDED
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

          FILES INCLUDED

          Your WILDMAIL! installation kit is distributed in three separate
          compressed files.  The names and contents of these files are
          listed below:

          WM301-1.ZIP - WILDMAIL! Executable/Documentation

               README.1ST     Any last minute changes/additions that
                              weren't included in the WM.DOC file.

               WM.EXE         Main executable file.

               WM.OVR         Overlay file.

               WM30.DOC       Extensive documentation file.


          WM301-2.ZIP - Configuration Program/Online Help

               WMCONFIG.EXE   Configuration program for WILDMAIL!

               WMCONFIG.HLP   Online context sensitive help file.


          WM301-3.ZIP - Upgrade Utility/Sample batch files

               WMINSTAL.EXE   Upgrade program to convert previous versions
                              of WILDMAIL! to v3.00.

               WMUTIL.EXE     Database repair, configuration report
                              generation and AREAS.BBS export/import
                              program.

               WMUTIL.HLP     Help file used by WMUTIL!

               WMUTIL.DOC     Documentation file for WMUTIL!

               REGISTER.DOC   Mail in registration form.

               FD-CFG.ZIP     FrontDoor sample batch files.
               BI-CFG.ZIP     BinkleyTerm sample batch files.
               DB-CFG.ZIP     D'Bridge sample batch files.


          If you are missing any of the above distribution files, please
          call the WILDMAIL! support BBS and download the appropriate one.




          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                        Page  10



          WILDMAIL! v3.01                    UPGRADE FROM PREVIOUS RELEASES
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

          UPGRADE FROM PREVIOUS RELEASES

          As with any major release, there's usually some form of structure
          change that makes it incompatible with any of the earlier
          releases.  Unfortunately, this is the case here with WILDMAIL!
          v3.00.


          UPGRADE PROCESS

          Because of all the time and effort you've spent configuring your
          system, we've created a program to simplify the upgrade process,
          called WMINSTAL.  This is a standalone utility that reads the
          contents of your old AREAS.BBS, WM.CFG files and optionally the
          contents of your AREAFIX.CTL file.  It then imports this
          information into the new database structures of WILDMAIL! v3.01. 

          This is a very fast and painless process for you to perform and
          it protects all the time and effort you've put into your current
          configuration.  Shown below is the step by step process to
          upgrade to WILDMAIL! v3.01.

               1)   Create a subdirectory called WM30.  Typically this can
                    be done from the DOS prompt by entering MD \WM30.

               2)   Change to this new directory by typing CD \WM30.

               3)   Copy the new WILDMAIL! distribution files called 

                         WM301-1.ZIP    WM301-2.ZIP    WM301-3.ZIP

                    into the \WM30 directory and uncompress them by using
                    the command PKUNZIP WM301*.ZIP.

               4)   Using your favorite printing utility, print the
                    contents of the WM30.DOC file.  If you don't have a
                    utility that does this, you could use the DOS command

                              copy WM30.DOC LPT1

                    followed by pressing [ENTER].  You should definitely
                    have the documentation handy when the conversion
                    process is completed because you'll have quite an array
                    of features to work with now.

               5)   Copy your AREAS.BBS and WM.CFG files from your old
                    WILDMAIL directory into the new \WM30 directory.  




          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                        Page  11



          WILDMAIL! v3.01                    UPGRADE FROM PREVIOUS RELEASES
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

               6)   If you're running AREAFIX, copy your AREAFIX.CTL file
                    into the \WM30 directory.

               7)   At the DOS prompt, type in WMINSTAL and press [ENTER]. 
                    You should now see a Main Menu selection screen. 
                    Position the highlight bar by using the Up/Dn arrow
                    keys on the option:

                              Upgrade WILDMAIL! v1.+ to v3.00

                    and press [ENTER].

               8)   A new screen is displayed with a list of processes to
                    complete, and various statistical information.  Press
                    [F10] to start the conversion process or [ESC] to quit
                    and return to the previous screen.  After pressing
                    [F10], WMINSTAL will proceed to convert the information
                    found in the AREAS.BBS, WM.CFG and AREAFIX.CTL files.  

                    Once the process is complete, pressing [ESC] will
                    return you to the menu selection screen.

               9)   Position the highlight bar on the menu selection

                              Important Upgrade Information

                    and press [ENTER].  A new screen comes up that allows
                    you to browse through the contents of a changes file
                    called UPGRADE.WM3.  This file contains information
                    about the upgrade process and any last minute changes
                    that didn't make it into the final copy of the WM30.DOC
                    file.

                    You may use the PgUp/PgDn and Up/Dn arrow keys to
                    scroll about the screen.  When you've finished viewing
                    this information, press [ESC] and you will be returned
                    to the Main Menu.  Pressing [ESC] a second time returns
                    you to the DOS prompt.

               10)  The conversion process is now complete and you are
                    ready to run the configuration program for WILDMAIL!. 
                    At the DOS prompt type in WMCONFIG and press [ENTER].  


          At this point, you should now have the documentation handy that
          was printed out in step #4 for easy reference.  You should go
          through all the options making sure the information from your old
          AREAS.BBS and WM.CFG files, and AREAFIX.CTL if it was found, has



          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                        Page  12



          WILDMAIL! v3.01                    UPGRADE FROM PREVIOUS RELEASES
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

          been correctly imported and make any necessary changes.

          When you are satisfied with the configuration, press [ESC] from
          the Main Menu allows you to exit and save the configuration.  You
          should now review the changes to the command line parameters in
          the following section before executing WILDMAIL! for the first
          time.


          D'BRIDGE USERS

          In previous versions of WILDMAIL!, a special "unknown" outbound
          directory was required to prevent D'Bridge from deleting the
          outbound mail created by WILDMAIL!.  This release now fully
          supports D'Bridges internal queue structure so you will need to
          update the outbound path settings in WMCONFIG! to reflect the
          same directory as where D'Bridges queue directory is located.


          DUPLICATE CHECKING

          With this new release comes new and more advanced methods of
          checking for duplicate messages.  Because of this, your old
          duplicates database files called WILDDUPS.DAT/.IX will no longer
          be compatible with this release.

          Consequently, for the next few mail runs, your system will have
          to build a completely new list of messages to check. This is done
          automatically and there is no method by which you can convert
          your existing duplicate database over.  

          Because of this, there is a slight chance that if duplicate
          messages do come to your system, they may not be caught by
          WILDMAIL!.  Fortunately, this will only be for the first couple
          of mail runs after the conversion and from that point on, your
          system should have built up enough of a duplicates database of
          messages to effectively catch them in the future.


          KEY FILE CHANGES

          Because this release of WILDMAIL! is a major update, all
          previously registered key files will no longer work with v3.01. 
          If you've registered v2.xx, there is an update fee of $15 + $5
          shipping and handling.  If you're trying WILDMAIL! out for the
          first time, you will need a 30 day eval key before you may use
          the program which is obtainable by dialing the Support BBS.




          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                        Page  13



          WILDMAIL! v3.01                    COMMAND LINE PARAMETER CHANGES
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

          COMMAND LINE PARAMETER CHANGES

          WILDMAIL! now has the ability to process Netmail and Echomail
          separately.  Because of this, new command line parameters were
          necessary and some of the existing ones were modified.  Shown
          below is a list of the differences.

          TOSS      In previous releases, this option would toss both
                    Netmail and Echomail messages into their respective
                    conferences.  Now this will only toss Echomail messages
                    leaving the Netmail messages untouched.

          SCAN      This parameter used to scan both the Netmail and
                    Echomail message bases and extract any new mail and
                    process it accordingly.  Now this will only scan the
                    Echomail message bases and leave the Netmail messages
                    untouched.

          MAILIN    This new parameter will toss any newly received Netmail
                    messages into the Netmail conference and leave the
                    inbound echomail bundles untouched.  This means that
                    only Netmail messages would get tossed and any pending
                    Echomail bundles would be left alone.

          MAILOUT   This new parameter will scan the Netmail conference for
                    any new messages and extract them accordingly leaving
                    the new Echomail messages completely untouched.  So any
                    new Echomail messages would not be extracted, only
                    Netmail.

          NETMAIL   This new parameter incorporates the features of both
                    the MAILIN and MAILOUT command line parameters.  This
                    means if you do a TOSS and SCAN, WILDMAIL! will extract
                    and toss Echomail messages.  By adding this parameter
                    it will now extract and toss the Netmail messages at
                    the same time. 


          The NETMAIL parameter (combined with the TOSS and SCAN
          parameters) effectively does the same thing as the old TOSS and
          SCAN parameters used to do.  So for the vast majority of the
          systems, this is the command line parameter that MUST be added to
          your existing batch files when you execute WILDMAIL!  

          NOTE:     If you run the new version of WILDMAIL! without adding
                    this parameter (or either the MAILIN or MAILOUT
                    parameters), your Netmail messages both inbound and
                    outbound will not be processed!



          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                        Page  14



          WILDMAIL! v3.01                      NECESSARY BATCH FILE CHANGES
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

          NECESSARY BATCH FILE CHANGES

          If you've just upgraded from the previous release of WILDMAIL!,
          because of the various changes in this release, you MUST go back
          and make the necessary changes to your batch files that execute
          WILDMAIL!.  Otherwise your system will still execute the previous
          version and not this new release!  Shown below is a brief list of
          changes that must be made.


          WILDMAIL! Directory

               As part of the upgrade process, you were required to create
               a directory called \WM30.  In previous versions you could
               place all the WILDMAIL! specific files into a directory of
               your choice.  Because of this directory change, you now MUST
               go back and edit any and all batch files that your system
               uses to execute WILDMAIL!.  

               You should make sure that you use the command CD \WM30 in
               place of the old CD \WILDMAIL (or what ever directory you
               executed WILDMAIL! from).  This ensures that you'll execute
               WILDMAIL! from the new directory.


          Command Line Parameters

               Because of the changes to the TOSS and SCAN command line
               parameters, you MUST go back and change the appropriate
               batch files that execute WILDMAIL! to add in either the
               MAILIN, MAILOUT or NETMAIL command line parameters.  If you
               don't, the Netmail on your system will just sit and not be
               tossed or extracted.  

               For additional information on the use of these parameters,
               please refer to the COMMAND LINE PARAMETERS section of this
               documentation.


          WILDMAIL! File Name

               WILDMAIL! v3.01 uses the exact same executable file as in
               previous releases.  So no changes need to be made in this
               area.







          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                        Page  15



          WILDMAIL! v3.01                      NECESSARY BATCH FILE CHANGES
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

          AreaFix Deactivation

               If you were previously using AreaFix and have enabled the
               AreaRequest Manager portion in WMCONFIG!, then you should
               modify the main batch file that used to run AreaFix and
               comment that section out.  Otherwise, AreaFix might grab the
               Netmail messages before AreaRequest does and attempt to make
               changes that won't be interpreted by WILDMAIL!.

               In addition, you should also go back and make sure you are
               executing WILDMAIL! with the AREAMGR command line parameter
               to invoke the AreaRequest Manager.  Otherwise, all your
               AreaFix style messages will just sit and not be processed. 
               For specifics on this parameter, please refer to the command
               line parameter section of this documentation.




































          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                        Page  16



          WILDMAIL! v3.01                              POST UPGRADE CLEANUP
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

          POST UPGRADE CLEANUP

          As part of the upgrade process, you created a new subdirectory
          called \WM30 and recreated your entire setup there.  Then you
          changed your batch files to use this new version.  This was done
          to allow you to have your old release completely intact should
          you encounter difficulties along the way that could not be
          resolved in a reasonable amount of time.  This would make it very
          easy to switch back to the old release in case you needed to.

          After successfully running WILDMAIL! v3.01 for a few days, you
          should take a few moments and do a little cleanup work.  Because
          you now have multiple copies of WILDMAIL! on your system taking
          up unnecessary disk space, you should go back and delete all the
          old WILDMAIL! files and even remove the directory it used to be
          executed from.

           
          WILDMAIL! Directory

               Something that should be pointed out is that the directory
               that WILDMAIL! v3.01 executes in doesn't HAVE to be called
               \WM30.  It may be called any name you desire and placed on
               any drive as long as you change to that <drive:\directory>
               before executing WILDMAIL!.  It must however contain all the
               necessary files for proper operation.  Please refer to the
               appropriate section in this documentation for the exact file
               names.

               As was mentioned earlier, the \WM30 directory was created to
               allow you to have two sets of WILDMAIL! at the same time in
               case of difficulties.


          Old Origin Lines

               One of the functions of WMINSTAL was to go out and retrieve
               all of your ORIGIN.nnn files (where nnn equals the
               conference number) from the WILDCAT! message directories and
               put them into WMCONFIG!'s internal database format.  Since
               those files are no longer used, you should go back into each
               directory they reside in and delete them.

               As mentioned in the Performance Tuning section in the back
               of this documentation, you should limit the files contained
               within the message subdirectories, so removing these old
               files is important!




          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                        Page  17



          WILDMAIL! v3.01                              POST UPGRADE CLEANUP
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

          AreaFix Directory

               For those systems that were running AreaFix and have enabled
               the AreaRequest Manager portion of WILDMAIL!, once you are
               satisfied with the performance of AreaRequest, you should
               remove it from your system.  Otherwise, it will just be
               sitting on your hard disk taking up precious disk space for
               no reason.


          WMINSTAL!

               This program along with its associated UPGRADE.WM3 file is
               only used to upgrade your system from v2.xx series to the
               most current release.  Once the process is complete, there's
               no real reason to have it on your system.  You may delete
               this from the \WM30 directory any time after the upgrade
               process.

               For whatever reason, you should always maintain a copy of it
               on diskette somewhere should it be needed at some point in
               the future.





























          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                        Page  18



          WILDMAIL! v3.01                           FIRST TIME INSTALLATION
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

          FIRST TIME INSTALLATION

          First time installations of any product can be a taxing process
          at times, especially with a complex product such as WILDMAIL!. 
          Although the product has been designed to be as user friendly as
          possible, there's simply no substitute for experience.  If you're
          new to echomail, the best advice we can offer is to take your
          time, read the documentation and have it handy when you go
          through all the options.  

          If you're an old hand at this, you'll appreciate some of the more
          advanced features available to you, but don't overlook the
          documentation.  An extensive amount of effort has been applied in
          this area in order to be as informative and insightful as
          possible, hopefully allowing you to understand the reasons for
          each of the various options.  We think you'll agree, there is a
          wealth of information contained within these pages!

          Shown below is the step by step process to perform an initial
          installation of WILDMAIL! v3.01.

               1)   Create a subdirectory called WM30.  Typically this can
                    be done from the DOS prompt by entering MD \WM30.

               2)   Change to this new directory by typing CD \WM30.

               3)   Copy the new WILDMAIL! distribution files called 

                         WM301-1.ZIP    WM301-2.ZIP    WM301-3.ZIP

                    into the \WM30 directory and uncompress them by using
                    the command PKUNZIP WM301*.ZIP.

               4)   Using your favorite printing utility, print the
                    contents of the WM30.DOC file.  If you don't have a
                    utility that does this, you could use the DOS command

                              copy WM30.DOC LPT1

                    followed by pressing [ENTER].  You should definitely
                    have the documentation handy when the conversion
                    process is completed because you'll have quite an array
                    of features to work with now.

               5)   At the DOS prompt type in WMCONFIG and press [ENTER].  


          At this point, you should now have the documentation handy that



          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                        Page  19



          WILDMAIL! v3.01                           FIRST TIME INSTALLATION
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

          was printed out in step #4 for easy reference.  You should go
          through all the options available making any necessary changes.

          At any point within the configuration program if you have any
          questions regarding a certain option, simply position the
          highlight bar on that field and press [F1].  This brings up help
          information specific to the field the cursor is on.  When you're
          satisfied with the configuration, pressing [ESC] from the Main
          Menu allows you to exit and save the configuration.


          CONVERTING OVER FROM A NON-WILDMAIL! TOSSER

          If you are performing a first time installation and are
          converting from another vendors tosser, DO NOT use WMUTIL!'s
          IMPORT option before entering in a minimum configuration.  This
          will cause an incomplete installation and erratic mail processing
          MAY result.  PLEASE BE CAREFUL!

          Instead, simply go thru the above instructions and enter in all
          the information about your system, origin lines and so on. 
          There's no need to enter in the Nodes or Conferences tho.  Once
          this minimum configuration is complete, then and ONLY then can
          you use the IMPORT option of WMUTIL! successfully.


          BATCH FILE ENTRIES

          WILDMAIL! can be executed various ways, but by far the most
          common method is from a batch file.  This can be part of your
          mailers batch file or from the one that executes your BBS.  For
          FrontDoor/Intermail systems, an example set of batch files have
          been included in one of the sections in the back of this
          documentation.

          Typically, you would want to do a minimum of two things in the
          batch file that executes WILDMAIL!.

               1)   Change directories to \WM30 or whatever you call the
                    WILDMAIL! v3.01 directory.

               2)   Execute WILDMAIL! along with the necessary command line
                    parameters.  

          Typically, the command to execute WILDMAIL! would be:

                              WM SCAN TOSS NETMAIL




          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                        Page  20



          WILDMAIL! v3.01                           FIRST TIME INSTALLATION
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

          Of course there are various different methods of doing this, but
          the minimum is to have WILDMAIL! extract any newly created
          messages and to toss any newly received messages.  

          Because WILDMAIL! now supports the ability to process Echomail
          separately from Netmail messages, you should make sure that
          ultimately you are doing both operations.  You don't have to do
          both at the same time, or even the same day, but you should make
          sure that mail that comes to your system is processed and any
          outbound mail is processed as well.

          For additional information, please refer to the command line
          parameter section for the specifics of each of the commands.






































          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                        Page  21



          WILDMAIL! v3.01                                COMMAND LINE USAGE
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

          COMMAND LINE USAGE:

               WM TOSS SCAN NETMAIL AREAMGR MAILIN MAILOUT PRETOSS PACK
                  -O
                  -R<conf #>,<zone:net/node.point>,<starting msg #>
                  -T<conf #>,<extract count>
                  -Q
                  -A
                  -XO -EO -DO

          Below is a list of all the available command line parameters that
          can be used when running WM.


          ?         This will cause WM to display a help screen that allows
                    menu style selection of command line parameters for
                    specific help information.

                         Example Usage:  WM ?

                    From that screen, you will be able to select the
                    desired topic by pressing the corresponding letter. 
                    Pressing [ESC] returns you to the DOS prompt.  Actually
                    any invalid or mis-matched combination of parameters
                    will also invoke the help menu.


          TOSS      This parameter will cause WM to toss messages into
                    their respective message bases.  

                         Example Usage:  WM TOSS

                    This process starts off by scanning your defined
                    BADECHO directory for any .MSG files and if there's a
                    defined conference, tosses them into their respective
                    conferences.  Next, it proceeds to decompress the first
                    mail archive found in the INBOUND directory and then
                    starts the process of tossing/adding echomail messages
                    to their respective conferences.

                    It should be noted that Netmail message will not be
                    processed with this option.

                    If the Maintain message limit option is enabled, then
                    WM will purge the oldest message before adding a new
                    one if the conference is at its defined limit as
                    specified in MAKEWILD.




          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                        Page  22



          WILDMAIL! v3.01                                COMMAND LINE USAGE
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

          SCAN      This is used to search for newly entered echomail style
                    messages, (not Netmail messages) then extracts and
                    forwards them to their downlink and/or Uplink
                    addresses.   

                         Example Usage:  WM SCAN

                    Any new echo mail message found will be packed up for
                    each node in its proper format and a corresponding
                    Netmail file attach message will be generated and
                    placed in the Netmail directory for transmission by
                    your mailer. (Frontdoor/Intermail systems only)


          PRETOSS   This parameter looks in the Preprocessing path for PKT
                    files to toss into the WILDCAT! message bases.  Only
                    mail existing in this directory will be processed. 
                    This option is only functional if you've previously
                    enabled the Preprocessing option.

                         Example Usage: WM PRETOSS

                    It should be noted that this parameter must be the only
                    one in use (at a time) and thus may not be used in
                    combination with any other parameters.


          MAILIN    This command line parameter is similar to the TOSS
                    parameter except it will only toss inbound Netmail
                    messages.  Any echo mail PKT files will not be
                    processed.

                         Example Usage:  WM MAILIN


          MAILOUT   This option is similar to the SCAN option except it
                    only scans for newly entered Netmail messages.  Any new
                    echo mail messages will not be extracted.

                         Example Usage:  WM MAILOUT


          NETMAIL   This command line parameter combines the functions of
                    both the MAILIN and MAILOUT parameters.  Normally this
                    is the command line parameter you will be using the
                    majority of the time.

                         Example Usage:  WM TOSS SCAN NETMAIL



          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                        Page  23



          WILDMAIL! v3.01                                COMMAND LINE USAGE
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

                    The above example is by far the most common usage for
                    tossing and extracting ALL forms of messages found on
                    your system.  


          PACK      This option is only used when BINKLEY has been selected
                    as the Mailer type.  

                         Example Usage:  WM PACK

                    At present WM does not support its own internal
                    packing, bundling and routing of outbound mail.  This
                    parameter will however, call an external program that
                    you have specified in the Mailer specific options from
                    the Main Menu selection, System Information. (for
                    BinkleyTerm systems)


          PURGE     This will maintain the allowable message count defined
                    in MAKEWILD for each message conference configured for
                    your system.  

                         Example Usage:  WM PURGE

                    Normally, this option would be used if you have set the
                    Maintain message levels option to N (under WILDCAT!
                    specific options) and could be run as a scheduled BBS
                    event.  There would be a minor savings in time to
                    process the incoming mail, minimizing downtime of that
                    node for processing mail.  However, disk space will be
                    taken up for those unused blank slots in the message
                    database.


          AREAMGR   This command line parameter is used to invoke the
                    AreaRequest manager.

                         Example Usage: WM AREAMGR

                    For this to operate properly, you must have previously
                    enabled its use by the Main Menu option, AreaRequest
                    Manager, Process AreaRequest Msgs.  With this set to Y,
                    WILDMAIL! will scan the Netmail directory for any names
                    matching those defined and if they have NOT been
                    received, will process them accordingly.  This
                    parameter may be used with others as needed such as
                    TOSS, SCAN, NETMAIL and so on.




          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                        Page  24



          WILDMAIL! v3.01                                COMMAND LINE USAGE
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

          NOTIFY    This option scans the Nodes database and produces a
                    message for each node showing the conferences they are
                    currently picking up from your system.

                         Example Usage: WM NOTIFY

                    This parameter must be the only one used for this
                    option to function properly.  Any nodes that have been
                    configured to be excluded from this feature will not
                    have the message sent to their system.  For specifics
                    on excluding nodes, please refer to the Notify Exclude
                    option found in the AreaRequest Manager section of
                    WMCONFIG!.


          -O        This option enables a cleanup of the outbound
                    directory.  

                         Example Usage:  WM -O

                    Most mailers automatically clean up the outbound
                    directory, so this option would normally not be used. 
                    If your mailer does not clean up the outbound
                    directory, ie. does not delete all the mail archives
                    after transmission, then you should use this option.


          -R<conf #>,<zone:net/node.point>,<starting msg #>

               This option will rescan a specified conference and extract
               mail for the address specified.  

                    Example Usage : WM -R14,1:161/502.0
                                             or
                                    WM -R14,1:161/502,50

               NOTE the placement of the "," between the <conf #>, the
               <zone:net/node.point> and the <starting msg #> as they are
               necessary for proper delimiting of the parameters.  

               The first example would rescan conference number 14 and
               forward that mail to the address 1:161/502.0.  The second
               example would rescan conference number 14 starting at
               message number 50 and forward mail to the address
               1:161/502.0.  The starting message number is optional and if
               left out will force a rescan or extraction of all messages
               in the defined conference.




          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                        Page  25



          WILDMAIL! v3.01                                COMMAND LINE USAGE
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

               For each message scanned out, the ORIGINAL Origin, SEEN-BY:
               and PATH: lines will be stripped out.  


               CAUTION!

               Because of the potential of creating duplicate messages in
               the network, this option can be disastrous if you don't
               fully understand what you are doing. CAUTION IS STRONGLY
               ADVISED! 


          -T<conf #>,<last extracted msg #>

               Resets the last extract message count to the number
               specified for the conference.  

                    Example Usage:  WM -T14,100

               Note the "," comma between the <conf #> and the <last
               extracted msg #> as well as the conference number NEXT to
               the -T parameter (no spaces).  The above example would reset
               the last extract number in conference 14 to 100.  All
               messages numbered ABOVE 100 would then be sent during the
               next execution of "WM SCAN".  


               CAUTION!

               If the conferences SEEN-BY: line processing option has been
               set to DELETE, DO NOT USE THIS OPTION because the SEEN-BY:
               line information was stripped before the message was
               originally saved in WILDCAT!  Because of this, you are
               GUARANTEED of creating duplicates in the network!

               If the SEEN-BY: line processing option for the selected
               conference is set to HIDDEN, then you may use this option
               with little fear of creating duplicate messages.


          -Q
               QUIET Mode.  WM processes the mail with minimal screen
               displays.  

                    Example Usage:  WM TOSS -Q


               This option is for use when running under multitaskers like



          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                        Page  26



          WILDMAIL! v3.01                                COMMAND LINE USAGE
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

               DESQview as it reduces the processing time by decreasing the
               resources required to maintain the WM full-screen
               status/activity display.


          -A
               If the Extract echo mail attaches option has been enabled,
               (for any of your conferences) this command line parameter is
               used to instruct WILDMAIL! to scan the defined \WM30\ATTACH
               directory and find the files that don't have a corresponding
               Netmail message and then delete them.

                         Example Usage: WM -A

               These are the files that have already been transmitted to
               their destination and thus no longer have a corresponding
               Netmail message.  The file attachments are the ones that the
               callers to your system have attached to the messages in the
               WILDCAT! message bases.

               By default, WILDMAIL! leaves these files alone and they can
               build up if you don't use this parameter.  Normally you
               would use this parameter together with your TOSS, SCAN
               NETMAIL and so on parameters when executing WILDMAIL!.


          LOADING THE OVERLAY FILE

          WILDMAIL! v3.01 now permits you to specify where the overlay file
          called WM.OVR should be loaded/read from.  The overlay file
          contains all the routines that WILDMAIL! uses throughout the
          course of processing mail.  These routines will be read from the
          overlay file only when they are needed thereby reducing the
          memory requirements.

          Since WILDMAIL! frequently reads from this file, placement can be
          a determining factor on overall performance.  By omitting any of
          the following parameters, WILDMAIL! by default will always
          attempt to load the overlay file into XMS memory, and if it's not
          available, EMS memory and if neither of the two types of memory
          are available (or there is insufficient memory to hold the
          overlay file), WILDMAIL! will simply read the file from disk as
          needed.








          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                        Page  27



          WILDMAIL! v3.01                                COMMAND LINE USAGE
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

          The following command line parameters allow you to specify where
          the overlay file should be loaded.  If any one of the options are
          used and the selected memory is not available (or insufficient
          memory exists) the overlay file will simply be read from disk.

          -XO
               Load overlay file (WM.OVR) into XMS memory.

          -EO
               Load overlay file into EMS memory.

          -DO
               Read WM.OVR file directly from disk.


          The above parameters are used in addition to the normal TOSS
          SCAN, NETMAIL (etc) parameters and cannot be used as the only
          command line parameter.  (If the latter was the case, WILDMAIL!
          would be effectively told to do nothing.)
































          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                        Page  28



          WILDMAIL! v3.01                                    USER INTERFACE
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

          USER INTERFACE

          WMCONFIG!, the configuration program for WILDMAIL! has been
          designed from the ground up with the novice user in mind.  A lot
          of extra care has been spent in thinking through the features in
          an effort to somewhat simplify the complex area of echomail and
          its varied methods of configuration/implementation.

          Industry standard selection and entry techniques are employed
          throughout the program as well as good old fashioned common sense
          programming.  The [ESC] key is used to abort any process, and
          pressing [F1] brings up help information.  Pressing [F10] is used
          to save a particular option or database entry or initiate a
          specific function.


          Context Sensitive Help

               Full context sensitive help is available anywhere by simply
               pressing the [F1] key.  This means that whatever the current
               cursor position is, pressing the [F1] key brings up help
               information relative to that field.

               You may also press [F1] a second time to display a list of
               help topics to choose from.  Simply position the highlight
               bar on the desired topic and press [ENTER].  Once you've
               finished viewing the help information, pressing the [ESC]
               key returns you to the previous configuration screen.

               Throughout the help topics, certain portions of the help
               text may contain highlighted words or phrases.  For those
               viewing in color, this is White Text on a Cyan background
               and mono systems is White Text on a Black background.  

               This highlighted text indicates that a relative subtopic is
               available for viewing.  Simply position the cursor to the
               highlighted text and press [ENTER].  When you've finished
               viewing this subtopic, pressing ALT [F1] will return you to
               the previous help topic.


          CRT Display Modes

               The configuration program has been designed to operate in
               any of three display modes.  The standard mode of 25 lines,
               43 and 50 line modes.  Depending on the section being
               configured, the window sizes will adjust themselves
               automatically, including those for the online help.  



          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                        Page  29



          WILDMAIL! v3.01                                    USER INTERFACE
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

               For those screens that contain more information than can be
               displayed in the standard 25 line mode, all the available
               options will be displayed on the screen.


          Status Bar

               Throughout the configuration process, a status bar located
               at the bottom of the screen (25, 43 and 50 line modes)
               always indicates the available options.  Depending on where
               you're at in the configuration process, these options will
               change automatically.


          DOS Shell

               Since WMCONFIG! has been designed with the user in mind,
               there may come a time when you're in the middle of the
               configuration process and you need to go to DOS to check on
               the location of a file or subdirectory.  Holding down the
               ALT key and pressing the letter D causes WMCONFIG! to swap
               itself out of memory and return you to the DOS prompt.

               As part of the swap process, only a small kernel of memory
               is taken up, making available nearly all of your memory to
               execute another program in.  Once you have finished with
               your work in DOS, at the prompt, typing the command:

                                   EXIT 

               will return you to same section within WMCONFIG! you
               originally exited from, and allows you to resume normally. 
               Again, you may press ALT-D anywhere within the configuration
               process to shell to DOS.


          Protected Mode

               When you first start up WMCONFIG!, it comes up in what is
               called Protected Mode (displayed in the top RH corner of the
               screen).  This means you can move about the configuration
               options but are not allowed to change anything.  This mode
               is handy if you wish to view your current configuration
               without the possibility of accidently making a change.

               If you wish to exit this mode, pressing [F8] toggles you
               back into Edit Mode (as indicated at the top RH corner of
               the screen).  From here you can make any changes desired. 



          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                        Page  30



          WILDMAIL! v3.01                                    USER INTERFACE
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

               Once the [F8] has been toggled to Edit Mode, you may not go
               back into Protected mode.  

               This is due in part to the various data files used to store
               your configuration.  Plus it may give you a false sense of
               protection when in reality you may have accidently changed
               something before toggling the setting a second time.


          Configuration Checking on Exit

               WMCONFIG! has been designed to check your settings to make
               sure the path names are correct, packer/unpacker programs
               exist for the selected nodes, duplication of AKA addresses
               don't exist and so on.  This is necessary to ensure that
               when WILDMAIL! is executed, there will be little fear of
               operating it improperly which could cause unpredictable
               results.

               If a configuration error has been detected, a screen will be
               displayed of all the settings that were found to be
               incorrect.  An output file is also created in the \WM30
               directory called WMCONFIG.ERR which contains a list of those
               errors.  

               From here you have two choices.  You can press [ESC] and
               return to the configuration process and make the necessary
               changes or press [F10] and exit with the incorrect
               configuration.  If you do the latter, when WILDMAIL! is
               executed, it will produce an error message telling you that
               the current configuration is incorrect and will not run. 
               This prevents misconfigured settings from interfering with
               WILDMAIL!'s ability to properly process the mail.


          Database Formats

               The conference area and node address databases both make use
               of special, high speed indexed B-Tree formatted files.  The
               Crash Mail users list is actually special flag information
               stored in the WILDCAT! users database.  This allows you full
               access to all the callers on your system without having to
               maintain a duplicate set of user names.








          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                        Page  31



          WILDMAIL! v3.01                 WMCONFIG! SETUP AND CONFIGURATION
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

          WMCONFIG! SETUP AND CONFIGURATION

          As stated earlier, WMCONFIG.EXE is the configuration program used
          the define the operational characteristics of WILDMAIL! including
          conference, node and area managers databases.  This program must
          be executed from the WILDMAIL! directory and may not be executed
          while WILDMAIL! is processing mail.


          DATA FILES USED

          Shown below is a description of the various datafiles WMCONFIG!
          maintains/uses for proper configuration of WILDMAIL!.

          WMCONFIG.DAT        Main configuration settings including
                              defaults, paths, archivers, and so on.

          WMAREAS.DAT/IX      Each conferences unique configuration
                              settings.

          WMNODES.DAT/IX      Node definition information for each of the
                              systems you will be transferring mail with.

          WMORIGIN.DAT        All of your Origin line information is stored
                              here.

          WMAMGR.DAT          This file contains the operational parameters
                              pertaining to how AreaRequest manager should
                              perform its tasks.

          WMCONFIG.HLP        This is the online help file used when
                              pressing [F1] on a selected field.  This file
                              is not editable and must exist in the
                              WILDMAIL! directory.


          CONFIGURATION CHECKING ON EXIT

          When exiting WMCONFIG!, a check is performed on the current
          configuration settings.  If errors are found and you use the
          [F10] option to save the settings anyway, the next time WILDMAIL!
          is executed, it will abort and inform you that configuration
          changes need to be made.  This prevents unpredictable results
          when processing mail.

          If no errors are found, no additional key presses are required
          and WMCONFIG! exits normally and saves the settings to disk.




          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                        Page  32



          WILDMAIL! v3.01                 WMCONFIG! SETUP AND CONFIGURATION
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

          SYSTEM GENERATED ERROR FILES

          When WMCONFIG! checks your configuration settings, if it finds an
          error, it will produce an associated ASCII text file containing
          the error(s) found.  Shown below are those files.

          WMCONFIG.ERR        This file is created when something in your
                              configuration is not set properly.  The text
                              it contains details the problems found. 
                              WMCONFIG! will automatically maintain this
                              file until all the settings are properly set. 
                              Once properly set, this file will be deleted.

          WMORIGIN.ERR        When using the [F4] Global option for
                              changing Origin lines, WMCONFIG! will check
                              to make sure the overall length of the Origin
                              line is not exceeded.  If it does, it will
                              truncate the Origin line enough so the Origin
                              address will still fit in the 78 character
                              limitation.  This file will then be created
                              indicating a list of all the conferences that
                              the truncation process was performed on.


          MENU SELECTIONS

          The following pages are divided up into categories as selected
          from the Main Menu.  Each category having its own options and
          sub-menus and are presented in the order they appear on the Main
          Menu.

          You may select the desired option by either pressing the
          associated hot key (accentuated by a different colored letter in
          the option name) or by positioning the highlight bar by using the
          Up/Dn arrow keys and pressing [ENTER].
















          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                        Page  33



          WILDMAIL! v3.01                                SYSTEM INFORMATION
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

          SYSTEM INFORMATION

          This category is used to define subdirectory paths for inbound
          and outbound mail, mailer specific information along with SysOp
          and BBS names and so on.

          Shown below is a complete breakdown of the available
          configuration options from this screen.


          System Operator Name:

               The Master SysOp name in First Name Last Name format as
               defined in your BBS configuration program.

               For WILDCAT! systems, this is the same name as defined in
               MAKEWILD, General Options Part 1, line numbers 1 and 2.


          Bulletin Board Name:

               The name of your Bulletin Board.  Typically, this is the
               same name as defined in your BBS configuration program.

               For WILDCAT! systems, this is the same name as defined in
               MAKEWILD, General Options Part 1, line number 3.


          Primary Address:

               Because more and more networks are popping up on a regular
               basis, most systems usually have more than one address. A
               default address must be known (due to certain situations)
               and this option is used to specify which of your addresses
               should be considered your primary or default address.

               The address specified here must be in <zone:net/node.point>
               format similar to 1:161/123.0.  Normally, this is the same
               address you've previously defined as your primary address in
               your front end mailer.

               For those that are running FrontDoor v2.02, in FDSETUP,
               Global menu option, Address option and then listed under
               Main will then display your primary address.

               Pressing [ENTER] on this field pops up another window
               allowing you to specify the individual zone, net, node and
               point numbers that make up your entire address.  Throughout



          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                        Page  34



          WILDMAIL! v3.01                                SYSTEM INFORMATION
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

               WMCONFIG! any address definition, whether it be an AKA,
               downlink node, uplink node, etc., will use the same format
               for the definition.  Shown below is a breakdown of these
               fields.


               Zone      To facilitate complete address specification, each
                         portion of the address is defined via a special
                         field.  In this case, this option is used to
                         specify the <zone> portion of the address.

                         Within Fidonet compatible networks, each system
                         must have its own unique address number.  This is
                         a four dimensional (4D) addressing scheme in
                         <zone:net/node.point> format similar to the
                         following address of:

                                        1:161/503.0
                                        ^
                         The first portion of the above address is the
                         actual zone number, which in this case is 1.


               Net       This option is used to specify the <net> portion
                         of the address.  This is a four dimensional (4D)
                         addressing scheme in <zone:net/node.point> format
                         similar to the following address of:

                                        1:161/503.0
                                          ^^^
                         The second portion of the above address is the
                         actual network number, which in this case is 161.


               Node      This option is used to specify the <node> portion
                         of the address.  This is a four dimensional (4D)
                         addressing scheme in <zone:net/node.point> format
                         similar to the following address of:

                                        1:161/503.0
                                              ^^^
                         The third portion of the above address is the
                         actual node number, which in this case is 503.


               Point     This option is used to specify the <point> portion
                         of the address.  This is a four dimensional (4D)
                         addressing scheme in <zone:net/node.point> format



          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                        Page  35



          WILDMAIL! v3.01                                SYSTEM INFORMATION
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

                         similar to the following address of:

                                        1:161/503.0
                                                  ^
                         The fourth portion of the above address is the
                         actual point address, which in this case is a 0. 
                         Points are unique in that they are nodes that pick
                         up their mail when they want to and are usually
                         not available 24 hours a day.  This prevents them
                         from being available for CRASH type mail.


          AKA Addresses:

               Because there are literally hundreds of different networks
               in existence today, each one requires you to have a unique
               address assigned for that network.  Besides your primary
               address, these additional addresses are referred to as AKA's
               (an acronym for Also Known As).  This option allows you to
               specify up to 20 different AKA's.

               WILDMAIL! uses these addresses to match incoming Netmail
               messages to their respective network addresses plus any
               additional processing.  Throughout WMCONFIG, any reference
               to an AKA (for example, zone matching, origin address for a
               specific conference, etc) requires you to have predefined
               AKA's before allowing you to proceed.

               After pressing [ENTER] on this field, displayed is a window
               from which you may define your AKA addresses.  Shown below
               are the available options and editing commands.


               Create a New AKA

                    Pressing the [INSERT] key pops up a window that allows
                    you to define your complete <zone:net/node.point>
                    address.  If your AKA doesn't contain a <point>
                    address, simply use the default value of 0 for the
                    point.  

                    Once the new address has been defined, pressing the
                    [ESC] key saves the changes and returns to the list of
                    previously defined AKA addresses.







          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                        Page  36



          WILDMAIL! v3.01                                SYSTEM INFORMATION
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

               Delete an AKA

                    After selecting the desired address definition by
                    positioning the highlight bar with the Up/Dn arrow
                    keys, pressing the [DELETE] key brings up a friendly
                    message asking if you're sure this is the correct
                    address to delete.  

                    Pressing Y deletes the AKA and [ESC] aborts the process
                    and returns you to the previous screen.


               Edit an AKA

                    After selecting the desired address by positioning the
                    highlight bar with the Up/Dn arrow keys, pressing the
                    [ENTER] key brings this address up in edit mode. 

                    From here, simply select the specific portion of the
                    address to change by positioning the cursor on the
                    appropriate field.  Once the changes are complete,
                    pressing the [ESC] key saves them and returns you to
                    the previous screen.


               NOTE:     If you belong to only one network (therefore have
                         only one node address) then leave these fields
                         blank.


          Primary Origin Line:

               Since in most networks it's a requirement to have an Origin
               line attached to the bottom of all outgoing echo style
               messages, this option is used to specify which Origin line
               you would like to be used as your default or primary Origin
               line.

               Pressing [ENTER] on this option displays a list of Origin
               lines from which to choose from.  To select an Origin line,
               simply position the highlight bar by using the Up/Dn arrow
               keys and press [ENTER].  If the presented list is blank, you
               must return to the Main Menu option, Origin Line Maintenance
               and create a new one before continuing.

               Once a default or primary Origin line has been selected,
               from the Main Menu selection, Origin Line Maintenance, it
               will now display a (*) to the left of it distinguishing it



          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                        Page  37



          WILDMAIL! v3.01                                SYSTEM INFORMATION
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

               from the regular Origin lines.

               Since WMCONFIG! has the ability to globally change and
               delete Origin lines in their respective conferences, a
               method was necessary to ensure at least one Origin line
               always existed to ensure compliance for messages leaving
               your system.  This requires that you have previously defined
               at least one Origin line from the Main Menu option, Origin
               Line maintenance.

               This newly selected Primary Origin line will replace any
               Origin lines that have been selected for deletion.  See Main
               Menu option, Origin Line Maintenance for additional
               information.


          Mailer Type:

               Selecting the desired Mailer type by tapping the [SPACEBAR]
               will cause WILDMAIL! to match the operating characteristics
               of the selected mailer for proper handling/processing of
               mail.  Shown below are the supported mailer types.

               FrontDoor

                    This is a very popular front end mailer.  It processes
                    mail in a standard method and requires no special
                    configuration requirements.  For those systems running
                    InterMail, you should select this type because for the
                    most part, they operate identically.


               D'Bridge

                    As with FrontDoor, this is a very popular mailer, but
                    has quite an array of features.  But because of those
                    features, it handles inbound and outbound mail a bit
                    different than one might expect.  However, WILDMAIL!
                    now directly supports D'Bridges own internal queue for
                    processing outbound mail.


               LYNXMAIL!

                    This is our own inhouse product that is currently under
                    development and will be available for release at some
                    point in the future.  




          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                        Page  38



          WILDMAIL! v3.01                                SYSTEM INFORMATION
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

               Binkley

                    This mailer type is unique from the others because it
                    doesn't have a mail packing mechanism built into it, so
                    a third party utility that does this must be used.  

                    If this mailer type is selected, WMCONFIG! allows you
                    to specify the packing program name and its associated
                    command line parameters via a special protected field
                    called Mailer specific options.  From there you can
                    then define the packer program name and the necessary
                    command line information.

               Since each system processes mail quite a bit differently
               from others, its definition here is critical for proper
               operation!


          Mailer specific options:

               This field is currently only available when the Mailer type
               has been set to Binkley.  This is used to specify the
               packing/routing program and command line parameters to use
               to properly create the outbound mail archives for your
               downlink node addresses.  

               When WILDMAIL! has completed its tossing duties, it will
               shell to DOS and execute the program name and command line
               parameters defined below.  Once the process is complete,
               WILDMAIL! will exit from the DOS shell and resume any
               remaining processes.

               Program name:

                    Here you specify the complete DOS file name or batch
                    file including its extension.  For example:

                                        QM-PACK.EXE

                    You may also be creative and specify a batch file here
                    should you wish to perform any additional processing
                    after the initial execution of the packing program.  

                    If you do this, MAKE SURE you simply end the batch file
                    and DO NOT call/execute WILDMAIL! a second time. 
                    Unpredictable results could occur, the least of which
                    may be the loss of mail.




          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                        Page  39



          WILDMAIL! v3.01                                SYSTEM INFORMATION
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

               Parameters:

                    This field allows you to specify the command line
                    parameters that should be added to the program name
                    when it's executed.  

                    If you specify a batch file in the program name to run,
                    you should refrain from any command line parameters
                    here and simply put them in the batch file.


          BBS Type:

               WILDMAIL! is capable of processing mail in any of three
               possible formats.  Selecting the desired BBS type by tapping
               the [SPACEBAR] will toggle these formats and specifies the
               processing methods necessary for proper operation.  Listed
               below are the available BBS types.

               WILDCAT!

                    This format is used when running WILDCAT! v3.xx or
                    higher.  Earlier versions of WILDCAT! can not be
                    supported due to structure limitations.


               FIDO      <Option not supported yet>

                    This format is used to produce a .MSG message format
                    for those bulletin board systems that support it such
                    as Opus.  Most front end mailers also support this
                    format for their internal message folders/conferences
                    such as D'Bridge and FrontDoor.

                    Depending on the BBS type, certain options may or may
                    not be available due to the configuration requirements
                    of each BBS program.


          BBS Specific Options:

               This option is used to define information specific to the
               previously selected BBS type.  Because each bulletin board
               system type is unique, each requires its own program
               specific information.  Depending on which BBS type has been
               selected dictates which options will be available. 
               Following is a breakdown of the supported types.




          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                        Page  40



          WILDMAIL! v3.01                                SYSTEM INFORMATION
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

               WILDCAT! BBS System

               Shown below are the options necessary when the BBS type
               selected has been set to WILDCAT!.

               Home directory/path:

                    When WILDMAIL! executes, it reads the contents of the
                    WILDCAT! configuration files and depending on the
                    configuration, it makes use of certain information like
                    maximum messages per conference, maximum lines per
                    message, etc.  Because WILDMAIL! uses these files, it
                    needs to know the exact <drive:\directory> where
                    they're located.  A typical path might be:

                                        C:\WC30

                    This directory is commonly referred to as the WILDCAT!
                    home directory.


               Pre-process echomail:

                    This option allows you to instruct WILDMAIL! to
                    automatically pretoss all mail destined for your
                    message bases into a temporary directory specified via
                    the Pre-processing path field.  

                    This is an extremely powerful option for those systems
                    that hub mail for your downlink nodes.  With this
                    option enabled, WILDMAIL! has the ability to check
                    either of two places for mail to toss driven by the use
                    of the appropriate command line parameter.  

                    Shown below are the command line parameters along with
                    a brief description.

                    TOSS

                         When WILDMAIL! is executed with this command line
                         parameter it will look in your inbound directory
                         for mail to toss.  Two things happen here. 

                         1)   Mail DESTINED for your systems message bases
                              (including your AKA addresses) will be tossed
                              into special PKT files and placed into the
                              <drive:\directory> specified via the
                              Preprocessing path option.  All the SEENBY &



          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                        Page  41



          WILDMAIL! v3.01                                SYSTEM INFORMATION
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

                              PATH line information remains completely
                              intact.

                         2)   All mail destined for your downlink node
                              addresses will be processed normally.


                    PRETOSS

                         When WILDMAIL! is executed with this command line
                         parameter, it looks in <drive:\directory> path
                         specified in the Preprocessing path option for
                         mail to process.  Any mail found in this directory
                         will be tossed into your WILDCAT! message bases
                         only.  No regular mail from the inbound directory
                         will be tossed.


                    NOTE:     The above command line parameters TOSS and
                              PRETOSS can not be executed simultaneously. 
                              You must execute one or the other but not
                              both at the same time.


                    For some reason, mail always seems to come during prime
                    time calling hours.  Since you normally don't want your
                    system tied up (for too long) processing mail during
                    this busy period, you could set up your system to
                    execute WILDMAIL! with just the TOSS parameter.  Then,
                    later on when your system is not very busy (maybe in
                    the early morning hours) execute WILDMAIL with the
                    PRETOSS parameter.  This has the effect of reducing
                    offline time while mail is being tossed thereby making
                    more of your system available during peak calling
                    times.

                    It should be pointed out though, since you will be
                    processing the same mail twice, it might take more time
                    to toss the entire amount of mail.  But the advantage
                    is that this extra time can be scheduled when your
                    system is not very busy.

                    With this option set to N, the Pre-processing path
                    field becomes unavailable.  Also, the PRETOSS command
                    line parameter no longer has any meaning and is simply
                    ignored by WILDMAIL!.  All mail will be processed
                    normally meaning mail will be tossed into your WILDCAT!
                    message bases and to your downlink node addresses



          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                        Page  42



          WILDMAIL! v3.01                                SYSTEM INFORMATION
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

                    simultaneously.


               Pre-processing path:

                    WILDMAIL! supports the ability to toss mail destined
                    for your system into a temporary packet(s) instead of
                    the WILDCAT! database for fast processing of mail to
                    your downlink node addresses.

                    The path specified here is where WILDMAIL! will create
                    these temporary PKTs should the Preprocess echomail
                    field be toggled to Y.  A typical path definition might
                    be:

                                   C:\WM30\PRETOSS

                    This path MUST be different than your inbound directory
                    for this function to work properly.


               File attach path:

                    WILDMAIL! now supports WILDCAT!'s ability to attach
                    files to echomail messages.  This option works in
                    conjunction with the Extract file attaches option for
                    the appropriate conference area definition.

                    When WILDMAIL! extracts a message from a conference
                    with an attached file, it will process that message
                    normally and make a copy of the attached file and place
                    it in the <drive:\directory> path specified here.  The
                    extracted message will be added to the appropriate PKT
                    file and WILDMAIL! will create a Netmail message with
                    the original file that was attached to the message in
                    WILDCAT! now attached to the Netmail message.  

                    A Netmail message with the attached file will be
                    created for each of the downlink nodes that are
                    receiving the conference the file attachment came from. 
                    During this process, no file attachments are sent
                    through echomail, only by Netmail messages which are
                    created by WILDMAIL!.

                    A typical path would be:

                                   C:\WM30\ATTACH




          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                        Page  43



          WILDMAIL! v3.01                                SYSTEM INFORMATION
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

                    Normal DOS naming conventions must be strictly adhered
                    to when defining the drive and subdirectory.


               Netmail conference number:

                    This option is used to specify the conference number
                    defined in MAKEWILD that has the option setting of Mail
                    type flagged as "Netmail".  This number is used so
                    WILDMAIL! will know what conference to toss messages
                    into that have special <zone:net/node.point> addressing
                    information in them.

                    Presently, only one conference in WILDCAT! may be
                    configured as a Netmail conference.  This conference is
                    unique in that when you enter a message in a conference
                    flagged as Netmail, you are asked what node address
                    this message is to be sent to prior to asking for the
                    persons name to address it to.

                    The "Netmail" flag differs from the standard "Normal"
                    type in that it uses a special node addressing scheme
                    for proper transmission on to the destination system. 
                    The remainder of the echomail style conferences as well
                    as your local message areas must be set to "Normal".

                    Pressing [F2] on this option brings up a complete list
                    of conferences defined within WILDCAT!.  You may view
                    the status of this flag by positioning the highlight
                    bar upon the desired conference and pressing [ENTER]. 
                    This will extract the same information as configured
                    when running MAKEWILD with the only difference being
                    you may not modify any of these fields.

                    Do NOT use 0 as the Netmail conference as WILDCAT! uses
                    this conference for system generated messages such as
                    Password Failure, Phone Number verification failure and
                    so on.


               Notify users of personal mail:

                    WILDCAT! offers callers to your system the feature of
                    being notified that mail is waiting for them when they
                    first logon.  WILDMAIL! can maintain this feature by
                    reading the TO: field of each message tossed and check
                    the user database to see if that person exists and if
                    so, sets a flag in their user record.  The next time



          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                        Page  44



          WILDMAIL! v3.01                                SYSTEM INFORMATION
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

                    they logon, WILDCAT! will inform them they have new
                    mail waiting in a particular conference.

                    Because of the additional searching of the user
                    database for each new message tossed, this option can
                    add a slight amount of processing time to the mail
                    tossing process.  Normally though, it's insignificant
                    as the databases within WILDCAT! are extremely fast.

                    For those conferences that are flagged as ALIAS,
                    WILDMAIL! also checks the users Alias name and flags
                    that individuals user record accordingly.


               Maintain message levels:

                    Within MAKEWILD, you normally define the maximum number
                    of messages allowed per conference to prohibit your
                    message bases from growing too large.  This option is
                    used to tell WILDMAIL! whether or not to maintain these
                    maximums as specified.

                    With this option set to Y, WILDMAIL! will purge the
                    oldest message to make room for the one about to be
                    added if the number of messages in that conference was
                    already at its defined limit.  This is a "one for one"
                    message purge/toss.  This can increase the amount of
                    time to process each message if the conference is
                    already at its established maximum but it does offer
                    automatic message count management.

                    With this option set to N, messages will be added to
                    the message bases without maintaining the limits and
                    WILL cause the database file sizes to continue to grow. 
                    You must then use the command line parameter PURGE when
                    executing WILDMAIL! (possibly in an event) to properly
                    maintain the message levels.  With this option set to
                    N, the primary disadvantage is if the conference is at
                    its limit of say 750, when WILDMAIL! tosses 200 new
                    messages, the database size now grows to 950 messages. 
                    When the command line parameter PURGE is used with
                    WILDMAIL!, it will purge the 200 oldest messages in the
                    conference leaving 200 blank slots while still
                    occupying 200 blank message slots worth of valuable
                    disk space.

                    The only way to effectively reduce the message base
                    back down to its true file size is to run WCREPAIR.  On



          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                        Page  45



          WILDMAIL! v3.01                                SYSTEM INFORMATION
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

                    systems carrying a large amount of conferences, care
                    must be taken when disabling this option, otherwise you
                    can end up wasting a SIGNIFICANT amount of disk space.


               Import Netmail as .MSG:

                    When a Netmail message is received, WILDMAIL! by
                    default creates a Netmail message (in the .MSG format)
                    and places it in the defined Netmail directory of your
                    front end mailer.  It also creates another one and
                    places it in the WILDCAT! Netmail conference.

                    By setting this option to N, when a Netmail message is
                    received, WILDMAIL! will toss the Netmail message into
                    the WILDCAT! Netmail conference only.  This is often
                    used to avoid having two sets of the same Netmail
                    message (one in WILDCAT! and one in your front end
                    mailers Netmail message folder).

                    If you use any third party utilities on your system
                    that requires Netmail messages to be found in the
                    mailers Netmail directory, then this option should be
                    set to Y.

                    If the incoming message is an AreaRequest message, and
                    this option is set to N, then WILDMAIL! will add the
                    message as a .MSG anyway.


               Delete Netmail after extraction:

                    This option is used to have WILDMAIL! automatically
                    flag each Netmail message extracted as deleted
                    (indicated by a flashing (D) next to the message
                    number).  Because of the way WILDCAT! manages deleted
                    messages, they will remain on your system until the
                    SysOp uses the [P]urge option found on the SysOp Menu.

                    This option could be useful in preventing Netmail
                    messages from building up on your system.  However,
                    caution must be used here to prevent important messages
                    you wish to keep from being automatically deleted.

                    Normally, this option is set to N.






          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                        Page  46



          WILDMAIL! v3.01                                SYSTEM INFORMATION
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

               Allow Netmail file attaches:

                    Presently, WILDCAT! does not permit file attaches in a
                    conference flagged as "Netmail".  In the future,
                    WILDMAIL! may offer a solution to this limitation, but
                    only time will tell.


               Allow CRASHMAIL support:

                    This option is used to tell WILDMAIL! whether or not to
                    allow Netmail messages entered within WILDCAT! and
                    flagged as CRASH to in fact go out as CRASH mail.

                    The term CRASH (or CRASHMAIL) is used to indicate that
                    the associated message needs to be transmitted
                    immediately regardless of the time of day or night. 
                    This is important to understand because prime time
                    calling charges may be incurred depending on the time
                    of day the message is extracted.

                    If this option is set to Y, the "Valid CRASHMAIL
                    users:" option is made available and is used to specify
                    which user names are allowed to send CRASH mail.

                    If this option is set to N, the "Valid CRASHMAIL
                    users:" option is dis-allowed and any Netmail messages
                    entered in WILDCAT! flagged as CRASH will automatically
                    have their status changed to NORMAL.  This could be
                    used to prevent ANYONE from sending out a Netmail
                    message (including the SysOp) flagged as CRASH from
                    within WILDCAT!.


               Valid CRASHMAIL users:

                    The information presented here is a list of user names
                    (read from the WILDCAT! user database) that are allowed
                    to send NETMAIL messages from your system to another
                    flagged as CRASH.  Selected user names are indicated by
                    a (é) to the left of their name.

                    In WILDCAT!, when a user enters in a new message or
                    sends a reply in the Netmail conference, WILDCAT!
                    prompts them similar to:

                                   Crash mail?  [Y]




          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                        Page  47



          WILDMAIL! v3.01                                SYSTEM INFORMATION
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

                    If they answer Y to this, WILDMAIL! will only maintain
                    the CRASH flag if the FROM: user name on the message
                    has been previously selected via this option.

                    If the user name has not been tagged, WILDMAIL!
                    automatically resets the CRASH flag back to NORMAL. 
                    Your system will then send this message out with the
                    regular mail instead of immediately.  This option
                    offers you a degree of control as to who has and
                    doesn't have access to sending CRASH mail.

                    Selecting a Crash User

                         You may select the desired user name by
                         positioning the highlight bar with the Up/Dn arrow
                         keys and tapping the [SPACEBAR] will automatically
                         update the user database within WILDCAT!.  You may
                         also use the PgUp/PgDn to scroll a screen at a
                         time through the database.

                         You may deselect a specific user by positioning
                         the highlight bar on their name and tapping the
                         [SPACEBAR].


                    Access Tip

                         Because the WILDCAT! users database can be quite
                         large on certain systems, instead of using the
                         PgUp/PgDn keys to find the user name, you can
                         press the first letter of their last name.  The
                         cursor will then be positioned at the first
                         occurrence of that letter in the users database.


               FIDO

               At present, the BBS type FIDO definition does not require
               any additional information so there will not be a BBS
               specific screen available.



          Inbound Path:

               This directory is where WILDMAIL! will look to see if any
               new mail has been received by your front end mailer for
               processing.  This <drive:\directory> path must be the exact



          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                        Page  48



          WILDMAIL! v3.01                                SYSTEM INFORMATION
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

               same one defined as your inbound directory for your front
               end mailer.  Typically;

                    C:\FD\FILE     for FrontDoor v1.99c or v2.02
                    C:\IM\SECURE   for InterMail v2.00+
                    C:\DB\FILE     for D'Bridge v1.30+
                    C:\LM\INBOUND  for LYNXMAIL! v1.00+

               For those running FrontDoor, refer to FDSETUP under Global
               options, menu selection of Filenames, the listing of Files
               will then indicate this path.


          Outbound Path:

               WILDMAIL! needs to know what <drive:\directory> to place all
               newly created outbound mail archives so your front end
               mailer can locate them for processing.  When D'Bridge or
               FrontDoor performs a rescan of the Netmail area, it will
               pick up these mail archive(s) and then add them to its
               outbound queue.

               FrontDoor

                    This must be the same path as defined in FDSETUP under
                    Global options, menu selection Filenames, the listing
                    of Packets.  In other words, use the same outbound path
                    here as you currently use in FrontDoor.


               LYNXMAIL!

                    This must be the exact same path defined in LMCONFIG,
                    General Information, Outbound Files location.


               D'Bridge

                    You should use the same outbound path here as you have
                    defined as your queue directory in DB SETUP.  Normally
                    this is the \DB\QUEUE directory.


               In previous versions of WILDMAIL! you used to have a special
               directory that was "unknown" by D'Bridge to prevent mail
               from being deleting.  Because WILDMAIL! now fully supports
               D'Bridges internal queue, you should now specify the queue
               directory of D'Bridge here.



          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                        Page  49



          WILDMAIL! v3.01                                SYSTEM INFORMATION
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ


          Netmail Path:

               When WILDMAIL! produces outbound mail, it creates a Netmail
               message with a corresponding file attach (echomail archive)
               and needs to know where to place these messages so your
               front end mailer can locate them for proper processing.

               Consequently, this MUST be the same <drive:\directory> as
               you've previously defined as your Netmail directory for the
               front end mailer.  Shown below are sample paths.

                    C:\FD\NETMAIL  for FrontDoor v1.99c or v2.02
                    C:\IM\NETMAIL  for InterMail v2.00+
                    C:\DB\NETMAIL  for D'Bridge v1.30+
                    C:\LM\NETMAIL  for LYNXMAIL! v1.00+

               For those running FrontDoor/InterMail, refer to
               FDSETUP/IMSETUP under the Global option, menu selection of
               Filenames, the listing of Netmail will then indicate this
               path.


          Bad Messages Path:

               From time to time, you might receive messages that don't
               have a conference to be tossed into.  Instead of just
               deleting them, WILDMAIL! will place them into a special sub-
               directory for holding until the problem can be resolved. 
               Because of this, WILDMAIL! needs to know what
               <drive:\directory> you wish to have these messages placed
               into should this situation arise.

               These messages will be stored in the standard .MSG format
               and typical paths are:

                    C:\FD\BADECHO  for FrontDoor v1.99c or v2.02
                    C:\IM\BADECHO  for InterMail v2.00+
                    C:\DB\BADECHO  for D'Bridge v1.30+
                    C:\LM\BADECHO  for LYNXMAIL v1.00+

               If messages are placed in this directory, the next time
               WILDMAIL! does a TOSS, it will read each file and attempt to
               find a matching conference to toss it into.  If no matches
               are found, WILDMAIL! will display a message indicating this
               and leaves the .MSG file intact.  If a conference is found,
               the file is tossed into its corresponding conference and the
               .MSG file is then deleted from this directory.



          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                        Page  50



          WILDMAIL! v3.01                                SYSTEM INFORMATION
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ


               Stray Messages

                    To resolve stray .MSG files, normally you would
                    manually display the contents of each .MSG file with a
                    file viewer utility such as ViewPKT! and make note of
                    the "AREA:" definition which is typically located
                    within the first few lines of the message.

                    You would then see if it matches up with any area
                    previously defined with the Main Menu option Conference
                    Area Management.  Adjustments could then be made if
                    necessary.  Usually this occurs because of spelling
                    errors when initially defining conference areas.

                    If the AREA: definition doesn't match any of your areas
                    and the message is of little use, simply delete the
                    .MSG file from the sub-directory.  If you continue to
                    receive messages that don't belong on your system, you
                    should contact the person you're picking up mail from
                    (for that network) and research the problem.


          WILDMAIL! Log File Name/Path:

               WILDMAIL! maintains a log file of all activity regarding the
               processing of mail both in and out of the system.  This
               information is useful for monitoring WILDMAIL's performance
               and mail activity.

               This option defines the <drive:\directory> and <filename> of
               the log file where all activity regarding mail processing is
               to be kept.  A typical statement would be:

                                   C:\WM30\WM.LOG

               Normal DOS conventions are required when defining the log
               file name.


               ALT-V  View File

               With the cursor positioned on the log file path, you can
               press and hold down the [ALT] key followed by tapping the V
               character and display the contents of the specified file. 
               If the specified file doesn't exist, this option is simply
               ignored.




          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                        Page  51



          WILDMAIL! v3.01                                SYSTEM INFORMATION
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

               You may scroll around the file by using the PgUp/PgDn, Up/Dn
               and Left/Right arrow keys.  Once you're finished viewing the
               file, you may press the [ESC] key and you'll be returned to
               the previous screen.


          Log File Options:

               This option is used to specify the level of information
               desired in the previously defined log file via the 
               WILDMAIL! Log File Name/Path  menu selection.

               Pressing [ENTER] on this field presents a sub-menu of
               available levels of information.  Additional help
               information is available after selecting this option by
               pressing [F1].

               General:

                    Log file entries that start off with an "!" are General
                    entries.


               Accounting:

                    Log file entries that start off with a "$" are
                    Accounting entries.


               Conference:

                    Log file entries that start off with an "#" are
                    Conference entries.


               Errors:

                    Log file entries that start off with an "*" are Serious
                    errors.


               Select All

                    With this option set to Y, it instructs WILDMAIL! to
                    produce all of the available levels of log information
                    that it can. This includes:

                                        General



          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                        Page  52



          WILDMAIL! v3.01                                SYSTEM INFORMATION
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

                                        Accounting
                                        Conference
                                        Errors

                    With all this information being added to the log file
                    on a regular basis, the log file can grow at quite a
                    rapid rate. Care should be taken to prevent this log
                    file from becoming to large.

               Since WILDMAIL! will recreate the log file if it doesn't
               exist, you may delete this file at any time. (Except when
               WILDMAIL! is executing of course!)







































          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                        Page  53



          WILDMAIL! v3.01                         MISCELLANEOUS INFORMATION
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

          MISCELLANEOUS INFORMATION

          Information defined here dictates the operational characteristics
          of WILDMAIL! such as number of duplicates, packet sizes and so
          on.  Shown below is a complete breakdown of the available options
          and their descriptions.


          Duplicates to maintain:

               Due to the way echomail is sent from one system to another,
               some form of method must be used to make sure messages
               already received by your system are not accidently added a
               second time.

               WILDMAIL! makes use of a special indexed database file with
               a record containing special MSGID duplicate checking
               information for EACH message that has been processed by the
               system.  This also includes those conferences defined as
               "passthru".  This information is stored in a file called
               WMDUPES.DAT which is located in the \WM30 directory.

               This option is used to define the maximum number of records
               this special file will hold.  For most systems, we suggest
               at least 3-5 days worth of messages.  For example, if you
               typically receive 5,500 messages a day, you would use a
               value of anywhere from 16500 to 27500. (3 x 5,500 = 16,500)

               Please note however, the larger you set this number, the
               larger the file size will be.  If you wish to disable
               duplicate message checking all together, simply specify a
               value of 0 (zero).


          Maximum messages per .PKT:

               When WILDMAIL! processes outbound mail, it creates special
               database type files containing messages for other systems
               with the extension of .PKT.  These files are the temporary
               storage medium when mail is sent from system to system.

               This option is used to define a limit on how many messages
               are added to a .PKT file before WILDMAIL! stops and creates
               a new one.  You should try and keep this number to a
               reasonable value because if for whatever reason a mail
               packet (.PKT file) becomes corrupted, mail will be lost. 
               The larger the packet, the larger the loss.




          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                        Page  54



          WILDMAIL! v3.01                         MISCELLANEOUS INFORMATION
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

               The average size of a message is somewhere between 1,100 to
               1,600 bytes in size.  Typically, values ranging from 200 to
               300 messages are appropriate.

               This is used in conjunction with the Max .PKT size option in
               determining when WILDMAIL! should create a new .PKT file. 
               Please note, this option shouldn't be confused with the
               number of .PKT files contained within a mail archive.


          Max .PKT size:

               When WILDMAIL! processes outbound mail, it creates special
               database files containing messages for other systems with
               the extension of .PKT.

               This option is used to define a limit on how large in
               kilobytes these .PKT files can get before WILDMAIL! creates
               a new one.  This is used with the Max messages per .PKT
               option in determining when WILDMAIL! should create a new
               .PKT file.

               You should try and keep this number to a reasonable value
               because if for whatever reason a mail packet (.PKT file)
               becomes corrupted, mail will be lost.  The larger the
               packet, the larger the loss.  Typically, values ranging from
               200 to 400 kilobytes are appropriate.

               A value of 0 (zero) disables this option and no checking
               will be done on PKT size.


          Check SEEN-BYs:

               Because of the various interpretations of the specifications
               for echo style messages, WILDMAIL! offers you the ability to
               decide if you want the SEEN-BY: line information checked in
               the inbound messages.

               With this option set to Y, (the default setting) WILDMAIL!
               will check for the existence of the SEEN-BY: lines before
               processing the message.  If they exist, WILDMAIL! will toss
               then accordingly.  If however they are not included at all,
               WILDMAIL! will toss them into the Bad Messages directory for
               later review.

               With this option set to N, WILDMAIL! will ignore the missing
               information and process them blindly.  Caution must be



          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                        Page  55



          WILDMAIL! v3.01                         MISCELLANEOUS INFORMATION
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

               exercised here because certain systems are very finicky
               about the proper formatting of messages.

               NOTE:     For specifics on special control information
                         contained within the messages, we have written a
                         program called ViewPKT! that displays all this in
                         a simple and easy to understand format.  The
                         latest version is always available for download
                         from the WILDMAIL! support BBS.


          Kill null messages:

               When processing echomail, Netmail messages are created that
               contain special information in the SUBJECT: line pertaining
               to the attached mail archive (the actual echomail messages).

               These Netmail messages are what's used to send mail from one
               system to another by using the addresses located in the TO:
               and FROM: fields.  They normally contain nothing in the body
               of the message except possibly kludge information.

               Since these messages are of little value once the attached
               mail archives (the actual echomail messages) have been
               received, you can use this option to have WILDMAIL!
               automatically delete these "null" messages.

               By definition, a null message is considered to be a Netmail
               message with a TO: and FROM: address and a empty message
               body except for possible kludge addressing information.

               It should be noted that kludge information is normally
               hidden from view by use of special control characters. 
               Since this information is specific to proper addressing
               between zones, it's not considered part of the "body" of the
               message.


          Flag NetMail as KILL/SENT:

               Since a Netmail message is generated for every echomail
               archive (to transfer it from system to system), these
               messages can "pile up" in a hurry.  WILDMAIL! makes use of
               this option to instruct your front end mailer to delete
               these messages automatically.

               Setting this option to Y causes WILDMAIL! to activate the
               KILL/SENT flag setting (on the message) when it's extracted.



          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                        Page  56



          WILDMAIL! v3.01                         MISCELLANEOUS INFORMATION
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

               This flag will then be interpreted by the front end mailer
               to delete the message after it has been successfully
               transmitted to its destination address.

               Setting this option to N will leave each message intact in
               your front end mailers Netmail message folder for manual
               disposal.  Remember, with this setting, these messages will
               pile up in a hurry!  You are then responsible for doing the
               cleanup of these old messages.


          Always use INTL kludge line:

               INTL kludge line information is used when a Netmail message
               (without or without attached echomail) is sent between
               different zone addresses.  It's a method used to ensure that
               mail gets sent to the proper address.

               With some of the early mailers, when mail is sent within the
               same zone, only the <net/node> information was being used. 
               Now that a lot more networks exist (different zone numbers)
               a method was needed to ensure that a message sent to
               86:250/110 didn't end up going to 1:250/110.  Notice the
               same <net/node> but different <zone> number.

               So the INTL kludge line was created to maintain proper
               inter-zone mail transportation/delivery.  This option is
               used to specify whether or not WILDMAIL! should insert the
               complete <zone:net/node.point> address on the first line of
               EVERY outbound Netmail message.

               Setting this option to N (the recommended setting) will
               instruct WILDMAIL! to only insert the complete
               <zone:net/node.point> address on Netmail messages destined
               for zones OUTSIDE of your Primary Zone.  For Netmail
               messages sent within the same zone, WILDMAIL! will NOT
               insert the full address on the first line of the message.

               Setting this option to Y, WILDMAIL! will insert the address
               along with special control characters (to hide this
               information) on EVERY Netmail message whether it's destined
               for the same zone or not.

               NOTE:     For some systems that don't properly handle this
                         hidden information, null messages (Netmail
                         messages with echomail file attaches) may not get
                         deleted.  WILDMAIL! however, fully conforms to the
                         specifications established for creating "null"



          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                        Page  57



          WILDMAIL! v3.01                         MISCELLANEOUS INFORMATION
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

                         messages.


          Use XMS/EMS for swap file:

               This option is used to establish whether or not WILDMAIL!
               should make use of XMS (extended memory) or EMS (expanded
               memory) for swapping out when packing/unpacking of the mail
               archives.

               When WILDMAIL! runs, it uses up a fair amount of the PC's
               base memory.  Generally there is insufficient memory left
               over to execute the programs necessary for packing and
               unpacking of the mail archives.

               WILDMAIL! overcomes this limitation by swapping out the
               contents of memory it occupies to a temporary swap file
               located either in XMS/EMS or to disk (depending on what's
               available) freeing up precious base memory to execute the
               compression/uncompression utilities.  When this process is
               complete, WILDMAIL! will swap itself back into base memory
               and resume processing of mail.


          Swap file path:

               This option is used to define the <drive:\directory> path
               where WILDMAIL! can create its temporary Swap File when it
               swaps out to compress/uncompress the mail archives.  This
               can be placed on any DOS drive that has at least 385K free.

               The preferred location would be a RAM disk because this
               would allow for extremely fast swapping.

               This option can be used on systems that are short on disk
               space on a given drive and you wish to redirect where this
               temporary file will be stored.


          Use EMS for database access:

               WILDMAIL! has been designed to take advantage of EMS
               (expanded memory) for increased speed when accessing the
               various databases.  This option is used to specify whether
               or not WILDMAIL! should take advantage of this type of
               memory (if it's available) for use specifically when
               accessing the databases.




          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                        Page  58



          WILDMAIL! v3.01                         MISCELLANEOUS INFORMATION
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

               If no EMS memory is available and this option is set to Y,
               WILDMAIL! automatically detects this and simply carries on
               normally.

               If you're running on a peer-to-peer style network (LAN) and
               encounter memory contention problems, disabling this option
               could possibly eliminate these memory related errors.

               If you're running under a multi-tasker such as DESQview, be
               aware that WILDMAIL! will attempt to grab as much free EMS
               as is available (at that moment in time).  This could be a
               problem if any other program on your system makes use of EMS
               memory, when WILDMAIL! executes, there may not be any left
               over.  The solution to this is to limit the amount of EMS
               memory in the window that WILDMAIL! executes in by editing
               the desired window (in DESQview) and selecting advanced
               options by pressing [F1].  Then setting the "Maximum
               Expanded Memory Size (in K):" option to a value acceptable
               for the requirements of your system.

               Please bear in mind, the more EMS memory you give WILDMAIL!,
               the faster it will run.


          Database lock count:

               WILDMAIL! has been designed to work in a true multi-user
               environment sharing databases with other users/processes
               simultaneously.  When a message is added to a conference,
               the database file needs to be locked for that brief moment
               it's being saved.  Once the message has been saved, the lock
               is then immediately removed making the database fully
               accessible again.

               Because the locking and unlocking of the message database
               causes an incredible amount of overhead (thereby increasing
               the time required to toss mail), this option is used to lock
               the database for a specified number of messages before
               unlocking it again.  This has the desirable effect of
               reducing overhead and causing a significant speed increase.

               Allowable numbers can range from 1 through 30 with a default
               value being 30.  With a value of 1, this means the database
               will be locked and then unlocked for each and every message
               added.  This is by far the slowest way to execute WILDMAIL!
               and is not recommended except in very rare circumstances.

               A value of 30 tells WILDMAIL! to keep the database locked



          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                        Page  59



          WILDMAIL! v3.01                         MISCELLANEOUS INFORMATION
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

               until the conference being tossed into changes or the
               maximum 30 message limit has been reached.  A value of 5
               indicates the database will be locked for the next 5
               messages (if they were all to go into the same conference
               database) and then unlocked.

               Caution must be exercised when using this option especially
               on slower PC's because in a multi-line environment, WILDCAT!
               will attempt to save information to a database for a period
               of 60 seconds before a fatal error will occur.  This process
               is indicated by the "Lock Retry ##" being displayed in the
               upper RH corner of the screen.  The slower the PC, the
               longer it can take to save messages and thereby possibly
               exceeding WILDCAT!'s 60 second limit.

               On faster machines, a value of 30 is normally sufficient,
               but this is on a case by case basis and warrants close
               monitoring to ensure the time limits on locking the database
               files aren't exceeded.  If a fatal error does occur, it
               indicates the number specified should be lowered (maybe 15
               or so) and executed/monitored again.  Remember the higher
               the number, the longer the database will be locked and the
               faster messages can be tossed.

               It should be pointed out that WILDCAT!'s "Lock Retry ##"
               displayed in the upper RH corner of the screen on a node (or
               task in DESQview) is a simple indication that a database is
               temporarily locked by another node or another utility while
               information is being save to the file.  This is not an error
               and can occur from time to time in a multi-line environment.

               The real error occurs when the file can't be accessed in the
               allotted amount of time.  That is the point where you want
               to recheck your settings here.


          Delete archives after tossing:

               During the course of processing newly received mail, a fair
               amount of disk space is required to hold copies of both the
               newly received mail archive and the uncompressed contents of
               that file.

               With this option set to Y, WILDMAIL! will save the original
               mail archive until all the .PKT files contained within it
               have been successfully tossed.  This is commonly used to
               ensure the messages are tossed properly before anything gets
               deleted.



          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                        Page  60



          WILDMAIL! v3.01                         MISCELLANEOUS INFORMATION
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

               With this option set to N, WILDMAIL! immediately deletes the
               original mail archive after uncompressing the contents and
               then starts the tossing process.  This saves on the amount
               of disk space required.  It should be noted that there is a
               point where both the original archive AND the uncompressed
               contents will be on the disk at the same time prior to the
               original archive being deleted.  This can be an important
               consideration when you're running low on disk space.

               Unfortunately, there is no way around this problem. The best
               advice is to make sure you have plenty of disk space prior
               to tossing mail.

               If for some reason, the mail is not successfully tossed, the
               next time WILDMAIL! tosses, it will attempt to uncompress
               the mail archive again and restart the process.  Since there
               could be .PKT files still left over from the original
               uncompression process, you need to make sure the compression
               format used has the command line parameter to automatically
               overwrite the existing .PKT files. (they're the same ones
               anyway)

               Otherwise, the uncompression utility will hang the system
               waiting for you to acknowledge the overwrite.  Since this
               could tie up your BBS all day long, this is an important
               consideration.  Please refer to the Main Menu, Mail Archive
               Definition, Parameter options for additional information for
               each specific format.


          Forward mail .PKTs:

               WILDMAIL! has the ability to forward complete .PKT files on
               to other nodes without processing them first.  The
               recommended setting is to disable this feature by selecting
               N.

               With this option set to Y, when WILDMAIL! encounters a .PKT
               file destined for an address different than your own, it
               will pack up the file using the default packer type (if a
               definition hasn't already be set for that address).  Then it
               creates a Netmail message with this file attached and places
               it in the outbound file area for transmission by your front
               end mailer.  Extreme caution must be used with this method
               because of the potential for message duplication loops.

               With this option set to N, any incoming .PKT files that are
               not intentionally destined for your systems primary address



          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                        Page  61



          WILDMAIL! v3.01                         MISCELLANEOUS INFORMATION
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

               or any of your AKA addresses will automatically be renamed
               to .BAD and no forwarding or processing will take place at
               all.

               If this occurs, it then requires manual intervention on your
               part to try and determine the reason for this .PKT's
               arrival.


          Default archive format:

               This field is used when setting a default compression and
               uncompression format.  Tapping the [SPACEBAR] toggles
               through the various formats available.  Presently they are:

                         ARC   ARJ   PAK   LZH   ZIP   ZOO  NONE

               This default value is used in several places.  First off, if
               your system has been configured to Forward PKT's, WILDMAIL!
               needs to know what compression method it should use when
               packing the PKT file(s) prior to preparing it for
               transmission.

               Secondly, this option is used whenever you add a new node
               address to your system.  This minimizes the amount of effort
               required by saving you an extra step.


          Enable quiet archiving:

               Due to the different methods used for displaying information
               to the screen during the compressing of outbound mail, this
               option is used to override the output of these programs and
               instead display a cleanly presented and informative display.

               With this option set to Y, WILDMAIL! will display the nodes
               address that mail is being compressed for along with its
               file size in bytes in a simple line by line format.

               With this option set to N, during the archival process, the
               compression programs will display to the screen in their
               usual fashion causing information to scroll up and
               potentially off of the screen.

               For those that use LZH as their compression type, bear in
               mind that these programs don't allow redirection and
               unfortunately will be displayed regardless of the setting
               here.



          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                        Page  62



          WILDMAIL! v3.01                         MISCELLANEOUS INFORMATION
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

          Process exclude names:

               This field is used to tell WILDMAIL! whether or not it
               should check the FROM: names on the inbound Netmail messages
               with the list of names found in the Exclude names option and
               prevent the ones that match from being tossed into the
               Netmail message conference.

               This could be handy if you want to prevent automatic
               notifications such as conference activation/deactivation
               messages or even mail from specific users from being added
               to your Netmail conference.

               Toggling this field to Y unprotects the Exclude names option
               allowing you to add, delete and modify user names
               accordingly.  Conversely, setting this field to N protects
               the Exclude names field and WILDMAIL! will not check the
               FROM names at all.

               NOTE:     Because of the additional overhead involved of
                         checking each new message before being tossed,
                         this option can slightly decrease the performance
                         of WILDMAIL!.


          Exclude names:

               As discussed above, after pressing [ENTER] on this field,
               displayed is a list of user names that WILDMAIL! will use
               (if the Process exclude names option has been set to Y) when
               checking inbound mail preventing messages FROM: the names
               contained here from being added to your message bases.

               Up to 30 user names may be added containing no more than 36
               characters each.  Shown below is a description of the
               available options.

               Create an exclude name:

                    Pressing the [INSERT] key pops up a window allowing you
                    to enter up to 36 characters of a user name.  The
                    normal editing keys are active.  Exact spelling of the
                    name is crucial because this is what WILDMAIL! will use
                    when comparing names.

                    When the new name has been entered, pressing [F10]
                    saves the changes while [ESC] aborts and exits.




          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                        Page  63



          WILDMAIL! v3.01                         MISCELLANEOUS INFORMATION
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

               Delete an exclude name:

                    After selecting the desired user name by positioning
                    the highlight bar with the Up/Dn arrow keys and
                    pressing the [DELETE] key, a prompt is displayed
                    confirming your request for deletion.  Pressing Y
                    deletes the entry while [ESC] aborts the process and
                    returns you to the previous screen.


               Edit an exclude name:

                    After selecting the desired user name by positioning
                    the highlight bar with the Up/Dn arrow keys and
                    pressing the [ENTER] key, a window is displayed with
                    the user name available for modification.

                    The normal edit keys are available such as [BACKSPACE],
                    [INSERT] and [CTRL-Y] to clear the entire entry.  When
                    the desired changes are completed, pressing [F10] saves
                    the changes while pressing [ESC] aborts and returns you
                    to the list of user names.


          Save duplicate messages:

               With this option set to Y, when WILDMAIL! encounters a
               duplicate message, it will toss it into the path specified
               via the Duplicate message path option (see below) as a
               standard .MSG formatted message.  This option handy in case
               you want to try an track down a duplicate message problem. 

               With the field set to N, when WILDMAIL! encounters a
               duplicate message, it will simply delete it.


          Duplicate message path:

               With the Save duplicate message option set to Y, you should
               use this option to specify the complete DOS path to where
               the duplicate messages are to be stored.  This directory
               should be unique and NOT shared with any other program!


          Program to run after unpacking:

               This option allows you to specify the DOS path and program
               name (or batch file) WILDMAIL! should execute immediately



          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                        Page  64



          WILDMAIL! v3.01                         MISCELLANEOUS INFORMATION
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

               after the mail unpacking process has been completed and
               before WILDMAIL! starts the tossing process.

               This could be used to execute some form of grundged mail
               detector on all the PKT files that WILDMAIL! just
               uncompressed or even some form of cost accounting system
               such as WMINFO! prior to the messages being tossed into
               WILDCAT! (and/or forwarded to your downlink nodes).

               If you are going to be executing more than one program, you
               should specify a batch file as the program name.  Simply
               include all the processes you wish to do in the batch file
               making sure you DO NOT execute WILDMAIL! a second time.

               The batch file should simply terminate once the desired
               programs have been executed.  This is because WILDMAIL! will
               swap itself out of memory and then execute the specified
               program name (or batch file).  Once the batch file is
               finished, WILDMAIL! restores itself into memory and resumes
               the tossing process.

               Normal DOS naming conventions must be strictly adhered to
               when defining the path and program name.  If the option is
               left blank, after all the mail has been unpacked, WILDMAIL!
               will simply begin the tossing process effectively bypassing
               this step.

























          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                        Page  65



          WILDMAIL! v3.01                  MULTI NETWORK/ZONE CONFIGURATION
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

          MULTI NETWORK/ZONE CONFIGURATION

          This selection allows you to configure how WILDMAIL! will handle
          mail when processing in multiple networks such as inbound and
          outbound zone matching, default zones and assigning specific zone
          information.  

          Typically this is used to maintain a degree of compatibility with
          some of the older mailers that may communicate with your system. 
          Also, since WILDCAT! doesn't provide the ability to specify a
          certain Origin Address when entering in Netmail messages, you
          would use the Outbound zone matching option to tell WILDMAIL!
          what address to use in that case.


          Assign a zone to an address:

               This option is used to offer backwards compatibility with
               some of the older style mailers still in use today.  It
               seems when these mailers would send out an Netmail message,
               it would only include the <net/node> address as opposed to
               the full address of <zone:net/node.point>.  Normally this
               wouldn't be a problem when a message was sent within the
               same zone, but when mail was sent to a different zone
               because the zone information was missing, it would never
               reach its destination address.

               The solution to this problem is to take the known net/node
               address and have WILDMAIL! assign a zone number to it.  This
               option is used to perform this function by allowing you to
               specify what the <zone> portion of the address should be
               automatically added to the <net/node> address they send
               Netmail to your system with.

               If node addresses have been previously defined, they will be
               displayed in the current window.  On the left will be the
               address they use to send Netmail to your system in the
               following <net/node.point> format.  To the right is the
               <zone> number that WILDMAIL! will automatically insert in
               front of the address to form a complete
               <zone:net/node.point> address.

               From this window, the following options are available.

               Create a Zone Assignment

                    Pressing the [INSERT] key allows you create an
                    assignment by popping up a window allowing you to



          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                        Page  66



          WILDMAIL! v3.01                  MULTI NETWORK/ZONE CONFIGURATION
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

                    specify the <zone> number to be assigned to the
                    <net/node.point> address.  Shown below is an
                    explanation of the various fields displayed.

                    Zone      This field is used to specify the <zone>
                              number you wish to be assigned to the
                              <net/node.point> address you will be defining
                              to the right of this field.

                              WILDMAIL! will then take this <zone> and
                              automatically append it to the
                              <net/node.point> address to form a more
                              complete <zone:net/node.point> address format
                              required for proper inter-zone (or across
                              networks) mail transfer.

                    Net       This field is used to specify the <net>
                              portion of the address you wish to have the
                              <zone> address added to.  

                    Node      This field is used to specify the <node>
                              portion of the address you wish to have the
                              <zone> address added to.

                    Point     This field is used to specify the <point>
                              portion of the address you wish to have the
                              <zone> address added to.

                    Up to 20 individual assignments of a <zone> to a
                    <net/node.point> can be made.  Once the assignment is
                    complete, pressing [F10] will save the entry.


               Delete an Assignment

                    After selecting the desired node address by using the
                    Up/Dn arrow keys, pressing the [DELETE] key brings up a
                    friendly prompt confirming your request.  Pressing Y
                    deletes the assignment while pressing [ESC] aborts and
                    returns you to the previous screen.


               Edit an Assignment

                    After selecting the desired node address by using the
                    Up/Dn arrow keys, pressing the [ENTER] key brings up
                    this assignment in edit mode.  By positioning the
                    highlight bar, you can make the necessary changes.  



          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                        Page  67



          WILDMAIL! v3.01                  MULTI NETWORK/ZONE CONFIGURATION
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

                    Once the modifications have been made, pressing [F10]
                    saves the new values and returns you to the list of
                    node assignments.


          Outbound zone matching:

               Presently within WILDCAT!, there is no method to define what
               your origin address should be when sending out Netmail
               messages.  This is important because if you wish to send a
               Netmail message to someone in a network different than your
               primary address, they wouldn't know your node address (for
               that network) to send a reply to, only your primary address
               from a different network.

               This option overcomes that limitation by allowing you to
               define which of your node addresses (AKA's) WILDMAIL! should
               use for each network you could be sending messages to.  In
               the above example, if you sent a Netmail message to someone
               in zone 86, WILDMAIL! would use your address of 86:250/100
               as the messages origin address.

               For example, let's say you belong to 2 networks and your
               node addresses were 86:250/100 and 1:161/123 with your
               primary address being 1:161/123.  When you wish to send
               someone a Netmail message in zone 86, because WILDCAT!
               doesn't allow you to specify origin addresses, they would
               think the message came from your primary address of
               1:161/123.

               To clarify this, in Fidonet there are currently 6 zones
               numbered 1 through 6, so if your address was 1:161/123, you
               would normally assign zones 1, 2, 3, 4, 5 and 6 to that
               address.  This way, any Netmail messages created from your
               system destined for zones 1 through 6, WILDMAIL! would use
               your address of 1:161/123 as the messages origin address.

               Normally you would assign the same <zone> number as your
               AKA's <zone> number for each AKA address you have.  In other
               words, if you had 2 AKA's, 86:250/110 and 100:910/13, you
               would assign <zone> 86 to AKA 86:250/110 and <zone> 100 to
               AKA 100:910/13.

               After selecting the desired node address by using the UP/DN
               arrow keys, pressing [ENTER] brings up this node in edit
               mode.  Once the modifications have been made, pressing [F10]
               saves the new values and returns you to the list of node
               assignments.



          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                        Page  68



          WILDMAIL! v3.01                  MULTI NETWORK/ZONE CONFIGURATION
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

               NOTE:     It should be noted that you will not be able to
                         add, edit or delete an AKA address here.  Only the
                         definition of the zone to use for a specific AKA
                         address.  AKA addresses are handled via the Main
                         Menu option System Information, AKA Addresses.  

               Also, the assignment of addresses with this option only
               affects the messages being extracted from the Netmail
               conference and NOT the other echomail conferences.  The
               origin addresses for echomail conferences are assigned via
               the Main Menu option, Conference Area Management.








































          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                        Page  69



          WILDMAIL! v3.01                          MAIL ARCHIVE DEFINITIONS
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

          MAIL ARCHIVE DEFINITIONS

          This option is used to define the actual programs used to
          uncompress the inbound mail archives and compress the outbound
          mail for the 6 archival formats supported.  In addition, command
          line parameters are defined to control the operational
          characteristics of each of these individual programs.

          InUse Flag

               This flag is used to indicate whether or not a node address
               has been configured to use this uncompression format as
               indicated by the presence of a (é).  When WMCONFIG is exited
               with the Save option, it will check only those formats that
               have the InUse flag set for the presence of the specified
               uncompression program to ensure it exists before allowing
               WILDMAIL! to be executed.

               If this option contains an asterisk (*) character, it
               indicates this compression/uncompression format has been
               selected as your Default archive format (as defined from the
               Miscellaneous Information menu).


          Type

               This column indicates the compression format that the
               following compression programs and command line parameters
               will be associated with.  Presently 6 different formats are
               supported.

                         ARC   ARJ   LZH   PAK   ZIP   ZOO

               These individual types are referenced throughout the
               configuration program, so the assignment of the program name
               and command line parameters are critical.

               The compression format of ARC has several programs written
               by different authors causing quote a bit of confusion and
               compatibility problems.  When defining the ARC format, be
               sure and carefully select the proper one that best suits
               your needs.

               Shown below are several popular ARC format compression
               programs.

                    ARCA.COM  - Written by Wayne Chin & Vernon Buerg
                    PKARC.COM - Written by Phil Katz of PKWARE, Inc



          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                        Page  70



          WILDMAIL! v3.01                          MAIL ARCHIVE DEFINITIONS
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

                    PKPAK.COM - Written by Phil Katz of PKWARE, Inc.

               Something that should be pointed out here is the fact that
               the reference to ARC, ARJ, LZH, PAK, ZIP and ZOO is simply
               just that, a reference.  Because you have the ability to
               assign a specific compression and uncompression program to a
               type, you have the ability to create a unique type, but one
               that uses one of the predefined type names.  This however
               only applies to outbound mail, or more specifically mail
               that is compressed for outbound transmission.

               WILDMAIL! does not use the uncompression format selected and
               "expect" that mail for a specific node will be in that
               format.  Instead, it reads the first few bytes of the mail
               archive and automatically determines it.  Once determined,
               it then uses the assigned uncompression program (for that
               type) and proceeds to uncompress the archive.

               So you will not be able to completely design a new type. 
               The limitation is the way WILDMAIL! detects the inbound mail
               archive.  Presently there are no plans on allowing this
               option because of the complexity involved in allowing the
               user to design a method by which WILDMAIL! should determine
               the compression method used on the inbound archive.

               Special Format - NONE

                    A special type called NONE exists when you don't want
                    WILDMAIL! to create compressed mail archive(s) of the
                    PKT files it has created.  Instead you want these PKT
                    file(s) to be placed into a special directory.

                    This special <drive:\directory> is defined via the PKT
                    Path field found in the Node Information and allows you
                    to specify where WILDMAIL! should put them.  This is
                    useful for those folks that are using FredMail to
                    process messages in and out of the InterNet network.


          Method

               This column references the appropriate compression or
               uncompression method to be used with the associated programs
               and its command line parameters.







          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                        Page  71



          WILDMAIL! v3.01                          MAIL ARCHIVE DEFINITIONS
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

          Program

               This option allows you to specify the actual DOS path and
               program name you want WILDMAIL! to use for the compression
               or uncompression process for the selected Type.

               When entering the file name, you must be sure to include the
               extension.  File names ending with anything other than .EXE
               or .COM are not allowed and normal DOS naming conventions
               are required.  Make sure this program resides in the DOS
               path so when WILDMAIL! attempts to execute it, it can easily
               be found.


          Parameters:

               This field is used to specify the command line parameters to
               be used with the selected compression or uncompression
               utility.  Typically the parameters are separated by a space
               but must strictly follow the requirements of the individual
               compression or uncompression program being used.  Please
               refer to Appendix A for specific command line parameters for
               the individual programs or the appropriate documentation
               from the utilities author.


          Archival Process

          When WILDMAIL! attempts to compress an outgoing mail archive, it
          creates a temporary batch file with the compression utility file
          name followed by its associated command line parameters and then
          the output name of the archive file. This batch file is then
          executed in a DOS shell.  When the compression process is
          completed, the temporary batch file is deleted and WILDMAIL!
          resumes any remaining processes.
















          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                        Page  72



          WILDMAIL! v3.01                           ORIGIN LINE MAINTENANCE
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

          ORIGIN LINE MAINTENANCE

          This option is used to create, edit, modify and delete origin
          line information and specify which origin line is to be used with
          what conference or group of conferences.  When WILDMAIL! extracts
          newly created messages (from your system) and prepares them for
          transmission into the various network(s), the selected origin
          line will be automatically added to the bottom of each extracted
          message.  

          As the name implies, it is used to identify where the message
          originated (or came) from and serves several purposes.  First
          off, it allows the network administrators to track a message to a
          specific system in case of duplicates or other various reasons
          and second, it gives you a mechanism with which you can advertise
          your BBS.

          Up to 60 characters containing system information like phone
          numbers, cute tag (style) lines, BBS name and such may be
          included.  The actual line length to limited to your Origin
          address for the selected conference plus the associated * Origin:
          prefix and the required parentheses and spaces enclosing your
          Origin Address for a maximum length of 78 characters as shown
          below.

             * Origin: xxxxxxxxxxxxxxxxxxxxxxxxxxxx (zone:net/node.point)

            |< By WM >|<-- Your information here ->|<-- Added by WM --->| 
            |<--------------- Maximum of 78 characters ---------------->|

          Since this is checked on a conference by conference basis
          (because of possible varying Origin Address lengths) the initial
          limit is set to 60 characters here.  Ultimately, the length is
          checked when adding a Origin line to a specific conference. See
          Main Menu selection, Conference Area Management for additional
          information.

          Entering specific node addresses in the Origin line is NOT
          necessary because WMCONFIG! automatically puts this information
          in based upon an address you've previously defined as the Origin
          Address for the selected conference.


          Active Keystrokes

          Following is a list of available keys you may use in the
          selection process of the existing origin lines.




          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                        Page  73



          WILDMAIL! v3.01                           ORIGIN LINE MAINTENANCE
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

          Up/Dn Arrow Keys

               You may use the Up/Dn arrow keys to position the highlight
               bar on the desired origin line.  If more Origin lines exist
               than will fit on the screen, holding down the Down arrow key
               will scroll through the entire list.  


          [SPACEBAR]

               Tapping the [SPACEBAR] on the highlighted Origin line will
               select it as indicated by the presence of a (é).  This is
               useful when you wish to delete a batch of Origin lines at
               one time.  Please refer to the Delete an Origin line option
               shown below.


          [CTRL-ENTER]

               Holding down the [CTRL] key and pressing [ENTER] functions
               identically to the [SPACEBAR] except that it will select all
               the available Origin lines at one time.  Pressing this
               combination a second time deselects them.


          The Origin line indicated with a (*) is not selectable because
          it's considered your Primary Origin line and can not be deleted
          unless it's replaced by a new one first.  This can be
          accomplished by using the [INSERT] key, creating a new Origin
          line and then returning to the Main Menu option, System
          Information and changing your Primary Origin line selection. 
          Then you may return and delete that Origin line.


          Create a new Origin line:

               Pressing the [INSERT] key pops up a window where you can
               enter in the new information.  The LEFT/RIGHT arrow keys and
               [BACKSPACE] keys are active for any editing changes. 
               Pressing [ESC] aborts any changes made while pressing [F10]
               saves the information.


          Delete an Origin line(s):

               After selecting the desired Origin line(s), pressing this
               key initiates the deletion process for the selected Origin
               line(s) by popping up a window confirming your request. 



          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                        Page  74



          WILDMAIL! v3.01                           ORIGIN LINE MAINTENANCE
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

               Answering Y to the prompt (confirming the deletion request)
               pops up another window asking you if you want to delete this
               Origin line from all the conferences that currently use it. 

               Answering Y to this will perform two steps.

                    1)   Searches the conference database for all
                         occurrences of this Origin line and automatically
                         replaces the old line with your previously defined
                         Default Origin line.  (The Origin line that
                         contains the (*) next to it).

                    2)   The Origin line is then physically removed from
                         the database of available Origin lines.

               Answering N to the prompt will simply delete the Origin
               line(s) from the database and leave the previously
               associated conferences with the old Origin information
               intact.

               Since the Primary Origin line (indicated by the (*) next to
               it) is used to replace the deleted Origin lines, it can only
               be deleted after it has been replaced by a new one.  This
               can be accomplished be creating a new one, select this new
               one as your Primary Origin line and then delete the old one.


          Edit an existing Origin line:

               After selecting the desired Origin line by using the Up/Dn
               arrow keys, pressing the [ENTER] key brings up this Origin
               line in edit mode.  The LEFT/RIGHT arrow keys and
               [BACKSPACE] keys are active for any editing changes. 
               Pressing [ESC] aborts any changes made while pressing [F10]
               saves the information.

               Once the editing process is complete, WMCONFIG! will
               automatically detect any changes made and then prompt you if
               you wish to have all the conferences that are using this
               Origin line to be updated as well.

               Selecting Y to this prompt causes WMCONFIG! to search all
               the conferences using this origin line and update it with
               the new changes.  Progress during this process is indicated
               by a bar graph.






          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                        Page  75



          WILDMAIL! v3.01                           ORIGIN LINE MAINTENANCE
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

          What is an Origin/Tear line combination?

          When WILDMAIL! extracts messages from the message base, it
          performs several operations the least of which is adding what's
          called a "Tear line" and a "Origin line" at the bottom of each
          extracted message.

          The Tear line is identified by the three leading dash marks "---"
          and typically indicates the tosser used along with its version
          and serial number.

          The Origin line is identified by the leading "* Origin:" and
          contains a brief description of the system it originated from, a
          BBS name and possibly a phone number.   This line also contains
          the nodes network address enclosed in parentheses, but this
          information is usually added automatically as is done by
          WILDMAIL!.

          Shown below is a sample Tear line/Origin line combination
          automatically added to the bottom of an extracted message.

          --- WM v3.00/90-0004
          * Origin: WILDMAIL! Support BBS (707) 552-0602 (1:161/123.0)

          Please note, since the Tear line is automatically inserted by
          WILDMAIL!, it's simply shown here for reference only.


          What are Tag lines?

          Tag lines are entirely different from an Origin line or Tear
          line.  These are special line(s) added to the bottom of a message
          (before WILDMAIL! adds the Origin/Tear line combination) by
          callers using special message editors called Offline Mail
          Readers.

          These offline mail readers permit the callers to download a QWK
          style mail packet from your system and read and reply offline
          saving online time, thus making more available to the other
          callers on your board.

          These lines usual display the offline readers name and serial
          number combination and normally contain some form of cute phrase. 
          They serve no necessary purpose in echo style mail and are merely
          additional "baggage" added to the message.






          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                        Page  76



          WILDMAIL! v3.01                                NETWORK ACCOUNTING
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

          NETWORK ACCOUNTING

          Within WMCONFIG, you define your various different node addresses
          for the different zones (or networks) via the AKA option found on
          the Main Menu option, System information - AKA's.

          WMCONFIG will produce a list of different zone numbers (taken
          from your AKA's) and you use this option to specify a cost
          associated with mail for each zone.  This is because typically
          you receive your mail for a particular network from a single
          source within that zone.

          This option is then used to define a cost factor for a specific
          zone by either of 2 methods, per message or per bytes received. 
          WMINFO! (Log file analyzer for WILDMAIL!) will make use of the
          numbers specified here when producing detailed cost accounting
          for the individual node addresses within a specific zone.

          It should be pointed out that all of the actual cost accounting
          is performed by WMINFO! and not WILDMAIL!. WMINFO! simply reads
          the log file generated by WILDMAIL! and extracts the information
          specified there and uses it for its report generation.  For
          additional information on WMINFO!, you may download the latest
          version from the WILDMAIL! support board listed in the
          documentation.

          Pressing [ENTER] on this field allows you to specify the costing
          factors for both methods, per message and per bytes received.


          Cost/Msg:

               This field allows you to specify the cost on an individual
               message basis.  WMINFO! uses this information when producing
               various reports.


          Cost/Byte:

               This field allows you to specify the cost based upon the
               number of bytes received.  Messages typically average
               anywhere from 800 - 1,600 bytes per message.  This value is
               then calculated by WMINFO! when doing cost analysis for your
               echomail.







          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                        Page  77



          WILDMAIL! v3.01                               DEFAULT DEFINITIONS
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

          DEFAULT DEFINITIONS

          WILDMAIL! provides you with the ability to use either the built
          in AreaRequest Manager or use an external one.  In order to use
          either the internal or external area manager (such as AreaFix)
          WMCONFIG! needs to know the minimum requirements for any newly
          added conferences.  

          This option provides the mechanism necessary to establish these
          minimums and provide additional features simultaneously.  These
          features include automatic addition of security levels, flag
          settings, PKT formats, archive naming conventions and so on. 
          This also comes in handy when you manually create a new database
          entry be it either a new node address or a new conference.  You
          just enter a couple of commands and you're finished.  It's about
          that simple!

          In order to maintain some degree of continuity with the multitude
          of options available to you for both conferences and nodes,
          certain fields availability/unavailability often depends on
          another fields settings.  Consequently, some options may not
          always be available depending on the systems current
          configuration.  

          It should be pointed out that a complete description of each of
          these fields is available from the appropriate section of this
          documentation and these settings are used primarily to define
          defaults.

          In the following section, each field that affects another's value
          (or accessibility) will be discussed along with the remaining
          fields allowing you to better understand the available options. 


          Default Node Settings

               The Nodes address and SysOp name by default are unavailable
               as are the selected conferences.  The mail archive type is
               protected as well due to the fact that its default value is
               assigned by the Main Menu, Miscellaneous Information Default
               archive format option.  You will see the currently selected
               value but will be unable to change it from this screen.

               Mail type when toggled to Type 2 packet format makes
               available the Fakenet ID option because with Type 2 packets
               only 3 dimensional addressing schemes are supported. 
               Consequently, you must define a Boss node and Fakenet
               address before you can configure point addresses.  Again,



          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                        Page  78



          WILDMAIL! v3.01                               DEFAULT DEFINITIONS
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

               this is only if the Type 2 format is selected.  The
               remaining fields are all available for assignment.


          Default Area Settings

               The conference area default definitions are a bit more
               important because with the AreaRequest manager active,
               conferences can be activated automatically by your downlink
               node addresses.  Consequently, the settings here will help
               you better manage these new activations.  Presently, there
               are 4 protected fields preventing you from assigning values
               to them.  They are as follows:

               Area name:

                    This field is self explanatory because each new area
                    added must have its own unique name associated with it. 
                    Normally this name will be pulled from one of the
                    Forwards lists associated with each network.


               WILDCAT! conference:

                    This setting is simply not available because presently
                    there is no way to automatically create conferences
                    within WILDCAT! without taking the entire system down
                    first.


               Origin line:

                    This field is not needed because when conferences are
                    added by your downlink nodes, they are normally
                    considered "passthru" and thus will not be originating
                    from your system.  Consequently, there isn't a need for
                    origin lines.  

                    However, you may notice that the currently selected
                    default origin line is automatically added.  This is
                    because if sometime in the future you wish to
                    incorporate this conference into your WILDCAT!
                    conferences, this minimizes the amount of extra effort
                    required to that.







          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                        Page  79



          WILDMAIL! v3.01                               DEFAULT DEFINITIONS
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

               Add to SEENBYs:

                    Because this is a rather unique option and can cause
                    certain problems in normal use, this is not available.

               All remaining fields from this screen are available for your
               systems unique configuration requirements.












































          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                        Page  80



          WILDMAIL! v3.01                                   NODE MANAGEMENT
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

          NODE MANAGEMENT

          This option is used to specify the operating characteristics of
          each node address that will be transferring mail with your
          system.  Parameters like compression method, conference areas,
          passwords for various functions and so on are defined here.

          The leftmost window displays a list of node addresses that have
          been previously defined.  From this list you can add, delete or
          edit each individual node address.  

          Once nodes have been defined, you should notice that as you
          scroll through the list of addresses in the leftmost window (via
          the Up/Dn arrow keys), the window to the right displays the nodes
          current operating characteristics.  This is handy for quick
          reference during configuration changes/browsing.


          Add a new Node Address

               Pressing the [INSERT] key presents you with a template of
               settings available.  All values specified via the Main Menu
               option of Default Definitions will be used as initial
               values.  You may then modify them as desired. Further down
               in the documentation are detailed explanations of each
               fields uses.


          Delete a Node Address

               After selecting the desired Node Address by using the Up/Dn
               arrow keys, pressing the [DELETE] key presents you with a
               prompt to confirm your request to delete the selected Node. 
               Pressing Y initiates that action.  Pressing [ESC] cancels
               and returns you to the previous screen.


          Edit a Node Address

               After selecting the desired Node address by using the Up/Dn
               arrow keys, pressing the [ENTER] key brings up this Node in
               edit mode and transfers control to the window displayed to
               the right of the node addresses.


          Global Change/Modify

               Pressing [F4] brings up a screen containing a set of fields



          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                        Page  81



          WILDMAIL! v3.01                                   NODE MANAGEMENT
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

               that are available for changing.  This is an extremely
               powerful option allowing you to make sweeping changes by
               simply selecting the desired nodes, the option(s) to change,
               followed by pressing [F10].

               Selecting the desired node addresses may be accomplished by
               positioning the highlight bar over the "Nodes to modify"
               field and pressing [ENTER].  Then positioning the highlight
               bar upon the desired node and tapping the [SPACEBAR] places
               a (é) next to the node address indicating its selection.

               You may also select (or deselect) all of the nodes by
               pressing and holding down the [CTL] key and pressing
               [ENTER].

               Once the desired node(s) have been selected, pressing [F10]
               confirms the selection and returns you to the Global Edit
               screen.  Pressing the [ESC] key aborts the selection(s) and
               returns to the previous screen.

               To select a specific field to be changed, position the
               highlight bar over the desired field and press [ENTER]. You
               may now change the value to the desired setting.  Once the
               value has been defined, simply press the [ENTER] key and you
               will now notice the field has been selected indicated by the
               presence of the (é) selection dot.  Selection value
               information for each of the fields is available by pressing
               the F1 key on the desired field. 

               The AreaRequest Flags option is unique in that there is a
               set of additional options allowing you to define the method
               by which to handle the individual flags.

               After selecting this option, you are presented with a list
               of previously defined flags from which you may select any of
               three methods of handling the changes.  Tapping the
               [SPACEBAR] upon the highlighted flag toggles these choices
               as explained below.

               Select    This indicates that all nodes processed,
                         regardless of the flags current setting, will be
                         toggled to on (or selected).  This means if the
                         flag was previously set, it will remain set.  If
                         it was off, it will now become selected.

               Clear     This functions identical to select except in
                         reverse.  If the flag was previously selected, it
                         is now toggled off.  If it was previously toggled



          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                        Page  82



          WILDMAIL! v3.01                                   NODE MANAGEMENT
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

                         off, it will remain that way.

               Ignore    You can use this option on those flags that you
                         wish to leave alone.  This means if this option is
                         selected, no changes will be made whatsoever to
                         this flags current setting in the individual
                         nodes/conferences to be processed.

               Once the settings have been defined, pressing the [ESC] key
               returns you to the main Global Edit screen and places a (é)
               next to the AreaRequest flag field indicating you wish
               changes to be made.

               Prior to starting the actual global change process, you may
               deselect a specific field (prevent WMCONFIG! from making any
               changes to this option) by simply highlighting the desired
               option and tapping the [SPACEBAR].  The selection dot now is
               removed and no action will be taken on that option.

               If you wish to completely abort the global change process,
               you may at any time (prior to pressing the F10 key) press
               the [ESC] key and you will be returned to the previous
               screen.

               Now, when you're ready to instruct WMCONFIG! to make the
               changes, simply press the [F10] key.  Once the update
               process is complete, pressing the [ESC] key returns you to
               the previous screen and you can then go back and verify the
               changes.


          View Accounting/General information

               Pressing [F9] displays the remainder of the nodes
               information normally hidden from view in 25 line mode.  This
               key toggles between the nodes accounting information and its
               current configuration settings.














          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                        Page  83



          WILDMAIL! v3.01                                   NODE MANAGEMENT
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

          NODE SPECIFIC SETTINGS

          Following is a complete breakdown of the available fields and
          their uses when configuring the node addresses for your system. 
          All available keystrokes for a given field are displayed on the
          status bar located at the bottom of the screen.  Depending on a
          previous fields value, certain options may or may not be
          available.  This is due to the configuration needs/rules for each
          option.


          Node's address:

               The address defined here is a complete <zone:net/node.point>
               address of the currently selected node.  Pressing [ENTER] on
               this field pops up another window allowing you to modify the
               current values. Pressing [ESC] saves the changes and returns
               you to the Node Characteristics window and resumes edit
               mode.


          SysOp name:

               This field is used to store the name of the SysOp that this
               node address reflects.  The name used here shows up in many
               different locations within WMCONFIG and is useful when
               identifying a particular system.

               Simply enter in the name of the SysOp (up to 36 characters)
               in First Name, Last Name format for this node address.


          Active node:

               Setting this option to N will temporarily interrupt mail
               delivery to this node so the next time WILDMAIL! processes
               mail, it will NOT forward it on to them.

               This option is useful in controlling mail flow on a global
               basis for this node address.  Since this setting would be
               considered the exception to the rule, the normal setting
               here would be Y.

               It should be noted that while this option is handy, mail is
               not "stored up" for this node address, so for the duration
               this flag is set to N, all mail (for all the selected
               conferences) destined for this node will be lost.




          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                        Page  84



          WILDMAIL! v3.01                                   NODE MANAGEMENT
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

               WMINFO! (log file analyzer for WILDMAIL!) can also toggle
               this option if there is insufficient account balance for the
               node to receive their mail. (if the option is implemented)
           
               Used in this fashion, it allows complete control over
               automatic deactivation of mail if the node has an
               insufficient account balance.


          Mail type:

               This option is used to select which format WILDMAIL! should
               use when creating mail for this node address.

               Within Fidonet style networks, there are presently three
               specific formats of .PKT files (the database files that
               contain the echomail messages) that can be created by the
               various mail tossers.  Presently only 2 of the 3 formats are
               available for outbound mail.

               Tapping the [SPACEBAR] toggles these different .PKT file
               formats.  Shown below is a breakdown of the individual
               formats.

               Type 2    This format relies on 3 dimensional addressing
                         scheme in the <zone:net/node> format.  If a node
                         address is toggled to use this PKT type and is
                         considered to be a <point> off of your system,
                         there must be a corresponding Fakenet ID number
                         assigned.  This is necessary for the translation
                         of 4D to 3D formats.

               Type 2.2  This format is by far the most commonly used and
                         makes use of the 4 dimensional addressing format
                         of <zone:net/node.point>.


               NOTE:     WILDMAIL! automatically detects the presence of
                         (the yet to be accepted) format of Type 2+ and can
                         make full use of it when reading the inbound PKT
                         files.  However, presently WILDMAIL! will only
                         offer the above outbound types until the Type 2+
                         format becomes more widely accepted.  This allows
                         a degree of compatibility with those systems that
                         are already using the Type 2+ PKT formats.






          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                        Page  85



          WILDMAIL! v3.01                                   NODE MANAGEMENT
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

          Fakenet ID:

               This option is used if you have downlink nodes that will be
               points off of your system and wish to pick up mail from you
               but they don't fully support 4D addressing.  Using this
               method considers you to be a Boss Node (or HUB) for these
               points.  Fakenet ID's are typically assigned by the ZC (Zone
               Coordinator) at 1:1/0 if in Fidonet, otherwise use your own
               arbitrary number.

               This option is only used when the .PKT format of the node
               address selected is of Type 2.  This is required because of
               the inability of Type 2 PKTs to properly support 4D or four
               dimensional <zone:net/node.point> addressing.

               Any 5 digit value less than 65535 is acceptable and must be
               the same as defined in your mailers PointNet nodelist for
               its corresponding network.  A Fakenet ID is used to
               substitute your existing <net/node> address with a new
               <net/node> consisting of your original <zone>, the Fakenet
               ID and the assumed point address.

               For example, your node address (for this conference) is
               1:161/123 and the Fakenet ID is set to 23456.  WILDMAIL!
               substitutes the 161/123 portion of your address with the
               Fakenet ID of 23456 followed by a / and the assumed point
               address of the node as shown below.

                         Original Address    :    1:161/123
                         New PointNet Address:    1:23456/1

               In the above example you'll notice the addition of the /1.
               This is the actual <point> portion of the address and is
               usually assigned by you when defining your point addresses.
               So in 4D addressing, a 1:161/123.1 would translate to
               1:23456/1, and a 1:161/123.2 would be considered 1:23456/2
               etc.

               Remember, this option is used to substitute the 4D
               addressing scheme of <zone:net/node.point> for the 3D scheme
               using only the <zone:net/node> format.

               Now, when defining your downlink nodes that will be using
               this special Fakenet ID addressing scheme, you should use
               the same format as described above via the New PointNet
               Address format. So instead of defining them in 4D format
               such as 1:161/123.1, you would use the 3D format of the
               translated Fakenet ID of 1:23456/1, 1:23456/2 etc.



          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                        Page  86



          WILDMAIL! v3.01                                   NODE MANAGEMENT
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ


          Tiny SEEN-BY:'s:

               PLEASE READ THE FOLLOWING VERY CAREFULLY!

               This option is used to have WILDMAIL! automatically strip
               ALL the SEEN-BY: lines from all the mail destined for this
               node address and replace it with only your systems address
               and the node address your editing.  Because of the danger of
               creating duplicate messages within the network, this option
               would normally be set to N.

               A common use for this option would be when your system is
               gating mail between zones and you need to strip all the
               SEEN-BY: line information out.  When sending mail between
               zones, it's possible for two nodes to have identical
               addresses with the only difference being the zone number. 
               Because zone numbers are not used in SEEN-BY: lines, one of
               these node addresses would receive the mail and the other
               wouldn't. This option would be used to ensure that the node
               address you're editing would receive its mail regardless if
               the same address was previously in the SEEN-BY: lines.

               If this option is set to Y, WILDMAIL! removes all the SEEN-
               BY: lines from each message and replaces it with the node
               address from your system and the node you're editings
               address.  In other words, if your systems node address was
               86:250/100 and this node's address was 86:250/120, the SEEN-
               BY: line would read as follows:

                              SEEN-BY: 250/100 250/120

               All previous SEEN-BY: information for each and every message
               WILL BE LOST!  If this option is set to Y, the end result
               means that this nodes address you're editing MUST NOT
               FORWARD ANY MAIL RECEIVED FROM YOUR SYSTEM on to any other
               addresses or duplicate messages will be introduced into the
               network!

               It should be noted that then vast majority of systems would
               NEVER use this option so make sure you fully understand this
               option before enabling it, because if this option is set to
               Y, the possibility of creating SERIOUS duplication loops is
               DANGEROUSLY HIGH!  Caution is advised.

               If you don't understand SEENBY: lines or don't know what to
               do, simply set this option to N and don't worry about it! 
               For additional information regarding SEEN-BY: lines, refer



          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                        Page  87



          WILDMAIL! v3.01                                   NODE MANAGEMENT
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

               to Appendix G in this documentation.


          Mail Status:

               When WILDMAIL! creates outbound mail for this node address,
               it creates a mail archive (made up of compressed .PKT files)
               containing the new mail and then generates a Netmail message
               indicating the mail archive is "attached".  When the node
               attempts to pick up this Netmail message, the mail archive
               will be automatically sent at the same time.

               This option is used to specify the transfer method for which
               this Netmail message is to be processed.  This is handled by
               setting a flag on the message which is then interpreted by
               your front end mailer to determine how it should be
               processed.

               Shown below is a list of the available flags.

               None      This option is used when you don't wish to set any
                         specific mail type flag on the Netmail message. 
                         In other words, let the mailer take full control
                         of the outbound mail.

               Hold      This option indicates that all mail destined for
                         this address will be immediately placed on hold. 
                         This means your mailer will not attempt to send
                         the message to the defined address.  Instead, it
                         will simply make it available for download the
                         next time this node calls to pick up mail.

               Crash     This flag is used when you wish to have your
                         system immediately call this address and deliver
                         the mail. Care must be taken with this option
                         because depending on the time of day (or night),
                         this might be a toll call.

               NOTE:  The actual configuration and current event schedule
               of your front end mailer will dictate how the message
               ultimately gets processed.  The above flag settings are used
               to establish the Netmail messages initial flag values.


          Selected conferences:

               Pressing [ENTER] on this field brings up a complete list of
               the available conferences previously defined within



          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                        Page  88



          WILDMAIL! v3.01                                   NODE MANAGEMENT
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

               WMCONFIG!.  In order for a node to receive a specific
               conference, it must be predefined via the Main Menu option,
               Conference Area Management.

               You may use the PgUp/PgDn and UpDn arrow keys to move about
               the displayed list.  Selection is displayed by the presence
               of a (é) selection dot to the left of the conference
               information.  This means the node address you're currently
               editing is set up to send and receive mail within this
               conference.

               Shown below is a description of the available commands while
               using this option.

               Select    Tapping the [SPACEBAR] allows you to select the
                         highlight conference as indicated by the presence
                         of a selection dot (é) to the left of the
                         conference number. 

               Deselect  Tapping the [SPACEBAR] a second time will deselect
                         the conference as indicated by the removal of a
                         selection dot ( ) to the left of the conference
                         number. 

               Filter    Pressing the [F5] function key will "filter out"
                         all the non-selected conferences and only display
                         the selected ones.  This can be handy when you
                         wish to get a quick picture of the conferences
                         this node is participating in.

                         Pressing [F5] a second time will toggle the filter
                         to off and redisplay all the available conferences
                         including the selected ones.


          Mail archive format:

               Since echomail messages are commonly compressed prior to
               transmission, this option is used to define the compression
               format to be used for this node.  Tapping the [SPACEBAR]
               toggles through the available compression formats.

               Available formats are:

                         ARC   ARJ   LZH   PAK   ZIP   ZOO   NONE

               This option works in conjunction with the Main Menu option,
               Mail Archive Definitions where you define the program names



          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                        Page  89



          WILDMAIL! v3.01                                   NODE MANAGEMENT
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

               and command line parameters used for the various compression
               formats.  Once the format has been selected, pressing
               [ENTER], PgUp/Dn or Cursor Up/Dn accepts the value and
               allows you to continue editing.


               FrEdMail and Mail Gating

               If the selected mail archive type is set to NONE, outbound
               mail is created but not compressed.  Because this option is
               primarily designed for those systems that gate mail from one
               system type to another such as FrEdMail, a path needs to be
               specified to tell WILDMAIL! where these uncompressed PKT
               files should be placed.

               Because the mail type of NONE has special conditions
               associated with it, if this type is selected, the PKT Path
               option will be available.  If something other than NONE has
               been chosen, then the Standard Naming option will replace
               it.  Shown below is one of the two configuration options
               that will be presented depending on the mail type selected.


               PKT Path:

                    Because this option is only available if the mail type
                    has been set to NONE, meaning that the outbound mail is
                    in uncompressed format, this option is used to specify
                    where WILDMAIL! should copy these files to.  For
                    FrEdMail systems might would be:

                                   C:\FREDMAIL\INBOUND

                    For non-FrEdMail systems, you should specify the
                    directory where your gating software expects to find
                    new mail.  If you're real creative here, in unique
                    configurations, this could be the inbound directory of
                    a "reserved" node address.

                    Normal DOS naming conventions must be strictly adhered
                    to when specifing the path.


               Standard naming:

                    When packing up outbound mail, WILDMAIL! uses the
                    selected file compression utility to packup the
                    outbound mail archives.  The naming of these archives



          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                        Page  90



          WILDMAIL! v3.01                                   NODE MANAGEMENT
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

                    is important in maintaining proper processing sequence
                    so mail tossing will be done on a first in first out
                    basis.  In other words, when WILDMAIL! tosses mail, it
                    will toss mail created on Monday before tossing mail
                    created on Tuesday.

                    When reading messages, this prevents replies to
                    messages from showing up before the original message
                    does.

                    Typically, the first 8 characters of the file name
                    indicates the address difference in hex between the
                    source and destination systems while the file name
                    extension is used to indicate the day the mail archive
                    was created on.  Standard naming conventions are as
                    follows:

                      Mon = .MOx    Wed = .WEx    Fri = .FRx    Sun = .SUx
                      Tue = .TUx    Thu = .THx    Sat = .SAx

                    In the above example, x is used to indicate the
                    sequential number of the archive.  This value can range
                    from 0 to Z for a total of 36 possible archives for the
                    same day which will be automatically assigned by
                    WILDMAIL! dictated by the current day of the week and
                    archive "number" for the day.

                    Since Mondays mail will be processed before Tuesdays
                    mail, the x value is used to maintain proper sequence
                    within the same day.  So an archive with the extension
                    .TU2 will be processed before an archive with a .TU3
                    extension.  In other words, the mail archives are
                    processed in sequential order starting from 0 and
                    incrementing to Z. (36 possible archives for a given
                    day)

                    If this option is set to N, then all outbound mail
                    archives will have the file extension of .MO0.  All new
                    mail will then be added to that single existing archive
                    file without creating any new archives.  This could
                    make for a rather large single mail archive should that
                    node not pick up their mail for a day or two.  Be
                    careful with this setting.


          PKT password:

               In addition to secure mail transfer sessions allowed by most



          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                        Page  91



          WILDMAIL! v3.01                                   NODE MANAGEMENT
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

               mailers, WILDMAIL! offers additional security at the packet
               (PKT) level by assigning a password to each packet as it's
               created.

               This option is used to specify the actual password that is
               required (at the destination end) to properly process this
               packet.  Up to 8 characters may be entered.

               Normally this option is not used on most systems because of
               possible compatibility problems between tossers and the
               various PKT formats supported by each tosser.


          AreaRequest password:

               AreaRequest has been designed to automate a requesting nodes
               activation and de-activation of conference areas by using
               specially formatted Netmail messages.

               In order to limit access to this very powerful feature, a
               password may be assigned to the node address you're editing
               so anytime this node requests a conference change, the
               correct password will be required before any changes can
               take place.

               Up to 8 character passwords can be defined.  To maintain
               proper security, make sure no one has access to this
               password except the SysOp of this node address.

               There is however a limitation to this options capability
               within WILDCAT!.  Conferences can be activated/de-activated
               by downstream nodes, but a new conference can not be
               automatically created within WILDCAT! (on your system), this
               must be done manually by using MAKEWILD.

               The reasoning behind this is two-fold.  First of all, your
               entire WILDCAT! system must be brought down to make
               configuration changes and two, there would have to be some
               sort of method to automatically place it somewhere on the
               system disk and then allow users access to this new
               conference.  Since this just doesn't exist, there is no way
               to automatically create conferences within WILDCAT! at this
               time.

               Please don't confuse an AreaRequest style request for a
               conference with trying to create a brand new conference
               within WILDCAT!.




          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                        Page  92



          WILDMAIL! v3.01                                   NODE MANAGEMENT
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

          AreaRequest security:

               AreaRequest has been designed to automate a requesting nodes
               activation and de-activation of conference areas by using
               specially formatted Netmail messages.

               In order to use this, each Node must be assigned a security
               access level and if necessary any additional sub-levels of
               access via the AreaRequest Flags option.  This value (and
               corresponding flags) are used to match up the requesting
               nodes security level to that of the conference they are
               trying to activate.

               If their security level is equal to or greater than this
               conferences security level and any corresponding flags
               match, they may activate/de-activate it.  So, let's say
               you're carrying adult echos with a security level set to
               200, in order for a node picking up mail from you to have
               the ability to activate/de-activate them, their security
               level must be equal to or greater than the level of the
               conference desired.

               For example:

                    Conf  Conference Description       Sec Level
                    ÄÄÄÄ  ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ  ÄÄÄÄÄÄÄÄÄ
                     10   Adult Fantasies                 200
                     11   Adult Parties                   200
                     12   Adult Romances                  200
                     20   General Messages                100
                     21   Technical Support               150

               In the above list of conferences, if a node was assigned an
               AreaRequest security level of 100, they would only have the
               ability to activate/de-activate conference 20.  Let's say
               another node has been defined with a security level of 150,
               it would only have access to conferences 20 and 21 but not
               conferences 10, 11 and 12.

               For a node to have access to conferences 10, 11 and 12, they
               must have a security level of 200 or greater in order to
               activate/de-activate them.  Remember, the corresponding
               AreaRequest security level is defined for each conference
               via the Main Menu option, Conference Area Management after
               selecting the desired conference.

               When establishing a security level here, a little
               forethought is required because you must already know what



          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                        Page  93



          WILDMAIL! v3.01                                   NODE MANAGEMENT
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

               each of your conferences security levels are set to and who
               should have access to what.  Once the desired level is
               known, simply enter the value in the highlighted field.


          AreaRequest flags:

               This works in conjunction with the AreaRequest Security
               level and is used as a secondary level security system to
               further narrow down the node addresses who have access to a
               specific conference.

               Typically, you would only use this option if have adult
               conferences on your system (or similar security need) and
               you wish to limit only those systems with under-age SysOps
               from gaining access to those conferences.  Otherwise, these
               adult conferences would be available to all SysOps over the
               age of 18 that pick up mail from your system.

               While the AreaRequest Security level offers security based
               upon "<=" (less than or equal to) a given security level,
               setting an additional flag here requires that the requesting
               system pass two tests now.

                    1)   Must pass AreaRequest Security level requirements.

                    2)   The node address must have at least the same
                         flag(s) toggled here for the selected conferences
                         in their corresponding database record.

               Since these flags are based upon conferences, you should
               review how you've previously defined your restricted
               conferences to know what flags should be given to each node
               address.

               The bottom line here is simple, if a requesting node passes
               the AreaRequest requirements and requests a conference with
               flags attached to it, their node specific AreaRequest flags
               must also match that conferences flags.  Otherwise the node
               will be unable to activate the conference.

               The node may actually have more flags than what's defined
               for the requested conference, but never less than.  Please
               keep in mind that the node must have at least the same flags
               that the requested conference requires.  For additional
               information please refer to the Main Menu, Conference Area
               Management option AreaRequest flags.




          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                        Page  94



          WILDMAIL! v3.01                                   NODE MANAGEMENT
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

          Comment:

               This field is used as a "scratch pad" to possibly leave
               yourself a note about this node address.

               Up to 35 characters may be entered in this field.


          Activation date:

               This field is used to indicate when the node was first added
               to your configuration.  You may edit this by using the
               dd/mm/yy format.  This is used in various reports generated
               by WMUTIL!.


          Deactivation date:

               This field is identical to the activation date field except
               that it initiates the date it was deactivated.  If you
               change the nodes status to inactive, this date will not be
               automatically updated.  You must manually set it yourself.

               If the nodes status has been changed by WMINFO!, this date
               will be set automatically.  This can be used to indicate how
               long the node has been inactive.


          Account balance:

               This option is used exclusively by WMINFO!, our Log File
               Analyzer for WILDMAIL!.  The value here indicates the
               current dollars amount associated with this nodes account
               balance.

               This balance information is updated by WMINFO! after it has
               run and can be used to have the node address automatically
               toggled off (prevented from picking up mail) if the node
               doesn't keep a positive account balance.


          Message count in:

               This option is used exclusively by WMINFO!, our Log File
               Analyzer for WILDMAIL!.  Information is stored here and
               directly relates to this node addresses statistics.

               This field indicates the total number of messages from all



          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                        Page  95



          WILDMAIL! v3.01                                   NODE MANAGEMENT
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

               the selected conferences this node has sent to your system
               since the activation date.


          Message count out:

               This option is used exclusively by WMINFO!, our Log File
               Analyzer for WILDMAIL!.  Information is stored here and
               directly relates to the node address statistics.

               This field indicates the total number of messages from all
               the selected conferences this node has received from your
               system since the activation date.


          Byte count in:

               This option is used exclusively by WMINFO!, our Log File
               Analyzer for WILDMAIL!.  Information is stored here and
               directly relates to this node addresses statistics.

               This field indicates the total number of bytes from all the
               selected conferences this node has sent to your system since
               the activation date.


          Byte count out:

               This option is used exclusively by WMINFO!, our Log File
               Analyzer for WILDMAIL!.  Information is stored here and
               directly relates to this node addresses statistics.

               This field indicates the total number of bytes from all the
               selected conferences this node received from your system
               since the activation date.


          PKT count in:

               This option is used exclusively by WMINFO!, our Log File
               Analyzer for WILDMAIL!.  Information is stored here and
               directly relates to this node addresses statistics.

               This field indicates the total number of PKT files that have
               been sent to your system since the activation date.






          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                        Page  96



          WILDMAIL! v3.01                                   NODE MANAGEMENT
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

          PKT count out:

               This option is used exclusively by WMINFO!, our Log File
               Analyzer for WILDMAIL!.  Information is stored here and
               directly relates to this node addresses statistics.

               This field indicates the total number of PKT files that have
               been sent to their system since the activation date.











































          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                        Page  97



          WILDMAIL! v3.01                        CONFERENCE AREA MANAGEMENT
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

          CONFERENCE AREA MANAGEMENT

          This section allows you to define what message area goes with
          each conference on your system by allowing you to add, edit and
          delete message conference areas.  Each conference area must be
          defined before a node address may obtain access to it.


          Add a new Conference

               Pressing the [INSERT] key presents you with a template of
               settings available.  All values specified via the Main Menu
               option of Default Definitions will be used as initial
               values.  You may then modify them as desired. Further down
               in the documentation are detailed explanations of each
               fields uses.


          Delete a Conference

               After selecting the desired Conference by using the Up/Dn
               arrow keys, pressing the [DELETE] key presents you with a
               prompt to confirm your request to delete the selected Node. 
               Pressing Y initiates that action.  Pressing [ESC] cancels
               and returns you to the previous screen.


          Edit a Conference

               After selecting the desired Conference by using the Up/Dn
               arrow keys, pressing the [ENTER] key brings up this
               Conference definition in edit mode.


          Global Change/Modify

               Pressing [F4] brings up a screen containing a set of fields
               that are available for changing.  This is an extremely
               powerful option allowing you to make sweeping changes by
               simply selecting the desired conference, the option(s) to
               change followed by pressing [F10].

               Selecting the desired conferences may be accomplished by
               positioning the highlight bar over the "Conferences to
               modify" field and pressing [ENTER].  Then positioning the
               highlight bar upon the desired conference and tapping the
               [SPACEBAR] places a (é) next to the conference name
               indicating its selection.



          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                        Page  98



          WILDMAIL! v3.01                        CONFERENCE AREA MANAGEMENT
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

               You may also select (or deselect) all of the conferences by
               pressing and holding down the [CTL] key and pressing
               [ENTER].

               Once the desired conferences have been selected, pressing
               [F10] confirms the selection and returns you to the Global
               Edit screen.  Pressing the [ESC] key aborts the selection(s)
               and returns to the previous screen.  To select a specific
               field to be changed, position the highlight bar over the
               desired field and press [ENTER]. You may now change the
               value to the desired setting.  Once the value has been
               defined, simply press the [ENTER] key and you will now
               notice the field has been selected indicated by the presence
               of the (é) selection dot.

               Selection value information for each of the fields is
               available by pressing the F1 key on the desired field.

               The AreaRequest Flags option is unique in that there is a
               set of additional options allowing you to define the method
               by which to handle the individual flags.

               After selecting this option, you are presented with a list
               of previously defined flags from which you may select any of
               three methods of handling the changes.  Tapping the
               [SPACEBAR] upon the highlighted flag toggles these choices
               as explained below.

               Select    This indicates that all conferences processed,
                         regardless of the flags current setting, will be
                         toggled to on (or selected). This means if the
                         flag was previously set, it will remain set.  If
                         it was off, it will now become selected.

               Clear     This functions identical to select except in
                         reverse.  If the flag was previously selected, it
                         is now toggled off.  If it was previously toggled
                         off, it will remain that way.

               Ignore    You can use this option on those flags that you
                         wish to leave alone.  This means if this option is
                         selected, no changes will be made whatsoever to
                         this flags current setting in the individual
                         conferences to be processed.

               Once the settings have been defined, pressing the [ESC] key
               returns you to the main Global Edit screen and places a (é)
               next to the AreaRequest flag field indicating you wish



          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                        Page  99



          WILDMAIL! v3.01                        CONFERENCE AREA MANAGEMENT
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

               changes to be made.

               Prior to starting the actual global change process, you may 
               deselect a specific field (prevent WMCONFIG! from making any
               changes to this option) by simply highlighting the desired
               option and tapping the [SPACEBAR].  The selection dot now is
               removed and no action will be taken on that option.

               If you wish to completely abort the global change process,
               you may at any time (prior to pressing the [F10] key) press
               the [ESC] key and you will be returned to the previous
               screen.

               Now, when you're ready to instruct WMCONFIG! to make the
               changes, simply press the [F10] key.  Once the update
               process is complete, pressing the [ESC] key returns you to
               the previous screen and you can then go back and verify the
               changes.


          Forward-To Nodes

               Pressing the [F9] key displays a list of node addresses that
               are currently receiving this conference along with its
               operational characteristics.  Since this option is used for
               information purposes only, no modifications can be made
               here.

               Using the Up/Dn arrow keys allows you to scroll through the
               list of addresses displaying the operation characteristics
               for each node address.

               If you wish to modify any of this information, you'll need
               to return to the Main Menu option, Node Management and after
               selecting the node address, make the necessary changes. 
               Once viewing is complete, simply press the [ESC] key to
               return to the previous screen.


          Find Conference Area

               Pressing ALT-F (holding down the ALT key and pressing F)
               brings up a window allowing you specify the search method
               used to locate a specific conference.  This option is handy
               for those systems that carry a lot of conferences and thus
               greatly simplifies locating a specific one.

               If the desired conference is not located, the highlight bar



          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                       Page  100



          WILDMAIL! v3.01                        CONFERENCE AREA MANAGEMENT
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

               will be positioned to the closest match.  Depending on the
               search method employed, different field specifications are
               available.  Shown below is a breakdown of those fields.


                Find via:

                    You may specify 2 different methods - Area name or Area
                    number.  Tapping the [SPACEBAR] toggles between the two
                    methods.

                    Number:

                         With this method toggled, the Area No: prompt is
                         displayed.  You may enter in any valid conference
                         number.  If the conference number you enter is not
                         valid, WMCONFIG! will simply ignore the request.


                    Area name:

                         With the Find via: option set to Name, you may
                         enter up to 36 characters to search for.  If you
                         are uncertain as to the exact area name, you may
                         enter in a partial string and once the search
                         process is initiated, WMCONFIG! will find the
                         closest match and position the highlight bar
                         their.


               Initiating the Search

                    Once the search parameters have been established, you
                    may start the search by pressing [F10].

















          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                       Page  101



          WILDMAIL! v3.01                        CONFERENCE AREA MANAGEMENT
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

          CONFERENCE SPECIFIC SETTINGS

          Following is a complete breakdown of the available fields and
          their uses when configuring the conferences for your system.  All
          available keystrokes for a given field are displayed on the
          status bar located at the bottom of the screen.  Depending on a
          previous fields value, certain options may or may not be
          available.  This is due to the configuration needs/rules for each
          option.


          Area name:

               This option is used to specify what area name (hidden within
               each message) is to be matched up with a specific conference
               number within WILDCAT!.  Area names must be contiguous in
               form and thus may NOT contain any spaces.  This name should
               NOT be confused with the actual conference description such
               as is entered via MAKEWILD.

                    CAUTION:

                    DO NOT specify your NETMAIL conference as a specific
                    conference in the database here.  The Netmail
                    conference number should be specified from the Main
                    Menu option System Information, BBS Specific Options,
                    Netmail Conference Number.

                    If you specify your Netmail conference here, you may
                    end up forwarding your Netmail messages to places where
                    they don't belong and cause unpredicatable results. 
                    PLEASE BE CAREFUL!

               When you receive Fidonet style mail, messages from various
               different conferences are usually bundled together.  In
               order to organize which message goes to what conference,
               there is a special keyword located within the header of each
               message called AREA:.  The name immediately following this
               definition is the actual conference area name this message
               belongs in.

               For example, if you use a file viewer utility (such as our
               ViewPKT! program) to view the header portion of a message
               and see the definition:

                                   AREA:WILDCAT

               It indicates the message came from the Wildcat! conference



          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                       Page  102



          WILDMAIL! v3.01                        CONFERENCE AREA MANAGEMENT
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

               and would be tossed into a conference with an area name
               definition of WILDCAT.


               [F2] - Area Pick

               If you have already defined Forward lists in the AreaRequest
               manager section, pressing [F2] displays a list of Forward
               lists to choose from.  Positioning the highlight bar on the
               desired list and pressing [ENTER] displays a complete list
               of area names and descriptions read directly from the
               defined Echo list filename defined for that network.

               From here you can select the desired area by positioning the
               highlight bar and pressing [F10].  The area name and
               description are automatically transferred to the appropriate
               fields and you are returned to the area definition screen.


          Long Description:

               This option is used as a verbose description of the message
               conference.  When you add a new conference, this name can be
               read automatically from the WILDCAT! database files by
               positioning the cursor on the WILDCAT! conference number and
               pressing [F2].

               Primarily this name is used for your reference only and will
               not affect the messages for this conference in any manner.
               However, if you make a change to the conference description
               here, it will NOT change the primary configuration in your
               WILDCAT! database files.

               To avoid confusion, it might be better to leave the long
               description the same as was initially read from the WILDCAT!
               database files.


          Passthru area:

               A conference is considered to be "passthru" when none of the
               messages for the conference are to be added to your systems
               message base(s).  This means you forward mail for this
               conference onto your downlink node address(es) without
               tossing them into your system.

               If you want messages from this conference to be tossed into
               your systems message base, then you should answer N to this



          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                       Page  103



          WILDMAIL! v3.01                        CONFERENCE AREA MANAGEMENT
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

               option. Otherwise toggling this option to Y will instruct
               WILDMAIL! to not look for a corresponding message base (on
               your system) to toss this mail into and simply forward this
               mail onto the designated downlink node address(es).


          WILDCAT! conference:

               This option is used to match a conference area name found in
               the PKT file being processed to your WILDCAT! conference
               number.

               For example, let's say conference number 18 on your system
               is called "Wildcat! Tech Support" and you defined this
               conference to use an area name of WILDCAT.  When WILDMAIL!
               encounters a message with the area definition (in the header
               of the message) of AREA:WILDCAT, WILDMAIL! will know to toss
               it into conference 18 on your system.

               Keypress  Description/Action
               ÄÄÄÄÄÄÄÄ  ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
               [F2]      Pressing this key brings up a list of available
                         conferences contained within WILDCAT!.  WMCONFIG
                         will check to ensure only one WILDCAT! conference
                         number is used preventing mail from two different
                         echo areas from ending up in the same WILDCAT!
                         conference.

               [F10]     Highlighting the selected conference by using the
                         Up/Dn arrow keys and pressing this key will copy
                         both the WILDCAT! conference number and
                         description into the conference definition you're
                         currently editing.

                         You may edit any of this information after
                         pressing [F10] but you should note that changes
                         made to the conference name/number will NOT affect
                         the actual WILDCAT! databases.  This information
                         is only presented as a master list of WILDCAT!
                         conferences from which to choose from.

               [ENTER]   Pressing this key on the highlighted conference
                         displays the conferences configuration as read
                         from your systems configuration files.  This can
                         be useful for checking Mail Type and various other
                         conference specific settings without having to go
                         into MAKEWILD.




          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                       Page  104



          WILDMAIL! v3.01                        CONFERENCE AREA MANAGEMENT
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

                         The information displayed here is taken directly
                         from CONFDESC.DAT file (located in the WILDCAT!
                         home directory) and is used as a simple reference
                         when configuring conference areas within WMCONFIG.
                         The screen displayed is the current conference
                         configuration as defined through the use of
                         MAKEWILD.

                         Checking certain configuration information like
                         Mail Type and whether or not Message Attachments
                         are allowed are the most common applications, but
                         also the number of messages allowed, directory
                         information, various flag settings and so on. 
                         Since this information is considered reference
                         only, no modification is allowed.

                         Once you're finished viewing the screen, pressing
                         [ESC] returns you to the WILDCAT! conference
                         selection pick list.


          Origin address:

               Because WILDMAIL! allows you to carry message conferences
               from different networks on your system, there needs to be a
               method by which you can define an origin address for each
               conference on your system.  This address will be appended to
               the bottom of all the new messages created on your system
               that get sent out into the network.

               Normally you are assigned a unique node address for each
               network you're in, so you should use this option to specify
               your node address for the network this conference is in. 
               For example, if your network address for MagNet is
               100:910/13 and this conference (the one you're editing) is
               from MagNet, you would use the address of 100:910/13 as your
               Origin address.

               Pressing [ENTER] on this option presents you with a list of
               predefined AKA Addresses you entered via the Main Menu
               option System Information.  Using the Up/Dn arrow keys, you
               can select which address you want to be used for this
               conferences origin address.

               If the desired address doesn't appear in this window, you
               must return to the Main Menu, select System Information,
               option AKA Addresses and enter in the desired network
               address.  Then you may return here and select/use the new



          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                       Page  105



          WILDMAIL! v3.01                        CONFERENCE AREA MANAGEMENT
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

               AKA Address.


          Origin line:

               This option is used to select which Origin line is to be
               used with this conference.  Pressing [ENTER] on this option
               will present you with a list to choose from.  Simply use the
               Up/Dn arrow keys to highlight the desired Origin line and
               press [ENTER] to accept it.

               You may have any Origin line associated with any number of
               conferences or a unique one for each conference, but they
               must be previously defined before one can be selected.  In
               other words, you must use the Main Menu option, Origin Line
               Maintenance to create an Origin line(s) before you can tell
               WILDMAIL! to use one for this conference.


          Originating node:

               This field is used to tell WILDMAIL! whether or not your
               system is the Uplink/Feed address for this conference. 
               Setting this value to Y means your system is the originating
               point for all mail within the network this conference is in
               and mail is simply forwarded to your downlink node(s).  

               With this option toggled to Y, the Uplink/Feed Address is
               dimmed (protected) and you will not be able to define an
               address here.  With this option toggled to N, you will then
               have access to the Uplink/Feed address option.


          Uplink/Feed Address:

               This field is used to specify the <zone:net/node.point>
               address of the system that you will be getting the mail for
               this conference from.

               When receiving mail for a specific network, the Uplink
               address you normally get this mail from may not be capable
               of carrying all of the conferences you would like to carry
               on your system.  Because of this, you may need to pickup
               mail from several different addresses for the individual
               conferences you desire.

               The address specified here becomes very important when you
               let WILDMAIL! automatically activate and deactivate



          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                       Page  106



          WILDMAIL! v3.01                        CONFERENCE AREA MANAGEMENT
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

               conferences for your downlink node addresses.  The reasoning
               here is simple.

               Lets say you pick up mail from 3 different Uplink addresses
               for the same network.  One of your downlink nodes requests a
               new conference via a specially configured Netmail message
               that you don't carry on your system.  WILDMAIL! needs to
               know which of those three Uplink addresses (that you get
               your mail from) that it should send a AreaRequest message
               to. 

               If there wasn't a mechanism to define a specific uplink
               address, the AreaRequest message would get sent to your
               primary Uplink address (possibly the wrong one) and the
               automatic area activation wouldn't always work reliably.  So
               specifying the address here ensures the AreaRequest message
               gets sent to the correct Uplink address.

               Pressing [ENTER] on this option allows you to select from
               the list of previously defined node addresses that will be
               your feed for this conference.


          Extract private mail:

               This option is used to specify whether or not PRIVATE
               messages entered on your system are to be extracted and
               forwarded on into the network.

               If you select N, any messages entered into this conference
               and flagged as PRIVATE (by the individual entering the
               message) will NOT be extracted and thus will never leave
               your system.  Caution should be exercised here for obvious
               reasons.

               Please note, some networks do NOT permit PRIVATE echomail
               messages, so you should be careful when selecting which
               conferences in which network(s) allow such a option.  If you
               have any questions, you should contact the node you're
               picking up mail from and ask them.


          Active area:

               This is a handy little option that allows you to temporarily
               disable a conference by removing it from WILDMAIL!'s "view".
               This means that WILDMAIL! will not attempt to scan mail out
               or toss mail into this conference with this option set to N.



          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                       Page  107



          WILDMAIL! v3.01                        CONFERENCE AREA MANAGEMENT
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

               This is useful if you wish to disable the conference without
               completely deleting it from your configuration.  Then, at a
               later time, you can simply set this option back to Y and
               WILDMAIL! will process it along with all the other active
               areas.

               When WILDMAIL! encounters a message that is destined for
               this conference, but an inactive status is detected, the
               mail will be tossed into the BADECHO directory just as if
               the conference didn't exist on your system.  Mail will not
               be forwarded to any of the downlink node addresses that were
               attached to this conference either.

               Any mail tossed into the BADECHO directory (from an inactive
               conference) can easily be tossed into its corresponding
               conference by simply reactivating it by setting the status
               back to active and re-running WILDMAIL! with the TOSS
               option.


          Restrict import:

               Setting this option to Y instructs WILDMAIL! to check the
               From: node address of the PKT file the mail came from prior
               to tossing mail into this conference to ensure the node
               address has been previously defined on your system.

               In very rare cases this is necessary to prevent mail from
               being accidently introduced into your systems message bases
               from an address that is not specified as a downlink or
               Uplink address for this conference.  This could happen if a
               misconfigured system accidently sends mail to your address
               for conferences that you happen to carry. 

               Since this causes additional overhead when tossing the mail,
               (decreased performance because of the additional checking)
               this option is normally set to N and is provided primarily
               as a troubleshooting mechanism and not a normal setting.


          Extract file attaches:

               With this option toggled to Y, when WILDMAIL! performs a
               scan of this conference and encounters an attached file, it
               will automatically extract it and create a Netmail message
               with the attached file to all the downlink nodes assigned to
               this conference.  




          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                       Page  108



          WILDMAIL! v3.01                        CONFERENCE AREA MANAGEMENT
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

               The extracted file will be placed in a separate directory
               defined from the Main Menu, System Information, BBS Specific
               Option, File attach path.  It should be noted, the file
               attachments are NOT sent out with the echomail, but rather
               via a Netmail message.

               Because this option depends on whether or not this
               conference within WILDCAT! has been configured to allow
               message attachments, you can easily check this setting
               within WMCONFIG!.  

               Simply return to the WILDCAT! conference option setting (a
               few fields above this option), make note of the current
               conference number and press [F2].  Then select the
               appropriate conference number from the list presented and
               press [ENTER].  For here a screen full of information about
               the conference definition (taken direction from WILDCAT!) is
               displayed.  In the bottom box, top left hand corner displays
               the "Allow message attachments" option setting. 

               Once you are finished viewing the information, pressing
               [ESC] twice will return you to the main screen and you can
               then resume your configuration settings.

               NOTE:     If you enable this option, you should use the -A
                         command line parameter when executing WILDMAIL!. 
                         This is used to cleanup the \WM30\ATTACH directory
                         of all files that have already been transmitted to
                         their downlink nodes.


          AreaRequest security:

               WILDMAIL! now fully supports conference activation and
               deactivation via specially formatted Netmail messages.  In
               order to use this, each conference must be assigned a
               security access level and, if necessary, any additional sub-
               levels of access via the AreaRequest Flags option.  This
               value (and corresponding flags) are used to match up the
               requesting nodes security level to that of the conference
               they are trying to activate.

               If their security level is equal to or greater than this
               conferences security level and any corresponding flags
               match, they may activate/de-activate it (if so desired).

               A bit of forethought should go into using this feature.  You
               might want to try and categorize the conference "types" on



          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                       Page  109



          WILDMAIL! v3.01                        CONFERENCE AREA MANAGEMENT
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

               your system so you can easily establish what security level
               this conference should be.

               So, let's say you're carrying adult echos with a security
               level set to 200, in order for a node picking up mail from
               you to have the ability to activate/de-activate them, their
               security level must be equal to or greater than the level of
               the conference desired.











































          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                       Page  110



          WILDMAIL! v3.01                        CONFERENCE AREA MANAGEMENT
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

               For example:

                    Conf  Conference Description       Sec Level
                    ÄÄÄÄ  ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ  ÄÄÄÄÄÄÄÄÄ
                     10   Adult Fantasies                 200
                     11   Adult Parties                   200
                     12   Adult Romances                  200
                     20   General Messages                100
                     21   Technical Support               150

               In the above list of conferences, if a node was assigned a
               Area Request security level of 100, they would only have the
               ability to activate/de-activate conference 20.  Let's say
               another node has been defined with a security level of 150,
               it would only have access to conferences 20 and 21 but not
               conferences 10, 11 and 12.

               For a node to have access to conferences 10, 11 and 12, they
               must have a security level of 200 or greater in order to
               activate/de-activate them.

               However, there is a limitation to this options capability
               within WILDCAT!.  Conferences can be activated/de-activated
               by downstream nodes, but a new conference can not be
               automatically created within WILDCAT!, this must be done
               manually by using MAKEWILD.

               The reasoning behind this is two-fold.  First of all, the
               entire WILDCAT! system must be brought down to make
               configuration changes and secondly, there would have to be
               some sort of method to automatically place it somewhere on
               the system disk and then allow users access to this new
               conference.  Since this just doesn't exist, there is no way
               to automatically create conferences within WILDCAT! at this
               time.

               Please don't confuse an AreaRequest for a conference with
               trying to create a brand new conference within WILDCAT!.


          AreaRequest flags:

               This works in conjunction with the AreaRequest Security
               level and is used as a secondary level security system to
               further narrow down the node addresses who have access to a
               specific conference.

               Typically, you would only use this option if you have adult



          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                       Page  111



          WILDMAIL! v3.01                        CONFERENCE AREA MANAGEMENT
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

               conferences on your system (or similar security need) and
               you wish to limit only those systems with under-age SysOps
               from gaining access to those conferences.  Otherwise, these
               adult conferences would be available to all SysOps over the
               age of 18 that pick up mail from your system.

               While the AreaRequest Security level offers security based
               upon "<=" (less than or equal to) a given security level,
               setting an additional flag here requires that the requesting
               system pass two tests now.

                    1)   Must pass AreaRequest Security level requirements.

                    2)   The node address must have at least the same
                         flag(s) toggled here for the selected conferences
                         in his/her corresponding database record.

               Since these flags are based upon conferences, you should
               review how you've previously defined your restricted
               conferences to know what flags should be given to each node
               address.

               The bottom line here is simple, if a requesting node passes
               the AreaRequest requirements and requests a conference with
               flags attached to it, their node specific AreaRequest flags
               must also match that conferences flags.  Otherwise the node
               will be unable to activate the conference.

               The node may actually have more flags than what's defined
               for the requested conference, but never less than.  Please
               keep in mind that the node must have at least the same flags
               that the requested conference requires.  For additional
               information please refer to the Main Menu, Conference Area
               Management option AreaRequest flags.


          SEEN-BY: line processing:

               This option is used to control the processing of the SEEN-
               BY: lines in each message added to this conference.  These
               SEEN-BY: lines are used by the various tossers to indicate
               what node address(es) have received this message.  This
               information is used to properly forward mail, thereby
               preventing duplicate messages from being sent to a node
               address that has already received it.  For additional
               information regarding SEEN-BY: lines, refer to Appendix G.

               Presently, there are three methods of processing the SEEN-



          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                       Page  112



          WILDMAIL! v3.01                        CONFERENCE AREA MANAGEMENT
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

               BY: lines in the messages.  Each option can be toggled by
               pressing the [SPACEBAR].  Shown below is a description of
               the available options.

               Hidden    When selected, this instructs WILDMAIL to keep the
                         SEEN-BY: lines completely intact and adds a ^A
                         (Control A) character in front of them to
                         effectively hide them from view.  The SEEN-BY:
                         lines can often times occupy more space than the
                         actual message, but are necessary if your downlink
                         nodes ever request conference rescans.  They're
                         also necessary to track down certain duplication
                         problems or even lack of mail getting delivered.
                         Hidden is the recommended setting.

               Display   This option is exactly the same as Hidden with the
                         difference being that no ^A (Control A) character
                         is added to the beginning of the SEEN-BY: lines. 
                         This means when reading this conferences message
                         base, all the SEEN-BY: line, PATH: line
                         information and AREA: definitions will be
                         displayed along with the rest of the message body.

               Delete    This setting tells WILDMAIL! to remove/delete all
                         SEEN-BY: line information before adding the
                         message to database.  THIS IS A DANGEROUS SETTING
                         because if you ever do a rescan of this conference
                         for your downlink nodes, these will be treated
                         exactly the same as brand new messages and WILL
                         CAUSE A SERIOUS DUPLICATION OF MESSAGES IN THE
                         NETWORK!  On that same note, if you NEVER do a
                         rescan and fully understand this option (effect)
                         then you can save on some disk space by using this
                         setting.

               Because of the dangerous nature of the Delete option, it is
               strongly discouraged unless you absolutely and completely
               understand what you're doing.

               The Display option is commonly used when troubleshooting a
               duplication loop problem and can become a irritant to your
               callers if you leave it set this way.  Plain and simple, it
               clutters up the messages with unnecessary information (from
               the callers perspective).

               Therefore the recommended setting here is Hidden.





          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                       Page  113



          WILDMAIL! v3.01                        CONFERENCE AREA MANAGEMENT
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

          Add to SEEN-BYs:

               Outside of the Origin Address specified for this conference,
               this option is used to select which additional address(es)
               you wish to have WILDMAIL! add to the existing SEEN-BY:
               lines of the messages leaving this conference.

               NOTE:     This option is rarely ever used.  Only in cases
                         where duplicates are being introduced into a
                         network should this option be considered.  And
                         then only for as long as it takes to find the
                         source of the problem.

               It should be pointed out that the address you've defined as
               the Origin Address for this conference is not available for
               selection.  This is because WILDMAIL! automatically adds
               this addresses <net/node> information to the messages
               processed from this conference.

               Only the actual <net/node> portion of the selected address
               will be added to the SEENBY lines because <zone> information
               is not stored in these lines.

               Highlighting the desired address and tapping the [SPACEBAR]
               will select the address as indicated by the (é) selection
               dot.

               The list of available addresses displayed is actually your
               AKA addresses, so if the address you wish to be added to
               this conferences SEEN-BY: lines doesn't exist, you'll need
               to return to the Main Menu option, System Information and
               update your AKA addresses before proceeding.

               At times this option is necessary in preventing one of your
               downstream nodes from sending the mail you just sent him/her
               back to your system as duplicates.  This can happen when
               your downstream node(s) are using one of your AKA addresses
               and not your primary address for this network.

               The primary solution to this problem is of course to have
               them forward mail back to you using your primary address
               (for this network).  But since this may not always be
               possible, you could simply add your AKA address (that the
               offending node is using) to the SEEN-BY: lines and prevent
               the mail from coming back to your system.






          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                       Page  114



          WILDMAIL! v3.01                               AREAREQUEST MANAGER
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

          AREAREQUEST MANAGER

          This feature is used to allow automatic activation and
          deactivation of conferences by your downlink nodes without any
          need for intervention on your part.  This is extremely useful
          because it frees you up from having to manually add/delete these
          conference requests.

          If your system carries sensitive conferences, for example adult
          related material you don't want anyone under 18 access to, or you
          would just like to restrict the automation of certain
          conferences, WILDMAIL! allows you to specify 2 different levels
          of security accesses to satisfy these needs.  These access levels
          are described below.


          SECURITY LEVELS

          Security levels are exactly what the name implies, levels.  This
          is used with both conferences and node addresses to form a
          mechanism by which a node must meet a certain requirement before
          it can obtain the desired conference(s).  

          Basically it works like this.  A node address may have access to
          any conference on your system that has a security level assigned
          to it EQUAL TO or LESS THAN its assigned security level.  If the
          value of the requesting nodes security level is LESS THAN the
          desired conference, WILDMAIL! will disallow the request. 

          So let's say you're carrying adult echos with a security level
          set to 200, in order for a node picking up mail from you to them,
          their security level must be equal to or greater than the level
          of the conference desired.  For example:

                    Conf  Conference Description       Sec Level
                    ÄÄÄÄ  ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ  ÄÄÄÄÄÄÄÄÄ
                     10   Adult Fantasies                 200
                     11   Adult Parties                   200
                     12   Adult Romances                  200
                     20   General Messages                100
                     21   Technical Support               150

          In the above list of conferences, if a node was assigned a
          AreaRequest security level of 100, they would only have the
          ability to activate/de-activate conference 20.  Let's say another
          node has been defined with a security level of 150, it would only
          have access to conferences 20 and 21 but not conferences 10, 11
          and 12.  For a node to have access to conferences 10, 11 and 12,



          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                       Page  115



          WILDMAIL! v3.01                               AREAREQUEST MANAGER
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

          they must have a security level of 200 or greater in order to
          activate/de-activate them.  

          The individual AreaRequest security levels are defined for each
          node and conference via the Main Menu options, Node Address
          Management or Conference Area Management after selecting the
          desired node/conference.

          While the security level approach works well in most situations,
          it offers somewhat limited protection of certain conferences that
          you would like to restrict on a more complex level.  This is
          where you can combine the security level approach with the
          individual AreaRequest Flags.


          AREAREQUEST FLAGS

          AreaRequest flags are commonly used as a secondary level security
          protection mechanism coupled with the value of the assigned
          Security Level which is designed to limit node address access to
          the various different conferences carried on/through your system. 
          If a flag is assigned to a conference, the requesting node must
          also have that flag before it can gain access to it.

          It should be pointed out that all flags created are on a equal
          basis whereby no one flag has a higher priority level than
          another.  These are simple flag toggles that can be assigned to a
          conference and then its respective downlink nodes who are to have
          access to that conference.

          Please bear in mind flags are a secondary level protection
          mechanism so if a requesting node desires a specific conference
          and his AreaRequest security level permits him access and no
          flags are attached to the conference requested, that system may
          gain access to it.

          Now if this same node sends a request for a conference where his
          normal AreaRequest security level is sufficient and a Conference
          AreaRequest flag is attached to the conference his system is
          requesting, his node address must also have this same Node
          AreaRequest flag in order to gain access to that conference. 

          So combining the AreaRequest Security level and the AreaRequest
          flags together provides two levels of security that a system must
          pass before gaining access to that conference.






          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                       Page  116



          WILDMAIL! v3.01                               AREAREQUEST MANAGER
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

          AREAREQUEST OPTION ACTIVATION

          AreaRequest Manager uses specially formatted Netmail messages
          when making changes to the Nodes and Conferences databases.  This
          section covers the available parameters and their formatting
          requirements when creating Netmail messages.

          Because these options are used by your downlink nodes, the
          information presented here will be viewed from the downlinks
          perspective.  In other words, its the commands that they will be
          using when utilizing the AreaRequest Managers features.

          Since AreaRequest Manager is a fully secure system, the
          requesting node must pass all the required security measures
          before the request can be processed.  If the node does not pass
          the required security measures, a special Netmail message is sent
          back to them informing them of the problem.


          TO: Name

               Presently AreaRequest supports up to 5 different names that
               the Netmail message can be addressed to.  The most common
               name to use would be AREAFIX, but can be any other names as
               configured.  The spelling on this must be EXACT in order for
               WILDMAIL! to process these requests.


          FROM: Name

               This field is normally your name.  There are no special
               requirements here.


          SUBJECT line: 

               This is one of the most crucial fields because here is where
               you define your password and any necessary parameters to
               activate the various options.  The most important part here
               is that the password MUST BE THE FIRST WORD ON THE LINE. 
               All the remaining parameters must be separated by a space
               and any combination may be used together.

               Shown below is a description of the available parameters
               that are used on the SUBJECT line of the Netmail messages.

               -Q   This option can be thought of as a query command to ask
                    WILDMAIL! what conferences your system is getting.



          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                       Page  117



          WILDMAIL! v3.01                               AREAREQUEST MANAGER
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

                              Example Usage: PASSWORD -Q

                    WILDMAIL! (the host system) will then send you a
                    complete list of all the conferences your currently
                    receiving.


               -L   This option is used when you are interested in
                    obtaining a list of all the available conferences the
                    host system is carrying.

                              Example Usage: PASSWORD -L

                    The host system will then send a Netmail message back
                    to you with a file attachment containing all the
                    conferences the host is carrying.  You may not have
                    access to all these conferences depending on how the
                    list is compiled so you should always refer to the host
                    system for specifics.


               -R   This parameter is used when you wish to rescan a
                    specific conference or group of conferences.  

                              Example Usage: PASSWORD -R

                    This option is a bit different than the previous
                    options in that it also uses information contained
                    within the body of the Netmail message.  This
                    information is the actual conference AREA name that a
                    rescan is to be performed on.

                    Each AREA name must be the only word on the line.  When
                    the host system (WILDMAIL!) receives this type of
                    request, the ENTIRE contents of the requested
                    conference will be rescanned for the node and then
                    packed up and attached to a Netmail message.














          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                       Page  118



          WILDMAIL! v3.01                               AREAREQUEST MANAGER
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

          MESSAGE BODY

          The message body portion of the Netmail message can be used for 2
          different purposes.  The activation/deactivation of conferences
          and for specifying which conferences are to be rescanned when
          using the -R parameter.  


          TEAR LINE

          As was previously described, a special group of characters called
          a Tear line should be placed at the end of the Netmail message to
          signal WILDMAIL! that it has reached the end of the message and
          to ignore any remaining text.  This Tear line consists of three
          dashes (---) together starting on column 1 of a blank line. 
          Although the Tear line is not required, it should be there as a
          matter of course.

          Shown below are the two different cases of message body usage
          (assuming all the security checks have been successfully passed).


          AREA Activation/De-activation

               By specifying the AREA name of the conference (one per line
               only), you may activate it by either of 2 methods as shown
               below:
                         Example Usage: +WILDCAT
                                           or
                                         WILDCAT

               Notice here that you may include the + character in front of
               the AREA name if desired.  It's not a requirement, but is
               used either with or without the plus sign.  As was
               previously mentioned, only one AREA name may be specified
               per line of the message.

               Now, to de-activate the conference, you would use:

                         Example Usage: -WILDCAT

               This is exactly the same as with the activation option only
               now you MUST specify the - (minus) character in front of the
               area to be deactivated.


          Rescanning Conferences




          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                       Page  119



          WILDMAIL! v3.01                               AREAREQUEST MANAGER
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

               This option requires that you have a -R on the subject line
               of the Netmail message (following the password) and then the
               body of the message contains the actual AREA names you wish
               to have rescanned.  

                         Example Usage: WILDCAT
                                        WCTECH
                                        FOR_SALE

               Again, each AREA name must be on its own line.  In future
               releases, look to see the ability to specify the number of
               messages to be rescanned.







































          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                       Page  120



          WILDMAIL! v3.01                               AREAREQUEST MANAGER
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

          AREAREQUEST CONFIGURATION OPTIONS

          In order for the AreaRequest option to perform properly, it must
          be configured to the unique requirements of your system.  All DOS
          path definitions are checked immediately after specifying them. 
          Shown below are the options to use when customizing it for your
          needs.


          Process AreaRequest Msgs:

               This option dictates whether WILDMAIL! will act upon receipt
               of specially formatted Netmail message(s) that arrive on
               your system.  

               Toggling this option to N will instruct WILDMAIL! to ignore
               these specially formatted Netmail messages and it will also
               prohibit any access to the remainder of the fields on this
               screen.

               With this field set to Y, all the remaining fields on the
               screen will be made available for your configuration
               requirements and instruct WILDMAIL! to process those
               specially formatted Netmail messages.


          Area Manager aliases:

               When automatic requests for conference activation and/or
               deactivation are received, WILDMAIL! needs to know what name
               to look for in the FROM: field of the Netmail message.

               This option allows you to specify up to a total of five (5)
               different names, 3 of which are added automatically.  These
               first 3 names can be deleted if necessary and are only
               provided because they are the most commonly used names.

                              AREAFIX   AUTOAREA  AREAMGR


               Add an Alias Name

                    Pressing [INSERT] allows you to enter up to 5 names up
                    to 35 characters in length which will be used to match
                    names found in the requesting Netmail message FROM:
                    field.  The exact spelling of this name is critical
                    before WILDMAIL! will acknowledge AreaRequests in
                    Netmail form.



          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                       Page  121



          WILDMAIL! v3.01                               AREAREQUEST MANAGER
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

                    Since three names are initially added, it's rare that
                    you would have to add another name, but is provided
                    here if a new program is developed that allows
                    conference area activation and/or deactivation via
                    Netmail messages.

                    Upon entering in the new name, pressing [ENTER] will
                    accept the name and return you to the main list of
                    names.  If you attempt to add more, WMCONFIG! will
                    simply ignore the keypress.


               Delete an Alias Name

                    After selecting the desired name definition by using
                    the Up/Dn arrow keys, pressing the [DELETE] key brings
                    up a friendly message confirming your request to
                    delete.  If you're sure you want to delete this, simply
                    press Y, otherwise [ESC] aborts and returns you to the
                    previous screen.


               Edit an Alias Name

                    After selecting the desired name definition by using
                    the Up/Dn arrow keys, pressing the [ENTER] key brings
                    up this name in edit mode.

                    By using the cursor LEFT/RIGHT keys you can position
                    the cursor to the desired location and add or delete
                    characters as needed.  Pressing the [INSERT] key
                    toggles the automatic insert mode and entering a ^Y
                    (Control Y) clears the entire line.

                    Once changes or additions are completed, pressing [F10]
                    will save them and return you to the previous screen
                    containing the list of Alias names.


          Purge areas:

               Setting this option to Y instructs WILDMAIL! to
               automatically remove a conference area definition from its
               areas database should the last remaining downlink node
               address turn off this conference.  If this option is set to
               Y, WILDMAIL! will then send a message to your Uplink Address
               (for this network) requesting a termination of this
               conference.



          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                       Page  122



          WILDMAIL! v3.01                               AREAREQUEST MANAGER
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

               This option is useful in maintaining conferences on your
               system to ensure that at least one node address is always
               receiving the available conferences.  This prevents your
               system from carrying conferences that no one is using.

               With this option set to N, WILDMAIL! will leave the
               conference definition in your areas database intact and your
               system will continue to receive this conference even if none
               of your downlink node addresses are receiving it.

               Please note, if you set this option to N, you may end up
               receiving mail that no one is using, so it doesn't make a
               lot of sense to pay for mail to "throw away".


          ALT-V  View File

          The following three path and file name specifications allow you
          to use a special function to display the contents of the
          highlighted file.  

          With the cursor positioned on the file path, you can press and
          hold down the [ALT] key followed by tapping the V character and
          display the contents of the specified file.  If the specified
          file doesn't exist, this option is simply ignored.

          You may scroll around the file by using the PgUp/PgDn, Up/Dn and
          Left/Right arrow keys.  Once you're finished viewing the file,
          you may press the [ESC] key and you'll be returned to the
          previous screen.


          Purge file:

               The complete <drive:\directory> and <filename> specified
               here works together with the Purge Areas option to maintain
               a log file of all areas that have been automatically turned
               off by WILDMAIL!.

               A typical path and filename definition might be:

                              C:\WM30\WMAMGR.DEL

               Normal DOS conventions are strictly adhered to when defining
               this filename and path.






          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                       Page  123



          WILDMAIL! v3.01                               AREAREQUEST MANAGER
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

          Master Conference List:

               This field is used to define the <drive:\directory> and
               <filename> of the ASCII text file that contains a complete
               list of all the conferences your downlink nodes can gain
               access to from your system.

               This is typically a complete list for each of the various
               networks you may be participating in.  In other words, this
               is a collection of all the Forward Lists your system uses to
               ensure a echo area is real before requesting it from your
               Uplink Hub address.

               This file is normally requested by your downlink nodes via
               the command line parameter -L (following the password on the
               SUBJECT: line of the request message).  Your downlink nodes
               can then use this list to "shop" for which conference they'd
               like to pick up from you.

               A typical path and filename definition might be:

                              C:\WM30\MASTER.LST

               Normal DOS path and naming conventions are strictly adhered
               to in this definition.


               SPECIAL TIP:

               WMUTIL! has a handy feature that will automatically create
               the above file for you by using all the defined Forward
               Lists respective Echo List files.  This process will combine
               these echo list files and properly format and properly
               paginate the file for easy viewing.  This is useful for
               automatically updating this Master Conference List file when
               a new echo list file is obtained.  

               For additional information on using this feature of WMUTIL!,
               please refer to the WMUTIL.DOC file supplied in the
               distribution archives of WILDMAIL! v3.01. 











          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                       Page  124



          WILDMAIL! v3.01                               AREAREQUEST MANAGER
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

          Area Manager Logfile:

               This option is used to define the <drive:\directory> and
               <filename> of the log file where all activity regarding
               conference activation and deactivation is to be kept.  A
               typical path statement would be:

                              C:\WM30\WMAMGR.LOG

               Normal DOS conventions are required when defining the log
               file name.


          Allow area rescan:

               This option is used if you wish your downlink node addresses
               to be able to use the -R command line parameter (following
               the password on the SUBJECT: line of the request message) to
               perform an automatic rescan of the selected areas.

               By setting this option to Y, WILDMAIL! will reset the high
               water mark for the selected conferences back to 0 and
               extract the entire contents of the selected conference areas
               and make it available for the requesting node address.

               If any of the selected conference areas are "passthru's", no
               messages will be extracted due to the fact that there isn't
               a corresponding database of messages in which they can be
               processed from.

               Discretion must be used with this option because depending
               on how large your systems message bases are allowed to get,
               the requesting node address could end up getting quite a
               bundle!

               CAUTION!

                    If you are using the DELETE option for processing of
                    SEEN-BY: lines, first off DON'T! and second, you SHOULD
                    NOT allow the rescan option!

                    This is due to the fact that the messages on your
                    system no longer carry any SEEN-BY: line information,
                    so when they are extracted as part of a rescan, they
                    will be reintroduced into the network the same as if
                    they were BRAND NEW MESSAGES and will cause a serious
                    duplication loop!  Network coordinators are NOT too
                    fond of this.  Caution is advised!



          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                       Page  125



          WILDMAIL! v3.01                               AREAREQUEST MANAGER
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

                    The bottom line here is simple, if you HUB mail for
                    downlink nodes, you MUST use either the DISPLAY or
                    HIDDEN options for SEEN-BY: line processing.  With
                    either of these two selected, this rescan option will
                    perform properly with little fear of causing
                    duplication loops.


          Allow area query:

               This option is used if you wish your downlink node addresses
               to be able to use the -Q command line parameter (following
               the password on the SUBJECT: line of the request message).

               With this option set to Y, this instructs WILDMAIL! to
               produce a message containing a list of all the available
               echo areas along with a list showing the conferences the
               requesting node address is currently receiving.

               Often times this is useful for the downlink node(s) to
               verify the conferences they're currently receiving from your
               system. Toggling this option to N, will cause WILDMAIL! to
               ignore any requests for active conference listings.


          Show feeds:

               As part of the follow up message to a nodes request, setting
               this option to Y will cause WILDMAIL! to automatically add a
               list of the active conferences to the confirmation message
               that the requesting node is receiving.


          Kill processed messages:

               With this option set to Y, WILDMAIL! will delete area
               request messages after it has processed them.

               If this option is set to N, WILDMAIL! will not delete
               processed area request messages so they will remain in your
               Netmail directory.  With this setting, these old (already
               processed) area request messages can quickly pile up in your
               Netmail directory so caution is advised.


          Notify with Echo List:

               WILDMAIL! has the ability to automatically generate Netmail



          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                       Page  126



          WILDMAIL! v3.01                               AREAREQUEST MANAGER
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

               messages to your downlink node addresses containing a list
               of all the conferences they are currently receiving from
               your system.

               The option here is used to tell WILDMAIL! whether or not it
               should attach the Master Conference List previously defined
               for all the different networks (and their associated
               conferences) which are available to them from your system.

               Setting this option to Y instructs WILDMAIL! to
               automatically attach a copy of this Master Conference List
               file to the generated messages for your downlink (and
               uplink) node addresses.  When your front end mailer sends
               them this message, they will also receive this attached
               file.

               With this option set to N, only the Netmail message about
               the active conferences they are receiving from your system
               will be sent to them.


          Notify exclude:

               WILDMAIL! has the ability to automatically generate Netmail
               messages to your downlink node addresses containing a list
               of all the conferences they're currently receiving from your
               system.

               This option allows you to specify which of your downlink
               node addresses you want to exclude when WILDMAIL! generates
               this information.

               Pressing [ENTER] presents a list of previously defined node
               addresses that are sending/receiving mail with your system. 
               After highlighting the desired address by using the Up/Dn
               arrow keys, tapping the [SPACEBAR] will tag the address as
               being selected indicated by a (é) selection dot.  Tapping
               the [SPACEBAR] a second time will deselect the node address.

               Up to 10 addresses may be tagged.  The next time WILDMAIL!
               is executed, it will automatically exclude these node
               addresses from getting the conference information.

               It should be noted that if the address you wish to exclude
               is not in the list presented, you will not be able to add a
               node address here.  You must return to the Main Menu
               selection, Node Address Management and add it there first
               and then return to tag it accordingly.



          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                       Page  127



          WILDMAIL! v3.01                               AREAREQUEST MANAGER
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ


          AreaRequest Mgr flags:

               AreaRequest flags are used as a secondary level security
               protection mechanism designed to limit which node address
               has access to the various different conferences carried
               on/through your system.

               If you used WMINSTAL! to upgrade with and you previously
               used AreaFix, your old flag names were automatically
               imported with a name similar to:

                              Original Flag = X 

               This means your old flag name was called X, but you should
               probably change the imported name from "Original Flag = X"
               to something a bit more descriptive.  This will be helpful
               later on in the configuration process and easier for you to
               remember what it was used for in the future.

               Pressing [ENTER] brings up another screen allowing you to
               create up to 16 individual flags using any names you desire
               up to 25 characters in length.  You may call them anything
               you wish and should describe what its used for.  You might
               even consider using part of the network name that this flag
               is associated with and its "requirement level" as the flag
               name to better categorize them.


               Add a New Flag

                    Pressing [INSERT] pops up a window allowing you to
                    create a new AreaRequest Flag.  The LEFT/RIGHT arrow
                    keys and [BACKSPACE] keys are active for any editing
                    changes.

                    Up to 25 characters may be entered.  Pressing [ESCAPE]
                    aborts any changes made while pressing [ENTER] saves
                    the information.


               Delete a Flag

                    After selecting the desired flag definition by using
                    the Up/Dn arrow keys, pressing the [DELETE] key brings
                    up a friendly message asking if you are sure you want
                    to delete this.  Answering Y will remove the flag from
                    the list and then scan both the conferences and nodes



          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                       Page  128



          WILDMAIL! v3.01                               AREAREQUEST MANAGER
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

                    databases removing any occurrence(s) found of that
                    flag.

                    Pressing [ESC] or answering N to the confirmation
                    request simply aborts and returns you to the list of
                    available flags.


               Edit a Flag

                    Using this option allows you to edit the flag name
                    displayed. By using the cursor LEFT/RIGHT keys you can
                    position the cursor to the desired location and add or
                    delete characters as needed.

                    Pressing the [INSERT] key toggles the automatic insert
                    mode and entering a [CTRL-Y] clears the entire line.


               It should be pointed out that all flags created are on a
               equal basis whereby no one flag has a higher priority level
               than another.  These are simple flag toggles that are
               initially assigned to a conference (if desired) and then its
               respective downlink nodes that are to have access to the
               selected conference.


          Forward Lists:

               A Forward list is a collection of parameters associated with
               a specific network allowing WILDMAIL! to verify the validity
               of a requested conference and then send the appropriate
               AreaRequest message to the defined Uplink or Hub address
               that specifically carries the requested conference.

               Additional information contained within these Forward lists
               is the AKA you wish to use, password, any associated
               AreaRequest flags etc.  You also have the ability to specify
               node addresses who should receive any conferences requested
               (by your downlink nodes) automatically upon activation.  A
               total of 20 different Forward lists may be defined.  Shown
               below is a breakdown of the available options.


               Create a New List

                    Pressing the [INSERT] key allows you to add a new file
                    name.  As was earlier stated, up to 20 lists may be



          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                       Page  129



          WILDMAIL! v3.01                               AREAREQUEST MANAGER
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

                    added.  If you attempt to add more, WMCONFIG! will
                    simply ignore the keypress.


               Delete a List

                    After selecting the desired name definition by using
                    the Up/Dn arrow keys, pressing the [DELETE] key brings
                    up a friendly message asking if you are sure you want
                    to delete this. 

                    Answering Y removes the forward list and returns you to
                    the remaining lists.  Pressing either [ESC] or N aborts
                    the deletion and redisplays the lists.


               Edit a List

                    After selecting the desired name definition by using
                    the UP/DN arrow keys, pressing this key brings up this
                    lists specifications in edit mode.


               Forward List Definitions

               As was mentioned earlier, Forward lists are a collection of
               parameters used to associate a group of conferences, where
               to get them and so on for a specific network.  Shown below
               is a description of each of these parameters required when
               defining each Forward list.


               Echo List:

                    This option allows you to specify the actual
                    <drive:\directory> and <filename> of the ASCII based
                    text file which contains a list of conferences specific
                    to its network.

                    For example, within Fidonet there is a file called
                    FIDONET.NA that is a complete list of all the available
                    conferences.  For this option, you would specify this
                    file name along with its complete DOS path.  A typical
                    definition might be:

                                   C:\FD\FIDONET.NA

                    Most networks provide an ASCII text file that contains



          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                       Page  130



          WILDMAIL! v3.01                               AREAREQUEST MANAGER
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

                    a list of available conferences within that network. 
                    This file is commonly formatted similar to:

                    WILDCAT        Support conference for WILDCAT! BBS's
                       :                :        :         :
                    TECH_SUPPORT   Technical support conference

                    The first column indicates the echomail AREA name and
                    the second column describes the conference topic or
                    theme.  WILDMAIL! will use these lists to confirm the
                    existence of a requested conference before sending a
                    message to the specified Uplink Address requesting it.

                    Standard DOS path and file naming conventions are
                    strictly adhered to.


                    ALT-V  View File

                    With the cursor positioned on the echo file path, you
                    can press and hold down the [ALT] key followed by
                    tapping the V character and display the contents of the
                    specified file.  If the specified file doesn't exist,
                    this option is simply ignored.

                    You may scroll around the file by using the PgUp/PgDn,
                    Up/Dn and Left/Right arrow keys.  Once you're finished
                    viewing the file, you may press the [ESC] key and
                    you'll be returned to the previous screen.


               Originating Node:

                    This field is used to specify whether or not your
                    system is the originating node for the conferences
                    defined in the Echo list.  

                    Setting this option to Y protects the Hub Node: option
                    and causes WILDMAIL! to process requests entirely
                    different than normal.  So, if a request for a
                    conference (in the Echo list) is not carried on your
                    system, WILDMAIL! will leave a message to the SysOp
                    indicating the requested conference which was not found
                    in your Conferences database.

                    This is done intentionally for those people that gate
                    conferences from one network format to another such as
                    QWK to FTSC.  Because your Uplink address would be



          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                       Page  131



          WILDMAIL! v3.01                               AREAREQUEST MANAGER
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

                    unable to process the AreaRequest message (if they were
                    a QWK system), a message is left on your system
                    informing the SysOp of the request.  The SysOp must
                    then manually activate that conference from their
                    Uplink address through whatever means necessary.

                    If you're not gating between network formats, then the
                    message is still generated and you can take the
                    necessary action to follow up the request.

                    Setting this option to N indicates you're not the feed
                    and makes the Hub Node: option available.  This is the
                    normal setting.


               Uplink Address:

                    This is the address where WILDMAIL! will go to request
                    conferences found in the associated conference (area)
                    list.  In other words, when WILDMAIL! is given a
                    shopping list (of conferences) from one of your
                    downlink node addresses, it needs to know what store
                    (hub address) to go in which to get them from.

                    Pressing [ENTER] on this field brings up a list of node
                    addresses that have been previously defined.  If the
                    node address you're looking for does not exist here,
                    you will need to return to the Main Menu option Node
                    Management and create this address before proceeding.


               Password:

                    This option is used to specify a password up to 8
                    characters long associated with obtaining conference
                    areas from the specified hub address.

                    You should verify that the specified hub address has
                    your system configured to use the exact same password. 
                    This allows a degree of security preventing
                    unauthorized requests from being made.


               From AKA:

                    When requesting new conferences, WILDMAIL! will send
                    the appropriate Netmail message to the defined hub
                    address.  This option is used to specify which of your



          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                       Page  132



          WILDMAIL! v3.01                               AREAREQUEST MANAGER
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

                    node addresses this message should be addressed from.

                    Since this is one of your AKA addresses, pressing
                    [ENTER] on this field displays a list of available
                    AKA's.  If the address you wish to use is not displayed
                    here, you will need to return to the Main Menu option,
                    System Information, select AKA's and enter in the
                    appropriate address before continuing.

                    To select the address, simply position the highlight
                    bar over the desired AKA and press [ENTER].


               AreaRequest Flags:

                    This option is used to specify a default set of flags
                    that would be required before a requested conference
                    maybe activated.  In other words, if a flag is assigned
                    to the entire forward list, then the requesting node
                    must also have that flag before they can activate any
                    conferences from that forward list.

                    Pressing [ENTER] on this field pops up a list of
                    previously defined AreaRequest flags.  Positioning the
                    highlight bar on the desired flag by using the
                    PgUp/PgDn keys followed by pressing the [SPACEBAR]
                    selects the desired flag.  Pressing [F10] saves the
                    settings and returns you to the previous screen.


               Add Nodes:

                    This option allows you to specify a list of node
                    addresses you want to have automatically added to the
                    Forward-To list for any conferences requested from this
                    hub address.

                    Selecting the desired node is accomplished by
                    positioning the highlight bar over the desired address
                    and pressing the [SPACEBAR].  Selection is indicated by
                    the (é) dot character next to the node address.  To de-
                    select a node, simply press the [SPACEBAR] a second
                    time.

                    For example, lets say you have 3 addresses that are
                    within the same network and all pick up the same
                    conferences.  Anytime a new conference gets added to
                    your system from this forward list, the selected nodes



          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                       Page  133



          WILDMAIL! v3.01                               AREAREQUEST MANAGER
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

                    (defined here) will be automatically added to the list
                    of nodes receiving this conference.

                    This is handy when nodes wish to be auto-activated when
                    a new conference comes out.














































          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                       Page  134



          WILDMAIL! v3.01                          WHAT ARE POINT ADDRESSES
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

          WHAT ARE POINT ADDRESSES?

          Points are BBS systems that send and receive mail in a specific
          network but can only be addressed through the node address they
          transfer mail with.  In other words, if you address mail to a
          <point> it doesn't go directly to their system but rather to the
          system they pickup their mail from.

          To be considered a full node (not a point) typically requires
          that their BBS must be up and running 24 hours/day especially for
          mail delivery during what's called Zone Mail Hour.  Because
          certain BBS's were not always operational 24 hours/day, there
          needed to be a way to make echomail available to them.  This is
          where points came into being.

          A common comparison would be a <point> is to a node address what
          a caller using QWK mail and an offline reader is to a regular
          BBS.  Mail is transferred on a regular basis, but only when the
          caller uploads his/her QWK mail REP packet.  Thus the caller can
          only be addressed through the system they upload their replies to
          and not directly.

          The problem was how to address them as a <point>.  Only 3D
          addressing was available at the time and there were hundreds of
          systems using this 3D addressing scheme.  Couple that with the
          original design limitations of the mail packets and mailer
          software and it made it difficult to implement a satisfactory
          change.  To solve this problem, a specially translated addressing
          scheme was devised.

          This required those systems to call a node address who was always
          available and pick up their mail using their specially translated
          address.  In the remaining portion of this section, we'll discuss
          the terminology and the "how and whys" of the implementation.


          BOSS NODE

          BOSS node is the name given to the node address that has point
          addresses attached to their system which it feeds mail to. 
          Whenever mail is addressed to a <point>, the BOSS node is where
          the mail actually gets sent to and then the <point> picks it up
          from them (the BOSS node).








          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                       Page  135



          WILDMAIL! v3.01                          WHAT ARE POINT ADDRESSES
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

          ADDRESSING SCHEMES

          Within the realm of Fidonet style mail, there are two distinctive
          methods of addressing called

                              3D   or   Three dimensional
                              4D   or   Four dimensional

          The term dimensional refers to the number of segments in the node
          address where:

               3D uses:  <zone:net/node>          or   1:161/123
               4D uses:  <zone:net/node.point>    or   1:161/123.1

          Notice that 4D uses an additional parameter at the end of the
          address indicated by the '.1'.  This is called the <point> and
          where the 4D address gets its 4th dimension.


          POINT DESCRIPTIONS

          Because of the difference between the two methods of point
          addressing, the following section discusses the unique
          characteristics of each of them.


          3D POINT ADDRESSES

          This section on translated addressing is a little confusing, so
          you might have to reread this a couple of times to get a good
          grasp of it, so hang in there.  As was mentioned above, the BOSS
          node is where the <point> addresses go to get their mail from, in
          this case where those systems who weren't available 24 hours/day
          would go to pick up their mail.

          From a fundamental level, 3D addressing dictates that <node>
          addresses get their mail from a their HUB address.  A collection
          of HUB's usually form a network or the <net> portion of the
          addressing scheme.  And then of course a collection of networks
          is called a <zone>.  

          So for those systems that weren't available 24 hours/day, they
          could use the <zone> number from the BOSS nodes address, use a
          "fake" <net> address created by the BOSS node and then the <node>
          portion of the 3D addressing scheme (1st point, 2nd point etc) to
          form a complete 3D <zone:net/node> address.  Consequently, this
          is where the term FakeNet address came from.  After all this was
          a fake address!  Here's how it works.



          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                       Page  136



          WILDMAIL! v3.01                          WHAT ARE POINT ADDRESSES
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

          FAKENET ADDRESS

          A special 5 digit value less than 65535 which is assigned by the
          ZC (Zone Coordinator) in Fidonet, otherwise created out of thin
          air by the BOSS node makes up the <net> portion of the address. 
          Each system would have a unique <node> number usually starting
          from 1 and incrementing for each additional point.  The address
          assigned to the point would be something like:

                                   32000/1

          Where 32000 was the fakenet <net> number and 1 was the <node>
          address.  So if the BOSS nodes <zone> was 1, the entire 3D
          address would now be:

                              1:32000/1      (1st point)
                              1:32000/2      (2nd point)
                              1:32000/3      (3rd point) etc..

          As you can see, this isn't too difficult to understand, the new
          node address would be assigned to the node and used when calling
          the BOSS node to transfer mail back and forth between their
          systems.  

          Now the BOSS node would have to create a special file called a
          pointnet nodelist that contained all of these specially created
          addresses so their mail processor would forward mail to them
          properly.  The pointnet nodelist then had to be merged with the
          BOSS nodes primary nodelist in order for these fake addresses to
          be usable.

          Because these fakenet addresses were unique to the BOSS node they
          simply could not be part of the normal addresses found in the
          primary nodelist (thats the one that gets distributed worldwide).


          DESIGN CHANGE

          As you can see, the 3D method is both cumbersome and awkward to
          say the least.  In order to overcome this special addressing, a
          design change was in order which required a structure change in
          not only the way mail was transferred from one system to another,
          but in the way the addressing information within the mail packets
          (PKT files) was stored.  Because of the magnitude of systems
          already in use, backwards compatibility was a must!






          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                       Page  137



          WILDMAIL! v3.01                          WHAT ARE POINT ADDRESSES
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ


          So a new mail packet type was created and was called an enhanced
          TYPE 2 packet (TYPE 2.2). It now uses the old 3D format for
          compatibility and simply appends the <point> information to the
          end of it.  This not only removes the requirement of the FakeNet
          method, but also adds in a few other options/features we won't go
          into here.


          4D ADDRESSING

          With this new mail packet type, node addressing now uses the full
          4 dimensional <zone:net/node.point> information.  No longer was
          any translation process required and the associated headaches of
          creating FakeNet ID's and so on was also removed.  Unfortunately,
          pointlists (special nodelist of points) are still required by the
          BOSS node and the point, but at least addressing the points was a
          bit more efficient now.

          In order for systems to make use of this new format, they MUST be
          configured to use a TYPE 2.2 mail packet.  Remember, the mail
          packet type (PKT file) is the format that WILDMAIL! will create
          their outbound mail in.




























          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                       Page  138



          WILDMAIL! v3.01                    USING 3D ADDRESSING FOR POINTS
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

          POINT CONFIGURATIONS

          WILDMAIL! fully supports both 3D and 4D points attached to a
          specific node address in any combination of networks desired.  So
          if you have 10 different zones (networks) on your system, you
          could have 10 different point "nets".  This is due to the fact
          that points are attached to a specific node address and since
          different node addresses for your system can be assigned through
          the use of AKA's, it's very easy to create a new AKA for your
          points to use as their BOSS node.

          Currently there are two distinctly different methods of point
          configurations.  These two methods are driven entirely upon the
          mail packet TYPE configured in the Node Management section of
          WMCONFIG!.  Below are the two mail types.

                         3D point uses a TYPE 2 
                         4D point uses a TYPE 2.2

          The following sections attempt to break out the configuration
          requirements within WMCONFIG! plus any additional requirements
          for proper implementation.


          USING 3D ADDRESSING FOR POINTS 

          Shown below is a description on how to configure points using 3D
          addressing formats from the BOSS node and point perspectives.


          IF YOU'RE A BOSS NODE

          If you'll be setting up your system to have points off of one of
          your AKA addresses and they must use the 3D format, then you will
          need to pick an arbitrary FakeNet ID number ranging from 1 to
          65530.  For clarity sake, you should probably use a 5 digit
          number (although it's not important).  Then, from the Node
          Management screen you should:

               1)   Specify the entire node address using a complete
                    <zone:net/node.point> address.

               2)   Active Node setting should be set to Y.

               3)   Mail Type should be set to TYPE 2.
           
               4)   Enter in the 5 digit FakeNet address (the one you
                    previously picked) in the FakeNet ID field.



          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                       Page  139



          WILDMAIL! v3.01                    USING 3D ADDRESSING FOR POINTS
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

               5)   Configure the remaining node information normally.  

          WILDMAIL! will now translate the <zone:net/node.point> address
          using the FakeNet ID number and create a new 3D address.  For
          example, if the FakeNet ID selected was 32000 and the <point>
          portion of the <zone:net/node.point> (see step 1) address was 1,
          then the translated point address would be <zone>:32000/1.

          You should now tell your point what your address is for the
          selected network (this is needed on their end to define the BOSS
          node address) along with the FakeNet address and point number you
          assigned earlier.  In the previous example, this would be the
          address of <zone>:32000/1 as their primary address when calling
          your system (where <zone> would be your zone address).

          As part of the requirements of being a BOSS node, you will now
          need to create a POINTLIST of all the addresses that will be
          points off of your system.  This will need to be compiled with
          your front end mailers main nodelist for proper mail transfers. 
          Please refer to the appropriate section of your mailers
          documentation for specifics on incorporating pointlists into the
          primary nodelist.


          IF YOU'RE A 3D POINT

          Probably one of the first things you should do is review what the
          requirements are for a BOSS node because several things are
          required from the BOSS node to become a point off of his/her
          system.  Pay particular attention to the FakeNet ID number and
          the point number.  The combination of these two form your
          address.

          Now, from the System Information Screen within WMCONFIG!, you
          should:

               1)   Specify your PRIMARY ADDRESS as the combination of the
                    BOSS nodes <zone>, FakeNet ID and your <point> number
                    off of their system.  So if your BOSS nodes address was
                    1:161/123 and the FakeNet ID was 32000 and you're the
                    3rd point off of their system, your address would be
                    1:32000/3.

               2)   As part of your AKA Addresses, you must enter in your
                    4D point address.  So in the above example, you would
                    use your BOSS nodes address of 1:161/123 and since
                    you're the third node off of their system, your 4D
                    address would be 1:161/123.3.  Enter that as a AKA



          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                       Page  140



          WILDMAIL! v3.01                    USING 3D ADDRESSING FOR POINTS
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

                    address.


          From the Node Address Management Screen, you should:

               1)   Create a Node Address of your BOSS nodes 3D address.

               2)   Set Active Node to Y.

               3)   Set Mail Type to TYPE 2.

               4)   FakeNet ID number should NOT be entered!.  Leave that
                    at the default value of 0.

               5)   Set the remaining options for their address
                    accordingly.


          From the Conference Area Management Screen you should set up ALL
          the conferences you get from your BOSS node as follows:

               1)   Set Active Area to Y.

               2)   Set the Origin Address to your FakeNet address (in the
                    above example it would be 1:32000/3).

               3)   Set the Uplink/Feed Address to your BOSS nodes 3D
                    address.

               4)   Set the remaining options for their address
                    accordingly.


          As you can see, the translated method is quite a bit confusing
          and certainly not the method of choice.  If you can steer clear
          of this, do so and use the 4D point method instead!















          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                       Page  141



          WILDMAIL! v3.01                    USING 4D ADDRESSING FOR POINTS
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

          USING 4D ADDRESSING FOR POINTS

          This section defines how to configure your system as either a
          BOSS node or as point using 4D addressing.  This is by far the
          simplest method and the easiest to understand.  So if you have a
          choice, always select this method!


          IF YOU'RE A BOSS NODE

          This is very simple.  From the Node Management Screen simply:

               1)   Define each point that will be picking up mail from you
                    using their 4D address in <zone:net/node.point> format. 
                    So if your address is 1:161/123, then your:

                              First point    1:161/123.1
                              Second point   1:161/123.2  <etc>


               2)   Set Active Node to Y.

               3)   Set Mail Type to TYPE 2.2.

               4)   Set the remaining options for each node accordingly.


          As part of the requirements of being a BOSS node, you will now
          need to create a POINTLIST of all the addresses that will be
          points off of your system.  This will need to be compiled with
          your front end mailers main nodelist for proper mail transfers. 
          Please refer to the appropriate section in your mailers
          documentation for specifics on incorporating pointlists in with
          your primary nodelist.


          IF YOU'RE A 4D POINT

          From the System Information Screen your should:

               1)   You should define your Primary Address as your BOSS
                    nodes address plus your point number.  So if your BOSS
                    nodes address was 1:161/123 and you're the third point
                    off of their system, then your address would be
                    1:161/123.3.

               2)   AKA addresses need not be specified unless you have
                    another address for a different network.  In other



          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                       Page  142



          WILDMAIL! v3.01                    USING 4D ADDRESSING FOR POINTS
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

                    words, no special definition is required.


          From the Node Address Management Screen you should:

               1)   Define your BOSS nodes address.

               2)   Set Active Node to Y.

               3)   Set Mail Type to TYPE 2.2.

               4)   Set the remaining options accordingly.


          From the Conference Management Screen you should define all the
          conferences you'll be getting from your BOSS node as follows:

               1)   Set Active Area to Y.

               2)   Set the Origin Address to your <zone:net/node.point>
                    address.  (In the previous example this would be
                    1:161/123.3)

               3)   Uplink/Feed address should be set to your BOSS nodes
                    address.

               4)   Set the remaining options accordingly.


          As you can see, setting up points in 4D format is very simple to
          do and a lot easier than the 3D translation method.




















          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                       Page  143



          WILDMAIL! v3.01                                   TROUBLESHOOTING
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

          TROUBLESHOOTING

          This section will try an address the most common problems
          encountered when running WILDMAIL!.  Because of the diversity of
          configurations, it's difficult to be precise, but we'll attempt
          to cover as much as possible.


          COMMON QUESTIONS/PROBLEMS

          Question:      I am unable to update any information within
                         WMCONFIG!, why?

          Answer:        When WMCONFIG! is first executed, it comes up in
                         Protected Mode.  This prevents you from accidently
                         changing anything.  If you wish to make changes,
                         you must press [F8] to toggle into Edit Mode.


          Question:      I can not position the cursor to the desired
                         field, it just skips over it, why?

          Answer:        Depending on previous options settings, certain
                         fields may become "protected".  This indicates the
                         field is no longer needed in the current
                         configuration.  Because this is affected by other
                         settings, you should press [F1] for additional
                         help information on the options presented to
                         determine why the field is not needed.


          Question:      I get an Unable to open Users Database. Status =
                         9903 error when accessing the Crash Users list,
                         why?

          Answer:        The Home directory/path under the WILDCAT!
                         specific options doesn't contain the necessary
                         WILDCAT! configuration files for WMCONFIG! to find
                         the users database.  Make sure this path correctly
                         points to the WILDCAT! home directory.


          Question:      I get a "CONFDESC.DAT Not Found" message when
                         pressing [F2] on the WILDCAT! conference option in
                         Conference Management.  Why?

          Answer:        The path defined for the WILDCAT! Home directory
                         path option in WILDCAT! specific option doesn't



          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                       Page  144



          WILDMAIL! v3.01                                   TROUBLESHOOTING
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

                         correctly point to the WILDCAT! home directory. 
                         Consequently, WMCONFIG! can't pull up the
                         conference information from WILDCAT!.  Change this
                         setting to reflect the correct directory and the
                         error will go away.


          Question:      You encounter a message stating "Error closing
                         Areas database - 10445" when running WMCONFIG!.

          Answer:        This can occur when WILDMAIL! is already running
                         and you attempt to run WMCONFIG!.  You may not run
                         WMCONFIG! while WILDMAIL! is running.


          Question:      I am unable to delete the Origin line with the
                         asterisk enclosed in parentheses, why?

          Answer:        This is considered the default Origin line and
                         WMCONFIG! forces you to always have one.  If you
                         want to change the default (or even delete it) you
                         will need to create a new one first, make that one
                         the default and then go back and delete the old
                         one.


          Question:      I have a node address defined in the Nodes
                         database with selected conferences but WILDMAIL!
                         doesn't create any outbound mail for it, why?

          Answer:        Check the status flag for that node.  If it's
                         toggled to N, then WILDMAIL! will not forward mail
                         to it because it's considered inactive.


          Question:      When WILDMAIL! tosses mail, certain messages end
                         up in the BADECHO directory, why?

          Answer:        There are several reasons why this can happen. 
                         First off, if the area name found in the message
                         doesn't match up to any of the conference areas
                         defined in the Areas Database, WILDMAIL! will
                         place it here.  Secondly, if you've enabled SEENBY
                         line checking and certain information is incorrect
                         or missing, WILDMAIL! will copy them here for your
                         review.

                         If the area name wasn't found in the database, you



          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                       Page  145



          WILDMAIL! v3.01                                   TROUBLESHOOTING
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

                         can always add it as a new area and the next you
                         execute WILDMAIL! with the TOSS parameter, it will
                         toss those "bad messages" into its corresponding
                         conference preventing mail from being lost.

          Question:      I enter a new message into a conference and the
                         next time I run WILDMAIL! with the scan option,
                         the message isn't extracted.  Why?

          Answer:        Within each conference database file, there is a
                         reserved portion that contains information like
                         the low and high message numbers, the total number
                         of messages.  In addition, there is field that
                         contains the number of the message that was last
                         extracted by WILDMAIL!.  For some reason, this
                         number is higher than the highest message number
                         in the conference, consequently, WILDMAIL! won't
                         extract it.  

                         This is easily resolved by executing WILDMAIL!
                         with the -T command line parameter along with the
                         necessary conference number, last extract value
                         etc.  For specifics, refer to the section on
                         command line parameters.


          Question:      Echomail messages seem to toss and extract
                         properly, but Netmail messages only appear in my
                         FrontDoor/InterMail Netmail directory, why?

          Answer:        If FrontDoor or InterMail is not executed with the
                         command line parameter -NOUNPACK, then it will
                         intercept the Netmail messages and toss them. 
                         Once they're tossed there's no way for WILDMAIL!
                         to know they even existed.  To prevent this from
                         happening, make sure you execute FD or IM with a
                         minimum of the following command line:

                                        FD -NOUNPACK
                                             or
                                        IM -NOUNPACK

                         You may have additional parameters, but you must
                         place the -NOUNPACK parameter if you want the
                         received Netmail messages to go into WILDCAT!.


          Question:      When I attempt to enter a message into the Netmail



          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                       Page  146



          WILDMAIL! v3.01                                   TROUBLESHOOTING
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

                         conference I receive the message:

                           "Netmail services are currently unavailable"

                         Why?

          Answer:        When you configure a conference within MAKEWILD
                         and use the mail type of NETMAIL, when a message
                         is entered into that conference WILDCAT! attempts
                         to use specially created files for looking up the
                         network address of the person you wish to send the
                         message to.  If these files can't be found, the
                         message is displayed.

                         You need to get a copy of the nodelist compiler
                         for WILDCAT! called WILDNODE.  This file is
                         available for download from the WILDMAIL! support
                         BBS and is free.  Simply follow the installation
                         instructions for the program and you'll be set.


          Question:      Because information is stored in the WILDCAT!
                         message bases regarding High, Low and Last
                         Extracted message numbers, what happens if I run a
                         WCRENUM on the message base?

          Answer:        This question can be answered two ways depending
                         on the version of WCRENUM you're running.

                         Pre v3.60 of WILDCAT!

                         If you haven't upgraded to at least v3.60 of
                         WILDCAT!, after renumbering the message base, you
                         must reset the last extract count via the -T
                         command line parameter.  Or you could use our fast
                         and simple RESETWC program to do this for you. 
                         Resetting the last extract value is a REQUIREMENT
                         otherwise newly entered messages will not be
                         extracted.


                         v3.60 or later of WILDCAT!

                         Nothing special needs to be done.  The version of
                         WCRENUM that came with WILDCAT! v3.60 or greater
                         correctly updates this last extract value
                         requiring no intervention on your part.




          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                       Page  147



          WILDMAIL! v3.01                                   TROUBLESHOOTING
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

          Question:      I'm getting reports from nodes I transfer mail
                         with that messages originating from my system have
                         the Origin line truncated.  Why?

          Answer:        If you've recently used the [F4] Global change
                         option in WMCONFIG! to replace origin lines or
                         have modified an existing Origin line in the
                         Origin line database (and let WMCONFIG!
                         automatically update the conferences that used
                         it), chances are the one you selected/modified for
                         the conference in question exceeded the allowable
                         78 character limitation.  If that was the case,
                         then WMCONFIG! will truncate the Origin
                         information enough to add in the Origin address
                         and its required parentheses.  To resolve this,
                         you should go back to the failing conference(s)
                         and reselect a new Origin line, or edit the
                         existing one and reduce its length.


          Question:      When WILDMAIL! is busy tossing mail on my WILDCAT!
                         system, every once in a while, it displays the
                         message:

                              "Unable to add message - Database full"

                         It then deletes the message and carries on
                         processing.  Why?

          Answer:        On WILDCAT! systems, each conferences database has
                         a numerical limitation on the maximum message
                         number allowed.  To be specific, 65,535.  This
                         should not be confused with the actual number of
                         messages in the database.  

                         To resolve this, you should look at the contents
                         of your WM.LOG file and see what conference number
                         this happened on.  From there you should run
                         WCRENUM on that conference and WILDMAIL! will now
                         toss messages into it properly.


          Question:      When running WMCONFIG! or WMUTIL! I get an error
                         message stating the databases are in use. 
                         WILDMAIL! is not running and no other program is
                         accessing the WILDMAIL! databases.  Why?

          Answer:        For some reason the databases have been left in



          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                       Page  148



          WILDMAIL! v3.01                                   TROUBLESHOOTING
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

                         use.  To clear this, you should execute WMUTIL!
                         with the /I parameter from the WILDMAIL! directory
                         and it will reset the inuse flag.

                         If WILDMAIL! is in use and you use this setting,
                         unpredictable results can occur and you run the
                         risk of corrupting information in the databases.


          Question:      Whenever I execute WILDMAIL!, all my mail is
                         processed normally, but the netmail messages get
                         tossed into the BADECHO directory.  Why?

          Answer:        If you don't execute WILDMAIL! with either the
                         MAILIN or NETMAIL command line parameters, when a
                         Netmail message is found, it needs to be placed
                         somewhere, so it's put into the BADECHO directory
                         until the MAILIN or NETMAIL command line
                         parameters are used.


          Question:      All mail both in and out of my system is running
                         fine, but for some reason AreaRequest is not
                         processing any of the AreaFix style messages, why?

          Answer:        First off, for AreaRequest to operate, you must
                         have previously enabled the option in WMCONFIG!. 
                         Secondly, you should make sure that you are using
                         the AREAMGR command line parameter when executing
                         WILDMAIL! as this invokes that function. Finally,
                         WILDMAIL! will only process those messages that do
                         not have the RECEIVED flag set.  Make sure the
                         messages have not been received and try again.


          Question:      My Uplink address is complaining that the <zone>
                         number is missing from the packet header when
                         their system receives it.  In other words, my
                         address of 1:161/123 is received as 161/123. 
                         Because of this, his system informs him of a
                         security violation.  Why?

          Answer:        Because WILDMAIL! supports multiple PKT formats,
                         you should make sure you are sending mail to their
                         system using the TYPE 2.2 format.  TYPE 2 PKTs do
                         not support the <zone> information, but are
                         provided as a method of remaining compatible with
                         some of the older mail processors in use today. 



          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                       Page  149



          WILDMAIL! v3.01                                   TROUBLESHOOTING
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

                         This information is contained in the Node
                         Management section, for the selected node under
                         Mail Type.


          LOGGING INFORMATION

          Depending on how you've defined the level of logging via the
          System Information, Log file options setting dictates the amount
          of information WILDMAIL! will place into the log file it
          generates.

          Whenever you encounter any problems, you should always view the
          contents of this file because this will typically indicate the
          error as WILDMAIL! saw it stating specific information about the
          problem and often times can give you a method to resolve it as
          well.  The higher level of logging, the more likely you'll
          understand the problem.


          WILDCAT! ERROR.LOG FILE

          Because WILDMAIL! tosses directly into the WILDCAT! message
          bases, it must observe the rules of the configuration
          requirements of WILDCAT!.  If there is a problem within WILDCAT!,
          WILDMAIL! may too experience the same problem.

          Any time you encounter a problem in WILDMAIL!, you should make a
          habit of checking the ERROR.LOG file found in the WILDCAT! home
          directory and see if any information has been logged there. 
          Together with that file and the WILDMAIL! log file, you should be
          able to put together a reason for the programs acting the way
          they did.  Then you can resolve the problem with a bit more
          insight than just a trial and error method of fixing things.

















          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                       Page  150



          WILDMAIL! v3.01              LICENSING AND DISTRIBUTION AGREEMENT
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

          LICENSING AND DISTRIBUTION AGREEMENT

          Copyright (C) 1991, 1993 by Online Computer Resources.  ALL
          RIGHTS RESERVED.  COMMERCIAL DISTRIBUTION AND/OR USE PROHIBITED
          WITHOUT WRITTEN PERMISSION FROM Online Computer Resources.


          Non-Commercial distribution and/or use is permitted under the
          following terms:

               1)   You may copy and distribute copies of WILDMAIL!
                    executable code as you receive it, in any medium,
                    provided that you do so in a lawful, friendly manner
                    and that you conspicuously and appropriately publish on
                    each copy of each file that is a part of the
                    distribution package a valid copyright notice:

                    "Copyright (C) 1991, 1993 by Online Computer Resources. 
                    Any copies that you distribute must be distributed free
                    of charge to the recipient of the copy.  WILDMAIL! may
                    not be sold and you may not rent or lease it to any
                    other person."

               2)   You must keep this License Agreement intact and give
                    any other recipients of the WILDMAIL! program a copy of
                    this License Agreement along with the program.

               3)   You must distribute WILDMAIL! in unmodified form.  You
                    may not add an advertisement for your Bulletin Board
                    System, User Group, or anything else either as a file
                    in the distribution packet or as a header in any
                    archive.  You may not add, modify or delete any of the
                    files in the WILDMAIL! distribution archive.

               4)   WILDMAIL! must be distributed for free. You may not
                    charge a distribution fee for the physical act of
                    transferring a copy of this program.  You may not place
                    this program in any file area of a Bulletin Board
                    System where a fee is required for download.

               5)   You may not modify your copy or copies of WILDMAIL! or
                    any portion of it and you can not copy and distribute
                    any modifications.  WILDMAIL! is distributed in ZIP
                    format and you may not distribute it in any other form.







          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                       Page  151



          WILDMAIL! v3.01              LICENSING AND DISTRIBUTION AGREEMENT
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

               6)   You may not copy, sublicense, distribute or transfer
                    WILDMAIL! except as expressly provided under this
                    License Agreement.  Any attempt otherwise to copy,
                    sublicense, distribute or transfer WILDMAIL! is void
                    and your rights to use the program under this License
                    agreement shall be automatically terminated.

               7)   You may not incorporate parts of WILDMAIL! into other
                    programs without the written permission of Online
                    Computer Resources. Permission may or may not be
                    granted based upon a determination of what your
                    intended use is.

               8)   For the purposes of this document, "COMMERCIAL USE" is
                    defined as concurrent operation of the software on
                    three or more computers or data lines owned by the same
                    for-profit organization.  Any organization may operate
                    this software under the terms of this Non-Commercial
                    Agreement if operation is limited to two or less
                    computers or data lines.

               9)   You may use the software only after understanding and
                    agreeing upon the above terms.




























          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                       Page  152



          WILDMAIL! v3.01              LICENSING AND DISTRIBUTION AGREEMENT
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

          NO WARRANTY

          WILDMAIL! v3.00 IS DISTRIBUTED AS AN EVALUATION COPY ONLY!  THIS
          PROGRAM REQUIRES THE USE OF A SPECIAL 30 EVALUATION KEY
          OBTAINABLE FROM THE WILDMAIL! SUPPORT BBS AT (707) 552-0602.  IF,
          AT THE END OF THE 30 DAY PERIOD, YOU HAVE NOT REGISTERED THE
          PRODUCT, WILDMAIL! WILL SIMPLY CEASE TO RUN.  REACTIVATION
          REQUIRES THE PLACEMENT OF THE REGISTERED KEY FILE IN THE
          WILDMAIL! DIRECTORY.  

          THIS PROGRAM IS GUARANTEED TO DO ABSOLUTELY NOTHING EXCEPT TAKE
          UP DISK SPACE.  USE IT AT YOUR OWN RISK.  NEITHER ONLINE COMPUTER
          RESOURCES NOR ANY OTHER PERSON INVOLVED IN ITS DISTRIBUTION IS
          RESPONSIBLE IN ANY WAY, FOR ANY DAMAGES RESULTING FROM ITS USE OR
          MISUSE, DIRECTLY OR INDIRECTLY.

          THE ENTIRE RISK AS TO THE QUALITY AND PERFORMANCE OF WILDMAIL! IS
          ENTIRELY WITH YOU.  SHOULD WILDMAIL! PROVE DEFECTIVE, YOU ASSUME
          THE COST OF ALL NECESSARY SERVICING, REPAIR OR OTHER DAMAGES TO
          YOUR EQUIPMENT, SOFTWARE, OR OTHER PROPERTY.

          ONLINE COMPUTER RESOURCES IS NOT RESPONSIBLE TO YOU FOR DAMAGES,
          INCLUDING BUT NOT LIMITED TO, ANY LOST PROFITS, LOST MONIES, OR
          OTHER SPECIAL, GENERAL, INCIDENTAL OR CONSEQUENTIAL DAMAGES
          ARISING OUT OF THE USE OR INABILITY TO USE (INCLUDING BUT NOT
          LIMITED TO LOSS OF DATA OR DATA BEING RENDERED INACCURATE OR
          LOSSES SUSTAINED BY THIRD PARTIES OR A FAILURE OF THE PROGRAM TO
          OPERATE WITH ANY OTHER PROGRAMS) OR ANY OTHER LOSS EVEN IF YOU
          HAVE BEEN ADVISED OF THE POSSIBILITY OF SUCH DAMAGES, OR FOR ANY
          CLAIM BY ANY OTHER PARTY.





















          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                       Page  153



          WILDMAIL! v3.01              LICENSING AND DISTRIBUTION AGREEMENT
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

          TECHNICAL SUPPORT

          You may contact Online Computer Resources at 1:161/123 via
          netmail or by logging on to the BBS for technical support.  We
          can also be reached in the WILDCAT! conference on Fidonet.  

          Business hours are 9am-6pm Monday through Saturdays PST and our
          voice number is (707) 552-1122.


          30 DAY EVALUATION COPY

          WILDMAIL! v3.00 is a fully functional, full featured mail
          processor for WILDCAT! v3.xx.  This program is not disabled in
          any way but does require the use of a special 30 day evaluation
          key. This key is obtainable by dialing the WILDMAIL! support BBS
          at the number listed above.  

          This temporary key will allow WILDMAIL! to run for 30 DAYS
          without registration, after which, the program will simply cease
          to run.  This should be sufficient time to properly evaluate the
          program for fitness prior to its actual registration.  

          After you register the program, you will receive the WM.ID file
          and then by placing it in the \WM30 directory, it will reactivate
          the program for normal use.

























          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                       Page  154



          WILDMAIL! v3.01                          TECHNICAL SPECIFICATIONS
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

          TECHNICAL SPECIFICATIONS

          Because of the complex nature of tossing mail, this section has
          been devoted to the requirements and assumptions that WILDMAIL!
          v3.00 operates under.


          Memory Requirements

               WILDMAIL!'s requires approximately 400K of BASE 640K memory. 
               It also will use XMS or EMS memory if it's found.  For
               swapping into XMS/EMS, approximately 400K is required
               otherwise swapping will occur to disk. 

               For database accesses, only EMS memory can be used and
               WILDMAIL! uses up everything that it finds.  Caution must be
               exercised here because in a multitasking environment, this
               could be disastrous.  To eliminate this problem, in DESQview
               you should limit the amount of EMS the window that WILDMAIL!
               executes in.

               With WILDMAIL! v3.01, 43 and 50 line VGA modes are now
               supported allowing you to view more of the messages
               displayed in the System Messages window at the bottom of the
               screen.  While this is a handy feature, it does come at a
               price.

               Executing WILDMAIL! in 43/50 line VGA mode requires an
               additional 16K+ of memory to store the higher resolution
               screen in.   So if memory requirements on your system are
               tight, make sure you execute WILDMAIL! in standard 25 line
               mode.


          Conference Areas Supported

               Because the conference information is stored in a database,
               fundamentally there is no limit to the number of conferences
               WILDMAIL! can process.  The only limitation being the
               available disk space.

               There is however a limit on the number of conferences
               contained within WILDCAT! which is carefully observed.








          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                       Page  155



          WILDMAIL! v3.01                          TECHNICAL SPECIFICATIONS
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

          Node Addresses

               As with the conferences, fundamentally there is no limit to
               the number of node addresses that may be defined.  The only
               limiting factor is available disk space.


          Downlink Nodes per Conference

               WILDMAIL! supports up to 75 node addresses that may be
               attached to a specific conference.  This means that although
               you can easily have more than 75 nodes in the nodes
               database, only 75 may be attached to a single conference.


          Tossing Mail in Date/Time Order

               Mail bundles are tossed in date/time order, no matter what
               order they are received in, beginning with .SU0, .MO0, etc. 
               .PKT files are tossed in date/time order also.


          Large Messages

               Messages that exceed the maximum line limit defined in
               MAKEWILD for its respective conference are automatically
               split into smaller ones in order to maintain the integrity
               of the original message.
            
               In other words, if the incoming message contains 250 lines
               and the destination conference is set to 150, the first 146
               lines are added to the initial message in WILDCAT! along
               with a 4 line prompt indicating the split.  WILDMAIL! then
               creates a new message using the same TO:, FROM: and SUBJECT:
               information and inserts a 4 line prompt (indicating the
               message continuation) and then adds the remaining 104 lines. 

               WILDMAIL! will automatically add as many new messages as
               required to toss the original message into the WILDCAT!
               conference.  It should be noted that the split is only done
               with the mail going into your WILDCAT! message conferences. 
               Any messages (exceeding the conference length limit)
               forwarded to your downlink nodes will not be split and thus
               left completely intact.







          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                       Page  156



          WILDMAIL! v3.01                          TECHNICAL SPECIFICATIONS
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

          Message Size Limitation

               Presently WILDMAIL! only supports messages up to 10K in
               length.  While this is rarely a problem in the FTS world,
               this can be an important factor if you are picking up mail
               from a InterNet or UUCP feed.

               If you know which system is doing the gating of messages
               from the InterNet/UUCP, make sure they set their gating
               software to split the messages up at the 8K mark.  This will
               prevent WILDMAIL! from spending unnecessary time trying to
               locate the SEEN-BY: lines of the current message and
               possibly loosing some mail in the process.


          No Content/Null Messages

               A NO CONTENT message (null message) is defined as any
               message not having any text body.  WILDMAIL! creates these
               as Netmail messages used to transmit the outbound echomail
               archives.

               Some systems may not be able to support "null messages" that
               contain the INTL kludge line information in the body of the
               Netmail message, but WILDMAIL! generates fully compatible
               null Netmail messages.

          Maximum AKA Addresses . . . . . . . . . . . . . . . . . . . .  20
          Maximum Forward Lists . . . . . . . . . . . . . . . . . . . .  20
          Maximum Area Manager Aliases  . . . . . . . . . . . . . . . .   5
          Maximum AreaRequest Flags . . . . . . . . . . . . . . . . . .  16
          Maximum Zone Assignments  . . . . . . . . . . . . . . . . . .  20



















          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                       Page  157



          WILDMAIL! v3.01                            APPENDIX A - ARCA/ARCE
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

          APPENDIX A - PACKER/UNPACKER PARAMETERS

          The following is a reference section devoted to assisting you in
          deciding which command line parameters are necessary when
          defining your packer types.  It is recommended to always use the
          overwrite feature of the unpacker.  This prevents system hangs
          due to the prompt waiting to confirm an overwrite.


                                      ARCA v1.28
                            10/4/87.   ALL RIGHTS RESERVED
                  Copyright (c) Wayne Chin and Vernon Buerg  1986-87
                 ===================================================

                    Usage:    ARCA [d:][\path]ArchiveName[.ARC]
                                   [d:][\path]FileName[.Ext] [/D]

                    Use /D to delete files after adding to archive
                    Filenames may contain * and ? wildcards



                                      ARCE v3.1b
                  Extract ARC files  9/16/87.  ALL RIGHTS RESERVED.
                Copyright (c) 1986-87 by Wayne Chin & Vernon D. Buerg
                ======================================================

                    Usage:    ARCE d:path\filename.ext [filespecs..]
                                   [d:\outpath][/R][/P][/Q][/T] [/Gpswd]

                    d:  = drive and path are optional
                    ext = defaults to .ARC
                    /R  = specifies reuse existing files
                    /P  = extracts files to standard output
                    /Q  = suppresses beeps and bells
                    /T  = test archive integrity only
                    /G  = supplies encryption password, e.g. /Gpswd


               NOTE:     The /R parameter is highly recommended to
                         overwrite existing files in case WILDMAIL!
                         encounters tossing difficulties.  See above for
                         additional details.

                            System Enhancement Associates
                            21 New Street, Wayne NJ 07470





          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                       Page  158



          WILDMAIL! v3.01                         APPENDIX A - PKARC/PKXARC
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

                                      PKARC v3.5
                        Archive Create/Update Utility 04-27-87
               Copyright (c) 1986,1987 PKWARE Inc. All Rights Reserved.
               ========================================================

               Usage:    PKARC [-oct,-nct] options[g<passwrd>] archive
                               [filename...]

               Options are:
                          -a = add files to archive
                          -d = delete files from archive
                          -f = freshen files in archive
                          -m = move files to archive
                          -u = update files in archive
                          -v = verbose listing of archive
                          -l = display software license
                          -c = add/update file comments
                          -x = add archive comment
                    -oct,nct = old/new compatibility
                          -g = encrypt w/password
                          -c = compression,
                          -t = timestamping


                                     PKXARC v3.5
                        Archive Create/Update Utility 04-27-87
               Copyright (c) 1986,1987 PKWARE Inc. All Rights Reserved.
               ========================================================

               Usage:    PKXARC [options] archive [d:path\] [file...]

               Options are:
                         -r = replace existing files
                         -v = verbose listing of archive(s)
                         -c = extract file(s) to screen
                         -p = extract file(s) to printer
                         -t = test archive integrity
                         -l = display software license
                      -e,-x = extract file(s)
               -g<password> = extract garbled file w/password

          NOTE:     The -r parameter is highly recommended to overwrite
                    existing files in case WILDMAIL! encounters tossing
                    difficulties.  See above for additional details.

                                     PKWARE, Inc.
                                9025 N. Deerwood Drive
                                 Brown Dear, WI 53223



          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                       Page  159



          WILDMAIL! v3.01                                APPENDIX A - PKPAK
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

           
                                  PKPAK Version 3.61
                        Archive Create/Update Utility 08-02-88
              Copyright (c) 1986-1988 PKWARE Inc.  All Rights Reserved.
              =========================================================

               Usage:    PKPAK [-b[path]] [-o,-n] options[g<passwrd>]
          archive
                               [@list] [files...]
               <Options>
                         -a = add files to archive
                         -b = create tmp archive on alternate drive
                         -c = add/update file comments
                         -d = delete files from archive
                         -f = freshen files in archive
                         -g = encrypt with password
                         -i = add changed files to archive
                         -l = display software license
                         -u = update files to archive
                         -x = add archive comment

                   -v[m][c] = verbose listing of archive [with more]
                              [with file comments]
                  -m[a,f,u] = move [with add/freshen/update] files to
          archive
                  -o[c][t],
                  -n[c][t]  = old/new compatibility,
                              [compression][timestamping]























          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                       Page  160



          WILDMAIL! v3.01                              APPENDIX A - PKUNPAK
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ


                                 PKUNPAK Version 3.61
                        Archive Create/Update Utility 08-02-88
              Copyright (c) 1986-1988 PKWARE Inc.  All Rights Reserved.
              =========================================================

               Usage:    PKUNPAK [options] archive [d:path\] [file...]

               <option>
                      -c[m] = extract to screen [with more]
                      -e,-x = extract file(s) (default)
               -g<password> = decrypt with password
                         -l = display software license
                         -n = extract only newer files
                    -p[a,b] = extract file(s) to printer [ascii mode,
                              binary mode]
                         -r = replace existing files
                         -t = test archive integrity
                      -v[v] = verbose list of archive(s) [made by]

               NOTE:     The -r parameter is highly recommended to
                         overwrite existing files in case WILDMAIL!
                         encounters tossing difficulties.  See above for
                         additional details.

                                     PKWARE, Inc.
                                9025 N. Deerwood Drive
                                 Brown Dear, WI 53223























          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                       Page  161



          WILDMAIL! v3.01                                  APPENDIX A - ARJ
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ


                                       ARJ 2.30
                  Copyright (c) 1990-92  Robert K Jung.  Jan 19 1992
             All Rights Reserved. ARJ file compression archiver utility.
             ===========================================================

               Usage:    ARJ <command> [-<sw> [-<sw>...]] <archive_name>
                             [<file_names>...]

               List of frequently used commands and switches.

               <Commands>
                          a = Add files to archive
                          m = Move files to archive
                          d = Delete files from archive
                          t = Test integrity of archive
                          e = Extract files from archive
                          u = Update files to archive
                          f = Freshen files in archive
                          v = Verbosely list contents of archive
                          l = List contents of archive
                          x = Extract files with full pathname

               <Switches>
                         -c = skip time-stamp Check
                         -n = only New files (not exist)
                         -d = with Delete (move)
                         -r = Recurse subdirectories
                         -e = Exclude paths from names
                         -u = Update files (new and newer)
                         -f = Freshen existing files
                         -v = enable multiple Volumes
                         -g = Garble with password
                         -w = assign Work directory
                         -i = with no progress Indicator
                         -x = Exclude selected files
                         -m = with Method 0, 1, 2, 3, 4
                         -y = assume Yes on all queries













          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                       Page  162



          WILDMAIL! v3.01                                APPENDIX A - LHARC
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ


                                    LHARC  v1.13c
                      Copyright (c) Haruyasu Yoshizaki, 1988-89
                 High-Performance File-Compression Program - 05/31/89
                 ====================================================

               Usage: LHARC [<command>] [{{/|-}{<switch>[-|+|2|<option>]}}] 
                      <archive_name> [{<drive_name>:}|
                      {<home_directory_name>\}] [<path_name> ...]

               <command>
                          a = Add files to archive
                          u = Update files to archive
                          f = Freshen files in archive
                          m = Move new files into archive
                          d = Delete files from archive
                        e,x = Extract files from archive
                          p = disPlay files in archive
                        l,v = View List of files in archive
                          s = make a Self-extracting archive
                          t = Test integrity of archive

               <switch>
                         -r = Recursively collect files
                         -w = assign Work directory
                         -x = allow Extended file names
                         -m = no Message for query
                         -p = distinguish full Path names
                         -c = skip time-stamp Check
                         -a = allow any Attributes of files
                         -v = View files by another utility
                         -n = display No indicator
                         -k = Key word for AUTOLARC.BAT
                         -t = archive's Time-stamp option

















          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                       Page  163



          WILDMAIL! v3.01                                  APPENDIX A - LHA
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

           
                                   LHA version 2.13
                      Copyright (c) Haruyasu Yoshizaki, 1988-91
                A High-Performance File-Compression Program - 07/20/91
                ======================================================

               Usage:    LHA  <command> [/option[-+012|WDIR]]
          <archive[.LZH]>
                              [DIR\] [filenames]

               <command>
                          a = Add files      u = Update files
                          m = Move files     f = Freshen files
                          d = Delete files   p = disPlay files
                          e = Extract files  l = List of files

                          x = Extract files with pathnames
                          v = View listing of files with pathnames
                          s = make a Self-extracting archive
                          t = Test the integrity of an archive

               <option>
                         /r = Recursively collect files
                         /w = assign Work directory
                         /x = allow Extended file names
                         /m = no Message for query
                         /p = distinguish full Path names
                         /c = skip time-stamp Check
                         /a = allow any Attributes of files
                         /z = Zero compression (only store)
                         /t = archive's Time-stamp option
                         /h = select Header level (default = 1)
                         /o = use Old compatible method
                         /n = display No indicator a/o pathname
                         /i = not Ignore lower case
                         /l = display Long name with indicator
                         /s = Skip by time is not reported
                         /- = '@' and/or '-' as usual letters













          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                       Page  164



          WILDMAIL! v3.01                                  APPENDIX A - PAK
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ



               Usage:    PAK <command> [/opt] [/opt..] <archive name>
          [file]

               <command>
                           A = Add files to archive
                           M = Move files to archive
                           U = Update archive files
                           F = Update duplicate files
                           E = Extract files from archive
                           X = Move files from archive
                           D = Delete files
                           L = List files
                           V = List files
                           P = Display files
                           T = Test files
                           C = Convert files
                           R = Revise remarks

               <option>
                         /C  = use Crunching compression
                         /S  = use Squashing compression
                         /G  = Garble with password
                         /M  = Move files
                         /D  = Duplicate files only
                         /R  = with Remarks
                         /P  = Pack archives
                         /ON = Sort by Name
                         /OT = Sort by time
                         /OS = Sort by Size
                         /OE = Sort by extension
                         /O- = no sort
                         /WA = Write over Always
                         /WP = Prompt Write over
                         /WO = Write over Older
                         /WN = Never Write over
                         /T  = set Temporary path













          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                       Page  165



          WILDMAIL! v3.01                                APPENDIX A - PKZIP
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ


                                   PKZIP (R) v1.10
                  Copr. 1989-1990 PKWARE Inc.  All Rights Reserved. 
              Reg. U.S. Pat. and Tm. Off. Create/Update Utility 03-15-90
              ==========================================================

               Usage:    PKZIP [-b[path]] [options] zipfile [files...]

               <options>
                    -d = delete files        -l = display license info
                    -a = add files           -c = add/edit file comments
                    -k = keep same ZIP date  -q = enable ANSI comments
                    -r = recurse subdirs     -z = add zipfile comment
                    -i = add changed files   -f = freshen files
                    -u = update files

                    -b = create temp zipfile on alternate drive
                    -C = add comments to new files only
                    -o = set ZIP date to latest file

                    -m[u,f]   = move files
                    -s<pwd>   = Scramble files with password
                    -$[drive] = save volume label

               -t[mmddyy]    = Compress files on or after specified date
                               (default=today)
               -e[x,i,s]     = use maximal compression/Implode only/Shrink
                               only
               -<p|P>        = store pathnames | p=recursed into |
                               P=specified   & recursed into
               -<w|W><H,S>   = | w=include | W=don't include | Hidden &
                               System files
               -<j|J><H,S,R> = | j=mask | J=don't mask | Hidden/System &
                               Readonly attributes


                                     PKWARE, Inc.
                                9025 N. Deerwood Drive
                                 Brown Dear, WI 53223












          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                       Page  166



          WILDMAIL! v3.01                              APPENDIX A - UNPKZIP
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ


                                  PKUNZIP (R) v1.10
                  Copr. 1989-1990 PKWARE Inc.  All Rights Reserved. 
              Reg. U.S. Pat. and Tm. Off. Create/Update Utility 03-15-90
              ==========================================================

               Usage:    PKUNZIP [options] zipfile [d:outpath\] [file...]

               <options>
                         -c[m] = extract to screen [with more]
                         -t = test zipfile integrity
                         -d = create directories stored in ZIP
                         -l = display software license
                         -n = extract only newer files
                         -o = overwrite existing files
                         -q = enable ANSI in comments
                    -s<pwd> = unscramble with password
                         -f = extract only newer & existing files
                         -$ = extract volume label if in ZIP

               -p[a,b,c][1,2,3]  = extract to printer [Asc mode,Bin
                                   mode,Com port] [port #]
               -<j|J><H,S,R>     = | j=mask | J=don't mask | Hidden,
                                   System/Readonly attributes
               -e[c,d,e,n,p,s]   = extract files in CRC/Date/Ext/Name &
                                   Percentage/Size order


          NOTE:     The -o parameter is highly recommended to overwrite
                    existing files in case WILDMAIL! encounters tossing
                    difficulties.  See above for additional details.


                                     PKWARE, Inc.
                                9025 N. Deerwood Drive
                                 Brown Dear, WI 53223















          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                       Page  167



          WILDMAIL! v3.01                                  APPENDIX A - ZOO
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ


                                  ZOO archiver v2.00
                                (1988/02/06 21:24:14)
             (C) Copyright 1988 Rahul Dhesi  Noncommercial use permitted
             ===========================================================

               Novice usage:  ZOO <-cmd> archive[.zoo] file...

               Where <-cmd> = -add -extract -move -test -print -delete
                              -list -update -freshen -comment

               Usage:    ZOO <command> [option] archive

               <command>
                    a = add files            P = pack archive
                    c = update comments      T = fix archive datestamp
                    D = delete stored files  u = add only newer files
                  e,x = extract files        U = undelete stored files
               l,L,v,V = list filename       g = adj. gen. limit/count

               <options>
                         -a = show archive name(s) in listing
                         -A = apply g or c to archive
                         -c = add/list comments
                         -d = extract/list deleted files too
                        -dd = extract/list only deleted files
                         -E = erase backup after packing
                         -f = fast add (no compression) or list
                         -M = move when adding (erase original)
                         -n = add only files not already in archive
                         -N = send extracted data to Neverland
                         -O = don't ask "Overwrite?"
                         -q = be quiet
                         -p = pipe extracted data to standard output
                         -: = don't store dir names
                      -/,// = extract full pathnames
                         -. = pack to current dir
                         -I = add filenames read from stdin
                         -C = show file CRC value
                       -+/- = enable/disable generations
                         -S = overwrite newer files
                         -g = list generation limits
                         -P = pack after adding
                         -@n = start extract/list at position n

          NOTE:     The -O parameter is highly recommended to overwrite
                    existing files in case WILDMAIL! encounters tossing
                    difficulties.  See above for additional details.



          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                       Page  168



          WILDMAIL! v3.01          APPENDIX B - FRONTDOOR/INTERMAIL SYSTEMS
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

          APPENDIX B - FRONTDOOR/INTERMAIL SYSTEMS

          This section is offered as a reference when using WILDMAIL! with
          the front end mailer called FrontDoor.  This is a very popular
          mailer and can be downloaded from just about any BBS under the
          name of FD202.ARJ.  The current version as of this writing is
          v2.02.  

          This section is devoted to the associated batch files and NOT the
          actual setup of FrontDoor via the FDSETUP program.  For specific
          information on FDSETUP, refer to its author for technical
          support.

          Again, the information presented here is for reference only!  We
          can not offer support on FrontDoor, but we have included this
          section due to its popularity.


          ASSOCIATED BATCH FILES

          FrontDoor can be run standalone, but for use with WILDMAIL! it
          MUST be run from a batch file.  This file for our example
          purposes will be called CAT.BAT.

          When using FrontDoor/WILDMAIL!/WILDCAT!, there are three batch
          files involved in this process.  These files all exist in the \FD
          directory.  Shown below is a brief description of these files.


               CAT.BAT -      This is the main batch file used when running
                              FrontDoor.  After this file has been
                              executed, FrontDoor will be ready to receive
                              calls and if a human caller is detected, it
                              will then pass control to DOBBS.BAT via the
                              DOS CALL command.

               DOBBS.BAT -    When a human caller is detected, FrontDoor
                              will create this file in the \FD directory
                              overwriting the previous DOBBS.BAT file and
                              exit with a errorlevel 100.  This is a one
                              line batch file that executes EXEBBS.BAT and
                              contains information that will be passed to
                              WILDCAT! for proper operation. 

               EXEBBS.BAT -   This is the main batch file used to execute
                              WILDCAT!  This file will test the contents of
                              DOBBS.BAT for specific character strings for
                              use in determining whether or not this is a



          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                       Page  169



          WILDMAIL! v3.01          APPENDIX B - FRONTDOOR/INTERMAIL SYSTEMS
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

                              reliable connection.  This information is
                              then passed onto WILDCAT! to enable/disable
                              the error correcting type protocols. 


          SYSTEM FLOW

          The basic flow of these batch files when a human caller connects
          to FrontDoor is as follows.

          CAT.BAT -> DOBBS.BAT -> EXEBBS.BAT (then return to CAT.BAT).

          When CAT.BAT is executed, FrontDoor will be brought up and will
          be waiting for calls.  When a human caller connects and FrontDoor
          displays the "Press Escape twice for WILDCAT!" message and after
          pressing escape twice, FrontDoor will drop with a errorlevel 100
          and create a batch file called DOBBS.BAT in the \FD directory. 
          This batch file contains information on the connect speed, com
          port, time remaining until FrontDoor's next event and a possible
          reliable connect mode string if the modem returned one.

          In the CAT.BAT file, after dropping with a errorlevel 100, the
          batch file will instruct it to use the CALL command when
          executing DOBBS.BAT.  This will ensure that when DOBBS.BAT is
          finished executing, it will return program execution to CAT.BAT.

          DOBBS.BAT then executes a batch file called EXEBBS.BAT which in
          turn tests for various reliable connect strings and then executes
          the appropriate command line to bring up WILDCAT!  

          When the caller logs off the BBS, WILDCAT! will terminate and
          program flow will return to EXEBBS.BAT.  This file basically just
          "ends" and returns to the batch file that executed it called
          DOBBS.BAT and since there was only one line to that batch file,
          it will then return to the CAT.BAT file and continue to the NEXT
          line AFTER executing the CALL command and continue on.  The
          program flow will return to the main loop and bring FrontDoor
          back up waiting for calls.

          If a mail call happens, the basic flow will remain in CAT.BAT and
          execute WILDMAIL! for processing and then return to FrontDoor. 
          For additional information on this process, refer to the section
          regarding the CAT.BAT file.

          This may sound a little complicated, but in the following
          examples, we will try and make more sense out of this.





          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                       Page  170



          WILDMAIL! v3.01          APPENDIX B - FRONTDOOR/INTERMAIL SYSTEMS
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

          Below is a sample batch file used to run FrontDoor as a front end
          mailer for WILDCAT! v3.x.  Throughout the example batch files,
          line numbers are shown to the immediate left with the > symbols.
          ie. 23> refers to line 23.  They DO NOT EXIST in the actual batch
          file.


                1>  @echo off
                2>  cls
                3>  SET FD=c:\fd
                4>  SET WCNODEID=1
                5>  SET WCMDM=USRHST

                6>  :START
                7>  c:
                8>  cd\fd
                9>  fd -NOUNPACK
               10>  IF ERRORLEVEL 100  goto RUN-BBS  
               11>  IF ERRORLEVEL  90  goto SCAN-TOSS
               12>  IF ERRORLEVEL  80  goto LOCAL-BBS
               13>  IF ERRORLEVEL   1  goto EXIT
               14>  IF ERRORLEVEL   0  goto EXIT
               15>  goto START

               16>  :RUN-BBS
               17>  call DOBBS.BAT
               18>  goto START

               19>  :SCAN-TOSS
               20>  cls
               21>  c:
               22>  cd\wm30
               23>  wm toss scan netmail areamgr
               24>  goto START

               25>  :LOCAL-BBS
               26>  c:
               27>  cd\wc30
               28>  wildcat /B LOCAL
               29>  goto START

               30>  :EXIT

          The following descriptions of this batch files assumes some
          understanding of how to create and use batch files.  The batch
          files used in these examples make use of 2 important DOS
          commands, the IF ERRORLEVEL/GOTO and the LABEL commands.  Please
          refer to the appropriate DOS manual for specifics if necessary.



          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                       Page  171



          WILDMAIL! v3.01          APPENDIX B - FRONTDOOR/INTERMAIL SYSTEMS
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

          CAT.BAT FILE 

          Line #1 - Simply turns off all display for each command that's
                    executed from this file. 

          Line #2 - This clears the screen.

          Line #3 - Sets environment variable FD equal to the path where
                    all the FrontDoor system files are located and is
                    required by FrontDoor.

          Line #4 - Lines #4 and #5 are used for WILDCAT! to set the Node
                    ID and the appropriate modem definition file (.MDM) to
                    use for operation when WILDCAT! is executed.

          Line #6 - This is the MAIN PROGRAM LOOP label.

          Line #7 - Changes to the appropriate drive letter.  You will need
                    to specify here which one is required for your system.

          Line #8 - Change directories to the location of the FrontDoor
                    program files.

          Line #9 - This line actually executes FrontDoor.  Notice the
                    command line parameter, -NOUNPACK.  This command is
                    used to make sure netmail messages are properly tossed
                    into WILDCAT!  If this parameter is NOT used, FrontDoor
                    will grab these messages and toss it into its own
                    internal message base and delete them before WILDMAIL!
                    can properly process them.

          Line 10 - This line tests to see of the errorlevel returned by
                    FrontDoor when it exited equals the value of 100.  If
                    it does, then it will 'goto' the label called RUN-BBS
                    in line #16.  This will start the process of bringing
                    up the BBS.  This is desired when a caller connects and
                    presses the Escape key twice.

          Line 11 - This functions exactly the same was as line #10 does,
                    except it will 'goto' a label called SCAN-TOSS on line
                    #19.  This is used with the active events 'behavior'
                    option when preparing to process the incoming mail. 
                    Normally, after mail has been received, FrontDoor will
                    drop with this errorlevel (any number can be specified,
                    but must be defined in FDSETUP) and then jump to line
                    #19 to start execution of WILDMAIL!





          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                       Page  172



          WILDMAIL! v3.01          APPENDIX B - FRONTDOOR/INTERMAIL SYSTEMS
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ


          Line 12 - Same as line #10 except tests for an errorlevel of 80
                    and if so, jumps to the label called LOCAL-BBS on line
                    #25.  This is a user defined errorlevel used to bring
                    up the BBS in local mode.  This value is defined in
                    FDSETUP, under Mailer, Function Keys and is normally
                    the F1 key to remain consistent with WILDCAT!'s SysOp
                    logon.  This option is presented here as a convenience
                    and is not required for proper operation.

          Line 13 - Lines #13 and #14 are used to test for abnormal/normal
                    shutting down (Alt-Q) of FrontDoor.  These lines will
                    jump to the label called EXIT on line #30 and will
                    return you to the DOS prompt.  This is a normal exit
                    routine.

          Line 15 - This line is a simple safety valve used to restart
                    FrontDoor in case one of the errorlevels didn't match
                    the ones that were included here.  Typically, this is
                    some sort of abnormal exit from FrontDoor, and instead
                    of ending up at the DOS prompt, this will attempt to
                    restart FrontDoor.

          Line 16 - Lines #16, #17 and #18 are used when a human caller is
                    detected and will used to bring up the BBS.  This line
                    contains the label for the MAIN LOOP when FrontDoor
                    drops with an errorlevel 100 from line #10.

          Line 17 - This line executes the DOBBS.BAT batch file created
                    when FrontDoor exited with a errorlevel 100.  The CALL
                    command is used here to ensure that when DOBBS.BAT is
                    finished executing, it will RETURN TO LINE #18 of this
                    file.  Without the CALL command, when DOBBS.BAT was
                    finished executing, it would simply drop to the DOS
                    prompt.  NOT GOOD!

          Line 18 - After DOBBS.BAT is finished executing, it will return
                    to this line and then 'goto' the label called START on
                    line #6.  This will complete the process of the caller
                    logging off the BBS and preparing to restart FrontDoor
                    and be ready to take additional calls.

          Line 19 - This is the main WILDMAIL! program loop for processing
                    mail.

          Line 20 - Clears the screen.





          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                       Page  173



          WILDMAIL! v3.01          APPENDIX B - FRONTDOOR/INTERMAIL SYSTEMS
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ


          Line 21 - Changes to the drive where the WILDMAIL! subdirectory
                    is located.

          Line 22 - Changes to the WILDMAIL! subdirectory where all the
                    configuration and executable files are located.

          Line 23 - Executes WILDMAIL! with the TOSS SCAN command line
                    parameters.  This will start the actual processing of
                    mail. 

          Line 24 - This terminates the mail processing loop and restarts
                    FrontDoor by jumping to a label called START in line
                    #6.

          Line 25 - The is the main LOCAL LOGON loop's label.  This
                    'subroutine' is executed when FrontDoor drops with a
                    errorlevel 80 from line #12.  This is used to allow
                    local logons to the BBS when the appropriate function
                    key has been pressed while FrontDoor is up and waiting
                    for calls. 

          Line 26 - Changes to the drive where WILDCAT! is located.

          Line 27 - Changes to the subdirectory containing all the WILDCAT!
                    files.

          Line 28 - Executes WILDCAT! using the options set in line #4 with
                    the /B LOCAL command parameters for allowing local
                    logons.

          Line 29 - After normal logoff, FrontDoor is brought back up by
                    returning to line #6.

          Line 30 - This is the label used when FrontDoor is brought down
                    via lines #13 or #14.  This is the last line in the
                    batch file and thus will return you to the DOS prompt. 














          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                       Page  174



          WILDMAIL! v3.01          APPENDIX B - FRONTDOOR/INTERMAIL SYSTEMS
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

          DOBBS.BAT FILE

          FrontDoor MUST BE configured to drop with a errorlevel 100 on ALL
          POSSIBLE CONNECT SPEEDS and create the .BAT file.  This
          information is found in FDSETUP under Mailer, Errorlevels.  

          This is a one line batch file created by FrontDoor and will
          change from caller to caller.  Shown below is a sample of this
          file. 

               EXEBBS 9600 1 897 /ARQ/V32/LAPM/V42BIS


               ^^^^^^ ^^^^ ^ ^^^ ^^^^^^^^^^^^^^^^^^^^
                 %0    %1 %2  %3        %4     <----- DOS Variables


          Below is a breakdown of the above command line.

               %0 = Command that DOS will execute
               %1 = Connect speed determined by FrontDoor
               %2 = Communications port
               %3 = Minutes remaining until next event
               %4 = Reliable mode connect string (if applicable)


          This line will execute a file called EXEBBS.BAT in the \FD
          directory passing the speed as 9600 (%1), com port 1 (%2), 897
          minutes (%3) until the next FrontDoor event and the connect
          string of /ARQ/V32/LAPM/V42BIS (%4).  The contents of EXEBBS.BAT
          will then take this information and properly evaluate it and then
          execute it for proper operation in WILDCAT!



















          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                       Page  175



          WILDMAIL! v3.01          APPENDIX B - FRONTDOOR/INTERMAIL SYSTEMS
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

          EXEBBS.BAT FILE

          This batch file is used primarily to bring up WILDCAT! with the
          parameters passed from the calling batch file called DOBBS.BAT. 
          The information contained in DOBBS.BAT is used to 'set up'
          WILDCAT! for the proper speed, time remaining before any
          FrontDoor events and whether or not this is a reliable
          connection.

          Sample EXEBBS.BAT file for use with FrontDoor.

                1>  @echo off
                2>  cls
                3>  SET comspec=c:\command.com

                4>  SET connect=

                5>  if %4 == /ARQ                   SET connect=/MNP
                6>  if %4 == /ARQ/HST               SET connect=/MNP
                7>  if %4 == /ARQ/V32               SET connect=/MNP
                8>  if %4 == /ARQ/LAPM              SET connect=/MNP
                9>  if %4 == /ARQ/MNP               SET connect=/MNP
               10>  if %4 == /ARQ/HST/HST           SET connect=/MNP
               11>  if %4 == /ARQ/LAPM/V42BIS       SET connect=/MNP
               12>  if %4 == /ARQ/MNP/MNP5          SET connect=/MNP
               13>  if %4 == /ARQ/HST/HST/MNP5      SET connect=/MNP
               14>  if %4 == /ARQ/HST/HST/V42BIS    SET connect=/MNP
               15>  if %4 == /ARQ/V32/LAPM/V42BIS   SET connect=/MNP
               16>  if %4 == /ARQ/V32/MNP           SET connect=/MNP
               17>  if %4 == /ARQ/V32/LAPM/MNP/MNP5 SET connect=/MNP

               18>  :START
               19>  c:
               20>  cd\wc30
               21>  ctty con
               22>  wildcat /B %1%connect% %3


          InterMail Systems

               In the above example you should note that all of the connect
               strings are in upper case.  Since InterMail operates
               virtually identically to FrontDoor, it has this little quirk
               in this it only uppercases the first character of the 
               connect string.  Since the batch == command is case
               sensitive, it's imperative that you understand theses
               differences.




          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                       Page  176



          WILDMAIL! v3.01          APPENDIX B - FRONTDOOR/INTERMAIL SYSTEMS
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

          EXEBBS.BAT FILE

          Line #1 - Simply turns off all display for each command that's
                    executed from this file. 

          Line #2 - This clears the screen.

          Line #3 - This is safety measure to make sure DOS knows where to
                    look for COMMAND.COM.

          Line #4 - This is a very important DOS environment variable. 
                    This is used to pass the /MNP flag associated with the
                    current connection to WILDCAT! to indicate whether or
                    not this is a reliable connect.  If this flag is set,
                    WILDCAT! will make the Ymodem/G and 1K-Xmodem/G
                    protocols available to the caller.  For now, we are
                    turning the flag off (actually removing the variable
                    entirely) because we will test the connect string for a
                    reliable connect in lines #5 through #17.

          Line #5 - Lines #5 through #17 are used to test the connect
                    string information passed to us from the DOBBS.BAT
                    file.  If you refer to the section on the DOBBS.BAT
                    file, note that this is DOS environment variable %4. 
                    Here we test for a exact match of the string supplied,
                    if there is a match, we will turn on the flag used in
                    line #4 (connect=) via the SET command, to now equal
                    /MNP.  If no match is found, the environment variable
                    'connect' will be untouched.

                    The strings in these lines are ones outputted by your
                    modem.  You will need to review each possible
                    combination for your EXACT modem type.  The ones shown
                    here are for the older USR Dual Standards without
                    v.32bis.  The strings you enter must be the ones that
                    are a EXACT MATCH and indicate a reliable connect. 
                    Some modems use a simple /REL and others may be more
                    complex.

          Line 18 - The MAIN PROGRAM LOOP for bringing up WILDCAT!

          Line 19 - Changes to the drive where WILDCAT! is located.

          Line 20 - Changes to the subdirectory containing all the WILDCAT!
                    files.






          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                       Page  177



          WILDMAIL! v3.01          APPENDIX B - FRONTDOOR/INTERMAIL SYSTEMS
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

          Line 21 - Redirects output to the CONsole.  This is a safety
                    valve to make sure there are not conflicts as to where
                    data is to be outputted to.  This line is not normally
                    needed, but is here in case a DOOR program goes nuts on
                    you. 

          Line 22 - This is the main command line that executes WILDCAT! 
                    The /B parameter is required and indicates that a front
                    end mailer is used with this configuration and to look
                    for additional command line information that is passed. 
                    If you recall in the DOBBS.BAT file, the DOS
                    environment variable %1 indicated connect speed.  The
                    '%connect%' parameter is the reliable connect flag used
                    in lines #4 through #17 and %3 is the time remaining
                    until the next FrontDoor event.

                    To help understand this, we will use the contents of
                    the example DOBBS.BAT file  The command on line #22;

                         wildcat /B %1%connect% %3

                    will be replaced with the parameters passed in
                    DOBBS.BAT and will now look like:

                         wildcat /B 9600/MNP 897

                    This indicates a reliable connection at 9600 baud with
                    897 minutes left until the next FrontDoor event.  A
                    match was found on line #15 so the DOS environment
                    variable 'connect' now equals /MNP.  If there wasn't a
                    match in lines #5 through #17, the command line would
                    read:

                         wildcat /B 9600 897

                    You will notice the /MNP parameter is now missing and
                    WILDCAT! will not allow the Ymodem/G and 1K-Xmodem/G
                    protocols.


          When the caller logs off the BBS, either normally, or by dropping
          carrier, WILDCAT! will exit and return to the EXEBBS.BAT file. 
          Since there are no remaining lines in this batch file to execute,
          the program flow will return to DOBBS.BAT, and since there are no
          more lines to execute in the DOBBS.BAT file, it will return to
          the CAT.BAT file, line #18.  This will then 'goto' line #6 and
          restart FrontDoor completing our 'human caller loop'.




          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                       Page  178



          WILDMAIL! v3.01            APPENDIX C - WHAT IS NETMAIL/ECHOMAIL?
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

          APPENDIX C - WHAT IS NETMAIL/ECHOMAIL?

          There is a lot confusion and misunderstanding of these two
          distinctly different types of mail especially by newcomers to the
          BBS arena.  This section will attempt to clarify these two terms
          into something a bit more palatable than just saying Netmail
          means direct and Echomail means going from system to system
          before reaching its destination.


          System Addressing

          Within the original designs of Fidonet style mail transfers, a
          method was needed to differentiate one system from another.  This
          was done in the form of system addressing meaning that each PC in
          the network would be assigned a unique number (or address)
          different from any other PC in the network.  Today, this is
          typically done in the standard <zone:net/node.point> or 4
          dimensional addressing method.

          Now that each PC had a address, a message could be sent to that
          address in a manner similar to the way the post office can
          forward letters from across town or out of state to our home
          address based upon the address on the letter.  This manner proved
          very effective and as long as systems were running 24 hours a
          day, a message could be sent literally any time of the day or
          night.   


          File Attachments

          This is where Netmail originally started.   You could create a
          message on your system and address it to a person and send it
          directly to the destination system.  Because this method proved
          so effective, people were not content with just sending a message
          anymore, they wanted to be able to send a file along with the
          message.  So special information was added to the Netmail message
          to inform the front end mailer that when it would send the
          Netmail message, it should also send the file that was "attached"
          to it.


          Sharing Message Bases

          Things were really starting to cook with this new technology! 
          Well, as things would have it, someone came up with the bright
          idea that wouldn't it be nice to have the same message base on
          one system (let's call it System #1) as on another (or System



          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                       Page  179



          WILDMAIL! v3.01            APPENDIX C - WHAT IS NETMAIL/ECHOMAIL?
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

          #2).  This means more people could have access to the same
          information on System #2 without having to call System #1 that
          the messages originated from.  

          Since we could already attach files to a Netmail message
          addressed to a specific system, why don't we just bundle up the
          entire message base and send it to the other system.  Sure!  It
          would be real easy to do, but what if people wanted to reply to
          those messages?  They would have to call the system the messages
          originated from (System #1) and leave the replies there.  That
          was nice but people being lazy as they are, a better plan was
          needed.  So the first thought was that System #2 could just send
          back the entire message database the following day.  But that
          wouldn't work because if System #1 had any new messages entered
          in its message base, they would be lost.

          Then the bright idea come to light.  Lets just send any "new"
          messages entered and not the entire message database.  This just
          might work!  All they had to do was take all the new messages,
          bundle them up into a special file, attach it to a Netmail
          message and send it to the other system.  Now they were cooking!

          So System #2 could send out any new messages to System #1 and
          System #2 could send any new messages to System #1.  Now both
          systems would have identical message databases.  This was great! 
          To say the idea caught on would be a understatement to say the
          least.  Now two entirely different PC's could share the same
          message database.

          Once the word got out about this new technology, more and more
          BBS's wanted to join in.  All they had to do was schedule a time
          when they could send the new messages created on their system
          back to the originating system and pick up any new messages
          created on that system.  With all this new technology, new
          problems started to crop up, like how to control duplicate
          messages and who could participate in this and so on.  

          Another major problem was with all these other systems
          participating, the message traffic really started to grow. 
          That's when the idea came about of having special message
          "sections" or conferences that pertained to specific topics of
          interest thereby focusing the conversations.  Well this solved
          one problem, but because more and more people wanted to join in,
          the originating system was now spending more time transferring
          mail to other systems and none was left over for the regular
          callers on the BBS.  Still yet another problem was all these
          other systems were having to call long distance just to pick up
          the new messages!



          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                       Page  180



          WILDMAIL! v3.01            APPENDIX C - WHAT IS NETMAIL/ECHOMAIL?
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

          Hub Creation

          It was decided that since systems were usually grouped close to
          each other, they could send mail to all the members of that group
          and then someone from that group would be responsible for sending
          the new messages back to the originating system and picking up
          any new one created from the other systems.  This would free up
          the originating system from all the individual BBS's calling and
          transferring mail and limit its use only to those BBS's that
          would feed a group of other systems.  Thus the birth of Echomail.

          These BBS's that would "feed" the group of systems in their area
          were called Hubs and the individual systems within the group were
          called Nodes.  This idea took off like wild fire.  After all,
          instead of calling long distance, they could place a local call
          and pick up the same new messages as if they called the
          originating system.  This was ideal!  

          Well, as life would have it, another major problem cropped up. 
          With so many Hubs trying to get mail for their Nodes, it was
          becoming increasingly difficult for the Hubs to transfer mail
          with the originating system.  So networks were created.  These
          were groups of Hubs that would get their mail (for their Nodes)
          from one central place that would then call the originating
          system for mail.  This effectively reduced the number of Hubs
          calling the originating system and now only the networks or Area
          coordinators (as they were called) would call the originating
          system.  The Hubs would then call the Area coordinators to get
          their mail to feed their Node addresses.

          Now, bringing us up the current mail technology, the principals
          are the same only with a few more "layers" of mail travels, but
          the basic method is still the same, one system calls another and
          "echoes" the mail to a group of downlink systems which then in
          turn forward it onto other systems.  Eventually, it makes it into
          the hands of the callers of the BBS's for their usage.  

          Something that's been intentionally left out in this discussion
          is the groups of message areas or conferences.  As was mentioned
          earlier, these were conference areas devoted to a specific topic
          of discussion, so if you wanted to discuss automotive repair, you
          wouldn't want to leave a message in the gardening conference. 
          Not all the systems in the network would want to carry all the
          conferences as this could easily exceed the available disk space
          on the smaller systems.  So most BBS don't carry all the
          available conferences, but rather only the ones that pertain to
          the main "focus" of the BBS itself.




          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                       Page  181



          WILDMAIL! v3.01            APPENDIX C - WHAT IS NETMAIL/ECHOMAIL?
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

          Netmail Definition

          So lets do a recap on what we've learned already.  Netmail is a
          method by which a special message originating on one system could
          be sent to another system directly.  In other words there would
          be an Originating Address and a Destination Address on each
          message generated (not to mention the TO: and FROM: names of the
          message itself).  

          The Destination address of the message is what's used to send it
          on its way to its destination system.  Netmail messages also have
          the ability to have special file attachments so when the Netmail
          message is sent to the destination system, the attached file is
          also transmitted at the same time.

          Typically, when a file is attached to a Netmail message, the body
          of the actual Netmail message itself is usually blank, but may
          also contain text for the person it's addressed to at the
          destination system.  In other words, the Netmail message itself
          may or may not contain text.  If it doesn't contain text, then
          usually the message is addressed to the actual BBS and not a
          specific person.  These were typically referred to as "null"
          messages.


          Echomail Definition

          As was previously mentioned, echomail was the actual "contents"
          of the message bases of the systems participating in the network
          of BBS's sending and receiving mail.  This included all the
          individual conferences (or message topics) as well.  These
          messages were usually bundled up and compressed into a file and
          attached to a Netmail message to be sent to the various systems
          within the network.

          Echomail messages therefore have no specific means designed into
          them to indicate they should go to a specific network address. 
          They relied ENTIRELY on the use of Netmail messages to send them
          on their way.  Remember, these were the message bases that were
          being echoed from system to system to update the nodes message
          databases.  










          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                       Page  182



          WILDMAIL! v3.01            APPENDIX C - WHAT IS NETMAIL/ECHOMAIL?
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

          Summary

          So it can be summarized that echomail messages are bundled up
          into special file(s) called mail archive(s) that are attached to
          Netmail message(s).  These Netmail message(s) then sends this
          attached mail archive onto the different systems into the network
          for inclusion into the individual message bases of the nodes in
          the network.  

          Once the Netmail message has been received at its destination, it
          is usually deleted because normally it doesn't contain any text
          in the body of it.  It was only used to send the attached
          echomail archive bundle.

          Obviously, todays technology permits a lot more capability with
          the use of Netmail messages, but the intent here was to describe
          the differences between to the terms.  We hope we've succeeded!


































          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                       Page  183



          WILDMAIL! v3.01              APPENDIX D - OBTAINING A NODE NUMBER
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

          APPENDIX D - OBTAINING A NODE NUMBER

          In the course of WILDMAIL!'s product support, one of the commonly
          asked questions is where do I go to get a node number?  Because
          of the frequency of this question, we've decided to include a
          very general approach to this process.


          Which Network to Join

               Today, there are literally hundreds of different networks
               that support a multitude of mail transfers.  Some in QWK
               format, some in Novell's MHS, others in Fido style etc. 
               Because of this diversity, we'll limit the discussion to
               Fido style networks.  These are the networks that use a
               front end mailer such as D'Bridge, FrontDoor, InterMail
               BinkleyTerm and several others.

               First off, you should probably select one that is reasonably
               close to you because you're bound to have a number of
               questions and long distance phone bills can quickly add up. 
               So you go about calling a BBS that is currently passing mail
               to and from a given network.  Once you find the one you'd
               like to join, you should obtain a Nodelist.


          What's a Nodelist

               A Nodelist is a ASCII based text file that contains all the
               nodes (different BBS's) in that network.  This is akin to a
               phone book for a given city.  Peoples phone numbers are
               listed as well as their "addresses".

               Nodelists are used by your front end mailer (the software
               program that actually does all the dialing and file
               transfers during mail sessions) to look up a specific node
               address and obtain the phone number to dial when mail needs
               to be sent to that address.  Since these files are text
               based, you can use your favorite file viewer utility to
               display the contents of them.


          Obtaining a Nodelist

               Normally the BBS you called when searching for a network to
               join has one of these Nodelist files available for download. 
               If you can't find it on their system, you should leave a
               message to the SysOp and ask them to make it available to



          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                       Page  184



          WILDMAIL! v3.01              APPENDIX D - OBTAINING A NODE NUMBER
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

               you for download.  

          Locating the Closest Hub

               Once you download the file, you should use your file viewer
               utility to display it and if you look closely, you will
               notice there is a definite pattern to how it's laid out. 

               What you want to do to use the "search" capability of your
               file viewer and search for all the nodes that exist within
               your city.  If none exist, you should search for cities that
               are close to yours.  Normally, you'll find these cities
               closely bunched together because they are usually all within
               a special sub-network or group that all share the mail.

               Once you've located this group of nodes, you should look for
               the for the word "Hub" which is normally located as the
               first word on a line.  On this line you will find the name
               of the BBS, the SysOps name and his BBS's phone number. 
               Immediately following the phone number is the highest modem
               speed his system supports for mail transfers.  

               This person is where all the nodes listed under him/her
               (until the next occurrence of a Hub statement) get their
               mail from and is the person you need to contact.


          Contacting the Hub SysOp

               Once you've located the Hub, you should logon to their
               system as a new user (if you've never called before) and
               leave a message to the SysOp requesting a node number.  You
               should leave a detailed message about your BBS regarding the
               following items:

                    *  Complete BBS name
                    *  City and state your calling from
                    *  Phone number of your front end mailer
                    *  Modem type and maximum baud rate
                    *  Any error correction methods your modem supports
                    *  Will your system accept mail 24hrs/day

               Once you've left the message, you should check back in with
               this system and see if you've received a reply.  Normally
               this is sufficient to start the ball rolling.






          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                       Page  185



          WILDMAIL! v3.01              APPENDIX D - OBTAINING A NODE NUMBER
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

          Netmail Transfer Capability

               As part of the qualification requirements for obtaining for
               a node number, most systems require you to prove that you
               have your mailer setup and at least semi operational.  This
               usually involves having your system send their system a
               Netmail message and then you being able to receive one back
               from them.  Normally, they will assign you a temporary node
               number to be used for the testing process until your actual
               address gets assigned to you.

               Because this is the fundamental requirement of mail
               transfers, it's very important to be able to do.  If you
               haven't already gotten a fairly good grasp on this process,
               you should spend a bit of time with the documentation that
               came with your mailers software and brush up on it.

               If you're already some form of another network, this
               "approval process" may require you to show that you can
               handle multi-network mail transfers.  This usually involves
               making sure your system correctly identifies itself for each
               network you're participating.  This isn't very hard to do,
               but does require you to understand the requirements and
               needs for this capability.  Again, there is no substitute
               for reading the mailers documentation!


          Receiving Your Node Address

               Once all the above steps have been accomplished, the time
               required to actually be assigned a node number can vary
               greatly.  This is due to the work schedules of the people
               administering the network.  If they're very busy, it could
               take up to 3-4 weeks, or possibly as quick as 7 days.

               Unfortunately, there is no way to say for sure, but if you
               haven't heard anything in a couple of weeks, you might want
               to send them a message reminding them of your "application". 
               Best thing to is not get in a hurry and try to be patient.












          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                       Page  186



          WILDMAIL! v3.01                   APPENDIX E - PERFORMANCE TUNING
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

          APPENDIX E - PERFORMANCE TUNING

          Because of the inherent complexity and disk intensive nature of
          processing mail, many systems find that mail processing time can
          be excessive at times.  This section discusses ways by which you
          can increase the efficiency of your entire system thereby
          reducing the amount of time required for WILDMAIL! to process
          your echomail needs.  

          Disk Caching Software

               These are third party program(s) that execute in background
               while your PC goes about its normal duties running your BBS
               and associated utility programs.  Basically it's a method by
               which portions of your hard disk are "mirrored" in some form
               of memory reducing the amount of mechanical action required
               to retrieve information for the disk drive(s).  This memory
               can be of several different types like EMS, XMS and less
               likely, base 640K memory.  

               Because of the disk intensive nature of running a BBS
               especially in a multiline environment, disk caching software
               is a must.  Add to that the increased demands of tossing
               mail and it can significantly reduce the effectiveness of
               your BBS causing very noticeable delays and slow response
               times.

               There are many different disk caching software packages out
               in both the shareware and commercial markets and it's not
               our intent here to recommend one package over another.  But
               rather inform you ahead of time that DISK CACHING of some
               form IS REQUIRED!  If you don't already use one, after
               installing it, you will see a DRAMATIC speed increase in
               your systems performance.  Of course as a byproduct,
               WILDMAIL! will also enjoy a speed increase.

               As a side note, DOS has its own pseudo disk caching ability
               via the BUFFERS= command found in the CONFIG.SYS file.  The
               larger the number, the more space in memory that's
               allocated.  The problem is that if the number is higher than
               30, it actually takes longer to search memory than it would
               to go to the disk drive and read the information directly. 
               If this command is omitted from the CONFIG.SYS file, DOS
               will assign a default value of 8.







          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                       Page  187



          WILDMAIL! v3.01                   APPENDIX E - PERFORMANCE TUNING
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

               Because disk caches are designed to replace the
               functionality of this command, you normally must reduce the
               value of this command to something like BUFFERS=3.  This
               minimizes DOS's internal searching ability and lets the disk
               caching software take over.  With this setting to anything
               higher than 3, it reduces the effectiveness of your disk
               caching software because it's now wasting time searching the
               internal buffers and not the disk caches more advanced
               searching algorithms.

               A value of anything lower than 3 will not be of any value
               and will only hinder the bootup time of your PC prior to the
               disk caching software being loaded.  A value of 0 is invalid
               and will produce unpredictable results on your PC, the
               minimum being that it may not always allow your PC to boot
               up properly.


          DOS File Count Limitation

               Since DOS v3.0 or higher is required to run WILDMAIL!, there
               is an inherent limitation to the number of files contained
               within a subdirectory before DOS starts to become EXTREMELY
               inefficient in locating a specific file.  As a general rule
               of thumb, it's usually safe to limit the number of files
               contained within a single subdirectory to 200.

               WILDCAT! allows you to specify a DOS directory where you
               want a specific conferences message database files to reside
               via a configuration program called MAKEWILD.  A common
               mistake is to group each networks conference into its own
               subdirectory allowing for better organization.  

               While this in itself is not a problem, if you have more than
               50 conferences from that network then you can easily exceed
               200 files within that subdirectory.  Here's why.

               WILDCAT! v3.x stores each conference into its own unique
               database format separate from the other conferences.  This
               allows an incredible amount of flexibility and protection
               against a single message destroying the entire mail for the
               BBS.  









          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                       Page  188



          WILDMAIL! v3.01                   APPENDIX E - PERFORMANCE TUNING
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

               Because each conference database is separate, it can have up
               to 4 files associated with it.  You may have noticed this
               already.  Shown below are those files.

               MSGxxx.DAT     -    Actual message content/information.

               MSGxxx.IX      -    Index file containing 6 keys for each
                                   message used for high speed searching
                                   from the above .DAT file.

               MSGxxx.DIA     -    This is a special, extremely small
                                   dialog file that used in multiline
                                   systems to manage record/file locking.

               MSGxxx.CRC     -    This file is generated by the TomCat!
                                   QWK mail door for its own internal
                                   management of the users information.

               The 'xxx' represents a numeric value associated with the
               conferences number padded by leading zeros.  For example, if
               the conference number is 39, the file names would be:

                    MSG039.DAT, MSG039.IX, MSG039.DIA and MSG039.CRC

               Because the above 4 files are associated with each
               conference, you can easily exceed the recommended limit of
               200 files in a subdirectory if you have more than 50
               conferences in the same location.

               Because more and more systems are involved in different
               networks, a consistent subdirectory naming convention is
               preferred for ease of reference.  You may not realize it,
               but DOS allows you to utilize the standard naming convention
               of files for subdirectories.  This means you can add an
               extension to a directory name if you want.  

               Following that thinking, you could use the first 5
               characters to indicate the network name followed by the
               starting conference number.  Then as the extension, you
               could use the ending conference number.  











          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                       Page  189



          WILDMAIL! v3.01                   APPENDIX E - PERFORMANCE TUNING
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

               For example, let's say you have 150 different conferences in
               Fidonet starting from conference #100 and ending with
               conference #249.  

               Now in FamilyNet you have 100 conferences ranging from
               conferences #300 through #399.  

               You could use the subdirectory naming scheme as follows:

                    FIDO100.149    -    Conferences 100 through 149
                    FIDO150.199    -    Conferences 150 through 199
                    FIDO200.249    -    Conferences 200 through 249

                    FAMLY300.349   -    Conferences 300 through 349
                    FAMLY350.399   -    Conferences 350 through 399

               As you can see, this method not only solves the files per
               subdirectory limitation but also gives you a distinct visual
               indication of what conferences database files are in each
               subdirectory.

               If you have grouped all your conferences together and this
               idea appeals to you, you must do several things.  

                    1)   Create the subdirectories desired.

                    2)   Manually move the conferences database files into
                         the correct directory keeping each conferences
                         associated .IX, .DIA, and .CRC files with it.

                    3)   Run MAKEWILD and change each conferences message
                         database paths to the new subdirectory.  MAKEWILD
                         has a very handy function called Global Change via
                         the [F4] key that can significantly speed up this
                         process.

               Once the changes are complete, before logging onto the BBS,
               you should manually verify all the changes first, then once
               you're satisfied, logon and make sure the message bases are
               available and intact.


          Database Safety Mode

               For those systems that are running WILDCAT! BBS software, it
               has a special option called Database File Safety Mode.  This
               can be found via MAKEWILD (the configuration program for
               WILDCAT!) from the Main Menu, General Definition Part 2,



          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                       Page  190



          WILDMAIL! v3.01                   APPENDIX E - PERFORMANCE TUNING
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

               option #2.

               This option allows you the ability to have WILDCAT!
               automatically maintain duplicate information or additional
               verification for each of the databases it manages.  This
               means the Users, File and Message databases can be protected
               in the event of power failures, user errors and so on.  

               The disadvantage to this is that it can add a significant
               "load" to the overhead WILDCAT! must go through to execute
               your BBS depending on the upon setting.  Currently there are
               three different settings that this checking can be set to.

               NONE      -    No checking is done outside of the normal
                              error trapping routines that WILDCAT! uses.

               PARTIAL   -    This setting performs verification that data
                              was successfully written to disk.

               FULL      -    With this setting, WILDCAT! makes use of the
                              .DIA file (dialog file) to store portions of
                              the data to be saved to the database in this
                              file prior to writing it to the actual
                              database file.  If it is saved properly, it
                              will then be flushed to disk.  

                              This allows protection by making a duplicate
                              copy of the information should an unexpected
                              shutdown occur.  This permits WCREPAIR to
                              easily reconstruct the potentially lost data.

               WILDCAT! by default uses the PARTIAL setting.  As is
               mentioned in the WILDCAT! documentation, WCREPAIR (database
               repair utility) will repair just about any error that your
               system encounters just short of an erased database file.  So
               the need for this option setting to be anything but NONE is
               normally of little use on the vast majority of the systems
               in use today.  

               To give you an idea as to the impact of this option, with
               this setting set to FULL, by simply changing this option to
               NONE, you can expect to see a 400% increase in speed.  The
               PARTIAL setting being reset to NONE would have approximately
               a 200% speed increase.  Now considering your mail processing
               takes an hour to toss, you could easily cut this in half or
               greater just by making sure this option is set to NONE.
               Please bear in mind, each system is unique because of
               hardware and software differences, but the fact remains that



          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                       Page  191



          WILDMAIL! v3.01                   APPENDIX E - PERFORMANCE TUNING
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

               while the PARTIAL and FULL options can offer you additional
               peace of mind, but they come at a cost.  That cost being
               performance.

               By personal experience from our own 10 line BBS system, we
               use the NONE setting and rarely (if ever) have to run
               WCREPAIR on the message bases.  We currently maintain over
               200,000 messages at any one point in time in 500 or so
               conferences, so we speak with a considerable amount of
               confidence in this area.


          Maintain Message Level Limits

               WILDCAT! v3.x allows you the ability to predefine the
               maximum number of messages that should be maintained within
               the conferences associated database file.  This means, if
               the conference is at its limit of say 100 messages, the next
               time a new one is to be added, WILDCAT! will delete or purge
               the oldest one first and then add the new message.

               With this option you can see that adding a new message to a
               "full" message database requires several additional steps
               before the new message can be added.  The oldest message
               must be deleted, and then each of the 6 search keys
               associated with that message must be deleted as well.  Only
               then can the new message be added.  This involves additional
               processing time for each new message added.

               WMCONFIG! allows you to override this setting on a global
               basis (not conference by conference) by use of the Maintain
               message levels options found from the Main Menu, System
               Information, WILDCAT! specific options.  But this option
               comes at a SIGNIFICANT cost in the terms of disk space.  

               Basically, if you tell WILDMAIL! to ignore WILDCAT!'s
               conference message limitations, the database file for each
               conference will grow considerably.  You can execute
               WILDMAIL! with the PURGE option to reduce the database file
               back to it original message limitation in WILDCAT!, but the
               database file stays at that the newly expanded size with
               just a bunch of blank "slots"  where the old messages were.

               Normally we don't recommend this setting unless you have a
               SIGNIFICANT amount of free disk space.  For additional
               information on this option, please refer to Maintain message
               levels option found from the Main Menu, System Information
               under WILDCAT! specific options.



          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                       Page  192



          WILDMAIL! v3.01                   APPENDIX E - PERFORMANCE TUNING
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

          Preprocessing Mail Deliveries

               Preprocessing mail is by far the fastest method to toss
               mail.  This is due mainly because WILDMAIL! will simply
               forward all mail to both your downlink nodes and to your
               system (into the defined PRETOSS directory).  This bypasses
               tossing mail directly into the WILDCAT! message databases
               and thereby processes the mail incredibly fast!

               This pretossing capability was primarily designed for those
               systems that hub mail for downlink systems which move a lot
               of mail.  Because the WILDCAT! databases are not used in
               this process, you may want to consider using this option if
               you move a lot of mail.  For those systems that are simply
               nodes and don't forward any mail, this option will be of
               little use to you.

               The advantage of this option is that you can schedule when
               WILDMAIL! will take the mail that has been preprocessed for
               your system and toss it into your WILDCAT! message bases. 
               This means all your downlink nodes will get their mail
               faster and your system won't be tied up as long on the
               initial tossing session.  Then when your system is not as
               busy, say in the early morning hours, you could execute
               WILDMAIL! with the PRETOSS command line parameter to process
               your systems mail.

               For specific information on using/setting up this option,
               please refer to the Main Menu option - System Information,
               BBS specific options - Pre-process echomail.


          Summary

          As you are probably aware, each system running a BBS is
          configured differently with rarely any two systems running
          exactly the same way.  Because of this, there is simply no way to
          accurately predict the outcome of performance tuning changes made
          to your system.  Unfortunately, this is strictly a trial and
          error basis with you being the judge of the effects.

          A lot of factors come into play when operating a BBS especially
          in a multiline environment.  Obviously the faster the components
          that make up your BBS, the more potential it has for performance
          gains.  Things to consider are:

               o    Available horsepower - 286/386/486 etc.




          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                       Page  193



          WILDMAIL! v3.01                   APPENDIX E - PERFORMANCE TUNING
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

               o    Disk drives capacity and its average seek time.

               o    Available memory and how it's being utilized.

               o    Multitasking software and its configuration.

               o    Number of lines running on a single machine.

               o    Modem speeds.


          While we have tried to give examples of the most significant
          causes for performance slowdowns, we can't go into each area
          fully and thus can only offer this bit of additional advice.

          Take your time troubleshooting and performance tuning.  A very
          methodical and accurate effect analysis technique will yield the
          highest results.  Unfortunately this requires a bit of patience
          on your part but it will be well worth it.  Please bear in mind,
          any performance tuning you do, you should always have a good
          backup before you start, especially when you start changing your
          disk caching software settings!  Otherwise, you run the risk of
          losing a lot of your hard work and effort.

          As a last note, this section has been devoted entirely to
          speeding up your PC, not WILDMAIL!.  Once your PC has been
          thoroughly tuned, only then will your callers and WILDMAIL! reap
          its full benefits.























          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                       Page  194



          WILDMAIL! v3.01            APPENDIX F - ERRORS UNCOMPRESSING MAIL
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

          APPENDIX F - ERRORS UNCOMPRESSING MAIL

          In the past when mail was uncompressed, no checking was done with
          regards to the outcome of the actual process.  If an error
          occurred, WILDMAIL! would process whatever PKT files were found
          and then cleanup after itself by deleting the mail archive.  

          During the unarchival process, certain situations could occur
          like running out of disk space or even running up against a
          partially corrupted mail archive.  If an error did occur, the
          outcome was often less than desirable, typically with the loss of
          mail.


          Errorlevel Checking

               WILDMAIL! now checks for an errorlevel returned by the
               uncompression program.  If something other than an
               errorlevel of zero is returned, WILDMAIL! will leave the
               mail archive intact as well as any PKT files that were
               successfully uncompressed.  


          Logfile Entries

               An entry is then placed in the WM.LOG file (or whatever you
               have named log file) of the errorlevel along with a brief
               description of the problem.  Since all the PKT files that
               were successfully uncompressed remain intact, WILDMAIL!
               proceeds to toss them as usual.

               The next time WILDMAIL! executes, it will attempt to
               uncompress the archive and the process will start all over
               again.  If the same PKT files are uncompressed, when
               WILDMAIL! starts to toss them, it will find the messages as
               duplicates and simply ignore them.  Bear in mind, each time
               WILDMAIL! encounters an error, it makes an entry in the log
               file.













          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                       Page  195



          WILDMAIL! v3.01                APPENDIX G - PATH AND SEENBY LINES
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

          APPENDIX G - PATH: AND SEEN-BY: LINES

          In Appendix C we talked about sending echomail messages from one
          system to another so that all BBS's could share a common message
          base.  A very important aspect of transferring mail between
          systems like this is how to prevent duplicate messages from being
          re-introduced in the network.

          This is handled in a rather ingenious way by adding information
          to the end of each message indicating all the systems that have
          processed this message.  So every time a new system would receive
          the message, its node address would be added to this special list
          of nodes.  So the more systems that have "Seen" the message, the
          more node addresses would be appended to the end of the message. 
          This is where the term SEEN-BY: lines comes from.


          FORMAT

          These SEEN-BY: lines only contain the <net/node> portion of the
          node addresses.  Notice that the <zone> information is NOT
          contained within them, thus limiting the duplicate checking to
          only nodes within the same <zone>.

          The keyword "SEEN-BY:" must start at position 1 on a new line
          following the origin line information (unless it's preceded by
          special characters which hide it).  The node addresses follow it
          separated by a single space and can inherit the <net> portion of
          the previous address on the line.  For example, if you have a
          SEEN-BY line such as:

                              SEEN-BY: 161/123 504

          It's assumed that node address 504 is actually 161/504.  Normally
          these lines are sorted by the mail processor each time a new node
          address is added with each line limited to approximately 78
          characters (total) in length before a new line is created.


          HIDDEN INFORMATION

          Because SEEN-BY lines are only used by the mail processors which
          handle the forwarding and tossing of the mail, this information
          is of little use to the actual message recipient so special
          control characters can be added to the SEEN-BY: lines.  Normally
          this is a Hex 01 or commonly referred to as a Control A.  This is 
          typically used by the message viewers to prevent the information
          from being displayed thereby reducing the "clutter" on the



          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                       Page  196



          WILDMAIL! v3.01                APPENDIX G - PATH AND SEENBY LINES
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

          screen.

          WILDMAIL! v3.01 has the ability to remove the Hex 01 (Control A)
          characters  from the AREA:, SEEN-BY: and PATH: lines allowing you
          to display the entire message information should some form of
          duplication occur.  This is handled on a conference by conference
          basis.  Please refer to the section on Conference Management,
          SEEN-BY: line processing for additional information.

          Normally however, you wouldn't want to leave this option enabled
          because it will clutter up the messages with information and your
          callers will start to complain.  But it is handy for isolating
          certain problems!


          PATH: LINES

          PATH: lines follow the SEEN-BY: lines in the message and operate
          almost identically to them except these lines indicate the route
          (or path) the message has taken to get to your system.  Unlike
          the SEEN-BY: lines, the PATH: lines are not sorted because they
          indicate from left to right the originating system and the
          systems the message encountered before arriving at your system.

          The same <net> inheritance from the previous node address applies
          as well.


          VIEWPKT

          For those of you interested, we have developed a program called
          ViewPKT! that will display the messages in your Netmail directory
          (or any directory you desire) and allow you to select a Netmail
          message.  You can then highlight the desired echomail bundle
          "attachment" and uncompress the contents and permit you to
          display the contents of the actual PKT files.

          This will show in great detail the specifics of each message in
          the PKT file along with specific information about the program
          that created it.  For those that process a lot of mail, this is
          essential for ensuring that mail is created and addressed
          properly!

          For more information, you can download the latest copy from the
          WILDMAIL! support BBS and try it yourself.






          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                       Page  197



          WILDMAIL! v3.01                              MASTER INDEX LISTING
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

          MASTER INDEX LISTING

          Following is a listing of selected words found throughout the
          documentation and their associated page number(s).


          Account balance . . . . . . . . . . . . . . . . . . . . .  85, 95
          Activation date . . . . . . . . . . . . . . . . . . . . . . 95-97
          Active area . . . . . . . . . . . . . . . . . . . . 107, 141, 143
          AKA  31, 35-37, 41, 62, 68, 69, 77, 105, 106, 114, 129, 132, 133,
                                                         139, 140, 142, 157
          ALIAS . . . . . . . . . . . . . . . . . . . . . . .  45, 121, 122
          Aliases . . . . . . . . . . . . . . . . . . . . . . . .  121, 157
          Area name . . . . . . . . . . . .  79, 101-104, 118-120, 131, 145
          AREA: definition  . . . . . . . . . . . . . . . . . . . . . .  51
          AreaRequest  1, 4, 16, 18, 24, 25, 32, 46, 78, 79, 82, 83, 92-94,
                       99, 103, 107, 109, 111, 112, 115-117, 121, 128, 129,
                                                         132, 133, 149, 157
          AreaRequest Flags . 82, 93, 94, 99, 109, 111, 112, 116, 128, 129,
                                                                   133, 157
          AreaRequest security  . . . .  4, 93, 94, 109, 111, 112, 115, 116
          BBS type  . . . . . . . . . . . . . . . . . . . . . .  40, 41, 48
          BinkleyTerm . . . . . . . . . . . . . . . . . . .  1, 10, 24, 184
          Byte count  . . . . . . . . . . . . . . . . . . . . . . . . .  96
          Compression format  . . . . . . . . . . . . . . . . .  61, 70, 89
          Conference number 17, 25, 26, 44, 89, 101-104, 109, 146, 148, 189
          Cost/Byte . . . . . . . . . . . . . . . . . . . . . . . . . .  77
          Cost/Msg  . . . . . . . . . . . . . . . . . . . . . . . . . .  77
          CRASH . . . . . . . . . . . . . . . .  4, 31, 36, 47, 48, 88, 144
          D'Bridge  . . . . . . . . . . . 1, 4, 10, 13, 38, 40, 49, 50, 184
          Deactivation date . . . . . . . . . . . . . . . . . . . . . .  95
          Default address . . . . . . . . . . . . . . . . . . . . . . .  34
          DESQview  . . . . . . . . . . . . . . . . . . . . 27, 59, 60, 155
          Disk space  . . 5, 17, 18, 24, 45, 46, 58, 60, 61, 113, 153, 155,
                                                         156, 181, 192, 195
          Distribution  . . . . . . . . . . .  5, 10, 11, 19, 124, 151, 153
          Downlink nodes  . . 1, 41, 43, 65, 79, 86, 107-109, 113, 115-117,
                                                    124, 126, 129, 156, 193
          Duplicates  . . . . . . . . . . . . . .  13, 26, 54, 73, 114, 195
          Duplication loops . . . . . . . . . . . . . . . . . . 61, 87, 126
          Echo List . . . . . . . . . . . . . . . . 103, 124, 126, 130, 131
          Evaluation  . . . . . . . . . . . . . . . . . . .  5, 8, 153, 154
          Expired . . . . . . . . . . . . . . . . . . . . . . . . . . . . 5
          Extract private mail  . . . . . . . . . . . . . . . . . . . . 107
          Fakenet ID  . . . . . . . . . . . . . . . . . 78, 85, 86, 138-141
          FIDO  . . . . . . . . . . . . . . . . . . . . . . . . 40, 48, 184
          Fidonet . .  1, 35, 68, 85, 86, 102, 130, 136, 137, 154, 179, 190
          File attach . . . . . . . . . . . . . . . . . . . 23, 43, 50, 109



          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                       Page  198



          WILDMAIL! v3.01                              MASTER INDEX LISTING
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

          File attaches . . . . . . . . . . . . . . . . . . 43, 47, 57, 108
          Filter  . . . . . . . . . . . . . . . . . . . . . . . . . . .  89
          Flags . 45, 82, 83, 88, 93, 94, 99, 109, 111, 112, 116, 128, 129,
                                                                   133, 157
          Forward List  . . . . . . . . . . . . . . . . . . . 129, 130, 133
          Four dimensional  . . . . . . . . . . . . . . . .  4, 35, 86, 136
          FROM: name  . . . . . . . . . . . . . . . . . . . . . . . . . 117
          FrontDoor 1, 10, 20, 23, 34, 38, 40, 49, 50, 146, 169-176, 178, 184
          Global Edit . . . . . . . . . . . . . . . . . . . . .  82, 83, 99
          Hold  . . . . . . . . . . . .  4, 8, 27, 51, 54, 60, 88, 123, 131
          Home directory  . . . . . . . . . . . . .  41, 105, 144, 145, 150
          Inbound directory . . . . . . . . . . . . .  5, 22, 41-43, 49, 90
          INTL  . . . . . . . . . . . . . . . . . . . . . . . . . . 57, 157
          INTL kludge . . . . . . . . . . . . . . . . . . . . . . . 57, 157
          InUse flag  . . . . . . . . . . . . . . . . . . . . . . . 70, 149
          KILL/SENT . . . . . . . . . . . . . . . . . . . . . . . . . .  56
          Lock Retry  . . . . . . . . . . . . . . . . . . . . . . . . .  60
          LYNXMAIL! . . . . . . . . . . . . . . . . . . . . . .  38, 49, 50
          Mail archive  1, 22, 49, 55, 56, 60, 61, 70-72, 78, 88-91, 183, 195
          Mail archives . . . . . . . . . .  25, 39, 49, 56, 58, 70, 90, 91
          Mailer  . . 1, 23-25, 34, 38, 39, 46, 48-50, 56, 57, 61, 88, 127,
                                 135, 169, 171, 173, 175, 178, 179, 184-186
          Mailer type . . . . . . . . . . . . . . . . . . . . .  24, 38, 39
          MAKEWILD  . 22, 24, 34, 44, 45, 92, 102, 104, 105, 111, 147, 156,
                                                                   188, 190
          Memory  . . . . . . . . . . 27, 28, 30, 58, 59, 65, 155, 187, 194
          Message count . . . . . . . . . . . . . . . .  24, 26, 45, 95, 96
          MSG . . . . . . . . . . . . 1, 22, 25, 26, 40, 46, 50, 51, 64, 77
          MSGID . . . . . . . . . . . . . . . . . . . . . . . . . . . .  54
          Net  22, 25, 34-36, 44, 57, 66, 67, 73, 84-86, 106, 114, 136-140,
                                                    142, 143, 179, 196, 197
          Node  .  1-5, 22-25, 31, 32, 34-37, 39, 42-44, 57, 60, 62, 66-68,
                            70, 71, 73, 77-79, 81, 82, 84-98, 100, 103-108,
                     110-112, 114-118, 122, 123, 125-129, 131-133, 135-143,
                      145, 150, 156, 172, 179, 181, 184, 185, 186, 196, 197
          Node addresses  1, 2, 39, 42, 43, 66, 68, 73, 77, 79, 81, 82, 84,
                     87, 94-97, 100, 107, 108, 111, 115, 123, 125-127, 129,
                                               132, 133, 139, 156, 181, 196
          Notify  . . . . . . . . . . . . . . . . . . . .  25, 44, 126, 127
          Null messages . . . . . . . . . . . . . . . . . . . . 56, 57, 157
          Offline . . . . . . . . . . . . . . . . . . . . . . . 42, 76, 135
          Opus  . . . . . . . . . . . . . . . . . . . . . . . . . . . .  40
          Origin address  .  4, 33, 36, 66, 68, 73, 105, 114, 141, 143, 148
          Origin line . 3, 4, 32, 33, 37, 38, 73-76, 79, 106, 145, 148, 196
          Outbound mail . 1, 5, 13, 21, 24, 34, 38, 39, 49, 50, 54, 55, 62,
                                           70, 71, 85, 88, 90, 91, 138, 145
          Packet  . . . . . 43, 54, 55, 76, 78, 92, 135, 138, 139, 149, 151
          Passthru  . . . . . . . . . . . . . . . . . . .  54, 79, 103, 125



          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                       Page  199



          WILDMAIL! v3.01                              MASTER INDEX LISTING
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

          Password  . . .  4, 44, 91, 92, 117, 118, 120, 124-126, 129, 132,
                                                     158-162, 165, 166, 167
          PATH  4, 5, 13, 23, 26, 31, 41-43, 48-52, 58, 64, 65, 71, 72, 90,
                      109, 113, 121, 123-125, 130, 131, 144, 158, 159, 161,
                                                     163-165, 172, 196, 197
          Path definition . . . . . . . . . . . . . . . . . . . . . . 4, 43
          Peer-to-peer  . . . . . . . . . . . . . . . . . . . . . . . .  59
          PKT . 1, 4, 5, 23, 41, 43, 54, 55, 60-62, 65, 71, 78, 85, 86, 88,
                 90, 91, 92, 96, 97, 104, 108, 137, 138, 149, 156, 195, 197
          PKT count . . . . . . . . . . . . . . . . . . . . . . . .  96, 97
          PKT password  . . . . . . . . . . . . . . . . . . . . . . . .  91
          Point .  7, 12, 13, 18-20, 22, 25, 34-36, 38, 44, 57, 60, 61, 66,
                             67, 73, 78, 84-86, 106, 135-143, 145, 179, 192
          PointNet  . . . . . . . . . . . . . . . . . . . . . . . . 86, 137
          Pre-processing  . . . . . . . . . . . . . . . . . . . . . . 41-43
          Primary address . . . . . . . . . . 34, 36, 61, 68, 114, 140, 142
          PURGE . . . . . . . . . . . . . . . . . 22, 24, 45, 122, 123, 192
          Purge areas . . . . . . . . . . . . . . . . . . . . . .  122, 123
          Purge file  . . . . . . . . . . . . . . . . . . . . . . . . . 123
          Quiet archiving . . . . . . . . . . . . . . . . . . . . . . .  62
          Rescan  . . . . . . . . . . . . . . .  25, 49, 113, 118, 125, 126
          Restrict import . . . . . . . . . . . . . . . . . . . . .  4, 108
          Scheduled . . . . . . . . . . . . . . . . . . . . . . . .  24, 42
          SEENBY  . . . . . . . . . . . . . . . . .  4, 5, 41, 87, 114, 145
          Selected conferences  . . . 78, 84, 88, 89, 94, 96, 112, 125, 145
          Standard naming convention  . . . . . . . . . . . . . . . . . 189
          SUBJECT:  . . . . . . . . . . . . . . . . . . .  56, 124-126, 156
          Swap file . . . . . . . . . . . . . . . . . . . . . . . . . 4, 58
          Tear line . . . . . . . . . . . . . . . . . . . . . . . . 76, 119
          TO: field . . . . . . . . . . . . . . . . . . . . . . . . . .  44
          Type 2  . . . . . . . . 4, 78, 79, 85, 86, 138, 139, 141-143, 149
          Type 2.2  . . . . . . . . . . . . . . 85, 138, 139, 142, 143, 149
          Uplink  . 1, 2, 4, 23, 35, 106-108, 122, 124, 127, 129, 131, 132,
                                                              141, 143, 149
          WILDCAT! conference . . . . . . . 79, 102-105, 109, 144, 154, 156
          WM.ID . . . . . . . . . . . . . . . . . . . . . . . . . . . . 154
          XMS/EMS . . . . . . . . . . . . . . . . . . . . . . . . . 58, 155
          Zone  . 4, 22, 25, 34-36, 44, 57, 66-69, 73, 77, 84-87, 106, 114,
                            135, 136, 137-140, 142, 143, 149, 157, 179, 196
          Zone matching . . . . . . . . . . . . . . . . . . . 4, 36, 66, 68











          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          Revised: 06/25/93                                       Page  200