The other file in this ZIP, PSLWGS.PSF, contains version 1.2 of
some PostScript code that allows control over gray scale and minimum
line width on a color-by-color basis for monochrome PostScript output
using the AutoCAD Release 12 PSOUT command.  It's been tested on an
NEC Silentwriter 90 and an Agfa 2400 dpi PostScript printer.
PSLWGS.PSF requires AutoCAD Release 12 (or higher).
    PSLWGS defines a minimum line width in inches for each AutoCAD
color. Entities with explicit widths (for example, plines) that are
greater than the minimum for that color will be printed with their
explicit width (this assumes interpreting AutoCAD drawing units as
inches).  In some cases some lines will be wider than desired (for
example, blocks inserted with X and Y scale factors that are not
equal in magnitude).
    Due to limitations in the way AutoCAD handles the PSOUT command
and the PSPROLOG system variable, it's not particulary convenient to
change line widths and gray scales.  I hope this will improve in the
future.  For now, you must edit either ACAD.PSF or each individual
.EPS file produced by PSOUT to change the line widths or gray scales. 
Changes in ACAD.PSF affect all files produced by PSOUT after the
change; changes in an .EPS file produced by PSOUT affect only that
file.
    Currently, PSLWGS only supports portrait output.  This means
that lines that are vertical on the AutoCAD screen will be parallel
to the long edge of the paper when printed.  If you're doing PSOUT to
import to another program and need another orientation, the program
into which you're importing the .EPS file amy be able to rotate it.

    To use this file:

I.  Initial setup:

    A.  Locate the file ACAD.PSF.  It's probably in the SUPPORT 
        subdirectory of your AutoCAD directory.
    B.  Use an ASCII text editor to insert PSWLGS.PSF at the end
        of ACAD.PSF.  (ACAD.PSF is covered in the Release 12
        "Customization Manual" on pages 228-232).
    C.  If you will normally use line widths other than 0.001" (note
        that a 300 dpi printer does line widths in units of 0.0033"),
        change the values in LGP_colortowidth (see step C, below) to
        be your most common linewidth settings.

II.  Using PSLWGS.PSF

    A.  In the Autocad drawing editor, set the PSPROLOG system
        variable to point to lw_gs_prolog.  NOTE THAT THIS IS
        CASE SENSITIVE!  You can do this by typing:

              psprolog lw_gs_prolog<Enter>

        (Note that PSPROLOG is saved in ACAD.CFG and not with the
        drawing.  This means that this setting will apply to all
        your drawings until you change it).

    B.  Perform a PSOUT command.

    C.  IF you want to change the line widths from the defaults
        (0.001" if you haven't changed them), use an ASCII text
        editor to edit the resulting .EPS file. Near the beginning
        of the file you'll find:

         /LGP_colortowidth
           [
             0.001          % Color 1 (red)
             0.001          % Color 2 (yellow)
             0.001          % Color 3 (green)
             0.001          % Color 4 (cyan)
             0.001          % Color 5 (blue)
             0.001          % Color 6 (magenta)
             0.001          % Color 7 (white)
             0.001          % Color 8
             0.001          % Color 9
             0.001          % Color 10
             0.001          % Color 11
             0.001          % Color 12
             0.001          % Color 13
             0.001          % Color 14
             0.001          % Color 15
           ] def

         Change the numbers as desired.  The units are inches. Note
         that on a 300 dpi printer, the minimum line width is 0.003333
         inches; any specified line width that's less than that will
         come out as 0.003333 inches.

         Just below this section you'll find:

         /LGP_colortogray
           [
             0            % Color 1 (red)
             0            % Color 2 (yellow)
             0            % Color 3 (green)
             0            % Color 4 (cyan)
             0            % Color 5 (blue)
             0            % Color 6 (magenta)
             0            % Color 7 (white)
             0            % Color 8
             0            % Color 9
             0            % Color 10
             0            % Color 11
             0            % Color 12
             0            % Color 13
             0            % Color 14
             0            % Color 15
           ] def

         Again change thise numbers as appropriate.  0 or 0.0 is
         black; 1 or 1.0 is white (invisible, but it may overwrite
         black or gray stuff depending on the order of drawing); 0.5
         is 50% gray, and so forth.

    D.  Save the file and copy it to your output device.


Jon Fleming

CIS:     70334,2443


REVISION HISTORY:

1.0 Initial release
1.1 Fixed bug of leaving an object on the stack after the entire
    procedure finished
1.2 (13 Jul 93) Fixed bug of desired line width not saved and
    restored with graphics state.  This manifested as "persistent
    polyline widths"; when a polyline with explicit width greater
    than the minimum was printed, all subsequent strokes were at the
    same width as the polyline until a color change or another
    polyline came along.