@(#)hdsinfo.doc  1.4 

HDS-300 Commands for IBM PC/AT
==============================
  By John Elliott, Motorola Development Systems, Austin, TX

1. Purpose

   The HDS-300 Commands for IBM PC/AT provide a useful method for
   transferring binary and ASCII files between an IBM PC/AT and a
   Motorola HDS-300 Hardware Development Station (CP/M-68K).  This
   provides a path for modem file transfers using the PC/AT with
   any type of communications software and also allows usage of
   more powerful editors for editing HDS-300 macro files.

2. Installation
   a. The files needed are listed below.  Delete all prior versions.

        Filename      Vers.  Description
        ------------  -----  -------------------------------------------
        HDSINFO.DOC          This information file you're reading now.
        HDSDEL.EXE     1.0   Deletes HDS-300 file command.
        HDSDIR.EXE     1.0   Directory for HDS-300 diskettes command.
        HDSREAD.EXE    1.0   Copies (reads) HDS-300 file to DOS file
                              command.
        HDSTYPE.EXE    1.0   Display HDS-300 file contents command.
        HDSWRITE.EXE   1.0   Copies (writes) DOS file to HDS-300
                              diskette command.

    b. An IBM PC/AT (or 100% compatible) with high capacity (1.2 MB)
       5-1/4" floppy disk drive is required.

    c. Place all the HDS*.EXE files in your execution directory, e.g.
       \BIN.  The HDSINFO.DOC file is not required to execute the
       commands.  It is for informational purposes only.
       
                                -- NOTE --
           The MS-DOS "PATH" command must be properly set  so  it
           can find the directory where the HDS*.EXE files reside.

3. Bugs Fixed
   a. Directory read/write problems have been resolved.

4. Known Bugs
   a. HDSWRITE.EXE:
        - Does not work reliably if you fill the HDS-300 disk beyond its
          storage capacity (624K).
        - Does not properly handle subdirectories in the source filename.
        - Sometimes gives "File not found" error, when in fact, the file
          does exist.  Re-issuing the command always seems to work.
   b. HDSDIR.EXE:
        - Does not report the proper amount of free space available.  It
          shows 4K more than what is actually available.  Remember, disk
          space is allocated in 2K "blocks", i.e. a 10 byte file actually
          occupies 2K of disk space, a 2050 byte file occupies 4K of disk
          space, etc.

5. Command Syntax

   The following descriptions are presented in the structure of the
   HDS-300 Commands Reference Manual.  If any command is invoked
   without any arguments, a one-line command syntax description along
   with the command version number is displayed.  The first release of
   these commands did not display any version number when invoked
   without any arguments.  Thus version 1.0 is really the second release.

   Wildcard characters are permitted in DOS and HDS-300 filenames
   as per their usual conventions.


   HDSDEL       Delete HDS-300 file
   --------------------------------
     Description:
        The HDSDEL command allows files on a HDS-300 diskette to be
        deleted from the diskette.

     Syntax:
        HDSDEL  <drive>[user]:[<filespec>]

     where:
        <drive>      selects the IBM PC/AT drive in which the HDS-300
                     diskette has been inserted.

        <user>       is the optional CP/M-68K user number for <filespec>.
                     Legal values are 0-15, with 0 as the default.

        <filespec>   is the HDS-300 filename to be deleted.

     Examples:
        HDSDEL  A:TEST.MAC   Deletes the TEST.MAC file on the HDS-300
                             diskette in drive A: of the IBM PC/AT.

        HDSDEL  A9:TEST.SCR  Deletes the TEST.SCR file under user 9 on
                             the HDS-300 diskette in drive A: of the
                             IBM PC/AT.



   HDSDIR       Disk directory
   ---------------------------
     Description:
        The HDSDIR command allows filenames on a HDS-300 diskette to
        be displayed.

     Syntax:
        HDSDIR  <drive>[user]:[<filespec>]  [/W]  [/P]

     where:
        <drive>      selects the IBM PC/AT drive in which the HDS-300
                     diskette has been inserted.

        <user>       is the optional CP/M-68K user number for <filespec>.
                     Legal values are 0-15.  If omitted, all user numbers
                     are searched.

        <filespec>   is an HDS-300 filename.

        /W           is the normal MS-DOS option to produce a wide dis-
                     play of the directory.

        /P           is the normal MS-DOS option to pause when the screen
                     is full.

     Examples:
        HDSDIR  A:           Lists all files for all user numbers on the
                             HDS-300 diskette in drive A: of the IBM PC/AT.

        HDSDIR  A3:*.MAC     Lists all macro files under user number 3
                             on the HDS-300 diskette in drive A: of the
                             IBM PC/AT.

        HDSDIR  B: /P        Lists all files for all user numbers on the
                             HDS-300 diskette in drive B: of the IBM PC/AT
                             and pauses when the screen becomes full.



   HDSREAD      Copy HDS-300 file to DOS File
   ------------------------------------------
     Description:
        The HDSREAD command allows files on a HDS-300 diskette to be
        copied to MS-DOS.  It follows a command format similar to the
        MS-DOS "COPY" command.

     Syntax:
        HDSREAD  <drive>[user]:[<filespec>]  <DOS_path>

     where:
        <drive>      selects the IBM PC/AT drive in which the HDS-300
                     diskette has been inserted.

        <user>       is the optional CP/M-68K user number for <filespec>.
                     Legal values are 0-15, with 0 as the default.

        <filespec>   is an HDS-300 filename to be read.

        <DOS_path>   is the MS-DOS destination path to be written.

     Examples:
        HDSREAD  A:USERINIT.MAC  C:    Copies the USERINIT.MAC file on
                                       the HDS-300 diskette in drive A:
                                       of the IBM PC/AT to a DOS file
                                       on drive C:.

        HDSREAD  A6:TMP.MAC  TST.MAC   Copies the TMP.MAC file under user
                                       number 6 on the HDS-300 diskette
                                       in drive A: of the IBM PC/AT to a
                                       DOS file named TST.MAC on the
                                       default drive.

        HDSREAD  B:BIG.MAC  .          Copies the BIG.MAC file on the
                                       HDS-300 diskette in drive B: of
                                       the IBM PC/AT to a DOS file on
                                       the current drive/directory.



   HDSTYPE      Display HDS-300 file contents
   ------------------------------------------
     Description:
        The HDSTYPE command allows the contents of files on a HDS-300
        diskette to be displayed.  It follows a command format similar
        to the MS-DOS "TYPE" command.  With this command, HDS-300 text
        files (.MAC, .SCR, .LOG) may be examined on the HDS-300 diskette
        without first copying them over to MS-DOS.

     Syntax:
        HDSTYPE  <drive>[user]:[<filespec>]

     where:
        <drive>      selects the IBM PC/AT drive in which the HDS-300
                     diskette has been inserted.

        <user>       is the optional CP/M-68K user number for <filespec>.
                     Legal values are 0-15, with 0 as the default.

        <filespec>   is an HDS-300 filename to be read.

     Examples:
        HDSTYPE  A:USERINIT.MAC      Displays the USERINIT.MAC file on
                                     the HDS-300 diskette in drive A:
                                     of the IBM PC/AT on the console.

        HDSTYPE  A15:TEST39.SCR      Displays the TEST39.SCR file under
                                     user 15 on the HDS-300 diskette in
                                     drive A: of the IBM PC/AT on the
                                     console.



   HDSWRITE     Copy DOS file to HDS-300 Diskette
   ----------------------------------------------
     Description:
        The HDSWRITE command allows DOS files to be copied to a
        HDS-300 diskette.  It follows a command format similar to the
        MS-DOS "COPY" command.

     Syntax:
        HDSWRITE  <DOS_path>  <drive>[user]:[<filespec>]

     where:
        <DOS_path>   is the MS-DOS source path to be read.

        <drive>      selects the IBM PC/AT drive in which the HDS-300
                     diskette has been inserted.

        <user>       is the optional CP/M-68K user number for <filespec>.
                     Legal values are 0-15, with 0 as the default.

        <filespec>   is an HDS-300 filename to be written.

     Examples:
        HDSWRITE  C:USERINIT.MAC  A:   Copies the USERINIT.MAC file on
                                       DOS drive C: to the HDS-300
                                       diskette in drive A: using the
                                       same filename.

        HDSWRITE  TMP.MAC  A5:TST.MAC  Copies the TMP.MAC file on the
                                       default DOS drive to the HDS-300
                                       diskette in drive A: under user
                                       number 5 using the filename
                                       TST.MAC.



4. Restrictions

   a. It is not physically possible to format an HDS-300 diskette in
      an IBM PC/AT drive.  Therefore, all formatting of HDS-300 disk-
      ettes MUST be done on the HDS-300 station using the supplied
      OFFLINE UTILITIES diskette for the matching SYSTEMS disk.  The
      boot track was changed for later releases, so to ensure a boot-
      able diskette, always use the matching UTILITIES diskette.

   b. When using a DOS based editor to edit HDS-300 macro files, the
      following cautions should be noted:
        1. A proper HDS-300 macro file is terminated with a CONTROL-Z
           (^Z) end-of-file character.  It is preferred to always end
           a macro file with a string of "******"s starting in column
           one.  This prevents possible end-of-file problems.

        2. A macro file can only have up thru 78 characters on any
           single line.  Some older versions only allow up to 77 char-
           acters per line.  Lines longer than the allowed limit will
           cause macro execution to halt.  Expansion of local symbols
           can also cause lines to become too long, so be careful.

        3. The HDS-300 software only accesses files under user number
           0.  Therefore, any files written to other user numbers will
           not be accessible by the HDS-300 software.  User number
           capability is provided for general CP/M-68K support.

**EOF**