Michael,

DAK's number is 800-788-7808, and the item number for
Microsoft Works Ultralite is 5826, currently sellnig for $29.90,
which includes the manuals, as you predicted.

Macronix's number is 800-432-1621, and they sell the serial cable
as part numbe MXA-000010, the MAXLITE/PC RS-232 cable, for $12.00.

The instructions for how to change the cluster size on your silicon
drive are as follows:

  1.  get all your files safely off the ultralite
  2.  pull out the silicon drive and wait 5 minutes to be sure it
      has forgotten everything it knows
  3.  re-insert silicon drive, boot ultralite, perform the standard
      disk init sequence "Initialize, Format, Setup Manager". In the event
      you have problems with "NON-SYSTEM DISK" messages and the machine won't
      boot, try using FILE MANAGER on D: to initialize C: then break out of the
      FILE MANAGER and format C: without the /S switch that makes it a system
      disk.
  4.  Now use laplink to get a disk sector editor onto the machine.
      I am using "YASE.EXE", which I am sending to you with this
      message.
  5.  Run YASE, tell it to use drive C, make sure you are
      looking at sector 0.
  6.  Using the L key (press it 13 times), move to offset 00d, that's 13 in 
      decimal.  It should currently say 08 as its value.  This means 8 
      sectors-per-cluster, or 4K.
  7.  Use E (Edit cursor position) to change this value to 02, 2 
      sectors-per-cluster, which is 1K.
  8.  Using the L key (press it 9 times) move to offset 016, that's 22 
      in decimal.  If you have a 1Meg drive, the value should currently 
      read 01; if you have a 2Meg drive it should currently read 02.  
      This value is the number of sectors in a FAT.
  9.  If you have a 1Meg drive, set the value to 03.
      If you have a 2Meg drive, set the value to 08.
      [Warning: I don't understand why this value matters, but I tested
       my ultralite with a 2Meg drive but setting this value to 03 and
       when I created lots of files the disk got corrupted.  However, with
       08 my machine seems to work fine.  The parameters given above were
       supplied to me by brian@theory3.caltech.edu.]
 10.  Write out sector 0.
 11.  Reboot the ultralite using control-alt-FUNCTION-delete to use drive D.
 12.  Perform the standard "Initialize, Format, Setup manager" sequence.
      [Note: It seems odd to me, but this uses the values from sector 0; I
       would have expected this procedure to start from scratch.]
 13.  Now try out drive C:, it should be using 1K blocks.  You can tell this
      by creating a short file and running DIR and looking at how much the
      available space went down.

To use YASE.EXE for editing sector 0, hit C when it starts up to pick
drive C, then hit ? for help on using the keyboard commands.

Hope this helps,

  --Jim O'Toole
  Phone: 617-253-6018
  Internet: otoole@mit.edu