The Western Digital Corporation's
    
                         Field Applications Engineering
    
                         Document for WDTYPES.EXE Utility

                         (C) 1993 Western Digital Corp.
    
            This document is intended to accompany the WDTYPES.EXE utility
            placed on this BBS for your convenience. First our disclaimer:
    
            Western Digital assumes no liability for the fitness, operation
            or results of this program. It was created solely for systems
            integrators' use in configuring an AT compatible computer.
    
            Now that that's out of the way, we shall go on ...
    
            This utility is intended to aid beginners or those stuck with
            undocumented equipment in the installation of Western Digital's


    

    


            hard disk controllers and / or drives in most AT compatible
            computers.
    
            When loaded, the utility will scan the entire 64K page of BIOS
            memory for a configuration that matches the original AT's
            drive type #1. This drive was defined as follows :
    
                    306 cylinders
                    4   heads
                    17  sectors per track
    
            This specific signature is searched throughout the BIOS area.
            If found, the utility calls this a drive type 1, and proceeds
            to display all other valid drive type tables. Many BIOS
            companies have nonsensical ones included in a string of valid
            configurations. The program is trained to ignore those types
            that have zero heads or cylinders, and to stop the search when
            a larger than 2047 cylinder or 16 head type is found.


    

    


    
            In the event a match for the 10 Megabyte drive test fails, the
            program will search for a 20 Megabyte drive of the following
            configuration :
    
                    615 cylinders
                    4   heads
                    17  sectors per track
    
            Several versions of BIOS were distributed with this configuration
            as the first drive type.
    
    







    

    


    
                            IN CASE OF DIFFICULTY ...
    
    
            To verify the findings of this utility, run your system's
            SETUP utility and define a hard drive type 1. Your hard drive
            can then be installed ( ... if it has at least 4 heads and 306
            cylinders ...) and it should function as a 10 Megabyte hard
            drive. The DOS utility FDISK should report 305 ( or 304 )
            cylinders.
    
                                 REMEMBER ...
    
            You can only use a drive type that meets the following :
    
                    1) LESS than or EQUAL TO the actual number of
                       CYLINDERS on the drive you are trying to
                       install.


    

    


    
                    2) EQUAL TO the actual number of HEADS on the
                       drive you are trying to install.
    
                    3) EQUAL to the SECTORS PER TRACK of BOTH THE
                       DRIVE AND CONTROLLER !!
    
                       ST-506 MFM DRIVES & CONTROLLERS HAVE 17 SECTORS
                       ST-506 RLL DRIVES & CONTROLLERS HAVE 26-31 SECTORS *
                       ESDI DRIVES AND CONTROLLERS HAVE 17-54 SECTORS  *
    
            * Western Digital manufactures controllers that have ON-BOARD
              BIOS ROMS to accept other than motherboard BIOS drive
              configurations. Contact your dealer.
    





    

    


    
    
            Below is an example of the program in operation:
    
    
    Scanning system BIOS for an AT drive type 1 ... PLEASE STAND BY ...
    
    
    
    
    
    
    







    

    


      TYPE    CYLINDERS    HEADS     PRECOMP     LAND ZONE    SECTORS      MEG
    
       1         306         4         128          305         17          10
       2         615         4         300          615         17          20
       3         615         6         300          615         17          30
       4         940         8         512          940         17          62
       5         940         6         512          940         17          46
       6         615         4         65535        615         17          20
       7         462         8         256          511         17          30
       8         733         5         65535        733         17          30
       9         900         15        65535        901         17          112
       10        820         3         65535        820         17          20
       11        855         5         65535        855         17          35
       12        855         7         65535        855         17          49
       13        306         8         128          319         17          20
       14        733         7         65535        733         17          42
    
    Press space bar to see other drive types ...


    

    


    
      TYPE    CYLINDERS    HEADS     PRECOMP     LAND ZONE    SECTORS      MEG
    
       15        0           0          0            0           0          0
       16        612         4          0            663         17         20
       17        977         5          300          977         17         40
       18        977         7          65535        977         17         56
       19        1024        7          512          1023        17         59
       20        733         5          300          732         17         30
       21        733         7          300          732         17         42
       22        733         5          300          733         17         30
       23        306         4          0            336         17         10
       24        0           0          0            0           0          0
       25        615         4          0            615         17         20
       26        1024        4          65535        1023        17         34
       27        1024        5          65535        1023        17         42
       28        1024        8          65535        1023        17         68
       29        512         8          256          512         17         34


    

    


       30        615         2          615          615         17         10
    
    Press space bar to see other drive types ...

















    

    


    
      TYPE    CYLINDERS    HEADS     PRECOMP     LAND ZONE    SECTORS      MEG
    
       31        989         5          0           989          17         41
       32        1020        15         65535       1024         17         127
       33        0           0          0           0            0          0
       34        0           0          0           0            0          0
       35        1024        9          1024        1024         17         76
       36        1024        5          512         1024         17         42
       37        830         10         1792        830          17         68
       38        820         10         65535       821          17         68
       39        615         4          128         664          17         20
       40        615         8          128         664          17         40
       41        917         15         65535       918          17         114
       42        1023        15         65535       1024         17         127
       43        823         10         512         823          17         68
       44        820         6          65535       820          17         40
       45        1024        8          65535       1024         17         68


    

    


       46        925         9          65535       925          17         69
    
    Press space bar to see other drive types ...

















    

    


    
      TYPE    CYLINDERS    HEADS     PRECOMP     LAND ZONE    SECTORS      MEG
    
       47        699         7          256         700          17         40
    
    End of drive tables ... press space bar to return to system ...
    
            You merely select the type number that best matches your
            hard drive, and run your manufacturer's SETUP program.
    
            The next step is to run a LOW-LEVEL FORMAT utility. If one
            is needed, we recommend the WD utility WDFMT, located
            elsewhere on this BBS. The WDFMT utility will prompt you for
            the ACTUAL parameters of the hard drive you are installing.
    
            If you are unsure of your drive's parameters, a file called
            DRIVES.LST is available on this TBBS to assist you in most
            of the popular (and some unpopular) hard drives.


    

    


    
            If you still need assistance ...
    
            WESTERN DIGITAL 24 HOUR TECH SUPPORT ==> 1-800-777-4787