ELX - EaziLink Xmodem external file transfer protocol
   -----------------------------------------------------

   ELX is supplied for use with our EaziLink communications package and
   may be used to upload and download files to and from most BBSs.

   Xmodem is the most basic and most common file transfer protocol and
   when installed as an EaziLink external protocol, will enable the user
   to download more exotic external protocol drivers such as DSZ (tm).

   ELX first 'negotiates' with the remote Xmodem for CRC error correction
   and only if the remote protocol does not support CRC will ELX default
   to Checksum error correction.  ELX can therefore be used, unaltered,
   with remote Xmodem protocols which support either one or both of the
   correction methods.  Please note that when ELX is used at the host end
   of a link, it waits 10 seconds before sending it's first signal to
   attempt to agree CRC error correction with the originator.  If no
   response is received within the next ten seconds the signal is sent
   once more.  If the originator's Xmodem is not ready to receive within
   this time it will miss the CRC signals and Checksum error correction
   will be used instead.  ELX uses a block size of 128 bytes by default
   but will also receive (Download) 1K blocks from a remote service which
   offers the Xmodem-1K protocol.

   The form of invokation is:

      Send -   ELX Sn filename.ext
   Receive -   ELX Rn filename.ext

   Where n is the number of the serial port to be used.

   For use with EaziLink the full EAZILINK.PRO entries would be as follows:

   name Xmodem
   hotkey X
   upload ELX.EXE S%port %file
   download ELX.EXE R%port %file

   ELX monitors the carrier signal and will abort if the carrier is lost
   during file transfer.  File transfer can be aborted by the user at any
   time by pressing the [ESC] key.


   - NOTE -

   ELX has not been designed as a stand alone protocol.  It expects the
   comms port to have been set up by the main communications package which
   should then run ELX as a child process or from a DOS shell.  ELX has
   been designed for use with EaziLink and we do not guarantee that it will
   work with other communications packages although, in many cases, it
   probably will.