SUPER MORSE (TM)
                                        ADVANCED TOPICS
          
                                            Ver. 4.10
                                         Copyright 1994
                                          M. Lee Murrah
          
                                             2-19-94
          
          
          
          1. How Morse Code Is Defined..................................   1
               a.DITS and DAHS..........................................   1
               b. Morse Characters......................................   1
               c. Code Weighting........................................   2
               d. Code "Speed"..........................................   2
               e. The "Farnsworth" Method...............................   3
          2. Learning the Morse Code....................................   3
               a. The Super Morse Teaching Method.......................   3
               b. Studying Hints........................................   4
          3. Scripted Disk Files........................................   5
               a. The Message Command...................................   6
               b. The Pause Command.....................................   6
               c. Set Speeds Command....................................   6
               d. Restore Speeds Command................................   6
               e. Speed Lock Commands...................................   6
          4. Customization of External Files............................   7
               a. General...............................................   7
               b. Data Files............................................   7
               c. License Classes File..................................   8
               d. Text Files............................................   8
          5. QSO Templates..............................................   8
          6. Equipment and System Requirements and Limitations..........  10
               a. System Configuration..................................  10
               b. Mouse.................................................  10
               c. Code Speed Calibration................................  10
               d. Video Display Card....................................  10
               e. Disk Cache Programs...................................  11
               f. Floppy Disk Write Protect Tabs........................  11
               g. Windows Capability....................................  11
               h. Speaker Volume........................................  11
          7. Sound Boards...............................................  11
          8. Interfacing External Equipment.............................  12
          9. Circuit Diagrams for External Connections..................  13
               a. Using an External Hand Key............................  13
               b.  Connecting to a Receiver.............................  14
               c. Driving a Transmitter or Other Device.................  14
               d. Using a Volume-Controlled Headphone...................  16
               e. Using an External Oscillator..........................  17
               f. Using an External Sound Output........................  18


                                                                      Page 1
               This file contains information on selected advanced
          features of Super Morse. See QUICK.DOC for basic information and
          and overview of Super Morse.
          
          
          1. How Morse Code Is Defined
          ----------------------------
          
               a.DITS and DAHS
               ---------------
          
               Morse code is a sound language that uses two different
          lengths of a single tone in various combinations to represent
          all the characters of the Morse alphabet. These two tones are
          distinguished by their length, one a "short" tone and t he other
          a "long" tone. The short tone is phonetically referred to as
          "DIT", and the long tone as "DAH".  "DIT" is usually written as
          "DI" when it is not the last element of a character. You will
          often see the short tone represented as a "." (dot) and th e long
          tone as a "-" (dash), but it is commonly agreed that use of these
          symbols encourages a visual approach to the code, which slows
          code learning.  You should never think of the Morse code as dots
          and dashes or write it in that way!
          
               The original Morse code as used in landline telegraphy was
          represented by a combinations of timed clicks.  However, when
          radio came into use, the code was revised to use tones which are
          more suited for radio use. The original Morse code is used in la
          nd telegraphy is called the American Morse code, but the code now
          commonly used in radio is called the International Morse code.
          
               b. Morse Characters
               -------------------
          
               The amateur radio Morse code set is a subset of the
          international Morse code.  It uses a reduced character set of
          the 26 letters, the 10 numerals, 4 punctuation marks and 5
          special procedure signs.  The Morse character set support ed by
          Super Morse is shown in the several figures that follow.
          
               The printable Morse characters are shown in Fig. 1-1.  The
          International Morse code that is used in amateur radio supports
          a number of punctuation marks, but the amateur subset uses only
          the five shown in Fig. 1-1.
          
               Morse code communications uses several special characters
          that convey procedural information in shorthand.  These are often
          longer characters that can be viewed as combinations of
          alphabetic characters without an intervening character space. The
          mos t common of these procedure signs, or "prosigns", used in
          amateur radio are shown in Fig. 1-2.  <KA> and <SN> along with
          <BT> are frequently used in traffic handling.
          


                                                                      Page 2
               Several international characters are used in Morse code,
          especially in Europe.  These characters shown in Fig. 1-3. are
          also supported by Super Morse in some modes:
          
               c. Code Weighting
               -----------------
          
               The various elements of Morse code are defined in relation
          to each other. The DIT is assigned the shortest duration and is
          defined as being one time unit in duration, and a DAH is 3 times
          as long as a DIT, or 3 time units in duration .  The silence
          between DITs and DAHs in a character, which we will call an
          "element space" is the same length as a DIT, i.e., one time unit
          in duration.  The silence between characters, which we will call
          a "character space", is 3 time units in duration. Finally, the
          space between words, which we will call a "word space" is 7 time
          units in duration.
          
               Perfectly sent code uses these standard relationships, but
          code is not usually perfectly sent except when a computer is
          used. Each person who sends code manually, develops a weighting
          slightly different from the standard, and this unusual weighting
          is said to constitute the operator's very recognizable "fist".
          
               Operators who use automatic keyers can usually set the
          weighting as a personal preference.  Weighting very far from the
          standard sound choppy and hard to copy.
          
               d. Code "Speed"
               --------------
          
               The speed of Morse code is measured in words per minute
          (WPM). Code speed is an elusive measure since words are of
          various lengths; and when random characters are being sent, there
          are no words at all!
          
               Code speed has therefore been arbitrarily defined by
          standard words.  The standard word for plain text is "PARIS",
          which, if you add up the time units in all the code sound
          elements used to send "PARIS" (DITs, DAHs, and spaces between the
          DIT's and D AHS, characters and words), you will find that it is
          50 units of time long.  One word per minute is defined as sending
          "PARIS" using code elements timed to fill one minute, including
          the word space following the last word.  Ten words per minute
          would be s ent at a speed necessary to send "PARIS" 10 times in
          one minute.  The code elements are calibrated at any particular
          speed against "PARIS", and when text is sent at, say, 10 words
          per minute, more or fewer actual words may be sent depending
          upon their len gth.
          
               The word "PARIS" will not work for random characters since
          the average Morse code character used to send English text is
          shorter than the average character used to send random
          characters.  This is because English does not use all the letters


                                                                      Page 3
          in equal numbers and because Morse code assigns the shortest
          codes to the most frequently used letters in English.  The most
          frequently used letter in English is "E", and it is assigned the
          shortest code, the DIT.  A less frequently used letter such as
          "Q" is ass igned a longer code, DAH DAH DI DAH.
          
               For random characters, therefore, the standard word "CODEX"
          was chosen. If you analyze "CODEX", you will find that it
          contains 60 code elements. The effect of this difference is that
          the DITS and DAHS in randomly sent characters should sound about
          20 % shorter than those in plain text at the same nominal speed.
          Randomly sent characters therefore should sound 20% faster that
          plain words.  This is the reason that manufacturers of code
          tapes can boast that the actual test will seem slow after using
          thei r random character tapes!
          
               e. The "Farnsworth" Method
               --------------------------
          
               Morse code is usually sent with the standard relationship
          between character spaces and the elements which make up the
          character.  In other words, the DITS, DAHS and element spaces are
          sent according to the same speed standa rd.  However, Farnsworth
          discovered that code learning can be accelerated if the DITs,
          DAHs and element spaces are compressed as if the code were being
          sent at a high speed while the character spaces are expanded to
          maintain an overall lower send speed. This is called the
          "Farnsworth method", and it is endorsed by the ARRL as the best
          way to learn the code.
          
               The Farnsworth method is supported and is used as the
          default method by Super Morse.  Two Farnsworth speeds are
          provided.  The "Lo" Farnsworth speed, preset at 18 WPM, is used
          at send speeds below 20 WPM; and the "Hi" Farnsworth speed,
          preset at 26 W PM, is used above 20 WPM. Beware, however, that
          not all code tests are given in the Farnsworth format, or, if
          they do, using these speeds ! Check with your testing
          coordinator to determine which method will be used, and then use
          that system when studying with Super Morse.
          
          
          2. Learning the Morse Code
          --------------------------
          
               a. The Super Morse Teaching Method
               ----------------------------------
          
               Unlike standard Morse code teaching methods, Super Morse
          does not begin by introducing characters. Instead Super Morse
          starts with sounds only -- characters are not taught or displayed
          in the early lessons.  The idea is to emphasize that Morse code
          is a sound language and to teach the fundamentals of code sound
          s. Two sound-only exercises are provided. First, the basic DIT
          and DAH sounds are taught. Second, Super Morse puts the basic


                                                                      Page 4
          sounds together into the four fundamental two-sound combinations.
          
               Only after the basic sounds and sound combinations are
          taught does Super Morse start identifying characters.  Before the
          standard code groups are introduced, code "steps", which are
          groups of two similarly sounding characters, are sent to
          gradually i ntroduce the characters in pairs. The idea is to
          teach the student to distinguish similar sounding characters from
          the beginning, such that those which do not sound so much alike
          will fall into place by themselves.  Also the characters are
          slowly learned in an indirect fashion in that the student is
          encouraged to concentrate on the differences rather than the
          content of the characters themselves. Only when the steps are
          completed are the standard code groups introduced.
          
               The Learn selections "DIT/DAH" through "Levels" are ordered
          to slowly build up your knowledge of the characters in a very
          logical way.It is recommended that the Learn subcommands be used
          in the same order as the selections are presented.
          
               b. Studying Hints
               -----------------
          
               There is no one best way to learn the Morse code.  As with
          foreign languages (to which Morse code is similar in some ways),
          some people can learn the code faster than others.  The best
          attribute that one can possess in learning the code is persistenc
          e.
          
               Super Morse implements one method of learning the Morse
          code.  If you follow the lessons provided in the Learn phase, you
          should have no trouble in learning the Morse code in a few weeks
          or months.
          
               In addition to the method provided by Super Morse several
          general tips on learning the Morse code can be provided as
          follows:
          
               i.  Learn the characters by sound, not by sight.  Each of
          the characters has its own characteristic length and rhythm.  Do
          not memorize the characters using the visual dot and dash
          symbols.  That will only slow you down and create bad habits that
          wil l be very hard to break!
          
               ii.  Set the character speed to 13 words per minute or
          higher (the ARRL uses 18 WPM) and the send speed at whatever
          lower speed you desire. (Super Morse automatically sets the
          character speed to 18 WPM). Since your ultimate goal is 13 words
          per minute , it is much better to learn the sounds of the
          characters at the higher speed even though they are spaced at a
          lower speed. As mentioned above this is called the Farnsworth
          method, and it helps to eliminate the "hump" that most people
          experience around 1 0 words per minute.
          


                                                                      Page 5
               iii.  Study every day, but if you feel you are stuck and
          not making progress, take a few days off.  It's amazing how this
          will sometimes clear your head.
          
               iv.  Try to copy code in you head as much as possible.
          
               v.  Obtain access to a ham receiver and try to copy real
          transmissions off the air.  Some general coverage short wave
          receivers permit reception of Morse code, but in general they
          are harder to tune in on a Morse code signal.
          
               vi.  As soon as possible learn the sounds of whole words.
          You will find that whole words have characteristic lengths and
          rhythms that distinguish them from all other words.
          
               vii.  Turn on the Super Morse Build/Groups function and let
          the computer send in the background while you are doing something
          else, such as reading a book or working on a construction
          project.  Try to identify characters while doing the other
          activity. This will help your brain shift to "automatic" and will
          help the code sounds become a natural "part of the wallpaper."
          
               viii.  Although the code test no longer requires that you
          demonstrate an ability to send Morse code, you should get a code
          practice oscillator and practice your sending.  Note that Super
          Morse can be used as a code practice oscillator using one of seve
          ral keys on the keyboard or an external telegraph key.
          
               ix.  As soon as you pass the novice test, get a rig on the
          air and operate on the novice bands.  Nothing will increase your
          speed and concentration as well as the pressure of an on-the-air
          contact.  Don't worry about being perfect--the other guy is pr
          obably in the same boat as you. II. Super Morse Basics
          
          3. Scripted Disk Files
          ----------------------
          
               The disk files that may be played with the Build|File
          command amy be scripted by inclusion of commands that control the
          operation of Super Morse. Scripted files permit Super Morse to be
          automated for special learning methods, to prepare code tapes, or
          to give tests.
          
               Disk files are "scripted" by placing a period (".") in the
          first column of any line followed by a command character in
          capitals and a space and text, if applicable.  With scripting
          Super Morse follows exactly the same line spacings as are used in
          the script file. Thus, if you want lines skipped before and after
          the message, place blank lines in your script file.
          
               Scripting permits the following commands to be inserted in
          a file.
          


                                                                      Page 6
               a. The Message Command
               ----------------------
          
               The "M" command line as follows causes the <text> to be
          printed in highlight on the screen:
          
                         .M This a message to the user
          
          This will print "* This is a message to the user" on the screen.
          
               b. The Pause Command
               --------------------
          
               The same effect as the message command, except with a pause
          for you to press a key to continue, is provided by the "P"
          command as follows:
          
                         .P Ask the user to do something
          
          This will print "* Ask the user to do something" and instruct
          you to press any key to continue.
          
               c. Set Speeds Command
               ---------------------
          
               Speeds can be programmed into the script at the indicated
          send speed ("<ss>"), character speed ("<cs>") and word speed
          ("<ws>") with the "S" command as follows:
          
                         .S <ss> <cs> <ws>
          
               d. Restore Speeds Command
               -------------------------
          
               The set speeds command automatically saves the current code
          speed before it is changed.  The former speeds can be restored
          with the following command:
          
                         .R
          
               e. Speed Lock Commands
               ----------------------
          
               The set speed keys can be disabled with the .L command and
          re-enabled with the .U command.  These commands are not followed
          by text.
          
          


                                                                      Page 7
          4. Customization of External Files
          ----------------------------------
          
               a. General
               ----------
          
               In addition to internal modifications, Super Morse permits
          customization by changing the contents of Super Morse's text
          files. Modifiable files all have the "SM" extension, such as
          NAMES.SM.
          
               If a word processor is used, the output must be ASCII text
          only!  Most modern word processors output not only the text that
          you enter in the document but also formatting information which
          is not displayed on the screen. This invisible formatting info
          rmation will cause to Super Morse produce garbage. If you use a
          word processor, be sure to check your user manual to determine
          how to save text in plain ASCII format without the formatting
          information.
          
               b. Data Files
               -------------
          
               Super Morse uses several files containing names, cities,
          and other information used in QSO generation (simulated radio
          contact), and other files for words used in word-based functions.
          If you are not satisfied with the contents of these files, you m
          ay change them to suit your tastes. Non-U.S. users will probably
          want to change the contents of the states file to include the
          provinces in their own country or other countries.
          
               All data files require that only one item be placed on a
          line starting in column 1 (not at the left margin of a word
          processor file if the margin is shown!) and that no blank lines
          be inserted in the middle of the file.
          
               The names, antenna types, city names, and rig types can be
          changed to reflect your desires by editing the files ANTENNAS.SM,
          NAMES.SM, CITIES.SM, RIGS.SM, and JOBS.SM as described earlier in
          this document. The maximum number and length of the entries are
          as follows:
          
                         File           Max. Entries   Max. Length
          
                         ANTENNAS.SM           50             15
                         CITIES.SM           200              15
                         JOBS.SM             100              20
                         NAMES.SM            200              10
                         RIGS.SM             100              15
                         STATES.SM           100              15
          


                                                                      Page 8
               c. License Classes File
               -----------------------
          
               The only data file having a special format is the
          CLASSES.SM file.  This file contains three lines in a special
          order. The file distributed with Super Morse defines the United
          States license classes and speeds as follows:
          
                                        05 Novice
                                        13 General
                                        20 Advanced
          
               The format is critical!  It must contain three lines and
          start in column 1 (not the left margin of a word processor
          file!). Each line begins with a speed in words per minute in
          columns 1 and 2, followed by a space, followed in column 4 by the
          name of the license class beginning at that speed, not exceeding
          8 characters in length.  If a speed is less than 10 WPM, a "0"
          must be placed at the beginning.  If only two license classes are
          used in your country, repeat the second class definition on the
          thir d line as in the following generic example:
          
                                        07 Junior
                                        11 Senior
                                        11 Senior
          
               If you have only one class of license, place the same
          information on all three lines.  If your country uses more than
          three classes of licenses, please let me know, and I will expand
          this file.
          
               d. Text Files
               -------------
          
               In some features Super Morse permits you to use a plain
          ASCII text file as input.  An example in the Disk File command in
          the Build phase.  These files should be created with a text
          editor or word processor in the ASCII output mode as described
          above .  The lines in these files can be any length and can start
          in any column.
          
          
          5. QSO Templates
          ----------------
          
          
               The external template may be selected in the Generate exam
          function. The external template is contained in a disk file
          named QSOn.SM where "n" is a number from 1 to 99.  The file
          QSO1.SM is provided as an example, but you may created other
          ASCII fil es yourself.
          
               An exam QSO template file comprises any desired text built
          around up to 20 pieces of randomly selected data.  When data is


                                                                      Page 9
          desired in the QSO file, insert the identifying number of the
          data type surrounded by curved brackets ("{" and "}").  The ident
          ifying numbers are as follows:
          
          
               1 - calling station      11 - countries worked
          
          
               2 - responding station   12 - band 1
          
          
               3 - rst report           13 - band 2
          
          
               4 - name                 14 - job
          
          
               5 - city                 15 - rig type
          
          
               6 - state                16 - antenna type
          
          
               7 - age                  17 - antenna height
          
          
               8 - years a ham          18 - power (watts)
          
          
               9 - license class        19 - weather
          
          
               10 - states worked       20 - temperature (Deg. F)
          
          
               The following is an example of a line in a QSO template:
          
          
                         My name is {4}, and I live in {5},{6}.
          
          
               Super Morse randomly generates a name and substitutes it
          for {4} and a city and state and substitutes them for {5} and
          {6}.  An example of the result is as follows:
          
          
                      My name is Joe, and I live in Northfield, KS.
          
               At least 10 pieces of data should be used in any exam file
          to support the 10 questions that are asked in the exam.
          


                                                                      Page 10
          6. Equipment and System Requirements and Limitations
          ----------------------------------------------------
          
               a. System Configuration
               -----------------------
          
               Your CONFIG.SYS file should authorize at least 20 files.
          This can be done with the following statement:
          
                                   FILES = 20
          
               b. Mouse
               --------
          
               Super Morse supports a Microsoft mouse.  In some
          configurations, Super Morse uses two serial ports. If you use a
          serial mouse, there may be a conflict.  To fully use all Super
          Morse features, three serial ports are required.
          
               c. Code Speed Calibration
               -------------------------
          
               In order for Super Morse to send properly-timed code,
          calibration to each computer is required.  Calibration is
          affected primarily by the computer clock speed and memory
          resident programs.
          
               Super Morse uses two different calibration methods, (a)
          clock and (b) loop, in order to handle various types of PC
          designs and operating systems. The method that you desire to use
          is selected from the Options menu.
          
               Both methods require some calibration using the Options|Code
          features. The timer method needs to be "tweaked" the first time
          you use it to match itself to your computer, but thereafter it
          self-calibrates to the computer clock speed each time the program
          loads.  However, if you use the loop method, you must calibrate
          Super Morse each time you add or remove a memory resident
          program.
          
               The loop method must be used if your computer does not
          implement the system clock chip in the same way as the original
          PC design, if you are running under Windows as a DOS application,
          or if running on a PC emulator on a MacIntosh or other computer.
          Super Morse is initially set for the clock method; but if the
          code is erratic or choppy on your computer, you should change to
          the loop method.
          
               d. Video Display Card
               ---------------------
          
               Super Morse supports CGA (color) and MDA (monochrome) video
          displays only.  The proper display adapter can be selected from


                                                                      Page 11
          the Options menu. Super Morse will operate on EGA and VGA
          monitors but in the CGA mode.
          
               e. Disk Cache Programs
               ----------------------
          
               Super Morse saves changes in the program parameters when
          you exit the program.  If you are using a disk cache program,
          the parameters may be saved to the cache area in memory and thus
          may not permanently saved to disk.  If you a re having this
          problem, you should try disabling any disk cacheing program which
          you have installed on your system.
          
               f. Floppy Disk Write Protect Tabs
               ---------------------------------
          
               If Super Morse is run from a floppy diskette, a write
          protect tab should not be used! Super Morse must be able to store
          configuration and user information to the diskette.
          
               g. Windows Capability
               ---------------------
          
               Super Morse is written as a DOS program, but it will run
          under Microsoft Windows under certain conditions.  The author
          has confirmed that it will operate under the 386 Extended mode
          (i.e., a 386 or 486 computer is required) using the loop timing
          method.  You must set up a PIF file, and set the background to
          foreground ratio to 10000 to 1 and set Execution to "Exclusive".
          These are available as Advanced options in the PIF editor menu.
          To save you time a PIF file to run Super Mor se under the
          conditions stated is provided on the distribution diskette.
          
               h. Speaker Volume
               -----------------
          
               The volume produced by the PC speaker is very low on some
          PC's, but unfortunately there is no way to increase it without
          an external amplifier. Some relief can be obtained by changing
          the speaker tone since speakers (and your ears!) are frequency
          dependent.  ADVICE: Get a Sound Blaster type sound card.  See
          next section for setup.
          
          7. Sound Boards
          ---------------
          
               Super Morse now supports the Sound Blaster card and
          compatibles. Super Morse initializes for use of the PC speaker,
          and the Sound Blaster must be selected in the Options|Code menu.
          A sound card is HIGHLY RECOMMENDED!
          
               If you plan to use the Sound Blaster card for sound output,
          you must use a text editor, such as EDIT or EDLIN, (or a word
          processor in ASCII output mode) to insert a line in the


                                                                      Page 12
          AUTOEXEC.BAT file specifying an "environment string". The line
          should b e in the following format:
          
                    SET BLASTER=A<addr> I<int no> D<DMA channel no> T<SB type>
          
               For a Sound Blaster 1.0 using I/O address 220, Interrupt 7
          and DMA channel 1, the string would look as follows:
          
                              SET BLASTER=A220 I7 D1 T1
          
               The I/O address, Interrupt number, and DMA channel can be
          determined using the TEST-SBC.EXE program provided with your
          Sound Blaster.  If you did not change any of the jumpers on the
          board when you installed it, you can use the factory default
          settin gs shown in the Sound Blaster manual.
          
               The SB type for Sound Blaster and compatible boards for use
          with the "T" parameter is one of the following:
          
                         1 - Sound Blaster 1.5 or earlier
                             Sound Blaster Micro Channel Version
                         2 - Sound Blaster Pro
                         3 - Sound Blaster 2.0
                             Audio Spectrum 16
                         6 - Sound Blaster 16
          
          8. Interfacing External Equipment
          ---------------------------------
          
               The primary I/O for Super Morse code is via the computer
          keyboard and the PC onboard speaker.  Secondary output is
          provided by toggling either the DTR or RTS pin at the selected
          RS-232 communications port.  Input is provided via either the DSR
          o pin at the same port.  You can select whether to expect either
          a high (+) or a low (-) voltage in the key-down condition and
          the opposite in the key-up condition. Output via DTR/RTS is
          available whenever code is being sent, but input via DSR/CTS is
          avail able only in the Manual key function of the Enhance phase
          and in the Operate phase.
          
               I/O via either COM1, COM2, COM3, or COM4 can be selected
          from the Options|Ports menu selected from the main menu bar. With
          a proper interface DTR/RTS can be used to drive an external
          oscillator for making high quality code tapes or to key a
          transmitt er. Likewise, DSR/CTS can be interfaced with a hand
          key, electronic keyer, or a receiver.
          
               Code output to the speaker and COM port can be selected
          from the Options menu. Code input can be selected from either one
          of several keys on the computer keyboard or the COM port using
          the Input Keying selection in the Options|Ports menu.
          
               A detailed explanation of how to use the DTR/RTS and
          DSR/CTS signals for the aforementioned purposes is beyond the


                                                                      Page 13
          scope of this manual and is left to your ingenuity.  However,
          limited information is provided in Section XI. The author would
          like to r eceive diagrams of tested circuits designed by users to
          take advantage of COM port I/O.
          
               If an external key does not work, check the following:
          
               a. The RS-232 connector pins are small and easily confused.
          Most connectors have the pin numbers beside the pins, but they
          are almost impossible to read without a strong light and
          magnifying glass. Remember that the connector pins on the
          computer ar e a mirror image of those on the cable connector.
          
               b. Some computers connect the RS-232 pins differently.
          Consult your owner's manual, or call your computer manufacturer's
          technical assistance line for information on the configuration.
          Some experimentation (i.e., random poking around in the connecto
          r) may be required to find the right pins. On the author's
          Gateway 2000, for example, it is necessary to use pin 20 as
          signal ground instead of pin 7. This is different from two
          previous computers which used pin 7.
          
               c. The pin numbers given in this manual are for the 25 pin
          DB-25 connector.  If you have a 9 pin DB-9 connector, match the
          pin names instead of numbers.  You will have to consult your
          owner's manual for a definition of the pins for that connector.
          
               d. Super Morse uses two COM ports, and you should make sure
          that different ports are set for the Modem function and the
          keying function.
          
               e. Be sure that the "External" keying source is selected in
          the Ports menu.
          
          
          9. Circuit Diagrams for External Connections
          --------------------------------------------
          
               a. Using an External Hand Key
               -----------------------------
          
          
                    To RS-232 DSR    o------------+
                      (Pin 6) or CTS              |
                      (Pin 5)                     o
                                                    /  Morse Telegraph Key
                    (COMPUTER)                     /   ("Straight" Key)
                                                  o
                                                  |
                    To RS-232        o------------+
                    Pin 7 (*)
                    GND
          


                                                                      Page 14
                                                                                Page 14
                    * Due to variations among manufacturers, you may have to
                    experiment to determine the correct pins
          
               b.  Connecting to a Receiver
               ----------------------------
          
                         No one has submitted a circuit for connection to a radio
                    receiver, but the following is the way it is done in concept.
          
          
                            +-----------+    +-----------+       +-----------+
                    DSR/CTS |           |    |           |       |           |
                    o-------+ Voltage   |    | Tone to   | Audio |           |
                            | Controlled+<---+ Voltage   +<------+   Radio   |
                    o-------+ Switch    |    | Converter |       |           |
                    GND     |           |    |           |       |           |
                            +-----------+    +-----------+       +-----------+
          
                         The connections to the computer are the same as for the
                    straight key above.  The voltage- controlled-switch can be a
                    transistor or relay. The tone to voltage converter can be a phase
                    locked loop, which is available in chip form.  The details are
                    left to the user, but circuits that can be used or adapted can be
                    found in the ARRL Handbook and other similar sources.
          
               c. Driving a Transmitter or Other Device
               ----------------------------------------
          
                         The following circuit designed by John Swancara, WA6LOD,
                    can be used to drive a keyer, code oscillator, or a transmitter.
                    It is described in QST Magazine, February, 1990, page 36.  A
                    similar circuit was provided by John Dilks, K2TQN.
          
                         If these connections do not work, first check the Port
                    settings in the Options menu.  Then check your computer's RS-232
                    information in case you computer uses something different from
                    the standard.
          


                                                                      Page 15
                                                                                Page 15
          
                                             +-----------------------+
                                             |  Radio Shack TIL-113  |
                                             |                       |
                                           +-+-+                   +-+-+
                                           ³   ³                   |   |
                     RS-232 Signal   o-----+ 1 +---+    +----------+ 6 +-o NC
                     ground (Pin 7)        ³   ³   |    |          ³   ³
                                           +-+-+   |    |          +-+-+
                                             |     |    |            |
                                             |     +    |            |
                                             |    \ /   |            |
                                             |     v    |            |
                                             |     -    |            |
                                             |     |    |            |
                                             |     |    |            |
                                      D1     |     | \  |            |
                                           +-+-+   |  \ |          +-+-+
                    RS-232     R1      /   ³   ³   | \  |          ³   ³
                    Pin  o--+--\/\/--|< +--+ 2 +---+  \ |      +---+ 5 +-o To
                    4       |          \   ³   ³        |          ³   ³   Positive
                            |              +-+-+        |     /    +-+-+   Keying
                            |                |          |   |/       |     Line
                           -+-  C1           |          |   |        |
                           -+-               |          |   |        |
                            |                |          +---+        |
                            |                |              |        |
                            |                |              |        |
                            |                |              |\       |
                         o--+                |                \      |
                            |              +-+-+               _|  +-+-+
                            |              |   |                   |   |
                           ---        NC o-+ 3 |               +---+ 4 +-+-o To
                            -              |   |                   |   | |   Trans-
                                           +-+-+                   +-+-+ |   mitter
                                             |                       |   |   Chassis
                        Board                |                       |   |
                        Ground               +-----------------------+   |
                                                                         |
                                                                        ---Interface
                                                                         - Board
                    Ground
          
                                      D1  = 1N914
                                      R1  = 1K Ohm, 1/4 Watt
                                      C1  = 0.01 Microfarad, 50 Volt
                                      DTR = Data Terminal Ready pin
                                      NC  = no connection
          
                    Note: (1) Voltage on pins 4 and 5 of TIL-113 should be kept below
                              20 volts, and the current draw should not exceed 100 ma.
          
                           (2) The Philco ECG 3041 may be substituted for the Radio
                                Shack TIL-113.


                                                                      Page 16
                                                                                Page 16
          
               d. Using a Volume-Controlled Headphone
               --------------------------------------
          
                         Splice a 50 ohm variable resistor and a headphone jack into
                    the PC speaker line as shown below.  The headphone jack should
                    break the speaker circuit and close the headphone circuit when
                    the headphone plug is inserted.
          
                                              Headphone Jack
          
                            o--------+           o     o
                                     |           |     |
                                      \          |     |
                       PC        50   / <--------+-------------+  /|
                     Speaker     ohm  \                |       | / |   PC
                       Line           /                |       |/  |   Speaker
                                     |                 |       |\  |
                                     |                 |       | \ |
                            o--------+-----------------+-------+  \|
          


                                                                      Page 17
                                                                                Page 17
               e. Using an External Oscillator
               -------------------------------
          
          
                         Following is a simple code oscillator driven from the COM
                    port of a PC designed by Jeff Furman, KD6MNP.
          
                    DB-25
                    FEMALE
                                 1N4001
                    +-----+
                    |     |       |\ |
                    |     +-------| \+-------+---+
                    |  4  |       | /|       |   |
                    |     |       |/         |   |  555
                    |     |             +----+---+------+
                    +-----+             |               |
                    |     |             |    4   8      |
                    |     |             |               |
                    |  7  +------+------+ 1             |
                    |     |      |      |               |
                    |     |      |      |               |
                    +-----+      |      |               |
                                 |      |    6   2   3  |             1/8" stereo
                                 |      +----+---+---+--+             headphone jack
                                 |           |   |   |
                                 |    ||     |   |   |    ||
                                 +----++-----+-+-+   +----++------------+---- V    |
                                 |    ||       |     |    ||            +-- v      |
                                 |             |     |                             |
                                 |              \/\/\                   +----------+
                                 | 0.001 uF       ?     0.01 uF         |                               ³   film        680k   ceramic or      ³
                                 |               ohms   film            |
                                 |                                      |
                                 +--------------------------------------+
          
          
                            This easily fits inside the DB-25 shell.
                            Adjust the 680k ohm resistor to change the pitch--
                            higher value for lower pitch, etc.
                            Decrease the value of the 0.01 uF cap. for lower volume.
          
                            Super Morse Options|Ports settings:
          
                                 Keying Port  : <your choice from what's available>
                                 Output Keying: ON
                                 RS-232 Output: RTS
                                 Output Sense : -
          


                                                                      Page 18
                                                                                Page 18
               f. Using an External Sound Output
               ---------------------------------
          
                         The following was submitted by Bruce G. Kinney, San Jose, CA
          
                                            +------------------+
                               30K    Shield|                  |
                    Pin 20 o--\/\/\/--+-- O + MOD IN           |      /|
                                      |   | |               O  +---- / |
                              .68uf  -+-  | |               U  |   <   | Speaker
                                     -+-  | |               T  +---- \ |
                                      |   | |                  |      \|
                    Pin 7  o----------+---+-+ GND              |
                                            |                  |
                                            +------------------+
                                               LEADER 1300S
                                             Function Generator