UNDERSTANDING YOUR CAD OUTPUT: BASIC PHOTOPLOTTING PRINCIPLES

         A supporting document for GraphiCode's GC-PREVUE: Shareware PCB
         CAD output data viewer/checkplot utility

         Copyright (C) GraphiCode Inc 1991,1992 All Rights Reserved.



	  What's a Photoplotter?


	 A photoplotter is just what the name implies: an plotter that
	 writes using light.  A plotter has to be told:

	   Which tool to use.
	   When to use the tool, and when not to.
	   Where to go next.
	   Whether to go there in a straight line or along an arc.

	 For a photoplotter, "tool" means specially shaped apertures
	 through which light passes to create a given shape on film.  An
	 aperture can be used without movement to make a shape (a "flash")
	 or with movement to make a line or an arc.

	 There are two major types of photoplotters, "Vector" and "Raster"
	 (or "laser").  Each handles apertures differently.

	 Vector Photoplotters

	 Aperture Wheels

	 Traditionally, the photoplotter counterpart to a pen plotter's
	 pen rack has been the aperture wheel.  The aperture wheel is a
	 disk with 24 or 70 apertures arrayed radially along its
	 circumference.

	 When the photoplotter selects an aperture, the aperture wheel is
	 rotated to place the desired aperture between the light source
	 and the film.  Apertures are themselves pieces of film and can be
	 made to any shape required, although in practice this is a time-
	 consuming process and there is a physical limitation on size.

	 Flash and Draw Apertures

	 To achieve constant exposure on a vector photoplotter, apertures
	 used for flashing pads are filtered differently than those used
	 for drawing traces.  Therefore, Flash and Draw apertures cannot
	 be used interchangeably without risk of localized over-exposure
	 and under-exposure.

	 Aperture Wheel Setup for Vector Plotters

	 The setup of an aperture wheel is an exacting and time consuming
	 process since each aperture in the wheel must be hand-mounted and
	 aligned.  In order to avoid repeated setup costs, designers have
	 the photoplotting vendor keep a wheel on file and are forced to
	 always use that same set of apertures.  This has obvious




	 drawbacks, both in terms of design flexibility and the ease of
	 migration to other vendors.

	 Raster (Laser) Plotters

	 Aperture Lists

	 Increasingly, vector photoplotters are being replaced by the
	 laser photoplotter, which emulates the older style machine in a
	 raster (bit-map) fashion.  While use of the term "aperture" to
	 describe a pad or trace shape persists, the term "aperture wheel"
	 is now being replaced by "aperture list", which implies the
	 greater flexibility now available to the designer.

	 There are three principle advantages with aperture lists on
	 raster plotters:

	   Aperture shapes can be easily generated in software, thus
	   eliminating the need to design a physical wheel.
	   More apertures can be defined on a list.
	   Allowable apertures sizes are typically (but not always)
	   greater than those imposed by the physical dimensions of an
	   aperture wheel.

	 Flash and Draw Apertures

	 No distinction need be made between Flash and Draw aperture types
	 since the light source intensity is constant.

	 Speed Advantage of Laser Plotters

	 Laser plotters operate much quicker than vector machines.  A
	 complex plot that required hours on a vector machine can usually
	 be performed in ten minutes or less on a laser photoplotter.
	 This decreases turnaround time and in many markets has driven
	 photoplotting costs down.

	 Talking to Photoplotters

	 The de facto standard for photoplotter data is the Gerber format,
	 more properly known as RS-274D.  The term Gerber refers to the
	 Gerber Scientific Instrument company, a pioneer and leader in
	 photoplotter manufacturing.

	 RS-274D is a variation on traditional Numerical Control (NC)
	 machine tool languages.  It differs from traditional NC formats
	 (i.e. drill data), as far as its use of tool selection codes but
	 is otherwise compatible.

	 RS-274D data is organized in "blocks".  A block consists of a
	 combination of codes:




	   Tool selection
	   Setup
	   Movement
	   And, an End Of Block (EOB) character, which only follows a
	   combination of the above codes.

	 An EOB character is usually an asterisk ('*') or dollar ('$'),
	 optionally followed by a carriage return and line feed.

	 An RS-274D code consists of a letter D,G,M,X,Y,I or J followed by
	 a numerical value.  These codes designate the following:

	   * - End of Block (end of command)

	   D - Select aperture, or set aperture use mode

	   X - Move to X value

	   Y - Move to Y value

	   G - Various setup codes

	   M - Various control codes

	   I - Relative X location for arc center

	   J - Relative Y location for arc center

	 D Codes

	 D codes have multiple purposes.  The first is to control the
	 state of the light being on or off. Valid codes for light state
	 are D01, D02, and D03.

	   D01 - Light on for next move.

	   D02 - Light off for next move.

	   D03 - Flash (Light On, Light Off) after move (effect is limited
	   to block in which appears, ie non-modal).  You can also think
	   of a D03 as D02, D01, D02 series of commands linked together.

	 D codes with values of 10 or greater represent the aperture's
	 position on the list or wheel.  It is very important to
	 understand that there is no universal "D10" or "D30".  Unlike the
	 D01 , D02, and D03 counterparts which have a fixed meaning (draw,
	 move, flash), D10 and higher values have aperture shapes and
	 dimensions assigned to them by each individual user.  Hence, one
	 job's D10 could be a 10 mil Round, when another job's D10 could
	 be a 45 mil Square.

	 There are two distinct ways to number an aperture list.  The
	 traditional 24 aperture system started with D10 - D19, jumping
	 suddenly to D70 - D71, then back to D20 - D29, ending with D72 -




	 D73.  This is still a common format for output for CAD packages,
	 and is still mandatory for old 24 aperture Gerber vector
	 photoplotters.

	 It is now common to start with D10, then increase numerically in
	 steps of 1 (D10, D11, etc.) continuing up to D70 and beyond,
	 rarely beyond 1000 individual apertures.

	 X & Y Codes

	 The X & Y values in the Gerber file determine where the aperture
	 shape and dimension will be positioned and drawn.  X & Y values
	 are used as coordinate pairs to determine where the light will be
	 exposed, using the D codes shapes (i.e. D10) and light exposure
	 status (i.e. D01, D02, D03) for drawing lines and arcs, as well
	 as moving between drawing entities.

	 Here are a few examples of using X & Y codes with D codes.

	   D10*  { Select aperture D10}

	   X1000Y1000D02* { The D02 tells us that the light will be off,
	   and we move to coordinate position X1000 and Y1000}

	   X2000Y3000D01* { The D01 tells us that we will draw (light on)
	   to coordinate position X2000 and Y3000}

	   X5500Y100D03* { The D03 tells us to move to coordinate position
	   X5500 and Y100 with the light off, then flash (turn the light
	   on and off)}

	 G Codes

	 G codes are used to configure the photoplotter.  Commonly
	 implemented codes include:




	   G01 - Future X,Y commands are straightline moves

	   G02 - Future X,Y commands are clockwise arcs

	   G03 - Future X,Y commands are counterclockwise arcs

	   G04 - Ignore the rest of this block (used for Comments)

	   G54 - Prepare to change apertures

	   G74 - Future arcs are quadrant arcs

	   G75 - Future arcs are Full 360 arcs

	   G90 - Absolute data

	   G91 - Incremental data



	 Typically for laser photoplotters, G54 codes are rarely
	 necessary.  Older vector plotter controllers may require this
	 preparatory G codes for changing apertures (i.e. G54D10*).

	 A common situation where G codes are mandatory for all machines
	 is when the data is switching from vectors to arcs and vice
	 versa.  When switching from drawing vectors (G01) to drawing arc
	 (G02, G03), the controller must be informed of the change of
	 mode.

	 Another important case for G codes is when determining if the arc
	 is a quadrant (G74) or Full 360 (G75).  Quadrant arcs never cross
	 quadrant boundaries, because the center coordinate offsets (I,J
	 Codes) are always unsigned (even if they are negative!).
	 Therefore, it requires at least four G74 arcs to draw one
	 complete circle.

	 Center coordinate offsets for 360 arcs (G75) can be positive or
	 negative, allowing for a single command to draw a complete
	 circle.

	 In either case, the center coordinates are given relative to the
	 start point of the arc.  The most dramatic difference between
	 Quadrant and Full 360 arcs is that a Quadrant arc with identical
	 start and end points has a sweep of 0 degrees, whereas a similar
	 Full 360 arc is a full circle.

	 The G90 code tells the machine controller that all data following
	 is absolute data.  Hence, if following X & Y data follows, the
	 controller will move to the absolute value given by the X & Y
	 value.




	 G91 tells the machine controller that all data following is
	 incremental data.  The machine will move the data by the amount
	 of the X & Y value, rather than to the absolute coordinate point.

	 Example:

	   X1000Y1000D02*

	   X3000Y3000D01*



	 In absolute mode (G90), the machine will first move to coordinate
	 point X1000 and Y1000 with the light off, then draw a line to
	 coordinate point X3000 and Y3000 with the light on.

	 In incremental mode (G91)  the machine will first move to
	 coordinate point X1000 and Y1000 with the light off, then draw a
	 line to coordinate point X4000 and Y4000 with the light on.  This
	 was done by adding X1000 + X3000 = X4000 and Y1000 + Y3000 =
	 Y4000.

	 Here are some more examples of G code usage in conjunction with
	 X, Y, and D code values:

	   G54D10*      { Prepare to change aperture position (G54), then
	   select aperture D10}

	   G01X1000Y1000D02*      { Prepare to draw a vector (G01) then
	   turn off the light (D02) and move to coordinate position X1000
	   and Y1000}

	   G90*    { This block (command) and all future commands will be
	   absolute data}

	   X2000Y3000D01*    Turn the light on (D01) and move to absolute
	   coordinate position X2000 and Y3000}

	   G91*              { The G91 command tells the controller that
	   this command and all future commands that the data is
	   incremental}

	   X5500Y100D03*     { Turn the light off and move incrementally
	   by a value of X5500 and Y100, then flash (D03) (light on and
	   off)}

	 M Codes

	 M codes are used for machine control.  Here are the most commonly
	 used:




	   M00 - Full machine stop.  Commonly ignored by many plotters.

	   M01 - Temporary machine stop.  Commonly ignored by many
	   plotters.

	   M02 - End of Plot.

	 I & J Codes

	 When you encounter an I & J code in a Gerber block, you have
	 found an arc command.  Arc commands come in two flavors, Full 360
	 or Quadrant.  The Gerber arc command is very complicated, and
	 this section will only briefly describe usage of the Gerber arc.

	 Full 360 arcs allow the plotter to draw a full circle (360
	 degrees of arc) in one single command..

	 Quadrant arcs only allow for an arc to be drawn through a maximum
	 of 90 degrees of arc, never crossing a quadrant boundary.  Due to
	 this restriction, I and J arc center offset codes can get away
	 with never having a negative value, even if the offsets are
	 negative!

	 When in a Full 360 arc (G75), only one command is required to
	 draw a circle.  In Quadrant mode, the same circle would require
	 at leaset 4 Quadrant arcs (G74), because a circle goes through
	 all four quadrants.

	 Quadrant arcs will always have positively signed I and J values,
	 even if the center offset is actually negative.  Full 360 arc
	 center offsets can be signed positively or negatively.  A
	 negative I or J is a sure indicator of Full 360 arcs.

	 Modality

	 It is often the case with Gerber data that when moving from one
	 XY coordinate point to another XY coordinate point, the X or Y
	 value will not change.  Likewise, it is likely that if the
	 plotter is drawing a line with multiple segments, the segments
	 will be connected and the light stays on from segment to segment.

	 In both of these cases, there are redundant commands, making the
	 plot data file larger than necessary.

	 RS-274D allows you to omit this redundant data.  This example
	 shows a box being drawn with four corners.




	   Non Modal Data         Modal Data

	   X0000Y0000D02*         X1000Y1000D02*

	   X0000Y1000D01*         Y1000D01*

	   X1000Y1000D01*         X1000*

	   X1000Y0000D01*         Y0000*

	   X0000Y0000D01*         X0000*

	 From this example, a large amount of data has not been written,
	 thus reducing the final data file size.

	 Establishing the Decimal Point

	 A numerical value in RS-274D data has an integer and a decimal
	 part, but the decimal point ('.') is not a valid RS-274D
	 character.  Thus, decimal values are written as a string of
	 integers.  The implicit position of the decimal point is
	 determined by three parameters:

	   Number of integer digits (whole digits)
	   Number of decimal digits (precision)
	   Zero suppression.

	 For example: In a system with integer digits=n and decimal
	 digits=m (an "n,m" system), a numerical value is written using
	 (n+m) digits.

	 For example, in a "2,3" format the value 12.345 is written
	 "12345".  In a "2,4" format, the same value is written "123450".

	 Zero suppression comes in three flavors - leading, trailing and
	 none.  The idea of zero suppression is to reduce data file sizes
	 by eliminating unneeded 0 characters.  The simplest and most
	 common form of zero suppression is leading zero suppression.

	 In a "2,4" format, with no zero suppression, the value 0.0100
	 would be 00 + 01000, written as "000100", but with leading zero
	 suppression the same value is written as "100".

	 With trailing zero suppression the same value 0.0100 would be
	 written as "0001".

	 How To Describe Data Formats

	 Gerber data and other XY languages use a standard method for
	 describing the data format.  Two examples include:




	   "2,3 leading inch" or "3,3 trailing metric".  The first number
	   specifies the whole digits used.  The second parameter states
	   the precision.  "Leading" and "trailing" pertain to the zero
	   suppression.  And the last part of the description indicates
	   the units.  Refer to the above sections if these concepts seem
	   unclear.