PrintGL 1.42 HP-GL and ADI Commands

                      (C) Copyright Ravitz Software Inc. 1990,1994


         Ravitz Software Inc.                              BBS/FAX 606-268-0577
         P.O. Box 25068
         Lexington, KY  40524-5068
         USA                                  Compuserve Cary Ravitz [70431,32]


         ------------------------------ Contents ------------------------------

         Introduction ....................................................... 2
         ADI Commands                                                         2
         HP-GL Commands ..................................................... 2
         HP-GL Character Sets                                                13


                                                                            p-2
         Introduction ---------------------------------------------------------

           This  document   is   a   description   of   the  subset   of  HP-GL
           (Hewlett-Packard Graphics Language) that is supported by PrintGL. If
           you are  using  PrintGL  to work with  commercial graphics software,
           then  you will  probably not need  this  manual.  If you are writing
           HP-GL code you  will  find here the  information needed to make your
           HP-GL compatible with PrintGL.

         ADI Commands ---------------------------------------------------------

           With the /YA option PrintGL can read Autodesk ADI 4.0 vector plotter
           binary commands intermixed in the HP-GL. 1016 dpi coordinates or the
           current HP-GL user coordinates are assumed. The table shows each ADI
           command  and  the  equivalent  HP-GL  command  (as  interpreted   by
           PrintGL).  In  the ADI code column,  the  code number  and  "b"s are
           bytes, and "x" and "y" are words.

             ADI command     ADI code     equivalent HP-GL

             begin plot      1 b          ignored
             end plot        2            PG;
             move            3 x y        PUx,y; (0 <= x,y <= 65535)
             draw            4 x y        PDx,y; (0 <= x,y <= 65535)
             pen             5 b          SPb;
             speed           6 b          ignored
             line type       7 b          if b=0 then LT; else LTb,2;
             raise pen       8            ignored
             abort           9            ignored

           Eight line types (other than solid) are supported.                    


         HP-GL Commands -------------------------------------------------------

           PrintGL's HP-GL specification is taken from the  programming manuals
           for the HP 7475A, ColorPro (7440/17440), and 7550A.  The 7550 manual
           is  the  best reference for HP-GL - HP  manual 07550-90001.  PrintGL
           supports  the 7475, and 7440/17440 command sets except for character
           set 8 (Katakana), digitize commands, output commands, the error mask
           command, and some device control  commands.  Supported commands  are
           listed below.  Commands that are not applicable to printing, such as
           pen velocity, are  considered supported  but are completely ignored.
           Commands that are not supported are flagged and then ignored.

           In addition, PG,  AF, ES, LO, the enhanced IW command, character set
           5, and proportional spaced fonts, from the 7550, are supported.  And
           forty pens are allowed instead of eight.

           In reading a plotfile, PrintGL ignores carriage returns, line feeds,
           and nulls  except where  they may be valid characters (LB,  SM,  DT,
           esc.), and ASCII EOF (026) is interpreted as an end of file mark.   


                                                                            p-3
           AA x_center , y_center , arc_angle [, chord_angle]

             arc absolute

             AA moves the pen through an arc, starting at the current position,
             with the pen in the current up/down state.

           AF

             advance full page (7550 extension)

             AF starts a new plot. PrintGL starts every page with the pen up at
             0,0.

           AP

             automatic pen pickup - IGNORED

           AR x_center_delta , y_center_delta , arc_angle [, chord_angle]

             arc relative

             AR moves the pen through an arc, starting at the current position,
             with the pen in the current up/down state.

           AS

             acceleration select - IGNORED

           CA character_set

             designate alternate character set

             See HP-GL Character Sets for a list of character sets.

           CI radius [, chord_angle]

             circle

             CI draws a  circle centered at the current position.  The  current
             up/down state and position are unchanged by a CI command.

           CP [spaces , lines]

             character plot

             CP  moves  the  pen by character spaces (+ is  along the text) and
             lines  (+  is  up),  using  the current up/down  state.  Using  no
             parameters is the same as a carriage return/line feed.

           CS character_set

             designate standard character set

             See HP-GL Character Sets for a list of character sets.            


                                                                            p-4
           CV

             curved line generator - IGNORED

           DF

             default values

             This sets default values for the following commands:  CA,  CS, DR,
             DT, ES, FT, IW, LO, LT, PA, PT, SC, SM, SL, SR, SS, TL.

           DI [run , rise]

             absolute character direction

             DI sets the baseline direction for labels.  The default is 1,0.

           DR [run , rise]

             relative character direction

             DR  sets the baseline  direction  for labels.  Run  and rise are a
             percentage of P2X-P1X and P2Y-P1Y. The default is 1,0.

           DTt

             define label terminator

             The label terminator ends an LB command. The default is ASCII 003.

           EA x_opposite_corner , y_opposite_corner

             edge rectangle absolute

             EA  draws a  rectangle defined  by  the  current position  and the
             parameters. The pen position and up/down state are unchanged.

           EC

             enable cutter - IGNORED

           EP

             edge polygon

             EP draws  the  current  polygon  edge.  Any  pen  up/down used  in
             creating the polygon is respected in drawing the edge.

           ER x_opposite_corner_delta , y_opposite_corner_delta

             edge rectangle relative

             ER draws a rectangle with corners defined  by the current position
             and the command  parameters.  The current pen position and up/down
             state are unchanged.                                              


                                                                            p-5
           ES [ space [, line]]

             extra space (7550 extension)

             ES adds to the space between characters and  lines.  The units are
             in character cells (1.5*width, 2*height).  The allowed range is -1
             to 1. -.3333 causes characters to touch.

           EW radius , start_angle , sweep_angle [, chord_angle]

             edge wedge

             EW draws a wedge centered at the current position. The current pen
             position and up/down state are unchanged.

           FP

             fill polygon

             FP  fills  the  current  polygon.  Pen up/down  commands  used  in
             creating the polygon are ignored.

             There is a limit of 2000 fill line segments per polygon.

           FS

             force select - IGNORED

           FT [type [, spacing [, angle]]]

             fill type

             These are  the  fill types.  Type  2  is identical to  type 1  for
             PrintGL.

               1  solid lines spaced at half the pen thickness (see PT command)
               2  unidirectional solid lines spaced at half the pen thickness
               3  lines at the specified spacing
               4  cross hatched lines at the specified spacing
               5  type ignored

             A spacing  parameter  of 0 sets  the  spacing  to 1%  of the P1-P2
             diagonal. Spacing is in x axis units (this is only relevant if the
             axes have different scaling).  PrintGL supports any  integer angle
             for fill. Cross hatched lines are at angle + 90.

           IN

             initialize                                                        


                                                                            p-6
           IP [p1x , p1y [, p2x , p2y]]

             sets scaling points P1 and P2

             IP sets the scaling points (P1 and P2) in plotter units. P1 and P2
             are used by several commands to help with size independent plots.

           IW [x_lower_left , y_lower_left , x_upper_right , y_upper_right]

             input window

             IW sets a  clipping window in plotter units.  With  no parameters,
             the clipping window is turned off.

             If  PrintGL's  /YE switch is  set and user  scaling  is on then IW
             parameters are in user units.  In this case the window is rescaled
             with an IP command, but any SC command locks the current window.

           LB..text..terminator

             label

             Labels use  the current character set, based on CA, CS, SA, and SS
             commands. See HP-GL Character Sets for font specifics.

           LO [ position_number ]

             label origin (7550 extension)

             LO  sets the label origins, shown below.  For positions  4..9  and
             14..19 the label buffer is limited to 150 characters.  The default
             is 1.

             13                     16                      19
                3......  .......  ...6...  .......  ......9
                .     .  .     .  .     .  .     .  .     .
             12 2     .  .     .  .  5  .  .     .  .     8 18
                .     .  .     .  .     .  .     .  .     .
                1......  .......  ...4...  .......  ......7
             11                     14                      17

           LT [pattern_number [, pattern_length]]

             line type

             PrintGL's line type  patterns  are close to, but  not identical to
             HP's.  Pattern length is a percentage of the P1-P2 diagonal with a
             default  of 4%  and a minimum  of 4 dots for types  1 and 2 and 16
             dots for other types.
                                            1  ù               ù
             no parameter  solid            2  ÄÄÄÄÄÄÄÄ        ÄÄÄÄÄÄÄÄ
                                            3  ÄÄÄÄÄÄÄÄÄÄÄÄ    ÄÄÄÄÄÄÄÄÄÄÄÄ
             0             dots at          4  ÄÄÄÄÄÄÄÄÄÄÄÄ  ù ÄÄÄÄÄÄÄÄÄÄÄÄ  ù
                           endpoints        5  ÄÄÄÄÄÄÄÄÄÄ  ÄÄ  ÄÄÄÄÄÄÄÄÄÄ  ÄÄ
                           only             6  ÄÄÄÄÄÄ  ÄÄ  ÄÄ  ÄÄÄÄÄÄ  ÄÄ  ÄÄ
                                            7  ÄÄÄÄÄÄÄÄÄÄ  ù ù ÄÄÄÄÄÄÄÄÄÄ  ù ù
                                            8  ÄÄÄÄÄÄ  ù ÄÄ  ù ÄÄÄÄÄÄ  ù ÄÄ  ù 


                                                                            p-7
           PA [x , y] [, x , y] ...

             plot absolute

             PA sets absolute mode and optionally moves the  pen in the current
             up/down state.

           PD [x , y] [, x , y] ...

             pen down

             PD sets  the pen  down and optionally  moves  it with  the current
             absolute/relative mode.

           PG [i]

             new page (7550 extension)

             PG starts  a new  plot.  The parameter is ignored.  PrintGL starts
             every page with the pen up at 0,0.

           PM i

             polygon mode

             PM 0 starts polygon mode.  The current position is the first point
             in the polygon.

             PM 1 starts  a new  subpolygon.  The  position after the next  pen
             movement is the first point in the subpolygon.  The first pen move
             of a subpolygon is done with the pen up, regardless of the current
             up/down status.

             PM 2 ends polygon mode.

             PM  1 and PM 2 close  the current subpolygon with  the current pen
             up/down state. If used without first starting polygon mode (PM 0),
             PrintGL adds an implied PM 0 before processing the PM 1 or PM 2.

             The following  commands are accepted in polygon  mode: PM, PA, PR,
             PU, PD,  AA,  AR,  CI  (circles  are  automatically  prefixed  and
             suffixed by PM 1), and IN (ends polygon mode).

             The polygon buffer is limited to 500 data points.

           PR [x_delta , y_delta] [, x_delta , y_delta] ...

             plot relative

             PR sets relative mode and optionally moves the  pen in the current
             up/down state.

           PS

             paper size - IGNORED

             PrintGL ignores PS. The paper size must be set with the /L option.


                                                                            p-8
           PT [thickness]

             pen thickness

             PT specifies twice the line spacing used in solid fills and may be
             from 0 to 5.0 mm. It is reset to .3 mm with each SP command.

           PU [x,y] [,x,y] ...

             pen up

             PU  raises  the  pen  and  optionally  moves it with  the  current
             absolute/relative mode.

           RA x_opposite_corner , y_opposite_corner

             shade rectangle absolute

             RA  fills a rectangle with corners defined by the current position
             and the command parameters.  The current pen  position and up/down
             state are unchanged. The rectangle edge is not drawn.

           RO [angle]

             rotated coordinate system

             RO or RO0 sets up a normal coordinate system. RO90, the only other
             allowed  value, sets up a system that is rotated  90 degrees.  The
             type of rotation depends on the paper size.  This command does not
             change the scaling points, so an IP command is useful after an RO.

             The HP 7475 specifies two different meanings for RO90 depending on
             the  paper  size (A/A4 or B/A3).  PrintGL  decides  which  type of
             rotation to do based on the sum of  the  print  window  width  and
             height.  If this sum  is  greater than 24 inches  then large paper
             rotation is used. Otherwise, small paper rotation is used.

             Small paper rotation:              Large paper rotation:

             RO 0             RO 90             RO 0             RO 90

               yÚÄÄÄÄÄÄÄÄ¿   0,0ÚÄÄÄÄÄÄÄÄ¿y     0,0ÚÄÄÄÄÄÄÄÄ¿y    yÚÄÄÄÄÄÄÄÄ¿
                ³        ³      ³        ³         ³        ³      ³        ³
                ³        ³      ³        ³         ³        ³      ³        ³
             0,0ÀÄÄÄÄÄÄÄÄÙx    xÀÄÄÄÄÄÄÄÄÙ         ³        ³      ³        ³
                                                   ³        ³      ³        ³
                                                   ³        ³      ³        ³
                                                   ³        ³      ³        ³
                                                  xÀÄÄÄÄÄÄÄÄÙ   0,0ÀÄÄÄÄÄÄÄÄÙx

           RR x_opposite_corner_delta , y_opposite_corner_delta

             shade rectangle relative

             RR  fills a rectangle with corners defined by the current position
             and the command parameters.  The current pen  position and up/down
             state are unchanged. The rectangle edge is not drawn.             


                                                                            p-9
           SA

             select alternate character set

             SA specifies the alternate character set as current. The alternate
             character set is chosen with CA.

           SC [xmin , xmax , ymin , ymax]

             scaling

             SC  sets user units for subsequent drawing.  The units are defined
             by  user values for P1 (xmin,ymin)  and  P2 (xmax,ymax).  Using no
             parameters  turns  scaling off, and  subsequent drawing is done in
             plotter units (1/1016 inch).

           SI [width , height]

             character size absolute

             SI sets the capital letter  box  width and height  in centimeters.
             Letter  spacing  is  1.5  *  width and line spacing is 2 * height.
             Using no parameters with B or A3 paper is the  same as SI.285,.375
             and any other paper is the same as SI.187,.269.

           SL [tan_angle]

             character slant

             SL sets the character slant.  The parameter is  interpreted as the
             tangent  of  the angle from vertical.  Using no parameter sets the
             slant to 0 degrees.

           SM[c]

             symbol mode

             SM  sets symbol  mode, which centers  the symbol mode character at
             any plotted point.  Any character from ASCII 033 to 127 except ";"
             sets symbol mode. Any other character turns symbol mode off.

           SP pen_number

             select pen

             SP selects a pen.  Using 0 or no parameter stores the pen  without
             selecting a new pen.  This is usually done at the  end of a  plot.
             PrintGL ignores any drawing with pen 0.

           SR [width , height]

             character size relative

             SR sets the capital letter box width and height as a percentage of
             P2X-P1X  and P2Y-P1Y.  Letter  spacing is 1.5  *  width  and  line
             spacing  is  2  *  height.  Using no  parameters  is the  same  as
             SR.75,1.5.                                                        


                                                                           p-10
           SS

             select standard character set

             SS specifies the standard character  set as current.  The standard
             character set is chosen with CS.

           TL [positive_length [, negative length]]

             tick length

             TL sets the tick lengths  used by XT and YT.  The  parameters  are
             lengths above  and  below the current position as a  percentage of
             P2Y-P1Y for x-axis ticks and  a percentage of  P2X-P1X  for y-axis
             ticks.

           UC [[pen_control ,] x_delta , y_delta] ...

             user character

             UC specifies  a user defined character.  The pen control number is
             99 for pen down  or -99  for pen  up.  Pen movements are relative,
             with x_delta in  units  of 1/4 the character  width and y_delta in
             units of 1/8 the character height.

           VA

             adaptive velocity - IGNORED

           VN

             normal velocity - IGNORED

           VS

             pen velocity - IGNORED

           WG radius , start_angle , sweep_angle [, chord_angle]

             shade wedge

             WG fills a wedge centered at the current position. The current pen
             position and up/down  state are unchanged.  The wedge  edge is not
             drawn.

           XT

             x-axis tick

             XT draws a vertical line, with length specified by the TL command,
             at  the current position.  The pen position  and up/down state are
             unchanged.                                                        


                                                                           p-11
           YT

             y-axis tick

             YT draws  a  horizontal  line,  with length  specified  by  the TL
             command, at the  current position.  The  pen position  and up/down
             state are unchanged.

           esc.(
           esc.Y

             plotter on

             Esc.(  and esc.Y turn the plotter on.  This is only relevant  with
             the /YY option.

           esc.)
           esc.Z

             plotter off

             Esc.) and esc.Z turn the plotter off. They are only effective with
             the /YY option.  The plotter on  and off commands let you  include
             comments  or  data  to  pass through  to  another  device  in  the
             plotfile. These are flagged as unsupported commands if /YD is set,
             as an indication that you should set /YY.

           esc.@, esc.H, esc.I, esc.M, esc.N, esc.R

             RS-232 device control commands - IGNORED                          


                                                                           p-12
         HP-GL Character Sets -------------------------------------------------

           PrintGL  supports all of the character sets that  are included  with
           the HP 7475 and 7440/17440 except Katakana, and adds character set 5
           and  the  proportional  spaced  fonts   from  the  7550.   PrintGL's
           characters are similar to but not identical to HP's.

              0  ANSI ASCII
              1  9825 character set
              2  French/German
              3  Scandinavian
              4  Spanish/Latin American
              5  Special Symbols (7550 extension)
              6  JIS ASCII
              7  Roman Extensions
              8  Katakana - NOT SUPPORTED BY PRINTGL
              9  ISO IRV (International Reference Version)
             30  ISO Swedish
             31  ISO Swedish For Names
             32  ISO Norway Version 1
             33  ISO German
             34  ISO French
             35  ISO United Kingdom
             36  ISO Italian
             37  ISO Spanish
             38  ISO Portuguese
             39  ISO Norway Version 2

           The character sets specify a font for codes 033..127. Codes 000..032
           and 128..255 are independent of the character set and are all no ops
           except these.

             003  default label terminator
             008  backspace
             009  half backspace
             010  line feed
             011  reverse line feed
             013  carriage return
             014  select alternate character set
             015  select standard character set
             032  space

           Each of  the  character sets  is available as a proportional font by
           adding 10 to the set number.  The proportional  fonts  are kerned to
           improve  appearance (the character spacing is adjusted to compensate
           for  character shape).  Use the LO  command to simplify working with
           proportional fonts. To improve the appearance of large text, use the
           ES command to reduce the character spacing.

           Codes 65 to 81 in character set 5 are symbols designed to be used in
           symbol mode (SM command) or as one character labels.  When used in a
           label (LB command) these characters  are centered at the current pen
           position and leave the pen position unchanged.                      


                                                                           p-13
           The  HP-GL  characters cannot  be printed  with  the  standard ASCII
           character  set.  The file HPGL.CHR is an HP-GL file that can be used
           to print a  replacement  for this page, showing  the character sets.
           Use  the command PRINTGL  HPGL.CHR  /M1  /AO0,0  with  a  /F  option
           specific to your printer to do this.