4DOS  Critical Error Handler

                                Version 2.00

                                     by

                                Niels Jensen
                              Copenhagen  1992

                         --------------------------


   This file is the documentation of the 4DOS Critical Error Handler
   (4DOS24H2.COM).


Generel Rules
~~~~~~~~~~~~~
   The program(s), the source code and this documentation file is given
   free to the PUBLIC DOMAIN.  Hence nobody is allowed to charge any amount
   of money for the files included in this package, and everybody can use
   the programs without paying for it.  Feel free to modify the code to fit
   your own needs but please don't put my name under a modified version if
   redistributed.


Disclaimer
~~~~~~~~~~
   Usage of 4DOS24H1.COM or 4DOS24H2.COM is done fully at your own risk and
   I am not to be held responsible for any kind of damage caused by using
   any of the programs in this archive.


Contents of this documentation
~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~
   Contents of the Archive      - A list of the files included in the
                                  arhive with a short description of each
   About This Documentation     - Things concerning how this documentation
                                  is written
   About 4DOS24H2               - A short introduction
   Highlights                   - A list of the most important features
   Installation                 - How to install the critical error handler
   Usage                        - How to operate 4DOS24H2
   Unloading                    - How to unload 4DOS24H2
   Trouble Shooting             - Look here if you encounter problems with
                                  4DOS24H2


Contents of the archive
~~~~~~~~~~~~~~~~~~~~~~~
   Originally the archive includes the following files:

       4DOS24H2.COM     - The new critical error handler.
       4DOS24H2.ASM     - Assembler source code for 4DOS24H2.COM.
       4DOS24H2.DOC     - This documentation file.
       4DOS24H1.COM     - A special version of the handler which uses only
                          40 columns across the screen.  This is necessary
                          if you use any of the old standard 40 columns
                          text modes and you don't want your display
                          garbled.
       README           - This file contains a short description of the
                          program and a quick-installation guide.  Also
                          any last minute information which could not be
                          integrated in this documentation file can be
                          found here.


About this documentation
~~~~~~~~~~~~~~~~~~~~~~~~
   When refering to the handler in the text the name "4DOS24H2" is used to
   mean "either 4DOS24H1 or 4DOS24H2."  The functionality of the programs
   are identical and both will be treated alike.  The only difference is
   the number of character columns used in their pop-up message windows
   when a critical error occurs.  4DOS24H1 uses only 40 character columns
   while 4DOS24H2 uses 41 columns to show the message window.


About 4DOS24H2
~~~~~~~~~~~~~~
   4DOS24H2.COM is a critical error handler to replace the one build into
   the otherwise excellent 4DOS command interpreter.  The critical error
   handler is the piece of code displaying the notorious "Abort, Retry,
   Ignore" message when you have forgotten to put a disk in the disk drive.
   Due to the nice behaviour of 4DOS it is possible to replace this piece
   of code with an external handler.  This is not possible when using
   COMMAND.COM and therefore this program will not work with COMMAND.COM.

   More specifically 4DOS24H2.COM is a RAM-resident routine that remains in
   the computers storage until you either reboot your computer or turn off
   the power (see also the TECHNICAL DETAILS in the README file).  It is
   written purely in assembler for maximum efficiency and is optimized for
   space efficiency (speed isn't very crucial in this context!).  The
   source code is included in 4DOS24H2.ASM and can be modified and
   reassembled to satisfy individual needs.


   A Special Thanks...

   This program is written on the basis of Patrick Philippot's excellent
   4DOS24H released to the public domain in 1990.  A special thanks
   therefore goes to Patrick Philippot for the original idea, source code
   and program.  Without the inspiration and basis from this work it would
   have been impossible to write 4DOS24H2.


Highlights
~~~~~~~~~~
   *  Gives a clear explanation of the error, it's locus and type
      and shows how to react.

   *  Restores the screen after an error.

   *  Handles all standard text modes.

   *  Handles extended text modes as well (e.g. Tseng ET4000 132x44
      character mode).

   *  Written in assembler and optimized to use minimum amount of
      memory.

   *  Can be loaded high using 4DOS version 4.00 or later.

   *  Source code with comments included.


Installation
~~~~~~~~~~~~
   To install the handler you just need to run 4DOS24H2.COM by putting
   the following line in your 4START.BTM (or 4START.BAT) file:

      [d:path]4DOS24H2.COM

   were [d:path] is the (optional) drive and path to the directory in which
   4DOS24H2 resides.  Drive and path can be omitted only if you keep
   4DOS24H2 in the root directory of your boot drive.  If you don't have a
   4START file consult your 4DOS documentation for details about how to
   create one.  Remember to replace 4DOS24H2 with the actual version of the
   handler (4DOS24H1.COM or 4DOS24H2.COM).

   If you are using 4DOS version 4.0 or later and DOS 5.0 or later you can
   load 4DOS24H2 into high memory (provided you have enough free memory of
   this type) by using the following lines in 4START.BTM:


      IFF "%_SHELL"=="0" THEN
         LOADHIGH  [d:path]4DOS24H2.COM
      ELSE
         [d:path]4DOS24H2.COM
      ENDIFF


   If you have 4DOS version 3.x or earlier it is not possible to load
   4DOS24H2.COM high (well, I haven't found a safe way of doing it yet!).

   If you are using 4DOS version 4.0 or later and a DOS version prior to
   DOS 5.0 it should still be possible to load 4DOS24H2 high using a memory
   manager capable of doing this (QEMM, 386Max etc.).  In that case you
   just need to replace the LOADHIGH command with the equivalent command
   supported by the memory manager.


   IMPORTANT !

   Do NOT run this program from AUTOEXEC.BAT.  If you load 4DOS24H2.COM
   from AUTOEXEC.BAT you will not benefit from the handler during shells
   (when you start a new copy of the 4DOS command interpreter).  The 4DOS
   command interpreter loads its own critical error handler every time a
   new shell is started.  Hence 4DOS24H2.COM need to be reinstalled when
   starting a new shell.  Because 4DOS executes 4START.BTM every time a new
   command interpreter is started (including the first one) the
   reinstallation can be done automatically from 4START.BTM.

   Note:  The handler does NOT actually load a new copy of itself in memory
          but merely reinstalls the one already present without using any
          additional memory.


Usage
~~~~~
   At best you will never see 4DOS24H2.  If 4DOS24H2 pops up a message
   window you have a critical error.  The following are examples of (well
   known) situations all leading to a critical error:

      - You forgot to insert a diskette or to close the diskette drive door
        before selecting the diskette drive.  This is harmless and you can
        recover by pressing the 'A' key to abort the operation (if you are
        a 4DOS user!) or by inserting a diskette and/or close the drive
        door before pressing the 'R' key to retry the operation.

      - Your diskette is damaged in some way.  This is often a *REAL*
        critical error and can be difficult to recover from. You will
        probably have to use a disk oriented tool to resque your data on
        the diskette if possible at all.

      - Your printer is offline or out of paper when you try to print
        something.  This is normally harmless and typically you can recover
        by switching on the power or setting your printer online or by
        inserting paper.

   There are more rare situations which will also lead to critical errors
   but hopefully you will not see them too often.

   When a critical error occurs 4DOS24H2 will pop up a window showing the
   following information:


    +---------------- 4DOS Critical Error Handler -----------------+
    |                        Version 2.00                          |
    |                                                              |
    |   A description of the error type (read or write error)      |
    |   and where it occured (e.g. the drive letter or port).      |
    |                                                              |
    |   If possible a somewhat more specific error description.    |
    |                                                              |
    |   Which possibilities you have to react and how to respond.  |
    |                                                              |
    +--------------------------------------------------------------+


   You may or may not have all of the four respond possibilities: Abort,
   Retry, Ignore, Fail -- this depends on the kind of error.  Aborting will
   normally stop the program/command that caused the error and return you
   to the 4DOS command line.  Choosing to retry will repeat the operation
   that caused the error and only if no errors occur this time the
   program/command will continue normally.  Choosing ignore will let the
   program/command continue as if no error ever occurred, while the fail
   respond will try to inform the program/command that an error has
   occurred.
   
   You can respond by pressing the first letter of the action, e.g. an 'a'
   to (a)bort the current operation, an 'i' to (i)gnore the error, an 'r'
   to (r)etry the operation and an 'f' to (f)ail the operation.  The actual
   case of the letter is unimportant and will be ignored.

   As a special feature of 4DOS24H2 you can also press Esc, 'q', 'x' or ^C
   (Ctrl-C) instead of 'a' to abort.  These keys are often used to quit or
   exit other applications and for some users they seem more natural.
   Likewise you can press Spacebar or Enter to retry the operation as an
   alternative to 'r'.  There are no alternative keys for the Ignore
   operation as I could not find any better than 'i'.  Any other keys will
   be ignored by the handler.

   When the critical error situation is properly handled the original user
   screen is restored upon exit.


Unloading
~~~~~~~~~
   If you for some reason should need to unload 4DOS24H2 you will either
   have to reboot your computer or use the TSR utilities from TurboPower
   Software (Public Domain package available on many BBS-systems) to remove
   4DOS24H2.COM from memory.  To keep memory usage at a minimum this
   feature is not implemented.

   Note:  If you want to remove the handler by rebooting your computer
          remember to edit your 4START.BTM file and remove the line(s)
          responsible for loading 4DOS24H2.COM or put a REM command in
          front of it/them.  Otherwise the handler will be loaded before
          you are given control.


Trouble Shooting
~~~~~~~~~~~~~~~~
   4DOS24H2 is very easy to install and use and should not cause trouble.
   In some rare situations, however, you might experience a problem covered
   in this section.

   More than one copy of 4DOS24H2 in memory ...

     If 4DOS24H2 seems to load a new copy of itself into memory every time
     you make a shell (and thereby wasting useful memory) you may have
     loaded a resident program (TSR) which interferes with 4DOS24H2. If you
     can identify the TSR causing the trouble you can sometimes recover by
     installing your TSR before 4DOS24H2 (e.g. in CONFIG.SYS using INSTALL
     under DOS 4.0 or later).

     If this is not possible or does not seem to solve the problem you may
     try to edit the source code and reassemble it.  The trouble might be
     that for some purpose your TSR uses interrupt 61h.  4DOS24H2 itself
     uses interrupt vector 61h to see if it is already installed and can
     not identify itself in memory if this interrupt is hooked by some TSR
     after installation of 4DOS24H2.  To solve the problem you can change
     the vector used by 4DOS24H2 by editing the EQU directive in line 96 of
     the source code:

         IDvector    EQU   61h

     to reflect another vector number.  Suitable numbers are vector numbers
     between 60h and 66h which are user defineable interrupt vectors.
     After editing you must reassemble according to the directives in the
     source code.


   4DOS24H2 seems to dissapear after a critical error ...

     When you have had a critical error and have recovered the next time
     you may see the original critical error handler responding.  This
     problem could be caused by two reasons.  Either you have started a new
     shell and forgotten to reinstall 4DOS24H2 or you may be trying to load
     4DOS24H2 high using 4DOS version 3.x.

     In the first case you may be loading 4DOS24H2 from AUTOEXEC.BAT or may
     otherwise exclude 4DOS24H2 from reloading when a new shell is started.
     Load 4DOS24H2 from 4START.BAT if you are not already doing this --
     refer to the Installation section for the correct installation
     procedure.

     If you are using 4DOS version 3.x you may be trying to load 4DOS24H2
     high using something like:

        COMMAND /C LH 4DOS24H2.COM

     You must either upgrade 4DOS or use conventional memory in order to
     keep the contact with 4DOS24H2.  Refer to the Installation section for
     details about loading 4DOS24H2 into conventional memory.


   "Divide overflow" error when loaded high ...

     If you get a "Divide overflow" error during a shell you may be trying
     to reload 4DOS24H2 using the LOADHIGH command but without having
     enough free high memory.  This is not a bug in 4DOS24H2 but the error
     is sometimes reported by 4DOS.

     Normally this situation does not lead to an error since 4DOS auto-
     matically uses conventional memory when no upper memory is available.
     However, the problem occurs while the excellent public domain ANSI
     driver NNANSI.COM version 9.92 by Tom Almy is loaded into high memory.
     At the moment I do not know of any other programs causing the same
     problems; neither do I know if this is a bug in the ANSI driver or in
     4DOS version 4.01, rev. B which I used for testing 4DOS24H2 in high
     memory.

     The solution is to load 4DOS24H2 high only when it is first installed.
     Reloading (when shelling) should be done using conventional memory
     only.  This can be accomplished by exploiting the special 4DOS
     environment variable "%_SHELL" and use the IFF construction shown in
     the Installation section.  Refer to this section for more information.


Epilogue
~~~~~~~~
   It took quite a long time to create 4DOS24H2 but the time spent was
   really funny and certainly not wasted.  I learned the 8088 assembler and
   some new tricks on how to optimize assembler code and somehow it became
   an obsession to see how much the code could be squeezed.

   I don't think it is possible to "squeeze" the memory consumption of the
   code much more than a few bytes but I would be happy to hear from every-
   body who succeeds in optimizing the code further without losing its
   features.

   You can reach me through Internet at the following adress:

        ehlig@ask.diku.dk

   Please use subject: 4DOS24H2



                               Enjoy and have fun


                                  Niels Jensen,  Copenhagen  August 1992
                                         (last revised May 1993)