Clone
                           A Disk Duplication Utility

                                       by

                                   Eric Tauck
                               1304 Deerpass Road
                             Marengo, IL 60152-9644
                                      U.S.A

                             Compuserve: 72457,1557
                       Internet: 72457.1557@compuserve.com

        Clone performs the same function as DISKCOPY, but with several
        improvements.  The major features of Clone are duplicating high
        capacity disks in a single drive without disk swapping, and
        writing multiple target disks without rereading the source disk.
        Other features include extra control over formatting, data veri-
        fication, a progress indicator, the ability to cancel a duplica-
        tion at any time, and improved disk serialization.

        Clone requires a PC/XT/AT compatible and DOS 3.0 or higher.  For
        reading high capacity disks (anything larger than a regular 360K
        disk), Clone needs XMS memory, EMS memory, or a hard or RAM disk
        to store the disk image.  Clone may be used and distributed
        freely.

        Clone syntax:

          CLONE X: [Y:] [switches]

          X:  The source drive (i.e. the drive to read from).

          Y:  The target drive (i.e. the drive to write to).  If the
              target drive is absent, it is assumed to be the same as the
              source drive.

        The switches may be specified on the command line or in the
        environment using the environment variable CLONE or CLONE_ET (use
        CLONE_ET if CLONE is already being used for something else).
        Switches that are used all the time (like image paths) should be
        stored in the environment, usually with a SET statement from the
        AUTOEXEC.BAT file.  Switches on the command line override switch-
        es in the environment.

        Clone switches:

          /C    Produce endless copies.  Clone will continue producing
                copies until ESC is pressed.

          /C:n  Produce n number of copies.  Clone will create a specific
                number of copies.  The default is /C:1.

          /E+   Use expanded (EMS) memory.  Clone will use expanded
                memory to store any of the source disk that doesn't fit




                in conventional or extended memory.  EMM386.SYS (or a
                compatible driver) must be installed to make expanded
                memory available.  This switch is the default.

          /E-   Don't use expanded (EMS) memory.  Clone will not try to
                access expanded memory.

          /F    Format target disk if necessary.  Clone will attempt to
                determine if the target disk is unformatted and then
                format it if necessary.  This is the default format
                setting.  This switch undoes the effects of the /F+ and
                /F- switches.

          /F+   Always format the target disk.

          /F-   Never format the target disk.  Clone will display an
                error if an unformatted disk is used as a target disk.

          /I:p  Define the image path p.  Image paths are the locations
                where Clone should store portions of the source disk that
                don't fit in memory.  Multiple image paths may be listed.
                Multiple image paths are used sequentially as their
                respective disks becomes full.  If no image path is
                specified, Clone will use the TEMP or TMP environment
                variable.

          /M:n  Set to message level n.  There are three message levels:
                1 to 3.  At message level one, Clone displays the least
                amount of information; and at message level three, Clone
                displays the most amount of information.  The default is
                /M:2.

          /N+   Enable disk serialization.  All target disks receive a
                serial number according to the serial number type as set
                by the /N:n, /N:D, or /N:T switches.  This switch is the
                default.

          /N-   Disable disk serialization.  All target disks will have
                the same serial number as the source disk.  Disk serial
                numbers were introduced with DOS version 4.00.  This
                switch should be used on systems running older versions
                of DOS.

          /N:n  Use n for all target disk serial numbers.  This switch
                lets you specify a specific serial number.  The number n
                can range from 0 to 4294967295.  Note that DOS typically
                displays the serial number in hexadecimal notation
                (rather than decimal notation used in this switch).

          /N:D  Use the DOS convention for creating target disk serial
                numbers.  This switch is the default.

          /N:T  Use the current time and date to create target disk
                serial numbers.  Both this switch and the /N:D switch use
                the time and date to generate serial numbers, but only




                this switch is guaranteed to produce a unique serial
                number every second.  Serial numbers generated from this
                switch can also be converted back to the date and time
                from which they were created.

          /P+   Turn source and target prompts on.  This switch is the
                same as using both the /S+ and /T+ switches.

          /P-   Turn source and target prompts off.  This switch is the
                same as using both the /S- and /T- switches.

          /R:n  Allow n errors when reading the source disk.  This switch
                sets the maximum number of unreadable tracks on the
                source disk.  If too many unreadable tracks are encoun-
                tered, the copy operation is aborted.  The default is
                /R:0 (no bad tracks allowed).

          /S+   Prompt for source disk.  Clone will display a message
                asking that the source disk be inserted and wait for a
                key to be pressed.  If ESC is pressed, Clone will termi-
                nate.  This switch is the default.

          /S-   Don't prompt for source disk.  Clone will start reading
                from the source drive immediately.

          /T+   Prompt for target disk.  Clone will display a message
                asking that the target disk be inserted and wait for a
                key to be pressed.  If ESC is pressed, Clone will termi-
                nate.  This switch is the default.

          /T-   Don't prompt for target disk.  Clone will start writing
                to the target drive as soon as the source disk has been
                fully read.  This switch will only work if the source and
                target drives are different AND only a single copy is
                being made (/C:1).

          /V    Set to verify level 3.  See the description of /V:n
                below.

          /V:n  Set to verify level n.  There are three verify levels: 1
                to 3.  Verify level one is no verify, level two checks to
                see if each track is readable after writing it, and level
                three reads each track back and compares it.  The default
                is /V:0.

          /W:n  Allow n errors when writing the target disk.  This switch
                sets the maximum number of unwriteable tracks on the
                target disk.  If too many unwriteable tracks are encoun-
                tered, the copy operation is aborted.  The default is
                /W:0 (no bad tracks allowed).

          /X+   Use extended (XMS) memory.  Clone will use extended
                memory to store any of the source disk that doesn't fit
                in conventional memory.  HIMEM.SYS (or a compatible
                driver) must be installed to make extended memory avail-




                able.  This switch is the default.

          /X-   Don't use extended (XMS) memory.  Clone will not try to
                access extended memory.

        A summary of these switches can be displayed by running:

          CLONE ?

        Example configuration, set in the AUTOEXEC.BAT file:

          SET CLONE=/I:D: /I:C: /S- /R:10

        This tells Clone to store the image on drive D: (presumably a RAM
        disk), and if it becomes full, to store the rest of the image on
        drive C: (a hard disk).  Also, the source disk prompting is
        turned off and 10 read errors are allowed.

        The following is a list of changes made to Clone according to the
        version number:

        1.00  Initial release.

        1.10  /E switch added (later changed to /R).  Messages changed:
              track read error added, disk parameters mostly removed, and
              image file list removed.

        1.11  Prompts for new disk if incompatible media (rather than
              aborting).

        1.20  Displays disk type in a more readable format.

        2.00  Complete rewrite.  XMS and EMS memory supported, disk
              serialization supported, error handling improved, can
              format low density disks in high density drives (well, it
              tried but failed), can press ESC at any time to abort, and
              the displayed enhanced.  Several switches and the format of
              switches have been changed: you now need a colon before
              numbers and paths; /I always specifies a path (never a
              file); and the /M, /N, /P, /V, and /W switches have been
              added.

        2.10  Improved EMS detection and formatting procedure (formatting
              should work now).  Added /E and /X switches to
              enable/disable expanded/extended memory usage.

                             DISCLAIMER OF WARRANTY

        THIS SOFTWARE AND MANUAL ARE DISTRIBUTED "AS IS" AND WITHOUT
        WARRANTIES AS TO PERFORMANCE OF MERCHANTABILITY OR ANY OTHER
        WARRANTIES WHETHER EXPRESSED OR IMPLIED.  BECAUSE OF THE VARIOUS
        HARDWARE AND SOFTWARE ENVIRONMENTS INTO WHICH THIS PROGRAM MAY BE
        PUT, NO WARRANTY OF FITNESS FOR A PARTICULAR PURPOSE IS OFFERED.

        GOOD DATA PROCESSING PROCEDURE DICTATES THAT ANY PROGRAM BE




        THOROUGHLY TESTED WITH NON-CRITICAL DATA BEFORE RELYING ON IT.
        THE USER MUST ASSUME THE ENTIRE RISK OF USING THE PROGRAM.  ANY
        LIABILITY OF THE SELLER WILL BE LIMITED EXCLUSIVELY TO PRODUCT
        REPLACEMENT OR REFUND OF PURCHASE PRICE.