June 1, 1994
   _ _ _
  / / (_)
 _\ \ \
(_)_/_/  Find-ATA v1.0 - An ATA interface identify drive utility.

Seagate Technology, Inc.
B-5 Technical Support
920 Disc Drive
Scotts Valley, CA 95066

Usage: FIND-ATA [P or S] [M or S] [optional: R or D]  or....
       FIND-ATA /filename.ATA

switches:
P or S        -  Primary or Secondary Port Address (these default to
                 1F0h and 170h)

M or S        -  Master or Slave drive

The optional R and D switches will only work if the Port and Drive
switches are also set on the command line.  ex: Find-ATA P M D

R             -  allow command line redirection (this feature is
                 useful for redirecting the output to a printer or a
                 file)

D             -  dump the Identify binary data to <filename>.ATA (this
                 allows a copy to be saved that can be studied at a
                 later time. A "collection" of various drive files
                 might be useful for reference purposes.)


/filename.ATA -  load a previously saved Identify data dump.

(no switches) -  program will prompt for Port and Drive info


Find-ATA is designed for the support of users with Seagate disc drives.


A little background:

The ATA interface has evolved rapidly since its initial design by
Compaq Corporation.  After refining the basic ATA interface concepts
and circuitry, Compaq Corporation worked with Imprimis (now a part of
Seagate) to build the first ATA interface drive.  At this stage, the
interface was far from being an accepted standard.  However, it was a
natural extension of the ATA I/O bus, and gained industry-wide
acceptance because most of the necessary framework needed for the
implementation was already present in the host machine.

Initially, there were no industry-wide standards for implementing the
ATA interface, leaving manufacturers free to extend and improve upon
it.  In the latter part of 1988, a Common Access Method (CAM)
committee was established to develop such standards.  Their results
were adopted by the American National Standards Institute (ANSI) with
the intent of creating a common ATA command specification.

The ANSI standard for the ATA interface now provides specifications
for mandatory commands, signal conventions, register descriptions and
other information necessary for basic compatibility across
manufacturers and platforms.  The current ANSI specification includes
provisions for extended features such as caching and power management,
while also providing options for vendor-specific enhancements.

The "Identify Drive" command is defined for the ATA interface.  This
valuable command, when executed, will return to the host 512 bytes
which describe the drive and its available features.  It is very
similar to the original Identify drive developed for the older ESDI
interface and is analogous to the SCSI interface's Mode Sense command,
albeit with less detail.  Find-ATA is a simple utility which helps
organize the data in a readable form.

The following screen print shows the Identify Drive bytes that
correspond to the Find-ATA field names.

ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍµ Find-ATA v1.0 ÆÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
³                                                                        ³
³     Drive: 27-46                                      Port:            ³
³  Serial #: 10-19                 CMOS Type:        Unit:               ³
³  Firmware: 23-26                                                       ³
³            Hardware       DOS            Current          Max ECC: 22  ³
³ Cylinders: 1                             54                            ³
³     Heads: 3                             55                            ³
³   Sectors: 6                             56                            ³
³  Capacity:                               57-58                         ³
³                                                                        ³
³                     Available  Information                             ³
³ R/W Multiple Mode:  47.7-0                 Current: 59.7-0             ³
³          LBA Mode:  49.9       total sectors 60-61                     ³
³          DMA Mode:  49.8       Single: 62         Multi: 63            ³
³ Advanced PIO Mode:  64.7-0               +,-IORDY: 68,67               ³
³                                                                        ³
³  Default PIO Mode:  51.15-8                                            ³
³                                                                        ³
³  Buffer: 21   - Type: 20                                               ³
³                                                                        ³
³                                                                        ³
ÔÍÍÍÍÍÍÍµ Copyright 1994 Seagate Technology, Inc. All rights reserved. ÆÍ¾

IDENTIFY DRIVE command

The Identify Drive command (command code ECh) transfers information
about the drive to the host.  When the command is issued, the drive
sets BSY, prepares to transfer a single 512-byte block of data, sets
DRQ, and generates an interrupt.  The host then reads the data from
the drive.  The data is organized as shown in the table below.  All
reserved bits or words are zero.

Words 53 to 49 and 62 to 63 change depending on the current operating
mode of the drive.  All other words are constant for a particular
drive.

An asterisk (*) indicates words for which a value of 0000h indicates
parameter not specified.

The following table is organized in words.  When a lower order of
detail is required, the bits under consideration are placed after a
period.  For example word 49 bit 8 would be expressed as 49.8.  If a
range of bits within a word is needed, a hyphen is placed between the
hi-lo range.  For example word 49 bits 7 to 0 is written as 49.7-0.

Word.Bit      Description
==========================
0.15      0 = reserved for non magnetic drives
0.14      1 = format speed tolerance gap required
0.13      1 = track offset option available
0.12      1 = data strobe offset option available
0.11      1 = rotational speed tolerance is > 0.5%
0.10      1 = disc transfer rate > 10 Mbit/sec
0.9       1 = disc transfer rate <= 10 Mbit/sec but > 5 Mbit/sec
0.8       1 = disc transfer rate <= 5 Mbit/sec
0.7       1 = removable cartridge drive
0.6       1 = fixed drive
0.5       1 = spindle motor control option implemented
0.4       1 = head switch time > 15 usec
0.3       1 = not MFM encoded
0.2       1 = soft sectored
0.1       1 = hard sectored
0.0       0 = ATA reserved (should be zero)
1         Number of user-addressable cylinders in the default
          translation mode.  When the formatted capacity of the drive
          exceeds 528 MB this field is set to 1024.
2         ATA reserved (should be zero)
3         Number of user-addressable heads in the default translation
          mode.  When the formatted capacity of the drive exceeds 528
          MB this field is set to 16.
4         Number of unformatted bytes per track
5         Number of unformatted bytes per sector
6         Number of user addressable sector in the default translation
          mode.  When the formatted capacity of the drive exceeds 528
          MB this field is set to 63.
7-9       ATA reserved (should be zero)
10-19  *  Serial number (20 ASCII characters and padded with spaces).
20     *  Buffer type.
          0000h = not specified
          0001h = a single-ported, single sector buffer which is not
                  capable of simultaneous data transfers to or from
                  the host and the disc.
          0002h = a dual ported multisector buffer capable of
                  simultaneous data transfers to or from the host and
                  the disc.
          0003h = a dual ported multisector buffer capable of
                  simultaneous transfers with a read caching
                  capability.
          0004h through FFFFh are reserved.
21     *  Buffer size in 512-byte increments
22     *  Number of ECC bytes available on read/write long commands.
23-26  *  Firmware revision (8 ASCII characters and padded with spaces
          [20h]).
27-46  *  Model number (40 ASCII characters and padded with spaces
          [20h]).
47.15-8   Seagate reserved.
47.7-0    00h = Read/Write multiple commands not implemented;
          xxh = Maximum number of sectors that can be transferred per
                interrupt on read and write multiple commands.
48        0000h = cannot perform double-word I/O
          0001h = can perform double-word I/O.  (included for
                  backwards compatible use)
49        Capabilities
49.15-13  ATA reserved (should be zero)
49.12     ATA reserved for advanced PIO mode support (should be one)
49.11     1 = IORDY supported (required for PIO modes > 2)
          0 = IORDY may be supported
49.10     1 = IORDY can be disabled
49.9      1 = LBA mode supported
49.8      1 = DMA mode supported
49.7-0    Seagate reserved.
50        ATA reserved
51.15-8   PIO data transfer cycle timing mode
51.7-0    Seagate reserved.
52.15-8   DMA data transfer cycle timing mode
52.7-0    Seagate reserved.
53.15-2   ATA reserved
53.1      1 = the fields reported in words 64 - 70 are valid
          (required for PIO modes > 2 or multiword DMA modes > 0)
          0 = the fields reported in words 64 - 70 are not valid
53.0      1 = the fields reported in words 54 - 58 are valid
          0 = the fields reported in words 54 - 58 are not valid
54        Number of current cylinders
55        Number of current heads
56        Number of current sectors per track
57        Current capacity in sectors HI-word
58        Current capacity in sectors LO-word
59.15-9   ATA reserved.
59.8      1 = Multiple sector setting is valid
59.7-0    xxh = Current setting for number of sectors that can be
          transferred per interrupt with Read/Write multiple commands
60        Total number of user addressable sectors HI-word (LBA mode
          only)
61        Total number of user addressable sectors LO-word (LBA mode
          only)
62.15-8   Single word DMA transfer mode active
62.7-0    Single word DMA transfer modes supported
63.15-8   Multiword DMA transfer mode active
63.7-0    Multiword DMA transfer modes supported
64.15-8   ATA reserved.
64.7-0    Advanced PIO transfer modes supported (bit significant
          field: 00000001 means PIO mode 3 supported, bits 7-1 are
          reserved for future use)
65        Minimum multiword DMA transfer cycle time per word in
          nanoseconds
66        Manufacturer's recommended  multiword DMA transfer cycle
          time per word in nanoseconds during a single sector host
          transfer while performing a multiple sector Read DMA or
          Write DMA command over all locations on the media under
          nominal conditions. If a host attempts to run at a faster
          cycle rate by operating at a cycle time of less than this
          value, the drive may be forced to negate DMARQ to prevent
          data corruption.  The rate at which DMARQ is negated could
          result in reduced throughput despite the faster cycle rate.
67        Minimum PIO transfer cycle time without flow control in
          nanoseconds (required for PIO modes > 2)
68        Minimum PIO transfer cycle time with IORDY flow control in
          nanoseconds (required for PIO modes > 2
69-70     ATA reserved for advanced PIO mode support
71-127    ATA reserved.
128-159   Seagate reserved.
160-255   ATA reserved.

Note: The definition of each of the Identify Drive bytes is subject to
change by the ATA review committee. Typically, once a definition is in
place it will not be changed.  Fields which are listed as "ATA
reserved" are the ones to watch for change.

=====Rev=Hist===============
Written with Borland Pascal v6.0 by B.Rudock, R.Dimick and R.Stacy.

Revision History:

        6/94   v1.0    Public release.

=====Legal=Disclaimer=======

                          LICENSE AGREEMENT

Seagate provides the accompanying object code software ("Software")
and nonexclusively licenses its use on the following terms and
conditions. The Software is copyrighted by Seagate.  YOU ASSUME FULL
RESPONSIBILITY FOR THE SELECTION OF THE SOFTWARE TO ACHIEVE YOUR
INTENDED PURPOSES, FOR THE PROPER INSTALLATION AND USE.  SEAGATE DOES
NOT WARRANT THAT THE SOFTWARE WILL MEET YOUR REQUIREMENTS, THAT THE
SOFTWARE IS FIT FOR ANY PARTICULAR PURPOSE OR THAT THE USE OF THE
SOFTWARE WILL BE ERROR FREE.  SEAGATE EXPRESSLY DISCLAIMS ALL
WARRANTIES, WHETHER ORAL OR WRITTEN, EXPRESSED OR IMPLIED, INCLUDING
WITHOUT LIMITATION WARRANTIES OF MERCHANTABILITY OR FITNESS FOR A
PARTICULAR PURPOSE.  IN NO EVENT WILL SEAGATE BE LIABLE TO YOU, YOUR
CUSTOMERS OR OTHER USERS FOR ANY INDIRECT, INCIDENTAL, CONSEQUENTIAL,
SPECIAL OR EXEMPLARY DAMAGES ARISING OUT OF OR IN CONNECTION WITH THE
USE OR INABILITY TO USE THE SOFTWARE.

End of License agreement.

=====Other==================
Available on the Seagate Tech Support BBS (408)438-8771 and many fine
and helpful BBS's around the world:

Specifications and jumper drawings for all Seagate Disc Drives and
Controllers.

Reprints of Installation Guides.

Troubleshooting essays.

FINDTYPE - Utility which displays bios drive type table and matches a
Seagate model to the best drive type.  Also prints complete
specifications lists and much more!

FINDINIT - Utility for Seagate controllers and host adapters that have
onboard bios. Queries the system to determine bios memory address and
initiates low-level format.

DESK REFERENCE - Hypertext data system for all Seagate products,
troubleshooting, other OEM phone numbers and much, much more. A must
for dealers who do a fair amount of support for Seagate products.

SEAGATE FORMAT - A lo-level and mid-level formatting utility for AT
systems (286+) which supports MFM, RLL, ESDI and ATA interface drives.

-=EOF: FIND-ATA.DOC=-