ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ·
      ³                                                                   º Û
      ³                                                                   º Û
      ³                           A M I s e t u p                         º Û
      ³                                                                   º Û
      ³ Documentation                                                     º Û
      ³                                                                   º Û
      ³ Copyright (c) Robert Muchsel 1992-1994                            º Û
      ³ All rights reserved.                                              º Û
      ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼ Û
       ßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßß

      AMIsetup is an external setup program for 386/486 PCs with modern AMI
      BIOS (AMI Hi-Flex BIOS).

      If you ever considered your built-in setup as incomprehensible,
      boring, inconvenient or incomplete, you've been waiting for
      AMIsetup.

      AMIsetup can save your configuration on disk and restore it. You
      can even change setup options missing in your BIOS! AMIsetup cracks
      your password and prints your setup as a list. You can install IDE
      hard disks automatically! Add comprehensive on-line help, Soundblaster
      support and an on-line reference that explains many setup options.
      Of course you can protect AMIsetup itself with a password.

      For diagnostic purposes, AMIsetup can on many machines measure the
      DMA frequency (avoid burnout of the DMA chip due to overload) and
      display the CMOS error flags. You can compare the CMOS real time
      clock and DOS time, change setup registers manually (experts only)
      and display the BIOS ID. Switch AMIsetup to high resolution video
      mode (EGA/VGA) and use the mouse...

      And once you are finished, AMIsetup can reboot your computer.

      Professionals will like the batch mode of AMIsetup. Configure
      identical computers in blitz speed!


      Important
      ÄÄÄÄÄÄÄÄÄ

       ÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜ
      ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
      ³                                                                    ³
      ³                         USE AT YOUR OWN RISK!                      ³
      ³  This program is based on undocumented data structures.            ³
      ³  Improper use, program errors or bad luck can cause hardware,      ³
      ³  software and stored data of the computer be irreversibly damaged! ³
      ³  The user is advised always to make adequate Back Ups of all       ³
      ³  valuable files or Data. Because he can have no control over how   ³
      ³  this program is used                                              ³
      ³          THE AUTHOR ACCEPTS NO LIABILITY FOR ANY DAMAGE!           ³
      ³                                                                    ³
      ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾
       ßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßß

      No part of this documentation may be reproduced, transmitted,
      transcribed, stored in any retrieval system, or translated into any
      other language or computer language in whole or in part, in any form
      or by any means, whether it be electronic, mechanical, magnetic,
      optical, manual or otherwise, without prior written consent of the
      author, Robert Muchsel.

      The author disclaims all warranties as to this software, whether
      express or implied, including without limitation any implied warranties
      of merchantability, fitness for a particular purpose, functionality,
      data integrity or protection, in so far as permitted by applicable
      legislation.

      All trademarks are property of their respective owners and appear for
      identification purposes only.



      Shareware
      ÄÄÄÄÄÄÄÄÄ

      ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
      ³  Writing this program has taken lots of work. If you continue     ³
      ³  using it after a reasonable trial period of 30 days, you have    ³
      ³  to pay a small fee to the author.                                ³
      ³                                                                   ³
      ³  SHAREWARE is NOT FREE SOFTWARE. You can, however, test shareware ³
      ³  before purchasing it.                                            ³
      ³                                                                   ³
      ³  For detailed information, see appendix A.                        ³
      ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

      You are encouraged to copy and pass on the unregistered shareware
      version of this program, if
      - the program is distributed in its original form
        (complete, unmodified, uninstalled)
      - the distribution fee does not exceed the equivalent of DM 15.-.

      It is forbidden to distribute the program bundled with books,
      magazines, etc. (including "bookware").

      The information contained in the on-line reference for registered users
      must not be copied, published or separated from the program. The author
      has taken every care to ensure the technical correctness of the
      information, but cannot accept any liability in case of any error.



      If you have comments or find an error, please send them to the author!



                                     Contents
                                     ÄÄÄÄÄÄÄÄ

        1   Caution!
        2   Starting the program
        3   Menus in detail
            3.1 ð (System) menu
            3.2 BIOS menu
            3.3 CMOS menu
            3.4 Setup
                1. Standard setup
                2. Extended/chipset setup
                3. Change register
                4. Password
                5. Load ROM setup defaults, load ROM power-on defaults
                6. Print current setup
                7. Analyze ID string
                8. Save changes and quit
                9. Exit without saving
            3.5 Options dialogue
            3.6 Help menu
        4   Key shortcuts

            Appendix

        A   Registration, limits of the shareware version,
            addresses, upgrades, about the author
        B   AMIsetup and OS/2 2.x, AMI BIOS and OS/2, Windows, Windows NT
        C   Known problems
            1. Is AMIsetup compatible with your BIOS?
            2. Frequent errors with compatible BIOS versions
            3. Stopgap: -OVERRIDE
            4. Additional trouble shooting options
        D   Glossary
        E   If the machine won't boot...
        F   Switching to the English user interface
        G   Soundblaster
        H   EISA
        I   Batch mode
        J   Obtaining new or bug fixed program revisions
        K   Tested BIOS revisions


            What's new

            Changes are described in a separate file, AMISETUP.NEW.



      1  Caution!
      ÄÄÄÄÄÄÄÄÄÄÄ

      If you are not familiar with setup options or if you don't know
      what they do, please consider whether changing the setup options
      is really necessary.

      ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
      ³  On many PCs, the DMA clock speed can be changed.                 ³
      ³  This may work at first, but later the DMA chip may be destroyed, ³
      ³  thus making the motherboard useless!                             ³
      ³                                                                   ³
      ³  Another critical point is the password option. Since you cannot  ³
      ³  erase CMOS RAM on some main boards (see appendix E), it may      ³
      ³  happen that because of - forgetfulness, BIOS errors, different   ³
      ³  keyboard layout, etc. - you are irreversibly locked out of your  ³
      ³  computer.                                                        ³
      ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

      Before making ANY change, ask yourself:
      - is it necessary?
      - what are the consequences?

      AMIsetup saves your configuration into a file after installation
      and whenever you invoke the program. However, this works only if
      you don't use AMIsetup on a write protected diskette.


      ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
      ³  N E V E R   C H A N G E   A   R U N N I N G   S Y S T E M  !!!   ³
      ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

      WHEN DID YOU DO YOUR LAST COMPLETE BACKUP???


      2  Starting the program
      ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

      First of all, please read the manual and the file "AMISETUP.NEW".

      The program needs write access to the current directory. Diskettes
      must not be write protected if file operations are to be used.

      Normally, you start AMIsetup without additional command-line options.
      There are exceptions though (see appendix C). You should read
      appendix B if you want to use AMIsetup under OS/2.

      If you are using an LCD screen, invoke AMIsetup by "AMISETUP -MONO".

      Adaptec SCSI Controllers: Be sure to use the ASPI4DOS driver to avoid
      possible problems with the memory management unit.

      If using AMIsetup for the first time, you have to choose the desired
      language:

              ÚÄÄÄÄÄÄÄÄÄÄÄÄ Welcome / Willkommen ! ÄÄÄÄÄÄÄÄÄÄÄÄ¿
              ³                                                ³
              ³  This is a bilingual version of AMIsetup.      ³
              ³  For English help texts and user interface,    ³
              ³  press [E].                                    ³
              ³                                                ³
              ³  Dies ist eine zweisprachige Version von       ³
              ³  AMIsetup. Dr�cken Sie [D] f�r deutsche Hilfe- ³
              ³  texte und Benutzeroberfl„che.                 ³
              ³                                                ³
              ³  [E] English version     [D] deutsche Version  ³
              ³                                                ³
              ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄAMIsetupÄÙ

      Should you decide on the German version, please continue reading in
      the file "AMISETUP.DOK".

      Next you must to accept the warning message with a "Y":

              ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ C A U T I O N ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
              ³                                                ³
              ³              USE AT YOUR OWN RISK!             ³
              ³                                                ³
              ³  This program is based on undocumented data    ³
              ³  structures. Hard- and software and stored     ³
              ³  data could be damaged irrevocably!            ³
              ³                                                ³
              ³ THE AUTHOR WILL NOT BE LIABLE FOR ANY DAMAGES! ³
              ³                                                ³
              ³ [Y] accept and start program   [N] back to DOS ³
              ³                                                ³
              ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄAMIsetupÄÙ

      If you have set a password in the "Options" dialogue (3.5), you will
      be prompted to enter it.

                   ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍ Password ÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
                   º                                      º
                   º AMIsetup is password protected.      º
                   º Please enter the current password.   º
                   º                                      º
                   º  Password    ****                    º
                   º                                      º
                   º                                      º
                   º          OK   Ü      Help  Ü         º
                   º        ßßßßßßßß     ßßßßßßßß         º
                   ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

      Next, a dialogue box containing program revision and registration
      number (or "UNREGISTERED") appears. If you haven't yet paid for
      AMIsetup and a registration number appears anyway, you've got an
      (illegal) pirated copy. Please contact the author.

                  ÉÍ[þ]ÍÍÍÍÍÍÍÍÍÍ Information ÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
                  º                                         º
                  º             AMIsetup v2.60              º
                  º         REGISTERED (#.........)         º
                  º                                         º
                  º  Copyright (c) 1992-94 Robert Muchsel   º
                  º           All rights reserved           º
                  º                                         º
                  º                                         º
                  º           Heap memory:  84080           º
                  º               ISA System                º
                  º                                         º
                  º            OK    Ü     Help   Ü         º
                  º          ßßßßßßßßß    ßßßßßßßßß         º
                  ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

      º You can also view this entire file from AMIsetup ("Help|View
      º AMISETUP.DOC").


      Quick start
      ßßßßßßßßßßß

      The most frequent error stems from use of AMIsetup with a memory
      manager (386MAX, QEMM-386, EMM386) loaded - EMM386 is installed
      automatically by the DOS 5/6 and Windows setup.
      Please note para 3.2 "BIOS|Write image to file" and appendix C.


      3  Menus in detail
      ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

      Using the mouse or pressing <F10>, you get to the main menu bar.
      There, you have the following pull down menus at your disposal:

       ð  BIOS  CMOS  Setup  Options  Help
      °°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

      Pressing <F1> gets you help. The on-line help contains nearly all of
      the manual.

      Hint for mouse users: The right button is equivalent to <Esc>.


      3.1 ð (System) menu
      ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

        ð  BIOS  CMOS  Setup  Options  Help
       ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿ °°°°°°°°°°°°°°°°°
       ³ About         Shift-F10 ³ °°°°°°°°°°°°°°°°°
       ³ Evaluate DMA clock      ³ °°°°°°°°°°°°°°°°°
       ³ Test coprocessor status ³ °°°°°°°°°°°°°°°°°
       ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´ °°°°°°°°°°°°°°°°°
       ³ Video mode        Alt-V ³ °°°°°°°°°°°°°°°°°
       ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´ °°°°°°°°°°°°°°°°°
       ³ Reboot                  ³ °°°°°°°°°°°°°°°°°
       ³ Exit              Alt-X ³ °°°°°°°°°°°°°°°°°
       ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ °°°°°°°°°°°°°°°°°
      °°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°
      °°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

      About
        Shows a dialogue box containing program revision and registration
        number (if any).

      Evaluate DMA clock
        Tries to determine the current DMA clock speed (this operation is
        very hardware dependent and it is possible it won't work - "Error"
        is displayed then).

        The measured clock speed is displayed in
          green  (up to 4.25 MHz): Everything OK
          yellow (up to 5.10 MHz): Caution, possibly decrease DMA clock speed
          red    (from  5.10 MHz): The clock is too fast and can cause damage!

        Conditioned by "DMA waits" it is possible that too low a clock is
        shown (especially on fast i486 systems). I.e.: If AMIsetup detects a
        "red" DMA clock, then it is truly time to decrease it - the DMA chip
        can be destroyed by overclocking!

        On many systems, DMA clock is coupled with bus clock (e.g. ETEQ,
        OPTI, SIS, UMC).

        You can compute the bus clock using the following formula:

        Bus Clock = 2 * DMA Clock

        Depending on the DMA waitstates, the factor can be 2.75
        (1 Waitstate) or 3 (2 Waitstates) instead of 2.

        It is neither possible to measure the bus clock nor the number of
        DMA waitstates directly.

        The routine doesn't work on some faster machines (i.e. Overdrive
        (tm), 66DX2) (it displays garbage values then).

        This function is disabled under OS/2.

      Test coprocessor status
        This function performs a coprocessor hardware check and compares the
        result with the BIOS coprocessor presence bit, which is set during
        system boot.

        If both results correspond (i.e. "Coprocessor present" and "Status
        bit set" or "No coprocessor present" and "Status bit not set"),
        everything is OK.

        If both results do not correspond ("*ERROR*" is displayed in
        addition), the BIOS most probably doesn't sense the coprocessor.

        If you have problems with applications which support a math
        coprocessor and the above error is shown, you should first look into
        "Setup|Extended Setup" and see if you can enable "Numeric
        Coprocessor" or "Numeric Coprocessor Test".

        If no such setting is available, you can create a small "SETNPU"
        program and add it to your AUTOEXEC.BAT.
        Please copy all characters exactly as shown:
          C:\> DEBUG SETNPU.COM
          The specified file name expression was not found.
          -a
          ....:0100 mov ax,40
          ....:0103 mov ds,ax
          ....:0105 or byte ptr [10],2
          ....:010A mov ax,4c00
          ....:010D int 21
          ....:010F                     [Press Enter]
          -rcx
          CX 0000
          :0f
          -w
          Writing 000F bytes
          -q
          C:\>

      Video mode
        Toggles the display mode between 25 lines and 43/50 lines and requires
        an EGA/VGA graphics adapter.
        AMIsetup automatically stores the last used video mode.

      Reboot
        Executes a cold boot. The keyboard controller is programmed to trigger
        a hardware reset.

        The "Reboot" function can be turned off using the "Options" dialogue.

        CAUTION! If you use a hard disk cache or disk doubler, this function
        could possibly cause data loss.

        AMIsetup first tries to flush the SmartDrive cache (if it is
        installed, you can disable this feature using the command line
        argument "-NOSM"), waits 2 seconds and then resets the computer
        (OS/2: only the program is closed).

      Exit
        Exits the program.


      3.2 BIOS menu
      ÄÄÄÄÄÄÄÄÄÄÄÄÄ

        ð  BIOS  CMOS  Setup  Options  Help
      °°° ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿ °°°°°°°°°°°°
      °°° ³ Test version        ³ °°°°°°°°°°°°
      °°° ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´ °°°°°°°°°°°°
      °°° ³ Write image to file ³ °°°°°°°°°°°°
      °°° ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ °°°°°°°°°°°°
      °°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

      Test version
        Verifies whether the BIOS and AMIsetup are compatible. This check
        is executed automatically whenever you start "Setup". If this test
        fails ("*ERROR*") and you use a memory manager (e.g. QEMM-386,
        EMM386, 386MAX), you may have to create a BIOS image (see below), or
        reboot from a plain vanilla DOS diskette. Please read appendix C for
        more information about compatible BIOS versions.

      Write image to file
        Using this function, you can create a "BIOS image" file. This file
        is necessary if you use a memory manager like QEMM-386, EMM386 or
        386MAX. Otherwise you don't need an image file. "BIOS|Test version"
        tells you whether you need an image file.

        To create a "BIOS image" file, do the following:
        1. Reboot the PC WITHOUT memory manager and WITHOUT shadow RAM (if
           possible). It's best to boot from a floppy disk.
           Example: To disable the DOS 6 memory manager, type
           "MEMMAKER /UNDO"
        2. Start AMIsetup.
        3. Turn off "Use BIOS image" in the "Options" dialogue.
        4. Select "BIOS|Test version" and verify that everything checks out
           OK.
        5. Select and execute "BIOS|Write image to file" (you can change the
           file name in the "Options" dialogue, if need be. Default is
           "BIOS.DAT").
        6. Finally don't forget to turn on "Use BIOS image" in the "Options"
           dialogue to use the newly created BIOS image.
        7. Now you can use both AMIsetup and your memory manager.


      3.3 CMOS menu
      ÄÄÄÄÄÄÄÄÄÄÄÄÄ

      S  CMOS  Setup  Options  Help
      ° ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿ °°°
      ° ³ Test checksums               ³ °°°
      ° ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´ °°°
      ° ³ Print                        ³ °°°
      ° ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´ °°°
      ° ³ Write image to file          ³ °°°
      ° ³ Restore from image           ³ °°°
      ° ³ Write EISA NVRAM to file     ³ °°°
      ° ³ Restore EISA NVRAM from file ³ °°°
      ° ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´ °°°
      ° ³ Reset CMOS RAM               ³ °°°
      ° ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´ °°°
      ° ³ Information                  ³ °°°
      ° ³ Time compare                 ³ °°°
      ° ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ °°°
      °°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

      Test checksums
        Verifies the CMOS RAM checksums. There are two areas - the first is
        in all AT computers, the second only in PCs with an AMI BIOS. If
        one of these two tests fails, the program declines to run "Setup".

        If you have written your Setup to a file before this error occurred,
        you can correct the problem through "Restore from image".

        AMIsetup saves your configuration automatically
        - when you first use the program into the file SAVECMOS.SAV
        - whenever you invoke the program into the file CMOSBKUP.SAV.

      Print
        Prints the CMOS RAM contents and is used for diagnostic and
        reference purposes only. To get a readable, plain English print,
        use "Setup|Print current setup".

                 °°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°
                 °ÉÍ[þ]ÍÍÍÍÍÍÍÍÍ Print CMOS ÍÍÍÍÍÍÍÍÍÍÍÍÍ»°
                 °º                                      º°
                 °º ¯Print to file                       º°
                 °º   PRN                                º°
                 °º                                      º°
                 °º                                      º°
                 °º  [  OK  ]    [Cancel ]   [ Help  ]   º°
                 °º                                      º°
                 °ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼°
                 °°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

        If you enter a name different from "PRN", the output will be
        redirected to a file, e.g. "CMOS.TXT". Of course you can also use
        device names (e.g. "LPT2")

        If your printer cannot print graphic characters, you must turn off
        "Extended character set" in the "Options" dialogue.

        Data is written in the following format:

                           Reg ³ Current value
                           ÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
                            00 ³ 13  00010011
                            01 ³ 23  00100011
                           ...    ...
                            7E ³ 00  00000000
                            7F ³ 00  00000000

        Opposite to the register number (hexadecimal), the current value is
        printed in hexadecimal and binary format.

        If you don't want a form feed at the end, turn it off in the
        "Options" dialogue.

      Write image to file
        Copies contents of CMOS RAM to a file. You can change the default
        directory in the "Options" dialogue.

      Restore from image
        Reads this file back to CMOS RAM and restores the saved state. Time
        and date are not set, however!

      Write EISA NVRAM to file
      Restore EISA NVRAM from file
        On some EISA computers, you can also save and restore the EISA
        NVRAM (parts of the configuration data are stored in the EISA NVRAM
        on these machines).

        See appendix H for more information.

      Reset CMOS RAM
        Caution: Reset CMOS erases the complete CMOS RAM contents,
        including checksums, date/time, hard disk parameters, etc.
        Please make a paper backup of your configuration before
        resetting the CMOS RAM!

      Information
        Shows the date of the RTC, the alarm time and information about
        errors at system boot.

                ÉÍÍÍÍ Information about CMOS RAM contents ÍÍÍÍÍ»
                º                                              º
                º  Date ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿                  º
                º  ³ 03/19/1993             ³                  º
                º  ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ                  º
                º                                              º
                º  Alarm ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿                  º
                º  ³ 00:00:00           off ³       OK    Ü    º
                º  ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ    ßßßßßßßßßß    º
                º                                              º
                º  Status ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿     Print   Ü    º
                º  ³ Battery:             û ³    ßßßßßßßßßß    º
                º  ³ Power:               û ³                  º
                º  ³ Checksum:            û ³      Help   Ü    º
                º  ³ Configuration:       û ³    ßßßßßßßßßß    º
                º  ³ Memory size:         û ³                  º
                º  ³ Hard disk C:         û ³                  º
                º  ³ Time:                û ³                  º
                º  ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ                  º
                ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

        Date
          The current system date of the real time clock (RTC).

        Alarm
          The RTC supports an "alarm clock" mode. You need an external
          program (TSR) that processes the RTC message and then activates.

        Status
          Shows possible errors from the last system boot. A "û" means
          "no error found".
          - Battery: CMOS battery is discharged and CMOS contents were invalid
          - Power: RTC power supply failed
          - Checksum: CMOS checksums were invalid
          - Configuration: Self test results and CMOS configuration were
            different
          - Memory size: Memory size determined by self test and memory size
            stored in CMOS were different
          - Hard disk C: Hard disk C: (if available) couldn't be initialized
            and couldn't be booted from
          - Time: Time was invalid

          Errors often disappear after a reboot (e.g. Checksum).

      Time compare
        Compares the current DOS time and the RTC time and is used for
        reference purposes only. If the difference is more than approx. 2
        seconds, you should check hard and software.


      3.4 Setup
      ÄÄÄÄÄÄÄÄÄ

        ð  BIOS  CMOS  Setup  Options  Help
      ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ Setup ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
      ³
      ³05/05/91(C)1990 American Megatrends Inc., All Rights Reserved
      ³ROM BIOS (C)1990 American Megatrends Inc.,
      ³
      ³
      ³                      ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
      ³                      ³        Standard setup         ³
      ³                      ³    Extended/chipset setup     ³
      ³                      ³        Change register        ³
      ³                      ³           Password            ³
      ³ DATE:                ³    Load ROM setup defaults    ³      WARNING:
      ³ 05/05/91             ³  Load ROM power-on defaults   ³      Improper
      ³                      ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´      Setup may
      ³                      ³      Print current setup      ³      severe pr
      ³                      ³       Analyze ID string       ³
      ³                      ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´
      ³                      ³     Save changes and quit     ³
      ³                      ³      Exit without saving      ³
      ³                      ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ
      ³
      ³ 30-0201-ABCDEF-00101111-050591-OPWB
      ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

      If the CMOS RAM checksums and the internal BIOS copyright strings are
      valid, the above Setup screen is displayed.
      If you are a registered user (see appendix A), you can begin with this
      screen automatically at program start. Simply set "Options|Auto start
      setup" to on.

      AMIsetup searches for two specific copyright strings at several
      locations. One of these is displayed at the top. At the left is
      the BIOS date, at the bottom the BIOS ID string (as displayed at
      system boot).


      3.4.1 Standard setup
      ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

      You can change the following settings (to change date and time,
      please use the DOS commands DATE and TIME).

      ÉÍ[þ]ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ Standard setup ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
      º                                                                  º
      º Base memory:       640K                                          º
      º Extended memory: 16384K           Auto detect hard disks Ü       º
      º                                   ßßßßßßßßßßßßßßßßßßßßßßßß       º
      º Drive A         Drive B           HDD 0 Ü         HDD 1 Ü        º
      º                                   ßßßßßßß         ßßßßßßß        º
      º  ( ) None        ( ) None          Type:    47    NONE / SCSI    º
      º  ( )  360K 5¬"   ( )  360K 5¬"     Cyl:   1024                   º
      º  ( )  1.2M 5¬"   (x)  1.2M 5¬"     Heads:   64                   º
      º  ( )  720K 3«"   ( )  720K 3«"     S/Trk:   26                   º
      º  (x) 1.44M 3«"   ( ) 1.44M 3«"     Size:  832M                   º
      º  ( ) 2.88M 3«"   ( ) 2.88M 3«"                                   º
      º                                                                  º
      º Display adapter      Options                                     º
      º  ( ) Not installed    [X] Keyboard installed                     º
      º  ( ) Color 40x25                                                 º
      º  ( ) Color 80x25                                                 º
      º  ( ) Monochrome                                                  º
      º  (x) VGA/PGA/EGA                  OK   Ü    Cancel Ü     Help  Ü º
      º                                 ßßßßßßßß    ßßßßßßßß    ßßßßßßßß º
      ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

      At top, the memory size as determined by the BIOS is displayed.

      Drive A
      Drive B
        Allows you to change the type of installed floppy disk drives.

        2.88 MB disk drives:
          Using AMIsetup, you can configure the drive type "2.88 MB" on
          any computer. To run a ED drive, you need a diskette controller
          capable of the 1 Mbps data rate (e.g. AHA1542CF).

          If your BIOS does not support 2.88 MB drives, AMIsetup displays
          a warning message (BIOS versions earlier than 06/12/91).

          Lack of BIOS support can cause the following problems:
          - Problems booting from diskette (especially 720 KB diskettes)
          - The built-in ROM "Standard setup" displays a line containing
            garbage characters (this does not adversely affect other setup
            functions).
          - You'll need software support for your floppy drive. OS/2 2.1
            automatically detects 2.88 MB drives. DOS 5.0 or later requires
            a device "DRIVER.SYS" (please consult your DOS manual). The
            author is currently developing a flexible BIOS enhancement which
            must be installed in CONFIG.SYS, supporting 360 KB to 2.88 MB
            floppy drives on any port, IRQ or DMA channel.
          - Dependent on your hardware, it might be better instead to tell
            the BIOS the drive was 1.44 MB.
          You can disable the warning message (displayed if your BIOS does
          not support 2.88 MB drives) using the command line parameter
          "-288".

      Display adapter
        With this you set the type of the installed graphics adapter.

             ( ) Not installed
             ( ) Color 40x25
             ( ) Color 80x25   = CGA
             ( ) Monochrome    = MDA, Hercules
             (x) VGA/PGA/EGA

        Often you have to change a jumper on the main board besides this
        setting.

      Options - Keyboard installed
        If the keyboard should be checked at system boot, check this box.
        Should the keyboard not be checked or if there is no keyboard
        installed (e.g. LAN server), leave it empty.

      Auto detect hard disks
        You don't need to enter the parameters of your hard disks manually
        if you have IDE type drives installed (maybe this works with ESDI
        drives, too). AMIsetup can detect the correct cylinder/head/sector
        values automatically (non-OS/2 systems only).

        ÉÍ[þ]ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ Confirm ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
        º                                                    º
        º               Install the following                º
        º              hard drives into setup?               º
        º                                                    º
        º  HDD 0: Conner Peripherals 170MB, CP30174E         º
        º  HDD 1: Not installed / SCSI                       º
        º                                                    º
        º                                                    º
        º           Yes   Ü      No    Ü     Help   Ü        º
        º         ßßßßßßßßß    ßßßßßßßßß    ßßßßßßßßß        º
        ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

        If no hard disks are found, it's most likely you have SCSI type
        drives (or old MFM or RLL drives).
        In the case of MFM/RLL type drives, you must enter the disk
        parameters manually; this also holds true for some SCSI
        controllers.

      HDD 0
      HDD 1
        With this you can set the type of installed MFM, RLL or IDE
        hard drives. Using a SCSI controller, you mustn't define a hard disk
        here - please read your controller and hard disk manual to prevent
        momentous wrong settings!

        The current parameters are displayed below the push-button - type
        (number) of the disk, cylinders, heads, sectors per track and the
        calculated size.
        Note: The disk size is displayed in real Megabytes, 2^20 bytes.
        Many disk vendors calculate in 10^6 bytes (this number is larger!).

        If you push the button, a list of predefined disk types appears:

             ÉÍ[þ]ÍÍÍÍÍÍÍÍÍ Hard disk 0 parameters ÍÍÍÍÍÍÍÍÍÍÍÍÍ»
             º Type³ Cyls. ³Heads³ Precomp³ LZone ³S/Trk³  Size º
             ºÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÅÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÅÄÄÄÄÄÄÄº
             º  32 ³  1024 ³  15 ³   NONE ³  1024 ³  17 ³  128M >
             º  33 ³  1024 ³   5 ³   1024 ³  1024 ³  17 ³   43M ±
             º  34 ³   816 ³  15 ³   NONE ³   816 ³  32 ³  191M ±
             º  35 ³  1024 ³   9 ³   NONE ³  1024 ³  17 ³   77M ±
             º  36 ³  1024 ³   8 ³    512 ³  1024 ³  17 ³   68M ±
             º  37 ³   615 ³   8 ³    128 ³   615 ³  17 ³   41M ±
             º  38 ³   745 ³   4 ³    512 ³   745 ³  28 ³   41M ±
             º  39 ³   987 ³   7 ³    987 ³   987 ³  17 ³   57M ±
             º  40 ³   820 ³   6 ³    820 ³   820 ³  17 ³   41M ±
             º  41 ³   977 ³   5 ³    977 ³   977 ³  17 ³   41M ±
             º  42 ³   981 ³   5 ³    981 ³   981 ³  17 ³   41M ±
             º  43 ³   755 ³  16 ³   NONE ³   755 ³  17 ³  100M ±
             º  44 ³   887 ³  13 ³   NONE ³   887 ³  34 ³  191M ±
             º  45 ³   968 ³  10 ³   NONE ³   968 ³  34 ³  161M ±
             º  46 ³   751 ³   8 ³      0 ³   751 ³  17 ³   50M þ
             º¯ 47 ³ USER DEFINED³        ³       ³     ³      ®<
             ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

        The columns contain type (number) of the disk, number of cylinders,
        heads, the precompensation cylinder (see glossary), landing zone,
        number of sectors per track and the calculated size (rounded) in
        megabytes. Please compare these items with the data sheet of your
        hard disk.

        It's likely you CANNOT find the specifications of the hard disk to
        be installed in this list. In this case, select type 47 (USER
        DEFINED).
        The following dialogue appears:

             ÉÍ[þ]ÍÍÍÍÍÍÍ  Change type 47 parameters  ÍÍÍÍÍÍÍÍÍÍÍÍ»
             º                                                    º
             º                                                    º
             º     615 ¯Cylinders                                 º
             º                                                    º
             º       4  Heads                                     º
             º                                                    º
             º     300  Precompensation (65535 for NONE)          º
             º                                     [  Save   ]    º
             º     615  Landing zone                              º
             º                                     [ Cancel  ]    º
             º      17  Sectors/track                             º
             º                                     [  Help   ]    º
             º                                                    º
             ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

        Here you can set the parameters yourself. Note that the value of
        precompensation has a special meaning: 65535 means DISABLED for the
        whole hard disk. 0 means ENABLED for the whole disk.
        Modern drives ignore precompensation and landing zone. For reasons
        of software compatibility, set precompensation to "NONE" and landing
        zone to the highest available cylinder+1.


      3.4.2 Extended/chipset setup
      ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

      A list of options and their current settings is displayed:

      ÉÍ[þ]ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ Extended setup ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ
      º            Option            ³Register³Bits ³ Current setting
      ºÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÁÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
      º¯  Typematic Rate Programming ³ 11  10000000 ³ 10000000  Enabled     ®
      º   Typematic Rate Delay (msec)³ 11  01100000 ³ 00000000  250
      º   Typematic Rate (Chars/Sec) ³ 11  00011111 ³ 00000011  21.8
      º ¨ Mouse Support Option       ³ 13  10000000 ³ 10000000   <1>
      º   Above 1 MB Memory Test     ³ 13  01000000 ³ 00000000  Disabled
      º   Memory Test Tick Sound     ³ 13  00100000 ³ 00000000  Disabled
      º   Memory Parity Error Check  ³ 13  00010000 ³ 00010000  Enabled
      º   Hit <ESC> Message Display  ³ 13  00001000 ³ 00000000  Disabled
      º   Hard Disk Type 47 Data Area³ 13  00000100 ³ 00000000  0:300
      º   Wait For <F1> If Any Error ³ 13  00000010 ³ 00000010  Enabled
      º   System Boot Up Num Lock    ³ 13  00000001 ³ 00000001  On
      º þ Numeric Processor          ³ 14  00000010 ³ 00000010  Present
      º   Weitek Processor           ³ 2D  10000000 ³ 00000000  Absent
      º   Floppy Drive Seek At Boot  ³ 2D  01000000 ³ 00000000  Disabled
      º   System Boot Up Sequence    ³ 2D  00100000 ³ 00000000  C:, A:
      º   System Boot Up Speed       ³ 50  00000100 ³ 00000000  High
      º   Cache Memory               ³ 2D  00001000 ³ 00001000  Enabled
      º ¨ Internal Cache Memory      ³ 2D  00000100 ³ 00000100   <1>
      ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ

      The four columns have the following meaning:

      Option
        The name of the setting to be changed, peeked from the BIOS.
        The signs "þ" and "¨" denote options that cannot be changed from
        the BIOS and are marked as "disabled" (see explanation under
        "Options|Display ...").
        If you change settings of options marked in this way, be especially
        careful. You can disable the display of these options selectively
        in the "Options" dialogue.
        By the way, blame the BIOS manufacturer for reversed letters in this
        row, not AMIsetup.

      Register
        Hexadecimal number of the CMOS register that stores the setting.
        This information may help experienced users to change settings
        by hand using "Change register". If a "+" sign is displayed behind
        the register number, possibly more than one registers are affected.

      Bits
        Bit mask for the setting. Only Bits marked with a "1" are used
        for the specified setting (see also Register).

      Current setting
        Bit mask of the setting stored in the program copy of CMOS RAM
        and the corresponding text in clear. If plain language is not
        available, a decimal value in acute brackets is shown. E.g.: <2>
        denotes the third possible setting, since <0> is valid, too.

      Now you can select an option with the mouse or the enter key, as
      appropriate. A new window is displayed (see below).

      Instead of pressing the enter key, <Ctrl><RightArrow>, <Ctrl><Enter>
      or <Ctrl><LeftArrow> increase or decrease the current setting
      respectively by one (for the hurried user).

      List:                                       Radio buttons:
      ÉÍ[þ]ÍÍÍÍÍÍÍÍ Typematic Rate (Chars/Sec)    ÉÍ[þ]ÍÍÍÍ Typematic Rat
      º                                           º
      º   ¯Options                 Bits           º   ¯Options
      º     30.0             <     00000011       º    ¯(x) Disabled®
      º     26.7             ±    À00011111Ù      º     ( ) Enabled
      º     24.0             þ                    º
      º    ¯21.8            ®±              [     º
      º     20.0             ±                    º
      º     18.5             ±              [     º
      º     17.1             ±                    º
      º     16.0             ±              [     º
      º     15.0             >                    º
      º                                     [     º
      º                                           º
      ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ    ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ

      Marked below "Options" or "Setting" is the current setting. To change
      the setting, scroll the list or press the appropriate button.

      The "Bits" field shows you which bit mask corresponds to the selected
      setting. Listed below the bit field are once again the bits that can
      be affected by the option.

      "Save" copies the changed setting into the program copy of CMOS RAM
      (use "Save changes and quit" to make the change permanent), "Cancel"
      cancels the operation.

      Caution: Some settings are "Reserved" or "RESERVED". Do consider
      whether you really want to set an option to "Reserved". For safety
      reasons, these changes have to be confirmed.

      "BIOS help": Sometimes, the BIOS ROM has an own (English) help text
      to the respective option. You can view this text using "BIOS help",
      e.g.:

             ÉÍ[þ]ÍÍÍÍÍÍÍÍÍ BIOS help ÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
             ºThe base address changes in           º
             ºsteps of 16k and 512k                 º
             ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

      "Reference": Registered users can look up explanations to the setup
      options.

      Options that are controlled entirely by the BIOS (these usually change
      more than eight bits and are marked with a "+") display a window
      containing the buttons "® < > ¯"; you can also use (<Ctrl>)<RightArrow>
      and (<Ctrl>)<LeftArrow>. The buttons "® ¯" are intended for fast
      leafing and don't work on all machines. On some machines, a window
      appears after pressing "® < > ¯". Here you can enter data - this input
      window is controlled by the BIOS, so mouse input and function keys are
      disabled.

      Setting controlled by BIOS:
      ÉÍ[þ]ÍÍÍÍÍÍÍÍ Non-Cacheable Block-0 Base ÍÍÍÍÍÍÍÍÍÍÍÍ»
      º                                                    º
      º                                                    º
      º                                                    º
      º                                      [BIOS help]   º
      º   Setting                                          º
      º   _0 KB_______________________       [Reference]   º
      º                                                    º
      º    [ ® ]  [ < ]  [ > ]  [ ¯ ]        [  Save   ]   º
      º                                                    º
      º                                      [ Cancel  ]   º
      º                                                    º
      º                                      [  Help   ]   º
      º                                                    º
      ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

      Note that some options affect each other!


      3.4.3 Change register
      ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

      You may not be able to set the CMOS the way you want from the
      "Extended/chipset setup" menu. In this case, you can make the change
      manually.

      Caution: Use this function only if you are absolutely, positively sure
      about what you're doing!

             ÉÍ[þ]ÍÍÍÍÍ Change register ÍÍÍÍÍÍÍÍÍ»
             º                                   º
             º  Enter register number:           º
             º   __   Range 10 to 7F (hex)       º
             º                                   º
             º                                   º
             º [ Change ]  [ Cancel ]  [ Help ]  º
             º                                   º
             ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

             ÉÍ[þ]ÍÍÍ Change register 12 ÍÍÍÍÍÍÍÍ»
             º  Current value: 00                º
             º                                   º
             º  Enter new value:                 º
             º   __   Range 00 to FF (hex)       º
             º                                   º
             º [  Set   ]  [ Cancel ]  [ Help ]  º
             º                                   º
             ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

      First, you have to enter the register number in hexadecimal and then
      the new value.


      3.4.4 Password
      ÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

      This function enables you to display the current CMOS password and to
      change it.

      This password can be called for at system boot or when entering the
      ROM setup.

             ÉÍ[þ]ÍÍÍÍÍÍÍÍÍÍ Password ÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
             º                                      º
             º Current password is "AMISET".        º
             º                                      º
             º                                      º
             º                                      º
             º  [Change]    [Cancel]    [ Help ]    º
             º                                      º
             ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

             ÉÍ[þ]ÍÍÍÍÍÍ Change password ÍÍÍÍÍÍÍÍÍÍÍ»
             º                                      º
             º  New password: FIDO__                º
             º                                      º
             º                                      º
             º                                      º
             º  [  OK  ]    [Cancel]    [ Help ]    º
             º                                      º
             ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

      Caution! If you use a foreign language keyboard (i.e. non-USA),
      note that no foreign keyboard support is loaded at boot time.
      Example: On German keyboards, "Z" and "Y" are reversed.

      Often you can enable the US-American keyboard by pressing
      <Ctrl><Alt><F1> and then test which keys are which. Use <Ctrl><Alt><F2>
      to re-enable the foreign keyboard.

      On some machines the password function has to be activated by the
      "Password" option in "Extended/chipset setup" (3.4.2).

      CAUTION! If you set the "Password" option to "Always", you cannot
      boot your machine if you forget the password!

      Hint: Try the setting "Setup" first.


      3.4.5 Load ROM setup defaults, load ROM power-on defaults
      ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

      There are two tables of predefined CMOS settings in the ROM. One of
      those, the "power-on defaults" is used to eliminate all possible
      hardware problems; thus the processor is switched to low speed, the
      cache is turned off, etc. Using "power-on defaults", the machine should
      boot in any case.

      Using this function, you can load a predefined configuration or simply
      view it for reference purposes, since all settings will be written to
      the program copy of CMOS RAM first and only be saved if you use "Save
      changes and quit".


      3.4.6 Print current setup
      ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

      With this function, you can print the current settings of the program
      copy of CMOS RAM to the printer or to a file.

             ÉÍ[þ]ÍÍÍÍÍÍÍÍ Print current setup ÍÍÍÍÍÍÍÍÍÍÍÍ»
             º                                             º
             º ¯Print to file                              º
             º   PRN______________________________         º
             º                                             º
             º  Format                                     º
             º   (x) Standard (current/possible)    Margin º
             º   ( ) Alternate (current bin&hex)     79_   º
             º                                             º
             º                                             º
             º  [  OK  ]    [Cancel]    [ Help ]           º
             º                                             º
             ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

      First the settings of "Standard setup" will be printed; then, a list:

      Standard
        The list is formatted as follows:

                        Option            ³ Current  ³ Possible settings
             ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
             Typematic Rate Programming   ³ Enabled  ³ Disabled
             Typematic Rate Delay (msec)  ³ 250      ³ 500 750 1000
             Typematic Rate (Chars/Sec)   ³ 24.0     ³ 30.0 26.7 21.8 [...]
             ¨ Mouse Support Option       ³ <1>      ³
             Above 1 MB Memory Test       ³ Disabled ³ Enabled
             ...

        "Margin" (61-254) is the maximum width of the list. "Possible
        settings" will be truncated to "[...]" if exceeding the maximum
        width.

      Alternate
        The list looks as the list displayed in "Extended/chipset setup".
        "Margin" is ignored.

                        Option            ³Register³Bits ³ Current setting
             ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÁÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
             Typematic Rate Programming   ³ 13  10000000 ³ 10000000  Enabled
             Typematic Rate Delay (msec)  ³ 13  01100000 ³ 00000000  250
             Typematic Rate (Chars/Sec)   ³ 13  00011100 ³ 00010000  15
             þ Mouse Support Option       ³ 11  10000000 ³ 10000000  Enabled
             ...

      Note: If your printer cannot print extended characters, disable them
      in the "Options" dialogue.

      Hint: If you disable "þ" and "¨" in the "Options" dialogue, you can
      create a list of those settings that can be changed from the ROM
      setup. This list you can distribute e.g. to your customers as a
      reference.


      3.4.7 Analyze ID string
      ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

      This function explains the meaning of the BIOS ID string displayed
      in the lower left corner.
      Note: The information determined by AMIsetup is not always 100 per cent
      correct, since not all manufacturers adhere to the standard (this is
      especially true for "Required processor").
      The ID string displayed at boot time shows the keyboard controller
      revision level in addition to the information displayed by AMIsetup.
      Example: 30-0201-ABCDEF-00101111-050591-OPWB-KF, where F is the
      revision level.

           ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ Analyze BIOS ID string ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
           º                                                      º
           º  30-0201-ABCDEF-00101111-050591-OPWB                 º
           º  23H-0-0000-00-00-0000-00-00-000                     º
           º  23H-1-0000-00-00-0000-00-00-00-2                    º
           º                                                      º
           º  Required processor:   386                OK    Ü    º
           º  BIOS size:            64 KB           ßßßßßßßßßß    º
           º  Version:              2.01                          º
           º  Reference number:     ABCDEF           Print   Ü    º
           º  BIOS date:            05/05/91        ßßßßßßßßßß    º
           º  Chipset ID:           OPWB                          º
           º  Clock switching pin:  23                Help   Ü    º
           º  Cache control pin:    23              ßßßßßßßßßß    º
           º  BIOS modified flag:   02                            º
           º                                                      º
           ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

      Use "Print" to print the information or to write it into a file.


      3.4.8 Save changes and quit
      ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

      Not until you use this function will changes be made permanent. "Save
      changes and quit" writes all CMOS settings from the program copy of
      CMOS RAM into the real CMOS RAM and exits setup.

      If "Options|Enable reboot" is enabled, you will be asked whether you
      want to reboot your computer (cf. "Reboot").


      3.4.9 Exit without saving
      ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

      Quits setup without changing the CMOS RAM.


      3.5 Options dialogue
      ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

      ÉÍ[þ]ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ Options ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
      º                                                              º
      º  Setup                         Display                       º
      º   [ ] Use BIOS image            [X] þ Options                º
      º   [X] Auto start setup          [ ] ¨ Options                º
      º   [ ] Print form feed                                        º
      º   [X] Extended character set    [ ] Soundblaster             º
      º   [ ] Enable reboot command                                  º
      º   [X] Beep on error                                          º
      º   [ ] Reverse mouse buttons      Password  Ü                 º
      º   [ ] German language           ßßßßßßßßßßßß                 º
      º                                                              º
      º  BIOS image file               CMOS and EISA image files     º
      º   C:\SETUP\BIOS.DAT             C:\SETUP\                    º
      º                                                              º
      º                                                              º
      º    Save  Ü    Cancel Ü     Help  Ü                           º
      º   ßßßßßßßß    ßßßßßßßß    ßßßßßßßß                           º
      ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

      Customize the program to your own needs using this dialogue.

      Use BIOS image
        Usage of an image file instead of peeking directly into the ROM. See
        "BIOS|Write image to file" for more information.

      Auto start setup
        Instead of selecting "Setup" manually each time using the menu,
        "Setup" can also be started automatically at program start
        (registered copies only).

      Print form feed
        Do a form feed after printing.

      Extended character set
        This box must be left blank if your printer doesn't print the extended
        character set (code page 437), e.g. characters like "«" or "þ".

      Enable reboot command
        If this box is blank, the "Reboot" function in the "ð" menu is
        disabled and you will not be asked whether you want to reboot
        after saving your setup.

      Beep on error
        If this option is checked, the program beeps if you enter incorrect
        values in (hexa-) decimal input boxes.

      Reverse mouse buttons
        You can reverse right and left mouse buttons (for left-handers or
        southpaws).

      German language
        You can disable the English user interface and work with the German
        one instead.

      Display
      ... þ
      ... ¨
        There are two types of disabled options in the ROM BIOS.
        1. Some options are actually there, but marked as "inadmissible".
           This can be e.g. redundant options. AMIsetup displays a "þ"
           in front of the option. Mostly the "þ" options work perfectly.
        2. Some options are marked as "inadmissible" AND there are no valid
           known settings. AMIsetup then displays a "¨". Often "¨" options
           don't work.
        You can enable and disable both types. If neither "þ" nor "¨" are
        enabled, then AMIsetup shows the same set of options as the ROM
        setup.

      Soundblaster
        See appendix G.

      BIOS image file
      CMOS and EISA image files
        You can change file name/directory of these files.

      Password
        You can define a password that will be needed at program start.
        Password protection reduces misuse of the AMIsetup.

               ÉÍ[þ]ÍÍÍÍÍÍ Change password ÍÍÍÍÍÍÍÍÍÍÍ»
               º                                      º
               º  New password:  ****                 º
               º                                      º
               º  Confirm:       ****                 º
               º                                      º
               º                                      º
               º                                      º
               º     OK   Ü    Cancel Ü     Help  Ü   º
               º   ßßßßßßßß    ßßßßßßßß    ßßßßßßßß   º
               ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

        For security reasons, you have to enter the same password in both
        lines.
        If you enter an empty password (simply press Enter), the password
        protection will be disabled.

        Changes of the password are written into the file AMISETUP.EXE,
        which must not be write protected for this operation.


      3.6 Help menu
      ÄÄÄÄÄÄÄÄÄÄÄÄÄ

        ð  BIOS  CMOS  Setup  Options  Help
      °°°°°°°°°°°°°°°°°°°°°°°°°°°°°°° ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿ °°°°°°°°°°
      °°°°°°°°°°°°°°°°°°°°°°°°°°°°°°° ³ Contents          ³ °°°°°°°°°°
      °°°°°°°°°°°°°°°°°°°°°°°°°°°°°°° ³ View AMISETUP.DOC ³ °°°°°°°°°°
      °°°°°°°°°°°°°°°°°°°°°°°°°°°°°°° ³ Print order form  ³ °°°°°°°°°°
      °°°°°°°°°°°°°°°°°°°°°°°°°°°°°°° ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´ °°°°°°°°°°
      °°°°°°°°°°°°°°°°°°°°°°°°°°°°°°° ³ On-line reference ³ °°°°°°°°°°
      °°°°°°°°°°°°°°°°°°°°°°°°°°°°°°° ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ °°°°°°°°°°
      °°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

      Contents
        Gives an overview about on-line help.

      View AMISETUP.DOC
        You can view AMISETUP.DOC without leaving AMIsetup. It is necessary
        that AMISETUP.DOC be installed in the same directory as AMISETUP.EXE.

        You can leave the AMISETUP.DOC window in the background while
        working with AMIsetup.

      Print order form
        To order AMIsetup, you can print an order form to the printer or
        to a file.

      On-line reference
        Registered users (read appendix A how to become a registered user)
        can read explanations of approx. 100 of the most widespread setup
        options.

        Select "On-line reference", and the index is displayed.

        ÉÍ[þ]ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ On-line reference ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ
        º
        º            Ü Index
        º            ßßßßßßß
        º
        º    General advice
        º    ÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
        º
        º  Caution!
        º  Beep codes
        º
        º
        º    Tuning tips
        º    ÄÄÄÄÄÄÄÄÄÄÄ
        º
        º
        º    Setup options
        º    ÄÄÄÄÄÄÄÄÄÄÄÄÄ
        º
        º  256KBÿMemoryÿRelocation
        º  256K/384KÿMemoryÿRelocation
        º  7CLK2ÿCASÿPulseÿWidth
        ÈÍþ±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±

        You can mark one of the bold terms using <Tab> or the mouse and get
        a closer explanation:

        ÉÍ[þ]ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ On-line reference ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ
        º
        º       Fast Gate A20 Option  [Disabled] [Enabled]
        º       Gate A20 Emulation Option
        º
        º Activates a faster method for enabling and disabling address line
        º needed for accessing extended memory.
        º
        º The address line A20 is normally toggled by the keyboard controlle
        º comparably slow 8042 processor.
        º
        º For reasons of compatibility with PC/XT systems (8086/8088), addre
        º A20 is disabled under DOS in most cases. PCs with the 8088 had onl
        º address lines up to A19. When on the 8088 PC address FFFF:XXXX (se
        º first 64KB was actually addressed.
        º
        º In order to access memory above 1MB (extended memory) on 286 or ne
        º address line A20 must be toggled. This also holds for switching be
        º line A20, allowing the first 63 KB of extended memory to be access
        º mode (and used as "high memory").
        º
        º Control by the keyboard controller can be replaced by a faster tec
        º option became famous as "OS/2 optimization".
        º
        º Modern software uses other methods of switching (triple fault or 3
        ÈÍþ±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±

        Use the <Tab> key to switch to the next highlighted topic (the
        cursor keys are for scrolling only).


      4 Key shortcuts
      ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

      <F1>         Help
      <Alt><F3>    Close active window
      <F5>         Zoom active window
      <Ctrl><F5>   Move active window (Cursor keys)
                   Change window size (<Shift>+Cursor keys)
      <F9>         Start Setup
      <F10>        Activate main menu
      <Shift><F10> Show program information
      <Alt><X>     Exit Setup or program
      or <Alt><F4>

      NB:  <>            = <Shift>
           <Return>, <Ù> = <Enter>
           <>            = <Tab>


                                   A P P E N D I X
                                   ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

      A  Registration
      ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

      If you want to continue using AMIsetup after 30 days, you have to
      register.

      The shareware version is limited in the following ways:

      þ The on-line reference is disabled
      þ Starting the setup automatically doesn't work

      See REGISTER.FRM for the registration fee valid for your
      country (DM 40.- to DM 55.- depending on the country), REGISTER.GER
      for Germany, REGISTER.JPN for Japan.

      Commercial users in the European Union ONLY: Please provide your
      VAT registration number and save 15% VAT!

      Inquire for more than 2 licenses!

      Send DM Eurocheques (other cheques: add DM 10.-), cash or postal
      money order to the following address:

                              Robert Muchsel
                              Hegaublick 2
                              D-78465 Konstanz
                              Germany

                              FAX +49-7533-3151

      ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
      ³ Please use the form "REGISTER.FRM" included with this program.    ³
      ³ You can print it using "Help|Print order form" directly from      ³
      ³ AMIsetup.                                                         ³
      ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

      ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
      ³  Email:                                                           ³
      ³            FidoNet 2:246/8100.11                                  ³
      ³            mccs BBS, Singen/Germany, +49-7731-69523               ³
      ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

      AMIsetup is shipped on 3.5" disks. If you really need a 5.25" disk,
      please indicate <5.25"> in BIG letters in the upper right corner of
      the order form.


      Upgrades
      ÄÄÄÄÄÄÄÄ

      If the user has a modem, upgrades are free. Other registered users
      only have to pay the fee of their shareware vendor.

      Upgrades will not be free if
      - there are too many illegal pirated copies
      - there are major enhancements

      Read README.!!! on your registration diskette for more information.


      The Author
      ÄÄÄÄÄÄÄÄÄÄ

      ...studies Computer Science at the ETH (Swiss Federal Institute of
      Technology) in Zurich/Switzerland (this is the explanation of the
      "Additional contributions" field on the order form).



      B  AMIsetup and OS/2 2.x, Windows, Windows NT
      ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

        OS/2 Version 2.1
        ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
      The program will run in a DOS session of OS/2 2.1. DMA clock speed
      detection and "Auto detect hard disks" will be disabled, however.

        OS/2 Version 2.0
        ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
      The program will not run in a DOS session of OS/2 2.0, not even in a
      DOS image (VDM). Write accesses to the CMOS RAM are redirected to a
      buffer by OS/2, which is discarded when exiting the virtual machine
      (source: "Redbooks, Vol. 2: DOS and Windows-Environment, Virtual CMOS
      Device Driver"; IBM Document Number GG24-3731-00).

      An OS/2 version of AMIsetup is impossible, since AMIsetup directly
      executes code of the real mode BIOS.

      If you create a DOS boot disk and copy AMIsetup as well as a disk
      editor there, then you've got a sort of "emergency disk".


        AMI BIOS and OS/2
        ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

      There are NO general problems with OS/2 2.x and the BIOS versions
      supported by AMIsetup. OS/2 runs with BIOS versions PRIOR to 05/05/91
      and with keyboard controller revision -K8.

      However, problems might arise e.g. when using faulty memory chips,
      too low refresh rates, wrongly installed cache memory or wrong
      bus clock. Because of the protected mode architecture, OS/2 is much
      more sensitive to errors than DOS software, which often ignores
      or doesn't even notice them.


        Windows
        ÄÄÄÄÄÄÄ
      Running AMIsetup under Windows is not recommended.
      The icon file, AMISETUP.ICO, contains an OS/2 icon which cannot
      be displayed under Windows.

        Windows NT
        ÄÄÄÄÄÄÄÄÄÄ
      The Windows NT DOS emulator is not compatible with AMIsetup.


      C  Known problems
      ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

      1. Is AMIsetup compatible with your BIOS?

         For technical reasons, AMIsetup only works with the newer generation
         of the AMI BIOS, the so-called "Hi-Flex BIOS".
         On one hand, the BIOS must be manufactured by "American Megatrends
         Inc." ("AMI") (this you can see when powering on your computer).

         Example of power-on screen:
         ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
         ³ 05/05/91(C)1990 American Megatrends Inc., All Rights Reserved ³
         ³                                                               ³
         ³ (C)1990 American Megatrends Inc.,                             ³
         ³                                                               ³
         ³                                                               ³
         ³                                                               ³
         ³                                                               ³
         ³                                                               ³
         ³                                                               ³
         ³                                                               ³
         ³ 30-0101-ABCDEF-00011001-050591-FORX                           ³
         ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

         On the other hand, a compatible BIOS has a colored ROM setup
         (or built-in setup) and normally three levels of setup ("Standard",
         "Advanced" and "Advanced Chipset"), "Password" and "Hard Disk
         Utility".

         ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
         º          BIOS SETUP PROGRAM-AMI BIOS SETUP UTILITIES         º
         º    (C) 1990 American Megatrends Inc., All Rights Reserved    º
         ÌÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¹
         º                                                              º
         º                     STANDARD CMOS SETUP                      º
         º                     ADVANCED CMOS SETUP                      º
         º                   ADVANCED CHIPSET SETUP                     º
         º            AUTO CONFIGURATION WITH BIOS DEFAULTS             º
         º          AUTO CONFIGURATION WITH POWER-ON DEFAULTS           º
         º                       CHANGE PASSWORD                        º
         º                      HARD DISK UTILITY                       º
         º                    WRITE TO CMOS AND EXIT                    º
         º                DO NOT WRITE TO CMOS AND EXIT                 º
         º                                                              º
         ÌÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¹
         º                                                              º
         º  Standard CMOS Setup for Changing Time, Date, Hard Disk, etc.º
         º                                                              º
         ÈÍÍÍÍÍµ ESC:Exit |-|-:Sel F2/F3:Color F10:Save & Exit ÆÍÍÍÍÍÍÍÍ¼

         Custom-made BIOS versions are NOT compatible with AMIsetup, even
         though they are from AMI. These have a so-called "XCMOS Setup" (and
         they are black & white).

                              ÚÄÄÄÄÄÄÄÄÄÄÄÄ¿
      2. Frequent errors with ³ compatible ³ BIOS versions
                              ÀÄÄÄÄÄÄÄÄÄÄÄÄÙ

         ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
         ³ Checking 34 .. 3F:              *ERROR* ³
         ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

         Possible causes:
         - A program has overwritten your CMOS. Restart your PC and follow
           the instructions of the ROM BIOS.

         ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
         ³ Checking "AAAAMMMMIIII":        *ERROR* ³
         ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ
         ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
         ³ Checking "American Megatrends": *ERROR* ³
         ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ
         ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
         ³ CX overflow - BIOS not compatible!      ³
         ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

         Possible causes:
         - You are using a memory manager that overwrites parts of your
           BIOS. Create a BIOS image following instructions in 3.2.
         - You are using an image file that is faulty (it was created while
           a memory manager was loaded?).
           Repeat the procedure EXACTLY following instructions (part 3.2)
         - Your version of AMIsetup is obsolete

         ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
         ³ Setup incomplete - may not work!        ³
         ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

         Your BIOS seems to be hacked. There could be some options that
         AMIsetup doesn't display. If your image file is OK (see above),
         your BIOS may have been patched by the manufacturer.

         ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
         ³ The BIOS register table contains invalid entries! ³
         ³ Register: XXh, CMOS RAM = ... Bytes               ³
         ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

         Your ROM setup defines values for CMOS registers that don't
         exist. AMIsetup ignores all missing registers, so pressing "OK"
         is perfectly OK.

         All entries where AMIsetup reports a register >= XXh will contain
         garbage values, changes made to these registers will be ignored.

         This error is caused either by an EISA BIOS (additional setup
         information is stored in a separate EISA NVRAM, see appendix H)
         or a BIOS that doesn't fit to your hardware. This error also
         occurs when running AMIsetup under OS/2 2.0 (not 2.1).

         If you have Headland's SHASTA chip set, you can modify your
         computer (you'll need a new clock chip and a BIOS patch). Other
         than this, there is no way to circumvent the problem.


      3. Stopgap: -OVERRIDE

         As a last resort you can start the program with the command-line
         option "-OVERRIDE". This option disables all error messages;
         faulty operation or a locked-up computer may  result, though.


      4. Additional trouble shooting options

         While loading, AMIsetup displays the current initalisation phase.
         If the program hangs, you might try the following phase dependent
         switches: "-NOPCI" (on ISA/EISA systems) or "-PCI" (on PCI
         systems), if the PCI check fails. If the EISA detection hangs,
         edit EISA.CFG. If the program fails in any other phase, please
         contact the author.

         If the program hangs when you start the "Extended setup",
         you may want to try the parameter "-NOROMJUMPS".

         There are two more parameters built into the program,
         "-EOBIOS:xxxx" and "-IMAGE:xxxx". Please use these two parameters
         only if the author tells you to do so.


      D  Glossary
      ÄÄÄÄÄÄÄÄÄÄÄ

      Some frequently used abbreviations and terms (explanations for setup
      options only on-line and only for registered users):

      AMI
        American Megatrends Inc., a BIOS manufacturer

      BIOS
        Basic routines contained in a nonvolatile memory (ROM) of the PC
        which e.g. drive the hard disk, but are also needed for system boot
        and system setup.

      BIOS Checksum
        The AMI BIOS calculates a 16 bit checksum (addition w/ overflow) over
        the BIOS ROM. If this checksum is 0, it is assumed that the BIOS
        is OK.

      CMOS RAM
        This chip can be read from and written to; unlike normal memory the
        contents are buffered by a battery or an accumulator after turning
        off the PC. CMOS RAM contains data like type of installed floppy
        disk drives, the time, etc.

      CMOS RAM Checksum
        A checksum is calculated for parts of the CMOS and stored in CMOS.
        If checksum and CMOS RAM contents differ, either the battery is
        defect or the CMOS RAM contents are invalid. In any case you must
        reenter the data, possibly replace the battery or accumulator,
        too.

      EISA
        See appendix H.

      Extended Character Set, Graphic characters
        Characters like „”� or æþ¨. Some printers cannot print these.

      NVRAM
        See appendix H.

      Precompensation
        Precompensation is used with some hard disks to compensate for the
        higher recording density in the inner tracks during write.
        Normally, precompensation and reduced write current begin
        approximately at half the cylinder count. The precompensation
        logic shifts certain bit patterns by +/- 12-15ns.
        Precompensation only affects writing, not reading of data.
        Many hard drives work perfectly with or without precompensation,
        newer hard disks ignore the setting (you should turn it off then).

      ROM
        Read Only Memory - memory that can only be read from and not
        written to.


      E  If the machine won't boot...
      ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

      If the setup has been altered so that the PC doesn't even display
      "Press <DEL> for Setup", some models have the following possibilities:

      1. On newer models, you can press <Ins> while powering on. All
         settings will be reset to standard values.

      2. On many machines there is a jumper on the main board which you can
         use to erase CMOS RAM. Sometimes this takes several hours.

      3. Often there is the possibility of connecting an external battery
         pack. To install it, you have to remove a jumper residing on a
         4 pinned connector. This jumper does the same as (2).

      4. Only when encountering password errors and only with BIOS from
         12/12/91 on: Pin 32 of the keyboard controller can be grounded
         to erase the password.

      Please note that after these steps all configuration data must be
      reentered. Make certain that you set the correct hard disk parameters!
      If you are not a hardware expert, you should contact your dealer first
      before destroying your hardware by wrong handling!


      F  Switching to the English user interface
      ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

      If you have installed the German version and want to switch,
      do the following:

      Disable "German language" or "Deutsche Oberfl„che" in the "Options"
      dialogue.
      Select OK, exit and restart AMIsetup.


      G  Soundblaster
      ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

      To make the monotonous task of setting up computers a little more
      fun, AMIsetup supports the Soundblaster audio card.
      Soundblaster support must be explicitly enabled (AMIsetup is, after
      all, a serious program).

      - Turn on "Soundblaster" in the "Options" dialogue (default: OFF)

      - The environment variable "BLASTER" must be set correctly, e.g.:
        SET BLASTER=A220 I5 D1

        The BLASTER variable has the following meaning:

        A220 : Port address of Soundblaster card
        I5   : IRQ (Interrupt) level
        D1   : DMA channel

               (all other settings, e.g. T4, will be ignored)

        If the variable is NOT set, the default values A220 I7 D1 will
        take effect.

        Note: The program could crash if a wrong DMA channel is given!

      - You must have the VOC files.

        Included are:

        CONFIRM.VOC  - Confirmation
        COPYRIGH.VOC - About AMIsetup
        ERROR.VOC    - Replaces the error beep
        ERRORBOX.VOC - Error
        EXIT.VOC     - Program exit
        WARNING.VOC  - Warning

        Not included:

        HELP.VOC     - Help


      AMIsetup has its own, built-in Soundblaster driver. This built-in
      driver should work with all Soundblaster and compatible cards with
      DSP level 1.05 and higher.

      If the driver CTVDSK.DRV is included with your Soundblaster card,
      AMIsetup can use it and adapt itself to the special features of your
      card (e.g. Stereo sound).

      AMIsetup looks for CTVDSK.DRV in the following directories:
      1. in the current directory
      2. in the directory of AMISETUP.EXE
      3. in the subdirectory "DRV\" of the directory specified by the
         environment variable "SOUND"
      4. in the subdirectory "DRV\" of the directory specified by the
         environment variable "CPSPRO4"
      5. in the PATH

      The built-in driver will only be activated if CTVDSK.DRV cannot be
      found.

      You can delete single VOC files and the corresponding action will be
      "quiet".

      You can replace these files with files from your own sound collection.
      The PLAY.EXE program (included with AMIsetup) can also play files
      from the command line ("PLAY Name"). Please send your own, better
      collection of VOC files to the author!

      AMIsetup can play files any size you want; if disk activity is too
      heavy, you can increase the replay buffer which defaults to 4*4 KB.
      Set the DOS enviroment variable SBBUF to the desired value.
      Example: SET SBBUF=16 -> replay buffer will be set to 4*16 KB.

      All sounds are turned off immediately when the corresponding
      action is aborted/finished.

      If the program hangs when you activate Soundblaster support, you can
      force the program to use its built-in driver. Type "SET SOUND=" at the
      DOS command prompt.

      Soundblaster support might fail on Media Vision sound cards. The
      reason of this incompatibility is unknown.

      AMIsetup Soundblaster support needs a lot of memory. If this is an
      issue, please consider disabling Soundblaster support.


      H  EISA
      ÄÄÄÄÄÄÄ

      EISA is an "Extended" and faster bus architecture found in better
      machines. AMIsetup tells you whether you have a standard "ISA" or
      EISA system.

      On some EISA computers, parts of the setup data are stored in the
      EISA NVRAM (Non Volatile RAM). On these machines, AMIsetup needs to
      access the NVRAM. On others, AMIsetup doesn't need to know about EISA
      NVRAM and simply ignores it.

      Since EISA NVRAM access is chipset dependent, AMIsetup uses EISA.CFG
      (see EISA.CFG for explanation of the syntax).

      If AMIsetup detects an EISA system and EISA.CFG contains valid data,
      "CMOS³Write EISA NVRAM to file" and "CMOS³Restore EISA NVRAM from
      file" are automatically enabled. Setup registers 40h to 7F are mapped
      into the EISA NVRAM.

      However, it is possible that AMIsetup doesn't know about YOUR
      particular EISA computer and displays "The BIOS register table
      contains invalid entries!". Please mail a copy of your BIOS.DAT,
      CMOS.SAV and EISANVR.SAV (if available). EISA.CFG can then be extended
      to include your computer.


      I   Batch mode
      ÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

      You can use AMIsetup in batch mode. This is especially useful if you
      - want to configure several identical machines (you don't have to use
        time consuming ECU, CMOS setup any more!)
      - want to document CMOS settings and/or save CMOS/EISA NVRAM
        automatically

      The batch mode of AMIsetup understands the following commands:
        -SAVE:CMOS:FILENAME          Save CMOS RAM into FILENAME.
        -SAVE:EISA:FILENAME          Save EISA NVRAM into FILENAME.
        -RESTORE:CMOS:FILENAME       Restore CMOS RAM from FILENAME.
        -RESTORE:EISA:FILENAME       Restore EISA NVRAM from FILENAME.
        -PRINT:DEVICE                Print setup to DEVICE.
        -PRINT:ALT:DEVICE            Print setup (alternate style) to
                                     DEVICE.

      Examples:
        You want to save CMOS & EISA NVRAM in a file:
          AMISETUP -SAVE:CMOS:CMOS.BIN
          AMISETUP -SAVE:EISA:EISA.BIN
        And now configure several more machines with the same settings:
          AMISETUP -RESTORE:CMOS:CMOS.BIN
          AMISETUP -RESTORE:EISA:EISA.BIN
        Finally, print setup to a parallel printer:
          AMISETUP -PRINT:LPT1


      J   Obtaining new or bug fixed program revisions
      ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

      There are lots of different BIOS/chipset combinations out there.

      If the program doesn't work with your machine, please do the
      following:

      1. Read the manual, especially appendix C (you did, didn't you?).

      2. Use the newest version of the program only. You can get it from
         your shareware vendor or, if you have a modem, from the mccs BBS
         in Singen/Germany.

         mccs BBS Singen/Germany (Sysop Martin Grass, Fido 2:246/8100-8104)

         Line 1: +49-7731-65833
         Line 2: +49-7731-69523
         Line 3: +49-7731-69524
         Line 4: +49-7731-69525
         Line 5: +49-7731-60195 (Multi line: Lines 1-5)
         ISDN:   +49-7731-984026

         FidoNet users: Request the file using the "magic" name AMISETUP.

         Others: Please log in as "GAST", password "GAST" and download
         AMISETUP directly from the main menu.

         You can also get the AMIsetup shareware from the Internet.
         SimTel ftp server and its mirrors (e.g. nic.switch.ch) carry the
         newest version in the directory pub/msdos/sysutl. There might also
         be a Compuserve-Internet gateway.


      3. ONLY if the NEWEST version doesn't work and you are sure it should
         work (appendix C!):

         Send a BIOS image and a CMOS RAM image produced by AMIsetup to
         the author.

         Please follow the instructions in the manual; ensure that NO
         memory manager is loaded.


         Thank you.


      K   Tested BIOS revisions
      ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

      Among others, the program has been successfully tested on the
      following chip set/BIOS combinations:


         Chip set   ³ BIOS date  ³ ID string
         ÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄ
         ACC        ³ 12/12/91   ³ ACC2046
                    ³ 06/06/92   ³ ACC2046
                    ³            ³
         Acer Logics³ 07/07/91   ³ ACER1217
                    ³ 07/07/91   ³ ACER1409
                    ³ 12/12/91   ³ ACER1419
                    ³ 08/08/93   ³ ALI1429
                    ³            ³
         ACT        ³ 07/07/91   ³ ACT
                    ³            ³
         Am. Megatr.³ 12/12/91   ³ AMI/S50
                    ³ 12/12/91   ³ AMI/S61
                    ³            ³
         Contaq     ³ 07/07/91   ³ CTQ486
                    ³ 12/12/91   ³ CTQ 386
                    ³ 12/12/91   ³ CTQ386&486
                    ³ 12/12/91   ³ CTQAUTO
                    ³ 06/06/92   ³ CTQ596
                    ³ 11/11/92   ³ CTQ596
                    ³ 11/11/92   ³ CTQ596-A
                    ³ 11/11/92   ³ CTQ-596A
                    ³ 08/08/93   ³ CTQ596
                    ³            ³
         Chips&Tech.³ 02/02/91   ³ PEAKDM
                    ³ 05/05/91   ³ PEAKDM_B
                    ³ 05/05/91   ³ NEAT286
                    ³ 05/05/91   ³ C&T386
                    ³ 07/07/91   ³ PEAKDM
                    ³ 07/07/91   ³ NEAT386
                    ³ 07/07/91   ³ NEAT3SX
                    ³ 12/12/91   ³ PEAKDM_B
                    ³            ³
         Headland   ³ 07/07/91   ³ HT12
         (LSI)      ³ 12/12/91   ³ SUMMIT_C
                    ³ 11/11/92   ³ SHASTA    (may contain no Extended
                    ³            ³            CMOS RAM)
                    ³            ³
         Eteq       ³ 02/02/91   ³ ET/386H
                    ³ 02/02/91   ³ ET/486H
                    ³ 05/05/91   ³ ET/486H
                    ³ 05/05/91   ³ ET/36H
                    ³ 07/07/91   ³ ETEQ486C
                    ³ 07/07/91   ³ ET/486H
                    ³ 07/07/91   ³ ETEQ/1C
                    ³ 12/12/91   ³ BENG486
                    ³ 12/12/91   ³ BENG386
                    ³            ³
         Forex      ³ 05/05/91   ³ FORX
                    ³ 07/07/91   ³ FORX
                    ³ 12/12/91   ³ FORX
                    ³ 06/06/92   ³ FORX
                    ³ 04/04/93   ³ 4X521
                    ³            ³
         Hint       ³ 07/07/91   ³ CAESAR
                    ³            ³
         Intel      ³ 05/05/91   ³ 80486
                    ³ 05/05/91   ³ ITOPDX
                    ³ 07/07/91   ³ 80486
                    ³ 07/07/91   ³ ITOPDX
                    ³ 07/07/91   ³ ITOPSX
                    ³ 08/08/93   ³ SATURN
                    ³ 04/06/94   ³ PCI82430
                    ³            ³
         Morse      ³ 05/05/91   ³ KP386DX
                    ³            ³
         Opti       ³ 04/15/91   ³ OPWB
                    ³ 05/05/91   ³ OPWB
                    ³ 05/05/91   ³ 386WB
                    ³ 05/05/91   ³ OP386WB
                    ³ 06/06/91   ³ OPWBSX
                    ³ 06/06/91   ³ OPWB493
                    ³ 07/07/91   ³ OPWBSX
                    ³ 07/07/91   ³ OPWB3/B
                    ³ 07/07/91   ³ OP3DX/PI
                    ³ 07/07/91   ³ OPTIEISA
                    ³ 07/07/91   ³ OPBC
                    ³ 07/07/91   ³ OPWB
                    ³ 08/31/91   ³ OPWBDS
                    ³ 12/12/91   ³ OPEISA
                    ³ 12/12/91   ³ OPTIDXBB
                    ³ 12/12/91   ³ OPSXPI
                    ³ 12/12/91   ³ OPTI8290
                    ³ 12/12/91   ³ 0495AUTO
                    ³ 06/06/92   ³ OPT495SX
                    ³ 06/06/92   ³ OPWB4SXB
                    ³ 06/06/92   ³ OPT4 498
                    ³ 06/06/92   ³ OPDXBB-B
                    ³ 06/06/92   ³ OPTIEISA
                    ³ 06/06/92   ³ OPTIAUTO
                    ³ 06/06/92   ³ OPWBB/B
                    ³ 11/11/92   ³ OPWB4SXB
                    ³ 11/11/92   ³ OP495SLC
                    ³ 11/11/92   ³ OP495SX
                    ³ 08/08/93   ³ OP495SLC
                    ³            ³
         PC Chip    ³ 07/07/91   ³ PC CHIP
                    ³ 12/12/91   ³ PC CHIP
                    ³            ³
         PICO       ³ 06/06/92   ³ PICO168
                    ³            ³
         SIS        ³ 02/02/91   ³ SISC
                    ³ 03/15/91   ³ SISA
                    ³ 03/15/91   ³ SISB
                    ³ 03/15/91   ³ SISC
                    ³ 05/05/91   ³ SIS-486
                    ³ 07/07/91   ³ SISAUTO
                    ³ 07/07/91   ³ SISD
                    ³ 07/07/91   ³ SIS486
                    ³ 12/12/91   ³ SIS-EISA
                    ³ 12/12/91   ³ SIS386D
                    ³ 06/06/92   ³ SISAUTO
                    ³ 06/06/92   ³ SIS3486
                    ³ 06/06/92   ³ SIS486
                    ³ 06/06/92   ³ SISEISA
                    ³ 06/06/92   ³ SIS-EISA
                    ³ 11/11/92   ³ SIS3486
                    ³ 11/11/92   ³ SIS461
                    ³ 12/12/92   ³ SIS-EISA
                    ³ 08/08/93   ³ SIS461
                    ³            ³
         Symphony   ³ 03/15/91   ³ SYMP
                    ³ 05/05/91   ³ SYM-486
                    ³ 05/05/91   ³ SYMP
                    ³ 05/05/91   ³ SYM_386B
                    ³ 07/07/91   ³ SYM486
                    ³ 10/25/91   ³ SYMPH_1B
                    ³ 10/25/91   ³ SYM_386B
                    ³ 12/12/91   ³ SYMP
                    ³ 01/20/92   ³ SYM486B
                    ³ 11/11/92   ³ SYMP-461
                    ³            ³
         Texas Instr³ 12/12/91   ³ TIEISA/S
                    ³            ³
         UMC        ³ 03/15/91   ³ UMCWB
                    ³ 05/05/91   ³ UMCWB
                    ³ 07/07/91   ³ UMC480A
                    ³ 07/07/91   ³ UMCWB
                    ³ 07/07/91   ³ U391B
                    ³ 07/07/91   ³ UCF/1
                    ³ 12/12/91   ³ UMCBAUTO
                    ³ 12/12/91   ³ UMCAUTO
                    ³ 06/06/92   ³ UMC480
                    ³ 06/06/92   ³ UMC4807
                    ³ 11/11/92   ³ UMC480
                    ³ 11/11/92   ³ UMC480B
                    ³ 11/11/92   ³ UMC480F
                    ³ 04/04/93   ³ UMC491
                    ³ 04/04/93   ³ UMC491C
                    ³ 08/08/93   ³ UMC480B
                    ³ 08/08/93   ³ UMC491F
                    ³            ³
         UNI        ³ 12/12/91   ³ UNI480
                    ³ 12/12/91   ³ UNICHIP
                    ³ 06/06/92   ³ UNI-4800
                    ³ 11/11/92   ³ U4800VLX
                    ³            ³
         USA        ³ 12/12/91   ³ USER
                    ³ 11/11/92   ³ USA-9204
                    ³            ³
         VIA        ³ 07/07/91   ³ VIAFLEX
                    ³ 06/06/92   ³ VIAEISA   (requires "OFF" in EISA.CFG)
                    ³            ³
         VLSI       ³ 05/05/91   ³ TOPCATSX
                    ³ 07/07/91   ³ SCMPSX
                    ³            ³

      07/25/1994