CHAPTER 4    D86 CONTROL KEYS

D86 has a set of functions invoked by single keys.  Keys which
switch the display (for example, to show a help screen) can be
pressed in any context, to be acted upon immediately.  Other
keys, such as the single-stepping keys, can be invoked any time
D86 is awaiting the beginning of an assembly language command.


Display Control Keys

There are numerous keys that let you control the switchable
window in the upper right corner of the screen.  The F10 and
Alt-F10 keys let you toggle between windows, giving you a "tour"
of what's available.  Various keys accessed by using the "Ctrl"
key as a shift key let you move directly to the window of your
choice.

The keys in this section are acted upon in any debugger context,
whether you are in the main command mode or in the middle of one
of the other modes (typing in a debugger command, an
immediate-execute line, a patch-memory line, or a memory window
specification):

ALT-F10   Toggles you between Help and Non-Help modes.  If the
          window is showing you a help page, it will switch to
          the last Non-Help page that was displayed.  If not, the
          window switches to the last Help screen displayed for
          the current context.

          (HELP key on Wang and DEC, F11 key on TI-PC, CTRL-PF5
          key on Sanyo)

F10       In non-help mode, toggles you between the available
          non-help windows: the sign-on/second disassembly
          window, the status window, the memory display window,
          and, if you have a floating-point chip, the
          floating-point display window.

          In help mode, toggles you between the help windows
          available in the current context.

          (Keypad 0 on the DEC, Print Screen on the Z-100)

Ctrl-I    (or TAB) takes you from any other window directly to
          the sign-on/second disassembly window.  This window
          contains the D86 sign-on message until the first time
          that the Instruction Pointer leaves the first
          disassembly page.  From that point on, the sign-on
          message is no longer available, and you get a second
          disassembly page instead.

Ctrl-S    Takes you from any other window directly to the
          debugger status window.

Ctrl-F    Takes you from any other window directly to the
          floating point display window, if your machine has a
          floating point chip in operation.  If not, this key is
          ignored.

                                                              4-2

Ctrl-N    If you have a memory display window in sight, this key
          advances to the Next window full of memory.

          If you do not have a memory display window, but do have
          at least one memory line specification, this key takes
          you from any other window to the memory display window,
          continuing from the end of the last line display.

          If you have no memory line specifications set up, this
          key is ignored.

Ctrl-P    If you have a memory display window in sight, this key
          retreats the pointer to memory displayed, by the amount
          displayed in the window.  If all the memory formats
          specified generate a fixed-size display (such as the
          B,W,T formats), then this will effect a "Previous page"
          function.  If there are formats producing a
          variable-size display (such as the N,D,C,S,L formats),
          then the retreat will be a probably imperfect
          approximation to an appropriate "Previous page" amount.

          If you do not have a memory display window, this key
          will go to one, just like the Ctrl-N key.

Ctrl-Q    If you are not displaying a help window, this key takes
          you to the last help window that was displayed for the
          current context.  If you are already displaying a help
          window, this key toggles through all the help windows
          available for this context.


Instruction Pointer Positioning Control Keys

All the remaining keys in this chapter can be invoked any time
the debugger is in its main command mode, awaiting the first key
of a debugger command or immediate assembly line.  They change
the value of the Instruction Pointer (IP register), and thus they
change the disassembly display.

None of the control keys in this section cause any program code
to be executed, other than the equivalent of a JMP instruction,
to the place that the disassembly cursor winds up.

WARNING: On some debuggers, you can change the location of what
is being disassembled without changing the IP register value.
I've decided on a "what you see is what you get" philosophy,
since you may well be moving the IP cursor to effect a jump in
the program (for example, you might use the Down-Arrow key to
experimentally skip over the execution of one or more
instructions in the program).  If your intention was just to look
around the program before continuing execution at the place you
left off, you may use the HOME key to return to the place where
execution last halted.

Down-Arrow   Jump to the instruction following the current one.
             Visually, the disassembly cursor moves down by one
             instruction line.

                                                              4-3

Up-Arrow     Jump to the instruction preceding the current one.
             Visually, the disassembly cursor moves up by one
             instruction line.  NOTE that the implementation of
             this function is a little tricky, since it's
             impossible to reliably disassemble backwards.  What
             D86 does is retreat a fixed, fair-sized distance,
             disassemble forward until the current instruction is
             reached, and take the instruction disassembled just
             before the current one.  If there is non-instruction
             code in memory shortly before the current position,
             the synchronization may fail, and this instruction
             may put you in the middle of a previous instruction
             instead of the beginning.  If this happens, you may
             adjust by using the Ctrl-D or Ctrl-U keys.

Ctrl-D       This key is identical to the Down-Arrow key, except
             the jump forward is just one byte, instead of a full
             (usually multibyte) instruction.  (IP is
             incremented.)  You use this key when you think
             you've landed in the middle, rather than the start,
             of an instruction.

Ctrl-U       This key decrements IP, moving the cursor "Up" by
             one byte's worth.  Like Ctrl-D, it is used to
             manually synchronize disassembly.

Pg Dn        Jump to the next disassembly page, at the memory
             location immediately following this page.  Repeated
             pressing of this key allows you to scan program code
             quickly.

             (Alt-Down-Arrow on the TI-PC, Ctrl-C on the Victor,
             Next Screen on the DEC, F12 on the Z-100)

Pg Up        Jump to the previous disassembly page, ending with
             the instruction just before the top instruction on
             the current page.  NOTE the warning given with the
             Up-Arrow description, about possible synchronization
             problems, applies here as well.

             (Alt-Up-Arrow on the TI-PC, Ctrl-R on the Victor,
             Prev Screen on the DEC, F11 on the Z-100)

Home         If you have moved the IP cursor since the last
             program instruction executed, then this key returns
             IP to that spot.  If you are already at that spot,
             this key returns you to the program's starting
             location.  For COM files, this is always location
             0100 in the original code segment.  For EXE files,
             this location was derived from the EXE header
             record.  Note that repeated pressing of HOME will
             cause IP to alternate between the two locations, so
             you can't mess yourself up by pressing the key one
             too many times-- just press it again.

             (Ctrl-K on the Victor, Find on the DEC)

                                                              4-4

Ctrl-E       Jump to the End of the program, as determined when
             it was loaded, and possibly advanced if the program
             was patched from the end.



Program Execution Control Keys

Ctrl-X       Single step the current instruction.  If the
             instruction is a call, go into the procedure to
             single step it.  If you want the entire procedure
             executed on a single keystroke, use the F2 key.

F1           Single-step the current instruction just like the
             Ctrl-X key, except that INT instructions are
             executed all at once, not stepped into.  This
             exception was added with D86 V3.21, because stepping
             into DOS or the BIOS is a hazardous operation,
             likely to crash the computer.

             (Keypad 1 on the DEC)

F2           Procedure step: start program, trapping at the
             instruction following the current one.  This is used
             for executing a procedure call all at once; for
             breaking out of a loop; and for executing a repeated
             string operation all at once.

F4           Start the program, setting a trap at the destination
             of the conditional jump instruction currently
             pointed to.  If we are not pointing to a conditional
             jump, then we single step.

F6           Start the program, setting a trap at the address on
             top of the stack (hopefully a procedure return
             address).

F9           Go until here: Start the program from the point at
             which it last stopped, setting a trap at the current
             CS:IP location.  If you didn't move the IP cursor
             since the program stopped, this will simply tell the
             program to go until the next time this same point is
             reached.  If you did change IP, (for example, if you
             paged forward to find an interesting section of
             code), this command saves you from having to go back
             and single-step up to this point.



Special Action Control Keys

F3           Repeat the last typed-in assembly language or
             debugger command

F7           Enter the Patch Memory mode, described in Chapter 3.

                                                              4-5

Shift-F7     Mark the current CS:IP memory location, for use by a
             following F debugger line command.  F can either
             return to this location, or find memory bytes that
             match the ones at this location.

             (Ctrl-7 on the Sanyo, Select on the DEC)

Alt-F9       If you have a Color video board, your debugger
             display may become corrupted by the program's
             console output.  If it does, press Alt-F9 to
             eliminate the corruption.  This key exists only
             temporarily; on later versions of D86, the
             corruption will be corrected automatically.

             (Ctrl-Shift-PF4 on the Sanyo)

Ctrl-T       Reset the debugger's internal Top-of-Stack pointer
             to the current SP value.  This will cause the
             current stack display to become empty, so that
             subsequently pushed values will appear by themselves
             on the stack display.