Basics for IBM XT and clones (compiled 3/6/94)

  (note: "brand name" clones are usually very different
    and if the BIOS is not Phoenix, switch settings can
    also be BIOS dependent)

    o)  Original IBM PC Beeps
	No beep(power), continuous beep(power), repeating short
	  (system board), long short (system bus),
	  long short short(display), short (blank or incorrect display)

For Phoenix error codes see PHNXERR.ZIP (included with this file)

  Dip switch (IBM and many clones)
	 (0 off, 1 on)
     1 -- Post test 0(enable) 1(disable)
     2 -- Coprocessor 0(yes) 1(no)
     3 --  0,0 (256K or higher)   0,1(128K)
     4 --^ 1,0 (192K)             1,1(64K)
     5 --  0,0 (mono)             0,1(40 by 25 color)
     6 --^ 1,0 (80 by 25 color)   1,1 (EGA or better)
     7 --  1,1 (1 disk drive)     0,1 (2 drives)
     8 --^ 1,0 (3 drives)         0,0 (4 drives)


    o)  Installing a 1.44:
	       This is first drive 0, and appears as D:
	   device=driver.sys /d:0 /t:80 /s:18 ;h:2 /f:7
	   or  drivparm= /d:0 /t:80 /s:18 /h:2 /i /f:7

***********************************************************************

The information on this subject is relayed through our Center from
our own work, Internet Sources and journals.

We relay pieces that have strong relevance to the future of the
Internet.

If this subject interest you, we are putting together an Ad Hoc
group of people for "envisioning" the Internet.

Please contact:
Dr. W. Curtiss Priest
Center for Information, Technology, and Society
466 Pleasant St.
Melrose, MA  02176
Voice: 617-662-4044
FAX: 617-662-6882
Email: bmslib@mitvma.mit.edu
       curt priest, Channel 1 BBS



		      CENTER FOR INFORMATION

			       AND

			   TECHNOLOGY

			      CITS

AN INTRODUCTION

"A Center for furthering Advances in Communication, Computers, and
Networks for Improved Education, Health and Industry"

Summary  --  About the Center for Information, Technology  and
Society

The Center for Information, Technology and Society was originally
a program at MIT and in 1986 became an independent non-profit
institution under the directorship of Dr. W. Curtiss Priest to
further advances in Communication, Computers and Technology.  The
Center is particularly interested in the process of technological
innovation of information systems for the areas of education,
training & manpower, health, medicine, industrial progress and
total quality.

The Center ascribes to the belief that there are better, informed
choices that can be made about technological advances and that
with limited human and monetary resources, these choices have
extreme importance.