***** PERFECT.DOC ***** (v 3.0)

                I.   INTRODUCTION:

                PERFECT BOX is a Computer Aided Design (CAD) program for the
           simulation of loudspeaker performance.  PERFECT BOX is a very
           powerful tool for the amateur or professional speaker builder.
                Loudspeaker design is a balance of compromises involving
           enclosure size, low frequency cutoff, and transient response.
           This program will allow you to model the loudspeaker-enclosure
           combination entirely on your PC.  You are assured of the best
           (lowest in frequency) bass response in the smallest enclosure.
           You can then build the enclosure with full confidence that the
           final result will not become the new dog house for Fido, but an
           accurate, natural sounding system.
                PERFECT BOX does not deal with midrange or tweeter drivers.
           It only considers the low frequency driver in a multi-way system
           (or the only driver in a full-range system.)  Since enclosure
           alignments, such as box size, box type, and box frequency  (now on
           refered to as Alignments), effect the woofer response, PERFECT BOX
           models systems covering low frequencies from 10 to 200 Hertz.  The
           mathematical model will hold for higher frequencies, but I have
           optimized the program for the most useful range.

                II.  REQUIREMENTS:

                PERFECT BOX requires certain parameters that uniquely define
           the driver's characteristics.  Some of these parameters have been
           coined as the Thiele/Small (or T/S) parameters.  If you are new to
           loudspeaker design, it isn't important that you understand what
           each value represents, only that you are able to obtain these
           values from the driver manufacturer, or measure them yourself
           (more accurate.)

                  PARAMETER                         UNITS
                Free air resonance    (Fs)         Hertz
                Q Electrical          (Qes)
                Q Mechanical          (Qms)
                Q Total               (Qts)
                Volume Equivalent
                     Compliance       (Vas)        Ft^3
                D.C. Voice Coil
                     Resistance       (Re)         Ohms
                Peak Cone
                     Displacement     (Xmax)       Inch
                Effective Piston
                     Diameter                      Inch
                Thermal Power         (P)          Watts, RMS

                NOTE:  Qts=(Qes*Qms)/(Qes+Qms)

                PERFECT BOX allows you to store these driver parameters in a
           data file ("BOXDATA").  This file can store characteristics for up
           to 998 different drivers.  A few sample drivers have been included
           so that you can experiment with PERFECT BOX.  These samples
           represent "real life" units which are currently available at this
           time.

                                   -1-





                III. DEFINITIONS:

                SYSTEM ORDER:  PERFECT BOX uses a classical high-pass filter
           model to simulate a loudspeaker mounted in an enclosure.  The
           order of a loudspeaker system represents the same characteristic
           roll off as that of an electrical filter.  The roll off rate (or
           slope) is:
                          roll off rate=(6 * system order) dB/octave
                or
                          roll off rate=(20 * system order) dB/decade

                PERFECT BOX can simulate both infinite baffle (sealed box),
           and vented (ported) systems.  Each of these systems have a natural
           order in which they resemble an electrical high pass circuit.  For
           infinite baffle, order=2, or that is to say that they are of 2nd
           order.  And for vented systems, order=4.  It seems that each kind
           of enclosure has pros and cons associated with them.  In general,
           both systems, if properly aligned, perform with the same low
           frequency response.  In practice, an infinite baffle system is
           easier to build, and possibly has better transient response.  The
           vented system offers slightly higher efficiency (2.9 dB), and good
           cone dampening near the vent frequency (but less below Fb.)  My
           preference is for 4th and 6th order systems.

                SYSTEM CUTOFF FREQUENCY:  This is the frequency at which the
           system amplitude response is exactly 3.0 dB less than at a
           mid-band reference frequency (where response is basically flat at
           0 dB.)  This is a standard point of interest that can be used to
           compare with another system's low frequency response data.  This
           point represents the "half-power" amplitude, as compared to the
           amplitude at the mid-band reference frequency.

                OTHER ORDERS:  As you are problably aware, a Graphic
           Equalizer can make a tremendous effect on the way your speaker
           system sounds.  The bad news is that an equalizer (EQ) usually
           doesn't have a control exactly centered on the proper frequency to
           properly extend low frequency cutoff, and thus will typically make
           matters worst.
                PERFECT BOX can incorporate the effects of either a 1st or
           2nd order, ACTIVE EQ into the loudspeaker model.  This mini EQ
           consists of a simple active high-pass filter, having a low
           turn-over (cutoff) frequency (typically 20-60 Hz), which actually
           has a slight boost (peak) in its amplitude response above its
           cutoff frequency.  If the amount of boost and cutoff freq. are
           suitably chosen, the total system response typically is extended a
           half-octave or more, while providing infrasonic (rumble) filtering
           to boot!
                In 2nd-order EQ's, the boost is controlled by the "D"
           parameter (D=1/filter Q, for you filter buffs.)  Typical values of
           "D" range from 0.3 to 1.414, giving most to least amount of
           amplitude boost.  A "D" of 0.52 gives approximately 6 dB of boost,
           typical starting value.  The EQ frequency and the "D" factor
           should be juggled for the flatest, most extended low frequency
           response.






                                   -2-




                A word of caution:  using large amounts of boost may tax
           small power amplifiers (less than 50 Watts,RMS) beyond their
           limits.  A properly designed 3, 3.5, 5, or 6th order system will
           not over tax your amplifier unless you listen to music either :
           1.  at extremely high SPL levels, 2.  with heavy organ pedal
           notes, or 3. use other signal modification equipment such as an
           extremely low-end boosted Graphic Equalizer (Stupid), or Sub-Sonic
           Synthesizer (Harmonizer.)
                The EQ can be inserted into the signal path of your system at
           either a "Pre-amp out/Amp in" loop, or "tape monitor" connection.
           A simple design for a 2nd order EQ is provided with PERFECT BOX:
           type EQ2  at the DOS prompt to execute this option.  You must have
           a graphics mode in order to run EQ2 because the electrical
           skematic is drawn on the screen after all the circuit values are
           calculated.  You may execute a screen dump (PrtSc) for a hardcopy
           (as with all screens in PERFECT BOX.)

                IV.  RUNNING PERFECT BOX:

                PROGRAM EXECUTION:  Before you start PERFECT BOX, you must
           execute your DOS command GRAPHICS.COM.  This command sets aside
           memory for doing graphic dumps of your CRT to your graphics
           printer.  I have created a simple batch file called GO.BAT, which
           will do this for you.  Of course you must have either GRAPHICS.COM
           on the program disk or in the current DOS path.  The actual
           program file is BOX3_0.EXE.
                1.  Insert the PERFECT BOX program disk into your default
           disk drive, and type GO <Return>.  You should see the PERFECT BOX
           opening screen.  After about 5 seconds, you may press RETURN to
           continue.  Note:  All questions requiring operator input that have
           default values will have those values prompted between
           parenthesis.  Just press RETURN for the default.
                2.  At this point, you need to choose either ;
                     1.  for Automatic Parameter Entry  or,
                     2.  for Manual Parameter Entry.
                If you choose 1., you can LIST, LOAD, STORE, EDIT or PRINT
           driver parameters from the BOXDATA database file.  Option 2. will
           ask you to enter each driver parameter and box characteristic, one
           at a  time.  This choice is good if you only want to run a driver
           through PERFECT BOX once, with out saving the parameters.  Since
           you can store up to 998 different drivers in the data file, I
           rarely use this option!
                3.  Choose "Automatic", and then choose "1. LIST current
           Drivers in database.  You should see a list of drivers with a
           record number for each.  You may choose a particular driver from
           this list by entering the record number, and then press RETURN.
                4.  Or, choose "LOAD a Driver by Record Number," and enter
           the record number you had memorized in the "LIST" step above.  You
           will be prompted if this is the right driver.  A "N" will take you
           back to "Enter Driver record number."









                                    -3-







                5.  At this point, PERFECT BOX will calculate the "Ideal Box"
           volume, the port frequency for that ideal box volume, and the
           cutoff frequency (-3dB point.)  The ideal box volume is the
           smallest enclosure that provides the flatest, deepest low
           frequency response.  The cutoff point will give you a general idea
           of how low the driver will perform in any box design (best case.)
           The port frequency (box frequency) must be set as calculated to
           obtain the cutoff predicted.
                6.  Now you must choose the system order.  If the driver Qts
           is 0.5 or greater, I would try infinite baffle (order=2) systems
           first, otherwise, use order=4, with the ideal box size and
           frequency.  Save the other order options for later.  PERFECT BOX
           will also recommend an order to you.
                7.  Enter the box volume in cubic feet.  I suggest that you
           use the ideal box size and box frequency (for 4th order up) as a
           starting point.  Then, on the next pass, change one of the box
           alignments and check how the response was affected.
                8.  PERFECT BOX will now calculate :   1. Amplitude,  2.
           Maximum Power, and 3. Maximum Sound Pressure Level, at each
           frequency cycle between 10 and 200 Hertz.  Then an Output Menu
           will be presented.
                     Option 1. will plot the classical Bode (pronounced BO
           DEE; or Frequency Response) plot.
                     Option 2, SPL & Power vs. Frequency, will give you an
           picture of the system driven at maximum power.  This plot gives
           the Sound Pressure Level (in dB) and the input power required to
           reach the excursion limit (Xmax) of the driver.
                     Option 3. will list on the screen, all calculated data,
           between the frequency limits of your choice.
                     Option 4. prints option 3. on your printer with the same
           limit choice.
                     Option 5. produces on your printer, a worksheet which
           gives you a handy reference table to use as you change the
           different alignments about your system.  Each block can be filled
           from data printed on the bode plot option.  I suggest that you do
           this option first (only if you have a printer on line.)
                     Option 6. allows you to save your current design
           parameters to the BOXDATA file for future use.  This becomes very
           handy if you want to keep track of your best designs for each
           driver.  If you are loading previously saved values, the default
           values of the next iteration are taken from the BOXDATA file.  You
           must go to the CHANGE menu, and choose "Change ALL Parameters," to
           complete the process.
                     Option 7. toggles you between EGA and CGA modes.  If you
           are using EGA and want to use the Print Screen function, you have
           to switch to CGA (Yuk!, I know), for the Graphics dump to work.
                     Option 8. (or RETURN) will take you to the Change Menu.
           At this point you may choose what parameter to change in an
           attempt to optimize the frequency plot, or what ever else you are
           trying to acheive.  If you are currently working on a 2nd or 4th
           order system, the "Change EQUALIZER Frequency or D." choice will
           not be allowed.  Thus if you want to change to an "equalized"
           order, you may do use the "Change ALL Parameters. option first.
           Remember that the previous value for each prompt in the CHANGE
           menu will be the default value (just press RETURN.)



                                   -4-







                After you are satisfied with the current design parameters,
           choose "NO CHANGES" in the Change Menu.  PERFECT BOX will now
           calculate the port lengths required to tune the box to the
           frequency last chosen.  A column for two identical length ports is
           given also.  Dual ports are useful when the box volume is large or
           the MACH speed is too large for a single port.  The MACH number is
           the percent of the speed of sound that will occur at the largest
           port output.  Stay away from large (speed> 0.2) port MACH speeds
           as they will cause unmusical whistle noises from the port.  Also,
           ports that are longer than the box depth, can be curved inside the
           enclosure with PVC swept elbows.

                V.   DESIGN HINTS:

                  If the ideal box volume is too large to be realistically
           built, PERFECT BOX will allow you to see just how the loudspeaker
           performance will suffer, as you down size box volume.  It is this
           iterative design process that PERFECT BOX is designed for.  By
           changing either box volume, port frequency, or in EQ cases, EQ
           frequency and boost, a "perfect" frequency curve can be obtained.
           At this point you can tell how good a driver really is because
           sometimes another driver will out perform others in half the
           enclosure volume!
                The port frequency is set by the area and length of the port.
           PERFECT BOX will calculate the port for you, but the length is
           typically 10-15% off, so add an inch to the calculated value, and
           measure the box frequency for yourself (or have a technician do
           it.)  The system will not perform as calculated if you miss the
           port frequency by as little as 1 Hz.  Also, after you have reached
           a final box size, increase the box volume by as much as required
           to account for volume used by the drivers, bracing, and crossover
           network.
                To find box diminsions from the box volume, take the volume
           in cubic feet, multiply by 1728 cubic in/ft^3, to get in^3.  Then
           take the cube root (or raise it to the 0.3333334 th power.)  Now
           this number is the width in inches.  Multiply the width by 1.62
           for the height, and multiply the width by 0.62 for the depth.
                     volume (ft^3) * 1728 = volume (in^3)
                     width  (in.)   =   (volume (in^3))^0.3333334
                     height (in.)   =   width * 1.62
                     depth  (in.)  =   width * 0.62
                NOTE: All diminsions are internal, not external!
                This will give the box a "typical speaker look" and also set
           the diminsions up for minimum internal reflections.  PERFECT BOX
           calculates these diminsions for you and prints them in the port
           length table.













                                      -5-






                VI.  REFERENCES:

                This document and the program PERFECT BOX are only tools for
           the speaker designer.  One must know how to use these tools
           properly before judging the usefulness of PERFECT BOX.  I suggest
           that you read any of the following publications on the finer art
           of speaker building.

                       SPEAKER BUILDER MAGAZINE (6 times a year)
                        Edward T. Dell, Jr., Publisher
                        PO Box 494
                        Peterborough, NH 03458

                       "The Loudspeaker Design Cookbook"
                        by Vance Dickason
                        Distributed by:
                        Old Colony Sound Lab
                        PO Box 243
                        Peterborough, NH 03458-0243

                       "How to Design, Build, & Test Complete
                        Speaker Systems"
                        by David B. Weems
                        Library of Congress # TK9968.W43
                        Published by:
                        TAB Books
                        Blue Ridge Summit, PA  17214
                        No. 1064

                VII. VERSION 2.3 ADDITIONS:

                The latest version of PERFECT BOX, v2.3, adds the following
           options to the previous versions.

                1.   The ability to change the path to the boxdata file.
           This allows you to have multiple boxdata files, each in separate
           subdirectory, or disk.  The current path is now displayed at the
           opening menu.  The default DOS path is the initial drive path.

                2.   The ability to save the current alignment (box volume,
           box frequency, order, EQ frequency, and D,) to the BOXDATA file.
           This allows you to save your favorite box alignment for each
           driver.  You may also load previously saved parameters for a
           starting point on a new design.

                3.  Dual driver systems are now handled.  You may now choose
           from three different configurations in series or parallel:
                  Standard --Drivers side-by-side, sharing the same box.
                  Push-Pull--Same box, mounted back-to-back or
           front-to-front, wired out of phase.
                  Isobaric (constant pressure) systems--Drivers close-coupled
                             by a small air-tight tunnel.
                See "The Loudspeaker Design Cookbook" for more information on
           these variations in system design.




                                   -6-







                4.   A BOXDATA file print option which makes a complete
           hardcopy of the current BOXDATA file drivers, including all
           parameters, or Ideal Box values.

                5.   Maximum SPL and minimum power values above 20 Hz. are
           denoted on the Excursion limit plot, for quick reference.  Also
           these values are helpful when designing dual-driver or very heavy
           power rated systems.

                6.   One of the prompts in the LOAD driver sequence has been
           deleted to speed up the process of parameter loading.

                7.   A DOS Shell is provided to allow non-resident DOS
           commands to be executed without leaving the PERFECT BOX program.
           Typical uses would be to : view disk directories, disk space,
           format disks or execute any new PERFECT BOX utilities (currently
           the BSORT.BAT and ADDATA.EXE progams.)

                See the PERFECT1.DOC for more details on new additions.


                VIII.  ERRATA:
                Your support helps!  PERFECT BOX is supported by you, the
           user.  Without user support, Shareware can not continue to exist!
           Use this program, give a copy of PERFECT BOX to your friends (the
           BBS Archive file is the best way to make sure all the PERFECT BOX
           files are present.)  Above all, don't forget your part in the
           deal!  If you are using PERFECT BOX on a trial basis, that's fine.
           If you are using PERFECT BOX in your business, that's great!  Just
           don't forget the concepts under which shareware functions.
                PERFECT BOX is under constant scrutany for improvement.  If
           you have any ideas for new features/functions, or problems in
           program operation, send them to me at AUSTIN ACOUSTICS.  Your
           suggestion could be included in the next revision of PERFECT BOX,
           of which you will recieve the first copy!
                By registering your copy with me, you will be notified of
           major PERFECT BOX revisions, and new BOXDATA file parameters.  I
           will update your present version, and append any BOXDATA
           parameters I have recieved from others to your disk.  Please send
           a COPY of your PERFECT BOX program disk (5.25" or 3.5") in a U.S.
           Post Office approved disk envelope (or safe equivalent,)
                              and $40 (check or money order)
           to cover registration and return postage ($52 for Overnight
           Express Return.)
                Please note that a registered user will not have to see the
           annoying "Please Register" boxes that are sprinkled throughout the
           program.  But this doesn't mean that the un-registered copy is
           "crippled" in any way, because it isn't.  All PERFECT BOX
           functions are available on the un-registered program.

                Please make checks payable to:

                               WARREN MERKEL
                               9874 LANCEWOOD STREET
                               ORLANDO, FL  32817-4251

                               *** End of Document ***









                                       -7-