DBTCHECK DOC - August 1990



          DBTCHECK
          August 1990
          Erik A McBeth

                                     INTRODUCTION


               DBTCHECK is designed to help in the fixing and diagnosing of
          dBASE memo problems in both dBASE III, III+ and IV.  Many common
          memo problems can be fixed by DBTCHECK and its strength lies in
          its simplicity and speed.  DBTCHECK is NOT intended to fix severe
          data corruption in memos, but fortunately most memo problems are
          related to factors outside of the data itself.  Neither 
          Ashton-Tate nor its author assumes ANY responsibility for damages
          incurred as a result of using DBTCHECK.  There is no guarantee
          that your data will be set right, always RUN THE PROGRAM ON
          BACKUP DATA.
               
               DBTCHECK will help with the following problems:

          1)  Memo marker staying uppercase after deleting all the data.
          2)  "Disk full" errors when saving/accessing memos.
          3)  Memo (DBT) files growing to extreme size during dBASE copy
              operations.

               In general, after running DBTCHECK and fixing any errors,
          you'll want to load dBASE and do the following:
                    
                    USE file
                    COPY TO temp
                    ZAP  (erases all records, do you have a backup file?) 
                    APPEND FROM temp

          This should help to shrink the DBT file and also reset any memo
          markers in the DBF file.

               This copy operation could also be accomplished by using a
          utility (developed by the author) called DBTCNVT which "packs"
          memo fields and will even allow you to optimize memo operations.


















                                   DBTCHECK INTRO




                             DBTCHECK DOC - August 1990



                                   DBTCHECK SYNTAX


          DBTCHECK dbf_file [/F /T /B /I /S /L /X /O /3 /4 /Rx /Jx]
          where:

          dbf_file    = the dBASE file you want checked

          /F          = Fix the errors in the dbF only. These errors
                        include deleted or lost blocks and version byte.
                                                
          /T          = Fix the errors in the dbT only.  These errors
                        include "too big" memos and wrong blocksize.  When
                        guessing the size of "too big" memos a guess of
                        blocksize-8 or 512-8=504 should be OK.
                
          /B          = Performs both the /F and /T parameters.

          /I          = Show Information on all records with memos.
                        DBTCHECK usually only shows information on a record
                        when errors are found.

          /S          = Speed mode, in this mode only lost memo blocks can
                        be checked and cleaned up.

          /Lx         = Set block number Limit or threshold.  If you
                        suspect that a block number is out of range and
                        DBTCHECK is not marking it as such then you can use
                        this parameter.  /L1234 would set the threshold at
                        1234, all memos with pointers greater than or equal
                        to this will be considered "lost."  

          /X          = Perform eXtensive testing, test for duplicate and
                        overlapping blocks.  In order to accomplish this
                        two files (_BLOCKS.DBF and _BLOCKS.NDX) must be
                        created in the current drive.  Info on each memo
                        takes up about 40 bytes.  This operation can be
                        slow, but is much faster than earlier versions of
                        DBTCHECK.

          /O          = Show information on all records with memos but in
                        block number, as opposed to record number, order. 
                        See /X above for info regarding diskspace.

          /3          = Force the opening of the file as a dBASE III type
                        memo file.  If we also specify the parameter /F (or
                        /B) then the version byte in the dbf file will also
                        be set.

          /4          = Force the opening of the file as a dBASE IV type
                        memo file.  If we also specify the parameter /F (or
                        /B) then the version byte in the dbf file will also
                        be set.




                                   DBTCHECK SYNTAX




                             DBTCHECK DOC - August 1990



          /Rx         = Read the memo file using a block size of x bytes. 
                        Use this if you suspect that the blocksize in the
                        memo header has become corrupted.  If you also
                        specify the parameter /T (or /B) then this
                        blocksize will be written to the memo header.

          /Jx         = Jump to record x to start the analysis/fixup.  This
                        is handy if you suspect that the corrupt memos
                        start toward the end of the file.


          all parameters besides the file name are optional, DBTCHECK will
          NOT fix a file unless you tell it to.

          EX:

                 DBTCHECK tester

          we want DBTCHECK to check for errors in the dBASE data file 
          TESTER.DBF.  DBTCHECK will only report problems, not fix them.  

                 DBTCHECK tester /B
                   
          This will cleanup errors found in both the data and memo file.

          Hint:  the headers of the DBF and DBT files are corrected first,
          before any other file operations (except looking for free blocks)
          and if that is all you need fixed then you might try something
          like this:

                 DBTCHECK tester /B /4 /R512 /J100

          This would set the DBF version byte to look for dBASE IV memos,
          the block size in the DBT to be 512 bytes, and the next available
          block number in the DBT to be end-of-file.  We use the /J
          parameter to jump to a record number far down field so we don't
          have to wade through all the memos.  This is of course only an
          example and your specific needs in changing the file headers
          would probably be different.


















                                   DBTCHECK SYNTAX




                             DBTCHECK DOC - August 1990



                               DBTCHECK ERROR MESSAGES

                      Explanation of errors which occur with memos.

          Deleted   - Memo block deleted, DBF marker points to a memo
                      which has been deleted or has a length of zero.  Fix
                      with /F or /B parameter.

          Lost      - Memo block doesn't exist, DBF marker points beyond
                      the end of the file.  Fix with /F or /B parameter.

          Too big   - Memo is too big, the memo either has a length
                      greater than the size of the file or the end of file
                      marker was never found in this memo.  You must run
                      DBTCHECK with the /T or /B parameter in order to
                      cleanup this sort of error.  You will be asked to
                      provide the memo lengths of these huge memos.
                      Guessing a number too high could destroy information
                      in subsequent memos - USE WITH CAUTION!  (See the
                      syntax section for more discussion on memo lengths)

          Dup       - If duplicate checking is on and DBTCHECK finds that
                      a block number has been used more than once than
                      this message will print along with the record number
                      containing the original block number.  Having
                      duplicate block numbers simply means that two record
                      lay claim to the same memo.  Can be fixed by copying
                      dbf to a new name (from inside of dBASE) and then
                      delete the duplicate memo data.

          Overlap   - A memo has been placed inside the space supposedly
                      occupied by another memo.  Can be fixed by copying
                      dbf to a new name (from inside of dBASE), this will
                      then place the memo data in its own block.

          Free lost - The link-list of free blocks points to a block which
                      does not exist.  Fix all "free" errors with the /T
                      or /B parameter, DBTCHECK will set the next
                      available block to the end of the file. 

          Free used - The link-list of free blocks is pointing to a block
                      which is already being used for a memo.

          Free loop - The link-list of free blocks has a loop (ex:
                      3->4->3).  


                                Other General Errors

          Error in closing file
                  Had some trouble closing the file.

          Error in creating file




                               DBTCHECK ERROR MESSAGES




                             DBTCHECK DOC - August 1990



                  Had some trouble creating a fresh file, check for files
                  with the same name that may be READ-ONLY.  

          Error in finding size of file
                  Couldn't figure out how big a file was.

          Error in memory allocation of
                  Ran out of memory to allocate memory for this object.

          Error in opening file
                  Had some trouble opening the file, check for files that
                  may be READ-ONLY.

          Error in parameter passed
                  You specified an unknown or incorrect parameter.

          Error in reading from file
                  Trouble reading from file, may be sign of file
                  corruption.

          Error in seeking in file
                  Trouble moving around in file, may be corruption or bad
                  disk.

          Error in value of parameter passed
                  The value passed may be too high or low.

          Error in writing to file
                  Trouble writing to file, may be corruption or bad disk.
                     



























                               DBTCHECK ERROR MESSAGES