PROCLIP2.LIB
                                         
                       - The Professional Clipper Library -
                                         
                                   Version 2.00
                                         
                                        By
                                Jason R. Matthews
                                         
                                         
                                February 15, 1988
                                         
                                         
                        **********************************
                        *   Programming extensions for   *
                        *  NANTUCKET CLIPPER SUMMER '87  *
                        **********************************












































                              - Table of Contents -
                                         
                                         
     ========================================================================
     
     
     COPYRIGHTS     Acknowledgments.........................................v
     
     DISCLAIMER     "As is".................................................v
     
     OVERVIEW       General overview.......................................vi
     
     REGISTRATION   How to become a "registered user."....................vii
     
     USAGE          General syntax of functions..........................viii
     
     CAUTIONS       Indicates possible conflicts.........................viii
     
     LINKING        With Microsoft, Plink86 or Turbo Link...................x
     
     ERROR
     HANDLING       Internal critical error handling functions.............xi
     
     SYNTAX
     CONVENTIONS    PROCLIP2 Documentation syntax conventions............xiii






























                                        - i -
                                          
          Copyright (c) 1985-88 by Jason R. Matthews - All Rights Reserved
                                          

                                          
     PROCLIP2.LIB 2.00 User Documentation                 February 15, 1988
     ======================================================================



                              - Table of Contents -
                                         
                                         
     BORDER         Using the color as set in the SET COLOR TO...,
                    activates the screen border on CGA and VGA
                    monitors................................................1
     
     BOXCOLOR       Change the color attribute of the border of a
                    "window" on the screen without having to
                    rewrite the BOX.........................................3
     
     CLOCK          Display a dynamic clock anywhere on the screen
                    using selectable colors and format......................6
     
     CURSOR         Set cursor to full, half, standard or any user
                    selectable size or completely disable cursor
                    from the current video screen...........................9
     
     ERASTEXT       Erase all text characters from within a
                    specific area of the screen.  Great for erasing
                    lines containing graphics characters you wish
                    to retain..............................................12
     
     FILEATTR       Set or reset a file's directory attributes.............14
     
     GETCOLOR       Obtain the current foreground and background
                    color attribute from the position requested............17
     
     ISCGA          Indicates if the attached monitor is driven by
                    a standard Color Graphics Adapter (CGA)................19
     
     ISEGA          Indicates if the attached monitor is driven by
                    a standard Enhanced Graphics Adapter (EGA).............20
     
     ISMONO         Indicates if the attached monitor is driven by
                    a standard Monochrome Adapter (MDA)....................21
     
     ISVGA          Indicates if the attached monitor is driven by
                    a standard Video Graphics Array Adapter (VGA)..........22
     
     NEWCOLOR       Change the color attribute of a "window" on the
                    screen without having to rewrite the data..............23
     
     PRTSC          Provides print screen and print screen
                    translation facilities.................................26
     
     RESET          Provides an instant hardware or software reset
                    of the computer........................................29







                                       - ii -
                                          
          Copyright (c) 1985-88 by Jason R. Matthews - All Rights Reserved
                                          

                                          
     PROCLIP2.LIB 2.00 User Documentation                 February 15, 1988
     ======================================================================



                              - Table of Contents -
                                         
                                         
     RESTBOX        Restore a "window" area of the screen to the
                    original, or different, screen location using
                    original, or different screen colors...................31
     
     RESTCURS       Restore the cursor to the shape and position
                    when it was saved into a numeric memory
                    variable with SAVECURS.................................34
     
     SAVEBOX        Save a "window" area of the screen into a
                    character memory variable..............................35
     
     SAVECURS       Save the current cursor shape and position.............37
     
     SCROLL         See VSCROLL
     
     SDIR           Read the directory entry by entry obtaining the
                    filename, file update date & time and current
                    file size using attributes specified...................39
     
     SOUND          Allows generation of a wide range on sounds for
                    variable durations.  Similar to Clipper's
                    TONE() command but with more flexibility on the
                    duration...............................................44
     
     SPRINT         Prints a given string onto the screen using
                    selectable color attributes without issuing a
                    SET COLOR TO command.  Optionally resets the
                    cursor position or not.................................47
     
     STAMP          Provides date and time stamping capabilities to
                    any file...............................................50
     
     UNRESET        Intercepts CTRL ALT DEL to either prevent or
                    warn the user of the attempt...........................52
     
     VIDEO          Turn on or off the video screen........................54
     
     VSCROLL        Provides vertical and horizontal scrolling with
                    full control over the color attribute used
                    during the scroll......................................56












                                       - iii -
                                          
          Copyright (c) 1985-88 by Jason R. Matthews - All Rights Reserved
                                          

                                          
     PROCLIP2.LIB 2.00 User Documentation                 February 15, 1988
     ======================================================================



                              - Table of Contents -
                                         
                                         
     WILDAT         Search a target string for the first occurrence
                    of another string or wildcard pattern
                    optionally ignoring case, in a left to right
                    search. ...............................................59
     
     WILDRAT        Search a target string for the first occurrence
                    of another string or wildcard pattern
                    optionally ignoring case, in a right to left
                    search.................................................63
     










































                                       - iv -
                                          
          Copyright (c) 1985-88 by Jason R. Matthews - All Rights Reserved
                                          

                                          
     PROCLIP2.LIB 2.00 User Documentation                 February 15, 1988
     ======================================================================



     ------------------------------------------------------------------------
                          - Copyright Acknowledgments -
     ------------------------------------------------------------------------
     
     
                    CLIPPER is a Trademark of Nantucket, Corp.
              IBM is a Trademark of International Business Machines.
              Tom Rettig Library is a Trademark of Tom Rettig Assoc.
            Microsoft Overlay Linker is a Trademark of Microsoft Corp.
        PLINK86 & PLINK86plus are Trademarks of Phoenix Technologies, Ltd.
               Turbo Link is a Trademark of Borland International.
                    Intel is a Trademark of Intel Corporation.
     
     All references in this documentation to trademarks, copyrights,
     registered names or the like are intended only as a reference and do not
     contain any inference.
     
              ******************************************************
              * The author is not associated with Nantucket, Corp. *
              ******************************************************
     
     ------------------------------------------------------------------------
                             - Software Disclaimer -
     ------------------------------------------------------------------------
     
     
     Although a great deal of time and effort have been spent designing,
     coding and debugging these functions, it cannot be certain that they are
     totally error free.  It should be clearly understood that PROCLIP2 is
     released "as is".  The author makes no warranties, express or implied,
     with respect to this software, including without limitation, warranties
     of merchantability and fitness for a particular purpose.  In no event
     shall the author be liable for any direct, indirect or consequential
     damages, real or imagined.





















                                        - v -
                                          
          Copyright (c) 1985-88 by Jason R. Matthews - All Rights Reserved
                                          

                                          
     PROCLIP2.LIB 2.00 User Documentation                 February 15, 1988
     ======================================================================



     ------------------------------------------------------------------------
                                   - Overview -
     ------------------------------------------------------------------------
     
     
     The Professional Clipper Library (PROCLIP2), Version 2.00, is designed
     for the CLIPPER programming language (Summer '87 release) from
     Nantucket, Corp.  It is for the programmer who desires more than the
     current language specifications can support.  PROCLIP2 is not designed
     to replace the standard Nantucket Clipper Library, but to provide
     enhanced capabilities in those areas Nantucket chose not to.  Some of
     the functions provided by PROCLIP2 will undoubtedly be made available in
     future releases of Clipper, but the need to utilize them in application
     development is today and PROCLIP2 was designed to meet some of those
     needs.  As with any language, Clipper contains features and functions
     which are unique to it and therefore make it more attractive.  By the
     same token, it lacks features which may appear to be "standard" in other
     languages and thus makes it somewhat frustrating to use from time to
     time.  While PROCLIP2 does not, and indeed cannot, solve all of these
     frustrations it will help where it can.
     
     
     Care has been taken to utilize only published and supported accesses
     into Clipper in an effort to ensure upward compatibility with future
     releases of Clipper.  Some of the routines contained within PROCLIP2 are
     similar in name to those provided by Nantucket or another creator of
     add-on libraries, Tom Rettig Assoc.  Each function has been created with
     the concept of enhancing existing functions and procedures regardless of
     their origin.  All functions contained within PROCLIP2 have been coded
     in Intel 8088/8086 assembly language for compactness of code, execution
     efficiency and compatibility through all Intel microprocessors.
     























                                       - vi -
                                          
          Copyright (c) 1985-88 by Jason R. Matthews - All Rights Reserved
                                          

                                          
     PROCLIP2.LIB 2.00 User Documentation                 February 15, 1988
     ======================================================================



     ------------------------------------------------------------------------
                                 - Registration -
     ------------------------------------------------------------------------
     
     
     A good deal of effort, time and money have been spent designing,
     creating and supporting PROCLIP2.  If these functions are of use, and
     you would like to support the creation of more, a donation to help
     defray these costs is greatly appreciated.  For a donation of US $25.00
     you may become a "registered user" of PROCLIP2 and will receive
     notification of upgrades prior to release to the general public as well
     as notification of any programmer errors discovered.  Input to define
     and develop useful functions to be added into PROCLIP2 are always
     solicited.
     
     
     Send all requests, registrations and suggestions to:
     
                                  Jason Matthews
                                  P.O. Box 1296
                              Rowlett, Texas  75088
                                         
                                  Source: NAN779
                              CompuServe: 71410,2051































                                       - vii -
                                          
          Copyright (c) 1985-88 by Jason R. Matthews - All Rights Reserved
                                          

                                          
     PROCLIP2.LIB 2.00 User Documentation                 February 15, 1988
     ======================================================================



     ------------------------------------------------------------------------
                                 - Usage Format -
     ------------------------------------------------------------------------
     
     
     As Nantucket was kind enough to provide the facility to create User
     Defined Functions (UDF), all of the PROCLIP2 functions utilize this
     format.  Programmed into most of the functions is a sub-function which
     validates parameter count, type and contents prior to attempting
     function execution.  Hopefully this will resolve runtime errors.  If a
     PROCLIP2 function is called and nothing seems to happen it quite
     probably was ignored due to a parameter difficulty.  Almost all of
     PROCLIP2s functions use the published Clipper vector names contained in
     the EXTENDA.MAC released with Clipper.  Hopefully this will prevent
     PROCLIP2 from becoming obsolete when Nantucket releases future versions
     of their language.
     
     
     ------------------------------------------------------------------------
                      - Cautions, Warnings & Compatibility -
     ------------------------------------------------------------------------
     
                          - Environment Compatibility -
     
     Some of the functions contained in PROCLIP2 assume they are operating in
     an IBM (or 100% compatible) system utilizing DOS 2.xx or greater, OS/2
     in "real" mode or Microsoft Windows.  What this means is that they will
     access the ROM BIOS or perform DMA (direct memory access) from time to
     time to perform specific functions or obtain information regarding the
     current system environment.  As long as you are using an IBM (or 100%
     compatible) with the proper version of DOS you should experience no
     difficulties.
     
                            - Monitor Compatibility -
     
     PROCLIP2 is intelligent enough to determine the current monitor type and
     treat it accordingly.  This includes Monochrome, Color Graphics (CGA),
     Enhanced Graphics (EGA) and Video Graphics (VGA) monitors in either
     native or emulated modes.  Those functions which offer DMA video buffer
     updating should be tested on the system prior to releasing it for use.
     These functions are again assuming they are operating in an IBM-type
     environment and so they "know" where the video buffer currently resides.
     DMA updating is useful when operating in personal computers which have a
     clock speed slower than 8MHz.  If one of the screen functions appears to
     be operating sluggishly try attempting the DMA update request specified
     in the function.
     








                                      - viii -
                                          
          Copyright (c) 1985-88 by Jason R. Matthews - All Rights Reserved
                                          

                                          
     PROCLIP2.LIB 2.00 User Documentation                 February 15, 1988
     ======================================================================



     ------------------------------------------------------------------------
                 - Cautions, Warnings & Compatibility (cont'd) -
     ------------------------------------------------------------------------
     
                             - Memory Compatibility -
     
     Some functions within PROCLIP2 require a temporary allocation of memory
     from the system.  If this allocation is not possible the function will
     refuse to function.  The typical allocation request is less than 1Kb
     (1024 bytes) so no real conflict should exist.  Once memory has been
     allocated and used by PROCLIP2 it will be returned to the system memory
     pool for use by other programs or DOS.  PROCLIP2 will not attempt to
     allocate any memory outside of the standard 640Kb limit.
     
     
                      - System / BIOS dependent functions -
     
     Some functions are dependent upon system level functions or internal
     BIOS interrupt vectors.  These functions, when active, have the ability
     to "hang" the computer if a serious error occurs in the system.
     PROCLIP2 will intercept DOS level critical errors before DOS is made
     aware of them and make every effort to restore any interrupt vectors or
     system functions to their previous state before passing the error to DOS
     for handling.  This feature of PROCLIP2 is unique to PROCLIP2 as it
     requires no additional coding or intervention on your part.  When a
     function is activated which depends on interrupt or system vectors (eg.
     CLOCK) it will automatically create the "hook" into the DOS critical
     error handler.  Should a critical error occur all PROCLIP2 functions
     which are using interrupt or system vectors will be deactivated by
     PROCLIP2.

























                                       - ix -
                                          
          Copyright (c) 1985-88 by Jason R. Matthews - All Rights Reserved
                                          

                                          
     PROCLIP2.LIB 2.00 User Documentation                 February 15, 1988
     ======================================================================



     ------------------------------------------------------------------------
                               - Linking PROCLIP2 -
     ------------------------------------------------------------------------
     
     
     Use of this library is identical to that of any other library designed
     for use with CLIPPER or other programming languages.  Refer to the
     Clipper programming manual or any manual containing a description of how
     to operate the linker you are currently using.
     
     Listed below are sample syntax for three of the most popular linkers.
     
     With MicroSoft Overlay Linker -
     
     C>LINK
     Microsoft (R) Overlay Linker  Version 3.61
     Copyright (C) Microsoft Corp 1983-1987.  All rights reserved.
     
     Object Modules [.OBJ]: YOURPROG
     Run File [YOURPROG.EXE]:
     List File [NUL.MAP]:
     Libraries [.LIB]: CLIPPER + PROCLIP2
     
     
     With Plink86 -
     
     C>PLINK86
     PLINK86plus ( Nantucket ) Version 2.24
     Copyright (C) 1987 by Phoenix Technologies Ltd.,
     All Rights Reserved.
     
     =>FI YOURPROG
     =>LIB CLIPPER
     =>LIB PROCLIP2
     =>;
     
     
     With Turbo Link -
     
     C>TLINK YOURFILE,YOURFILE,NUL,CLIPPER + PROCLIP2
     Turbo Link  Version 1.0  Copyright (c) 1987 Borland International
     
                                 * * * NOTE * * *
     If you are using PROCLIP2 with any other library which contains the same
     function names (eg. CLOCK) you will see some warning errors generated by
     whichever linker you are using.  If you like the PROCLIP2 function
     better than the others just make certain that PROCLIP2 is the first
     library in the list after the CLIPPER library is specified.  Otherwise
     make certain their library is first in the list.






                                        - x -
                                          
          Copyright (c) 1985-88 by Jason R. Matthews - All Rights Reserved
                                          

                                          
     PROCLIP2.LIB 2.00 User Documentation                 February 15, 1988
     ======================================================================



     ------------------------------------------------------------------------
                                - Error Handling -
     ------------------------------------------------------------------------
     
     
     PROCLIP2 currently contains three functions which intercept low level
     (BIOS) interrupt vectors to perform their functions.  They are:
     
               *    CLOCK
     
               Intercepts INT 08H, which is the timer interrupt.  This
               interrupt was chosen over the more typical INT 1CH in order to
               make it more usable under some TSR's which never relinquish
               INT 1CH.  The CLOCK routine calculates the time at every timer
               tick (18.2 times per second).
     
               *    PRTSC
     
               Intercepts INT 05H, which is the print screen interrupt.
               PRTSC uses this interrupt vector to replace the standard BIOS
               print screen with the translation facilities of PROCLIP2.
     
               *    UNRESET
     
               Intercepts INT 09H, which is the basic keyboard interrupt.
               UNRESET requires access at this level in order to prevent the
               CTRL ALT DEL sequence from resetting the computer.
     
     
     With these three routines, and more to be included in subsequent
     releases of PROCLIP2, it became evident that some type of error handling
     was necessary.  Clipper Summer '87 now contains an extensive runtime
     error handling function to intercept most errors and allow your
     application to determine the best course of action.  While each of the
     PROCLIP2 functions contains an "off" command, a given application could
     not be expected to intercept every possible error condition.  In light
     of this, PROCLIP2 now contains it's own built-in critical error handling
     system.  The error handling system in PROCLIP2 is designed specifically
     for these interrupt driven routines, nothing more.  When a critical
     error is declared by the operating system (as in drive failure), the
     PROCLIP2 critical error routine will automatically "unhook" all
     interrupt driven routines.  The interrupt vectors in BIOS and DOS will
     be restored to their original state and the PROCLIP2 interrupt driven
     functions will cease their operation immediately.  This feature is
     unique to PROCLIP2 in that no additional programming is necessary.
     There is no need for you to remember which functions are currently
     active, PROCLIP2 maintains it's own internal table and uses it to
     process the error handling.  As an additional feature, you can invoke
     the PROCLIP2 error recovery system by yourself.  Application error
     trapping is great, but sometimes it can determine the best course of
     action is a rapid termination of the program.




                                       - xi -
                                          
          Copyright (c) 1985-88 by Jason R. Matthews - All Rights Reserved
                                          

                                          
     PROCLIP2.LIB 2.00 User Documentation                 February 15, 1988
     ======================================================================



     ERROR HANDLING (cont'd)
     
                                     BAILOUT
                                     -------
     
     
     The BAILOUT function should only be used when a runtime error has
     occurred which the application program determines is unrecoverable.
     Invoking the BAILOUT function effectively terminates all PROCLIP2
     interrupt driven functions.
     
     
     Format:
     
               bailout()
     
     
     Parameters:
     
               None.
     
     
     Example:
     
               1.   The ERRORSYS.PRG has determined that a runtime error is
                    unrecoverable.  Before quitting the program any interrupt
                    driven PROCLIP2 functions need to be disabled.
     
                    .
                    .
                    .
                    bailout()
                    .
                    .
                    quit
     
     
     Returns:
     
               Nothing.















                                       - xii -
                                          
          Copyright (c) 1985-88 by Jason R. Matthews - All Rights Reserved
                                          

                                          
     PROCLIP2.LIB 2.00 User Documentation                 February 15, 1988
     ======================================================================



     ------------------------------------------------------------------------
                              - Syntax Conventions -
     ------------------------------------------------------------------------
     
     The follow are the syntax conventions used throughout the PROCLIP2
     documentation.
     
     [...]     Indicates an optional parameter.  Any parameter surrounded by
               square brackets should be considered optional.  All optional
               parameters have a default.
     
     '...'     Indicates a parameter string.  A parameter string is a word or
               phrase used to inform the function of a certain request, as in
               'on' or 'off'.  All examples use lower case but case is not
               sensitive in any of the PROCLIP2 functions which use a
               parameter string.
     
     |         Indicates an exclusive or.  In other words, multiple
               parameters separated by the | character are mutually exclusive
               and cannot be used in the same function call, as in 'on' |
               'off'.
     
     Example:
     
     As this function employs all syntax possibilities, it is the best to
     discuss in an example.
     
               cursor(['std' | 'off' | 'half' | 'full'] | [start,end])
     
     [...]     The parameters surrounded by square brackets are optional in
               that they are not necessary for the function to operate in
               default mode.  When two or more parameters are enclosed within
               the same bracket pair they are dependent upon each other in
               one way or another.
     
     'std'     This, and the other parameters specified in this fashion, are
               string parameters informing the function of the action to
               take.  This mechanism makes reading the resulting source code
               easier as no "cryptic" codes need to be interpreted.
     
     |         All parameters separated by the "|" character are mutually
               exclusive in that they cannot be used in the same function
               call.  Notice how all of the "pre-programmed" cursor sizes in
               the example are grouped in the square brackets, but are also
               mutually exclusive.  Further, the "pre-programmed" sizes are
               exclusive from the programmable size specified in the
               [start,end] group.








                                      - xiii -
                                          
          Copyright (c) 1985-88 by Jason R. Matthews - All Rights Reserved
                                          

                                          
     PROCLIP2.LIB 2.00 User Documentation                 February 15, 1988
     ======================================================================



     
                                      BORDER
                                      ------
     
     
          Although syntactically supported in the SET COLOR TO... command,
          Clipper does not actually set the border color to the specified
          color.  BORDER provides this functionality to standard color (CGA)
          and the new VGA monitors.  EGA standards do not allow for border
          color support but some EGA's will support them.
     
          This function can either accept a standard Clipper color string or
          an individual color string to set the border color.
     
     
     Format:
     
               border(aColor)
     
     
     Parameters:
     
               aColor....Character string variable or constant, non case
                         sensitive, which contains the color to use when
                         setting the border.  Must be the alpha
                         representation of the color, the numeric will be
                         rejected.  If the string is a standard Clipper color
                         command (eg. 'W/N,N/W,R,,N/W') the function will
                         locate the border color within the string position
                         as specified in the Clipper documentation.
                         Otherwise the function assumed the color for the
                         border is the string (eg. 'r').
     
                                  (valid colors)
                         black                         N
                         blue                          B
                         green                         G
                         cyan                          BG
                         red                           R
                         magenta                       RB
                         brown                         GR
                         white                         W
     
     











                                       Page #1
                                          
          Copyright (c) 1985-88 by Jason R. Matthews - All Rights Reserved
                                          

                                          
     PROCLIP2.LIB 2.00 User Documentation                 February 15, 1988
     ======================================================================



     BORDER (cont'd)
     
     Examples:
     
               1.   Set the colors, including the border, to a nice shade of
                    blue.
     
                    .
                    .
                    .
                    aColor = '+gr/b,b/gr,b,,n/w'
                    set color to &aColor
                    border(aColor)
                    .
                    .
                    .
     
     2.          Set the border to red without affecting anything else.
     
                    .
                    .
                    .
                    border('r')
                    .
                    .
                    .
     
     
     Returns:
     
               Nothing.
     
     
     Cautions:
     
               None.
     


















                                       Page #2
                                          
          Copyright (c) 1985-88 by Jason R. Matthews - All Rights Reserved
                                          

                                          
     PROCLIP2.LIB 2.00 User Documentation                 February 15, 1988
     ======================================================================



     
                                     BOXCOLOR
                                     --------
     
     
          Changing the color attributes within a given area can be
          accomplished with NEWCOLOR, but BOXCOLOR will only change the color
          attribute of the border of the area.  With an optional parameter
          you can instruct the function to change the color of the first
          column and last column inside the area thereby showing a more
          appealing BOX.  Changing the background color with BOXCOLOR you can
          create your own "boxes" or even exploding and imploding emulation.
     
     
     Format:
     
               boxcolor(top,left,bottom,right,attr[,double][,type])
     
     
     Parameters:
     
               top.......Numeric variable or constant indicating the top row
                         of the area to be changed.  Value checked to be
                         between 0 and 24 inclusive.
               
               left......Numeric variable or constant indicating the left
                         column of the area to be changed.  Value checked to
                         be between 0 and 79 inclusive.
               
               bottom....Numeric variable or constant indicating the ending
                         row of the area to be changed.  Value checked to be
                         greater than TOP but less than or equal to 24.
               
               right.....Numeric variable or constant indicating the right
                         column of the area to be changed.  Value checked to
                         be greater than LEFT but less than or equal to 79.
               
               attr......Character string variable or constant, non case
                         sensitive, which contains a valid color command or
                         combination for character and background.  Must be
                         the alpha representation of the color, the numeric
                         will be rejected.













                                       Page #3
                                          
          Copyright (c) 1985-88 by Jason R. Matthews - All Rights Reserved
                                          

                                          
     PROCLIP2.LIB 2.00 User Documentation                 February 15, 1988
     ======================================================================



     BOXCOLOR (cont'd)
     
                                  (valid colors)
                         black                         N
                         blue                          B
                         green                         G
                         cyan                          BG
                         red                           R
                         magenta                       RB
                         brown                         GR
                         white                         W
                         intense                       +
                         blink                         *
     
               double....OPTIONAL.  Character string variable or constant,
                         non case sensitive, which instructs the function to
                         change the attribute of the first and last columns
                         within the area specified.  As columns are "slimmer"
                         than rows, changing these columns as well causes a
                         more appealing border.
     
                         'd'            This is the only valid parameter.
                                        Any other letter will be rejected as
                                        a bad parameter.
     
               type......OPTIONAL.  Logical variable or constant instructing
                         the function to use DMA updating or not.
     
                         .T.            DEFAULT.  If not specified, the
                                        function will use DMA screen
                                        updating.
               
                         .F.            Setting this flag to a logical false
                                        will cause the function to use the
                                        standard BIOS INT 10H for screen
                                        updating.
     
     
     Examples:
     
               1.   Change the color of the border of an area.
     
                    .
                    .
                    .
                    boxcolor(05,05,10,10,'n/w')
                    .
                    .
                    .
     





                                       Page #4
                                          
          Copyright (c) 1985-88 by Jason R. Matthews - All Rights Reserved
                                          

                                          
     PROCLIP2.LIB 2.00 User Documentation                 February 15, 1988
     ======================================================================



     BOXCOLOR (cont'd)
     
               1.   Change the color of the border of the same area, but use
                    double wide columns.
     
                    .
                    .
                    .
                    boxcolor(05,05,10,10,'n/w','d')
                    .
                    .
                    .
     
     
     Returns:
     
               Nothing.
     
     
     Cautions:
     
               None.

































                                       Page #5
                                          
          Copyright (c) 1985-88 by Jason R. Matthews - All Rights Reserved
                                          

                                          
     PROCLIP2.LIB 2.00 User Documentation                 February 15, 1988
     ======================================================================



     
                                      CLOCK
                                      ------
     
     
          Many programmers have wanted to display the current time on the
          screen from with Clipper, but due to the overhead involved in
          trying to keep it correct have dismissed the idea.  Now, with
          CLOCK, you simply specify the location, format and color attributes
          and PROCLIP2 will maintain the dynamic clock for you.  Formats
          include military (24 hour) or meridian (12 hour), with or without
          seconds displayed.  If no seconds are selected the colon between
          the hour and minutes will pulse every second re-enforcing the fact
          that it is keeping time.
     
     
     Format:
     
               clock('on' | 'off' [,format] [,seconds][,attr] )
     
     
     Parameters:
     
               'on'......Character string variable or constant, non case
                         sensitive, which instructs the CLOCK to become
                         active at the current cursor position.  Mutually
                         exclusive with the "off" parameter.
     
               'off'.....Character string variable or constant, non case
                         sensitive, which instructs the CLOCK to deactivate
                         itself.  The constant updating of the clock will
                         cease but the clock will remain on the display.
                         Mutually exclusive with the "on" parameter.
     
               attr......OPTIONAL.  Character string variable or constant,
                         non case sensitive, which informs the function what
                         color attributes to use when displaying.  If not
                         specified the function will use the attribute
                         currently displayed on the screen at the position
                         indicated.
     














                                       Page #6
                                          
          Copyright (c) 1985-88 by Jason R. Matthews - All Rights Reserved
                                          

                                          
     PROCLIP2.LIB 2.00 User Documentation                 February 15, 1988
     ======================================================================



     CLOCK (cont'd)
     
                                  (valid colors)
                         black                         N
                         blue                          B
                         green                         G
                         cyan                          BG
                         red                           R
                         magenta                       RB
                         brown                         GR
                         white                         W
                         intense                       +
                         blink                         *
     
               format....OPTIONAL.  Character string variable or constant,
                         non case sensitive, which informs the function of
                         the display format to use.
     
                         '12 hour'      DEFAULT.  Instructs the CLOCK
                                        function to display in standard 12
                                        hour format (eg. 10:00pm)
                         
                         '24 hour'      instructs the CLOCK function to
                                        display in military format (eg.
                                        22:00)
     
               seconds...OPTIONAL.  Character string variable or constant,
                         non case sensitive, which informs the function
                         whether to display the current seconds or not.
               
                         'seconds'      instructs the CLOCK function to
                                        display the seconds in the current
                                        format.
                         
                         'no seconds'   DEFAULT.  Instructs the CLOCK
                                        function to suppress display of the
                                        seconds and activate the pulse of the
                                        colon separator in hh:mm

















                                       Page #7
                                          
          Copyright (c) 1985-88 by Jason R. Matthews - All Rights Reserved
                                          

                                          
     PROCLIP2.LIB 2.00 User Documentation                 February 15, 1988
     ======================================================================



     CLOCK (cont'd)
     
     Examples:
     
               1.   At row #00 and column #00 display the clock in military
                    format with the seconds displayed using a white
                    background with black characters.
     
                    .
                    .
                    .
                    @ 0,0 say clock('on','24 hour','seconds','n/w')
                    .
                    .
                    .
     
               2.   Disable the clock.
     
                    .
                    .
                    .
                    clock('off')
                    .
                    .
                    .
     
     
     Returns:
     
               Nothing.
     
     
     Cautions:
     
               This function should not be placed into an overlay as it is
               interrupt driven.  Any error routines which determine an
               unrecoverable runtime error has occurred should disable this
               function prior to exiting the program.  Failure to follow this
               caution may result in the computer locking up.
















                                       Page #8
                                          
          Copyright (c) 1985-88 by Jason R. Matthews - All Rights Reserved
                                          

                                          
     PROCLIP2.LIB 2.00 User Documentation                 February 15, 1988
     ======================================================================



     
                                      CURSOR
                                      ------
     
     
          While Clipper contains a CURSOR command, it can't match the
          flexibility of this one.  CURSOR provides the programmer with full
          cursor shape control as well as information regarding the current
          cursor state.
     
          To use the "pre-programmed" mode, simply tell CURSOR what type of
          cursor you want.  Choices are 'off', 'std', 'half' and 'full' size.
          CURSOR will automatically adjust to different monitors so there is
          no need to remember starting and ending scan lines.
     
          For those programmers wishing even more control, CURSOR will accept
          starting and ending scan lines to adjust the cursor shape
          accordingly.  This is an excellent way to get that "special" cursor
          for your application.
     
          The last function contained in CURSOR is revealed when no
          parameters are used.  No parameters informs CURSOR that you want
          the current cursor state, on or off.  If the cursor is currently
          shown on the screen, regardless of shape, a logical true (.T.) will
          be returned, otherwise a logical false (.F.) will be.
     
     
     Format:
     
               cursor(['std' | 'off' | 'half' | 'full'] | [start,end])
     
     
     Parameters:
     
               'std'.....Character string variable or constant, non case
                         sensitive, instructing the function to set the
                         cursor to the default for the current monitor type.
     
               'off'.....Character string variable or constant, non case
                         sensitive, instructing the function to set the
                         cursor off.  The cursor will not show on the current
                         monitor.
     












                                       Page #9
                                          
          Copyright (c) 1985-88 by Jason R. Matthews - All Rights Reserved
                                          

                                          
     PROCLIP2.LIB 2.00 User Documentation                 February 15, 1988
     ======================================================================



     CURSOR (cont'd)
     
               'half'....Character string variable or constant, non case
                         sensitive, instructing the function to set the
                         cursor to one half of the total character size for
                         the current monitor type.
     
               'full'....Character string variable or constant, non case
                         sensitive, instructing the function to set the
                         cursor to cover the total character position for the
                         current monitor type.
     
               start.....Numeric variable or constant which will be used by
                         the function as the starting scan line.  Validity
                         determination is left up to the application program
                         in order to provide full flexibility.  Specifying
                         START assumes an END will be specified and is
                         mutually exclusive from the pre-programmed parameter
                         types.
     
               end.......Numeric variable or constant which will be used by
                         the function as the ending scan line.  Validity
                         determination is left up to the application program
                         in order to provide full flexibility.  Specifying
                         END assumes a START was specified and is mutually
                         exclusive from the pre-programmed parameter types.
     
               ()........If no parameters are given to the function, it will
                         return indicating whether the cursor is currently
                         displayed or not.
     
     
     Examples:
     
               1.   Set the cursor to one half of the current size and then
                    turn it off for some other activity.
     
                    .
                    .
                    .
                    cursor('half')
                    .
                    .
                    .
                    cursor('off')
                    .
                    .
                    .
     






                                      Page #10
                                          
          Copyright (c) 1985-88 by Jason R. Matthews - All Rights Reserved
                                          

                                          
     PROCLIP2.LIB 2.00 User Documentation                 February 15, 1988
     ======================================================================



     CURSOR (cont'd)
     
               2.   Change the cursor to a special shape.
     
                    .
                    .
                    .
                    cursor(2,7)
                    .
                    .
                    .
     
               3.   Determine if the cursor is currently displayed and turn
                    it off if it is.
     
                    .
                    .
                    .
                    if cursor()
                         cursor('off')
                    endif
                    .
                    .
                    .
     
     
     Returns:
     
               .T.  .....If no parameters were specified a return of a
                         logical true indicates that the cursor is currently
                         shown on the display.
               
               .F.  .....If no parameters were specified a return of a
                         logical false indicates that the cursor is not
                         currently shown on the display.
     
     
     Cautions:
     
               None.















                                      Page #11
                                          
          Copyright (c) 1985-88 by Jason R. Matthews - All Rights Reserved
                                          

                                          
     PROCLIP2.LIB 2.00 User Documentation                 February 15, 1988
     ======================================================================



     
                                     ERASTEXT
                                     --------
     
     
          If you've ever constructed a screen using the Clipper BOX command
          you know that it can be difficult to remember where the box border
          stops and your text begins, especially if you only want to erase a
          few lines of the text.  Generating FOR...NEXT loops to erase only
          that portion of an enclosed area is no fun.  Enter ERASTEXT, which
          will erase all standard ASCII characters (text & numbers) from
          within the requested area.  Simply specify the coordinates and
          "zap" all the text is gone.  Does not affect the attribute in use
          at the time.
     
     
     Format:
     
               erastext(top,left,bottom,right [,type])
     
     
     Parameters:
     
               top.......Numeric variable or constant indicating the top row
                         of the area to be changed.  Value checked to be
                         between 0 and 24 inclusive.
               
               left......Numeric variable or constant indicating the left
                         column of the area to be changed.  Value checked to
                         be between 0 and 79 inclusive.
               
               bottom....Numeric variable or constant indicating the ending
                         row of the area to be changed.  Value checked to be
                         greater than TOP but less than or equal to 24.
               
               right.....Numeric variable or constant indicating the right
                         column of the area to be changed.  Value checked to
                         be greater than LEFT but less than or equal to 79.
     
               type......OPTIONAL.  Logical variable or constant instructing
                         the function to use DMA updating or not.
     
                         .T.            DEFAULT.  If not specified, the
                                        function will use DMA screen
                                        updating.
               
                         .F.            Setting this flag to a logical false
                                        will cause the function to use the
                                        standard BIOS INT 10H for screen
                                        updating.
     




                                      Page #12
                                          
          Copyright (c) 1985-88 by Jason R. Matthews - All Rights Reserved
                                          

                                          
     PROCLIP2.LIB 2.00 User Documentation                 February 15, 1988
     ======================================================================



     ERASTEXT (cont'd)
     
     Examples:
     
               1.   Erase a video line without affecting the BOX borders
                    around the line.
     
                    .
                    .
                    .
                    @ 08,20,16,60 box '(special characters)'
                    @ 09,21 say (something useful)
                    @ 10,21 say (something useful)
                    @ 11,21 say (something useful)
                    @ 12,21 say (something useful)
                    @ 13,21 say (something useful)
                    .
                    .
                    .
                    erastext(11,20,13,60)
                    .
                    .
                    .
     
     
     Returns:
     
               Nothing.
     
     
     Cautions:
     
               None.






















                                      Page #13
                                          
          Copyright (c) 1985-88 by Jason R. Matthews - All Rights Reserved
                                          

                                          
     PROCLIP2.LIB 2.00 User Documentation                 February 15, 1988
     ======================================================================



     
                                     FILEATTR
                                     --------
     
     
          If you have clients who like to tinker too much, this function can
          be invaluable.  Employing this function properly it is now
          extremely easy to "lock" a file where the average user cannot
          inadvertently damage it.
          
          The FILEATTR function allows setting or resetting the directory
          attributes of a given file.  Attributes available are read-only,
          archive, hidden and system.  Prudent use of the read-only and/or
          hidden attribute can protect your databases from prying eyes.  To
          reaccess the database simply have your application remove the
          necessary flags prior to use, it's that easy.
     
     
     Format:
     
               fileattr(filename,fileattr)
     
     
     Parameters:
     
               filename..Character string variable or constant, non case
                         sensitive, which contains the filename whose
                         attributes you wish to change.  The filename should
                         follow the standard [drive:][\path\]filename format
                         where drive and path are optional.  Wildcards (* &
                         ?) are not allowed in the filename.
     
               fileattr..Character string variable or constant, non case
                         sensitive, which provides the function with a list
                         of all attributes to set or reset.
               
                         + (plus sign)  An attribute proceeded by a plus sign
                                        (+) instructs the function to set
                                        this flag in the directory entry for
                                        this file.
               
                         - (minus sign) An attribute proceeded by a minus
                                        sign (-) instructs the function to
                                        clear this flag in the directory
                                        entry for this file.
               









                                      Page #14
                                          
          Copyright (c) 1985-88 by Jason R. Matthews - All Rights Reserved
                                          

                                          
     PROCLIP2.LIB 2.00 User Documentation                 February 15, 1988
     ======================================================================



     FILEATTR (cont'd)
     
                         NOTE:          Although not advisable, it is
                                        possible to place an activate (+) and
                                        deactivate (-) for the same flag in
                                        the attribute string (eg. '+r/o -arc
                                        -r/o').  The last flag encountered in
                                        a left to right scan will be the
                                        action taken.  In this example the
                                        file would have the read-only and
                                        archive cleared (not set), the '+r/o'
                                        would have no effect.
     
                                  (valid file attributes)
     
                              r/o                 Read only
                              hid                 Hidden
                              sys                 System
                              arc                 Archive
     
     
     Examples:
     
               1.   Suppose you have "dangerous" clients who are constantly
                    fiddling with your files and inadvertently deleting them
                    from time to time.  In order to prevent this your
                    application could set the "read-only" attribute prior to
                    terminating.  To access the files again the application
                    could reset the "read-only" attribute when starting up.
     
                    (program start)
                    .
                    .
                    fileattr('CLIENT.DBF','-r/o')
                    .
                    (program executes)
                    .
                    fileattr('CLIENT.DBF','+r/o')
                    .
                    .
                    (program ends)
     













                                      Page #15
                                          
          Copyright (c) 1985-88 by Jason R. Matthews - All Rights Reserved
                                          

                                          
     PROCLIP2.LIB 2.00 User Documentation                 February 15, 1988
     ======================================================================



     FILEATTR (cont'd)
     
               1.   Combined with the DIR function, do the above example
                    through all existing files in the subdirectory.
     
                    (program starts)
                    .
                    .
                    filename = DIR('*.*','first')
                    do while .not. empty(filename)
                         fileattr(filename,'-r/o')
                         filename = DIR('next')
                    enddo
                    .
                    (program executes)
                    .
                    filename = DIR('*.*','first')
                    do while .not. empty(filename)
                         fileattr(filename,'+r/o')
                         filename = DIR('next')
                    enddo
                    .
                    (program ends)
     
     
     Returns:
     
               .T.  .....Logical true (.T.) to indicate success of function.
                         Setting or resetting attributes which have already
                         been set or reset will still return a success flag.
     
               .F.  .....Logical false (.F.) to indicate failure of the
                         function.
     
     
     Cautions:
     
               In order to assume proper operation, all files should be
               closed which may be accessed by the function.
















                                      Page #16
                                          
          Copyright (c) 1985-88 by Jason R. Matthews - All Rights Reserved
                                          

                                          
     PROCLIP2.LIB 2.00 User Documentation                 February 15, 1988
     ======================================================================



     
                                     GETCOLOR
                                     --------
     
     
          GETCOLOR goes to the screen location specified in the parameters
          and obtains the current color attribute.  This attribute is then
          returned to your program in the form of a standard Clipper
          character string compatible with the SET COLOR TO format (eg.
          '+gr/b').  The function may optionally "flip" the color attribute
          in that the returned string will be the exact inverse of what is
          actually there (eg. '+b/gr').
     
     
     Format:
     
               <memvar> = getcolor(row, col [,flip])
     
     
     Parameters:
     
               row.......Numeric variable or constant which, when combined
                         with COL, informs the function of the screen
                         location from which to obtain the current color.
     
               col.......Numeric variable or constant which, when combined
                         with ROW, informs the function of the screen
                         location from which to obtain the current color.
     
               flip......OPTIONAL.  Logical variable or constant which
                         instructs the function as to whether to invert the
                         color attribute before returning it
               
                         .T.            Force the attribute to invert (flip)
                                        itself.  For example, a color of
                                        '+w/b' would be flipped to be '+b/w'.
               
                         .F.            DEFAULT.  Do not flip the color
                                        attribute, return it as it actually
                                        is.















                                      Page #17
                                          
          Copyright (c) 1985-88 by Jason R. Matthews - All Rights Reserved
                                          

                                          
     PROCLIP2.LIB 2.00 User Documentation                 February 15, 1988
     ======================================================================



     GETCOLOR (cont'd)
     
     Examples:
     
               1.   After your application program loads you wish to obtain
                    the current screen color so it may be restored before
                    your application completes.  (The color of the screen
                    BEFORE your program invoked it's colors was bright yellow
                    text on a blue background)
     
                    doscolor = getcolor(0,0)
                    * now doscolor = '+gr/b'
                    .
                    .
                    set color to &mycolors
                    clear
                    .
                    .
                    (application program)
                    .
                    .
                    set color to &doscolor
                    quit
     
     
     Returns:
     
               memvar....A character string variable which will contain a
                         text description of the current color at the
                         position selected.  If nothing is returned an error
                         was detected in your screen coordinates.  The valid
                         range is (0,0) thru (24,79).
     
     
                          (Possible Return Color Values)
                         black                         n
                         blue                          b
                         green                         g
                         cyan                          bg
                         red                           r
                         magenta                       rb
                         brown                         gr
                         white                         w
                         intense                       +
                         blink                         *
     
     
     Cautions:
     
               None.





                                      Page #18
                                          
          Copyright (c) 1985-88 by Jason R. Matthews - All Rights Reserved
                                          

                                          
     PROCLIP2.LIB 2.00 User Documentation                 February 15, 1988
     ======================================================================



     
                                      ISCGA
                                      -----
     
     
          Determines if the current screen is driven by a Color Graphics
          Adapter (CGA).  Adapters which are supersets of the CGA standard
          should be tested for EGA or VGA compatibility first.  An EGA or VGA
          emulating a CGA will not return indicating a CGA is attached.
          Returns a logical true (.T.) or false (.F.) indicator.
     
     
     Format:
     
               iscga()
     
     
     Parameters:
     
               None.
     
     
     Examples:
     
               1.   Determine if the current monitor is standard CGA.
     
                    .
                    .
                    .
                    if iscga()
                         (do color stuff)
                    endif
                    .
                    .
                    .
     
     
     Returns:
     
               .T.  .....Indicates that the current screen is a CGA type.
               
               .F.  .....Indicates that the current screen is not a CGA type.
     
     
     Cautions:
     
               None.








                                      Page #19
                                          
          Copyright (c) 1985-88 by Jason R. Matthews - All Rights Reserved
                                          

                                          
     PROCLIP2.LIB 2.00 User Documentation                 February 15, 1988
     ======================================================================



     
                                      ISEGA
                                      -----
     
     
          Determines if the current screen is driven by an Enhanced Color
          Graphics Adapter (EGA).  Adapters which are supersets of the EGA
          standard should be tested for VGA compatibility first.  A VGA
          emulating an EGA will not return indicating an EGA is attached.
          Returns a logical true (.T.) or false (.F.) indicator.
     
     
     Format:
     
               isega()
     
     
     Parameters:
     
               None.
     
     
     Examples:
     
               1.   Determine if the current monitor is an EGA.
     
                    .
                    .
                    .
                    if isega()
                         (do fancy stuff)
                    endif
                    .
                    .
                    .
     
     
     Returns:
     
               .T.  .....Indicates that the current screen is an EGA type.
               
               .F.  .....Indicates that the current screen is not an EGA
                         type.
     
     
     Cautions:
     
               None.







                                      Page #20
                                          
          Copyright (c) 1985-88 by Jason R. Matthews - All Rights Reserved
                                          

                                          
     PROCLIP2.LIB 2.00 User Documentation                 February 15, 1988
     ======================================================================



     
                                      ISMONO
                                      ------
     
     
          Determines if the current screen is a monochrome or fully
          monochrome compatible monitor.  A VGA emulating a monochrome
          monitor will not return indicating a monochrome is attached.
          Returns a logical true (.T.) or false (.F.) indicator.
     
     
     Format:
     
               ismono()
     
     
     Parameters:
     
               None.
     
     
     Examples:
     
               1.   Determine if the current monitor is monochrome.
     
                    .
                    .
                    .
                    if ismono()
                         (do monochrome stuff)
                    endif
                    .
                    .
                    .
     
     
     Returns:
     
               .T.  .....Indicates that the current screen is a monochrome
                         type.
               
               .F.  .....Indicates that the current screen is not a
                         monochrome type.
     
     
     Cautions:
     
               None.







                                      Page #21
                                          
          Copyright (c) 1985-88 by Jason R. Matthews - All Rights Reserved
                                          

                                          
     PROCLIP2.LIB 2.00 User Documentation                 February 15, 1988
     ======================================================================



     
                                      ISVGA
                                      -----
     
     
          Determines if the current screen is driven by a Video Graphics
          Array Adapter (VGA) or 100% compatible.  Returns a logical true
          (.T.) or false (.F.) indicator.
     
     
     Format:
     
               isvga()
     
     
     Parameters:
     
               None.
     
     
     Examples:
     
               1.   Determine if the current monitor is a VGA.
     
                    .
                    .
                    .
                    if isvga()
                         (do real pretty and fancy stuff)
                    endif
                    .
                    .
                    .
     
     
     Returns:
     
               .T.  .....Indicates that the current screen is a VGA type.
               
               .F.  .....Indicates that the current screen is not a VGA type.
     
     
     Cautions:
     
               None.










                                      Page #22
                                          
          Copyright (c) 1985-88 by Jason R. Matthews - All Rights Reserved
                                          

                                          
     PROCLIP2.LIB 2.00 User Documentation                 February 15, 1988
     ======================================================================



     
                                     NEWCOLOR
                                     --------
     
     
          Changing colors on entire areas of the screen, regardless of the
          current screen contents, can now be managed very effectively and
          efficiently with NEWCOLOR.
          
          The NEWCOLOR function provides the programmer with the ability to
          change colors on the screen without having to reset the color and
          rewrite the screen information.  This is particularly useful in
          those occasions when a highlighting of information is necessary
          which would normally be prohibitive due to slow screen update
          characteristics.  Self programmed light bar menus and highlighting
          screen selections becomes much easier with this function employed.
     
     
     Format:
     
               newcolor(top, left, bottom, right, attr [,type])
     
     
     Parameters:
     
               top.......Numeric variable or constant indicating the top row
                         of the area to be changed.  Value checked to be
                         between 0 and 24 inclusive.
               
               left......Numeric variable or constant indicating the left
                         column of the area to be changed.  Value checked to
                         be between 0 and 79 inclusive.
               
               bottom....Numeric variable or constant indicating the ending
                         row of the area to be changed.  Value checked to be
                         greater than TOP but less than or equal to 24.
               
               right.....Numeric variable or constant indicating the right
                         column of the area to be changed.  Value checked to
                         be greater than LEFT but less than or equal to 79.
               
               attr......Character string variable or constant, non case
                         sensitive, valid color command or combination for
                         character and background.  Must be the alpha
                         representation of the color, the numeric will be
                         rejected.
     








                                      Page #23
                                          
          Copyright (c) 1985-88 by Jason R. Matthews - All Rights Reserved
                                          

                                          
     PROCLIP2.LIB 2.00 User Documentation                 February 15, 1988
     ======================================================================



     NEWCOLOR (cont'd)
     
                                  (valid colors)
                         black                         N
                         blue                          B
                         green                         G
                         cyan                          BG
                         red                           R
                         magenta                       RB
                         brown                         GR
                         white                         W
                         intense                       +
                         blink                         *
     
               type......OPTIONAL.  Logical variable or constant instructing
                         the function to use DMA updating or not.
     
                         .T.            DEFAULT.  If not specified, the
                                        function will use DMA screen
                                        updating.
               
                         .F.            Setting this flag to a logical false
                                        will cause the function to use the
                                        standard BIOS INT 10H for screen
                                        updating.
     
     
     Examples:
     
               1.   This will change the character attributes from row #10,
                    column #20 through row #12, column #60 to intense
                    blinking red (*+r) on a black background (n).
     
                    .
                    .
                    .
                    newcolor(10,20,12,60,'*+r/n)
                    .
                    .
                    .
     














                                      Page #24
                                          
          Copyright (c) 1985-88 by Jason R. Matthews - All Rights Reserved
                                          

                                          
     PROCLIP2.LIB 2.00 User Documentation                 February 15, 1988
     ======================================================================



     NEWCOLOR (cont'd)
     
               2.   This will change the character attributes from row #05,
                    column #10 through row #05, column #15 to inverse white
                    (w) with black characters (n).
     
                    .
                    .
                    .
                    newcolor(5,10,5,15,'n/w')
                    .
                    .
                    .
     
     
     Returns:
     
               Nothing.
     
     
     Cautions:
     
               None.
































                                      Page #25
                                          
          Copyright (c) 1985-88 by Jason R. Matthews - All Rights Reserved
                                          

                                          
     PROCLIP2.LIB 2.00 User Documentation                 February 15, 1988
     ======================================================================



     
                                      PRTSC
                                      -----
     
     
          Many times users of your applications have simply wanted a print
          screen of what they see.  In order to accommodate them you usually
          need to write a routine will recreates the information on the
          printer.  With PRTSC this is no longer necessary.
          
          The PRTSC function actually contains two separate functions.  The
          first function is a command driven print screen.  Embedded in your
          source code, the PRTSC command will cause a print screen to happen
          just as if the SHIFT PRTSC keys were pressed.
          
          The second function of PRTSC is that of a translator.  With the use
          of the BOX command many screens have become "unprintable" by usual
          standards.  Doing a print screen causes strange characters or
          control codes to be sent to the printer.  The PRTSC function has
          the ability to intercept those "unprintable" characters and
          translate them into simple, unoffensive periods (.).  The basic
          design of your screen is intact but without lots of programming
          effort.
     
     
     Format:
     
               prtsc(['xlat' | 'off'])
     
     
     Parameters:
     
               ()........If no parameters are specified, instructs the
                         function to perform an immediate print screen.  If
                         the translate facility has been activated then the
                         function will perform the print screen translation,
                         otherwise the standard BIOS interrupt perform as
                         usual.
     
               'xlat'....Character string variable or constant, non case
                         sensitive, which instructs the function to begin
                         translation of all print screen activity.  If a
                         print screen is invoked, either from PRTSC() or from
                         the keyboard, all characters will be translated
                         which do not fall into the following range: ASCII 32
                         to 127 (" " to "~").  The characters are translated
                         into a period (.).
     







                                      Page #26
                                          
          Copyright (c) 1985-88 by Jason R. Matthews - All Rights Reserved
                                          

                                          
     PROCLIP2.LIB 2.00 User Documentation                 February 15, 1988
     ======================================================================



     PRTSC (cont'd)
     
               'off'.....Character string variable or constant, non case
                         sensitive, which instructs the function to terminate
                         translation of all print screen activity.  Control
                         is returned to the BIOS for print screen requests.
     
     
     Examples:
     
               1.   A user wishes a snapshot of the currently displayed
                    record.  Rather than writing a report routine, a print
                    screen is invoked but, as the screen contains graphical
                    box characters, a translation is first required.
     
                    .
                    .
                    .
                    prtsc('xlat')
                    prtsc()
                    prtsc('off')
                    .
                    .
                    .
     
               2.   Thinking ahead, the programmer has determined during
                    installation that the user's printer cannot print the
                    graphical box characters used on the display screen.  The
                    translate facility has been activated and when the user
                    performs a manual print screen the translation is still
                    effective.
     
                    .
                    .
                    prtsc('xlat')
                    .
                    .
                    (user presses Shift PrtSc)
                    .
                    .
                    prtsc('off')
                    (end of program)
     
     











                                      Page #27
                                          
          Copyright (c) 1985-88 by Jason R. Matthews - All Rights Reserved
                                          

                                          
     PROCLIP2.LIB 2.00 User Documentation                 February 15, 1988
     ======================================================================



     PRTSC (cont'd)
     
     Returns:
     
               Nothing.
     
     
     Cautions:
     
               This function should not be placed into an overlay as it is
               interrupt driven.  Any error routines which determine an
               unrecoverable runtime error has occurred should disable this
               function prior to exiting the program.  Failure to follow this
               caution may result in the computer locking up.









































                                      Page #28
                                          
          Copyright (c) 1985-88 by Jason R. Matthews - All Rights Reserved
                                          

                                          
     PROCLIP2.LIB 2.00 User Documentation                 February 15, 1988
     ======================================================================



     
                                      RESET
                                      -----
     
     
          The ultimate in password protection, and possibly frustrating
          enough to prevent future attempts is a complete reset of the
          computer.  The RESET function provides an instantaneous reset of
          the computer.  The reset may either be a software reset or a full
          hardware reset.
     
     
     Format:
     
               reset([.T. | .F.])
     
     
     Parameters:
     
               .T.  .....Logical variable or constant which instructs the
                         function to perform a full hardware reset of the
                         computer.  A hardware reset is defined as a reset
                         which causes all hardware interrupts to be halted
                         and restarted by the regular BIOS routines.
                         Hardware reset may not prove functional on non-100%
                         compatible BIOS computers.  Hardware reset invokes
                         all BIOS manufacturer tests (i.e. RAM test).
     
               .F.  .....DEFAULT.  Logical variable or constant which
                         instructs the function to perform a standard
                         software reset.  This reset is similar in nature to
                         the CTRL ALT DEL key sequence.  If no parameter is
                         given to RESET then .F. is assumed.
     
     
     Examples:
     
               1.   Perform a hardware reset of the computer.
     
                    .
                    .
                    .
                    reset(.t.)
                    .
                    .
                    .
     








                                      Page #29
                                          
          Copyright (c) 1985-88 by Jason R. Matthews - All Rights Reserved
                                          

                                          
     PROCLIP2.LIB 2.00 User Documentation                 February 15, 1988
     ======================================================================



     RESET (cont'd)
     
               2.   Perform a software reset of the computer.
     
                    .
                    .
                    .
                    reset()
                    .
                    .
                    .
     
     
     Returns:
     
               Nothing.
     
     
     Cautions:
     
               This function will immediately halt all operation in the
               computer.  Due to this it is strongly suggested that no files
               or background operations (print queues) be active when RESET
               is invoked.































                                      Page #30
                                          
          Copyright (c) 1985-88 by Jason R. Matthews - All Rights Reserved
                                          

                                          
     PROCLIP2.LIB 2.00 User Documentation                 February 15, 1988
     ======================================================================



     
                                     RESTBOX
                                     -------
     
     
          Possibly one of the most flexible functions in PROCLIP2, the
          RESTBOX function is the companion to SAVEBOX.  Once a section of
          the screen has been placed into a memory variable by SAVEBOX, the
          RESTBOX function may be used to restore it.
          
          RESTBOX "knows" where the screen portion originally came from, so
          remembering the coordinates is no longer a necessity.  It is
          possible, however, to override those original coordinates and
          reposition the screen portion anywhere on the screen.  You may also
          use either the original colors, as it was saved, or override them
          with a new color attribute.
          
          Through creative use of SAVEBOX, RESTBOX and the standard Clipper
          BOX command an impressive control of the screen may be obtained.
          
          RESTBOX is not compatible with memory variables saved by the
          Clipper SAVESCREEN function.
     
     
     Format:
     
               restbox([top, left,] scrnarea [,attr][,type])
     
     
     Parameters:
     
               top.......OPTIONAL.  Numeric variable or constant indicating
                         the top row of where the SAVEBOX'd area is to be
                         restored.  Value checked to be between 0 and 24
                         inclusive.  If TOP is specified then LEFT must also
                         be specified.  If TOP,LEFT is not specified RESTBOX
                         will obtain the original position from within the
                         SAVEBOX'd variable.
               
               left......OPTIONAL.  Numeric variable or constant indicating
                         the left column of where the SAVEBOX'd area is to be
                         restored.  Value checked to be between 0 and 79
                         inclusive.  If LEFT is specified then TOP must also
                         be specified.
               
               scrnarea..Character string variable containing a saved portion
                         of the screen which was saved with SAVEBOX.  No
                         changes to this memory variable should have occurred
                         between the SAVEBOX command and RESTBOX.  Cannot be
                         a memory variable saved by the Clipper SAVESCREEN
                         function.




                                      Page #31
                                          
          Copyright (c) 1985-88 by Jason R. Matthews - All Rights Reserved
                                          

                                          
     PROCLIP2.LIB 2.00 User Documentation                 February 15, 1988
     ======================================================================



     RESTBOX (cont'd)
     
               attr......OPTIONAL.  Character string variable or constant,
                         non case sensitive, which contains a valid color
                         combination for character and background.  This
                         color attribute will be used during the restore to
                         the screen but the original image as saved by
                         SAVEBOX will not be modified.  Must be the alpha
                         representation of the color, the numeric will be
                         rejected.
     
                                  (valid colors)
                         black                         N
                         blue                          B
                         green                         G
                         cyan                          BG
                         red                           R
                         magenta                       RB
                         brown                         GR
                         white                         W
                         intense                       +
                         blink                         *
     
               type......OPTIONAL.  Logical variable or constant instructing
                         the function to use DMA updating or not.  As this is
                         an optional parameter the function will assume you
                         wish IBM standard BIOS INT 10H updating.
               
                         .T.            DEFAULT.  If not specified, the
                                        function will use DMA screen
                                        updating.
               
                         .F.            Setting this flag to a logical false
                                        will cause the function to use the
                                        standard BIOS INT 10H for screen
                                        updating.
     
     
     Examples:
     
               1.   This will restore a previously saved screen area to the
                    original location but use a different color attribute.
     
                    .
                    .
                    .
                    restbox(scrn1,'+r/n')
                    .
                    .
                    .
     




                                      Page #32
                                          
          Copyright (c) 1985-88 by Jason R. Matthews - All Rights Reserved
                                          

                                          
     PROCLIP2.LIB 2.00 User Documentation                 February 15, 1988
     ======================================================================



     RESTBOX (cont'd)
     
               2.   This will restore a previously saved screen area to row
                    #10, column #20 even if this is a different location than
                    it was originally obtained from.
     
                    .
                    .
                    .
                    restbox(10,20,scrn1)
                    .
                    .
                    .
     
               3.   A typical SAVEBOX and RESTBOX combination.
     
                    .
                    .
                    .
                    scrn1 = savebox(10,20,12,60)
                    .
                    .
                    .
                    restbox(scrn1)
                    .
                    .
                    .
     
     
     Returns:
     
               Nothing.
     
     
     Cautions:
     
               None.


















                                      Page #33
                                          
          Copyright (c) 1985-88 by Jason R. Matthews - All Rights Reserved
                                          

                                          
     PROCLIP2.LIB 2.00 User Documentation                 February 15, 1988
     ======================================================================



     
                                     RESTCURS
                                     --------
     
     
          The companion function to SAVECURS, the RESTCURS function will
          restore the cursor to it's original shape and position as specified
          in the memory variable.  Great for restoring the look of a given
          screen without having to remember where everything was.
     
     
     Format:
     
               restcurs(<memvar>)
     
     
     Parameters:
     
               <memvar>..A numeric memory variable which was created through
                         SAVECURS and contains the cursor shape and position
                         to restore.
     
     
     Examples:
     
               See SAVECURS.
     
     
     Returns:
     
               Nothing.
     
     
     Cautions:
     
               See SAVECURS.



















                                      Page #34
                                          
          Copyright (c) 1985-88 by Jason R. Matthews - All Rights Reserved
                                          

                                          
     PROCLIP2.LIB 2.00 User Documentation                 February 15, 1988
     ======================================================================



     
                                     SAVEBOX
                                     -------
     
     
          The SAVEBOX function provides the programmer with a method of
          saving partial screen images into character memory variables and,
          using the RESTBOX function, restore them back when needed.
          
          SAVEBOX will allow the programmer to save any area of the screen
          which contains at least one (1) character and up to the entire
          screen (4000 bytes).  This allows multiple "snapshots" of various
          area of the screen using the minimum amount of memory necessary.
          
          As a temporary storage buffer is required for the screen area
          during the snapshot, this function temporarily allocates memory
          from DOS.  If insufficient memory is available the function will
          refuse to perform and none of the screen area will be saved.  It is
          very unlikely that this could happen as even the entire screen
          requires less than 4Kb for temporary storage.
     
     
     Format:
     
               <memvar> = savebox(top, left, bottom, right [,type])
     
     
     Parameters:
     
               top.......Numeric variable or constant indicating the top row
                         of the area to be saved.  Value checked to be
                         between 0 and 24 inclusive.
               
               left......Numeric variable or constant indicating the left
                         column of the area to be saved.  Value checked to be
                         between 0 and 79 inclusive.
               
               bottom....Numeric variable or constant indicating the ending
                         row of the area to be saved.  Value checked to be
                         greater than TOP but less than or equal to 24.
               
               right.....Numeric variable or constant indicating the right
                         column of the area to be changed.  Value checked to
                         be greater than LEFT but less than or equal to 79.
               










                                      Page #35
                                          
          Copyright (c) 1985-88 by Jason R. Matthews - All Rights Reserved
                                          

                                          
     PROCLIP2.LIB 2.00 User Documentation                 February 15, 1988
     ======================================================================



     SAVEBOX (cont'd)
     
               type......OPTIONAL.  Logical variable or constant instructing
                         the function to use DMA updating or not.
               
                         .T.            DEFAULT.  If not specified, the
                                        function will use DMA screen
                                        updating.
               
                         .F.            Setting this flag to a logical false
                                        will cause the function to use the
                                        standard BIOS INT 10H for screen
                                        updating.
     
     
     Examples:
     
               1.   To save the screen data, and attributes, into a memory
                    variable from row #10, column #20 through row #12, column
                    #60.
     
                    .
                    .
                    .
                    scrnarea = savebox(10,20,12,60)
                    .
                    .
                    .
     
     
     Returns:
     
               <memvar>..A character string variable which contains the data
                         as it was read from the screen preceded by four (4)
                         bytes of control information.
     
     
     Cautions:
     
               Do not modify the contents of the memory variable after it is
               returned from SAVEBOX.  The results may not be as you desire.














                                      Page #36
                                          
          Copyright (c) 1985-88 by Jason R. Matthews - All Rights Reserved
                                          

                                          
     PROCLIP2.LIB 2.00 User Documentation                 February 15, 1988
     ======================================================================



     
                                     SAVECURS
                                     --------
     
     
          SAVECURS provides the programmer with the ability to save the
          current cursor shape and position on the video screen.  This is
          extremely useful when using any type of on-line help system or
          other functions which temporarily occupy the screen and you'd like
          the cursor to return where it was when completed.  See RESTCURS.
     
     
     Format:
     
               <memvar> = savecurs()
     
     
     Parameters:
     
               None.
     
     
     Examples:
     
               1.   Save the current cursor shape and position while invoking
                    a subfunction.
     
                    .
                    .
                    .
                    aCursor = savecurs()
                    .
                    (do a sub function)
                    .
                    restcurs(aCursor)
                    .
                    .
                    .
     
     















                                      Page #37
                                          
          Copyright (c) 1985-88 by Jason R. Matthews - All Rights Reserved
                                          

                                          
     PROCLIP2.LIB 2.00 User Documentation                 February 15, 1988
     ======================================================================



     SAVECURS (cont'd)
     
     Returns:
     
               <memvar>..a numeric variable which will contain the cursor
                         shape and position on the screen.  These values are
                         embedded in this variable and the variable will
                         return a zero (0) value if accessed from Clipper.
     
     
     Cautions:
     
               In order to properly restore the cursor care should be taken
               not to use the numeric variable in any other fashion.









































                                      Page #38
                                          
          Copyright (c) 1985-88 by Jason R. Matthews - All Rights Reserved
                                          

                                          
     PROCLIP2.LIB 2.00 User Documentation                 February 15, 1988
     ======================================================================



     
                                       SDIR
                                       ----
     
     
          Similar to the standard Clipper ADIR command, the SDIR command
          provides the programmer with the ability to read any valid
          directory and obtain standard directory information on an entry by
          entry basis.  Entries include all valid directory entries including
          subdirectory and volume label names.  Using the attribute filter,
          the SDIR function will only return those files matching the
          attributes.  SDIR will return the entry name, date, time or file
          size depending upon the function call used.
     
     
     Format:
     
               <memvar> = SDIR(pattern, 'first' [,fileattr])
               <memvar> = SDIR('next')
               <memvar> = SDIR('date')
               <memvar> = SDIR('time')
               <memvar> = SDIR('size')
               <memvar> = SDIR(pattern, 'count' [,fileattr])
     
     
     Parameters:
     
               pattern...Character string variable or constant, non case
                         sensitive, which informs the function of the entry
                         pattern to search with.  The PATTERN may contain any
                         valid drive or DOS path as well as wildcards (eg.
                         "*" & "?").
     
               'first'...Character string variable or constant, non case
                         sensitive, which instructs the function to obtain
                         the first matching directory entry in the specified
                         directory.  If FIRST is specified then a PATTERN
                         must be supplied.  FIRST reinitializes the search
                         function and sets up the function for subsequent
                         activity based on the PATTERN provided.
     














                                      Page #39
                                          
          Copyright (c) 1985-88 by Jason R. Matthews - All Rights Reserved
                                          

                                          
     PROCLIP2.LIB 2.00 User Documentation                 February 15, 1988
     ======================================================================



     SDIR (cont'd)
     
               'next'....Character string variable or constant, non case
                         sensitive, which instructs the function to obtain
                         the next matching entry based on the last FIRST
                         function.  In other words, a FIRST must be called
                         first in order to obtain the first entry and
                         initialize the function.  Subsequent NEXT functions
                         will continue reading the directory one entry at a
                         time until all entries have been read.
     
               'date'....Character string variable or constant, non case
                         sensitive, which instructs the function to obtain
                         the date of the last entry returned with either
                         FIRST or NEXT, whichever was last.  If the file is
                         currently open (as in an active database file) this
                         date may not reflect the actual last update date.
                         In these cases the active file should be closed to
                         allow the operating system to update the directory
                         prior to requesting this function.
     
               'time'....Character string variable or constant, non case
                         sensitive, which instructs the function to obtain
                         the time of the last entry returned with either
                         FIRST or NEXT, whichever was last.  As in DATE the
                         file should be closed prior to requesting this
                         function.
     
               'size'....Character string variable or constant, non case
                         sensitive, which instructs the function to obtain
                         the size of the last entry returned with either
                         FIRST or NEXT, whichever was last.  As in TIME and
                         DATE above the file should be closed prior to
                         requesting this function.
     
               'count'...Character string variable or constant, non case
                         sensitive, which instructs the function to obtain
                         the number of files matching PATTERN.  If COUNT is
                         specified then PATTERN must also be specified.
     















                                      Page #40
                                          
          Copyright (c) 1985-88 by Jason R. Matthews - All Rights Reserved
                                          

                                          
     PROCLIP2.LIB 2.00 User Documentation                 February 15, 1988
     ======================================================================



     SDIR (cont'd)
     
               fileattr..Character string variable or constant, non case
                         sensitive, which instructs the function to only
                         select those directory entries which have at least
                         these attributes.
     
                                  (valid file attributes)
               
                              r/o                 Read only
                              hid                 Hidden
                              sys                 System
                              vol                 Volume label
                              sub                 Subdirectory
                              arc                 Archive
     
     
     Examples:
     
               1.   Read the current directory and when the chosen file is
                    found obtain the date, time and size of the file.  As no
                    attribute is specified all directory entries will be
                    returned which match the pattern and have at least the
                    archive attribute set (arc).
     
                    .
                    .
                    .
                    pattern = 'YOUR????.DBF'
                    filename = sdir(pattern,'first')
                    if .not. empty(filename)
                         filedate = sdir('date')
                         filetime = sdir('time')
                         filesize = sdir('size')
                    endif
                    .
                    .
                    .
     
















                                      Page #41
                                          
          Copyright (c) 1985-88 by Jason R. Matthews - All Rights Reserved
                                          

                                          
     PROCLIP2.LIB 2.00 User Documentation                 February 15, 1988
     ======================================================================



     SDIR (cont'd)
     
               1.   Read a different, valid, directory and return all of the
                    names of all subdirectory entries by specifying an
                    attribute of subdirectory only.
     
                    .
                    .
                    .
                    aSubDir = sdir('C:\LEVEL1\LEVEL2\*.*','first','sub')
                    do while .not. empty(aSubDir)
                         ? direntry
                         aSubDir = sdir('next')
                    enddo
                    .
                    .
                    .
     
     
     Returns:
     
               'first'...If successful, <memvar> is set to a character string
                         type and returned with the filename of the first
                         file matching PATTERN.  If unsuccessful, <memvar> is
                         set to a character string type and returned with a
                         zero length (null).
     
               'next'....Same as FIRST.
     
               'date'....If successful, <memvar> is set to a date type and
                         returned with the entry date per the active
                         directory entry.  If unsuccessful, <memvar> is set
                         to a date type and returned with a '00/00/00' date.
     
               'time'....If successful, <memvar> is set to a character type
                         and returned with the entry time per the active
                         directory entry in HH:MM:SS format.  If
                         unsuccessful, <memvar> is set to a character type
                         and returned with a zero length (null).
     
               'size'....If successful, <memvar> is set to a numeric type and
                         returned with the file size (subdirectory entries
                         are always zero (0) length) per the active directory
                         entry.  If unsuccessful, <memvar> is set to a
                         numeric type and returned with a zero value (0).
     









                                      Page #42
                                          
          Copyright (c) 1985-88 by Jason R. Matthews - All Rights Reserved
                                          

                                          
     PROCLIP2.LIB 2.00 User Documentation                 February 15, 1988
     ======================================================================



     SDIR (cont'd)
     
               'count'...If successful, <memvar> is set to a numeric type and
                         returned with the number of entries matching the
                         specified pattern.  If unsuccessful, <memvar> is set
                         to a numeric type and returned with a zero value
                         (0).
     
     
     Cautions:
     
               None.











































                                      Page #43
                                          
          Copyright (c) 1985-88 by Jason R. Matthews - All Rights Reserved
                                          

                                          
     PROCLIP2.LIB 2.00 User Documentation                 February 15, 1988
     ======================================================================



     
                                      SOUND
                                      -----
     
          Similar in general concept to the Clipper TONE() command, SOUND()
          provides the programmer with the added flexibility of creating
          sounds for a shorter duration of time.  The Clipper TONE() command
          is driven off the internal timer of the computer which "pulses"
          18.2 times per second.  Due to this the TONE() command has a
          "resolution" of 1/18th of a second in that it cannot generate a
          tone for a shorter duration of time.  With SOUND() it is possible
          to create a sound for as little as 1/100th of a second.  Although
          1/100th of a second is the same from computer to computer, software
          can have difficultly calculating what 1/100th of a second is due to
          timing differences between computers.  SOUND() does not have this
          problem as it automatically calculates the exact timing necessary
          for 1/100th of a second to pass, regardless of CPU speed.
     
     
     Format:
     
               sound(tone, duration [,type])
     
     
     Parameters:
     
               tone......Numeric variable or constant which informs the
                         function of the frequency you wish to use.  The
                         frequency is the number of Hertz (cycles per
                         second).  The higher the frequency the higher the
                         tone, the lower the frequency the lower the tone.
                         Allowable range for this parameter is 37 through
                         32767.
     
               duration..Numeric variable or constant which informs the
                         function of the duration to use.  The duration is
                         the amount of time the speaker will generate the
                         tone before shutting off.  As two duration
                         resolutions are available (timer and internal), this
                         value will have different meanings.  See the "type"
                         description below.














                                      Page #44
                                          
          Copyright (c) 1985-88 by Jason R. Matthews - All Rights Reserved
                                          

                                          
     PROCLIP2.LIB 2.00 User Documentation                 February 15, 1988
     ======================================================================



     SOUND (cont'd)
     
               type......OPTIONAL.  Logical variable or constant which
                         informs the function as to the type of duration to
                         use.
               
                         .T.            DEFAULT.  Instructs the function to
                                        use timer ticks as the duration
                                        count.  A duration of 5 would last
                                        for 5 timer ticks or 5/18ths of a
                                        second.  Resolution range in this
                                        mode is 1/18th of a second to 3,640
                                        seconds (approx 1 hour).
               
                         .F.            Instructs the function to use
                                        1/100ths as the duration count.  A
                                        duration of 5 would last for 5/100ths
                                        (1/20th) of a second.  Resolution
                                        range in this mode is 1/100th of a
                                        second to 655 seconds (10.9 minutes).
     
     
     Examples:
     
               1.   Generate a good tone for an error message.  Use the
                    "internal timing" of 1/100ths of a second.  Each tone
                    will be generated for 3/100ths of a second.
     
                    .
                    .
                    .
                    sound(2000,3,.F.)
                    sound(500,3,.F.)
                    sound(2000,3,.F.)
                    .
                    .
                    .
     
               2.   Generate a tone indicating a different condition than
                    above.  Use the default timing of "timer ticks".  Each
                    sound will be generated for 1/18th of a second.
     
                    .
                    .
                    .
                    sound(2000,1)
                    sound(1000,1)
                    .
                    .
                    .
     




                                      Page #45
                                          
          Copyright (c) 1985-88 by Jason R. Matthews - All Rights Reserved
                                          

                                          
     PROCLIP2.LIB 2.00 User Documentation                 February 15, 1988
     ======================================================================



     SOUND (cont'd)
     
     Returns:
     
               Nothing.
     
     
     Cautions:
     
               None.













































                                      Page #46
                                          
          Copyright (c) 1985-88 by Jason R. Matthews - All Rights Reserved
                                          

                                          
     PROCLIP2.LIB 2.00 User Documentation                 February 15, 1988
     ======================================================================



     
                                      SPRINT
                                      ------
     
     
          Add new flexibility to your programming with the SPRINT command.
          This function allows display of a character string on the screen
          using a different color attribute than that which is currently
          selected through SET COLOR TO.  The function will either retain the
          current cursor position or move the cursor to the end of the newly
          displayed string.  Not subject to SET DEVICE TO so updating of
          screen and printer can be performed easily.
     
     
     Format:
     
               sprint([row, col,] string [,attr][,type])
     
                    or
     
               @ x,y say sprint(string [,attr][,type])
     
     
     Parameters:
     
               row.......OPTIONAL.  Numeric variable or constant which
                         informs the function of the row (line) number on
                         which to begin display of the string.  Use of ROW
                         assumes a COL will be specified.  ROW must be a
                         valid video line number between 0 and 24 inclusive.
                         If the string will not fit on ROW it will be wrapped
                         to the following line (if any).
     
               col.......OPTIONAL.  Numeric variable or constant which
                         informs the function of the column number on which
                         to begin the display of the string.  Use of COL
                         assumes the use of ROW.  COL must be a valid video
                         column number between 0 and 79 inclusive.  Using the
                         format of sprint(row,col...) will not reposition the
                         cursor, the cursor position will not change.  Using
                         the @ x,y say... format will reposition the cursor
                         to the end of the displayed string.
     
                         sprint(row,col...)
                                        After printing the string, the cursor
                                        will be returned to the position last
                                        known by Clipper.  In other words the
                                        cursor will not move.
               






                                      Page #47
                                          
          Copyright (c) 1985-88 by Jason R. Matthews - All Rights Reserved
                                          

                                          
     PROCLIP2.LIB 2.00 User Documentation                 February 15, 1988
     ======================================================================



     SPRINT (cont'd)
     
                         @...SAY sprint(...)
                                        After printing the string, the cursor
                                        will be moved to the end of the
                                        string just printed.  Acts similar to
                                        the standard @...SAY... in this
                                        fashion but you still get the color
                                        override capability.
     
               string....Character string variable or constant which will be
                         displayed beginning at the requested position.
     
               attr......OPTIONAL.  Character string variable or constant,
                         non case sensitive, which informs the function what
                         color attributes to use when displaying.  If not
                         specified the function will use the attribute
                         currently displayed on the screen at the starting
                         position for the string.
     
                                  (valid colors)
                         black                         N
                         blue                          B
                         green                         G
                         cyan                          BG
                         red                           R
                         magenta                       RB
                         brown                         GR
                         white                         W
                         intense                       +
                         blink                         *
     
               type......OPTIONAL.  Logical variable or constant instructing
                         the function to use DMA updating or not.
               
                         .T.            DEFAULT.  If not specified, the
                                        function will use DMA screen
                                        updating.
               
                         .F.            Setting this flag to a logical false
                                        will cause the function to use the
                                        standard BIOS INT 10H for screen
                                        updating.
     
     










                                      Page #48
                                          
          Copyright (c) 1985-88 by Jason R. Matthews - All Rights Reserved
                                          

                                          
     PROCLIP2.LIB 2.00 User Documentation                 February 15, 1988
     ======================================================================



     SPRINT (cont'd)
     
     Examples:
     
               1.   Print a warning message on the screen but do not
                    reposition the cursor.  Further, print the message in
                    bright red on a black background even though those colors
                    are not currently selected.
     
                    .
                    .
                    .
                    sprint(24,00,"Don't press that key again!","+r/b")
                    .
                    .
                    .
     
               2.   Print a message on the screen and reposition the cursor
                    to the end of the message.  Use the intense white on a
                    black background.
     
                    .
                    .
                    .
                    @ 10,00 say sprint('Enter your password: ','+w/b')
                    .
                    .
                    .
     
     
     Returns:
     
               null......A null character string is returned thereby allowing
                         SPRINT to be used "in line" with a standard Clipper
                         @... SAY...  (eg.  @ X,Y SAY "Hi" + sprint(...) is
                         valid).
     
     
     Cautions:
     
               None.














                                      Page #49
                                          
          Copyright (c) 1985-88 by Jason R. Matthews - All Rights Reserved
                                          

                                          
     PROCLIP2.LIB 2.00 User Documentation                 February 15, 1988
     ======================================================================



     
                                      STAMP
                                      -----
     
     
          Many times date and time stamps are the only way to know when a
          database was last used.  The STAMP functions provides the
          programmer with the ability to change the date and/or time of any
          file.  If no date and time are given in the function call, the
          STAMP function will set the date and time of the file to the
          current date and time as maintained by DOS.
     
     
     Format:
     
               stamp(filename [,date] [,time])
     
     
     Parameters:
     
               filename..Character string variable or constant, non case
                         sensitive, which contains the filename to STAMP.
                         STAMP will not accept filenames containing wildcards
                         (* & ?) but paths and alternate drives are
                         acceptable.
     
               date......Date variable or constant which is the date to set
                         the file to.  If DATE is not specified, and TIME is
                         specified, the file's date stamp will not be
                         affected.
     
               time......Character string variable or constant containing the
                         time to set the file to.  The time format should be
                         HH:MM:SS but seconds are not necessary (eg. HH:MM is
                         also valid).  If TIME is not specified, and DATE is
                         specified, the file's time stamp will not be
                         affected.
     
                         If no parameters are specified other than the
                         FILENAME, the date and time will be obtained from
                         DOS and the file's date and time stamps will be
                         updated accordingly.
     
     











                                      Page #50
                                          
          Copyright (c) 1985-88 by Jason R. Matthews - All Rights Reserved
                                          

                                          
     PROCLIP2.LIB 2.00 User Documentation                 February 15, 1988
     ======================================================================



     STAMP (cont'd)
     
     Examples:
     
               1.   Set all of the DBF files in the directory to a specific
                    date and time.
     
                    .
                    .
                    .
                    aDate = ctod("10/22/86")
                    aTime = "10:12:15"
                    filename = sdir("*.*","first")
                    do while .not. empty(filename)
                         stamp(filename,aDate,aTime)
                         filename = sdir('next')
                    enddo
                    .
                    .
                    .
     
     
     Returns:
     
               Nothing.
     
     
     Cautions:
     
               The file being STAMPed should not currently be opened by any
               other process.  Close all files first.
























                                      Page #51
                                          
          Copyright (c) 1985-88 by Jason R. Matthews - All Rights Reserved
                                          

                                          
     PROCLIP2.LIB 2.00 User Documentation                 February 15, 1988
     ======================================================================



     
                                     UNRESET
                                     -------
     
     
          Having frustrated users reset the computer in the middle of your
          application is not fun...neither is recovering corrupted data
          bases.  UNRESET is designed to intercept the CTRL ALT DEL keyboard
          sequence and, optionally, prevent the computer from resetting.
          
          UNRESET will, at the programmers option, either intercept and
          ignore CTRL ALT DEL keyboard sequences or intercept and display a
          warning message to the operator which requires a second CTRL ALT
          DEL to activate the reset.
     
     
     Format:
     
               unreset('on' | 'off' | 'warn')
     
     
     Parameters:
     
               'on'......Character string variable or constant, non case
                         sensitive, which instructs the function to become
                         active and intercept and ignore all CTRL ALT DEL
                         keyboard sequences.
     
               'off'.....Character string variable or constant, non case
                         sensitive, which instructs the function to disable
                         itself and allow CTRL ALT DEL keyboard sequences
                         through to the regular computer keyboard routines.
     
               'warn'....Character string variable or constant, non case
                         sensitive, which instructs the function to become
                         active and intercept all CTRL ALT DEL keyboard
                         sequences.  Once intercepted the function will warn
                         the user of their action by opening a window
                         centered on the screen which reads:
     
                                 CTRL + ALT + DEL
     
                              Press again to confirm
     
                         The user must then reissue the CTRL ALT DEL sequence
                         to force a reset or, by pressing any regular key,
                         close the window and resume execution of the
                         program.
     
     





                                      Page #52
                                          
          Copyright (c) 1985-88 by Jason R. Matthews - All Rights Reserved
                                          

                                          
     PROCLIP2.LIB 2.00 User Documentation                 February 15, 1988
     ======================================================================



     UNRESET (cont'd)
     
     Examples:
     
               1.   Completely disable CTRL ALT DEL during critical
                    processing.
     
                    .
                    .
                    .
                    unreset('on')
                    use dbffile index ntxfile
                    append blank
                    replace ...
                    close databases
                    unreset('off')
                    .
                    .
                    .
     
               2.   Issue a warning prior to allowing a reset to occur.
                    Disable the UNRESET function before exiting program.
     
                    .
                    .
                    .
                    unreset('warn')
                    .
                    .
                    .
                    unreset('off')
                    quit
     
     
     Returns:
     
               Nothing.
     
     
     Cautions:
     
               This function should not be placed into an overlay as it is
               interrupt driven.  Any error routines which determine an
               unrecoverable runtime error has occurred should disable this
               function prior to exiting the program.  Failure to follow this
               caution may result in the computer locking up.









                                      Page #53
                                          
          Copyright (c) 1985-88 by Jason R. Matthews - All Rights Reserved
                                          

                                          
     PROCLIP2.LIB 2.00 User Documentation                 February 15, 1988
     ======================================================================



     
                                      VIDEO
                                      -----
     
     
          The VIDEO function has the ability to disable or enable the video
          signal to the current video controller.  This has the effect of
          "blanking" a monitor during idle times which will prevent monitor
          burn.  Current supported monitor types are monochrome (MONO), color
          (CGA), enhanced (EGA) and video graphics array (VGA).
     
     
     Format:
     
               video('on' | 'off')
     
     
     Parameters:
     
               'on'......Character string variable or constant, non case
                         sensitive, instructing  the function to enable the
                         video signal on the video controller.  Uses the last
                         BIOS saved screen mode to enable the video signal
                         through a direct command to the video controller.
                         The screen will restore to the current contents of
                         the video memory instantaneously.
     
               'off'.....Character string variable or constant, non case
                         sensitive, instructing the function to disable the
                         video signal on the video controller.  Uses the last
                         BIOS saved screen mode, modified with proper bit
                         settings, to disable the video signal through a
                         direct command to the video controller.  None of the
                         information is lost from the screen as the screen is
                         simply "turned off", not erased.
     
     
     Examples:
     
               1.   Turn off the video controller video drive signal after
                    waiting sixty (60) seconds for some keystroke.
     
                    .
                    .
                    .
                    inkey(60)
                    video('off')
                    .
                    .
                    .
     




                                      Page #54
                                          
          Copyright (c) 1985-88 by Jason R. Matthews - All Rights Reserved
                                          

                                          
     PROCLIP2.LIB 2.00 User Documentation                 February 15, 1988
     ======================================================================



     VIDEO (cont'd)
     
               2.   Turn on the video controller drive signal.
     
                    .
                    .
                    .
                    video('on')
                    .
                    .
                    .
     
     
     Returns:
     
               Nothing.
     
     
     Cautions:
     
               None.


































                                      Page #55
                                          
          Copyright (c) 1985-88 by Jason R. Matthews - All Rights Reserved
                                          

                                          
     PROCLIP2.LIB 2.00 User Documentation                 February 15, 1988
     ======================================================================



     
                                     VSCROLL
                                     -------
     
     
          The premier scrolling function...bar none.  Many times we've all
          needed a scrolling function like VSCROLL.  The VSCROLL function
          performs video scrolling, either vertically (up and down) or
          horizontally (left and right), and allows the programmer to control
          the attribute of the blank line (or column) left behind by the
          scrolling action.
     
     
     Format:
     
               vscroll(top, left, bottom, right, lines, dir [,attr])
     
     
     Parameters:
     
               top.......Numeric variable or constant indicating the top row
                         of the area to be scrolled.  Value checked to be
                         between 0 and 24 inclusive.
               
               left......Numeric variable or constant indicating the left
                         column of the area to be scrolled.  Value checked to
                         be between 0 and 79 inclusive.
               
               bottom....Numeric variable or constant indicating the ending
                         row of the area to be scrolled.  Value checked to be
                         greater than TOP but less than or equal to 24.
               
               right.....Numeric variable or constant indicating the right
                         column of the area to be scrolled.  Value checked to
                         be greater than LEFT but less than or equal to 79.
     
               lines.....Numeric variable or constant indicating the number
                         of lines or columns to be scrolled, or zero (0) to
                         scroll entire window (effectively erasing it).
                         Value checked to be equal to or less than BOTTOM -
                         TOP if a vertical scroll or equal to or less than
                         RIGHT - LEFT if horizontal.  If greater than the
                         number of available lines or columns within the
                         specified area zero (0) will be assumed.
     
               dir.......Character string variable or constant, non case
                         sensitive, indicating the direction of the scroll
                         ('u' = Up, 'd' = Down, 'l' = Left, 'r' = Right).
     






                                      Page #56
                                          
          Copyright (c) 1985-88 by Jason R. Matthews - All Rights Reserved
                                          

                                          
     PROCLIP2.LIB 2.00 User Documentation                 February 15, 1988
     ======================================================================



     VSCROLL (cont'd)
     
               attr......OPTIONAL.  Character string variable or constant,
                         non case sensitive, containing a valid color command
                         or combination for character and background.  Must
                         be the alpha representation of the color, the
                         numeric will be rejected.  The default is the color
                         attribute currently on the screen for the character
                         in the TOP, LEFT position.
     
                                  (valid colors)
                         black                         N
                         blue                          B
                         green                         G
                         cyan                          BG
                         red                           R
                         magenta                       RB
                         brown                         GR
                         white                         W
                         intense                       +
                         blink                         *
     
     
     Examples:
     
               1.   This will scroll one line down in the area from row #10,
                    column #20 through row #12, column #60 using an attribute
                    of black character (n) and white background (w).
     
                    .
                    .
                    .
                    vscroll(10,20,12,60,1,'d','n/w')
                    .
                    .
                    .
     
               2.   This will scroll one column to the right in the area from
                    row #05,column #00 through row #20, column #79 using
                    whatever the attribute of the character at 10,20
                    currently is.
     
                    .
                    .
                    .
                    vscroll(05,00,20,79,1,'r')
                    .
                    .
                    .
     
     




                                      Page #57
                                          
          Copyright (c) 1985-88 by Jason R. Matthews - All Rights Reserved
                                          

                                          
     PROCLIP2.LIB 2.00 User Documentation                 February 15, 1988
     ======================================================================



     VSCROLL (cont'd)
     
     Returns:
     
               Nothing.
     
     
     Cautions:
     
               None.













































                                      Page #58
                                          
          Copyright (c) 1985-88 by Jason R. Matthews - All Rights Reserved
                                          

                                          
     PROCLIP2.LIB 2.00 User Documentation                 February 15, 1988
     ======================================================================



     
     
                                      WILDAT
                                      ------
     
     
          The WILDAT function will perform a search of a target string for
          the first occurrence matching the specified string pattern.  The
          pattern string may contain the wildcard character (?) indicating a
          "don't care" for this position within the match.  The function also
          has the options of ignoring case during the match or altering the
          offset within the target string for the scan to begin.
     
     
     Format:
     
               wildat(pattern, target [,offset] [,case])
     
     
     Parameters:
     
               pattern...Character string variable or constant which is the
                         string to look for in the TARGET string.  The
                         PATTERN length must be greater than zero, less than
                         32,767 and shorter than the TARGET length.  The
                         following are special cases within the pattern.
     
                         ? (wildcard)   Indicates to the matching process
                                        that it should ignore the character
                                        in this position, but that a
                                        character will exist in that
                                        position.  The PATTERN of "t??" will
                                        match on all of the following
                                        examples: "that", "test", "text" and
                                        "with this".  The last one will match
                                        because of the .."th t.." matches the
                                        wildcard pattern.
     
                         \ (literal)    Indicates to the matching process
                                        that it should take the next
                                        character in the PATTERN literally.
                                        This may be used when attempting to
                                        match on the wildcard character
                                        itself.  For instance, a pattern of
                                        "\?" will match in the phrase "Do you
                                        understand?" when the question mark
                                        is encountered.  To match on the
                                        backslash character (\) itself, just
                                        precede it with a literal flag (eg.
                                        "\\").





                                      Page #59
                                          
          Copyright (c) 1985-88 by Jason R. Matthews - All Rights Reserved
                                          

                                          
     PROCLIP2.LIB 2.00 User Documentation                 February 15, 1988
     ======================================================================



     WILDAT (cont'd)
     
               target....Character string variable or constant which is the
                         string to search for the occurrence of PATTERN.  The
                         TARGET length must be greater than zero, equal to or
                         less than 32,767 and greater than the PATTERN
                         length.
     
               offset....OPTIONAL.  Numeric variable or constant which is the
                         offset within the TARGET for the search to begin.
                         The default is no offset so searching will start at
                         the first character in the TARGET.  The first
                         character in the TARGET is at offset zero (0) so all
                         offsets are the actual character position in the
                         string minus one.  Think of the offset as telling
                         the function to "ignore this many characters before
                         beginning the search."  The length of the PATTERN
                         string plus this OFFSET must not exceed the length
                         of the TARGET string.
     
               case......OPTIONAL.  Logical variable or constant which
                         instructs the function to ignore case during the
                         search.
               
                         .T.            DEFAULT.  Forces the matching process
                                        to adhere to case matching.
               
                         .F.            Setting this flag to false (.F.)
                                        instructs the function to ignore case
                                        matching.  Therefore, "The" and "the"
                                        will be considered identical for
                                        matching purposes.
     
     





















                                      Page #60
                                          
          Copyright (c) 1985-88 by Jason R. Matthews - All Rights Reserved
                                          

                                          
     PROCLIP2.LIB 2.00 User Documentation                 February 15, 1988
     ======================================================================



     WILDAT (cont'd)
     
     Examples:
     
               1.   Search the TARGET text and return the position of every
                    occurrence of the word "the" and ignore case matching.
                    The function will find two occurrences, one at position
                    #01 and the other at position #33.
     
                    .
                    .
                    .
                    target = 'The quick brown fox jumped over the lazy dog.'
                    offset = 0
                    do while .T.
                         offset = WILDAT('the', target, offset, .f.)
                         if offset < 1
                              exit
                         endif
                         (do something)
                    enddo
                    .
                    .
                    .
                    
                    The quick brown fox jumped over the lazy dog
                    ^                               ^
     
               2.   Search the TARGET text and return the position of every
                    occurrence of the pattern "t??t" and enforce case
                    matching.  The function will find four occurrences, at
                    positions #16, #25, #32 and #35.
     
                    .
                    .
                    .
                    pattern = 't??t'
                    target = 'That guy gives tests on text with that book.'
                    offset = 0
                    do while .T.
                         offset = WILDAT(pattern, target, offset)
                         if offset < 1
                              exit
                         endif
                         (do something)
                    enddo
                    .
                    .
                    
                    That guy gives tests on text with that book.
                                   ^        ^      ^  ^




                                      Page #61
                                          
          Copyright (c) 1985-88 by Jason R. Matthews - All Rights Reserved
                                          

                                          
     PROCLIP2.LIB 2.00 User Documentation                 February 15, 1988
     ======================================================================



     WILDAT (cont'd)
     
               3.   Search the TARGET text and return the position of every
                    question mark (?).  As this is the wildcard character
                    remember we must use the literal (\) expression.  The
                    function will find two occurrences, one at position #13
                    and the other at position #24.
     
                    .
                    .
                    .
                    pattern = '\?'
                    target = 'Did you know?  Does she?'
                    offset = 0
                    do while .T.
                         offset = WILDAT(pattern, target, offset)
                         if offset < 1
                              exit
                         endif
                         (do something)
                    enddo
                    .
                    .
                    .
                    
                    Did you know?  Does she?
                                ^          ^
     
     
     Returns:
     
               memvar....Number variable which, if greater than zero,
                         indicates the position within the TARGET where the
                         PATTERN was found.  This position is relative to the
                         start of the TARGET not the start of the
                         TARGET+OFFSET.  If zero then no match was found.  If
                         less than zero then an error in one of the
                         parameters prevented the search from beginning.
     
     
     Cautions:
     
               None.












                                      Page #62
                                          
          Copyright (c) 1985-88 by Jason R. Matthews - All Rights Reserved
                                          

                                          
     PROCLIP2.LIB 2.00 User Documentation                 February 15, 1988
     ======================================================================



     
                                     WILDRAT
                                     -------
     
     
          The WILDRAT function will perform a search of a target string for
          the first occurrence matching another string pattern but in a right
          to left type search.  The target string is searched in a right to
          left manner looking for the first occurrence of the pattern string.
          The pattern string may contain the wildcard character (?)
          indicating a "don't care" for this position within the match.  The
          function also has the options of ignoring case during the match or
          altering the offset within the target string for the scan to begin.
     
     
     Format:
     
               WILDRAT(pattern, target [,offset] [,case])
     
     
     Parameters:
     
               pattern...Character string variable or constant which is the
                         string to look for in the TARGET string.  The
                         PATTERN length must be greater than zero, less that
                         32,767 and shorter than the TARGET length.  The
                         following are special cases within the pattern.
     
                         ? (wildcard)   Indicates to the matching process
                                        that it should ignore the character
                                        in this position, but that a
                                        character will exist in that
                                        position.  The PATTERN of "t??" will
                                        match on all of the following
                                        examples: "that", "test", "text" and
                                        "with this".  The last one will match
                                        because of the .."th t.." matches the
                                        wildcard pattern.
     
                         \ (literal)    Indicates to the matching process
                                        that it should take the next
                                        character in the PATTERN literally.
                                        This may be used when attempting to
                                        match on the wildcard character
                                        itself.  For instance, a pattern of
                                        "\?" will match in the phrase "Do you
                                        understand?" when the question mark
                                        is encountered.  To match on the
                                        backslash character (\) itself, just
                                        precede it with a literal flag (eg.
                                        "\\").




                                      Page #63
                                          
          Copyright (c) 1985-88 by Jason R. Matthews - All Rights Reserved
                                          

                                          
     PROCLIP2.LIB 2.00 User Documentation                 February 15, 1988
     ======================================================================



     WILDRAT (cont'd)
     
               target....Character string variable or constant which is the
                         string to search for the occurrence of PATTERN.  The
                         TARGET length must be greater than zero, equal to or
                         less than 32,767 and greater than the PATTERN
                         length.
     
               offset....OPTIONAL.  Numeric variable or constant which is the
                         offset within the TARGET for the search to begin.
                         The default is no offset so searching will start at
                         the last character in the TARGET.  The last
                         character in the TARGET is at offset zero (0) so all
                         offsets are the actual character position in the
                         string minus one.  Think of the offset as telling
                         the function to "ignore this many characters before
                         beginning the search."  The length of the PATTERN
                         string plus this OFFSET must not exceed the length
                         of the TARGET string.
     
               case......OPTIONAL.  Logical variable or constant which
                         instructs the function to ignore case during the
                         search.
               
                         .T.            DEFAULT.  Forces the matching process
                                        to adhere to case matching.
               
                         .F.            Setting this flag to false (.F.)
                                        instructs the function to ignore case
                                        matching.  Therefore, "The" and "the"
                                        will be considered identical for
                                        matching purposes.
     
     





















                                      Page #64
                                          
          Copyright (c) 1985-88 by Jason R. Matthews - All Rights Reserved
                                          

                                          
     PROCLIP2.LIB 2.00 User Documentation                 February 15, 1988
     ======================================================================



     WILDRAT (cont'd)
     
     Examples:
     
               1.   Search the TARGET text and return the position of every
                    occurrence of the word "the" and ignore case matching.
                    The function will find two occurrences, one at position
                    #13 and the other at position #45.
     
                    .
                    .
                    .
                    target = 'The quick brown fox jumped over the lazy dog.'
                    offset = 0
                    do while .T.
                         offset = WILDRAT('the', target, offset, .f.)
                         if offset < 1
                              exit
                         endif
                         (do something)
                    enddo
                    .
                    .
                    .
                    
                    The quick brown fox jumped over the lazy dog
                    ^                               ^
     
               2.   Search the TARGET text and return the position of every
                    occurrence of the pattern "t??t" and enforce case
                    matching.  The function will find four occurrences, at
                    positions #10, #13, #20 and #29.
     
                    .
                    .
                    .
                    pattern = 't??t'
                    target = 'That guy gives tests on text with that book.'
                    offset = 0
                    do while .T.
                         offset = WILDRAT(pattern, target, offset)
                         if offset < 1
                              exit
                         endif
                         (do something)
                    enddo
                    .
                    .
                    
                    That guy gives tests on text with that book.
                                   ^        ^      ^  ^




                                      Page #65
                                          
          Copyright (c) 1985-88 by Jason R. Matthews - All Rights Reserved
                                          

                                          
     PROCLIP2.LIB 2.00 User Documentation                 February 15, 1988
     ======================================================================



     WILDRAT (cont'd)
     
               3.   Search the TARGET text and return the position of every
                    question mark (?).  As this is the wildcard character
                    remember we must use the literal (\) expression.  The
                    function will find two occurrences, one at position #01
                    and the other at position #12.
     
                    .
                    .
                    .
                    pattern = '\?'
                    target = 'Did you know?  Does she?'
                    offset = 0
                    do while .T.
                         offset = WILDRAT(pattern, target, offset)
                         if offset < 1
                              exit
                         endif
                         (do something)
                    enddo
                    .
                    .
                    .
                    
                    Did you know?  Does she?
                                ^          ^
     
     
     Returns:
     
               memvar....Number variable which, if greater than zero,
                         indicates the position within the TARGET where the
                         PATTERN was found.  This position is relative to the
                         end of the TARGET not the end of the TARGET+OFFSET.
                         If zero then no match was found.  If less than zero
                         then an error in one of the parameters prevented the
                         search from beginning.
     
     
     Cautions:
     
               None.












                                      Page #66
                                          
          Copyright (c) 1985-88 by Jason R. Matthews - All Rights Reserved