TurboDraw

                              User's  Manual

                           Last Revised 09/09/89




















                           Daytron Electronics Inc.
				P.O.Box 851591
			  Richardson,  Tx 75085-1591
                                (214) 669-2137




        COPYRIGHT

        (c)Copyright  1988,1989  Daytron  Electronics  Inc.   All  Rights 
        Reserved

        TRADEMARK

        EZ-CAD and TurboDraw are trademarks of Daytron Electronics Inc.
        Hercules  Graphics  Card  is  a trademark  of  Hercules  Computer 
        Technology
        Hewlette-Packard is a trademark of Hewlett-Packard Co.
        IBM,PC,XT,AT,and  PS/2 are trademarks of  International  Business 
        Machines Corporation
        Mouse Systems is a trade mark of Mouse Systems Corporation
        Okidata is a registered trademark of Oki America Inc.
        NEC is a registered trademark of Nippon Electric Co.
        DM/PL and Houston Instrument are trademarks of Amtek Inc.

        DISCLAIMER

        Daytron  Electronics  warrants  that the enclosed  software  will 
        perform substantially in accordance with this manual for a period 
        of  30  days from the day of receipt.  No  other  warranties  are 
        implied.

        GRANT OF LICENSE

        This  product  is  only licensed and not  sold.  It  remains  the 
        property of Daytron Electronics Inc.




        TABLE OF CONTENTS


        1: ABOUT TURBODRAW............................................ 1

        2: INSTALLING TURBODRAW....................................... 2

           2.1 System Requirements.................................... 2

           2.2 Installation........................................... 5

        3: STARTING TURBODRAW......................................... 7

           3.1 Resolving Mouse Problems............................... 7 

           3.2 Resolving Loading Problems............................. 8

           3.3 Running TurboDraw From Another Directory...............10

        4: USING TURBODRAW............................................11

           4.1 TurboDraw Menus........................................11

               4.1.1 Main Menu........................................12

               4.1.2 Submenus.........................................12

           4.2 Select and Cancel Buttons..............................12

           4.3 Cursor Movement........................................13

               4.3.1 Cursor Keys......................................13

               4.3.2 Screen Cursors...................................14

           4.4 Auto Select............................................14

           4.5 Pan....................................................14

           4.6 Auto Delete/Reposition.................................15

           4.7 Drag/Reposition........................................15

           4.8 Stretch/Flip...........................................15

           4.9 Single key commands....................................15
          
        6: OPTIONS AND COMMANDS.......................................17




           6.1 Draw...................................................17

               6.1.1 Variable and Fixed Size Symbols..................17

               6.1.2 Lines and Curves.................................18

               6.1.3 Circle...........................................20

               6.1.4 Half Circle and Quarter Circle...................20

               6.1.5 Arc..............................................20

               6.1.6 Fill.............................................20

           6.2 Edit...................................................21
             
               6.2.1 Edit Text........................................21

               6.2.2 Select Element, Object, Section..................23

               6.2.3 Reduce and Enlarge...............................24

               6.2.4 Cut and Paste....................................24

               6.2.5 Move.............................................25

               6.2.6 Delete Last Object...............................25

               6.2.7 Deselect.........................................26

               6.2.8 Redraw...........................................26

               6.2.9 Change Style.....................................26

               6.2.10 Trim............................................26

               6.2.11 Rotate..........................................26

           6.3 Configuration..........................................27

               6.3.1 Drawing Size.....................................27

               6.3.2 Full View........................................27

               6.3.3 Clear............................................28
           
               6.3.4 Border Line......................................28

               6.3.5 Info Box.........................................28





               6.3.6 Grid.............................................28

               6.3.7 Snap to Grid.....................................29

               6.3.8 View = 1:1.......................................29

               6.3.9 View = 1/2.......................................29

               6.3.10 View = X2.......................................29

           6.4 File...................................................30

               6.4.1 Read into Cut Buffer.............................30

               6.4.2 Write from Select Buffer.........................30

               6.4.3 Create PCX File..................................30

               6.4.4 Create TIFF File.................................31

               6.4.5 Load .LBR File...................................31

               6.4.6 Load.............................................31

               6.4.7 Save.............................................31

               6.4.8 Dir, Del, Copy...................................31

               6.4.9 Print............................................32

               6.4.10 Plot............................................34

               6.4.11 Quit............................................35

               6.4.12 Exit............................................35

           6.5 Style..................................................36

               6.5.1 Font Size........................................36

               6.5.2 Line Type........................................36

               6.5.3 Plotting with Colors.............................36
                       
           6.6 Library................................................38

        APPENDIX A: Building Library Files............................39




        APPENDIX B: Drawing File Format...............................43

        APPENDIX C: Font File Format..................................44

        APPENDIX F: TurboDraw Memory Layout...........................50

        APPENDIX G: Devices Supported by EZCAD........................52

        APPENDIX H: TurboDraw Software Interrupts.....................57

        APPENDIX I: Coordinate System.................................58

        APPENDIX J: Resolving Plotter Problems........................59

        APPENDIX K: Resolving Printer Problems........................60

        APPENDIX L: Porting Drawings to DSP or WP.....................61

        APPENDIX M: Modifying Text Fonts..............................62




        1: ABOUT TURBODRAW


        Congratulations  on having purchased TurboDraw.  We believe it is 
        the   easiest  computer-aided  drafting (CAD) program  available. 
        It is our goal to provide capable software to maximize the use of 
        many  home  or  office  microcomputers at a  price  that  can  be 
        justified by casual users.

        This  manual  is intended as a reference guide for TurboDraw  and 
        familiarity with microcomputer hardware and operating systems  is 
        assumed.  If  you are not familiar with microcomputer hardware or 
        software,  please  refer to the documentation supplied with  your 
        equipment.

        Although  we try to keep this manual as up-to-date  as  possible, 
        some  changes and additional features may be found in the READ.ME 
        file on the TurboDraw diskette. We recommand that your print this 
        file and paste the printout on the blank pages toward the end  of 
        this manual.

        TurboDraw  is  an entry level CAD program that combines the  easy 
        point-and-click  user interface and the ability to generate  user 
        symbol  libraries.  TurboDraw  can produce  professional  quality 
        drawings   for   electrical,    architectural,   and   mechanical 
        engineers,   as  well  as  dataflow, program flow, and structural 
        charts for programmers, systems analysts, and database managers.

        The  drawings  produced  by TurboDraw  consist  of  elements  and 
        objects  (also  referred  to  as symbols) which  are  defined  as 
        follows:

        * Element - line, curve, circle, dot, characters etc.

        * Object/Symbol - collection of elements.

        The files used to store drawings consist of descriptions of these 
        elements (or vectors).  In other words, TurboDraw does not handle 
        bit-mapped  images like some painting/drawing  programs.   It  is 
        best  used to create technical drawings that consist primarily of 
        lines and curves.

        TurboDraw is menu-driven. That means when the program is ready to 
        accept a command, it displays all possible choices on the screen.

        A  convenient  feature of TurboDraw is  the  SPOOLing  capability 
        which  redirects output to a file instead of to a  device.   This 
        enables you to print or plot output at a more convenient time, or 
        from a PC that is connected to the proper printer or plotter.  


                                        1




        2: INSTALLING TURBODRAW


        2.1 System Requirements

        An  IBM PC,  XT,  AT or compatible with CGA,  EGA,  or   Hercules 
        monochrome  graphics card running MS DOS/PC DOS 2.0 or higher  is 
        required.

        IBM   PS/2  family  computers  with  MCGA  or  VGA  are  downward 
        compatible with CGA and EGA and therefore are also supported.

        A  mouse is recommended but not required.  The following  devices 
        are supported:

        * EPSON/IBM Graphics compatible printer

        * EPSON 24-pin printers

        * IBM QuietWrite printer

        * OKIDATA printers

        * NEC/TEC or compatible printers

        * HP LaserJet, DeskJet, or any PCL compatible printers 

        * Toshiba 24-pin printers

        * Tally printers

        * HP or any HP/GL compatible plotters

        * Houston Instrument or any DM/PL compatible plotters

        * Sweet P/ComScriber I plotters

        * All  mouse  devices and digitizers that conform to the INT  33H 
          standard

        Either  standard  carriage (10") or wide carriage (15")  printers 
        can be used.









                                        2




        The  amount of memory required depends  on  the type of  graphics 
        card  used and the selected drawing size.  The minimum  is  256K, 
        although we recommend 640K.

        The  TurboDraw  package  consists of  the  following 
        programs:

        * Mouse driver
             EZMOUSE.COM

        * Graphics card drivers
             EGA.COM
             CGA.COM
             MGC.COM

        * Printer drivers
             EPSON.COM
             EPSON24.COM
             OKIDATA.COM
             IBM.COM
             NEC.COM
             PCL.COM
             QUIETW.COM
             GENER24.COM
             TOSHIBA.COM
             TALLY.COM

        * Plotter drivers
             HPGL.COM
             DMPL.COM
             SWEETP.COM

        * Installation program
             INSTALL.COM

        * Drawing program
             EZCAD.COM

        * Application program
             TBDRAW.COM
             TBSYMB.COM

        * Fonts
             *.FNT

        * Symbol libraries
             *.LBR




                                        3




        * Utilities
             EZMODE.COM
             EZPRINT.COM
             FNTTXT.COM
             TXTFNT.COM

        * Sample Drawing Files
             *.DRW











































                                        4




        2.2 Installation


        Before  configuring TurboDraw,  use the DOS command  DISKCOPY  or 
        COPY  to  create a working diskette from the  original  diskette.  
        Then store the original diskette in a safe place.

        To Install TurboDraw on a Fixed-disk System:

             1.   Insert the  working diskette in drive A. Set the fixed-
                  disk  default  directory and copy the contents  of  the 
                  working diskette to the fixed disk using DOS commands.

             2.   Type INSTALL and press Enter.
             
             3.   Follow  the instructions on the screen to continue.

        To Install TurboDraw on a Diskette-based System:

             1.   Insert the DOS diskette in drive A.

             2.   Insert the TurboDraw working diskette in drive B.

             3.   At the DOS prompt type B: and press Enter.

             4.   At the B> prompt, type INSTALL and press Enter.

             5.   Follow  the instructions on the screen to continue.

        ================================================================
        EZCAD Installation Menu Rev 1.3


             1) Video Display    : EGA
             2) Printer          : EPSON10
             3) Plotter          : SWEETP
             4) Mouse Port       : Installed by user
             5) Plotter Port     : LPTn or special
             6) Plotter model    :

        Please enter item number to change or <enter> to exit:
        ================================================================









                                        5




        The  INSTALL  program  defaults to the  following  settings:

             1. EGA monitor
             2. Standard carriage EPSON printer
             3. Sweet P plotter
             4. Mouse driver loaded by the user before starting TrubDraw.

        PS/2  users should select CGA instead of MCGA,  or EGA instead of 
        VGA for video display.

        The  INSTALL  program generates  a  "batch file" called  DRAW.BAT 
        which   loads  the  proper  drivers/programs  into  memory   when 
        executed.   INSTALL  is menu-driven and should be sufficient  for 
        most users. 

        For special configurations,  e.g., if a special printer driver is 
        needed,  you can load the drivers manually,  or use an editor  to 
        modify  the  existing  DRAW.BAT file.   If you  modify  DRAW.BAT, 
        ensure  that the application program (TBDRAW.COM) is the last  to 
        be  loaded,  because it takes control from  the operating  system 
        and starts the TurboDraw session.


        Non-US Keyboard Users:

        When   you enter text onto the drawing,   the character shown  on 
        the  screen   may  not   be what you  expect.   This  is  because 
        TurboDraw  assumes  a US keyboard and forms  the  shape   of  the 
        characters  according  to it.   If you  are  a   non-US  keyboard  
        user,   you  may  want  to modify our fonts  to  add  in  country  
        dependent  symbols  or letters.  Please refer to Appendix  M  for 
        detail.



















                                        6




        3: STARTING TURBODRAW


        If  you use a mouse,  load your own mouse driver before  starting 
        TurboDraw.   If  you  purchased  a  mouse  from  us,  follow  the 
        instructions on the mouse manual.

        To start TurboDraw,  type DRAW. You should see on the screen that 
        the  drivers are loaded  by DRAW.BAT.  After all the programs are 
        loaded,  the  screen should be cleared and the main  menu  should 
        appear on the left of the screen. Your are now ready to draw. 

        To  avoid  losing  hours  of work (by  a  sudden  power  failure, 
        computer  crash,  etc.) you should occasionally save your drawing 
        to disk.  It is also a good practice to save your drawing  before 
        every major change.


        3.1 Resolving Mouse Problems

        There is a mouse driver EZMOUSE.COM on the TurboDraw disk.  It is 
        supplied for 2 purposes:

             1. If  you do not have a mouse and plan to use the  keyboard 
                cursor  keys  to draw,  EZMOUSE will be  responsible  for 
                displaying and moving the graphics cursor.

             2. If your mouse is compatible with the Mouse Systems mouse, 
                and  its  mouse driver does not seem to work in  graphics 
                mode, you can try using EZMOUSE in lieu of your own mouse 
                driver.

        Note  that  EZMOUSE does not override any existing  mouse  driver 
        already loaded.

        In  the  rare event that EZMOUSE.COM works for TurboDraw but  not  
        other programs,  and your MOUSE.COM works for other programs  but 
        not TurboDraw,  you should change the first line of your DRAW.BAT 
        file to be

                EZMOUSE /F1

        if your mouse is connected to COM1, or

                EZMOUSE /F2

        if  your mouse is connected to COM2.  The "F" option  forces  the 
        mouse driver to be loaded even if another driver has already been 
        loaded.


                                        7





        At the end of DRAW.BAT you should add the folllowing line:

                EZMOUSE /P

        The  "P"  option purges the previously  loaded  EZMOUSE.COM,  and 
        reactivates the original MOUSE.COM.

        If  you  still  have  problems  with  your  mouse,  you  can  try 
        contacting  the  manufacturer of your mouse and get an update  of 
        your mouse driver.


        3.2 Resolving Loading Problems

        If  your  computer  freezes  or crashes  during  the  process  of 
        loading, it is possibly caused by one of the following:

             1. A memory resident program has been loaded.

                  Memory resident programs are usually those that can be 
                  invoked by pressing a "hot key". These programs may 
                  interfere with TurboDraw. Rename your AUTOEXEC.BAT file 
                  to something else and reboot the system to get rid of 
                  these programs to verify this problem.

                  The solution is to remove this program from the memory.

             2. Any interrupt vector between 60H through 67H has be used

                  This can be verified by using the DEBUG to look at 
                  memory location 0:180 through 0:19F for non-zero bytes.

                  The solution is to remove the program that uses this 
                  interrupt. If this is not possible, try relocate it to 
                  some other vector.

             3. You have specified the wrong video display

                  The following are the most common causes -

                  * MGC does not work:

                       1. The original IBM monochrome display  controller 
                          does not have graphics capability.

                       2. The  monochrome  display  is  actually  a   CGA 
                          connecting to a monochrome monitor.



                                        8




                  * EGA does not work:

                       Your EGA board is not 100% compatible.
















































                                        9




        3.3 Running TurboDraw from another directory

        To   run   TurboDraw   from  another  directory,   the  following  
        procedure  is recommended:

                  1. Delete the following line from your DRAW.BAT file:

                            TBDRAW

                  2. Set current directory to the TurboDraw subdirectory, 
                     type DRAW to load all the drivers.

                  3. Set   your  desired  working  directory,   type  the 
                     following line  to start TurboDraw

                            \TurboDraw path name\TBDRAW

                  4. To restart TurboDraw, goto 2.

































                                       10




        4: USING TURBODRAW 


        4.1 TurboDraw Menus

        TurboDraw is always in one of three distinct levels:

             Level 1 - Main menu function selection

             Level 2 - Submenu function selection

             Level 3 - Submenu function execution

        It  is very important that you know what level the program is in.  
        When  you load TurboDraw,  it displays the level 1 menu which  is 
        the main menu.   To move from level 1 to level 3 or from level  3 
        to level 3 you must go through level 2.   To move from level 2 to 
        level 2, you must go through level 1.  

        The shape of the cursor indicates the program level: 

             Level 1 - Arrow, main menu displayed

             Level 2 - Arrow, submenu displayed

             Level 3 - Non-arrow, no menu displayed

        Only one menu is active at any given time.  

        To select a menu item, simply move the cursor over the menu until 
        the item is highlighted and press the select button.




















                                       11




        4.1.1 Main Menu

        The  main menu is displayed on the left side of the drawing area. 
        Below  the  main menu area in the  lower  left-hand  corner,  the 
        current  drawing size and cursor position expressed in x- and  y-
        coordinates are displayed. 

        Each  main  menu entry encompasses a set of related functions  as 
        follows:

        * DRAW places objects on the drawing.

        * EDIT  edits a drawing using delete, copy, move, etc.

        * CONFIG  sets  the drawing environment,  including  paper  size, 
          grid, etc.

        * FILE is the disk file read/write function  which includes load, 
          save, print, exit, etc.

        * STYLE sets line types and character sizes.

        * LIBRARY allows you to draw user-defined symbols.


        4.1.2 Submenus

        When  you select any function in the main menu,  TurboDraw always 
        displays  a submenu in the drawing area.   Chapter 6  contains  a 
        detailed discussion of the submenus.


        4.2 Select and Cancel Buttons

        The Select button sets a point or confirms an operation,  and  is 
        either the left button on the mouse, the Enter key, or the F1 key 
        on the keyboard.

        The Cancel button cancels an operation,  exits a menu,  or serves 
        as  a negative response,  and is either the right button  on  the 
        mouse, the Esc key, or the F2 key on the keyboard.










                                       12




        4.3 Cursor Movement

        The  cursor  keys allow you to interact with TurboDraw to  create 
        and alter drawings.


        4.3.1 Cursor Keys

        The  keypad  cursor keys control the movement  of  the  currently 
        displayed  screen cursor,  and move in units of 8  pixels.   When 
        pressed simultaneously with the Shift key, the keypad cursor keys 
        move the cursor in units of 128 pixels.

        To move the cursor one pixel at a time, use the following control 
        keys (the ^ denotes pressing the Ctrl key simultaneously with the 
        next key):


                            ^E (up)

                  ^S (left)          ^D (right)

                           ^X (down)


        Other keys on the keypad also have special meaning:

        * Home - Move the cursor to the upper left corner.

        * End  - Move the cursor to the lower right corner.

        * PgUp - Move the cursor up 128 pixels.

        * PgDn - Move the cursor down 128 pixels.

















                                       13





        4.3.2 Screen Cursors

        TurboDraw employs four types of screen cursors, each 
        having a special meaning:

        * Arrow (->) - Select a menu item. 

        * Crosshair (+) - Marking location on the drawing.

        * Left bracket ([) - Enter text.

        * Question mark (?) - Verify action.

        The  arrow (->) cursor selects a function  from  the 
        main  menu  or from a submenu if a submenu  is  dis-
        played.  TurboDraw  always displays the arrow cursor 
        once an operation is complete.  To complete an oper-
        ation,  press either the Select button or the Cancel 
        button.   


        4.4 Auto Select

        To  display the previously selected  submenu,  press 
        the Select button in the drawing area instead of  in 
        the  main menu area.   

        To perform the last selected submenu function, place 
        the  cursor  off  the submenu and press  the  select 
        button  again. 


        4.5 Pan

        Pan  allows  you  to scan portions  of  the  drawing 
        quickly.   To  use Pan,  move the cursor so that  it 
        touches  the side of the drawing display  area  that 
        you want to view. TurboDraw moves the drawing in the 
        opposite direction.











                                       14




        4.6 Auto Delete/Reposition

        If the previous submenu is DRAW, EDIT or LIB, pressing the Cancel 
        button causes the last drawn or edited symbol to disappear.  This 
        operation if equivalent to the Delete Last Object command  (refer 
        to  6.2.6) followed by the Paste command.  To delete the  symbol, 
        press Cancel again. To reposition the symbol, move the dotted box 
        to the desired location and press the select button.

        If the previous operation was a "paste",  "autodelete" cuts the 
        whole pasted section.

        If objects are selected, auto-delete deselects only.


        4.7 Drag/Reposition

        While Pasting/Repositioning,  you can press and hold the keyboard 
        Ctrl  key  to  cause the actual symbol or section of  drawing  to 
        appear on the screen instead of the dotted box. This operation is 
        usually  referred  to  as "Dragging",  and  is  useful  for  fine 
        alignment.   Note  that  the  ^S,  ^E,  ^D  and  ^X  control  key 
        combinations also enable dragging.


        4.9 Single Key Commands

        The   following single key commands can be invoked at any time by 
        pressing the proper key, except during submenu selection:

        Single key menu selection:

             You can use single key stroke to select an item in any  text  
             menu,  if   there   is  one and only one field in  the  menu  
             that   has   this character  as its first character  in  the 
             field.  For example,  you can type FQ to quit TurboDraw.

        Single key style selection:

             "1" - Select single solid line and regular text.

             "2" - Select double solid line and small text.

             "3" - Select Tripple solid line and large text.

             "4" - Select dotted line.

             "5" - Select dashed line.



                                       15





        Single key commands:

             "G" - Turns "Snap to" of or off.

             "O" - Set  origin of relative coordinate and to  toggle  the 
                   coordinate    display  from  absolute  coordinate   to 
                   relative coordinate and vice versa.











































                                       16




        6: OPTIONS AND COMMANDS


        6.1 DRAW


        The  DRAW  submenu  is a graphics menu  that  contains  flowchart 
        symbols. Refer to appendix E for interpretation of the Icons.


        6.1.1 Variable-size and Fixed-size symbols

        STEP 1 - Select symbol

             To  select a symbol from the menu,  move the cursor over the 
             cell  containing the icon and press the Select  button.  The 
             submenu  will  disappear  and the cursor will  change  to  a 
             crosshair.

        STEP 2 - Place symbol

             NOTE:   To help you align your drawing,  TurboDraw  provides 
             the  grid function which you can turn on through the  Config 
             submenu.

             To  place  the  selected symbol on  the  drawing,  move  the 
             crosshair  cursor to the location where you want  the  upper 
             left  corner  of  the  symbol placed and  press  the  Select 
             button.  

             Symbols  can be of FIXED or VARIABLE size.  If the symbol is 
             FIXED, TurboDraw places the upper left corner of the icon at 
             the location defined by the cursor position. Go to Step 4 if 
             this is the case.

             If  the  symbol is VARIABLE,  TurboDraw draws a  dotted  box 
             representing  the  icon's default  boundaries,  placing  the 
             upper left corner of the box at the location defined by  the 
             original  crosshair cursor position and moving the crosshair 
             cursor to the lower right corner of the box.   Go to Step  3 
             if this is the case.
             
             If  you  select the TEXT icon,  TurboDraw displays the  text 
             cursor ([).   Use the keyboard to enter text.   See  section 
             6.2.1  for  rules about text-editing.  To terminate  a  text 
             block, press Ctrl-Z.  Then go to Step 4.


        STEP 3 - Set lower right corner


                                       17





             Move  the cursor to adjust the size of the dotted box before 
             pressing the Select button.

        STEP 4 - Draw another symbol or exit

             * To draw the same symbol again, go to Step 2.

             * To  exit  or draw a different symbol,  you can do  one  of 
               three things:

               - Press Cancel to exit to level 1 and select any item from 
                 the main menu.

               - Move the cursor off the menu and press the Select button 
                 to auto-select the DRAW submenu.

               - Go to Step 1 to draw another symbol.

             * To delete or reposition the symbol,  perform the following 
               steps:

               A - Press  Cancel  to exit to level 1.   The arrow  cursor 
                   appears.

               B - Cancel  again.   The symbol last drawn disappears from 
                   the  screen.   The cursor is replaced by a dotted  box 
                   which indicates the boundaries of the symbol.

               C - Move   the   box   to  the   desired   location    and            
                   press Select. The symbol will appear on  the screen at 
                   that location.

               D - Repeat  Step  C  to place multiple copies  of  of  the 
                   symbol.  Or, press Cancel to exit to level 1.


        6.1.2 Draw line or curve

             * To  draw  a  line,  move  the cursor to the starting point 
               and   press  the Select button.   Then,  begin moving  the 
               cursor   to   the   desired    ending  point.    TurboDraw 
               displays a dotted line which moves as you move the cursor.  
               When  you  reach the desired ending  point,  press  Select 
               again.  You can either press the cancel button to complete 
               the line, or continue to mark the ending point of the next 
               segment  of the line.  Continue in this fashion until  you 
               have finished drawing the line.  



                                       18





             * To    draw   a  CURVE,   you  must  mark   three   control        
               points,  P1,  P2,  and P3.  First,  move the cursor to the 
               beginning point (P1)  and press Select.  Then begin moving 
               the cursor to the desired mid-point (P2).  TurboDraw draws 
               a  dotted  line between P1 and P2.   Press Select  at  the 
               desired mid-point.  Finally, move the cursor to the ending 
               point (P3) of the curve and press Select.   Note that  the 
               curve   does  not  actually  pass  through  P2  but   only 
               "approaches" P2.









































                                       19




        6.1.3 Draw Circle

        STEP 2 - Mark   center  of  circle.   Rubberband  line   appears, 
                 representing the radius.

        STEP 3 - Mark radius of circle. Circle is drawn. Go to STEP 4.


        6.1.4 Half Circle and Quarter Circle

        STEP 2 - Mark starting point. Rubberband line is formed.

        STEP 3 - Mark  ending point.  An arc is drawn clockwise from  the 
                 starting point to the ending point. Go to STEP 4.


        6.1.5 Arc (partial circle)

        STEP 2 - Mark  the  center of circle.  Rubberband  line  appears, 
                 representing the radius.

        STEP 3 - Mark the starting point (the radius is also defined),  A 
                 dotted circle appears. Then mark the ending point on the 
                 circle.  The  Arc is drawn clockwise from  the  starting 
                 point to the ending point. Go to STEP 4.

        6.1.6 Fill

             To fill an closed area with a pattern, you must mark a point 
             within the area.  The marked point becomes the control point 
             of the Fill element. Note that since the area is first solid 
             filled  then turned into the pattern,  the pattern may  leak 
             into adjacent fill pattern,  if it contains solid horizontal 
             lines.

















                                       20




        6.2 EDIT


        The  EDIT submenu allows you to modify a drawing using a  variety 
        of methods. 

        6.2.1 Edit Text

        STEP 1 - Select Text

             Pan  the screen so that the whole text block appears on  the 
             screen.   Move  the  cursor close to the start of  the  text 
             block and press the Select button.  This action displays the 
             text cursor ([) at the end of the text block.

        STEP 2 - Modify text

             Modify text using the following rules:

             1.  You cannot replace (overstrike) characters.

             2.  Newly entered text is always  inserted.

             3.  You can  create new lines of text by pressing the  Enter 
                 key, which generates a Carriage Return <cr> character.

             4.  The  first  character of the text block marks  the  left 
                 margin for subsequent lines.

             5.  Cursor keys move the cursor WITHIN the text  block,  and 
                 do  not generate spaces.  Use the Space Bar to  generate 
                 spaces. 

             6.  The   Backspace   or  Delete  key  deletes   characters, 
                 including <cr>.

             7.  The    maximum   length  for  a  text   block   is   256          
                 characters, including <cr>'s.


        STEP 3 - Terminate or abort
             
             To terminate the current text block, press Ctrl-Z.

             To  abort  and exit to level 1,  press  Ctrl-C.


        STEP 4 - Create another text block or exit



                                       21




             When you complete a text block,  the program reactivates the 
             crosshair  cursor which you can move to a new  location  and 
             start  another text block.  Press the Cancel button to  quit 
             entering text. 















































                                       22




        6.2.2 Select Element, Object, and Section

        To edit a drawing, first you must specify the element, object, or 
        section  to be modified.   To do this,  choose one of the  Select 
        items from the Edit submenu.  

        After selecting and exiting to the main menu,  the program places 
        the selected element,  object,  or section in the SELECT  BUFFER.  
        Although the program still displays the selected element, object,  
        or  section,  the program  actually deletes it from the database.  
        The dotted boxes on the screen are not part of the  drawing,  and 
        therefore  disappear when you Pan or Refresh the screen.   If you 
        subsequently  choose  the Config or File submenu,  or  Select  or 
        Deselect from the Edit submenu,  the program returns the selected 
        element, object, or area to the drawing database.

        * Select Element or Object

        STEP 1 - Pick element

             Move  the cursor to the vicinity (within .5") of one of  the 
             control  points of the desired element and press  Select.  A 
             dotted  box  appears  around the  element,  and  the  cursor 
             changes into a question mark.

        STEP 2 - Confirm selection

             Press Select to confirm your selection,  or Cancel if it  is 
             the wrong element.

             If  another element shares the same control point,  a dotted 
             box  appears around that element as well.   If this  is  the 
             case, repeat this step.

             Once  you confirm your selection,  the cursor  changes to  a 
             crosshair.

        STEP 3 - Exit or select another

             Press  Cancel  to exit,  or go to Step 1 to  select  another 
             element. 

        STEP 4 - Another way to exit

             Move the cursor to the main menu area and press Select.


        * Select Section



                                       23




        STEP 1 - Mark upper left corner of area

             Move  the  cursor to the upper left corner of the  area  you 
             wish to select, and press the Select button.

        STEP 2 - Mark lower right corner of area

             Move  the  cursor to the lower right corner of the  area  so 
             that the dotted box encompasses the target area,  and  press 
             the Select button.

        6.2.3 Reduce/Enlarge

        You  can  reduce or enlarge the selected area using one  of  four 
        options:  Reduce 70.7%, Reduce 84.7%, Enlarge 118.0%, and Enlarge 
        141.4%.  Note the following calculations.

        * 0.707=1/1.414

        * 0.847=1/1.18

        * 0.707*0.707=.5

        * 1.414*1.414=2

        After  the  operation,  the reduced or enlarged  elements  remain 
        selected,  as  indicated by the presence of the dotted box.   You 
        can repeat the operation as many times as necessary.


        6.2.4 Cut and Paste 

        You  will  generally use the Cut option to  remove  the  selected 
        element,  object,  or area from the drawing. You can then use the 
        Paste  option  to  restore the CUT BUFFER contents,  or  to  make 
        multiple copies of the CUT BUFFER contents on the drawing.


        * Cut

        Cut removes the selected element, object, or area from the SELECT 
        BUFFER  and from the display and puts the associated data in  the 
        CUT  BUFFER.  You  can restore the CUT BUFFER contents  with  the 
        Paste command.  

        WARNING:   If  you  perform  another Cut,  or a  File  or  Config 
        operation,  the  program purges the CUT BUFFER  and the  previous 
        contents  are   lost.   Other editing commands  such  as  Reduce, 
        Enlarge, Edit Text, and  Move also overwrite the CUT BUFFER. 


                                       24





        If you select Cut without specifying an element,  line,  or area, 
        it behaves like a Select section followed by a Cut.  This feature 
        provides  you  with  a  shortcut for deleting an  area  from  the 
        drawing. 

        * Paste 

        The  Paste command transfers the  data in the CUT BUFFER  to  the 
        drawing.  Paste  also  moves  or  makes multiple  copies  of  the 
        element, object, or section in the CUT BUFFER.


        STEP 1 - Mark location to paste

             When you choose Paste,  the program replaces the cursor with 
             a dotted box which represents the boundaries of the element, 
             object,  or  area in the CUT BUFFER.   Move the box  to  the 
             desired  location and press the Select button.  The  program 
             draws the element,  object, or area in the CUT BUFFER at the 
             selected location.

        STEP 2 - Cancel or repeat

             To copy the CUT BUFFER contents at other  locations,  repeat 
             Step 1.  Otherwise, press Cancel to exit to level 1. 



        6.2.5 Move

        The  Move command is essentially a combination of Cut and  Paste.  
        Refer to 6.2.4 for instructions. 


        6.2.6 Delete Last Object

        The  primary use of Delete Last Object is to reposition the  last 
        drawn  object.   Essentially,  it  cuts the most  recently  drawn 
        object  and  places the associated data in the  CUT  BUFFER.   To 
        restore the object, use the Paste command. 

        WARNING:   Repititious  use of this command can clear the  entire 
        drawing.

        Another  convenient  way  to delete the last drawn object  is  to 
        press  the Cancel button in level 1,  but this only works if  the 
        previous submenu is DRAW. 



                                       25





        6.2.7 Deselect

        Deselect appends the selected element,  object, or section to the 
        database,  which  means  that the  element,  object,  or  section 
        becomes the most recently drawn element.


        6.2.8 Redraw

        Redraw causes TurboDraw to clear the drawing area and repaint  it 
        using the element descriptors in the database. If you have edited 
        the  drawing  extensively,  you should use this option since  the 
        drawing may not exactly match the database.   For  example,  when 
        you  delete  one of two intersecting or  overlapping  lines,  the 
        remaining line will appear disjointed.

        Redraw also causes causes the grid to be cleared.


        6.2.9 Change Style

        This  command cuases the line style of the selected symbols to be 
        changed  to  the current line style setting.  If no  symbols  are 
        selected,  the  cursor  will change to a cross hair and  you  are 
        expected to select a section of symbols.


        6.2.10 Trim

        This  powerful command can be used to move the control points  of 
        drawn  elements and therefore change the shape of  objects.  Move 
        your cursor close to the control point that you want to move, and 
        press   the  select  button.   The  selected  control  point   is 
        highlighted by having a dotted box around it.  You should mark  a 
        new  locatin for the control point.  All elements having the same 
        control point are affected.  This command is useful in  adjusting 
        the  length  of a line,  adjusting the curvature of a  curve,  or 
        changing the shape of a symbol.


        6.2.11 Rotate

        This command is used to change the shape of the selected objects. 
        The effect of rotate X and rotate Y is similar to stretching.  If 
        the  angle  of rotation is less than 180 degrees,  the object  is 
        reduced.  If the angle is greater than 180 degrees, the object is 
        expanded.



                                       26




        6.3 CONFIGURATION

        From the Config submenu, you can select the drawing size, display 
        a full view of most drawings,  clear the drawing,  create  border 
        lines and an information box, and turn on the grid.


        6.3.1 Drawing Size

        TurboDraw  supports  six drawing sizes,  ranging from the ANSI  A 
        size  to  the ANSI E size.  The dimensions for  these  sizes  are 
        listed  in  the  table below.  The default  drawing  size  (after 
        startup) is A (11" wide, 8.5" high).

        Wide  carriage printer 11" x 14" paper is also supported  and  is 
        dubbed W (for wide carriage).


                size   dimension      printed area
                ----   ---------      ------------
                  A    8.5 x 11           8 x 10.5
                  B     11 x 17        10.5 x 16
                  C     17 x 22          16 x 21
                  D     22 x 34          21 x 32
                  E     34 x 44          32 x 42
                  W     11 x 14        13.5 x 10.5


        Each  size has two orientations,  horizontal (width > height)  or 
        vertical  (height > width),  giving  you  a total of twelve  (12) 
        drawing sizes to select from.

        Note that due to the 640K memory restriction,  the E size drawing 
        is  shown  on  the  screen in  a  70.7%  scale,  but  the  actual 
        printed/plotted drawing is full size.

        WARNING:  If you change the paper size after you have started the 
        drawing,  you will lose everything up to that point.   Therefore, 
        ensure that you change the paper size BEFORE doing any work.


        6.3.2 Full View

        Full  View  shrinks  the  drawing  and  displays  it  in  reverse 
        highlight at the upper left corner of the screen.   To remove the 
        Full  View  display  from  the screen,  pan the  drawing  in  any 
        direction.




                                       27





        6.3.3 Clear

        Clear deletes the drawing display and database.   Note,  however, 
        that the CUT BUFFER is not affected by this operation. 


        6.3.4 Border Line

        Border  Line  draws a line around the border of the  drawing  .8" 
        from the paper edge.   If you decide to use this feature,  do  it 
        before you start the actual drawing.


        6.3.5 Info Box

        Info  Box  draws an information box on the lower right corner  of 
        the drawing.  If you decide to use this feature, do it before you 
        start the actual drawing.  An example of how to use this  feature 
        appears below.

          
                   --------------------------------
                  |  company name/logo             |
                  |--------------------------------|
                  |  project name                  |
                  |--------------------------------|
                  | SIZE | drawing name/revision   |
                  |--------------------------------|
                  | scale     | date     | sheet   |
                   --------------------------------


        6.3.6 Grid

        Grid  superimposes  a  grid on your drawing by displaying  a  dot 
        every 16 pixels both horizontally and veritcally.   This  feature 
        enables you to align the objects in the drawing. 

        Note  that the grid is not part of the drawing,  and only appears 
        on the screen for reference.   This command acts like a toggle in 
        that it turns the grid on and off.









                                       28





        6.3.7 Snap to Grid

        This  command  causes the cursor to be attracted to  the  closest 
        grid point,  or to the mid point between grid points.  In essence 
        the cursor moves in .125 (1/8") steps.

        Using  the cursor keys causes the cursor to snap to grid  whether 
        the command is in effect or not. Note that this commnad also acts 
        like a toggle.


        6.3.8 View = 1:1

        This commnad causes the drawing to be displayed in full size.


        6.3.9 View = 1/2

        This  command  causes the drawing to be displayed in one half  of 
        the original size.  Note that this command only affects the  view 
        of the drawing, the size of the drawing remain unchanged.

        The result of this commnad is cumulative.  Executing this command 
        twice causes the drawing to appear to be 1/4 the original size.


        6.3.10 View = X2

        This  command causes the drawing to be displayed in twice of  the 
        original  size.  

        This  command allows you to zoom-in  to  your drawing for  detail 
        work.  Note  that  the drawing area remains the same  size,   and 
        therefore  only 1/4 of the drawing remains in the  drawing  area.  
        To  view the whole drawing in this expanded  view,   change  your 
        drawing size to 4 times larger before executing this command.














                                       29




        6.4 FILE


        The  File  submenu  enables you to  perform  several  fundamental 
        tasks,  for  example,  load a drawing,  load a .LBR  file  (user-
        defined object definition file),  save a drawing, print or plot a 
        drawing,  and  exit or quit the program.   In addition,  you  can 
        perform  several  essential  DOS commands from  inside  TurboDraw 
        without having to exit the program,  for example,  delete a file, 
        copy  a  file,  and  list the contents  of  the  current  default 
        directory. 

        Note  that  a  file  name can  include  drive  specification  and 
        pathname,  or  can  be  a device name.  The file  name  extension 
        defaults to the following if not specified. To specify blank file 
        name extension you must terminate your file name with a period.

             * When saving or loading a file,  the file name extension is 
               assumed  to  be  .DRW  if  not  specified.  File  name  is 
               deblanked.

             * When  saving  a  file,  the original file  is  renamed  to 
               "filename.BAK" to provide a backup.

             * When  loading a library file,  the file name extension  is 
               assumed to be .LBR.


        6.4.1 Read into Cut Buffer

        This option reads a previously saved partial drawing into the Cut 
        Buffer and make it ready to be pasted.

         
        6.4.2 Write from Select

        The selected objects are saved to the specified file. This option 
        is  used to save partial drawing which can later be  merged  with 
        other drawings.


        6.4.3 Write PCX file

        TurboDraw   can  save  the  drawing in  .PCX  file  format.   The  
        resultant  drawing   has  the  same  resolution  as  your   video  
        display.  Note  that TurboDraw cannot read .PCX files.





                                       30





        6.4.4 Write TIFF file

        TurboDraw can save the drawing in .TIF file format. The .TIF file 
        has  a resolution of 150 dpi in both the horizontal  or  vertical 
        direction.   The maximum drawing area that is written to the .TIF 
        file is 14"X11". Note that TurboDraw cannot read .TIF files.


        6.4.5 Load .LBR File

        This  option  allows  you to open and read into  memory  a  user-
        defined  or  user-created (using TBSYMB,  refer  to  appendix  A) 
        object definition file.

        On startup,  TurboDraw automatically loads the file DRAW0.LBR  as 
        the default library file.


        6.4.6 Load

        Load  allows you to read into memory a previously saved  drawing. 
        Since this operation DOES NOT CLEAR the current drawing,  you can 
        use it to merge multiple drawings.


        6.4.7 Save

        This option saves the current drawing to the file you specify, in 
        the format as defined in Appendix B.


        6.4.8 Dir, Del, Copy

        The Dir option allows you to list the file names and sizes in the 
        current default directory. 

        Del deletes a file.

        Copy copies a file.











                                       31




        6.4.9 Print

        The   Print  option  saves  the  current  drawing  in  EZCAD.TMP, 
        generates  printer output,  and sends the output to a printer  or 
        SPOOL file.

        A  convenient  feature  of TurboDraw is the  SPOOLing  capability 
        which  enables you to direct drawing output to a  file.   If  you 
        direct  output to a file,  you can print drawing output at a more 
        convenient  time,  or from a PC that is connected to  the  proper 
        printer.  

        In  addition,  you  can create a SPOOL command to  print  drawing 
        files in background.  See Appendix D for instructions on creating 
        SPOOL.COM. 

        When  you  select Print from the File submenu,   it displays  the 
        following prompt:

             Device name: PRN

        You your output is not LPT1,  you must specify another file  name 
        or device name. 

        To  accept the default,  simply press Enter.   This action causes 
        the drawing output to be printed on your printer.

        To enter another file name, type the file name using standard DOS 
        file-naming conventions, and press Enter.  This action causes the 
        drawing  output  to  be  written  to  the  file  whose  name  you 
        specified.  TurboDraw generates one output file for each sheet in 
        the drawing.   In this case,  TurboDraw increments the file  name 
        extension.   For example,  if you entered SPOOL.0, the output for 
        the first sheet is written to SPOOL.0, the second to SPOOL.1, and 
        so on.   If you specify another file name,  e.g. TEST.A, then the 
        first  sheet is written to TEST.A,  the second to TEST.B,  and so 
        on.

        To print a SPOOL file, use the TurboDraw EZPRINT utility included 
        in this package. 

        WARNING:   Since  the TurboDraw Print option generates  a  binary 
        bit-image  dump  and the DOS "PRINT" command expects  ASCII-coded 
        characters,  you cannot use DOS "PRINT" to print TurboDraw  SPOOL 
        files.






                                       32




        EZPRINT has the following format:

             EZPRINT <filename> <devicename>

        For  example,  if the file name is SPOOL.0 and the device name is 
        LPT1, the command would be:

             EZPRINT SPOOL.0 LPT1

        To  send drawing output directly to a  device  (e.g.  PRN,  LPT1, 
        COM1,  or  other  custom-installed  devices supported  by  custom 
        drivers), type the device name at the prompt, and press the Enter 
        key.   Note  that if the target printer is connected to a  serial 
        port,  you  must  set  the proper baud rate using  the  DOS  MODE 
        command prior to loading TurboDraw.

        You can abort the Print command by pressing the Escape key or the 
        Ctrl-C combination.

































                                       33




        6.4.10 Plot

        The Plot option generates plotter commands and sends the commands 
        directly to a plotter or SPOOL file.

        A  convenient  feature of TurboDraw is  the  SPOOLing  capability 
        which  enables  you to direct drawing output to a file.   If  you 
        direct  output  to a file,  you can plot the drawing  at  a  more 
        convenient  time,  or  from a PC that is connected to the  proper 
        plotter.

        Ensure that the plotter is on line and set up properly before you 
        start to plot.

        When  you  select  Plot from the File submenu,  it  displays  the 
        following prompt:

             Device name: SPOOL.0

        You  can  accept  the default file  name  (SPOOL.0),  or  specify 
        another file name or device name. 

        To accept the default,  simply press Enter.   This action  causes 
        the drawing output to be written to the file named SPOOL.0.  

        To enter another file name, type the file name using standard DOS 
        file-naming conventions, and press Enter.  This action causes the 
        drawing  output  to  be  written  to  the  file  whose  name  you 
        specified.  

        To  plot  a  SPOOL file,  use any program that sends files  to  a 
        device (e.g.,  COPY,  PRINT,  EZPRINT,  etc.).  Since SPOOL files 
        contain  only "printable" ASCII codes,  you can use  any  program 
        that  sends  files to a device to plot them as in  the  following 
        examples.

                  COPY SPOOL.0 COM2

                  PRINT SPOOL.0
                  Name of List Device [PRN]: COM2

                  EZPRINT SPOOL.0 COM2
           
        To send drawing output directly to a device (e.g.  COM1, COM2, or 
        other  custom-installed  devices sup-ported by  custom  drivers), 
        simply  type the device name at the prompt,  and press the  Enter 
        key.

        To resolve plotting problems, refer to Appendix J.


                                       34




         
        6.4.11 Quit

        Quit  ABANDONS  the  current drawing and returns control  to  the 
        operating system.  

        WARNING:   This  option does NOT SAVE the current  drawing.   Use 
        this option only to ABORT.


        6.4.12 Exit

        Exit saves the current drawing to the file you originally  loaded 
        and returns control to the operating system.





































                                       35




        6.5 STYLE


        The  Style  submenu  allows you to set the font  size  (character 
        size),  line  spacing  and style,  and color  for  plotting.   An 
        asterisk  (*) to the immediate left of a submenu  item  indicates 
        the current selection. 



        6.5.1 Font Size
              
        You can select from three font (character) sizes:  small, medium, 
        and large.  The last-selected font size stays in effect until you 
        change it again.  

        * Small

             Character  cell size is .07" x .15",  which is equivalent to 
             14 CPI and 6.7 LPI.

        * Regular

             Character cell size is .12" x .25",  which is equivalent  to 
             8.3 CPI and 4 LPI.

        * Large

             Character  cell size is .2" x .3",  which is equivalent to 5 
             CPI and 3.3 LPI.

        Note  that these sizes are not compatible with the 10 CPI  and  6 
        LPI industry-standard  printer or typewriter character size.

        The  characters consist of built-in bit-mapped images and  cannot 
        be  enlarged  or reduced.   TurboDraw dynamically loads the  font 
        files (*.FNT) according to the type of display used.


        6.5.2 Line Type

        You  can  select from among  five  line  types:  Single,  Double, 
        Triple, Dotted, and Dashed.
          
        TurboDraw  uses the line type to construct symbols consisting  of 
        lines.  As with font size, the last-selected line type remains in 
        effect until you change it again.   




                                       36




        Note  that  the plotter driver does not support double or  triple 
        line  types,  and therefore draws these lines using single  solid 
        lines.


        6.5.3 Plotting with Colors

        You  can select a different color  for each object or  symbol  on 
        your  drawing through the Style submenu.   As with line type  and 
        font,  the last-selected color remains in effect until you select 
        another.  

        Note  that the colors are plotted only,  and do not appear on the 
        display.





































                                       37




        6.6 LIBRARY


        The  Library Submenu allows you to draw with user-defined symbols 
        contained in library files.   The default file name for the  file 
        containing  user-defined  symbols  is DRAW0.LBR.  You  can  build 
        additional  libraries or expand DRAW0.LBR  using the  information 
        in Appendix A.

        As  shipped,   DRAW0.LBR  contains  four  non-standard   symbols:  
        Organizational  chart  box,   Floppy  diskette,  Queue  structure 
        (FIFO), and Stack structure (LIFO).







































                                       38




        APPENDIX A: Building Library Files


        A.1 Elements, Objects, and Control Points

        The  element  is  the  most basic drawing  unit  that  EZCAD  can 
        produce.   All  drawings are built from command codes  describing 
        elements  which  EZCAD interprets.  Command codes with  values 0 
        through 20 are for elements. 

        An object or symbol  consists of a set of elements and is usually 
        a common symbol on a drawing.   For example,  a box consists of 4 
        lines (elements).  Objects are defined in the application program 
        or in libraries.

        Elements  are defined by control points.  For example,  a line is 
        defined by the starting and ending points.  These points form the 
        "descriptors"  for elements.  The descriptors also contain  style 
        and size information.


        A.2 Symbol Libraries

        A  symbol  library is not just a collection of lines  and  curves 
        that  you draw and save.  Instead,  it is a program written in  a 
        simple language consisting of single byte commands followed by 0, 
        1,   or  two-byte  operands,   which   EZCAD.COM  interprets  and 
        executes. You can write the program in straight-forward Assembler 
        syntax  and  assemble  it into  binary  code.  DRAW0.ASM  on  the 
        distribution  disk contains the source for DRAW0.LBR.   A summary 
        of available Assembler commands appears on the  next page.


        A.3 Using TBSYMB

        A  more  productive  way tªŒªûbrary file is  to  use  the 
        TBSYMB utility:

             1. Draw your symbols, save each symbol in one file.

             2. Exit TurboDraw

             3. Load your CRT driver (EGA, CGA or MGC)

             4. Load EZCAD

             5. Run TBSYMB

             6. Speficy Icon or Text menu.


                                       39





             7. Enter symbol file names, wild card is recommended.

             8. TBSYMB  will  continue to prompt for  symbol  file  names 
                until a single <Enter> is pressed as the reply.

             9. Specify how menu cells are organized.

             10. Enter  output  library  file name.  File  type  .LBR  is 
                 recommended

        A.4 EZCAD commands

        Mnemonic  Value     Function
        --------- -----     --------
        RETURN        0     End    of   object.     Put   all    elements                     
                            into database.
        LINE        1       Draw line from PNT1 to PNT2.
        OVAL        2       Draw  ellipse  using  PNT1 and  PNT2  as  the 
                            envelope.
        CURVE3      3       Draw curve through PNT1, PNT2, and PNT3.
        CURVE4      4       Draw curve starting at PNT1,  using imaginary 
                            line  formed by PNT1 and PNT2 as the  tangent 
                            vector,   and  ending  at  PNT4,   using  the 
                            imaginary line formed by PNT3 and PNT4 as the 
                            tangent vector at PNT4.
        ERASE       5       Blank a 16x16 bit area.
        DOT         6       Draw a solid dot with radius of .06" at PNT1.
        CIRCLE      7       Draw  a small circle with  radius of .04"  at 
                            PNT1.
        ARROW       8       Draw   an  arrow  head  at  PNT2  using   the  
                            imaginary   line formed  by PNT1 and PNT2  as 
                            the vector.
        BITMAP      9       Draw  a   24x36  bitmap  at   PNT1.    (Upper 
                            left corner of bitmap is aligned with PNT1).
        PRINTS     10       Draw ASCII string.
        POINT      11       Turn one dot (pixel) on at PNT1.
        HCIRCLE    12       Draw  half circle clockwise  (visually)  from 
                            PNT1 to PNT2.
        QCIRCLE    13       Draw quarter circle clockwise (visually) from 
                            PNT1 to PNT2.
        RBOXON     21       Form  rubber band box using PNT1 as the upper 
                            left  corner  and  PNT2 as  the  lower  right 
                            corner.
        RBOXOFF    22       Turn rubber band box off.
        RBNDON     23       Form rubber band line from PNT1 to PNT2.
        RBNDOFF    24       Turn rubber band line off.
        PNT1       25       Change  cursor  to crosshair  and  read  next 
                            location,  marked by the Select button,  into 


                                       40




                            PNT1.
        PNT2       26       Same as PNT1.
        PNT3       27       Same as PNT1.
        PNT4       28       Same as PNT1.
        PNT5       29       Same as PNT1.
        PNT6       30       Same as PNT1.
        PNT7       31       Same as PNT1.
        PNT8       32       Same as PNT1.
        MOV        33       Move word from operand 2 to operand 1.
        SWAP       34       Swap word operand 1 with operand 2.
        ADD        35       Add word operand 2 into operand 1.
        SUB        36       Subtract word operand 2 from operand 1.
        MUL        37       Multiply  word  operand  2  with  operand  1, 
                            leaving result in operand 1. 
        DIV        38       Divide  word operand 1 by operand 2,  leaving 
                            result in operand 1.
        AND        39       AND operand 2 into operand 1.
        OR         40       OR operand 2 into operand 1.
        NOT        41       Invert word operand.
        NEG        42       Negate word operand.
        SHFR       43       Arithmetic shift right word operand.
        SHFL       44       Shift left word operand.
        CONST      45       Define  word  operand  as the  CON  (used  as 
                            operand).
        MSG        46       Display message pointed to by word operand.
        TEXT       47       Draw text pointed to by word operand.
        ATTR       48       Define attribute contained in word operand.
        D2I        49       Convert dot coordinate contained in PNT1 to 
                            real (.01") coordinate.
        I2D        50       Convert   real  (.01")  coordinate   to   dot 
                            coordinate.




















                                       41




        SETPNT     51       Move word operand 2 into operand 1,  and move 
                            cursor to operand 1.
        TLINE      52       Draw  line  from operand 1 to operand  2.  As 
                            long as ABS(X1-X2) or ABS(Y1-Y2) is less than 
                            7 (pixels) the line is drawn as a vertical or 
                            a horizontal line.













































                                       42




        APPENDIX B: Drawing File Format


        The drawing file contains 16-byte records.  Each record  contains 
        information for one element, with the following two exceptions:

        * 4-point-curve

             This  element  requires four control points,  and  therefore 
             consists of two records.  PNT4 is located at offset 4 in the 
             second record.

        * Text string

             The text string can contain up to 256  bytes;  therefore,  a 
             text  string  can require up to 22      contiguous  records. 
             The extension flag in each      record indicates whether the 
             text string extends into the next record.   Text information 
             starts at offset 8 in the first record, and starts at offset 
             4 in the extended records.

             The record format for the remaining elements appears on  the 
             next page. Note that only the control points required by the 
             element  are  filled  in.   The  rest of  the  bytes  remain 
             undefined. 

        Offset    Size      Contents
        ------    ----      --------
          0       word      (Ignored)
          2       byte      Element code,  taking a value from 0  through 
                            20 as listed in Appendix A.
          3       byte      b7 : start of object flag
                            b6 : extension flag
                            b5-b3 : color
                            b2-b0 : line type or character size.
          4       word      PNT1, X
          6       word      PNT1, Y
          8       word      PNT2, X
         10       word      PNT2, Y
         12       word      PNT3, X
         14       word      PNT3, Y










                                       43




        APPENDIX C: Font File Format


        EZCAD  character  fonts are defined in special font  files  which 
        differ for each display or printer.   The number of dots required 
        by  each  character  cell for some standard  devices  are  listed 
        below. Note that the Epson printer, printing with a resolution of 
        120 dpi horizontal and 144 dpi vertical,  requires more dots than 
        any other device.

        The  size  of  a cell is actually larger than  the  character  to 
        provide  spacing between characters.  For example,  a 6 X 8  cell 
        contains a 5 X 7 character.

              Device        Small     Regular   Large
             -----------------------------------------
             MGC (12")      6 x 8    10 x 14   17 x 17
             CGA (13")      5 x 4     8 x 7    14 x 9
             EGA (14")      5 x 8     8 x 13   14 x 16
             IBM            8 x 10   14 x 18   24 x 21
             EPSON          8 x 21   14 x 36   24 x 43
             NEC            6 x 10   11 x 18   19 x 21
             OKIDATA        5 x 10    8 x 18   14 x 21
         

        All  characters of the same style occupy the same amount of space 
        in the font file.   Unused bits are zero-filled so that all cells 
        are of the same size regardless of the type of the device.   This 
        allows the font files to be accessed uniformly.


        Byte offset  Contents
        ----------------------------------------------------
           0 - 0A1F  144 8 x 18 small fonts, ASCII 20-AF
         A20 - 2BDF  144 16 x 30 regular fonts, ASCII 20-AF
        2BE0  3593  23 24 X 36 special symbols, ASCII B0C6
        3594 - 35B3  32 filler bytes
        35B4 - 7273  144 24 x 36 large fonts, ASCII 20-AF













                                       44




        APPENDIX F: TurboDraw Memory Layout


        The  DRAW.BAT  command file causes the following programs  to  be 
        loaded into memory.  When you exit TurboDraw, all programs except 
        the mouse driver are purged from the memory.

             1. Mouse driver

             2. Video driver

             3. Printer driver (optional)

             4. Plotter driver (optional)

             5. Drawing program (EZCAD)

             6. Application (TBDRAW)
                  Stack
                  Font
                  Drawing Area (virtual screen)
                  User Library
                  8K Bytes reserved for Library
                  Database

        The  application program (TBDRAW) is the last to be loaded and is 
        responsible  for providing the stack.  The memory space from  the 
        end of this program (which is also the end of stack area) to  the 
        end of memory (as reported by BIOS) is used for storing the draw-
        ing  and the database.  The order in which the drivers are loaded 
        is not important.

        TurboDraw uses two main data structures--the drawing area and the 
        database.

















                                       50




        * Drawing area

             This is a contiguous piece of memory used to store the image 
             of  the whole drawing as it appears on the screen.  Each bit 
             in this area corresponds to a pixel on the screen.  What you 
             see  on the screen is a small  section  of  this  area.  The 
             amount  of  memory used  depends on the type of display  and 
             the drawing size.

        * Database

             The  element descriptors are stored in  the  database.   The 
             database  is a linked list of 16-byte buffers which  extends 
             to the end of memory.

             When  TruboFlow  is terminated  or  aborted,  the  operating 
             system  purges  the  application (TBDRAW)  and  regains  all 
             memory used by the drawing area and the database area.

































                                       51




        APPENDIX G: Devices Supported by EZCAD


        Before discussing the devices supported by EZCAD, we will clarify 
        some  characteristics of the IBM asynchronous port (also known as 
        the serial port or RS-232 port,  designated as COM1 or COM2). The 
        asynchronous  port  on  the PC is  a  DTE  device.  That  is,  it 
        transmits  on  pin 2 and receives on pin 3.  To connect to a  DCE 
        device,  use a straight- through cable (pin 2 to pin 2,  pin 3 to 
        pin 3,  etc.).  To connect to another DTE device, cross pin 2 and 
        pin 3 (pin 2 to pin 3, pin 3 to pin 2). 

        Also,  for the port to transmit,  the CTS signal (pin 5) must  be 
        high;  for  the port to receive,  the DSR signal (pin 6) must  be 
        high.  The  DTR  signal  on  the PC (pin 20)  is  output  and  is 
        programmed high once initialized.


        G.1 Video Display

        MGC - Compatible  with  the  IBM monochrome display  adapter  and 
              monitor, but with all-dots-addressable graphics capability. 
              Not supported by  BIOS INT 10H.  It  has  more  dots on the 
              screen than both the CGA and the EGA.  It is also known  as 
              the  Hercules  monochrome graphics card,  or simply as  the 
              Hercules  card.  (Note  that Hercules  also  markets  color 
              graphics cards.)

        CGA - IBM Color Graphics Adapter.  It loses color capability when 
              used  in the high resolution all-dots-addressable  graphics 
              mode. Supported by BIOS and BASIC.

        EGA - IBM  Enhanced Graphics Adapter.  Delivers 16 colors even in 
              the graphics mode.  When treated as a CGA it  automatically 
              switches to the CGA mode.

        MCGA- Multi-Color  Graphics Array.  Built on the system board  of 
              the  PS/2  model 30.  Providing CGA compatibility  (in  CGA 
              mode, the MCGA doubles the number of scan lines, delivering 
              a sharper and much more pleasing image).











                                       52




        VGA - IBM Video-Graphics Array.  Built on the system board of the 
              PS/2 model 50,  60 and 80.  Compatible with the EGA and the 
              MCGA.   Providing  16  colors  in  the  highest  resolution 
              graphics mode.


               MGC      CGA      EGA      MCGA/CGA VGA/EGA
        ----------------------------------------------------
        Dots   720X348  640X200  640X350  640X400  640X350 
        Colors    2        2       16        2       16
        DPI     85X58    72X31    72X54    72X31    72X54


        Memory Requirement:

        Device    Min. (8" X 10.5")       Max. (32" X 21")
        ----------------------------------------------------
        MGC     48K bytes (640x609)   400K bytes (2688x1218)
        CGA     26K bytes (640x325)   184K bytes (2304x651)
        EGA     44K bytes (640x567)   319K bytes (2304x1134)
        EPSON  177K bytes (960x1512)  299K bytes (1620x1512)


        G.2 Printers

        EZCAD  supports  4  major  categories  of  printers:   EPSON/IBM, 
        NEC/TEC,  OKIDATA, and HP LaserJet and DeskJet. Most printers are 
        either  compatible  with,  or  emulate  at  least  one  of  these 
        categories.

        * IBM

             The IBM Graphics Printer is actually an EPSON printer. It is 
             emulated by almost all dot matrix printers. It is capable of 
             printing 240 dpi horizontally,  and 216 dpi vertically.  The 
             EZCAD IBM printer driver prints with a resolution of 120 dpi 
             by 72 dpi.

        * EPSON

             The  EZCAD EPSON printer driver prints with a resolution  of 
             120  dpi by 144 dpi.  Since it lacks the ability to  advance 
             the  paper in increments of 1/144",  the vertical  dot  gaps 
             (center-to-center) are 1/216",  2/216",  1/216",  and so on. 
             Delivers an average resolution of 144 dpi.






                                       53




        * EPSON 24-pin printer

             EPSON24 printer driver prints with a resolution of 120dpi by 
             180 dpi.

        * NEC

             Capable  of  printing  at 136 dpi horizontally and  144  dpi 
             vertically,   the   driver  delivers  96  dpi  and  72   dpi 
             respectively.

        * OKIDATA

             Prints  at 72 dpi horizontally and 72  dpi  vertically.  You 
             must set this printer to accept 8-bit data.

        * HP LaserJet and DeskJet

             Capable  of  printing  at 300 dpi horizontally and  300  dpi 
             vertically, the driver delivers 150 dpi in both directions.


        The  following table lists the dimensions of the  twelve  drawing 
        sizes supported by EZCAD.


        CODE   SIZE      10"           15"       ACTUAL SIZE
        ----------------------------------------------------
        A,A' 8.5"x11"  8x10.5         8x10.5        8"x10.5"
        B,B'  17"x11"  8x10.5(2)      8x10.5(2)    16"x10.5"
        C,C'  22"x17"  8x10.5(4)      8x10.5(4)    21"x16"
        D,D'  34"x22"  8x10.5(8)   10.7x10.5(6)    32"x21"
        E,E'  44"x34"  8x10.5(16)  10.7x10.5(12)   42"x32"
        W,W'  14"x11"   N/A        13.5x10.5     13.5"x10.5"


        G.3 Plotters

        * HP

             The  Hewlett-Packard HP/GL graphics language is emulated  by 
             other  plotter  manufacturers.   The  following  models  are 
             supported: 

             7090A,  7440A (ColorPro), 7470A, 7475A, 7510A, 7550A, 7570A, 
             7580A/B, 7585A/B, 7586B, 7595A, 7596A.

             The  DTE-DTE  cable must connect the DTR signal (pin 20)  on 
             each  end to the CTS (pin 5) and DSR (pin 6) signal  on  the 


                                       54




             other end.

        * HI

             The Houston Instruments DM/PL graphics language is  emulated 
             by  other  plotter manufacturers.  The following models  are 
             supported:

             PC595,    PC695A,   DMP29,   DMP40,   DMP41/42, 
             DMP51/52, DMP56C

             The  DTE-DTE  cable  must connect the DTR  signal  from  the 
             plotter (pin 5 on the RJ12 or pin 20 on the DB25  connector) 
             to the CTS signal on your PC (pin 5). In addition, pin 6 and 
             20  on      the PC should be wired together.  The  plotter's      
             operation manual should contain information for making  such 
             a cable.

        * Enter

             EZCAD  supports  the  Sweet-P 100  plotter,  which  is  also 
             marketed by COMREX as the ComScriber I plotter.

             The  Sweet-P  model 600 and model 1000 emulate  HP/GL.   The 
             Sweet-P model 1200 emulates DM/PL.

        * Comrex

             The ComScriber I plotter is supported.

        * Roland

             Compatible with HP/GL.

        * Zericon

             Emulates DMP41.














                                       55




        * Mural

             Emulates HP 7475A.

        * Western Graphtec

             Compatible  with  HP/GL.   EZCAD  does  not  support   GP/GL 
             (Graphtec Protocol / Graphics Language). 


        G.4 Mouse Devices and Digitizers

        EZCAD  supports  all mouse devices and digitizers.   Since  EZCAD 
        provides the driver,  you can use a low-cost Mouse Systems serial 
        mouse or compatible that comes without software.


        G.5 Non-standard Printer/Plotter Ports

        Standard  ports  and  semi-standard  COM3  and  COM4  ports   are 
        supported  at  the BIOS level.  Other custom installed ports  are 
        interfaced through DOS.





























                                       56




        APPENDIX H: TurboDraw Software Interrupts


        All  loaded  programs communicate with one another  via  software 
        interrupts. Interrupts X'60' to X'67' are either used or reserved 
        by  TurboDraw.  The EZCAD Interface Guide contained in the  EZCAD 
        Developer's  Package covers details about software  interface  to 
        these software interrupts.
             
             Interrupt      Interface to
                  
                60          EZCAD
                61          Video driver 
                62          Reserved
                63          Plotter
                64          Printer driver
                65          Reserved
                66          Reserved
                67          Used by video driver
































                                       57




        APPENDIX I: Coordinate System


        EZCAD  uses  a two-dimensional coordinate system with the  origin 
        (0,0) fixed at the upper left corner of the drawing.  The unit is 
        in inches.  The resolution is .01 inch. This coordinate system is 
        referred to as the "real coordinate system."

        The  real  coordinate  system is used by  the  database  and  for 
        displaying  on the screen only.  The rest of the system uses  the 
        dot  coordinate system which is in unit of screen  pixels.  EZCAD 
        performs the conversion internally. 







































                                       58




        APPENDIX J: Resolving Plotter Problems


        The   plotter   driver  sets  the  baud  rate,   cleans  up   the 
        communication link, and sets the timeout period to the maximum if 
        the plotter is connected to the RS-232 port.  

        Always reset the plotter before plotting,  regardless of  whether 
        you redirected output or are plotting directly to the device.

        If  you  have rebooted the computer for any reason  (by  powering 
        down or Ctrl-Alt-Del), the serial port is no longer set up.  This 
        situation is certain to cause problems when you attempt to send a 
        SPOOL  file  to the plotter.  In this the case,  run  the  EZMODE 
        utility to initialize the serial port. 

        EZMODE works exactly as the DOS command MODE, with one exception: 
        it  also  clears  any pending characters sent from  the  plotter. 
        Without  this  last step,  the Houston Instrument  plotters  will 
        probably not work.

        If  the targer plotter is connected to a serial  port,  TurboDraw 
        sets the serial port as follows:

             HP-GL plotters:  9600,N,8,1
             DM/PL plotters:  2400,N,7,2

        If you cannot set the plotter to the conditions shown  above,  or 
        if you have a "handshaking" or baud rate problem, direct the plot 
        to a SPOOL file, and use the following procedure to plot:

        1.   Reset  or power off/power on the plotter to set the  current 
             baud rate,  parity,  and number of stop bits to known values  
             (either the power-on default or dip-switch setting).

        2.   Use the EZMODE command to set the proper baud rate,  parity, 
             and number of stop bits for your computer.

        3.   Use the COPY,  PRINT,  or EZPRINT command to send your SPOOL 
             file to the plotter.











                                       59




        APPENDIX K: Resolving Printer Problems


        If   your  Okidata printer does not print  properly,   make  sure  
        that  your printer is setup to  accept  8-bit  data instead of 7-
        bit data. Note also that your COM port has to be setup to 
        handle 8-bit data.

        If  your  network OS does not intercept BIOS call,  you  need  to 
        redirect your printer output to a file,  and use the copy command 
        or  EZPRINT  utility to send that file over the  network  to  the 
        printer.

        Some  printers that are EPSON compatible are not 100% compatible. 
        Please send us a copy of the control codes of your printer and we 
        may  come  up  with a patch in our EPSON driver  to  handle  your 
        printer.


































                                       60




        APPENDIX L: Porting Drawings to DSP or WP


        Most   desktop publishing or drawing/painting programs support at 
        least one of the following file formats:

             1. PC-Paintbrush .PCX file

                  TurboDraw   can  save the drawing in .PCX file  format.  
                  The  resultant drawing  has the same resolution as your 
                  video  display.   Note  that TurboDraw cannot read .PCX 
                  files.

             2. Scanned Image TIFF file

                  The  .TIF file has a resolution of 150 dpi in both  the 
                  horizontal  or vertical direction.  The maximum drawing 
                  area that is written to the .TIF file is 14"X11".  Note 
                  that TurboDraw cannot read .TIF files.

             3. HP-GL plotter file

                  To  create  an  HP-GL file you  should  specify  an  HP 
                  plotter  even  if you do not have a plotter  when   you 
                  install  TurboDraw,  and  plot your drawing to  a  file 
                  which has a file name extension of .PLT.

























                                       61




        APPENDIX M: Modifying Text Fonts


             1. Make sure that you have backup copies of the font  files: 
                EGA.FNT, CGA.FNT and EPSON.FNT.

             2. Use  the FNTTXT utility to convert the desired font  file 
                to plain text file, for example, type

                FNTTXT EGA.FNT

                would  cause EGA.TXT be created in the same directory  as 
                EGA.FNT.  A portion of the text file is shown here:

                ;Medium font"A", ASCII 41H
                ................
                ................
                ...X............
                ..XXX...........
                .XX.XX..........
                XX...XX.........
                XX...XX.........
                XXXXXXX.........
                XX...XX.........
                XX...XX.........
                XX...XX.........
                ................
                ................
                ................
                ................
                ................
                ................
                ................
                ................
                ................
                ;Medium font"B", ASCII 42H
                ................
                ................
                XXXXXX..........
                .XX..XX.........
                .XX..XX.........
                .XX..XX.........
                .XXXXX..........
                .XX..XX.........
                .XX..XX.........
                .XX..XX.........
                XXXXXX..........
                ................
                ................


                                       62




                The  text  file  contains  comment lines which start with  
                a   ";"  and pattern  lines     which  consist   of  "." 
                and "X" characters.

             3. Use  your  editor/word processor to edit the  text  file. 
                Refer  to Appendix C for font file  format.   The   width  
                and    height of  each  character   cell  (pattern  lines 
                between  2  comment  lines) should not be changed.

             4. Then   use  the  TXTFNT utility to convert the text  file  
                back  to  the binary font file:

                TXTFNT EGA.TXT

             5. Once  the  .FNT file is verified,  the text file  can  be 
                deleted.

             6. Modify all font files.

        Note that TurboDraw supports ASCII 20H through 0AFH only.































                                       63




















                                       65