..pgno28
..foot63A7-##
..head02L-----------------------------------------------------------------
..head04L-----------------------------------------------------------------
..head03AbvSet1FhFontPtr
þ Display Adapters    [EGA] [MCGA] [VGA]

þ Source Module Name  b101120d.asm

þ Description

  Sets the Int 1Fh pointer to the user's font table. The table is
  used for character codes 80h-FFh in graphics modes 04H-06H.


þ Summary

  VOID FPENTRY bvSet1FhFontPtr( VOID *fonttbl );

  Parameter    Description
  ---------    -------------------------------------------------
  fonttbl      pointer to the font table


þ Remarks

  If this function is used at any other time than immediately
  after a set mode, the results will be unpredictable.
..page
..head03AbvSet43h8x14Font
þ Display Adapters    [EGA] [MCGA] [VGA]

þ Source Module Name  b101122d.asm

þ Description

  Sets the vector for Int 43h to point to the ROM BIOS default
  8x14 font and updates the video ROM BIOS data area.


þ Summary

  VOID FPENTRY bvSet43h8x14Font( INT2 spec, INT2 scnrows );

  Parameter    Description
  ---------    -------------------------------------------------
  spec         must be a value from 0-3 to specify the number of
               character rows on the screen.

               Specifier   Description
               ---------   -----------------------------
                  00       use value in scnrows variable
                  01       14 rows
                  02       25 rows
                  03       43 rows

  scnrows      number of rows per screen when spec(ifier) is
               zero.


þ Remarks

  If this function is used at any other time than immediately
  after a set mode, the results will be unpredictable.

  When this function is used on the MCGA, the BIOS substitutes
  function call bvSet43h8x16Font.
..page
..head03AbvSet43h8x16Font
þ Display Adapters    [MCGA] [VGA]

þ Source Module Name  b101124d.asm

þ Description

  Sets the vector for Int 43h to point to the ROM BIOS default
  8x16 font and updates the video ROM BIOS data area.


þ Summary

  VOID FPENTRY bvSet43h8x16Font( INT2 spec, INT2 scnrows );


  Parameter    Description
  ---------    -------------------------------------------------
  spec         must be a value from 0-3 to specify the number of
               character rows on the screen.

               Specifier   Description
               ---------   -----------------------------
                  00       use value in scnrows variable
                  01       14 rows
                  02       25 rows
                  03       43 rows

  scnrows      number of rows per screen when spec(ifier) is
               zero.


þ Remarks

  If this function is used at any other time than immediately
  after a set mode, the results will be unpredictable.
..page
..head03AbvSet43h8x8Font
þ Display Adapters    [EGA] [MCGA] [VGA]

þ Source Module Name  b101123d.asm

þ Description

  Sets the vector for Int 43h to point to the ROM BIOS default
  8x8 font and updates the video ROM BIOS data area.


þ Summary

  VOID FPENTRY bvSet43h8x8Font( INT2 spec, INT2 scnrows );


  Parameter    Description
  ---------    -------------------------------------------------
  spec         must be a value from 0-3 to specify the number of
               character rows on the screen.

               Specifier   Description
               ---------   -----------------------------
                  00       use value in scnrows variable
                  01       14 rows
                  02       25 rows
                  03       43 rows

  scnrows      number of rows per screen when spec(ifier) is
               zero.

þ Remarks

  If this function is used at any other time than immediately
  after a set mode, the results will be unpredictable.
..page
..head03AbvSet43hUsrFont
þ Display Adapters    [EGA] [MCGA] [VGA]

þ Source Module Name  b101121d.asm

þ Description

  Sets the vector for Int 43h to point to the user's font table
  and update the video ROM BIOS data area.

þ Summary

  VOID FPENTRY bvSet43hUsrFont( INT2 rows,     UINT2 points,
                                INT2 scnrows,  VOID  *fonttbl );

  Parameter    Description
  ---------    -------------------------------------------------
  rows         character rows specifier
  points       bytes per character
  scnrows      rows per screen
  fonttbl      pointer to the user font table


þ Remarks

  If this function is used at any other time than immediately
  after a set mode, the results will be unpredictable.
..page
..head03AbvSetAltPrtSc
þ Display Adapters    [EGA] [VGA]

þ Source Module Name  b101220d.asm

þ Description

  Selects an alternate print-screen routine for the EGA and VGA
  that works properly if the screen length is not 25 lines.


þ Summary

  VOID FPENTRY bvSetAltPrtSc( VOID );
..page
..head03AbvSetBlink
þ Display Adapters    [PCjr] [EGA] [MCGA] [VGA]

þ Source Module Name  b101003d.asm

þ Description

  Determines if the significate bit in an attribute will display
  either blinking or intensified.


þ Summary

  VOID FPENTRY bvSetBlink( INT2 *state );

  Parameter    Description
  ---------    -------------------------------------------------
  state        0 - enables intensity
               1 - enables blinking
..page
..head03AbvSetBlkSpec
þ Display Adapters    [EGA] [MCGA] [VGA]

þ Source Module Name  b101103d.asm

þ Description

  Determies character blocks selected by bit 3 of the character
  attribute bytes in alphanumeric display modes.


þ Summary

  VOID FPENTRY bvSetBlkSpec( INT2  block );

  Parameter    Description
  ---------    -------------------------------------------------
  block        select code for char generator block


þ Remarks






..page
..head03AbvSetBorder
þ Display Adapters    [PCjr] [EGA] [VGA]

þ Source Module Name  b101001d.asm

þ Description

  Controls the color of the screen border.


þ Summary

  VOID FPENTRY bvSetBorder( INT2 color );

  Parameter    Description
  ---------    -------------------------------------------------
  color        color of border
..page
..head03AbvSetColorPgMode
þ Display Adapters    [VGA]

þ Source Module Name  b101013d.asm

þ Description

  Sets paging mode for color registers


þ Summary

  VOID FPENTRY bvSetColorPgMode( INT2 pgstate );

  Parameter    Description
  ---------    -------------------------------------------------
  pgstate      00 - sets 4 pages of 64 registers
               01 - sets 16 pages of 16 registers


þ Remarks

  This function is invalid for graphics video mode 13H (320x200,
  256 colors).
..page
..head03AbvSetColorReg
þ Display Adapters    [MCGA] [VGA]

þ Source Module Name  b101010d.asm

þ Description

  Set red-green-blue values for a color register


þ Summary

  VOID FPENTRY bvSetColorReg( UINT2 colorreg, INT2 green,
                              INT2  blue,     INT2 red  );

  Parameter    Description
  ---------    -------------------------------------------------
  colorreg     color register
  green        green color value
  blue         blue color value
  red          red color value


þ Remarks

  When gray-scale summing is on, the gray-scale weighted values
  are calculated as described under the function bvSetGrayScale
  and stored into the components of the color register.
..page
..head03AbvSetColorRegBlk
þ Display Adapters    [MCGA] [VGA]

þ Source Module Name  b101012d.asm

þ Description

  Set a series of consecutive color registers.


þ Summary

  VOID FPENTRY bvSetColorRegBlk( UINT2 startreg
                                 INT2  regcount,
                                 BYTE  colortbl[][3] );

  Parameter    Description
  ---------    -------------------------------------------------
  startreg     first color register
  regcount     number of registers
  colortbl     color table that consists of 3 bytes for every
               register.  Each group of 3 bytes will specify the
               red, green, and blue values, respectively for the
               associated register.


þ Remarks

  When gray-scale summing is on, the gray-scale weighted values
  are calculated as described under the function bvSetGrayScale
  and stored into the components of the color register.
..page
..head03AbvSetColorRegPg
þ Display Adapters    [VGA]

þ Source Module Name  b101013d.asm

þ Description

  Set a color register page.


þ Summary

  VOID FPENTRY bvSetColorRegPg( INT2 pg );

  Parameter    Description
  ---------    -------------------------------------------------
  pg           color register page to select.

þ Remarks

  This function is invalid for graphics video mode 13H (320x200,
  256 colors).
..page
..head03AbvSetCurPos
þ Display Adapters    [MDA] [CGA] [PCjr] [EGA] [MCGA] [VGA]

þ Source Module Name  b100200d.asm

þ Description

  Sets cursor position for the selected page.


þ Summary

  VOID FPENTRY bvSetCurPos( INT2 pg, INT2 row, INT2 col );

  Parameter    Description
  ---------    -------------------------------------------------
  pg           page to set cursor position
  row          row (y coordinate)
  col          col (x coordinate)
..page
..head03AbvSetCurType
þ Display Adapters    [MDA] [CGA] [PCjr] [EGA] [MCGA] [VGA]

þ Source Module Name  b100100d.asm

þ Description

  Selects starting and ending scan lines for the cursor in text
  modes.


þ Summary

  VOID FPENTRY bvSetCurType( INT2 StScan, INT2 SpScan );

  Parameter    Description
  ---------    -------------------------------------------------
  StScan       starting scan line for cursor
  SpScan       ending scan line for cursor


þ Remarks

  In text modes, the hardware causes the cursor to blink, which
  cannot be disabled.  In graphics mode, the cursor is not
  available.

  The scan line ranges for the cursor are:

  Mode    Start    End
  ----    -----    ---
   7        0      12
  0-3       0       7

        0 ----+
        1     |
        2     |
        3     +---> Scan lines for a Color/Graphics display.
        4     |
        5     |
        6     |
        7 ----+

  In text modes 0-3 the EGA, MCGA, and VGA provide cursor
  emulation for the starting and ending scan lines.  The staring
  and ending values are remapped from an 8x8 cell to the true
  character cell dimension.

  One technique used to hide the cursor is by passing in the
  value 32 for the starting and ending scan lines.
..page
..head03AbvSetGrayScale
þ Display Adapters    [MCGA] [VGA]

þ Source Module Name  b10101bd.asm

þ Description

  Sets red, green and blue values of one or more color registers
  into the gray-scale equivalents.


þ Summary

  VOID FPENTRY bvSetGrayScale( UINT2 startreg, INT2  regcount );

  Parameter    Description
  ---------    -------------------------------------------------
  startreg     first color register
  regcount     number of registers


þ Remarks

  For the range of color registers specified, each register is
  read and each new color value is calculated as 30% red + 59%
  green + 11% blue.
..page
..head03AbvSetMode
þ Display Adapters    [MDA] [CGA] [PCjr] [EGA] [MCGA] [VGA]

þ Source Module Name  b1000xxd.asm

þ Description

  Set video display mode.


þ Summary

  VOID FPENTRY bvSetMode( UINT mode, UINT clear );

  Parameter    Description
  ---------    -------------------------------------------------
  mode         video mode to set
  clear        0 - clear display buffer for new mode.
               1 - do not clear display buffer for new mode. This
                   parameter is ignored on PC's and PC/XT's with
                   a cga or monochrome display adapter.


þ Remarks

  The video modes applicable for the various video adapters
  are as follows:

                           Text/
  Mode Resolution  Colors  Graphics  MDA CGA PCjr EGA MCGA VGA
  00h  40x25         16    text           .   .    .   .    .
  01   40x25         16    text           .   .    .   .    .
  02   80x25         16    text           .   .    .   .    .
  03   80x25         16    text           .   .    .   .    .
  04   320x200        4    graphics       .   .    .   .    .
  05   320x200        4    graphics       .   .    .   .    .
  06   640x200        2    graphics       .   .    .   .    .
  07   80x25          2*   text       ù            .        .
  08   160x200       16    graphics           .
  09   320x200       16    graphics           .
  0A   640x200        4    graphics           .
..page
                             Text/
  Mode Resolution  Colors  Graphics  MDA CGA PCjr EGA MCGA VGA
  0B   reserved
  0C   reserved
  0D   320x200       16    graphics                .        .
  0E   640x200       16    graphics                .        .
  0F   640x350        2*   graphics                .**      .
  10   640x350        4    graphics                .***
  10   640x350       16    graphics                .        .
  11   640x480        2    graphics                    .    .
  12   640x480       16    graphics                         .
  13   320x200      256    graphics                    .    .

  *   Monochrome monitor only.
  **  EGA with 64 KB of RAM.
  *** EGA with 128 KB or more of RAM.

  On the PC/AT, PCjr, and PS/2, if the "clear" parameter is
  set, the display buffer is not cleared when a new mode is
  selected.  This capability is only available on PC or PC/XT
  when an EGA or VGA adapter is installed.
..page
..head03AbvSetPage
þ Display Adapters    [MDA] [CGA] [PCjr] [EGA] [MCGA] [VGA]

þ Source Module Name  b100500d.asm

þ Description

  Select active display page


þ Summary

  VOID FPENTRY bvSetPage( INT2 pg );

  Parameter    Description
  ---------    -------------------------------------------------
  pg           page to select.
..page
..head03AbvSetPalBorder
þ Display Adapters    [PCjr] [EGA] [VGA]

þ Source Module Name  b101002d.asm

þ Description

  Sets palette registers and border color


þ Summary

  VOID FPENTRY bvSetPalBorder( CHAR list[17] );

  Parameter    Description
  ---------    -------------------------------------------------
  list         Bytes 0-15 are the color values to be loaded into
               the appropriate palette registers.  Byte 16 is
               stored in the border color register.
..page
..head03AbvSetPalReg
þ Display Adapters    [PCjr] [EGA] [MCGA] [VGA]

þ Source Module Name  b101000d.asm

þ Description

  Sets appropriate palette register to a displayable color.


þ Summary

  VOID FPENTRY bvSetPalReg( INT2 color, INT2 reg );

  Parameter    Description
  ---------    -------------------------------------------------
  color        color value
  reg          palette register


þ Remarks

  For MCGA the color must be 07h and the reg variable must
  be 012h.
..page
..head03AbvSetScanLines
þ Display Adapters    [VGA]

þ Source Module Name  b101230d.asm

þ Description

  Selects the number of scan lines for text modes. The selected
  value takes effect the next time the bvSetMode function is
  called to select the display mode.


þ Summary

  INT2 FPENTRY bvSetScanLines( INT2 scancode );


  Parameter    Description
  ---------    -------------------------------------------------
  scancode     0 - 200 scan lines
               1 - 350 scan lines
               2 - 400 scan lines

þ Function Return Value

  18 - VGA is active
  00 - VGA is not active
..page
..head03AbvSetState0B
þ Display Adapters    [CGA] [PCjr] [EGA] [MCGA] [VGA]

þ Source Module Name  b100b00d.asm

þ Description

  Text mode the border color is set. Graphics mode sets the
  border and background color.


þ Summary

  VOID FPENTRY bvSetState0B( INT2 color );

  Parameter    Description
  ---------    -------------------------------------------------
  color        color to set background, border
..page
..head03AbvSwDsp
þ Display Adapters    [VGA]

þ Source Module Name  b101235d.asm

þ Description

  Allows selection of one of two video adapters in the system,
  when memory usage or port addresses conflict between the two
  adapters.


þ Summary

  UINT FPENTRY bvSwDsp( INT2 setting, CHAR *buffer );

  Parameter    Description
  ---------    -------------------------------------------------
  setting      0 - disable initial video adapter
               1 - enable system board video adapter
               2 - disable active video adapter
               3 - enable inactive video adapter
  buffer       128-byte buffer to use if setting is 1, 2, or 3.


þ Function Return Value

  18 - Function is supported.

  If the function is called with setting set to 0 or 2 then the
  video adapter state information is stored in the buffer
  variable.  If the function is called with setting set to 3 then
  the information in the buffer variable will be used to restore
  the video adapter state.
..page
..head03AbvVioAccess
þ Display Adapters    [MCGA] [VGA]

þ Source Module Name  b101232d.asm

þ Description

  Enables or disables CPU access to the video adapter's I/O prts
  and video refresh buffer.


þ Summary

  INT2 FPENTRY bvVioAccess( INT2 setting );

  Parameter    Description
  ---------    -------------------------------------------------
  setting      0 - enables access
               1 - disable access


þ Function Return Value

  18 - Function is supported.
..page
..head03AbvWrtNCell
þ Display Adapters    [MDA] [CGA] [PCjr] [EGA] [MCGA] [VGA]

þ Source Module Name  b100900d.asm
þ Description

  Write a character and attribute to the display at the current
  cursor position for n times.


þ Summary

  VOID FPENTRY bvWrtNCell( INT2 ch,    INT2 attr,
                           INT2 count, INT2 pg   );

  Parameter    Description
  ---------    -------------------------------------------------
  ch           character
  attr         attribute
  count        number of cells to replication
  pg           page to write cell to


þ Remarks

  The cursor position is not updated are the character attribute
  values are displayed.

  In graphics mode the replication factor given in count will
  display character attribute combinations only for the current
  row.

  All characters will display something, including the bell,
  backspace, carriage return and the line feed.  These control
  characters are NOT recognized as special characters and will
  not affect the cursor position.

  The character definition tables is stored in the vector for the
  bvSet43hxxxxFont functions for the EGA, MCGA and VGA displays
  inn graphics modes.
..page
..head03AbvWrtNChar
þ Display Adapters    [MDA] [CGA] [PCjr] [EGA] [MCGA] [VGA]

þ Source Module Name  b100a00d.asm

þ Description

  Write a character to the display at the
  current cursor position for n times.


þ Summary

  VOID FPENTRY bvWrtNChar( INT2 ch, INT2 count, INT2 pg );

  Parameter    Description
  ---------    -------------------------------------------------
  ch           character
  count        number of cells to replication
  pg           page to write cell to
..page
..head03AbvWrtPix
þ Display Adapters    [MDA] [CGA] [PCjr] [EGA] [MCGA] [VGA]

þ Source Module Name  b100c00d.asm

þ Description

  Display pixel at the specified graphics coordinates


þ Summary

  VOID FPENTRY bvWrtPix( INT2 row,    INT2 col,
                         INT2 pixval, INT2 pg  );

  Parameter    Description
  ---------    -------------------------------------------------
  row          row for pixel to be displayed on
  col          col for pixel to be displayed on
  pixval       color of pixel
  pg           page to display pixel on
..page
..head03AbvWrtTTYChar
þ Display Adapters    [MDA] [CGA] [PCjr] [EGA] [MCGA] [VGA]

þ Source Module Name  b100e00d.asm

þ Description

  Write character at the current cursor position using
  the color speicifed (if in graphics mode).


þ Summary

  VOID FPENTRY bvWrtTTYChar( INT2 ch, INT2 pg, INT2 color );

  Parameter    Description
  ---------    -------------------------------------------------
  ch           character to display
  pg           page to display the character on
  color        color of character if in graphics mode
..page
..head03AbvWrtTTYStr
þ Display Adapters    [MDA] [CGA] [PCjr] [EGA] [MCGA] [VGA]

þ Source Module Name  b1013xxd.asm

þ Description

  Displays a string to the video buffer starting
  at the specified location.

þ Summary

  VOID FPENTRY bvWrtTTYStr( INT2 mode, INT2 row, INT2 col,
                            INT2 len,  INT2 pg,  INT2 attr,
                            CHAR *st );

  Parameter    Description
  ---------    -------------------------------------------------
  mode         0 - use attr, st is chars only, cursor not updated
               1 - use attr, st is chars only, cursor updated
               2 - st is char, attr; cursor not updated
               3 - st is char, attr; cursor updated
  row          y coordinate
  col          x coordinate
  len          length of st
  pg           display page to display string on.
  attr         attribute is mode is 0 or 1
  st           string to display on the screen
..page