E
     Unicorn Library Documentation  3.1                         page 48

     __________________________________________________________________

                               ellipser
F
     Plots an ellipse on the graphics screen.  The ellipse may be
     rotated in 6 degree increments from 0 to 90 degrees.  To obtain
     full 360 degree rotation the major axis may be defined as either
     x or y with rotation.



     Call:   ellipser(xc, yc, rotate, r1, r2, color);

             xc      =  column coordinate of center
             yc      =  row coordinate of center
             rotate  =  angle of rotation (0, 6, 12, 18 etc.)
             r1      =  half the distance along the x-axis (columns)
             r2      =  half the distance along the y axis (rows)
             color   =  color of the ellipse



     Example:    main()
                 {
                   sm(4);  /*  set graphics mode  */

                   /* draw an ellipse in color 2 rotated 48 degrees */

                   ellipser(100,100,48, 50, 80, 2);
                 }



Unicorn 1 Documentation  3.1                                      page 49

__________________________________________________________________________


                               equipchk


Returns an integer idicative of the equipment contained on the PC.  The
number may be interpreted as follows:

bit 0           -  diskette installed
bit 1           -  not used
bit 2, 3        -  always 11
bit 4, 5        -  initial video mode
                     01  =  40 x 25 BW
                     10  =  80 x 25 BW
bit 6, 7        -  number of diskette drives ( only if bit 0 = 1)
                     00 = 1
                     01 = 2
bit 8           -  0 = dma present
                   1 = no dma on system
bit 9, 10, 11   -  number of RS-232 cards installed
bit 12          -  game I/O attached
bit 13          -  not used
bit 14, 15      -  number of printers



Call:         equipchk();


Example:      main()
              {
                 equipchk();  /* get current equipment status */
              }




E
     Unicorn Library Documentation  3.1                         page 50

     __________________________________________________________________

                               flagdec
F

    Decrements the mouse cursor flag.  If the flag is greater than or equal
    to zero the cursor is visible, if 0 or less then the cursor is not
    visible.


   Call:  flagdec();


   Example:
            main();
            {
              mreset();
              flagdec();
            }





E
     Unicorn Library Documentation  3.1                         page 51

     ___________________________________________________________________
                               flaginc
F

    Increments the mouse cursor flag.  If the flag is greater than or equal
    to zero the cursor is visible, if 0 or less then the cursor is not
    visible.


   Call:  flaginc();


   Example:
            main();
            {
              mreset();  /* sets cursor flag to -1 */
              flaginc(); /* now cursor is visible */
            }





E
     Unicorn Library Documentation  3.1                         page 52

     __________________________________________________________________

                               forward
F
     Moves the turtle (turtle graphics) in its current direction by a
     specified distance.  The distance is measured in pixels.




     Call:   forward(pixels);

             pixels  =  number of pixels to move in current direction




     Example:    main()
                 {
                    sm(4);  /* set graphics mode */
                    pendown();  /* set pen down on screen to draw */
                    forward(50);  /* move forward 50 pixels */
                 }




E
     Unicorn Library Documentation  3.1                         page 53

     __________________________________________________________________

                              GAL_LT
F
    This macro converts gallons to liters.


    Call:   GAL_LT(gallons);



    Example:
             main()
             {
                printf("%lf gallons is %lf liters\n", 4.5, GAL_LT(4.5));
             }



E
     Unicorn 1 Documentation  3.1                               page 54

     _____________________________________________________________________


F                               gcomtype


    Returns a ROM byte indicating what type of computer is in use.


    Call:
          gcomtype();


    Example:
              main()
              {
                 printf("%d", gcomtype());
              }

E
     Unicorn 1 Documentation  3.1                                  page 55

     _____________________________________________________________________


F                               gcurpos

     A C bios call to get the current cursor position.  This is similar to
     the assembly language call getcurp.  By examining both you will see
     how to implement both types of functions.


     Call:  gcurpos(row, column, page);

     Where:
            row     =  the current cursor row
            column  =  the current cursor column
            page    =  the current cursor page

     Example:
              main()
              {
                  int row, column, page;

                  gcurpos(row, column, page);
              }

      The values are placed into the variables.




E
     Unicorn 1 Documentation  3.1                                  page 56

     _____________________________________________________________________


F                               getbcnt


     Returns the count of button presses.


     Call:   getbcnt(which);

     Where:
             which = 0 for left button count or
                     1 for right button count


     Example:

         main()
         {
            printf("There haas been a total of %d left presses", getbcnt(0));
         }





E
     Unicorn 1 Documentation  3.1                                  page 57

     _____________________________________________________________________


F                               getrbcnt


     Returns the count of button releases.


     Call:   getbrcnt(which);

     Where:
             which = 0 for left button count or
                     1 for right button count


     Example:

       main()
       {
          printf("There haas been a total of %d left releases", getbrcnt(0));
       }




E
Unicorn 1 Documentation  3.1                                      page 58

__________________________________________________________________________


F                               getbstat

     Returns the current mouse button status.  The return is is follows:
     0 - no button is pressed
     1 - left button is pressed
     2 - right button is pressed
     3 - both buttons are pressed


     Call:  getbstat();

     Example:
              main();
              {
                 if (getbstat == 0)
                    printf("No mouse button is pressed");
                 if (getbstat == 1)
                    printf("The left button is pressed");
                 if (getbstat == 2)
                    printf("The right button is pressed");
                 if (getbstat == 3)
                    printf("Both buttons are pressed");
               }



E
Unicorn 1 Documentation  3.1                                      page 59

__________________________________________________________________________


F                               getchne

Get a character from the standard input with no echo.





Call:         getchne();






Example:      main()
              {
                 int a;
                 a = getchne(); /* return a character in a with no echo */
              }




Unicorn 1 Documentation  3.1                                      page 60

__________________________________________________________________________

                               getctype


Returns an integer indicating the type of IBM-PC.

return:
       FFh  =  Original IBM-PC
       FEh  =  PC XT, portable PC or PC with revised system board
       FDh  =  PCjr
       FCh  =  PC-AT



Call:         getctype();



Example:      main()
              {
                 int a;
                 a = getctype();  /* find what type of machine it is */
                 if (a==255)
                   printf("This is an original IBM-PC");
              }




E
     Unicorn Library Documentation  3.1                         page 61

     __________________________________________________________________

                               getcurp

F     This returns the current position of the cursor on the screen in
     row, column format.




     Call:    getcurp(&row, &column);

              row     =  the current cursor row position
              column  =  the current cursor column position



     Example:   main()
                {
                   getcurp(row, column);
                }





E
Unicorn 1 Documentation  3.1                                      page 62

__________________________________________________________________________


F                               getdmaj


    Returns the DOS major version.  If using DOS 3.2 this will return 3.

    Call:  getdmaj();


    Example:
            main()
            {
               printf("The DOS major version is %d\n", getdmaj());
             }






E
Unicorn 1 Documentation  3.1                                      page 63

__________________________________________________________________________


F                               getdmin


    Returns the DOS minor version.  If using DOS 3.2 this will return 2.

    Call:  getdmin();


    Example:
            main()
            {
               printf("The DOS minor version is %d\n", getdmin());
             }







E
Unicorn 1 Documentation  3.1                                      page 64

__________________________________________________________________________


F                               getdver


    Returns the DOS version.  If using DOS 3.2 this will return 3.2.

    Call:  getdver();


    Example:
            main()
            {
               printf("The DOS version is %d\n", getdver());
             }






E
Unicorn 1 Documentation  3.1                                      page 65

__________________________________________________________________________


F                               gethpos

    Returns an integer value for the mouse cursor's current horizontal
    position.  It must be within the current virtual screen limits.


    Call:  gethpos();


    Example:
             main()
             {
                 printf("The mouse's horizontal position is %d", gethpos());
             }








E
Unicorn 1 Documentation  3.1                                      page 66

__________________________________________________________________________


F                               getkey

    Returns the ASCII code for a keypress.  If no key is available it
    will wait until a key is pressed.



    Call:  getkey();


    Example:
            main()
            {
               printf("The ASCII code is %d", getkey());
            }



E
Unicorn 1 Documentation  3.1                                      page 67

__________________________________________________________________________


F                               getkeycd

    Returns the ASCII code for a keypress.  If no key is available it
    will wait until a key is pressed.



    Call:  getkeycd();


    Example:
            main()
            {
               printf("The ASCII code is %d", getkeycd());
            }




E
Unicorn 1 Documentation  3.1                                      page 68

__________________________________________________________________________


F                               getscode

    Returns the scan code for a keypress.  If no key is available it
    will wait until a key is pressed.



    Call:  getscode();


    Example:
            main()
            {
               printf("The scan code is %d", getscode());
            }




E
Unicorn 1 Documentation  3.1                                      page 69

__________________________________________________________________________


F                               getstate

    Returns the current video mode.



    Call:  getstate();


    Example:
            main()
            {
               printf("The video mode is %d", getstate());
            }




E
Unicorn 1 Documentation  3.1                                      page 70

__________________________________________________________________________


F                               getvpos

    Returns the current mouse cursor vertical position.



    Call:  getvpos();


    Example:
            main()
            {
               printf("The mouse vertical position is %d", getvpos());
            }




E
Unicorn 1 Documentation  3.1                                      page 71

__________________________________________________________________________


F                               get_page

    Returns the current video page.



    Call:  get_page();


    Example:
            main()
            {
               printf("The video page is %d", get_page());
            }




E
Unicorn 1 Documentation  3.1                                      page 72

__________________________________________________________________________

                               gliss
F

Produces a sliding sound or glissando using the IBM mode of sound
production.




Call:         gliss(beg, end, rate);

              beg  = starting frequency
              end  = ending frequency
              rate = rate of increase/decrease.  a larger rate slows it down




Example:      main()
              {
                 gliss(300, 2000, 1); /* rapid slide from 300 to 2000 cycles*/
                 gliss(2000, 300, 10); /* slower slide down from 2000 to
                                          300 cycles */
              }





E
Unicorn 1 Documentation  3.1                                      page 73

__________________________________________________________________________


F                               GM_OZ

    Returns the number of ounces in a given numbe of grams.



    Call:  GM_OZ(grams);

    Where:
          grams = grams to convert to ounces.

    Example:
            main()
            {
               printf("There are %d ounces in %d grams", GM_OZ(56.9), 56.9);
            }



E
     Unicorn Library Documentation  3.1                         page 74

     __________________________________________________________________

                               gothic

F     Displays Gothic characters on the graphics screen.  All characters
     are displayed in a 16 pixel wide by 20 pixel high matrix.



     Call:   gothic(char, ulc, ulr, color);

             char   =  character to print
             ulc    =  upper left corner column
             ulr    =  upper left corner row
             color  =  color of the character





     Example:   main()
                {
                  sm(4);   /*  set graphics mode */

                  /*  print a gothic W at 20, 30 in color 3 */

                  gothic('W', 20, 30, 3);
                }





E
     Unicorn Library Documentation  3.1                         page 75

     ___________________________________________________________________

                              hollow
F
     This function prints outline characters on the graphics screen.  The
     characters are defined in a 16 column by 30 row pixel matrix.



     Call:    hollow(char, ulc, ulr, color);

             char   =  character to print
             ulc    =  upper left corner column
             ulr    =  upper left corner row
             color  =  color of the character





     Example:   main()
                {
                  sm(4);   /*  set graphics mode */

                  /*  print an outline W at 20, 30 in color 3 */

                  hollow('W', 20, 30, 3);
                }




E
     Unicorn Library Documentation  3.1                         page 76

     ___________________________________________________________________

                              INCH_CM
F
    Converts inches to centimenters.  Implemented as a macro in UC.H.








     Call:   INCH_CM(inches);

     Where:
             inches  = number of inches to convert to cm.






     Example:
             main()
             {
                printf("There are %d cm in %d inches", INCH_CM(5.6), 5.6);
             }




E
     Unicorn Library Documentation  3.1                         page 77

     __________________________________________________________________

                              indexch

F     Returns the position of a character withing a string.





     Call:   indexch(str, ch);

             str  =  string to be searched
             ch   =  character to search for



     Example:    main()
                 {
                     /*  find the position of the character 'i' */
                     /*  should return a 2 */
                     indexch("This is a test", 'i');
                 }




E
     Unicorn Library Documentation  3.1                         page 78

     __________________________________________________________________

                              indexr

F     Returns the rightmost position of a character in a given string.
     Returns -1 if the character is not found in the string.






     Call:   indexr(str, ch);

             str  =  string to be searched
             ch   =  character to search for




     Example:    main()
                 {
                    /* find the rightmost poistion of 'i' in "this is a
                       test".  Should return 5  */
                    indexr("This is a test", 'i');
                 }





E
     Unicorn Library Documentation  3.1                         page 79

     ___________________________________________________________________

                               iskey
F

    Returns non-zero if there is a key waiting in the keyboard buffer.
    If there is no key it returns 0.






     Call:   iskey();



     Example:     main()
                  {
                    printf("%d", iskey());
                  }





E
     Unicorn Library Documentation  3.1                         page 80

     ___________________________________________________________________

                               kbstat
F

     Returns the keyboard status byte.





     Call:   kbstat();



     Example:     main()
                  {
                    printf("The keyboard status is%d", kbstat());
                  }






E
     Unicorn Library Documentation  3.1                         page 81

     ___________________________________________________________________

                               keystat
F

     Returns the keyboard status byte.

     bit 0 - right shift
     bit 1 - left shift
     bit 2 - ctrl
     bit 3 - alt
     bit 4 - scroll lock
     bit 5 - num lock
     bit 6 - caps lock
     bit 7 - insert


     Call:   keystat();



     Example:     main()
                  {
                    printf("The keyboard status is%d", keystat());
                  }




E
     Unicorn Library Documentation  3.1                         page 82

     ___________________________________________________________________

                               KG_LB
F

     Converts kilograms to pounds.

     Call:   KG_LB(kilograms);

     Where:  kilograms  = the number of kilograms to convert to pounds.



     Example:
           main()
           {
             printf("There are %d pounds in %d kilograms", KG_LB(5.6), 5.6);
           }




E
     Unicorn Library Documentation  3.1                         page 83

     ___________________________________________________________________

                               LB_KG
F

     Converts pounds to kilograms.

     Call:   LB_KG(pounds);

     Where:  pounds = the number of pounds to convert to kilograms.



     Example:
           main()
           {
             printf("There are %d kilograms in %d pounds", LB_KG(5.6), 5.6);
           }





E
     Unicorn Library Documentation  3.1                         page 84

     ___________________________________________________________________

                               lhjoystk
F

     Returns the current left horixontal position for the joystick.

     Call:   lhjoystk();



     Example:
           main()
           {
              printf("The left horizontal position is %d", lhjoystk());
           }





E
     Unicorn Library Documentation  3.1                         page 85

     ___________________________________________________________________

                               lightpen
F

     Returns the current position of the lightpen.

     Call:   lightpen(&row, &column, &ras_line, &ras_col);

     Where:
          row      =  The current text row
          column   =  The current text column
          ras_line =  the current graphics raster line row
          ras_col  =  the current graphics raster column


     Example:
           main()
           { int row, col, ras_line, ras_col;
                  /* place lightpen position into the above variables */
             lightpen(&row, &col, &ras_line, &ras_col);
           }




E
     Unicorn Library Documentation  3.1                         page 86

     __________________________________________________________________

                               line

F     Draws a line on the graphics screen given the two endpoints and
     the color.




     Call:    line(x1, y1, x2, y2, color);

              x1, y1  =  end point coordinates
              x2, y2  =  second end point coordinates
              color   =  color of the line


     Example:   main()
                {
                   sm(4);  /*  set the graphics mode  */

                   /*  draw a line in color 3 from 30,50 to 180, 140 */

                   line(30,50,180,140,3);
                }



E
     Unicorn Library Documentation  3.1                         page 87

     __________________________________________________________________

                               locate

F     Returns the color of a pixel on the graphics screen.




     Call:  variable = locate(row, column);

            variable  =  the return variable
            row       =  the row of the pixel
            column    =  the column of the pixel




     Example:   main()
                {
                   int a;
                   sm(4);  /*  set graphics mode  */

                   /* find the color of the pixel located at 100, 110 */
                   a = locate(100,110);
                   /* print it out */
                   printf("The color of the pixel at 100, 110 is %d\n", a);
                }



Unicorn 1 Documentation  3.1                                      page 88

__________________________________________________________________________

                               lprintf


Send a string to line printer 1.





Call:         lprintf(string);

              string = a pointer to string to be printed on printer




Example:      main()
              {
                 lprintf("This is a test"); /* send string to printer */
              }




Unicorn 1 Documentation  3.1                                      page 89

__________________________________________________________________________


                              lputch


This function prints a single character to the printer.  It is limited to
supporting only line printer #1.



Call:         lputch(char);

              char  =  the character to be printed.

Return:       printer status
                 bit 0 = timeout occurred
                 bit 1 = [unused]
                 bit 2 = [unused]
                 bit 3 = I/O error
                 bit 4 = selected
                 bit 5 = out of paper
                 bit 6 = acknowledge
                 bit 7 = not busy


Example:      main()
              {
                 char a;

                 a = 'x';
                 lputch(a);      /* print the letter 'x' on the printer */
                                 /*  at the current print head location */
              }




E
     Unicorn Library Documentation  3.1                         page 90

     ___________________________________________________________________

                               lsthpos
F

     Returns the last horizontal position when a button was pressed.

     Call: lsthpos(which);

     Where:
            which = 0 for last left button press
                    1 for last right button press

     Example:

  main()
  {
    printf("The position was %d on the last left button press", lsthpos(0));
  }




E
     Unicorn Library Documentation  3.1                         page 91

     ___________________________________________________________________

                               lsthrpos
F

     Returns the last horizontal position when a button was released.

     Call: lsthrpos(which);

     Where:
            which = 0 for last left button press
                    1 for last right button press

     Example:

        main()
        {
          printf("The position was %d on the last");
          printf(" left button release", lsthrpos(0));
        }




E
     Unicorn Library Documentation  3.1                         page 92

     ___________________________________________________________________

                               lstvpos
F

     Returns the last vertical position when a button was pressed.

     Call: lstvpos(which);

     Where:
            which = 0 for last left button press
                    1 for last right button press

     Example:

        main()
        {
          printf("The position was %d on the last");
          printf(" left button press", lstvpos(0));
        }




E
     Unicorn Library Documentation  3.1                         page 93

     ___________________________________________________________________

                               lstvrpos
F

     Returns the last vertical position when a button was released.

     Call: lstvrpos(which);

     Where:
            which = 0 for last left button press
                    1 for last right button press

     Example:

        main()
        {
          printf("The position was %d on the last");
          printf(" left button release", lstvrpos(0));
        }




E
     Unicorn Library Documentation  3.1                         page 94

     ___________________________________________________________________

                               LT_GAL
F

     Converts liters to gallons.  Defined as a macro in UC.H.

     Call: LT_GAL(liters);


     Example:

        main()
        {
          printf("There are %lf gallons in %lf liters", LT_GAL(67.8), 67.8);
        }




E
     Unicorn Library Documentation  3.1                         page 95

     ___________________________________________________________________

                               lvjoystk
F

     Returns the left vertical position of the joystick.


     Call: lvjoystk();


     Example:

        main()
        {
          printf("The joystick vertical position is %d", lvjoystk());
        }




Unicorn 1 Documentation  3.1                                      page 96

__________________________________________________________________________


                              memsize


Returns an integer containing the number of kilobytes of memory installed.




Call:         memsize();






Example:      main()
              {
                 int a;
                 a = memsize(); /* get kilobytes of memory */
              }




E
     Unicorn Library Documentation  3.1                         page 97

     ___________________________________________________________________

                               mgun
F

     Produces a popping machine gun type sound.

     Call: mgun();


     Example:

        main()
        {
          mgun();
        }




E
     Unicorn Library Documentation  3.1                         page 98

     __________________________________________________________________

                               moveto

F     Moves the turtle pen to an absolute pixel location without
     drawing.





     Call:   moveto(col, row);

             col  =  the new column coordinate
             row  =  the new row coordinate



     Example:   main()
                {
                   sm(4);  /* set the graphics mode  */

                   /*  move the turtle pen to 100, 30 */
                   moveto(100, 30);
                 }




E
     Unicorn Library Documentation  3.1                         page 99

     ___________________________________________________________________

                               mreset
F

     Checks to see if the mouse driver is installed.  Returns 0 if NOT
     installed or -1 if mouse IS installed.

     Call: mreset();


     Example:

        main()
        {
           if (mreset() == 0)
              then printf("There is no mouse installed - Boo-Hoo!");
           else printf("Hooray, the mouse is present!");
        }




E
     Unicorn Library Documentation  3.1                         page 100

     __________________________________________________________________

                              msize

     Returns the current memory size in kilobytes.


F


     Call:   msize();



     Example:
              main()
              {
                 printf("There are %d KBytes of memory", msize());
              }




E
     Unicorn Library Documentation  3.1                         page 101

     __________________________________________________________________

                             OZ_GM

     Converts ounces to grams.  Defined as a macro in UC.H.


F


     Call:   OZ_GM(ounces);



     Example:
           main()
           {
              printf("There are %lf ounces in %lf grams", OZ_GM(53.8), 53.8);
           }




E
     Unicorn Library Documentation  3.1                         page 102

     __________________________________________________________________

                               note

F                         Tandy 1000 only

     Plays a musical tone on the internal speaker.  This function
     includes all sharps and flats and a total of 7 octaves.  The user
     is given access to all three voices and full control over the
     volume.
     Future versions will include duration for added control over the
     note.




     Call:   note(voice, octave, note, volume);

             voice   =  1, 2, or 3 ( selects sound channel)
             octave  =  1 - 7 with 1 being the lowest
             note    =  note from below table
             volume  =  0 (off) to 15 (loudest)

             A  - 1      octave 3 contains middle C
             A# - 2
             B  - 3
             C  - 4
             C# - 5
             D  - 6
             D# - 7
             E  - 8
             F  - 9
             G  - 10
             G# - 11




E
     Unicorn Library Documentation  3.1                         page 103

     __________________________________________________________________

                               paint

F     Fills an area containing a seed point and bounded by a single color
     with a specified color.





     Call:   paint(column, row, paintc, boundry);

             column   =  column coordinate of seed point inside boundry
             row      =  row coordinate of seed point inside boundry
             paintc   =  color to paint the enclosed region
             boundry  =  color of the boundry to the region to fill





     Example:   main()
                {
                   sm(4);  /* set graphics mode  */
                   /* draw a circle */
                   circle(100,100,50,1,1,3);
                   /* paint the circle (watch the border color! */
                   paint(100,100,2,3);
                }



E
     Unicorn Library Documentation  3.1                         page 104

     __________________________________________________________________

                               palette

F                             IBM-PC only

     Changes the palette or color set to be used on an IBM-PC.





     Call:   palette(a, b, c);

             a  =  the palette number (0 to 3)
             b  =  mode ( 4-normal,  5- extra or highlighted color sets)
             c  =  background color



     Example:  main()
               {
                  sm(4);  /* set the graphics mode */
                  /* set the color set to highlighted palette 2 with a
                     blue background.                                 */
                  palette(2, 5, 1);
               }




E
     Unicorn Library Documentation  3.1                         page 105

     __________________________________________________________________

                             pcurpos

     Puts the cursor at a specific screen location.


F


     Call:   pcurpos(row, col, page);

     Where:
             row  = desired cursor row
             col  = desired cursor column
             page = desired cursor page.


     Example:
           main()
           {
              pcurpos(20, 40, 0); /* place the cursor at row 20, column
                                     40 on video page 0.  */
           }




E
     Unicorn Library Documentation  3.1                         page 106

     __________________________________________________________________

                               pencolor

F     Sets the turtle graphics pen color.







     Call:    pencolor(color);

              color  =  the pen color to use.  may be 0-3 for IBM or
                        0-16 for Tandy 1000



     Example:   main()
                {
                   sm(4);  /*  set graphics mode  */
                   /* change pen color to 3 */
                   pencolor(3);
                }



E
     Unicorn Library Documentation  3.1                         page 107

     __________________________________________________________________

                               pendown

F      Places the turtle graphics "pen down" on the screen so that it
     may draw.





     Call:   pendown();





     Example:   main()
                {
                   sm(4);  /*  set the graphics mode */
                   /* place the pen down in preperation for drawing */
                   pendown();
                }


E
     Unicorn Library Documentation  3.1                         page 108

     __________________________________________________________________

                               penup

F     Lift the pen up so that it may be moved without drawing.





     Call:  penup();





     Example:   main()
                {
                   sm(4);  /* set the graphics mode  */
                   /* lift up the pen */
                   penup();
                }



Unicorn 1 Documentation  3.1                                     page 109

__________________________________________________________________________


                              phasor


Make a phasor sound.





Call:         phasor();




Example:      main()
              {
                 phasor(); /* make phasor sound */
              }





E
     Unicorn Library Documentation  3.1                         page 110

     __________________________________________________________________

                             playibm

F
     Plays tones on an IBM or compatible speaker.  It produces only a
     single tone.  Octave 3 contains middle C.  All octaves are defined
     for A through G#.



     Call:   playibm(note, octave, time);

     Where:
            note    = the note number from the below table
                      A,  A#,  B,  C,  C#,  D,  D#,  E,  F,  F#,  G,  G#
                      1,   2,  3,  4,   5,  6,   7,  8,  9,  10, 11,  12
            octave  = octave from 1 to 8 starting from the lowest octave
            time    = the time of the tone in milliseconds

     Example:
           main()
           {
              play(4,3,500); /* play middle C for .5 seconds */
           }




E
     Unicorn Library Documentation  3.1                         page 111

     __________________________________________________________________

                               point

F     Light up a single pixel in a specified color.




     Call:  point(column, row, color);

            column  =  the pixel column
            row     =  the pixel row
            color   =  color to light the pixel



     Example:    main()
                 {
                    sm(4);  /*  set the graphics mode  */
                    /*  light the pixel at 110,110 in color 3 */
                    point(110, 110, 3);
                 }