HDSENTRY - HARD DISK PROTECTION FROM TROJAN PROGRAMS
              (c) Copyright 1987 by Andrew M. Fried

Every day, thousands of free programs are downloaded from  public
bulletin  board systems throughout the world.  While  the  system
itself is generally owned and operated by an individual, much  of
the contents of the BBS come from the public domain.

The system operators of these bulletin boards, or sysops as  they
are affectionately called, rely on their callers for new material
that could be of interest to others.  Some of the stuff  uploaded
by  users include technical articles, software  reviews,  program
patches,  unprotects (ways to crack copy protection),  pleas  for
assistance and, of course, software.

A problem has recently surfaced concerning the software  uploaded
to  these  systems.  Every once in a while,  a  program  surfaces
that, when run, maliciously attacks the systems hard disk.  Since
these  programs  are  often disguised, they are  referred  to  as
'trojan' programs.

HDSENTRY was written at the request of a friend of mine (who also
happens  to  be  a sysop). During the past  few  months,  several
'trojan'  programs have been uploaded to his BBS.  He asked if  a
simple  program could be developed which would insulate the  hard
disk from the rest of the system.  Thus, HDSENTRY was born.

HDSENTRY  will  enable you to run any program on a  floppy  drive
undisturbed. This will permit you to 'test' an unknown program on
a  floppy disk without fears that it will jump over to your  hard
disk and "eat it up". The program running on the floppy may  even
make  calls to the fixed disk so long as the calls do not pose  a
threat  to the system.

HDSENTRY will prevent most programs from accessing the hard  disk
for  any type of destructive call. Nondestructive calls  such  as
reading  or  resetting the drive are  permitted;  formatting  and
writing  to  the disk are trapped and  prevented  from  occuring.
Interrupt  26h,  the  absolute  disk  write  interrupt,  is  also
effectively removed from the system by this program.

The  only way to bypass HDSENTRY's protection scheme would be  to
write  directly  to the ports of the fixed  disk  controller  and
manipulate the disk with the aid of DOS or ROM BIOS.  This is  no
simple task; only a very experienced and knowledgeable programmer
could  do  this. It is my belief that anyone  that  sophisticated
would not be spending their time writing vandalous programs.


CALLING THE PROGRAM
-------------------
The  program  is  called without any  extensions  or  arguements.
Simple  type  'HDSENTRY' at the DOS prompt.  HDSENTRY  will  load
itself  and remain resident in memory (programs such as this  are
often  referred  to  as  TSR or  "terminate  and  stay  resident"
programs).


PROTECTION
----------
Once  HDSENTRY  is run, interrupt vector 13h  (the  diskette  and
fixed disk interrupt handler) and interrupt vector 26h  (absolute
disk  write  interrupt) are changed to point to  routines  inside
HDSENTRY. Any subsequent calls to interrupt 26h will be ignored.

Calls made to interrupt 13h are first checked to see if they  are
accessing  the fixed disk or the floppy. If the floppy  is  being
accessed, HDSENTRY permits the interrupt to continue undisturbed.
If,  on the other hand, one of the fixed disks is the  target  of
the  function call, HDSENTRY checks the interrupt request to  see
if a write or format command has been issued. If so, the  program
flashes an error message on the screen and the program  continues
(unaware  that it did not reach the fixed  disk).  Nondestructive
calls  are permitted, and those requests will be passed onto  the
original interrupt handler for execution.


Technical Information
---------------------
HDSENTRY was written in IBM assembly language and designed to  be
used on IBM PC/XT's and PC/AT's.  Systems without a hard disk are
not supported under this version of HDSENTRY.

Basically,  HDSENTRY operates by revectoring all of the ROM  BIOS
calls which are responsible for providing direct hardware control
of the systems disk drives.  I am referring to interrupts 13h and
26h, ofcourse.

Once  HDSENTRY  has  been  initialized  in  memory,  all  support
requests for disk services are sent to its handler.
If  HDSENTRY finds that the service call is  requesting  services
from  the  diskette,  the  parameters are  passed  along  to  the
original  interrupt  handler for processing.  If,  on  the  other
hand,  the  call is directed towards a fixed  disk,  the  handler
examines the AH register in order to ascertain what BIOS  service
is being requested.  The possibilities include:
     0 - reset diskette system
     1 - read status of system
     2 - read disk sector
     3 - write to disk sector
     4 - verify desired sector
     5 - format desired track
     8 - read drive parameters
    21 - read dasd type  (AT only)
    22 - disk change line status (AT only)
    23 - set dasd type for format (AT only)

If HDSENTRY finds that the call involves either a write or format
command,  a  warning  is displayed and  an  interrupt  return  is
generated.   The original interrupt handler never sees  the  call
and cannot be invoked.

One  technical point to mention concerning interrupt 26h is  that
it,  unlike  all  other  interrupts, does  not  perform  a  clean
interrupt return.  Upon return, a word is left in the stack which
must  be removed by the application program making  the  function
request.

The  significance of this is that if our program failed to add  a
word  to  the stack before performing an  interrupt  return,  the
offending  program would cause chaos by popping information  from
the  stack  when it shouldn't.  The stack pointer would  get  all
messed   up   and  unpredictable  results  would   occur   almost
immediately.


Conclusion
----------
This program should be invoked before running any newly  acquired
software downloaded from a BBS.  It permits you to run a  program
on  your  floppy  disk drive without worrying  that  a  concealed
command will trash your hard disk.  Removing the program once  it
is invoked, however, requires you to reboot the system.

The program is a good example of memory resident programming,  as
well.

Andrew M. Fried
895 Cynthia Drive
Titusville, Fla. 32780