T E S T   D R I V E  (tm)


                   A Comprehensive Disk Drive Diagnostic Tool




                                OPERATOR'S MANUAL       


                                   Version 1.2













                            Microsystems Development
                            4100 Moorpark Ave.  #104
                            San Jose, CA  95117  USA
                                 (408) 296-4000
                            











                Copyright (C) Microsystems Development 1987,1988.
                              All Rights Reserved











        TEST DRIVE (tm)                                     Version 1.2



                                TABLE OF CONTENTS 


        I.   INTRODUCTION............................................1

        II.  WARRANTY................................................3

        III. COPYRIGHT AND TRADEMARK INFORMATION.....................3

        IV.  ORDERING INFORMATION....................................4

        V.   BASIC DISK INFORMATION..................................5

        VI.  OPERATION...............................................7

             F1   Program Information................................7

             F2   General Test.......................................8
                  A) Sample display for a good drive.................9
                  B) Sample display for a bad drive.................10

             F3   Alignment Test....................................11
                  A) Sample display for a good drive................13
                  B) Sample display for a bad drive.................14

             F4   Spindle Speed.....................................15
                  A) Sample display for a good drive................16
                  B) Sample display for a bad drive.................16

             F5   Write / Read Test.................................17
                  A) Sample display for a good drive................18
                  B) Sample display for a bad drive.................19

             F6   Hysteresis Test...................................20
                  A) Sample display for a good drive................21
                  B) Sample display for a bad drive.................22

             F7   Head Azimuth Test.................................23
                  A) Sample display for a good drive................24
                  B) Sample display for a bad drive.................25
             
             F8   Hub Centering.....................................26
                  A) Sample display for a good drive................27
                  B) Sample display for a bad drive.................28

             F9   Continuous Alignment..............................29
                  A) Sample display for a good drive................30
                  B) Sample display for a bad drive.................31

             F10  Cleaning Utility..................................32 

        GLOSSARY OF TERMS...........................................34

        CUSTOMER FEEDBACK FORM......................................37


        Copyright (C) Microsystems Development 1987, 1988.            i





        TEST DRIVE (tm)                                     Version 1.2



        I.   INTRODUCTION

             Floppy disk drives are your computer's lifeline.  They 
        provide the easiest and in many cases the only method of 
        transferring data from one computer to another.  It is extremely 
        important that your computer's disk drives be operating at peak 
        performance at all times.

             TEST DRIVE is a comprehensive floppy disk drive diagnostic 
        tool.  It accurately measures and displays important operating 
        parameters, so that the exact operating condition of a drive can 
        be determined.  In addition, this manual will help in 
        understanding the basics of disk operation, will help to analyze 
        the test results, and recommend corrective procedures.

             Have you ever gotten the dreaded "Abort, Retry, Ignore?" 
        message when using a disk you thought was good?  TEST DRIVE will 
        let you know if your drive is functioning properly.

              Have you ever had problems in transferring files on disk 
        between different computers?  Perhaps one computer can reliably 
        read and write to a diskette, but that same diskette will not 
        work in another computer?  TEST DRIVE will pinpoint the problem.

             Have you ever experienced unexplainable data loss on 
        diskettes?  Perhaps a backup disk that your computer generated 
        months ago will no longer work in your computer?  Periodic 
        testing with TEST DRIVE will help avoid this problem.  

             Do you need to be absolutely sure that the diskettes your 
        disk drive writes to can be read by another computer?  TEST DRIVE 
        will confirm proper operation of your drive.     

             Have you ever had repairs made only to have the same or new 
        problems occur?  TEST DRIVE will keep the technician honest by 
        reporting and quantifying the drive's performance, before and 
        after repair.  

             Want to dig in and make adjustments yourself?  TEST DRIVE 
        provides continuous tests which can be run on your computer while 
        adjustments are made.   

             Ever wonder if you should be cleaning your drives, and if 
        so, how often?  TEST DRIVE will indicate when cleaning may be 
        necessary.  In addition, TEST DRIVE provides a helpful utility to 
        be used with a standard cleaning disk.

             Does cleaning really help?  TEST DRIVE can measure your 
        drive's performance before and after cleaning to determine if the 
        cleaning has been helpful.

             How important is the diskette media?  Bulk purchased generic 
        disks are generally tested to a lesser extent that the more 
        expensive name brands.  In general, the generics are tested for 


        Copyright (C) Microsystems Development 1987, 1988.            1





        TEST DRIVE (tm)                                     Version 1.2


        media defects only where a perfectly aligned drive would read and 
        write.  If your drive's alignment is off, the probability of a 
        data loss using an inferior disk is greatly increased. 

             In addition, as drive densities continue to increase, data 
        is packed closer and closer together on the magnetic media.  This 
        makes precise operation of your drive even more crucial.

             The TEST DRIVE disk drive diagnostic package consists of the 
        TEST DRIVE program disk and an Dysan Digital Diagnostic Disk 
        (DDD).  The program diskette contains the following files:         

                  testdriv.com   -    Executable program
                  testdriv.doc   -    This documentation 

             To use the full capabilities of TEST DRIVE you will need the 
        Dysan precision alignment disk manufactured by Xidex Corporation, 
        available for sale from Microsystems Development (see ordering 
        information).  The Dysan Digital Diagnostic Disk (DDD) is a test 
        disk with data written at precise distances and angles along the 
        tracks.  TEST DRIVE will analyze the disk drive's ability to read 
        the specialized data patterns contained on the DDD.  Some of TEST 
        DRIVE's tests require the use of the DDD, some do not.

             Together, these two disks allow you, the user, to perform 
        comprehensive diagnostic tests, and perform certain adjustments 
        on floppy disk drives.  The use of expensive and special test 
        equipment, oscilloscopes, etc., is unnecessary.  The following 
        tests are performed by TEST DRIVE:

               *  General Test     
               *  Alignment Test
                  Spindle Speed
                  Write/Read Test
               *  Hysteresis Test
               *  Head Azimuth Test
               *  Hub Centering                 
               *  Continuous Alignment          * These tests require the
                  Cleaning Utility                Dysan diagnostic disk  
            
             This version of TEST DRIVE will test 5 1/4" (360KB  or less) 
        disk drives.  Updates for high density 5 1/4" and 3 1/2" drives 
        are under development.  Please inquire for availability.

        System Requirements:

                IBM PC/XT/AT or Compatible
                64K RAM
                DOS 2.0 or greater
                An 80 column monitor (Color or Monochrome)
                One working 5 1/4" disk drive that can load the program.  

             Once loaded, TEST DRIVE can later be run from a hard disk.  
        In fact, this is recommended for periodic testing to insure your 
        drives are in proper operating condition.


        Copyright (C) Microsystems Development 1987, 1988.            2





        TEST DRIVE (tm)                                     Version 1.2


        II.  WARRANTY

             Microsystems Development makes no warranty of any kind, 
        express or implied, including without limitation, any warranties 
        of merchantability and/or fitness for any specific application or 
        use.  Microsystems Development shall not be liable for ANY loss 
        or damage arising from a failure of this program to operate in 
        the manner described, or in a manner desired by the user. 
        Microsystems Development shall not be liable for any damage to 
        data or property which may be caused directly or indirectly by 
        use of the program.

             IN NO EVENT SHALL MICROSYSTEMS DEVELOPMENT OR IT'S SUPPLIERS 
        BE LIABLE FOR ANY CONSEQUENTIAL, INCIDENTAL OR EXEMPLARY DAMAGES 
        INCLUDING, BUT NOT LIMITED TO LOSS OF PROFITS OR REVENUES, LOSS 
        OF USE OF ANY PRODUCT, SERVICE OR REPLACEMENT COSTS, OR CLAIMS BY 
        ANY THIRD PARTY.


        III. COPYRIGHT AND TRADEMARK INFORMATION

             This version of TEST DRIVE may be copied and distributed 
        freely, with the following restrictions:

              1)  The program and documentation may not be modified, 
              2)  The entire documentation file must be included with the 
                  program, 
              3)  No fee for the program may be charged outside of a 
                  reasonable and customary charge for diskette media, 
                  copying and/or shipping, and
              4)  It may not be packaged or sold in conjuction with any 
                  other product.

             The software code and screen displays used in TEST DRIVE are 
        the sole property of Microsystems Development, and may not be 
        copied, in any form, in whole or in part, or included in any 
        other program or document without the express written permission 
        of Microsystems Development.

             If you'd like to make use of the full capabilities of TEST 
        DRIVE, you are encouraged to purchase the Dysan Diagnostic Disk 
        directly from us (see ordering information).  This will help 
        support our effort, make you a registered user, and ensure that 
        you are kept up to date on new versions and enhancements.

        Digital Diagnostic Diskette (DDD) is a trademark of Dysan.  

        Dysan is a registered trademark of Xidex Corporation.

        IBM, IBM PC, IBM XT and IBM AT are registered trademarks of 
             International Business Machines Corporation.

        MS-DOS is a trademark of Microsoft Corporation.

        TEST DRIVE is a trademark of Microsystems Development.


        Copyright (C) Microsystems Development 1987, 1988.            3





        TEST DRIVE (tm)                                     Version 1.2


        IV.  ORDERING INFORMATION

                              TEST DRIVE ORDER FORM

        ____ Dysan Digital Diagnostic Disk,
               includes TEST DRIVE registration.......US$50.00 ea _______

        ____ Dysan disk, Latest version of TEST DRIVE,
              Printed manual, and Registration........US$75.00 ea _______


                                           Subtotal..............._______

             Calif. residents add 6%, 6.5% or 7% sales tax........_______

             Shipping charges.  $2.50 within the continental             

             USA, $5.00 outside the continental USA..............._______


                                           TOTAL...............$_________


        ______ Enclosed is a check for the above amount.

        ______ Please charge the above amount to my:  Visa( )  MC( )

               Account number:__________________________________Exp._____

               Cardholder signature:_____________________________________

            
        Purchase orders are accepted from qualified corporations.
        Please call first for approval.


             Name:    _____________________________________________

             Company: _____________________________________________

             Address: _____________________________________________

                      _____________________________________________

             Phone:   (________) __________________________________


                    Remit to:  Microsystems Development
                               4100 Moorpark Ave.  #104
                               San Jose, CA  95117  USA

              Phone:  (408) 296-4000  10 AM to 4 PM  Pacific Time.

             Please inquire for availability of high density
             5 1/4" and 3 1/2" versions of TEST DRIVE. 


        Copyright (C) Microsystems Development 1987, 1988.            4





        TEST DRIVE (tm)                                     Version 1.2


        V.   BASIC DISK INFORMATION

             It is not necessary to have a degree in computer engineering 
        to use or benefit from TEST DRIVE.  However, a basic 
        understanding of disk operation is helpful in identifying 
        problems.  This section is meant to introduce you to basic disk 
        operation and terminology.

             Diskette density specifies the amount of data the disk is 
        capable of holding.  Densities are measured in kilobytes (KB) or 
        megabytes (MB).  A kilobyte is 1024 bytes and a megabyte is 1000 
        kilobytes.  

             Information is written on a floppy disk magnetically, in 
        much the same way as audio information is stored on cassettes or 
        reel to reel tapes.  The disk is rotating so data is written in 
        circles around the disk.  These circles are called tracks.  Each 
        track is divided into a number of sectors.  

             Each sector contains addressing marks, a fixed amount of 
        data, and a Cyclic Redundancy Check (CRC) for the data.  The CRC 
        is an integrity check on the data.  To retrieve data, the disk 
        drive controller must position the head over the desired track 
        and wait for the correct sector address to come around.  Once the 
        sector is found, the disk controller reads the information from 
        the sector and stores it in a buffer.  Then the CRC is computed 
        and compared to the CRC read from the disk.  If this does not 
        compare an error is reported.  A write operation occurs in much 
        the same manner except that the CRC is computed and stored with 
        the data and no verification is performed.  

             One indicator of disk density is the TPI specification.  
        This stands for Tracks Per Inch.  In a 48TPI disk the tracks are 
        spaced 1/48 of an inch apart.  Since a 360K diskette has 40 
        tracks, the width of the media containing data is somewhat less 
        than an inch.  A 96 TPI diskette usually contains 80 tracks or 
        double the 40 tracks of a 360K.   This would tend to make us 
        think that the density would be 720K, and this is true for the 3 
        1/2 inch technology.  But the high density 5 1/4 inch standard 
        has 15 sectors per track instead of the 9 on a 360 KB disk.  This 
        makes 1.2 MB (see table below).  It seems that as the technology 
        becomes available to store more information on a disk, someone 
        will.  However, the basics for data storage and retrieval is 
        relative constant no matter what the density is.  













        Copyright (C) Microsystems Development 1987, 1988.            5





        TEST DRIVE (tm)                                     Version 1.2


             A 360KB diskette is formatted with 40 tracks, 9 sectors per 
        track, on both sides.  512 bytes are written in each sector.

             Total    40 tracks   9 sectors   2 sides    512 bytes
             bytes  =    ------ X   ------- X          X     ------
                          side       track                   sector
                       
                    OR

             Total bytes = 368,640 

             This is usually abbreviated to 360 KB, which is 360 x 1024 
        bytes.

             The computer's operating system normally uses a few sectors 
        for overhead such as label and directory information.  This is 
        why there are slightly less than 368,640 usable bytes on a 
        formatted disk.  

             The address marks and CRC are stored between the data and 
        are not included in the formatted capacity of a disk.

             The following table illustrates the storage specifications 
        for the most commonly used disk densities:


        Storage   Physical  Sectors     Bytes       Tracks     Number 
        Size      Size      per Track   per Sector  per Side   of Sides
        ----------------------------------------------------------------
         160 KB    5 1/4"       8          512         40         1
         180 KB    5 1/4"       9          512         40         1
         320 KB    5 1/4"       8          512         40         2
         360 KB    5 1/4"       9          512         40         2
         1.2 MB    5 1/4"      15          512         80         2
         720 KB    3 1/2"       9          512         80         2
        1.44 MB    3 1/2"      18          512         80         2


             This version of TEST DRIVE is designed to test 360 KB 
        drives.  It will also test the first 3 types, however.  Since the 
        first 2 types (160 and 180 KB) have only 1 head in the disk 
        drive, TEST DRIVE will report errors for Head 1, but the Head 0 
        results are correct.














        Copyright (C) Microsystems Development 1987, 1988.            6





        TEST DRIVE (tm)                                     Version 1.2


        VI.  OPERATION

             To operate, first load the operating system, then type 
        'testdriv', followed by the enter key.  After the opening screen 
        appears, press any key to proceed to the main menu.  You will see 
        a list of available selections.  The number of drive selections 
        you see is dependent on the number of drives available in your 
        system.  To make a selection, press the key indicated to the left 
        of the selection, or highlight your choice by using the up and 
        down arrows, then press enter.  

             Some tests require the use of the Dysan DDD.  The speed test 
        will work with any standard formatted diskette OR the DDD.  The 
        Write/Read test will only work a normal diskette, not the DDD.  
        TEST DRIVE always checks for the type of diskette inserted.

             Data is never written to the DDD.



        F1   Program Information

             This screen gives a very brief "on-line" description of TEST 
        DRIVE.  This document is provided for more detailed information.

             After the information screen, the user is given the option 
        of displaying an 'Instant Order Form'.  If a printer is attached, 
        simply use the PrtSc (print screen) function of your computer to 
        print a copy of the order form.




























        Copyright (C) Microsystems Development 1987, 1988.            7





        TEST DRIVE (tm)                                     Version 1.2


        F2  General Test

            In this test, six areas of drive performance are displayed 
        and measured, with Pass / Fail results given for each.  
        The measured results are also displayed, along with the 
        criteria used for Pass / Fail determination.  For more detailed 
        information on each of the tests, see the appropriate section
        describing that particular test in detail.

             The TEST DRIVE general test is a good overall test which 
        should usually be run first to determine if there are any  
        problem areas.  You encouraged to read the rest of this document 
        for a detailed description of each test.

        Display Information:

             Alignment and Sensitivity are combined in the first part of 
        the test.  Three tracks for each head are measured.  The drive 
        will pass the test if it can read data written at least +/- 8 
        milli-inches from the track centerline.  Some manufacturers 
        specify +/- 9 milli-inches as passing criteria.

             The next part of the test measures the drive's ability to 
        precisely seek to a specified track from either direction.  This 
        is called hysteresis.  Only one track is used for this test.  If 
        the hysteresis is less than or equal to 1.5, it passes.

             Next, the spindle speed is measured.  For a 360KB disk 
        drive, the speed must be between 295 and 305 RPM.  Some 
        manufacturers specify a smaller range.

             Hub centering is the next test.  The alternate offset track 
        which has data written at +/- 8 milli-inches offset around the 
        track is used for this part of the test.  No errors allowed for 
        the drive to pass.
             
             The last test in the general test is Head Azimuth.  If the 
        drive can read data placed on the disk at an angle of +/- 39 
        minutes of a degree from centerline, it is considered good.

             The Pass / Fail criteria used in the General Test is in 
        accordance with generally accepted standards.  However, different 
        manufacturers, equipment, testing labs, etc., may use different 
        criteria.  The criteria used in TEST DRIVE are not meant to imply 
        absolute minimums or maximums, but were simply chosen to help 
        interpret the data.  In all cases, the measured data is also 
        displayed for the user's own interpretation.

             In addition, the measured data displayed for the General 
        Test, as well as the other tests may vary slightly each time they 
        are run.  This is because the tests push the drive past its 
        normal operating points, and operation outside the normal ranges 
        may not be consistent.




        Copyright (C) Microsystems Development 1987, 1988.            8





        TEST DRIVE (tm)                                     Version 1.2


        A) Sample display for a good drive



                                   TEST DRIVE
                                  General Test

                                            Criteria   Test     Result
                                            -------- --------- --------
           Alignment /    Track  0 Head 0     +/- 8   +10 -10    Pass
           Sensitivity    Track  0 Head 1     +/- 8   +11 -10    Pass
                          Track 19 Head 0     +/- 8   +10 -10    Pass
                          Track 19 Head 1     +/- 8   +10 - 9    Pass
                          Track 39 Head 0     +/- 8   +12 -10    Pass
                          Track 39 Head 1     +/- 8   + 8 - 9    Pass

           Hysteresis     Track 19 Head 0      1.5       0.5     Pass

           Spindle Speed  . . . . . . . .   295 - 305    301     Pass

           Hub Centering  . . . .  Head 0   0 Errors  0 Errors   Pass

           Head Azimuth   . . . .  Head 0    +/- 39'  +42 -42    Pass
                                   Head 1    +/- 39'  +42 -42    Pass



        Analysis:

             The above drive has passed all the tests, and the drive 
        appears to be in good condition.     

        Alignment     - the drive was able to read data 8 milli-inches 
                        or greater from the track centerline.
             
        Hysteresis    - is less than 1.5.

        Spindle Speed - is in the acceptable range at 301 RPM.
           
        Hub Centering - no errors were detected.

        Head Azimuth  - both heads were able to read data angled at 
                        39 minutes of a degree or greater.














        Copyright (C) Microsystems Development 1987, 1988.            9





        TEST DRIVE (tm)                                     Version 1.2


        B) Sample display for a bad drive



                                   TEST DRIVE
                                  General Test

                                            Criteria   Test     Result
                                            -------- --------- --------
           Alignment /    Track  0 Head 0     +/- 8   + 6 -12    Fail
           Sensitivity    Track  0 Head 1     +/- 8   +11 -10    Pass
                          Track 19 Head 0     +/- 8   + 7 -11    Fail
                          Track 19 Head 1     +/- 8   +11 - 9    Pass
                          Track 39 Head 0     +/- 8   + 6 -11    Fail
                          Track 39 Head 1     +/- 8   + 8 - 9    Pass

           Hysteresis     Track 19 Head 0      1.5       2.0     Fail

           Spindle Speed  . . . . . . . .   295 - 305    309     Fail

           Hub Centering  . . . .  Head 0   0 Errors  2 Errors   Fail

           Head Azimuth   . . . .  Head 0    +/- 39'  +42 -42    Pass
                                   Head 1    +/- 39'  +42 -21    Fail


        Analysis:
             
             In the above example, Head 0 is poorly aligned.  It is 
        shifted slightly away from the spindle as indicated by the high 
        negative values and low positive values.  

             The above drive has also failed the hysteresis test 
        indicating a possible problem with the positioning mechanism.  

             The TEST DRIVE General Test indicates that the spindle 
        speed is too high.  Hub centering has also failed indicating a 
        possible clamping problem.  It was not able to read some of the 
        data written at 8 milli-inches from track center. 

             Head 1 is also rotated slightly in one direction.  It cannot 
        read data written in a position greater than 21 minutes of a 
        degree from track centerline.

             For all the above problem areas, each individual test should 
        be run in full to determine the extent of each problem.











        Copyright (C) Microsystems Development 1987, 1988.            10





        TEST DRIVE (tm)                                     Version 1.2


        F3  Alignment Test


             Alignment is a measure of how centered the read/write head 
        is over the track center.  This is sometimes called Radial 
        Alignment.  For a 48TPI disk, each track is 1/48 inch wide which 
        is 20.833 milli-inches.  Data on the progressive offset tracks of 
        the DDD are progressively displaced from 6 to 13 milli-inches  
        toward and away from the spindle.  Therefore, data  will span 26 
        milli-inches which is slightly wider than a 48 TPI track.  The 
        tracks adjacent to the progressive offset track of the DDD are 
        not used.  

             Sensitivity is a measure of how much data on a given track 
        is readable, or the width to which the head is sensitive to.  If 
        a head is able to read data from +10 to -10 milli-inches on a 20 
        milli-inch track, you have a drive performing very well.  If the 
        same drive read +13 to -7, we still have perfect sensitivity but 
        the alignment is now shifted.

             The successful reading of data greater than +/- 10 milli-
        inches will cover the entire track.  If a disk drive is able to 
        read data that is progressively offset to +8 and only to -7, the 
        drive is slightly mis-aligned and suffers from poor alignment 
        sensitivity.  A drive that will read -11 to +8 milli-inches, 
        shows good sensitivity but is poorly aligned.  In the latter 
        case, the drive will likely function reliably until the head 
        becomes dirty and the sensitivity decreases.

             The alignment test will push the drive's operation beyond 
        normal limits and report back the results,  You will certainly 
        see errors in this test simply because the drive is not supposed 
        to read data placed beyond the normal track width.

        Display Information:

             The alignment test uses all of the progressive offset tracks 
        available on the Dysan Digital Diagnostic test.  These are tracks 
        0, 5, 16, 19, 30, and 39.  It attempts to read all the data on 
        the tracks, from 6 to 13 milli-inches off center in either 
        direction.  If the read was successful, it will display four 
        solid characters, represented in this document as '~~~~'.  If the 
        read was not successful, it will display 'erxx', where xx is the 
        hex error code returned by the BIOS read routine.  













        Copyright (C) Microsystems Development 1987, 1988.            11





        TEST DRIVE (tm)                                     Version 1.2


             The following is a list of errors than can be reported:

             ERROR ERROR
             CODE  TYPE                REASON
             ----  ------------------  --------------------------------- 
             er80  time_out            Drive did not respond

             er40  bad_seek            Drive failed to seek to track

             er20  bad_nec             Drive controller chip failed

        *    er10  bad_crc             Cyclic redundancy check failed
                                 
             er09  dma_boundary        Attempt to direct memory
                                       across 640K boundary

             er08  bad_dma             DMA overrun on operation

             er06  media_change        media not identified
                                       on multiple media drive

        *    er04  record_not_found    sector not found

        *    er02  bad_addr_mark       address mark not found
             

        * Commonly induced errors in alignment test.

        Adjustments for poor Alignment Sensitivity: 

             Poor alignment sensitivity indicates that the heads are not 
        picking up as much data as they should.  This could be due in 
        part to a build up of dirt on the heads.  The correction for this 
        to simply clean the heads.  If the problem is a dirty head, 
        cleaning will eventually correct the problem.  Cleaning, however, 
        generally will not have a drastic effect.  If the problem 
        persists, it may be necessary to replace the drive since 
        replacing the head assembly usually is not done economically.
             
        Adjustments for poor Alignment: 

             Most drives come equipped with an adjustment screw which 
        will translate a turning motion into a linear head adjustment.  
        Since drives are becoming so inexpensive however, manufacturers 
        are saving costs by eliminating expendable mechanisms such as 
        alignment hardware.  It is more cost effective for the 
        manufacturer to set the alignment once, than it is to provide 
        adjustment screws.  

             If your drive has such an adjustment, we suggest you use the 
        Continuous Alignment Test if you wish to make adjustments.  
        Please see the explanation of that test for more information.

             If the alignment is just slightly off, we recommend that you 
        leave it alone, and monitor its condition with TEST DRIVE.  


        Copyright (C) Microsystems Development 1987, 1988.            12





        TEST DRIVE (tm)                                     Version 1.2



        A)  Sample display for a good drive

                            TEST DRIVE Alignment Test

              <------------------------  Track  ------------------------->
              39   30   19   16   5    0       0    5    16   19   30   39

        - 13 er02 er02 er02 er02 er02 er02    er02 er02 er02 er04 er10 er04
        - 12 er02 er02 er02 er02 er02 er02    er02 er02 er02 er02 er02 er02
        - 11 er02 er02 er02 er02 er02 er02    er02 er02 er02 er02 er02 er02
        - 10 ~~~~ ~~~~ ~~~~ ~~~~ ~~~~ ~~~~    ~~~~ ~~~~ ~~~~ ~~~~ er02 er02
        -  9 ~~~~ ~~~~ ~~~~ ~~~~ ~~~~ ~~~~    ~~~~ ~~~~ ~~~~ ~~~~ ~~~~ er02
        -  8 ~~~~ ~~~~ ~~~~ ~~~~ ~~~~ ~~~~    ~~~~ ~~~~ ~~~~ ~~~~ ~~~~ ~~~~
        -  7 ~~~~ ~~~~ ~~~~ ~~~~ ~~~~ ~~~~    ~~~~ ~~~~ ~~~~ ~~~~ ~~~~ ~~~~
        -  6 ~~~~ ~~~~ ~~~~ ~~~~ ~~~~ ~~~~    ~~~~ ~~~~ ~~~~ ~~~~ ~~~~ ~~~~
                         Head  0                          Head  1
        +  6 ~~~~ ~~~~ ~~~~ ~~~~ ~~~~ ~~~~    ~~~~ ~~~~ ~~~~ ~~~~ ~~~~ ~~~~
        +  7 ~~~~ ~~~~ ~~~~ ~~~~ ~~~~ ~~~~    ~~~~ ~~~~ ~~~~ ~~~~ ~~~~ ~~~~
        +  8 ~~~~ ~~~~ ~~~~ ~~~~ ~~~~ ~~~~    ~~~~ ~~~~ ~~~~ ~~~~ ~~~~ ~~~~
        +  9 ~~~~ ~~~~ ~~~~ ~~~~ ~~~~ ~~~~    ~~~~ ~~~~ ~~~~ ~~~~ ~~~~ ~~~~
        + 10 er02 er02 er02 ~~~~ ~~~~ ~~~~    ~~~~ ~~~~ ~~~~ ~~~~ ~~~~ er02
        + 11 er02 er02 er02 er02 er02 er02    er02 er02 er02 er02 er02 er02
        + 12 er02 er02 er02 er02 er02 er02    er02 er02 er02 er02 er02 er02
        + 13 er02 er04 er04 er04 er04 er04    er04 er04 er02 er02 er04 er02

             
        Analysis:

             This drive is in good shape, the '~~~~' pattern is 
        symmetrical between the + and - readings.  This indicates very 
        good alignment.  This test also indicates the sensitivity of the 
        head.  For the most part, the heads are sensitive to data from -
        10 to +10 milli-inches or a total of 20 milli-inches.  On track 
        39 of head 1, the head is sensitive only from -8 to +9 milli-
        inches or 17 milli-inches.  Since these tracks on the diskette 
        are 20 milli-inches wide, this drive is performing well.




















        Copyright (C) Microsystems Development 1987, 1988.            13





        TEST DRIVE (tm)                                     Version 1.2


        C)  Sample display for a bad drive

                            TEST DRIVE Alignment Test

              <------------------------  Track  ------------------------->
              39   30   19   16   5    0       0    5    16   19   30   39

        - 13 er02 er02 er02 er02 er02 er02    er02 er10 er04 er10 er10 er04
        - 12 er02 er02 er02 er02 er02 er02    er02 er04 er04 er02 er02 er02
        - 11 er02 er02 er02 er02 er02 er02    er02 er04 er02 er02 er02 er02
        - 10 er02 er02 er02 er02 er02 er02    er02 er02 er02 er02 er02 er02
        -  9 er02 er02 er02 er02 er02 er02    er02 er02 er02 er02 er02 er02
        -  8 er02 ~~~~ ~~~~ ~~~~ ~~~~ ~~~~    ~~~~ er02 er02 er02 er02 er02
        -  7 er02 ~~~~ ~~~~ ~~~~ ~~~~ ~~~~    ~~~~ ~~~~ er02 er02 er02 er02 
        -  6 ~~~~ ~~~~ ~~~~ ~~~~ ~~~~ ~~~~    ~~~~ ~~~~ ~~~~ er02 er02 er02
                         Head  0                          Head  1
        +  6 ~~~~ ~~~~ ~~~~ ~~~~ ~~~~ ~~~~    ~~~~ ~~~~ ~~~~ ~~~~ ~~~~ ~~~~
        +  7 ~~~~ ~~~~ ~~~~ ~~~~ ~~~~ ~~~~    ~~~~ ~~~~ ~~~~ ~~~~ ~~~~ ~~~~
        +  8 ~~~~ ~~~~ ~~~~ ~~~~ ~~~~ ~~~~    ~~~~ ~~~~ ~~~~ ~~~~ ~~~~ ~~~~
        +  9 ~~~~ ~~~~ ~~~~ ~~~~ ~~~~ ~~~~    ~~~~ ~~~~ ~~~~ ~~~~ ~~~~ ~~~~
        + 10 er02 er02 er02 ~~~~ ~~~~ ~~~~    ~~~~ ~~~~ ~~~~ ~~~~ ~~~~ ~~~~
        + 11 er02 er02 er02 er02 er02 er02    er02 er02 er02 ~~~~ ~~~~ ~~~~
        + 12 er02 er02 er02 er02 er02 er02    er02 er02 er02 er02 er02 er02
        + 13 er02 er04 er04 er04 er04 er04    er04 er04 er02 er02 er04 er02

        Analysis:

             This drive shows problems in both alignment and possibly in 
        sensitivity as well.  The alignment pattern shows a shift of the 
        successful read operations toward the positive side.  This 
        indicates that the physical positioning of the head is shifted 
        off the center of the track.  This problem could be remedied by 
        adjusting the head positioning to make the pattern symmetrical.  

             For most of the disk the total sensitivity reads about +10 
        to -7 or 17 milli-inches of read sensitivity.  However, head 1 
        cannot even read data at -6 milli-inches on tracks 19, 30 and 39.  
        In this case, the sensitivity cannot be determined until the 
        alignment is corrected.


















        Copyright (C) Microsystems Development 1987, 1988.            14





        TEST DRIVE (tm)                                     Version 1.2


        F4   Spindle Speed

             This test measures the speed at which the diskette rotates 
        in the drive.  It can use either the Dysan DDD or a standard 
        formatted diskette.  If an error occurs when the test starts, the 
        user is given the opportunity to override by pressing 'O'.  If 
        errors still occur, speed will be displayed as '---'.

             Speed is measured by the time it takes for the diskette to 
        rotate from a given sector back around to the same sector.  This 
        time is then converted to revolutions per minute, or RPM.  The 
        acceptable range is 295 to 305 RPM.  A drive can operate outside 
        this range and cause no apparent problems, but it should be 
        adjusted to be within range.  Otherwise, it may be difficult to 
        interchange data written by it with another drive.

             Other types of drives operate at different speeds as        
        follows:

                  high density 5 1/4"    355 to 365 RPM
                               3 1/2"    295 to 305 RPM

        Display Information:

             The test will run for several trials, continually updating 
        the speed and the pointer on the display.  It then stops in order 
        to save wear on the disk.  If you wish to run it continuously, 
        press "C".  Any other key will return you to the main menu.  If 
        you select "C" for continuous testing, the test will not stop 
        until you press another key.


        Adjustment:

             On most drives,there is a small screw adjustment for spindle 
        speed.  This adjustment can be made while this test is running, 
        and TEST DRIVE will continually update the display accordingly.  
        If the speed is adjusted too far out of range so that the program 
        can no longer read any data, TEST DRIVE will report '---'.    

             If the speed varies erratically, say 4 RPM or more, the 
        problem could be a loose or bad drive belt.  In many cases, 
        replacement of the belt will help or cure the problem.

             Some drives have direct drive from the motor so do not have 
        belts.  Some do not even have a speed adjustment.  In these 
        cases, the drive should either be repaired professionally or 
        replaced.









        Copyright (C) Microsystems Development 1987, 1988.            15





        TEST DRIVE (tm)                                     Version 1.2


        A)  Sample display for a good drive


                      TEST DRIVE Spindle Speed Measurement




                              |---- Acceptable ---|
                              |       Range       |

         285       290       295       300       305       310       315
          |---------|---------|---------|---------|---------|---------|

                                        ^

                                Speed =   300 RPM

                          Using Dysan DDD Model 508-400


        Analysis:

             Here, the speed is directly in the middle of the acceptable 
        range, at 300 revolutions per minute. 



           
        B)  Sample display for a bad drive


                      TEST DRIVE Spindle Speed Measurement




                              |---- Acceptable ---|
                              |       Range       |

         285       290       295       300       305       310       315
          |---------|---------|---------|---------|---------|---------|

                      ^

                                Speed =   291 RPM

                          Using Dysan DDD Model 508-400


        Analysis:

             The above drive is running slightly slow, at 291 revolutions 
        per minute.



        Copyright (C) Microsystems Development 1987, 1988.            16





        TEST DRIVE (tm)                                     Version 1.2


        F5   Write / Read Test

             This test measures the drive's ability to correctly write, 
        then read back, each sector of the disk.  It can also be used to 
        verify the operation of a particular diskette, that is, its 
        ability to store data on all parts of it.

             The computer's operating system normally checks both the 
        write and the read processes for errors.  TEST DRIVE checks for 
        those errors and reports them.  In addition, each byte that was 
        written is compared with what was read back to determine if it's 
        exactly the same.  Any discrepancy is reported as a compare 
        error.

        Display Information:

             This test requires the use of a formatted scratch diskette.  
        It writes 512 random bytes of data to each sector on the disk, 
        reads them back and compares them.  Errors can occur while 
        Writing, Reading or Comparing the data, and are reported sector 
        by sector.  There are several types of write and read errors 
        returned by the system's BIOS, such as bad seek or bad CRC.  
        These errors are not reported individually in this test.  Only 
        'W' or 'R' are displayed, depending on whether the error was the 
        result of a write or a read operation.

             Since TEST DRIVE writes random data to all sectors including 
        those used by the operating system for file and directory 
        information, any diskette used for this test will have to be re-
        formatted before it can be used for normal purposes.
            
             Insure that the media used is of high quality and does not 
        introduce errors into the test.

             No errors should be tolerated for this test. 


        Adjustment:

             There is no adjustment.  In some cases, the drive heads may 
        simply need to be cleaned.  Use a good quality cleaner and try 
        the test again.















        Copyright (C) Microsystems Development 1987, 1988.            17





        TEST DRIVE (tm)                                     Version 1.2



        A)  Sample display for a good drive



                          TEST DRIVE Write / Read Test

                   Sector-+   Track -->
                          |   0 - - -  9  - - - 19 - - -  29 - - -  39
                          1 - ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~-
                          2 - ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~|
        ~ = Sector OK     3 - ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~|
                          4 - ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~|
                          5 - ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~| Head
        W = Write error   6 - ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~|   0
                          7 - ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~|
        R = Read error    8 - ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~|
                          9 - ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~|
        C = Compare error 1 - ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~-
                          2 - ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~|
                          3 - ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~|
        Total errors = 0  4 - ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~|
                          5 - ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~| Head
                          6 - ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~|   1
                          7 - ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~|
                          8 - ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~|
                          9 - ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~-


        Analysis:

             The above display indicates that the program was able to 
        successfully write, then read back the same data, to every sector 
        on the diskette.























        Copyright (C) Microsystems Development 1987, 1988.            18





        TEST DRIVE (tm)                                     Version 1.2


        B) Sample display for a bad drive



                          TEST DRIVE Write / Read Test

                   Sector-+   Track -->
                          |   0 - - -  9  - - - 19 - - -  29 - - -  39
                          1 - ~~C~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~-
                          2 - ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~|
        ~ = Sector OK     3 - W~~~~~~~~~~~~~~~W~~~~~~~~~~~~~~~~~~~~~~~|
                          4 - WR~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~|
                          5 - WR~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~| Head
        W = Write error   6 - WW~~~~~~~~~~~~~~~W~~~~~~~~~~~~~~~~~~~~~~|   0
                          7 - WR~~~~~~~~~~~~~~~R~~~~~~~~~~~~~~~~~~~~~~|
        R = Read error    8 - R~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~|
                          9 - ~~~~~~~~~~~~~~~~~~~~~~~~R~~~~~~~~~~~~~~~|
        C = Compare error 1 - ~~~~~C~~~~~~~~~~~~~~~~~~WR~~~~~~~~~~~~~~-
                          2 - ~~~WRW~~~~~~~~~~~~~~~~~~WWR~~~~~~~~~~~~~|
                          3 - ~~~WWWW~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~|
        Total errors = 54 4 - ~~~WWWW~~~~~~~~~~~WWW~~~~~~~~~~~~~~~~~~~|
                          5 - ~~~WWRW~~~~~~~~~~~WWW~~~~~~~~~~~~~~~~~~~| Head
                          6 - ~~~~RWW~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~|   1
                          7 - ~~~~WRR~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~|
                          8 - ~~~~~RR~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~|
                          9 - ~~~~~RRWC~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~-


        Analysis:

             The above display shows many errors of different types.  The 
        problem could simply be a bad diskette.  If the problem occurs 
        with more than 1 formatted diskette of good quality, there is a 
        problem with the read/write mechanism of the drive.

             





















        Copyright (C) Microsystems Development 1987, 1988.            19





        TEST DRIVE (tm)                                     Version 1.2


        F6  Hysteresis Test


             Hysteresis is a measure of the drive mechanism's ability to 
        seek a specified track from either direction and position the 
        head in precisely the same position.  

             The head is moved to an inner track (toward the hub) and 
        then sent to the middle of the disk.  Measurements of alignment 
        are recorded and displayed.  The head is then sent to an outer 
        track and subsequently sent to the center again.  Measurements 
        are taken and compared to the previous center measurements to 
        determine the hysteresis.

             The hysteresis error is determined by the difference in the 
        center of the alignment pattern.  For example:  The first 
        alignment readings are +10 and -9 milli-inches.  This is to say 
        that the head is in such a position that data offset +10 and -9 
        milli-inches can be read.  The head is then sent to the outer 
        track and back to the center to again take readings of +10 and -9 
        milli-inches.  This is simply 0 milli-inches of hysteresis.  The 
        head had positioned itself at precisely the same position when 
        seeking a track from either direction.  If the second set of 
        readings were +9 and -10 the hysteresis would be 1.0 milli-inch.  
        In general, the center of each reading is compared to determine 
        the hysteresis.  The center of +10 and -9 is +0.5 and the center 
        of +9 and -10 is -0.5.  The difference is 1 milli-inch.

             Although these numbers are confusing the graphical 
        representation will make more sense.

             In this test, the alignment sensitivity is ignored and only 
        the center of the data pattern is used in determining hysteresis.  
        The actual alignment of the drive is unimportant in this test but 
        the repeatability of the positioning is crucial.  Disk drives 
        with excessive hysteresis are unreliable.  

        Display Information:

             TEST DRIVE uses two of the middle progressive offset tracks 
        on the DDD for this test:  tracks 16 and 19.  The horizontal bars 
        on the display span the distance from track centerline that the 
        drive was able to read successfully.  Each set of bars is for a 
        particular head and track, with the head having been positioned 
        there from opposite directions.  Ideally, each set of bars should 
        be equal in length.

        Adjustment:

             There is no adjustment and the drive should be discarded or 
        sent to the manufacturer for reconditioning.






        Copyright (C) Microsystems Development 1987, 1988.            20





        TEST DRIVE (tm)                                     Version 1.2


        A)  Sample display of a good drive


                           TEST DRIVE Hysteresis Test


                        <----------- m i l l i - i n c h e s ---------->
        H Tr Dir Error  -13-12-11-10 -9 -8 -7 -6 +6 +7 +8 +9+10+11+12+13
        - -- --- -----  |--|--|--|--|--|--|--|--|--|--|--|--|--|--|--|--|
        0 16 -->                 ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~
             <--  0.0            ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~

        1 16 -->                    ~~~~~~~~~~~~~~~~~~~~~~~~~~~~
             <--  0.5            ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~

        0 19 -->              ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~
             <--  0.5         ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~   

        1 19 -->                ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~
             <--  0.0           ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~


        Analysis:

             The above drive has no significant hysteresis.  Some error 
        is normal since data written too far off track center may be 
        read unreliably.  If the error is consistently greater, the drive 
        has a problem. 

             The drive also exhibits good sensitivity since it can read to 
        a minimum of +10 and -9 milli-inches. 


























        Copyright (C) Microsystems Development 1987, 1988.            21





        TEST DRIVE (tm)                                     Version 1.2


        B)  Sample display of a bad drive


                           TEST DRIVE Hysteresis Test


                        <----------- m i l l i - i n c h e s ---------->
        H Tr Dir Error  -13-12-11-10 -9 -8 -7 -6 +6 +7 +8 +9+10+11+12+13
        - -- --- -----  |--|--|--|--|--|--|--|--|--|--|--|--|--|--|--|--|

        0 16 -->                 ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~
             <--  2.0      ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~

        1 16 -->                    ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~
             <--  2.0         ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~

        0 19 -->                 ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~
             <--  1.5      ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~   
                                      
        1 19 -->                       ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~
             <--  2.5      ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~   


        Analysis:

             This drive has more hysteresis than normal and indicates a 
        possible problem with its positioning mechanism.

             For example, when head 1 is moved toward the spindle to 
        track 19 it can read data at 8 milli-inches away from the spindle 
        and 12 milli-inches toward the spindle.  When head 1 is moved 
        away from the spindle and is stopped at track 19, it can read 
        data at 12 milli-inches away from the spindle and 9 inches toward 
        the spindle.  This indicates that the head was not in the same 
        physical location.

             This drive would probably pass the alignment test however, 
        since in all the above cases it can read data to +/-8 milli-inches.  



















        Copyright (C) Microsystems Development 1987, 1988.            22





        TEST DRIVE (tm)                                     Version 1.2


        F7  Head Azimuth Test 


             Head rotation or azimuth is an indication of the angular 
        position of the head with respect to a line tangent to the track 
        centerline. If the head is "twisted", or "rotated", with respect 
        to the track centerline the data written to the diskette will be 
        "slanted" and will eventually cause problems when interchanging 
        diskettes with other drives.  

             For these measurements, TEST DRIVE uses the azimuth rotation 
        track (track 34) of the DDD.  This track has data written on 
        track centerline, but at increasingly greater angles, both toward 
        and away from the spindle.  The angle range from 21 to 42 minutes 
        of a degree.  If the drive's head is angled slightly out of 
        position, it will be able to read data on the tracks at one 
        angle, but will have problems with data written at the opposite 
        angles.


        Display information:
             
             For each successful read operation, the display shows four 
        slashes '/' or four reverse slashes '\'.  It will show four 
        capital x's if it was unable to read data written at a particular 
        angle.


        Adjustment:

             There is no adjustment for head azimuth in most drives, and 
        the head assembly or the entire drive should be replaced.

























        Copyright (C) Microsystems Development 1987, 1988.            23





        TEST DRIVE (tm)                                     Version 1.2


        A)  Sample display of a good drive


                        TEST DRIVE Head Azimuth Test
                                                                          /
            \                                                         /  /
             \  \                                                 /  /  /
              \  \  \                                         /  /  /  /
               \  \  \  \                                 /  /  /  /
                   \  \  \  \                         /  /  /  /          /
            X          \  \  \  \                 /  /  /  /          /  /
             X  \          \  \  \  \         /  /  /  /          /  /  /
              X  \  \          \  \  \  Head /  /  /          /  /  /  /
               X  \  \  \          \  \  1  /  /          /  /  /  /
                   \  \  \  \          \   /          /  /  /  /
                       \  \  \  \                 /  /  /  /
        \ = OK             \  \  \  \         /  /  /  /
                               \  \  \  Head /  /  /
        X = Error                  \  \  0  /  /
                                       \   /

        -42 -39 -36 -33 -30 -27 -24 -21    +21 +24 +27 +30 +33 +36 +39 +42
         <---------------------  Angular Rotation  ---------------------->
                  Angular position of head in minutes of a degree.



        Analysis:

             The above drive shows no problems with head azimuth.  Both 
        heads were able to acceptably read the data on the test tracks.


























        Copyright (C) Microsystems Development 1987, 1988.            24





        TEST DRIVE (tm)                                     Version 1.2


        B)  Sample display of a bad drive



                        TEST DRIVE Head Azimuth Test
        \                                                                 /
         \  \                                                         /  /
          \  \  \                                                 /  /  /
           \  \  \  \                                         /  /  /  /
               \  \  \  \                                 /  /  /  /
        \          \  \  \  \                         /  /  /  /          X
         \  \          \  \  \  \                 /  /  /  /          X  X
          \  \  \          \  \  \  \         /  /  /  /          X  X  X
           \  \  \  \          \  \  \  Head /  /  /          X  X  X  X
               \  \  \  \          \  \  1  /  /          X  X  X  X
                   \  \  \  \          \   /          X  X  X  X
                       \  \  \  \                 /  X  X  X
        \ = OK             \  \  \  \         /  /  X  X
                               \  \  \  Head /  /  X
        X = Error                  \  \  0  /  /
                                       \   /

        -42 -39 -36 -33 -30 -27 -24 -21    +21 +24 +27 +30 +33 +36 +39 +42
         <---------------------  Angular Rotation  ---------------------->
                  Angular position of head in minutes of a degree.




        Analysis:

             The above display indicates that Head 1 does not have an 
        azimuth problem, but that Head 0 may be rotated slightly in one 
        direction,  Head 0 was able to read all the data angled in one 
        direction, but could not read data angled at 27' or greater in 
        the opposite direction.





















        Copyright (C) Microsystems Development 1987, 1988.            25





        TEST DRIVE (tm)                                     Version 1.2


        F8  Hub Centering


             Hub Centering is a measure of how well the disk clamping 
        mechanism holds the disk media centered and rotates it in a 
        perfect circle.  

             The DDD has three test tracks for three levels of clamping 
        sensitivity, 7, 8 and 9 milli-inches.  These tracks are called 
        the alternate offset tracks.  Data is alternately offset +/- 7, 
        +/- 8 or +/- 9 milli-inches all around the disk.  All disks 
        should pass the 7 milli-inch test and some with perfect clamping 
        and good sensitivity will pass the 9 milli-inch test.  A drive 
        should be considered to be in good shape if the 8 milli-inch test 
        is passed.


        Display information:

             The display for hub centering shows 3 sinusoidal waveforms 
        each indicating results from different tracks.  A solid block 
        (indicated by a '~' in this document) is displayed for a 
        successful read, and an 'X' is displayed for an unsuccessful 
        read.

             The results for head 0 are displayed first, and the user is 
        given the option to test head 1 also.


        Adjustment:

             There generally is no adjustment for disk clamping or hub 
        centering.  Poor centering us usually an indication of a worn 
        out drive.


        Note:  The DDD does not have a reinforcing hub.  This is to        
               avoid any centering error that could be introduced by 
               the hub reinforcer ring.


















        Copyright (C) Microsystems Development 1987, 1988.            26





        TEST DRIVE (tm)                                     Version 1.2


        A)  Sample of a good drive     


                       TEST DRIVE Hub Centering Head 0 

                           ~   ~
                       ~           ~
                                       ~
                   ~       ~   ~
                       ~           ~       X
                                       ~                                   ~
        9 -->  ~   ~       ~   ~
                       ~           ~       ~   ~
                                       ~                               ~   ~
        8 -->  ~   ~                               ~
                                           ~   ~       ~           ~ 
                                                           ~   ~       ~   ~
        7 -->  ~                                   ~
                                               ~       ~           ~
                                                           ~   ~       ~
                                                   ~
        ~ = OK  X = Error                              ~           ~
                                                           ~   ~
               <-----------------  One Disk Revolution  ------------------->



        Analysis:

             This drive is functioning properly.  The 9 milli-inch test 
        shows an occasional error but this is acceptable.


























        Copyright (C) Microsystems Development 1987, 1988.            27





        TEST DRIVE (tm)                                     Version 1.2


        B)  Sample of a bad drive     


                       TEST DRIVE Hub Centering Head 0 

                           ~   X
                       X           ~
                                       X
                   ~       ~   X
                       X           ~       ~
                                       X                                   ~
        9 -->  X   ~       ~   ~
                       X           ~       ~   X
                                       ~                               X   ~
        8 -->  X   ~                               ~
                                           ~   X       X           ~
                                                           ~   X       X   ~
        7 -->  ~                                   ~
                                               ~       X           ~
                                                           ~   ~       ~
                                                   ~
        ~ = OK  X = Error                              ~           ~
                                                           ~   ~
               <-----------------  One Disk Revolution  ------------------->



        Analysis:

             The drive is not rotating the disk in a perfect circular 
        fashion.  Errors may be tolerated at 9 milli-inches but never at 
        7 milli-inches.  This indicates that as the disk is rotating, 
        with the head in a fixed position, the data track is not 
        consistently under the head.























        Copyright (C) Microsystems Development 1987, 1988.            28





        TEST DRIVE (tm)                                     Version 1.2


        F9  Continuous Alignment


             The continuous alignment test is provided as a way to `zero 
        in' on a particular head and track and take continuous 
        measurements.

             The test defaults to head 0, track 19, but by using the 
        left, right, up and down arrows, the user can select any of the 
        progressive offset tracks on the DDD.

             When the continuous alignment test begins to run, it will 
        first test for the presence of the Dysan DDD.  If it is present, 
        the test will proceed.  If it is not, the operator is given the 
        opportunity to override and continue anyway.  If the drive is so 
        poorly adjusted that TEST DRIVE cannot sense the Dysan disk, the 
        override feature allows the operator to at least start the test, 
        presumably so that a technician can attempt adjustment.  If the 
        user selects the override feature, and a non-Dysan DDD is 
        inserted, TEST DRIVE will report "Unable to read any data on 
        disk" for each measurement trial.     

        Display information:

             The horizontal bars on the display span the distance from 
        track centerline that the drive was able to read.  When new 
        measurements are taken, the previous bars are scrolled down, and 
        the current measurements are displayed on the top line.  If the 
        head or track is switched, all previous measurements are cleared 
        before new data is displayed.


        Adjustments:

             If you attempt to make alignment adjustments, you can do so 
        while the continuous alignment test is running.  The test will 
        continually report any change.  Keep in mind that a disk drive is 
        a precision instrument.  If the data pattern shows a 2 milli-inch 
        shift, this is indicating the physical positioning needs to be 
        shifted 1/1000 of an inch to gain symmetry.  This is a very small 
        distance.  Once you start to move the head assembly, the 
        alignment may worsen.  

             In any case, when adjusting the heads be careful not to 
        cause damage to the DDD.
             











        Copyright (C) Microsystems Development 1987, 1988.            29





        TEST DRIVE (tm)                                     Version 1.2


        A)  Sample display of a good drive


                      TEST DRIVE Continuous Alignment Test


                       <----------- m i l l i - i n c h e s ---------->
                       -13-12-11-10 -9 -8 -7 -6 +6 +7 +8 +9+10+11+12+13
                       |--|--|--|--|--|--|--|--|--|--|--|--|--|--|--|--|

              Current >         ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~
             Previous           ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~
                                ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~
                                ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~
                                ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~
                                ~~~~~~~~~~~~~~~~~~~~~~~~~~~~
                                ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~
                                ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~
                                ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~
                                ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~
                                ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~

        Use the up & down arrows >  Head 0  Track 19 < Use the left & right
        to switch heads                             arrows to switch tracks



        Analysis:

             The above drive appears to be perfectly aligned, as 
        evidenced by the fact that it can read data at equal distances on 
        either side of track center.  If other tracks and the other head 
        also display good results, alignment can be considered excellent.

             Sensitivity is 20 (10 + 10) which is also very good.

             Keep in mind, that some variations in the above display are 
        normal, particularly at the sides.  Data written greater than 8 
        milli-inches from track center may be read unreliably.  If this 
        test display were to show some slight variation in alignment or 
        sensitivity, it does not necessarily mean that the drive is in 
        need of adjustment.  

             Some variation is normal since data written too far off 
        track center may be read unreliably.












        Copyright (C) Microsystems Development 1987, 1988.            30





        TEST DRIVE (tm)                                     Version 1.2


        B)  Sample display of a bad drive


                      TEST DRIVE Continuous Alignment Test


                       <----------- m i l l i - i n c h e s ---------->
                       -13-12-11-10 -9 -8 -7 -6 +6 +7 +8 +9+10+11+12+13
                       |--|--|--|--|--|--|--|--|--|--|--|--|--|--|--|--|

              Current >   ~~~~~~~~~~~~~~~~~~~~~~~~~~~~
             Previous  ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~
                       ~~~~~~~~~~~~~~~~~~~~~~~~~~~~
                          ~~~~~~~~~~~~~~~~~~~~~~~~~~~~
                       ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~
                       ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~
                       ~~~~~~~~~~~~~~~~~~~~~~~~~~~~
                          ~~~~~~~~~~~~~~~~~~~~~~~~~~~~
                       ~~~~~~~~~~~~~~~~~~~~~~~~~~~~
                       ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~
                       ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~

        Use the up & down arrows >  Head 0  Track 19 < Use the left & right
        to switch heads                             arrows to switch tracks


        Analysis:

             The above drive shows poor alignment since the horizontal 
        bars are all skewed to one side.  It is definitely in need of 
        adjustment.  

             The head is shifted slightly away from the spindle as 
        indicated by the higher negative values.  Sensitivity is 19 (6 + 
        13 or 7 + 12), which is good.  Therefore, this drive can probably 
        be adjusted to within acceptable tolerances.





















        Copyright (C) Microsystems Development 1987, 1988.            31





        TEST DRIVE (tm)                                     Version 1.2


        F10  Cleaning Utility


             The disk read/write heads may in time build up a deposit of 
        oxide, smoke or dust particles that will adversely effect the 
        sensitivity of the heads.  Depending on the amount of buildup, 
        cleaning may improve the performance of the disk drive. 

             The TEST DRIVE cleaning utility is designed to be used with 
        a standard cleaning disk and cleaning solution.  It will rotate 
        the disk for a set length of time, and move the heads across the 
        surface of the cleaning disk.  

             Most manufacturers of cleaning disks recommend that you 
        invoke a DIR command and continue the drive motion for about 30 
        seconds.  This will cause the head to seek to track zero looking 
        for the directory information.  In doing this, the only portion 
        of the cleaning disk that is used is the portion physically 
        located where track zero is supposed to be (the outer edge).  The 
        TEST DRIVE cleaning utility will move the head across the disk 
        from track 0 to track 39.  Each cycle from track 0 to 39 takes 
        approximately 10 seconds.  By using the cleaning utility in 
        conjunction with a standard cleaning disk you will get more 
        efficient usage of the cleaning disk and more efficient cleaning 
        of the heads.

             Most drive cleaners recommend that you use the cleaning disk 
        only 10 to 20 times before discarding.  Since the head itself is 
        physically less that 1/8 inch wide, and it can be moved almost 1 
        inch across the disk, it stands to reason that if the head 
        positioning is varied and you follow manufacturers advice, you 
        can expect to obtain 80 or more cleanings from a single cleaning 
        disk.  


        Drive cleaning tips:

             Does cleaning really help?  We recommend that you monitor 
        head sensitivity with TEST DRIVE before and after you clean the 
        heads to illustrate what effect the cleaning has on the 
        performance of the heads.  Sensitivity is a measure of how well 
        the heads read.  The General Test and the Alignment Test indicate 
        sensitivity in the +x to -x readings.  The larger the span 
        between the + and - numbers the greater the sensitivity.  Take 
        note of the sensitivity before cleaning and after.  If the 
        sensitivity did not increase the heads didn't need cleaning. 

             Are cleaning disks harmful to the drives?  The cleaning 
        media in the revolving  disk cleaners must be stiff to allow for 
        the hub to clamp and spin it.  This stiff characteristic 
        generally means that the cleaner is somewhat abrasive also.  
        Excessive usage of abrasive cleaning disks may cause excessive 
        wear on the heads, but occassional cleaning is not harmful.

             


        Copyright (C) Microsystems Development 1987, 1988.            32





        TEST DRIVE (tm)                                     Version 1.2


             How often should floppy disk drives be cleaned?  One 
        cleaning disk manufacturer recommends daily cleaning, most all 
        recommend cleaning at least once a week.  However, we recommend 
        that you clean your drive only when needed based on usage and 
        environment.  If the environment is smoky or dusty the heads will 
        build up a deposit quickly.  In an extremely clean location the 
        heads will require less cleaning.  The amount of usage the drive 
        receives will only slightly effect the cleaning requirements.  
        Since the time the head is in contact with the media is generally 
        so short, this does not have as much effect as the environment.  
        In a generally clean environment with moderate usage a disk drive 
        may require cleaning every 3 to 4 months, but there are no hard 
        and fast rules.  The best indicator of when to clean your drives 
        can be obtained by using TEST DRIVE to periodically check their 
        performance. 

             What is the best way to clean disk drives?  Any standard 
        cleaning disk is acceptable.  It appears as though there are only 
        a few manufacturers that provide several name brand distributors.  
        We recommend that a lint free cloth saturated in a good cleaning 
        solvent be used if access to the head assembly if possible.  If 
        the access is limited be careful not to disturb the alignment by 
        moving the head assembly.  The commercially available cleaning 
        solution provided with cleaning disks is generally a form of 
        isopropyl alcohol and freon.  This is fine to use but isopropyl 
        alcohol by itself is sufficient to do the job.  The purer it is, 
        the better.  Ninety-one percent isopropyl alcohol is available in 
        many drug stores, and 99% is rarer but still available.  





























        Copyright (C) Microsystems Development 1987, 1988.            33





        TEST DRIVE (tm)                                     Version 1.2


                                GLOSSARY OF TERMS



        1.2MB          1200 x 1024 or 1,228,800 bytes.  The amount of 
                       data stored on a high density diskette,  High 
                       density drives are normally found in AT type 
                       computers.

        360KB          360 * 1024 or 368,640 bytes.  The amount of data 
                       stored on standard 5 1/4 inch diskette.

        720KB          720 * 1024 or 737,280 bytes.  The amount of data 
                       stored on a 3 1/2 inch diskette.

        Alignment      The measure of how centered the Read/Write head is 
                       over the track centerline.  Sometimes referred to
                       as Radial Alignment.

        Alignment      The measure of how much of the track the head will 
        Sensitivity    respond to.  In a 48 TPI drive, if the head reads 
                       -11 to +10 milli-inches the head is sensitive to 
                       21 milli-inches of data and is very good.  If the 
                       head reads -8 to +7 milli-inches of data the 
                       sensitivity is 15 milli-inches and is poor.
          
        Alternate      Alternate offset refers to the data pattern on the 
        Offset         centering test tracks.  There are 3 tracks used 
                       for this test.  Data is written at +/- 7 milli-
                       inches on the first, +/- 8 on the second, and 
                       +/- 9 on the third.
         
        Azimuth        The angular displacement of the Read/Write Head
                       relative to a line tangent to the track center 
                       line.

        BIOS           Basic Input/Output System.  The built functions of 
                       a computer to facilitate many functions including 
                       disk reads and writes.

        Centering      The ability of the disk clamping mechanisms to 
                       clamp on the diskette precisely in the center of 
                       the disk and spin the disk in a perfect circle.  
                       See Alternate Offset.  Sometimes referred to as 
                       eccentricity.

        Clamping       See Centering. 

        CRC            Cyclic Redundancy Check.  A type of error checking 
                       used by the computer's BIOS to help insure 
                       integrity of data on a diskette.

        Cylinder       A set of concentric equal size tracks, stacked on 
                       top of one another.  Usually used when discussing 
                       hard disks, but sometimes with diskettes also.


        Copyright (C) Microsystems Development 1987, 1988.            34





        TEST DRIVE (tm)                                     Version 1.2



        Diskette       The magnetic media inserted into a floppy disk 
                       drive, used to store information.     

        DDD            Digital Diagnostic Disk, manufactured by Dysan 
                       Corporation.  Contains data patterns written at 
                       precise angles and distances from track center. 

        Eccentricity   See Centering.

        Head           The portion of the drive that reads and writes the 
                       stored magnetic information from the diskette.

        Hub            The center of the diskette sometimes reinforced 
                       with ring.

        Hysteresis     A measure of the drive mechanism's ability to seek 
                       to a specified track from either direction and 
                       position the head at precisely the same distance 
                       from the center.

        Milli-inch     One 1/1000th of an inch.

        Minute         One 1/60th of a degree.  Used to measure the 
                       rotational position or azimuth of a head relative 
                       to track centerline.

        Progressive    Progressive offset refers to the data pattern on
        Offset         the alignment test tracks.  The pattern starts at 
                       -/+6 milli-inches and progresses to -/+13 milli-
                       inches.  The data progressively gets farther away 
                       from track center.

        Radial         See Alignment
        Alignment                          

        RPM            Revolutions per minute, the number of times the 
                       disk spins around in 1 minute. 

        Sector         A slice of a track containing data, like a piece 
                       of a pie.  Each track contains a number of 
                       sectors.  For 360KB drives, there are 9 sectors 
                       per track.  High density 1.2MB drives use 15 
                       sectors per track.

        Seek           The process of moving the drive's head to a
                       particular track.

        Sensitivity    See Alignment Sensitivity

        Spindle        The mechanism in the disk drive used to spin the
                       diskette. 





        Copyright (C) Microsystems Development 1987, 1988.            35





        TEST DRIVE (tm)                                     Version 1.2


        Spindle Speed  The angular rotational speed of the diskette 
                       media, or how fast the disk spins around.  This is 
                       measured in revolutions per minute (rpm).

        TPI            Tracks per inch.  The density of tracks on a disk.  
                       For example:  A 48 TPI disk will have 48 tracks 
                       per inch, each track spaced 1/48 of an inch apart.  
                       A disk with 40 tracks will utilize 40/48ths of an 
                       inch on the disk.
                  
        Track          A circle around a disk made up of a number of 
                       sectors.  Sometimes called a cylinder.


               










































        Copyright (C) Microsystems Development 1987, 1988.            36





        TEST DRIVE (tm)                                     Version 1.2


                             CUSTOMER FEEDBACK FORM

        Your comments, suggestions, criticisms, etc. are most welcome.  
        They help us bring you a quality product at a reasonable price.  
        Just fill out this form and send it to us. 


        Brand and model of computer:_____________________________________

        Comment( ) Suggestion( ) Criticism( ) Problem( ) Other___________


        _________________________________________________________________

        _________________________________________________________________

        _________________________________________________________________

        _________________________________________________________________

        _________________________________________________________________

        _________________________________________________________________

        _________________________________________________________________

        _________________________________________________________________

        _________________________________________________________________

        _________________________________________________________________


             Name:    ________________________________________________

             Company: ________________________________________________

             Address: ________________________________________________

             City, State, Zip: _______________________________________

             Phone:  (__________) ____________________________________


        Do you need a reply?_________ Are you a registered user?_________  

        We guarantee a reply to all registered users who request one. 

        Microsystems Development may use the information you supply 
        without incurring any obligation whatsoever.

             Mail this form to:  Microsystems Development
                                 4100 Moorpark Ave.  #104
                                 San Jose, CA  95117  USA



        Copyright (C) Microsystems Development 1987, 1988.            37