Tseng ET4000 - Windows 3.1 BETA Drivers
			       10/29/91


Copy all of the supplied files to a 5 1/4" HD or 3 1/2" HD diskette.


INSTRUCTIONS - FIRST TIME WINDOWS 3.1 BETA INSTALLATION

Choose the "Other (Requires disk provided by a hardware manufacturer)"
option within the Windows 3.1 BETA setup program for display type.
See the Windows 3.1 BETA documentaion for further information.


INSTRUCTIONS - ALREADY INSTALLED WINDOWS 3.1 BETA

Choose the "Other (Requires disk provided by a hardware manufacturer)"
option within the Windows 3.1 BETA setup program for display type.
See the Windows 3.1 BETA documentaion for further information.


ADDITIONAL INFORMATION:

	Supplied files:

		VGA443.DRV
		VGA448.DRV
		VGA463.DRV      USES 8514 FONTS
		VGA463S.DRV     USES VGA FONTS
		VGA464.DRV	USES 8514 FONTS
		VGA464S.DRV	USES VGA FONTS
		VGA468.DRV	USES 8514 FONTS
		VGA468S.DRV 	USES VGA FONTS
		VGA474.DRV
		VGA478.DRV
		VGA414.DRV
		VGAMONOX.GR2
		VGACOLRX.GR2
		VDDTLI4.386
		OEMSETUP.INF    SETUP FILE FOR WINDOWS
		README.DOC	THIS DOCUMENT
                WIN30DRV.DOC	HOW TO USE THESE DRIVERS WITH WIN 3.0 & 3.0a

                                IMPORTANT
                                *********
When you run the Windows Setup to change to a different driver Windows may
prompt you for some of the Windows Installation diskettes. The drivers use 
display fonts which are contained on the standard Windows distribution
diskettes.

The enclosed drivers are generic and should work with most ET4000 based boards.
The drivers have various display memory requirements and of course your display
monitor and display card must be able to support the resolution you select.

The drivers support the following:

 Resolution	Mode 	Minimum display     Driver name         Windows Font
                (HEX)   memory required
 640x480x2	11h          256kb	    VGAMONO.DRV  **     VGA
 640x480x16	12h          256kb          VGA.DRV      **     VGA
 800x600x16	29h	     256kb          VGA464.DRV          8514
 800x600x16	29h	     256kb          VGA464S.DRV         VGA
1024x768x16	37h	     512kb          VGA474.DRV          8514
1280x1024x16	3Dh	     1 meg          VGA414.DRV          8514
 640x480x256	2Eh	     512kb          VGA448.DRV          VGA
 640x480x32k	2Eh xx	     1 meg          VGA443.DRV          VGA
 800x600x256	30h	     512kb          VGA468.DRV          8514
 800x600x256	30h	     512kb          VGA468S.DRV         VGA
 800x600x32k	30h xx	     1 meg          VGA463.DRV          8514
 800x600x32k	30h xx	     1 meg          VGA463S.DRV         VGA
1024x768x256	38h	     1 meg          VGA478.DRV          8514

** uses Windows 3.1 BETA supplied VGA driver
xx requires a ET4000 BIOS which supports the Tseng/Sierra HICOLOR mode

                                IMPORTANT
				*********
It is important that the drivers be installed properly, replacement
grabbers (GR2 extension) and Virtual-Display-Device handler (386 extension) are
included to properly support the extended feature set of the ET4000 VGA chip.

If you encounter a problem please report it to Tseng Labs, Inc.
Please, attempt to reproduce any problem you encounter using the standard
Windows 3.1 supplied VGA and SVGA drivers (VGA 640x480x16 and SVGA 800x600x16).

You may report a problem by sending mail or a FAX containing the information to
reproduce the problem to:

	Tseng Labs, Inc.
	Newtown Industrial Commons
	10 Pheasant Run
	Newtown, PA 18940
	FAX # (215) 860-7713
	ATTN: TSENG WIN 3.1 DEVELOPMENT

At this time, the enclosed drivers are based on the Windows 3.0 DDK.
As other drivers become available we will provide them on Compuserve.

Thank You for your support !!!!!!!