TABLET.COM(TM) is a tablet driver which can emulate Microsoft(R)'s
Mouse.com driver. TABLET.SYS is a system file that can be used in your
CONFIG.SYS file. TABLET.COM is a TSR (Terminate and Stay Resident) program that
can be run from the DOS command prompt or from a batch file, including the
autoexec.bat.

TABLET.SYS and TABLET.COM should  NOT  be loaded at the same time.

Usage: DEVICE=TABLET.SYS [Com Port] [Pointing Device] [Options]
      or
       TABLET.COM [Com Port] [Pointing Device] [Options]

Where: Com Port = /1       for Com Port 1   <DEFAULT>
                  /2       for Com Port 2
                  /3       for Com Port 3, PS/2 models only
                  /4       for Com Port 4, PS/2 models only
         	  /BAxxxx  selects serial port with base address xxxx (in HEX)
		  /Ix      selects serial port with IRQ line number x
			   (allowable IRQ 2 through 7)
                  /OFF     to disable the driver

       Pointing
       Device =   /C4      for four-button cursor
                  /CP      for stylus  <DEFAULT>

OPTIONS:          /A    Absolute Tracking
                  /R    Relative Tracking  <DEFAULT>
                        (Following options work in relative mode only)
                  /S##  Sets both horizontal and vertical sensitivity -
                        Range = 0 - 99, Default = 50
                  /H##  Sets only the horizontal sensitivity -
                        Range = 0 - 99, Default = 50
                  /V##  Sets only the vertical sensitivity -
                        Range = 0 - 99, Default = 50

NOTES:		    - When selecting a serial port other than 1,2,3 or 4, the
                      /BA and /I options must be used together.

		    - When using the /BA option, all four digits must be 
                      specified (Example:  for Com 1 - /BA03F8)

                    - Use the /BA and /I options only when a non-standard
                      serial address is used in the computer.


Serial Port Address Table

Command Line	Serial	   Serial Port	 System
Switch		Port	   Address
------------------------------------------------------------------------------
/1		1	   03F8 Hex	 All (PC, XT, AT, 386, and any PS/2)
/2		2	   02F8 Hex	 All (PC, XT, AT, 386, and any PS/2)
/3		3	   3220 Hex	 Any PS/2
/4		4	   3228 Hex	 Any PS/2
------------------------------------------------------------------------------