UIOF.COM       SummaSketch II Set UIOF Format Utility
Copyright Summagraphics Corporation 1990, 1991.   All rights reserved.

UIOF transmits a two character command (zu) to the tablet out the selected
serial port. This will switch the tablet from MM to UIOF format.

Usage: UIOF [ options ]
    /1  (default) selects serial port 1 {PC, XT, AT, PS/2}
    /2  selects serial port 2 {PC, XT, AT, PS/2}
    /3  selects serial port 3 {PS/2 only}
    /4  selects serial port 4 {PS/2 only}
    /5  selects serial port 5 {PS/2 only}
    /6  selects serial port 6 {PS/2 only}
    /7  selects serial port 7 {PS/2 only}
    /8  selects serial port 8 {PS/2 only}
    /BAxxxx  selects serial port with base address of xxxx (in HEX)
    /N  selects no parity configuration
    /? or /H  displays help screen

Notes: -When using the BA option (Base Address) all four digits must be
        specified.  (example: for COM 1 - /BA03F8)
       -This program transmits in the SummaSketch default serial communication
        configuration which is 9600 baud, 8 data bits, odd parity, and
        1 stop bit.
       -Use the /BA switch only when the serial port is located at a non-
        standard address within the computer.
       -A summary of command line switches are always available by starting
        the program with the /? or /H switch.


Serial Port Address Table

Command Line	Serial	   Serial Port	 System
Switch		Port	   Address		
------------------------------------------------------------------------------
/1		1	   03F8 Hex	 All (PC, XT, AT, 386, and any PS/2)
/2		2	   02F8 Hex	 All (PC, XT, AT, 386, and any PS/2)
/3		3	   3220 Hex	 Any PS/2
/4		4	   3228 Hex	 Any PS/2
/5		5	   4220 Hex	 Any PS/2
/6		6	   4228 Hex	 Any PS/2
/7		7	   5220 Hex	 Any PS/2
/8		8	   5228 Hex	 Any PS/2
------------------------------------------------------------------------------