Tseng ET4000 - Windows 3.0 and 3.0a Display Drivers

INSTRUCTIONS - FIRST TIME WINDOWS 3.0 and 3.0a INSTALLATION

Follow the instructions contained in the WIN30DRV.DOC file to install the
Tseng ET4000 display drivers.


INSTRUCTIONS - WINDOWS 3.0 or 3.0a ALREADY INSTALLED

To use the Tseng ET4000 Windows drivers you need to copy the following
files into the \WINDOWS\SYSTEM subdirectory.

				VGA443.DRV
				VGA448.DRV
				VGA463.DRV      USES 8514 FONTS
				VGA463S.DRV     USES VGA FONTS
				VGA464.DRV	USES 8514 FONTS
				VGA464S.DRV	USES VGA FONTS
				VGA468.DRV	USES 8514 FONTS
				VGA468S.DRV 	USES VGA FONTS
				VGA474.DRV
				VGA478.DRV
				VGA414.DRV
				VGAMONOX.GR2
				VGACOLRX.GR2
				VDDTLI4.386
				SETUP.INF       SETUP.INF FOR WINDOWS 3.0
                                SETUP.W3A	SETUP.INF FOR WINDOWS 3.0a

If you have ALREADY installed Windows 3.0, you can copy the above list of
files into the \WINDOWS\SYSTEM subdirectory. After you copy the files, change
the display configuration from within Windows itself to one of the extended
drivers. See the Windows documentation for further information.

                                IMPORTANT
If you have Windows 3.0a, you also need to copy the SETUP.W3A file as SETUP.INF
before you run the SETUP program.


When you run the Windows Setup to change to a different driver Windows may
prompt you for some of the Windows Installation diskettes. The drivers use 
display fonts which are contained on the standard Windows distribution
diskettes.

The enclosed drivers are generic and should work with most ET4000 based boards.
The drivers have various display memory requirements and of course your display
monitor must be able to support the resolution you select.

The drivers support the following:
 Resolution	Mode 	Minimum display     Driver name         Windows Font
                (HEX)   memory required

 640x480x2	11h          256kb	    VGAMONO.DRV  **     VGA
 640x480x16	12h          256kb          VGA.DRV      **     VGA
 800x600x16	29h	     256kb          VGA464.DRV          8514
 800x600x16	29h	     256kb          VGA464S.DRV         VGA
1024x768x16	37h	     512kb          VGA474.DRV          8514
1280x1024x16	3Dh	     1 meg          VGA414.DRV          8514
 640x480x256	2Eh	     512kb          VGA448.DRV          VGA
 640x480x32k	2Eh xx	     1 meg          VGA443.DRV          VGA
 800x600x256	30h	     512kb          VGA468.DRV          8514
 800x600x256	30h	     512kb          VGA468S.DRV         VGA
 800x600x32k	30h xx	     1 meg          VGA463.DRV          8514
 800x600x32k	30h xx	     1 meg          VGA463S.DRV         VGA
1024x768x256	38h	     1 meg          VGA478.DRV          8514

** uses Windows 3.0 or 3.0a supplied VGA driver
xx requires a ET4000 BIOS which supports the Sierra HICOLOR mode

                                IMPORTANT
It is important that the drivers be installed properly, replacement
grabbers (GR2 extension) and Virtual-Display-Device handler (386 extension) are
included to properly support the extended feature set of the ET4000 VGA chip.