SpeedSTAR DRIVER INSTALLATION
                    FOR MICROSOFT WINDOWS 3.0

The instructions which follow are applicable to users of 
Microsoft Windows 3.0 and the SpeedSTAR SVGA. Note that, to use 
800x600 and 1024x768 modes, an ANALOG color display capable of
these high resolutions is required.

The "SpeedSTAR SVGA - Windows 3.0 Driver Disk" contains 256 color 
and high-resolution drivers, as well as a file called SETUP.INF 
that replaces the files of the same name on the Microsoft Windows 
3.0 Setup 5.25" "DISK 1" diskette. Follow the instructions listed 
below carefully to install the drivers.

Instructions:

1. Make a DISKCOPY of the Setup "Disk 1" diskette.  
   Example (for systems with a single floppy and hard drive):

         C:>DISKCOPY A: A:

   The system will use drive A: for both the original and the 
   copy as the source and target diskettes are inserted 
   alternately for the copy.

2. After the copy is made, return the original to its jacket and 
   store safely.

3. Copy the file SETUP.INF from the SpeedSTAR SVGA - Windows 3.0 
   Driver Disk to the newly-created copy of the Setup "Disk 1" 
   diskette. Example (for systems with a single floppy and hard 
   drive):

         C:>COPY A:SETUP.INF B:

   The system will use drive A: as drive B: also. After the copy 
   is finished, type A: [ENTER].

4. Type SETUP [ENTER] to begin installation of Windows 3.0.

5. Review the configuration list when it is shown. If you wish to 
   change Display type, move the cursor (highlighted line) to the 
   "Display:" line and press [ENTER] to select from the available 
   list. 

6. The program will ask you to insert the SpeedSTAR SVGA - 
   Windows 3.0 Driver Disk in order to install the drivers as 
   required. After this is done, the installation program will 
   continue normally.

After you complete the above steps you can begin using Windows 3.0.

Note: If you wish to change the display type after completing the 
installation, click on the Windows Setup icon found in the Main 
desktop window.