1
-
-
-
-
-
                          Program Documentation
                                   for
                                  BESTOP
-
-
-
-
-
-
-
-
0                                          
                                                  
                                                      
-

-
-
                              DATE PREPARED:
                              FEBRUARY 1989
1                           TABLE_OF_CONTENTS
+                           _____ __ ________

0I.__FOREWORD                                                           1
+__  ________
0II.__INTRODUCTION                                                      2
+___  ____________
   A.  Background                                                       2
   B.  Program Control                                                  2
   C.  Data Constants And Work Areas                                    4
0III.__INSTRUCTION_SPECIFICATIONS                                       7
+____  ___________ ______________
   A.  Instructions                                                     7
   B.  Conditional Instructions                                         8
     1.  IF (Character Field Comparison)                                9
     2.  IF (Numeric Field Comparison)                                 10
     3.  IF (Multiple Comparison)                                      10
     4.  IF (character comparison)                                     11
     5.  IF (Control Break)                                            12
     6.  IF (Printer Line Test)                                        12
     7.  IF (Condition Test)                                           12
     8.  OTHERWISE                                                     13
     9.  UNCONDITIONAL                                                 13
   C.  Data Movement Instructions                                      14
     1.  MOVE                                                          14
     2.  EDIT                                                          14
     3.  CLEAR                                                         15
   D.  Arithmetic Instrictions                                         15
     1.  ADD                                                           15
     2.  SUBTRACT                                                      16
     3.  MULTIPLY                                                      16
     4.  DIVIDE                                                        16
   E.  Output And Control Instructions                                 17
     1.  WRITE (Numbered Files and Punch File)                         17
     2.  WRITE (Listing with Spaces)                                   18
     3.  WRITE (Listing with Skip to Numbered Line)                    18
     4.  Write (Space Printer without Printing)                        18
     5.  WRITE (Skip to Numbered Line without Printing)                18
     6.  GET                                                           19
     7.  HALT                                                          19
   F.  Soubroutine Linkage Instruction                                 19
     1.  SUBROUTINE                                                    20
     2.  RETURN                                                        20
     3.  BRANCH                                                        20
   G.  Table Lookup Instructions                                       20
     1.  TABLE DEFINITION                                              21
     2.  TABLE ENTRY                                                   21
     3.  LOOKUP                                                        21
   H.  Matched File Control                                            22
     1.  MATCH KEYS                                                    24
   I.  Advanced Techniques                                             24
     1.  FIND                                                          24
     2.  MOVE (to displaced field)                                     25
     3.  MOVE (from displaced field)                                   26
     4.  DO AGAIN                                                      27
0IV.__PROGRAMMING_TECHNIQUES                                           29
+___  ___________ __________
   A.  Routines                                                        29
0
                                   -i-
1  B.  Subroutines                                                     30
   C.  Tables                                                          32
   D.  Matched Input Files                                             34
   E.  Page Format Control                                             36
   F.  Summarizing Data                                                38
0V.__PROGRAM_DEBUGGING                                                 42
+__  _______ _________
   A.  Compilation Diagnostics                                         42
   B.  Instruction Diagnostics                                         42
   D.  Record Counts And File Dumps                                    44
   E.  Test Runs                                                       45
0VI.__APPENDIX_A_-_OS/370_OPERATING_INSTRUCTIONS                       46
+___  ________ _ _ ______ _________ ____________
   A.  Job Control Language                                            46
   B.  JOB Statement                                                   46
   C.  EXEC Statement                                                  46
   D.  STEPLIB Card                                                    47
   E.  DD Statements                                                   47
   F.  Completion Codes                                                48
   G.  External Tables                                                 49
0VII.__APPENDIX_B_-_MAXIMUM_FIELD_SIZES                                50
+____  ________ _ _ _______ _____ _____
0VIII.__APPENDIX_C_-_EIA_IMPLEMENTATIONS_OF_BESTOP                     51
+_____  ________ _ _ ___ _______________ __ ______
   A.  BESTOP50, BESTOPVL, BEST400                                     51
   B.  SUPERB                                                          51
   C.  BESTOP                                                          51
-
-
-
-
-
-
-
-
-
-
0
                                  -ii-
1
                                  BESTOP
 ________________________________________________________________________


                               I.__FOREWORD
+                              __  ________
0
      This document is a revised text originally written in November 1971
 by   the   Office   of   Research   and   Statistics,   Social  Security
 Administration.  This new documentation includes some new  features  and
 other enhancements.

      This program product has performed exceedingly well for a number of
 years  at  this  istallation.   But no guarantee is expressed or implied
 that this program will necessarily perform in accordance with the  users
 specified needs.



-
-
-
-
-
-
-
-
-
-
-
-

 ________________________________________________________________________

                                   -1-
1
                                  BESTOP
 ________________________________________________________________________


                            II.__INTRODUCTION
+                           ___  ____________
0
      A.__Background
+     __  __________

      The  original  Business  Economics  Statistical  Operations Program
 (BESTOP) was developed by the Office of Business Economics  (OBE),  U.S.
 Department  of  Commerce, in 1965.  Since that time it has been extended
 both by OBE and by other organizations to whom the program has been made
 available.  The  BESTOP  language  is  the  principal  one  in  use  for
 applications programming in OBE and has been used extensively by several
 other  agencies  of  the Federal Government.  While there is no accurate
 estimate of the number of programs that have been written in BESTOP,  it
 numbers in the tens of thousands in OBE alone.

      BESTOP was developed to meet a requirement for fast turnaround on a
 large number of relatively short jobs.  It has been used successfully by
 programmers  and  non-programmers alike and is particularly effective in
 report writing, file maintenance, and similar applications.

      The BESTOP Compiler produces an executable program in  memory  from
 BESTOP  source  statements.   Machine  code  is assembled in line as the
 statements are read.  The program is executed when  the  last  statement
 has been processed unless an error is detected in the program.

      The  syntax  of  the  BESTOP  language permits the diagnosis of all
 syntactical errors during the  translation  process.   Such  errors  are
 noted  on  a  printed  listing  of  the  source  statements  and must be
 corrected before the  program  can  be  executed.   A  program  that  is
 syntactically  correct  is  executed.   A  program that is syntactically
 correct is executed immediately and will not stop until all of the input
 records have been processed or a "HALT" instruction is executed  in  the
 program.   The  program will not normally "hang up" without a diagnostic
 message although some care must be taken to  avoid  program  loops  when
 writing subroutines.  In addition to the compilation diagnostics, record
 counts  and  partial  file  dumps are produced as an aid to checking the
 results of a run.

      B.__Program_Control
+     __  _______ _______

      A  BESTOP  program consists of a specialized record reading routine
 followed by an object program that is compiled from BESTOP  instructions
 as  shown  in  figure  1.  In the execution of a program, control passes
 first to the record reading routine to read a record (or two records  in
 the  case  of  matched file operations), then to the object program, and
 then back to the reading routine.  This  cycle  is  repeated  until  the
 input  file  is exhausted or until a HALT instruction is executed in the
 object program.


0
 ________________________________________________________________________

                                   -2-
1
                                  BESTOP
 ________________________________________________________________________


                             ________________
                             |  Specialized |
                             |    Record    |
                     |------>|    Reading   |
                     |       |    Routine   |
                     |       |______________|
                     |              |
                     |              |
                     |    __________v__________
                     |    | Object Program    |
                     |____| Produced from the |
                          | Instructions Cards|
                          |___________________|


            Figure 1.  The flow of Control in a BESTOP Program


      Not  all  of  the  instructions  will  be executed during each pass
 through  the  object  program.   Conditional  instructions  permit   the
 specification  of  tests  that  must  be  met  before  other  processing
 instructions will be executed.  Other  non-executable  instructions  are
 provided for the creation of tables and subroutines.

      The  program attempts to execute all of the processing instructions
 in each pass through the object program  unless  a  GET  instruction  is
 executed.   The GET instruction causes an immediate return to the record
 reading routine to get the next record and processing then resumes  with
 the first instruction in the program.

      After  the last input record has been processed, there is one "last
 pass" through the object program to execute any instructions  that  must
 be  executed at the end of the run.  Other instructions are not executed
 in the last pass.

      The record reading routine is automatic and is always performed  by
 the  record  reading  routine.   The  specific  file(s)  to  be  read is
 specified in a job control language parameter.  If two files are  to  be
 read simultaneously, a special sequence key instruction must be included
 at the beginning of the program to provide routine.

      To  write  records, one or more WRITE instructions must be included
 in the object program.  The WRITE  instruction  also  provides  vertical
 spacing control when printing.

-
-

 ________________________________________________________________________

                                   -3-
1
                                  BESTOP
 ________________________________________________________________________


      C.__Data_Constants_And_Work_Areas
+     __  ____ _________ ___ ____ _____

      All  of  the  data  that is processed by the object program must be
 contained in tables, instruction constants, or one  of  the  work  areas
 shown  in  figure 2.  Work areas of appropriate size are always provided
 for input from the card reader and for data that is  to  be  punched  or
 printed.   Additional  areas  may  be  used for tape or disk files.  The
 length of each tape or disk area is equal to the length of  the  logical
 records  in  the corresponding file.  The date area contains the current
 date and time in several forms  as  shown  below.   Finally,  a  working
 storage  area  of 4096 characters called "scratchpad" is provided in all
 programs.

                Code       Area in Memory

                  L        Listing Area
                           132 characters

                  R        Card Reader Area
                           80 characters

                  P        Card Punch Area
                           80 characters

                  1-6      Numbered File Areas (up to 6)
                           Length equal to record length

                  S        Scratchpad Area
                           4096 characters

                  D        Date Area
                           42 characters

                  V        Variable-length records
                           length area.

               Figure 2. Work Areas in a BESTOP Program
-     References  to  data  contained  in the work areas include the area
 code, that is shown to the left of  each  area  in  figure  2,  and  the
 beginning  and  ending  positions of the field within the area.  Thus, a
 reference to a data field in positions 25 through 30 of the card  reader
 area  would  be  "R.25.30".   The  area  codes  are  also  used in WRITE
 instructions to indicate that the entire contents of an area are  to  be
 written out onto the corresponding output file.

      To  illustrate,  a  program  to reproduce a deck of cards must move
 each card image from the reader area to the punch area and then have the
 contents of the latter area punched into a  card.   The  entire  program
 consists do the following two instructions:

 ________________________________________________________________________

                                   -4-
1
                                  BESTOP
 ________________________________________________________________________


                            M R.1.80 P.1.80
                            W P

      The  input cards are automatically placed in the reader area by the
 record reading routine.  The output area is cleared to blanks after  the
 record has been written.

      Constants  are  enclosed in apostrophes and may be used in a manner
 similar to data field references in many instructions.  For example,  if
 a  "25"  is  to  be  punched  in  columns  79-80 of a deck of cards, the
 instruction to move that number into the punch area would be:

                            M '25' P.79.80

      The use of data contained in tables is covered in section 2.

      Variable  length  records  are  read  and  written  on the basis of
 information contained in file header labels, JCL and  the  program  work
 area   "V".    For  variable  length  record  files,  the  size  of  the
 corresponding file area (1-6) in the program is  equal  to  the  maximum
 size  of  the  records in the file less the four characters required for
 the record descriptor work (RDW) of the variable  length  record.   That
 is,  a maximum logical record length of 156 for a variable length record
 file would require an area of 152 characters in the  program  as  BESTOP
 does  not  store  the  RDW  information  in  the  work area of the file.
 Instead, the actual length of the records in each of the file  areas  is
 stored in the appropriate positions of area "V" as follows:


                Locations       Actual Length of Record for

                V.1.4                     File 1
                V.5.8                     File 2
                V.9.12                    File 3
                V.13.16                   File 4
                V.17.20                   File 5
                V.21.24                   File 6


      For  input  files,  the  record form (RECFM), maximum record length
 (LRECL) and block size (BLKSIZE) are provided by the header label of the
 file and  either  fixed  length  (RECFM=FB  or  F)  or  variable  length
 (RECFM=VB  or  V)  records may be read by the program.  If the record is
 variable length, the actual length of  the  record,  less  the  RDW,  is
 stored  by  the  program  as  a decimal integer in the appropriate field
 within area V.  Positions in the input area that are not filled  by  the
 input record are set to blanks.

      For  output  files,  the record form (FB,F,VB or V), maximum record
 length, and block size must be provided in a data  control  block  (DCB)
0
 ________________________________________________________________________

                                   -5-
1
                                  BESTOP
 ________________________________________________________________________


 entry  for the file in the JCL.  For variable length records (VB,V), the
 LRECL of the DCB entry must include 4 positions for the RDW.  The actual
 length of a variable length record, excluding the RDW, must be stored by
 the programmer in decimal integer form in the appropriate  field  within
 area V before the record is written.  The contents of that field are not
 affected  by  the  record  writing  operation.   A record of the maximum
 length is written if the record length field in area V contains a  zero,
 blanks, or non-numeric characters.


             Locations           Date or Time

              1-18               Long form date, right justified
                                 (e.g., November 25, 1971)

             19-26               Short form date, right justified
                                 (e.g., 11/25/71)

             27-32               Standard form, YYMMDD
                                 (e.g., 71329)

             33-37               Julian form, YYDDD
                                 (e.g.), 71329)

             38-42               Starting time of run, HH:MM



-
-
-
-
-
-
-
-
 ________________________________________________________________________

                                   -6-
1
                                  BESTOP
 ________________________________________________________________________


                     III.__INSTRUCTION_SPECIFICATIONS
+                    ____  ___________ ______________
0
      A.__Instructions
+     __  ____________

      BESTOP instructions fall into categories as follows:

             1.   Conditional Instructions

                    I - IF
                    O - OTHERWISE
                    U - UNCONDITIONAL

             2.   Processing Instructions

                    M - MOVE
                    E - EDIT
                    C - CLEAR
                    + - ADD
                    - - SUBTRACT
                    X - MULTIPLY
                    / - DIVIDE
                    W - WRITE
                    G - GET
                    H - HALT
                    B - BRANCH
                    L - LOOKUP
                    F - FIND
                    M - MOVE (TO DISPLACED FIELD)
                    M - MOVE (FROM DISPLACED FIELD)
                    D - DO AGAIN

             3.   Subroutine Definition Instructions

                    S - SUBROUTINE
                    R - RETURN

             4.   Table Definition Instructions

                    T - TABLE
                    constant - ENTRY

             5.   Matched File Instruction

                    K - KEYS


-
0
 ________________________________________________________________________

                                   -7-
1
                                  BESTOP
 ________________________________________________________________________


      BESTOP instructions generally consist of an operation code followed
 by  parameters  which  may  include field specifications, constants, and
 modifiers.  The single exception to this rule is the table  entry  which
 is coded as a single constant without an operation code.

      Field  specifications are of the form "f.s.e" where "f" is the file
 code, "s" is the starting location, and "e" is the ending location.  For
 example, the specification R.23.28 refers to positions 23 through 28  of
 the  reader  area.  The ending location, with its separating period, may
 be omitted for single character  fields  as  in  L.67,  a  reference  to
 position 67 of the listing area.

      Constants  are  enclosed  in  apostrophes.   If  it is necessary to
 include an apostrophe within a constant,  it  should  be  coded  as  two
 contiguous  apostrophes.   The  compiler will omit the second apostrophe
 from the resulting constant.

      Modifiers are single character parameters that are used  to  invoke
 specific forms of some instructions.

      Only  one  instruction  may  be  coded  on  a  single card or line.
 Instructions may be numbered by coding a decimal  number  prior  to  the
 operation  code.   Comments  may  follow  an  instruction or instruction
 number by coding an asterisk (*) to indicate that the remaining  portion
 of  the  line  or card is a comment.  The instruction numbers, operation
 code, parameters, and instruction comment must all be  separated  by  at
 least one blank.  Instructions, including numbers, comments and spacing,
 may not exceed 80 characters.

      Several  notation conventions have been followed in the instruction
 specifications.  Operation codes and modifiers are  denoted  with  their
 actual  upper  case  letters, numbers, or special characters.  The lower
 case words 'field' and 'const' denote  a  field  or  constant  parameter
 respectively.   A blank parameter (which may be omitted) is denoted with
 the special symbol "( )".  Stacked brackets indicate  that  one  of  the
 parameters in the stack should be selected.

      B.__Conditional_Instructions
+     __  ___________ ____________

      The conditional instructions (IF, OTHERWISE, and UNCONDITIONAL) are
 used  to start routines and to establish the conditions that must be met
 before a routine will be executed.  A routine may start with one or more
 "IF"  instructions  which  establish  a  set  of  conditions,  with   an
 "OTHERWISE"  instruction  which  identifies  a  routine  that  is  to be
 executed if the previous IF instruction routine  was  not  executed,  or
 with  the  UNCONDITIONAL  instruction which is needed to start a routine
 that will be executed  unconditionally  following  an  IF  or  OTHERWISE
 routine.  IF, OTHERWISE and UNCONDITIONAL instructions may never be used
 together within a single routine.  The OTHERWISE instruction may only be
 used  to  start  a  routine that immediately follows an IF routine.  The
0
 ________________________________________________________________________

                                   -8-
1
                                  BESTOP
 ________________________________________________________________________


 UNCONDITIONAL instruction is only used immediately after IF or OTHERWISE
 routines and is not used at the start of a  program  or  subroutine,  or
 immediately following a subroutine or table.

      The  various  forms  of  the  IF  instruction  end with the linking
 modifiers A,O, or blank for "and", "or" and "no link"  respectively.   A
 linking  modifier  specifies  the  relationship  between  the current IF
 instruction and the IF instruction that follows.  It must be left  blank
 if the next instruction is not an IF instruction.

      When both "and" and "or" links are used as modifiers in a set of IF
 instructions,  the  "and"  links  take  precedence  over the "or" links.
 Thus, in a set of condition instructions with tests X, Y, and Z that are
 linked as follows:

                                  X and Y or Z,

      the  correct  interpretation  is as though parenthesis were used to
 group the tests as:

                                 (X and Y) or Z

      and not as:

                                  X and (Y or Z)


 1.__IF_(Character_Field_Comparison)
+__  __ __________ _____ ___________

 ------------------------------------------------------------------------
                             (E)            (A)
                   I  field  (G)   (field)  (O)
                             (L)   (const)  ( )
                             (U)
 ------------------------------------------------------------------------



      The  contents  of  the first field are compared with the second for
 the relationship specified by the first modifier as follows:

                  E - first equals second
                  G - first is greater than second
                  L - first is less than second
                  U - first is unequal to second

      The  two  fields  must be the same size.  The comparison is made on
 character for character basis from  left  to  right  until  two  unequal
 characters are compared on the fields are exhausted.

0
 ________________________________________________________________________

                                   -9-
1
                                  BESTOP
 ________________________________________________________________________


 2.__IF_(Numeric_Field_Comparison)
+__  __ ________ _____ ___________

 ------------------------------------------------------------------------
                             (E)            (A)
                  I N field  (G)  (field)   (O)
                             (L)  (const)   ( )
                             (U)
 ------------------------------------------------------------------------


      The  numeric  values of the contents of the two fields are compared
 for the relationship specified by the second modifier as follows:

                  E - first equals second
                  G - first is greater than second
                  L - first is less than second
                  U - first is unequal to second


      The  fields need not be the same size since it is the numeric value
 and not the character values of the two fields that  are  compared.   In
 the  numeric  comparison, values are ranked from plus infinity (high) to
 minus infinity (low).  Blanks are equivalent to  zeros.   The  digits  0
 through  9,  blanks  and  minus  signs  are the only characters that may
 appear in a field or constant used in a numeric comparison.

        Example

        Test  the contents of file 1 positions 12-19 for a
        value greater than zero.

                       I N 1.12.19 G '0'


 3.__IF_(Multiple_Comparison)
+__  __ _________ ___________

 ------------------------------------------------------------------------
                             (E)            (A)
                  I M field  (U)   const    (O)
                                            ( )
 ------------------------------------------------------------------------


      The  field  is  compared  against a list of values specified in the
 constant on a character by character basis.  Each value in the  constant
 must  have  the  same length as the field.  Individual comparison values
 within the constant must be  separated  by  commas  or  dashes  and  not
 blanks.   However,  blanks  may  be  included  in the comparison values.
 Commas in the constant separate discrete values while a dash indicates a
 range of values whose limits are specified by the two values  joined  by
 the dash.

 ________________________________________________________________________

                                   -10-
1
                                  BESTOP
 ________________________________________________________________________


      When  the  second  modifier is an "E", the test is satisfied if the
 contents of the field are identical to any of the values in the list  or
 if  they  fall  within  a  range specified in the list.  When the second
 modifier is a "U", the test is satisfied only if  the  contents  of  the
 field are not identical to any of the values in the list and do not fall
 within a range specified in the list.

        Examples

        Test  the  code  in  reader  positions 8-9 for the
        values 05, 09, or 16 or a value in the range  from
        25 to 29.

                     I M R.8.9  E '05,09,16,25-29'

        Test  the  code  in file 1 position 15 for a value
        that is not equal to a blank, 2,  or  9  and  that
        does not fall in the range from 4 to 7.

                     I M 1.15  U  ' ,2,4-7,9'


 4.__IF_(character_comparison)
+__  __ __________ ___________


 ------------------------------------------------------------------------
                       I C field (E) const
                                 (U)
 ------------------------------------------------------------------------

      Each individual character in the field is tested against the set of
 characters  contained  in  the constant for the equal (E) or unequal (U)
 relationship specified in the instruction.  The equal test is met if all
 of the characters in the field are found in the constant.   The  unequal
 test  is  met if any of the characters in the field are missing from the
 constant.

        Example

        Set  the contents of 1.6.9 to blank if it contains
        non-numeric characters.

                      I C 1.6.9 U '0123456789'
                      C 1.6.9 ' '

-
-

 ________________________________________________________________________

                                   -11-
1
                                  BESTOP
 ________________________________________________________________________


 5.__IF_(Control_Break)
+__  __ ________ ______

 ------------------------------------------------------------------------
                                 (A)
                       I field   (0)
                                 ( )
 ------------------------------------------------------------------------


      The  contents  of  the  field are compared with the contents of the
 same field at the time of the last testing of  the  conditions  for  the
 current  routine.   The  test is satisfied if there has been a change in
 the contents.  It is never satisfied the first time that it is  executed
 as  there  is  no  basis  for  a  comparison.  A control break is always
 satisfied on the last pass to permit the processing of group totals  and
 similar end of group results.


 6.__IF_(Printer_Line_Test)
+__  __ ________ ____ _____

 ------------------------------------------------------------------------
                            (E)          (A)
                      I C   (G)  const   (0)
                            (L)          ( )
                            (U)
 ------------------------------------------------------------------------


      The contents of the printer line counter are compared against a two
 digit  zero filled constant for the relationship specified by the second
 modifier as follows:

             E - counter equals constant
             G - counter is greater than constant
             L - counter is less than constant
             U - counter is unequal to constant


 7.__IF_(Condition_Test)
+__  __ __________ _____

 ------------------------------------------------------------------------
                         (M)  (A)
                      I  (A)  (0)
                         (B)  ( )
                         (S)
                         (F)
 ------------------------------------------------------------------------


      This  instruction  tests  for  condition  specified  by  the  first
 modifier as follows:

 ________________________________________________________________________

                                   -12-
1
                                  BESTOP
 ________________________________________________________________________


        M  - Matching records were read from the two input
        files under matched file control.

        A - There is an unmatched record  in  the  A  file
        that was read under matched file control.

        B  -  There  is  an unmatched record in the B file
        that was read under matched file control.

        S - Start of run, the  first  record(s)  is  being
        processed.

        F  -  Finish  of run,  the last record(s) has been
        processed and the program is in the last pass.


 8.__OTHERWISE
+__  _________

 ------------------------------------------------------------------------
                                O
 ------------------------------------------------------------------------


      The  OTHERWISE  instructions is used to start a routine that should
 be executed if the conditions set forth  for  the  immediately  previous
 routine  were  not met.  It may only be used after a routine that begins
 with an IF instruction.


 9.__UNCONDITIONAL
+__  _____________

 ------------------------------------------------------------------------
                                U
 ------------------------------------------------------------------------


      The UNCONDITIONAL instruction is used to end the routine associated
 with  the  previous  set  of  condition  instructions and to start a new
 routine that will be executed unconditionally.
-
-
-
-

 ________________________________________________________________________

                                   -13-
1
                                  BESTOP
 ________________________________________________________________________


      C.__Data_Movement_Instructions
+     __  ____ ________ ____________

      The basic data movement instructions are the MOVE, EDIT, and CLEAR.
 The  MOVE  instruction moves data from one field to another in memory or
 moves a constant into a field.  The EDIT instruction moves data from one
 field to another and  inserts  any  necessary  punctuation.   The  CLEAR
 instruction  fills a field with any desired character and can be use for
 such operations as clearing counters or drawing lines of dashes across a
 page.

 1.__MOVE
+__  ____

 ------------------------------------------------------------------------
                        M    (field)  field
                             (const)
 ------------------------------------------------------------------------


      The  contents  of the first field (or constant) are copied into the
 positions specified by the second  field.   The  sending  and  receiving
 fields must have the same length.

 2.__EDIT
+__  ____

 ------------------------------------------------------------------------
                        E  field  field  const
 ------------------------------------------------------------------------


      The  contents  of  the  first  field  are  edited  with the symbols
 contained in the constant and placed in  the  second  field.   Zeros  or
 blanks  in the constant are replaced by characters from the first field.
 All other characters in the constant will appear in  the  same  relative
 positions  within  the  second  field.  A zero in the constant indicates
 that leading zeros should appear in any blank positions to the right  of
 and  including the zero position and that leading commas in the constant
 to the left of the zero should be suppressed.  Blanks are  used  in  the
 remaining  positions  of  the  constant corresponding to positions to be
 occupied by data from the first field.  The length of the constant  must
 be  equal  to  the  length of the second field and should contain enough
 replaceable blanks and zeros to accommodate the characters of the  first
 field.

      This operation may only be performed on numeric data.

        Examples

        Read  area positions 31-39 contain a dollar amount
        expressed to the nearest hundredth  of  a  dollar.
        Edit  the field to insert commas and decimal point
0
 ________________________________________________________________________

                                   -14-
1
                                  BESTOP
 ________________________________________________________________________


        where appropriate and place the edited  result  in
        listing positions 42-53.

                   E R.31.39  L.42.53   ',   ,  .0 '

        Zero  fill  the  contents of file 1 positions 8-12
        and place the result in file 2 positions 1-5

                   E 1.8.12  2.1.5  '0    '


 3.__CLEAR
+__  _____

 ------------------------------------------------------------------------
                       C  field const
 ------------------------------------------------------------------------


      All  of  the  positions  in the specified field are filled with the
 single character specified by the constant.

        Example

        Draw  a line of dashes across the next line of the
        listing.

                        C L.1.132 '-'

      D.__Arithmetic_Instrictions
+     __  __________ ____________

      The  arithmetic  instructions  are the ADD, SUBTRACT, MULTIPLY, and
 DIVIDE.

      Arithmetic operations may be  performed  on  positive  or  negative
 data.   Minus  signs,  if  any, must be carried to the left of the first
 significant digit in a field.  Positive or  zero  data  should  be  left
 unsigned;  the  positive  or zero results of any computations are always
 unsigned.  All arithmetic operations are algebraic, i.e., the  signs  of
 any data items used in a computation are taken into account.

 1.__ADD
+__  ___

 ------------------------------------------------------------------------
                       +    (field)  field
                            (const)
 ------------------------------------------------------------------------

      The contents of the first field or constant are added to the second
 field.  The result replaces the second field.

0
 ________________________________________________________________________

                                   -15-
1
                                  BESTOP
 ________________________________________________________________________


      The  width  of  the first field or constant must not be larger than
 the width of the second field.

 2.__SUBTRACT
+__  ________

 ------------------------------------------------------------------------
                       -    (field)  field
                            (const)
 ------------------------------------------------------------------------

      The contents of the first field or constant are subtracted from the
 second field.  The result replaces the second field.

      The  width  of  the first field or constant must not be larger than
 that of the second field.


 3.__MULTIPLY
+__  ________

 ------------------------------------------------------------------------
                       X  field  (field)  (0-9)  field
                                 (const)
 ------------------------------------------------------------------------

      The  first field is multiplied by the second or by the constant and
 the rounded result is placed in  the  third  field.   The  single  digit
 modifier  indicates  the  number of digits that will be rounded from the
 result.

        Example

        Multiply the contents of read area positions 11-17
        by  read  area  positions 18-23.  Round the result
        three places and place  it  in  file  1  positions
        21-30.

                   X R.11.17  R.18.23  3  1.21.30


 4.__DIVIDE
+__  ______

 ------------------------------------------------------------------------
                       /  field  (field)   (0-9) field
                                 (const)
 ------------------------------------------------------------------------


      The first field is divided by the second or by the constant and the
 result  is  placed in the third field.  Prior to the division operation,
 the first field is extended by the number  of  zeros  specified  in  the
 modifier to obtain greater precision.

 ________________________________________________________________________

                                   -16-
1
                                  BESTOP
 ________________________________________________________________________


      The  value  of  the  precision  modifier can be calculated from the
 following formula for fields with implied decimal locations:

        Modifier = B - A + C    where:

        B  =  the implicit number of decimal places in the
        divisor,
        A  =  the implicit number of decimal places in the
        dividend, and,
        C = the implicit number of decimal places required
        in the result.


        Example

        The  total income in dollars for a group of people
        is contained in file 1  positions  35-44  and  the
        number of people in the group is contained in file
        1 positions 51-56.  Compute the per capita income
        to the nearest hundredth of a dollar and place the
        result in file 2 positions 11-16.

                 / 1.35.33   1.51.56   2  2.11.16



      E.__Output_And_Control_Instructions
+     __  ______ ___ _______ ____________

      The  output  and control instructions are the WRITE, GET, and HALT.
 The WRITE instruction is used to write records from the  various  output
 areas  of  the program.  It is also used to control the vertical spacing
 of the  printer.   There  is  no  record  reading  instruction  as  that
 operation  is performed by the record reading routine.  However, the GET
 instruction will cause an immediate return to the record reading routine
 to get and process the  next  record  without  executing  any  remaining
 instructions in the program on the current record.  The HALT instruction
 may be used to stop the program before the end of the input file(s).

 1.__WRITE_(Numbered_Files_and_Punch_File)
+__  _____ _________ _____ ___ _____ _____

 ------------------------------------------------------------------------
                             W    (1-6)
                                  (P)
 ------------------------------------------------------------------------

      A  record is written from the specified output area and the area is
 cleared to blanks.
-
0
 ________________________________________________________________________

                                   -17-
1
                                  BESTOP
 ________________________________________________________________________


 2.__WRITE_(Listing_with_Spaces)
+__  _____ ________ ____ _______

 ------------------------------------------------------------------------
                             W L  (1-9)
                                  (H)
 ------------------------------------------------------------------------

      A  line  is  printed  with the contents of the listing area and the
 area is cleared to blanks.  The printer is spaced from 1 to 9  lines  or
 to the head of form (H).

 3.__WRITE_(Listing_with_Skip_to_Numbered_Line)
+__  _____ ________ ____ ____ __ ________ _____

 ------------------------------------------------------------------------
                             W L S const
 ------------------------------------------------------------------------


      A  line  is  printed  with the contents of the listing area and the
 area is cleared to blanks.  The printer skips to the line  specified  in
 the two digit zero-filled constant after printing the line.

        Example

        Write a line and skip to line 52.

                      W L S '52'


 4.__Write_(Space_Printer_without_Printing)
+__  _____ ______ _______ _______ _________

 ------------------------------------------------------------------------
                            W S  (1-9)
                                  (H)
 ------------------------------------------------------------------------


      The  printer is spaced from 1 to 9 lines or to the head of form (H)
 without printing a line.   The  contents  of  the  listing  area  remain
 unchanged.


 5.__WRITE_(Skip_to_Numbered_Line_without_Printing)
+__  _____ _____ __ ________ ____ _______ _________

 ------------------------------------------------------------------------
                             W S const
 ------------------------------------------------------------------------


-
 ________________________________________________________________________

                                   -18-
1
                                  BESTOP
 ________________________________________________________________________


      The  printer  is  skipped  to  the  line specified in the two digit
 zero-filled constant without printing  a  line.   The  contents  of  the
 listing area remain unchanged.

 6.__GET
+__  ___

 ------------------------------------------------------------------------
                                  G
 ------------------------------------------------------------------------

      The  processing  of  the  current  record(s)  is terminated and the
 program makes an immediate return to the record reading routine  to  get
 the  next  record(s).   Processing resumes with the first instruction in
 the program.

 7.__HALT
+__  ____

 ------------------------------------------------------------------------
                              H  (R)
                                 (J)
 ------------------------------------------------------------------------

      The  current run or step (R) or the entire job (J) is terminated as
 specified by the modifier.  In terminating the run, the program executes
 the last pass and closes all input and output files before returning  to
 the operating system.


      F.__Soubroutine_Linkage_Instruction
+     __  ___________ _______ ___________

      Subroutines  may  be  included  in  BESTOP  programs  by  using the
 SUBROUTINE instruction to identify the subroutine and following it  with
 the  routine(s)  that  are  to  be  included  in  the  subroutine.   The
 subroutine is terminated by  a  RETURN  instruction.   A  subroutine  is
 executed  with  a  BRANCH  instruction.   After  the subroutine has been
 executed, control returns to the instruction following the BRANCH.

      Subroutines may not be defined within  other  subroutines  although
 they  may  contain branches to other subroutines.  Care must be taken to
 avoid constructing a string of branches which includes a branch back  to
 a  subroutine  earlier  in the string.  Such a sequence will destroy the
 return linkage back to the calling routine.

      A subroutine may only be entered with a branch instruction.  It  is
 skipped  when  encountered  in the normal execution of the routines in a
 program.  Any number of branches may be made to the same subroutine.
-
-
 ________________________________________________________________________

                                   -19-
1
                                  BESTOP
 ________________________________________________________________________


 1.__SUBROUTINE
+__  __________

 ------------------------------------------------------------------------
                             S    (1-9)
                                  (A-Z)
 ------------------------------------------------------------------------

      A  subroutine is started which is identified by the single digit or
 letter specified  in  the  modifier.   All  instructions  following  the
 SUBROUTINE  instruction  up to the final RETURN instruction are included
 in the subroutine.

 2.__RETURN
+__  ______

 ------------------------------------------------------------------------
                             R    (C)
                                  ( )
 ------------------------------------------------------------------------

      A  return  is  made  to the instruction following the branch to the
 subroutine.  If the modifier is omitted, the subroutine  is  terminated.
 The  modifier  "C"  indicates that the instructions following the RETURN
 are to be included in the  subroutine  until  a  terminating  RETURN  is
 encountered, that is a subroutine may have multiple returns.

 3.__BRANCH
+__  ______

 ------------------------------------------------------------------------
                             B    (1-9)
                                  (A-Z)
 ------------------------------------------------------------------------

      A  branch  is  made  to  the subroutine identified by the modifier.
 Control returns to  the  instruction  following  the  branch  after  the
 subroutine has been executed.


      G.__Table_Lookup_Instructions
+     __  _____ ______ ____________

      A  table  lookup may be used to obtain a title, code, or other item
 that corresponds to a value shown in a table.  It is  useful  in  coding
 and recoding data and in translating codes into titles.  A table is made
 up  of a number of constant width entries.  Each entry has two parts, an
 argument, the test value, and the result, the code or title to which the
 argument corresponds.  A table  is  defined  with  a  TABLE  instruction
 followed  by  the  entires  of  the table.  It is searched with a LOOKUP
 instruction.

      In the lookup operation, a program argument in a specified field is
 tested against the arguments of the table and a result corresponding  to
0
 ________________________________________________________________________

                                   -20-
1
                                  BESTOP
 ________________________________________________________________________


 the  table  argument that meets the specified lookup test is stored in a
 result field.  The program argument and result fields are  specified  in
 the  TABLE  instruction.   The  lookup  test  is specified in the LOOKUP
 instruction.  The result field is cleared to blanks if there is no table
 argument that meets the lookup test.

 1.__TABLE_DEFINITION
+__  _____ __________

 ------------------------------------------------------------------------
                        T    (1-9)  field  field
                             (A-Z)
 ------------------------------------------------------------------------

      A  table  is  created  and identified by the single digit or letter
 specified in the modifier.  The first field specifies  the  location  of
 the  lookup  argument;  the second specifies the location into which the
 result will be placed.

      The entries of the table follow the TABLE instruction.  The  length
 of  each  entry  must be equal to the sum of the lengths of the argument
 and result fields.

 2.__TABLE_ENTRY
+__  _____ _____

 ------------------------------------------------------------------------
                                const
 ------------------------------------------------------------------------

      A  table  entry  is  generated  from  the  specified constant.  The
 leftmost portion of the constant is assumed to be the table argument and
 the rightmost is assumed to be the table result.   The  lengths  of  the
 table  argument  and  result  portions of the constant are assumed to be
 equal to the lengths of the argument and result fields specified in  the
 TABLE instruction


 3.__LOOKUP
+__  ______

 ------------------------------------------------------------------------
                         L  (1-9)   (E)
                            (A-Z)   (L)
                                    (H)
 ------------------------------------------------------------------------

      A  search  is made of the table specified in the first modifier for
 the entry which meets the test  specified  by  the  second  modifier  as
 follows:

        E    -  Lookup  equal,  the  program will select a
        table entry only if the argument in the entry   is
0
 ________________________________________________________________________

                                   -21-
1
                                  BESTOP
 ________________________________________________________________________


        equal  to  the contents of  the  program  argument
        specified in the TABLE instruction.  If the  table
        argument   is  equal to the program argument , the
        table result  is  stored   in  the  result   field
        specified   in  the TABLE instruction.  The result
        area is cleared to blanks if there  is  no   equal
        entry.

        L - Lookup low or equal, the program searches  for
        the  entry  whose argument is the highest of those
        with arguments lower than or equal to the  program
        argument  and the corresponding result is moved to
        the result field.  The result field is cleared  to
        blanks  if  there  are  no  entries  in  which the
        argument is lower than or  equal  to  the  program
        argument.


        H - Lookup high or equal, the program searches for
        the  entry  whose  argument is the lowest of those
        entries with arguments higher than or equal to the
        program argument and the corresponding  result  is
        moved  to  the  result field.  The result field is
        cleared to blanks if there are no entries in which
        the argument  is  higher  than  or  equal  to  the
        program argument.


      H.__Matched_File_Control
+     __  _______ ____ _______

      A  program will read two input files when the necessary information
 is  provided  to  further  specialize  the   record   reading   routine.
 Otherwise,  a  program is limited to one input file.  Both files must be
 sorted on an identical set of sequence  keys  although  these  keys  may
 occupy  different  positions  in  the  records  of  the  two files.  For
 identification purposes, one file is designated the A file and the other
 is designated the B file.

      The record reading  routine  compares  the  sequence  keys  in  the
 current  records  from  each  file  and  sets one of the following three
 indicators:

        M  -  The  records  in  the two files are matching
        records.

        A  -  There is a record in the A file which is not
        matched in the B file, i.e., the value of the keys
        in the current A file record is less than that for
        the current B file record.

0
 ________________________________________________________________________

                                   -22-
1
                                  BESTOP
 ________________________________________________________________________


        B  -  There is a record in the B file which is not
        matched in the A file, i.e., the value of the keys
        in the current B file record is less than that for
        the current A file record.

      These  indicators may be tested with the condition test form of the
 "IF" instruction.

      Subsequent record reading operations are controlled by the previous
 setting of the above indicators and the "run type." The run  type  codes
 are the following:

        1  - There should be one record in file A for each
        record in file B.  If  either  file  contains  two
        records with the same values in the sequence keys,
        the  program  will  treat  the second record as an
        unmatched record.

        2  -  There  may be more than one record in file B
        for each file A record.  However, there should  be
        no  more  than  one  file A record for each file B
        record.  Thus, duplicate file B  records  will  be
        treated  as  matches  for  a  single file A record
        while duplicate file A records will be treated  as
        unmatched records.

      A  record  from  the  A  file  is always read by the record reading
 routine if the A indicator was set after the last reading operation.   A
 record  from  the  B file is always read if the B indicator was set.  If
 the M indicator was set and the run type is "1", both an A and a B  file
 record  are read before they are compared and an indicator is set on the
 basis of that comparison.  If the M indicator was set and the  run  type
 is  "2", a B file record is read first and compared with existing A file
 record.  The M indicator is then set if they  match.   If  they  do  not
 match, an A file record is read and the comparison is repeated before an
 indicator is set.

      At  the  end  of  the  record  reading operation the current A file
 record will appear in the memory area corresponding to the A  file  code
 and   the  current  B  file  record  will  appear  in  the  memory  area
 corresponding to the B file code.  If either file  has  been  exhausted,
 the  corresponding  area  will  be  filled with padding (the hexadecimal
 character FF).

      Up to five sequence keys may be used in the record comparison.  The
 locations of these keys in major to minor order for the records in  each
 of  the  two files is specified in a KEYS instruction.  The run type and
 the  A  file  and  B  file  specifications  are  job  control   language
 parameters.



 ________________________________________________________________________

                                   -23-
1
                                  BESTOP
 ________________________________________________________________________


 1.__MATCH_KEYS
+__  _____ ____

 ------------------------------------------------------------------------
          K  field field  (field field). . .(field field)
 ------------------------------------------------------------------------

      The KEYS instruction specifies up to five pairs of sequence keys in
 the  records  of  the  A and B files that establish the order of the two
 files.  The first field  in  each  pair  specifies  the  location  of  a
 sequence  key in the A file records while the second field specifies the
 location in the B file records.  The  order  of  the  pairs  within  the
 instruction  must  be  a  major  to minor.  The widths of the two fields
 within a pair must be equal although different pairs may have  different
 widths  and  the  actual locations of the keys within the records of the
 two files need not be the same.


      I.__Advanced_Techniques
+     __  ________ __________

      Several  instructions  are available that emulate array processing.
 The  first  three  instructions  use  a  displacement  field  in   their
 operations.    It   provides   a   capability  similar  to  indexing  or
 subscripting in other languages.  The displacement is a  1  to  4  digit
 number  that  specifies  a character location within a field in terms of
 the number of characters between the specified character and  the  first
 character  of  the  field.   For  example,  the displacement of the 25th
 character of a field is 24 as it is  displaced  24  character  positions
 from  the 1st character.  The displacement itself is stored in a field 1
 to 4 characters long and is always preceded by the  modifier  "D".   For
 example, a displacement stored in scratchpad positions 22 to 25 would be
 expressed in the form:
                           D   S.22.25
      The  "DO  AGAIN" instriction provides the capability similar to the
 DO WHILE of PL/1.



 1.__FIND
+__  ____

 ------------------------------------------------------------------------
                    F   (field)   field  D  field
                        (const)
 ------------------------------------------------------------------------

      The  second  field  is  searched  for  a  character  string that is
 identical to the contents of the first (or constant).  The  displacement
 of  the  first  character of the found string within the second field is
 placed in the third field.  The third field is cleared to blanks if  the
 string  is  not  found.   The  search beings at the character within the
 field that is specified by the initial value of the displacement.
0
 ________________________________________________________________________

                                   -24-
1
                                  BESTOP
 ________________________________________________________________________


        Example

        Find  the  displacement  of  the  character string
        "#7609" within the field 1.20.80  and  record  the
        displacement in  S.1.4.

                  F  '#7609'  1.20.80  D  S.1.4


        Notes

        1.  The search beings at the first position of the
        second   field   if   the  initial  value  of  the
        displacement is blank or zero.

        2.  The search ends when the number of  characters
        remaining  in  the  second  field is less than the
        number of characters in the first field.

        3.  The resulting displacement  is  always  stored
        without   leading   zeros   except   that  a  zero
        displacement  is  stored  as  a  single  zero.   A
        resulting  displacement  that  is  blank indicates
        that he string was not found.

        4.   The  leftmost   digits   of   the   resulting
        displacement  are  truncated  if  there  are  more
        characters in the displacement value than  in  the
        displacement field.

        5.   The displacement field may not be more than 4
        characters wide.



 2.__MOVE_(to_displaced_field)
+__  ____ ___ _________ ______

 ------------------------------------------------------------------------
                    M  (field)  field  D  field
                       (const)
 ------------------------------------------------------------------------


      The  contents  of  the  first  field  or  constant are moved to the
 locations in the second field that are specified by the displacement  in
 the  third  field.   The entire contents of the first field are moved if
 the number of positions between the displaced  location  in  the  second
 field  and  the  end of the second field is greater than or equal to the
 length of the first field.  Unfilled positions in he second field retain
 their original values.  The right most positions of the  field  are  not
0
 ________________________________________________________________________

                                   -25-
1
                                  BESTOP
 ________________________________________________________________________


 moved  if  their is insufficient space in the displaced locations in the
 second field.  The operation  is  not  executed  if  the  value  of  the
 displacement is greater than or equal to the width of the second field.

        Example

        Given  the  specified  contents  of  the following
        fields:

                  2.40.45      "A3    "

                  S.1.2        " 2"

        The instruction

                  M  ';'  1.40.45  D  S.1.2

        changes the contents of 2.40.45 to

                  "A3;   "



        Notes

        1.   The displacement field may not be more than 4
        characters wide.

        2.  The MOVE operation  is  not  executed  if  the
        displacement     field     contains    non-numeric
        characters.



 3.__MOVE_(from_displaced_field)
+__  ____ _____ _________ ______

 ------------------------------------------------------------------------
                     M  field  D field  field
 ------------------------------------------------------------------------

      The  third  field  is  filled  with characters from the first field
 starting with the character in the first field that is specified by  the
 displacement  in the second field.  The third field is filled completely
 unless there is an insufficient number of characters  in  the  displaced
 portion  of  the  first  field.   Unfilled  positions in the third field
 retain their original values.

        Example

        Given  the  specified  contents  of  the following
        fields:

 ________________________________________________________________________

                                   -26-
1
                                  BESTOP
 ________________________________________________________________________


                  1.8.14        "ABCDEFG"

                  S.6.8         "  2"

                  2.4.7         "HIJK"


        The instruction

                  M  1.8.14  D  S.6.8  2.4.7

        changes the contents of 2.4.7 to:

                  "CDEF"

        Notes

        1.   The displacement field may not be more than 4
        characters wide.

        2.  The MOVE operation is not  executed  if  there
        are  non-numeric  characters  in  the displacement
        field.



 4.__DO_AGAIN
+__  __ _____

 ------------------------------------------------------------------------
                               D
 ------------------------------------------------------------------------


      This instruction causes the IF instructions at the beginning of the
 routine  containing  the  DO  AGAIN  instruction  to  be  retested.  The
 instruction should always be the last instruction in a routine as is  it
 will  prevent  any  remaining  instructions  in  the  routine from being
 executed.  The IF condition at the start of the routine must be designed
 to terminate the looping effect of the DO AGAIN  instruction  after  the
 desired  number of iterations.  To avoid indefinite looping, the program
 will terminate abnormally (condition code 16) if any combination  of  DO
 AGAIN instructions is executed 1000 times without reading a record.

        Example

        Branch to subroutine A seven times.


                  C S.8 '0'
                  I S.8 L '7'
0
 ________________________________________________________________________

                                   -27-
1
                                  BESTOP
 ________________________________________________________________________


                  B A
                  +'1'S.8
                  D


        Notes

        The DO AGAIN may also be used in a routine started
        by  an UNCONDITIONAL instruction when that routine
        calls  a   subroutine   which   executes   a   GET
        instruction  as a means of terminating the looping
        effect.



-
-
-
-
-
-
-
-
-
-
-
-

 ________________________________________________________________________

                                   -28-
1
                                  BESTOP
 ________________________________________________________________________


                       IV.__PROGRAMMING_TECHNIQUES
+                      ___  ___________ __________
0

      A.__Routines
+     __  ________
      Within  a  routine, instructions are arranged in the order in which
 they are to be executed.  Most routines begin with a set of  conditional
 instructions  that  establish  conditions  which  must be met before the
 processing instructions  of  the  routine  will  be  executed.   If  the
 conditions  are  not  met,  the  routine  is skipped until the next pass
 through the object program.  When present, conditional instructions (IF,
 OTHERWISE,  UNCONDITIONAL)  must  always  come  before  the   processing
 instructions in a routine.

        Example: Routines


        File  1  contains  records  that are 25 characters
        long with the following code position 14:

                       1 - MALE
                       2 - FEMALE
                       3 - DATA ERROR

        Recode  female records with the code "4" and write
        the recoded file as File 2.    Print  any  records
        with  invalid   codes.   Only  records  with valid
        codes should be written on file 2.


      The  resulting  program  contains four routines and is shown below.
 The instructions have been  numbered  for  identification  and  sequence
 purposes.   Instruction  numbers  may  precede the operation code of any
 instruction.  They are not  checked  by  the  BESTOP  Compiler  and  are
 ignored during the compilation process.  For purposed of discussion, the
 routines  in  each  example  are  identified  by the number of the first
 instruction in the routine.


                       1  M 1.1.25 2.1.25
                       2  I 1.14 E '2'
                       4  M '4' 2.14
                       5  I 2.14 U '1' A
                       6  I 2.14 U '4'
                       7  M 2.1.25 L.1.25
                       8  W L 1
                       9  O
                      10  W 2




 ________________________________________________________________________

                                   -29-
1
                                  BESTOP
 ________________________________________________________________________


        Routine

        1  Unconditionally  moves a copy of each record to
        the File 2 areas.  The first routine in a  program
        is  always  executed  unconditionally when no "IF"
        instructions are included in the routine.

        2 Tests position 14 of each input record  for code
        "2"  and  assigns the new code "4" to records that
        meet that test.

        5 Prints those records that have a  code  that  is
        unequal   to   both   "1"   and "4." The lines are
        single spaced.

        9 Writes all  of  the  records  that  have   valid
        codes,  i.e., all those that were not processed by
        routine 5.

      Any of the following instructions will start a routine:

             1.    A   conditional   instructions  following  a
             processing instruction.

             2.   The  first  instruction  in  a   program   or
             subroutine.

             3.   The  first instruction following a subroutine
             or table.

      A routine ends with the last instruction prior to:

             1.  The next routine

             2.  A table or subroutine.

             3.  The end of the program.



      B.__Subroutines
+     __  ___________

      Subroutines  start  with  a  SUBROUTINE  instruction and end with a
 RETURN instruction.  All of the routines between these two  instructions
 are  included in the subroutine.  A subroutine may not be started within
 another subroutine,  i.e.,  a  SUBROUTINE  instruction  may  not  appear
 between  the  SUBROUTINE  instruction  of  another  subroutine  and  its
 terminating RETURN instruction.

-
 ________________________________________________________________________

                                   -30-
1
                                  BESTOP
 ________________________________________________________________________


      Subroutines may be placed anywhere in a program since they are  not
 executed  when  they are encountered; they are executed only by a BRANCH
 to the subroutine.  Control returns to  the  instruction  following  the
 BRANCH after the subroutine has been executed.


        Example: Subroutines

        File  2  contains  records  that are 60 characters
        long with the following code fields:

        Location Contents

           1-5 Individual identification number

           16 Race 1 - white 2 - negro 3 - other non-white

           34 Sex 1 - male 2 - female

        Screen the file for valid sex and race  codes  and
        print the following line for each invalid code:

        Location Contents

           1-5 Individual identification number

           7 Race

           9 Sex

           11-27  Error  message "INVALID RACE CODE" "INVALID
           SEX CODE"


      The  resulting  program  contains  three  routines, one of which is
 enclosed in a subroutine.


                       1    I 2.16 L '1' 0
                       2    I 2.16 G '3'
                       3    M 'INVALID RACE CODE' L.11.27
                       4    B 1
                       5    I 2.34 U '1' A
                       6    I 2.34 U '2'
                       7    M 'INVALID SEX CODE' L. 11.26
                       8    B 1
                       9    S 1
                      10    M 2.1.5 L.1.5
                      11    M 2.16 L.7
                      12    M 2.34 L.9
0
 ________________________________________________________________________

                                   -31-
1
                                  BESTOP
 ________________________________________________________________________


                      13    W L 1
                      14    R


        Routine

        1    Moves  the message "INVALID RACE CODE" to the
        listing area if  the  race  code  is  under  1  or
        greater  than  3.   Branches  to  Subroutine  1 to
        complete the printing of the error message.

        5 Moves the message  "INVALID  SEX  CODE"  to  the
        listing  area if the sex code is unequal to both 1
        and 2.  Branches to Subroutine 1 to  complete  the
        printing of the error message.

        9  The  start  of a subroutine which ends with the
        RETURN  instruction  number  14.   The  subroutine
        includes  only  one  routine but could contain any
        number that might be required.

        10 A routine which completes and prints a standard
        error message.   While  the  routine  is  executed
        unconditionally, it is only executed when a branch
        is made to subroutine 1.



      C.__Tables
+     __  ______

      A  table  consists  of  a TABLE instruction followed by one or more
 ENTRIES.  The TABLE INSTRUCTION identifies the table name and  specifies
 the  field  containing  the argument to be used in lookup operations and
 the field that is to contain the result of the lookup.   Each  entry  in
 the  table  is a single constant which includes an argument and a result
 in that order.  A table ends with the last entry prior to an instruction
 that is not an entry or with the end of  the  program,  whichever  comes
 first.   Tables  are  used only by lookup instructions and may be placed
 anywhere in a program.

        Example: Table Lookup

        File   1   contains   35   character   records  on
        individuals  with  the  age  of   the   individual
        recorded  with  leading  zeros in positions 12-13.
        The age of the individual must  be  coded  in  the
        manner  shown  below  and  the  age code should be
        added to the end of each record to produce  a  new
        record which should be written on File 2.

0
 ________________________________________________________________________

                                   -32-
1
                                  BESTOP
 ________________________________________________________________________


                       CODE      AGE

                        1        UNDER 14
                        2        14-19
                        3        20-24
                        4        25-34
                        5        35-44
                        6        45-54
                        7        55-64
                        8        65 AND OVER



      The program consists of a single routine and table.



                       1    M 1.1.35 2.1.35
                       2    L 1 H
                       3    W 2
                       4    T 1 1.12.13 2.36
                       5    '131'
                       6    '192'
                       7    '243'
                       8    '344'
                       9    '445'
                      10    '546'
                      11    '647'
                      12    '998'


        Routine


        1  Moves  the  input  record  to  the output area,
        performs a table lookup to get  the  required  age
        code and writes the coded record onto File 2.  The
        "lookup   high   or  equal"  form  of  the  lookup
        instruction has been used  to  stratify  the  data
        into  age  classes  corresponding to the resulting
        codes.

        4 A table whose entries extend through instruction
        number 12.  When a lookup operation  is  executed,
        the  program  argument  will  be  taken from field
        1.12.13 and the result will  be  placed  in  field
        2.36.

-

 ________________________________________________________________________

                                   -33-
1
                                  BESTOP
 ________________________________________________________________________


      D.__Matched_Input_Files
+     __  _______ _____ _____

      A program may read and match two input files as long as both are in
 the  same  sequence  on  a  similar  set  of  key  fields.   One file is
 arbitrarily designated as the "A" file, and the other is  then  the  "B"
 file.   A  special  form of the IF instruction permits program tests for
 matching records or for unmatched records in either file.   A  run  type
 code  must  also  be  specified  to indicate whether more than on B file
 records may match a single A file record.

      The sequence keys for the two  files  are  specified  in  the  KEYS
 instruction.   The  designation  of  the  A file, B file and run type is
 handled through the execute parameter in the job control language.

        Example: Matched File Operations

        Match  a  set  of correction cards against the 120
        character master file records in file 1 using  the
        state  and  industry codes in the two files as the
        basis for the match.  If there is a match, replace
        the income data in file 1  with  the  income  data
        from   the   transaction   cards.   If  there  are
        unmatched correction cards,  print  the  card  and
        construct  a new record containing only the state,
        industry,  and  income  fields.    The   remaining
        records  from  file  1  should  be copied onto the
        updated file.  Both files are in  order  by  state
        and industry.


                  File 1 format (required fields only)

                    Location        Contents

                       2-3          State code

                      26-29         Industry code

                      41-48         Income


                  Card format

                    Location        Contents

                       1-2          State code

                       3-6          Industry code

                       7-14         Income


 ________________________________________________________________________

                                   -34-
1
                                  BESTOP
 ________________________________________________________________________


      The  run  type  (1)  and  the  A  (File 1) and B (Reader) files are
 specified in the job control language.  The  first  instruction  in  the
 program specifies the location of the keys to be used in the match.  The
 remaining  instructions are grouped into four routines to handle each of
 the possible match or mismatch situations and to write the output file.

                       1  K 1.2.3 R.1.2 1.26.29 R.3.6
                       2  I M
                       3  M 1.1.120 2.1.120
                       4  M R.7.14 2.41.48
                       5  I B
                       6  M R.1.14 L.1.14
                       7  W L 1
                       8  M R.1.2 2.2.3
                       9  M R.3.6 2.26.29
                      10  M R.7.14 2.41.48
                      11  I A
                      12  M 1.1.120 2.1.120
                      13  U
                      14  W 2

        Routine

        2  Replaces  the income field in the income record
        with the income field from the matching correction
        card.

        5  Prints  the  unmatched  correction   card   and
        constructs  a  new  output record containing the
        state, industry and income fields.

        11 Moves records that are not to be  corrected  to
        the output file.

        13  Writes  an  output  record,  regardless of its
        source.


-
-
-
-
0
 ________________________________________________________________________

                                   -35-
1
                                  BESTOP
 ________________________________________________________________________


      E.__Page_Format_Control
+     __  ____ ______ _______
      A  two  character  zero  filled line counter provides the essential
 element of control in the printing of page headings, the skipping of the
 printer to a specific line or to the next page,  and  the  execution  of
 similar  functions  that  affect  the page layout of a report.  The line
 counter records the position of the next line to be printed on  a  page.
 It  is  set  to  "01"  when the printer is at the top of the page and is
 incremented an appropriate amount with each WRITE  instruction  that  is
 directed  to the printer.  It is reset to "01" with a skip to the top of
 a new page.  The counter may be tested with the "printer line test" form
 of the IF instruction.

        Example: Page Format Control

        Print  the  fields  specified  in  the line format
        below from each  record  in  File  1.   Print  the
        report title "Average Income Report" at the top of
        each  page  along  with  a  page  number and date.
        Print appropriate headings  over  the  columns  of
        data.   Do  not print beyond the 54th line of each
        page.


               File 1 Format (required fields only)

                      Location       Contents

                         8           Region

                      14-15          Age

                        18           Race

                        22           Sex

                      31-36          Average Income (unedited)


                     Location        Contents

                         4           Region

                     11-12           Age

                        19           Race

                        26           Sex

                     33-39           Average Income (edited XXX,XXX)
-
 ________________________________________________________________________

                                   -36-
1
                                  BESTOP
 ________________________________________________________________________


      The program consists of three routines as follows:

          1    I C G '54'
          2    W S H
          3    I C E '01'
          4    M 'AVERAGE INCOME REPORT' L.1.21
          5    M 'PAGE' L.32.35
          6    + '1' S.1.3               * PAGE COUNTER
          7    M S.1.3 L.37.39
          8    W L 1
          9    M D.1.18 L.1.18           * DATE
          10   W L 2
          11   M 'AVERAGE' L.34.40
          12   W L 1
          13   M 'REGION   AGE   RACE' L.1.20
          14   M 'SEX    INCOME' L.25.39
          15   W L 2
          16   U
          17   M 1.8 L.4                 * REGION
          18   M 1.14.15 L.11.12         * AGE
          19   M 1.18 L.19               * RACE
          20   M 1.22 L.26               * SEX
          21   E 1.31.36 L.33.39 '   ,   '
          22   W L 1


        Routine

        1  Tests for the end of a page (line counter value
        greater than 54) and skips to the  top  of  a  new
        page if the test is met.  The line counter is then
        reset to '01'.

        3  Prints  headings  at  the top of the page (line
        counter equal to '01'); numbers  and  dates  (from
        the  date area) each page.  It is good practice to
        place the heading routine  immediately  after  the
        end  of  page  routine.   If  the order of the two
        routines had been  reversed,  headings  would  not
        have  been  printed after the first page.  The end
        of page routine would have caused the line counter
        to be reset to "01", but the data printing routine
        below would have incremented the counter  to  "02"
        with  the  printing  of  a  data  line  before the
        heading routine was encountered.

        Care  must  be  taken  with  the  spacing  of  the
        constants  that make up the titles in the heading.
        It is good practice to layout the necessary titles
        on a printer spacing work sheet prior to coding  a
        heading routine.

 ________________________________________________________________________

                                   -37-
1
                                  BESTOP
 ________________________________________________________________________


        16 Unconditionally print  the required fields from
        each record.  The average earnings field is edited
        to insert a comma after the thousands digit and to
        suppress leading zeros.



      F.__Summarizing_Data
+     __  ___________ ____

      Data  in separate records may be summarized to provide group totals
 as long as the input file is sorted on the code field(s) that define the
 groups.  A file may be sorted with a standard utility  routine  that  is
 provided  with the operating system.  The "control break" form of the IF
 instruction is used to test for the change of a group in  routines  that
 process group totals.

        Example: Summarizing Data

        In   a  file  of   health   insurance   data,  the
        records are identified by state, program, and type
        of   service   with   one    record    for    each
        combination of those characteristics.  Each record
        also  contains  the  amount in dollars expended in
        the specified State on the  program  and  type  of
        service  in  a calendar year.  National totals are
        required for all expenditures, for  each  program,
        and for each type of service within a program.

        The  file  must first be sorted by program by type
        of service so that all of the records for a single
        program will  be  grouped  together  in  ascending
        sequence  by  program code and within those groups
        in ascending sequence by type of service.  In this
        sort the program code field is  called  the  major
        key  and  the  type  of  service code field is the
        minor key.  The first few records  in  the  sorted
        file might contain the following codes and data in
        the  order  shown.  The records have been numbered
        for reference



                          RECORD CONTENTS

        Record                        Type of
        Number         Program        Service        Expenditures

          1              01             3              284921
          2              01             3               17634
          3              01             3               43172
0
 ________________________________________________________________________

                                   -38-
1
                                  BESTOP
 ________________________________________________________________________


          4              01             5                9519
          5              01             5               38178
          6              01             7                8027
          7              01             7               23213
          8              02             2                6521
          9              02             3               18276
         10              03             3               50332
         11              03             3                9235
         12              03             3               45378
         13              03             5               87389
         14              03             5               20426
         15              03             7               72464
         16              03             7               15400
         17              04             2               57441

      The data records have the following format:


              Position            Contents

                1-2               Program code

                3-4               State code

                5                 Type of Service

                6-12              Expenditure in dollars



        The resulting program contains six routines, three
        to  print various levels of totals, an end of page
        routine, a heading routine, and routine which adds
        the expenditure data into counters.  Counters have
        been set up in scratchpad fields S.1.7, S.8.14 and
        S.15.24 for the service, program and grand  totals
        respectively.   Routines  to  print  totals appear
        first  in  the  program  so  that  totals  for   a
        completed   group   will  be  printed  before  the
        expenditures shown in the first record  of  a  new
        group  are  added  into the counters and so that a
        page will not start with a program or grand total.
        "Control break" IF instructions are used to detect
        changes in the program and type of  service  codes
        that  signal  the end of a group.  An "end of run"
        IF instruction controls the printing of the  grand
        total.   Routines  that  depend on "control break"
        and "end of run" IF instructions are the only ones
        that can be executed during the  "last  pass:   so
        that  totals  covering  routines  are  arranged in
0
 ________________________________________________________________________

                                   -39-
1
                                  BESTOP
 ________________________________________________________________________


        minor to major order so  that  subtotals  will  be
        printed before higher level totals.

          1    I 1.1.2 0                  * PROGRAM BREAK
          2    I 1.5                      * ST OR PGM BRK
          3    E S.1.7 L.21.29            * TYTPE TOTAL
          4    W L 1
          5    C S.1.7                    * CLEAR COUNTER
          6    M 1.5 L.14
          7    I 1.1.2                    * PROGRAM BRK
          8    M 'TOTAL' L.12.16
          9    E S.8.14 L.21.29           * PROGRAM TOTAL
         10    W L 2
         11    C S.8.14                   * CLR PGM TOTAL
         12    M 1.1.2 L.4.5
         13    M 1.5 L.14
         14    I F                        * US TOTAL
         15    M 'ALL PROGRAMS' L.5.16
         16    E S.15.23 L.19.29
         17    W L 1
         18    I C G '54'
         19    W S H
         20    I C E '01'
         21    M 'PROGRAM   SERVICE    AMOUNT' L.2.29
         22    W L 2
         23    M 1.1.2 L.4.5
         24    M 1.5 L.14
         25    U
         26    + 1.6.12 S.1.7             * TYPE TOTAL
         27    + 1.6.12 S.8.14            * PROGRAM TOTAL
         28    + 1.6.12 S.15.23           * US TOTAL


        Routine

        1 Prints type of service totals with a  change  in
        either  the  program or type of service code.  The
        test for a change in program code was included  to
        avoid  problems with situations such as that which
        arises between records 10 and 11 when a change  in
        program  code  was  not accompanied by a change in
        the type of service code.   The  type  of  service
        code  for  the next group is stored in the listing
        areas after the total for the last  service  group
        has  been  printed.   The service total counter is
        cleared for the next service group total.

        7 Prints program  totals  with  a  change  in  the
        program  code.   Both  the  program  code  and the
        service code are stored in the listing area  after
0
 ________________________________________________________________________

                                   -40-
1
                                  BESTOP
 ________________________________________________________________________


        printing  since the service code stored by routine
        #1 was wiped cut by the word  "TOTAL."  Note  that
        the  program  code  is  only stored (and therefore
        printed) with a change in  program.   Such  "group
        indicating"   improves   the  readability  of  the
        resulting listing.

        14 Prints the grand total at the end of  the  run.
        There  is no need to clear the grand total counter
        as it will not be used again.

        18 Skips to the top of  the  next  page  when  the
        printer goes beyond line 54.

        20  Prints column headings at the top of the page.
        The program and service codes are  stored  in  the
        listing   area   to   provide   for   the   proper
        identification of the first  date  line  following
        the headings.

        25  Adds  the  expenditure amount from each record
        (unconditionally) into the service,  program,  and
        grand total counters.

        Note  the  comments  throughout the program.  They
        make  the  program  more  readable  and   aid   in
        debugging.   Also,  should changes have to be made
        to the program, comments  tend  to  be  exceedinly
        helpful.



-
-
-
-
-
-
0
 ________________________________________________________________________

                                   -41-
1
                                  BESTOP
 ________________________________________________________________________


                          V.__PROGRAM_DEBUGGING
+                         __  _______ _________
0
      A BESTOP run produces a number of items which are useful in program
 debugging  or  in  checking  the  results  of  the  run.   These include
 compilation diagnostics and end of run file dumps and record counts.  It
 is also possible to execute runs which produce only program diagnostics.

      A.__Compilation_Diagnostics
+     __  ___________ ___________

      Compilation diagnostic messages are produced during the compilation
 of  the  individual  instructions  and  at  the  end  of the compilation
 process.  The instruction diagnostics note such things  as  unrecognized
 instruction  patterns, invalid field specifications, incorrect sequences
 of instructions and overlapping fields.  They are printed to  the  right
 of  the  instruction  that  is in error.  End of compilation diagnostics
 note irregular conditions that might exist at the end of  a  compilation
 such  as  a  missing  KEYS  statement  in  a matched file run.  They are
 printed at the end of the instruction listing.

      Diagnostic errors  must  be  corrected  before  a  program  can  be
 executed.

      B.__Instruction_Diagnostics
+     __  ___________ ___________

      An  instruction  diagnostic  is  printed as a series of dots to the
 left of the  instruction  with  the  dots  representing  the  individual
 parameters of the instruction from left to right.  The dot corresponding
 to the parameter that is in error is replaced by a letter that indicates
 the nature of the error.  The meanings of the error letters are provided
 below.

         .F....  File  Code Error (may occur in the second through
         the sixth instruction parameters) The file  code  of  the
         specified  field  is  not  a  legal file code.  Check and
         recode the field specification.

         .I.... Write File Error - The file specified in  a  WRITE
         instruction  has  been  specified as an input file in the
         EXEC statement.  Check  the  program  logic  and  correct
         either the WRITE or the EXEC statement.

         .L....  Field  Length  Error  (may  occur  in  the second
         through the sixth instruction parameters) The  length  of
         the  specified  field  exceeds  the maximum permitted for
         that  type  of  instruction.   See   the   appendix   for
         instruction field length restrictions.

         .M....  Match  File  Code  Error (may occur in the second
         through the eleventh parameters) The  file  code  of  the
0
 ________________________________________________________________________

                                   -42-
1
                                  BESTOP
 ________________________________________________________________________


         field specification does not match the corresponding A or
         B file code specified in the job control language.

         .O....  Field  Overlap  Error  (may occur in two or three
         parameters within a  single  instruction)  The  specified
         fields overlap, i.e., they have one or more characters in
         common.   Overlapping  fields  are not permitted within a
         single instruction.  Recode the instruction to  eliminate
         the  overlap  or replace it with two or more instructions
         which  will  perform  the   desired   operation   without
         overlapping fields within a single instruction.

         .P... Instruction Pattern Error - There is no instruction
         in  the  BESTOP  language  with the particular pattern of
         operation  code,  constant,  field   specifications   and
         modifiers  as that specified.  Recheck the description of
         the desired instruction.

         .R... Field Range Error (may occur in the second  through
         the  sixth  instruction  parameters)  Part  or all of the
         specified field is beyond the limit of the records in the
         specified file.  For input files the limit is the  actual
         record  length  as  specified in the data set label.  For
         numbered output files the  limit  is  4096  bytes  unless
         record  lengths are provided in the DD statements for the
         output files.  Record length limits for the reader, punch
         and listing files are 80, 80 and 132  respectively.   The
         limit  for  the  date  area is 42 bytes.  In any event, a
         field

         .S...  Instruction Sequence Error - indicates a violation
         of one of the following sequence rules:

             1.   An  IF instruction with an and/or link can only
             be followed by an IF instruction.  Conversely, an IF
             instruction  cannot   immediately   follow   an   IF
             instruction that does not have an and/or link.

             2.  An UNCONDITIONAL instruction can only be used to
             start  a  routine that immediately follows a routine
             started by an IF or OTHERWISE Instruction.

             3.  An OTHERWISE instruction can  only  be  used  to
             start  a  routine that immediately follows a routine
             started by an IF instruction.

             4.  IF, OTHERWISE, or UNCONDITIONAL instructions may
             not immediately precede or follow each  other  since
             only one type of conditional instruction may be used
             to   start   a   routine.    However,   several   IF
0
 ________________________________________________________________________

                                   -43-
1
                                  BESTOP
 ________________________________________________________________________


             instructions may appear in succession when they  are
             properly linked.

             5.   A SUBROUTINE or TABLE may not be defined within
             a SUBROUTINE.  However, a SUBROUTINE may  contain  a
             BRANCH  to another subroutine as long as it does not
             result in a direct or indirect branch  back  to  the
             SUBROUTINE containing the BRANCH.


         T.....  Parameter Type Error (may occur in any parameter)
         - The specified parameter was  not  of  a  type  that  is
         recognized  by  the  BESTOP program.  The following types
         are permitted:

             1.    Operation   codes   and   modifiers  -  single
             characters

             2.   Constants  -  enclosed  in   apostrophes.    An
             apostrophe  within  a constant is represented by two
             successive apostrophes.

              3.  Field specifications of
             the form F.S.E or F.S where:

                  F  is a valid file code,
                  S  is one to four digits denoting the starting
                     position of the field, and
                  E  is one to four digits denoting the ending
                     position of the field.

        Parameters  must  be  separated from each other by
        one or more blanks.


      D.__Record_Counts_And_File_Dumps
+     __  ______ ______ ___ ____ _____

      Record counts for each file processed by the program are printed at
 the end of the run.  These counts should be checked for consistency with
 the anticipated results of the run.

      The program also prints a dump of the first fifty records that were
 processed  in the order in which they were read or written.  The records
 are printed 100 characters to the  line  and  are  identified  by  file.
 Record  lengths  and  consecutive  record  numbers are also shown on the
 listing.  These  dumps  should  be  reviewed  carefully  to  verify  the
 processing performed by the program.

-

 ________________________________________________________________________

                                   -44-
1
                                  BESTOP
 ________________________________________________________________________


      E.__Test_Runs
+     __  ____ ____

      Test  runs  may be performed to obtain any diagnostic messages that
 might be produced by the compilation  of  a  program  or  to  check  the
 processing of a limited number of records from the input files(s).

      A program that contains diagnostic errors cannot be executed.  If a
 diagnostic error is encountered, the run is terminated at the end of the
 compilation  step.   It  is  frequently  advantageous  to submit a short
 production run without testing since the program will either be executed
 or Bestop will issue diagnostic messages indicating why the  run  cannot
 be executed.

      Occasionally,  it  is  useful  to  compile a program for diagnostic
 purposes without executing it even if there are  no  diagnostic  errors.
 It  is possible to do this by specifying a diagnostic run in the program
 parameters of the job control language.

      Short test runs can be executed on a portion of the  input  file(s)
 by  including  a  halt  procedure in the program.  This procedure should
 count the number of passes through the object program and halt  the  run
 when a sufficient number of records have been processed.  For example, a
 procedure  that  would limit the processing to 500 records from a single
 input file would be:

                         + '1' S.1.3
                         I N S.1.3 G '500'
                         H R



-
-
-
-
-
-
-
 ________________________________________________________________________

                                   -45-
1
                                  BESTOP
 ________________________________________________________________________


             VI.__APPENDIX_A_-_OS/370_OPERATING_INSTRUCTIONS
+            ___  ________ _ _ ______ _________ ____________
0
      A.__Job_Control_Language
+     __  ___ _______ ________
      Job  control  language  (JCL) provides information to the operating
 system on the files and other resources required for  a  job.   It  also
 identifies the user and provides necessary accounting information.


      B.__JOB_Statement
+     __  ___ _________

      The JOB statement identifies the user, specifies his account number
 and  establishes  the  work class of the job.  The parameters of the JOB
 card are covered in the User's Guide.

      C.__EXEC_Statement
+     __  ____ _________

      The  EXEC  statement  calls  the  BESTOP  compiler,  passes program
 parameters, specifies core memory requirements and sets a time limit for
 the run.  An EXEC statement is required for each BESTOP program that  is
 to be run within a job.  It is normally written in the following form:


 //step  EXEC  PGM=BESTOP,REGION=sizeK,PARM='parameters'

        where:

        step  -  is  the name of the step within the
        job.  It must begin with  a  letter  and  may  not
        exceed 8 characters.

        size  -  is the memory requirement in thousands of
        bytes.  This number must be followed by the letter
        "K." Bestop requires a minimum of 54K if  tape  or
        disk  files  are  not used.  Additional memory for
        tape and disk  files  is  equal  to  approximately
        twice  the  sum  of  the  tape  or disk file block
        sizes.  (See BLKSIZE in the DD statement.)


        parameters - are the program  parameters  required
        by the BESTOP compiler.  They must be separated by
        commas and enclosed in apostrophes.  The following
        parameters may be used:
             N           Suppresses the Bestop program listing

             I=(R/1-6)   Specifies the file code of the input file
                         in runs with a single input file.

             T=(1/2)     Specifies the run type in matched file
                         runs.

 ________________________________________________________________________

                                   -46-
1
                                  BESTOP
 ________________________________________________________________________


             A=(R/1-6)   Specifies the A file in a matched file
                         run.

             B=(R/1-6)   Specifies the B file in a matched file
                         run.

             D           Specifies a diagnostic run.

             C=number    Specifies the number of records to
                         be dumped on DDN=FILEDUMP, the
                         default is fifty.

        Example: Exec Statement

 //STEP1  EXEC  PGM=BESTOP,REGION=420K,PARM='T=1,A=1,B=2'


      D.__STEPLIB_Card
+     __  _______ ____

      The  STEPLIB  card is required.  It identifies the library on which
 the BESTOP compiler is located.

 //STEPLIB DD DISP=SHR,DSN=FEA.LINKLIB


      E.__DD_Statements
+     __  __ __________

      The DD Statement is used to identify the files to be processed in a
 step,  to  designate  them  as  input or output files and to specify the
 disposition of the files at the end of the run.  They are also  used  to
 specify  the  logical  record  length  and  block size for output files.
 Consult the instalations User's Guide and various manuals for details.


        Example: Job Control Language

        To transfer a deck of cards to a temporary file on
        disk  that  is  to  be used in a later step in the
        job.


 //STEPA  EXEC  PGM=BESTOP,REGION=240K,PARM='I=R'
 //STEPLIB  DD  DISP=SHR,DSN=FEA.LINKLIB
 //FIELDUMP DD  SYSOUT=A
 //LISTING  DD  SYSOUT=A
 //FILE1    DD  UNIT=SYSDA,DISP=(NEW,PASS),SPACE=(CYL,(5,5)),
 //             DCB=(LRECL=80,BLKSIZE=6400),DSN=&&CARDS
 //PROGRAM   DD   *
 M R.1.80 1.1.80
 W 1
 //READER  DD   *

 ________________________________________________________________________

                                   -47-
1
                                  BESTOP
 ________________________________________________________________________


         .
         .
         .
     data cards
         .
         .
         .

        To  read  and process a tape file to produce a new
        tape file.

 //PROCESS  EXEC   PGM=BESTOP,REGION=190K,PARM='I=1'
 //STEPLIB  DD  DISP=SHR,DSN=FEA.LINKLIB
 //FILEDUMP DD  SYSOUT=A
 //LISTING  DD  SYSOUT=A
 //FILE1    DD  DSN=CNaaaa.uuu.MY.DATA,DISP=OLD
 //FILE2    DD  DSN=CNaaaa.uuu.COPY.DATA,DISP=(,CATLG),
 //             DCB=(LRECL=80,BLKSIZE=6160,RECFM=FB),
 //             UNIT=DASD,SPACE=(TRK,(10,10),RLSE)
 //PROGRAM  DD     *
        .
        .
 program cards
        .
        .


      F.__Completion_Codes
+     __  __________ _____

      The following completion codes may be encountered in BESTOP runs.


 S000  Normal end of run

 S004  run ended by halt run instruction.

 S008  Diagnostic run

 S00C  Run ended by HALT JOB instruction

 S322  Execution of the job step took longer than the time
       allowed by the TIME parameter.

 S722  Maximum number of lines exceeded.

 S80A  The program required more memory than specified in the
       REGION parameter.

 S813  The dsname specified in a DD statement does not agree
       with the dsname in the file header label.
0
 ________________________________________________________________________

                                   -48-
1
                                  BESTOP
 ________________________________________________________________________


      G.__External_Tables
+     __  ________ ______

      Frequently  it  may  be  more convenient to code a Bestop table and
 save it into a dataset that may be referenced  by  the  Bestop  program.
 This  may  be  accomplished  by  coding the table entries (arguments and
 results) on a records and saving these records into a  card  image  file
 .The table is then referenced via a special DD statement identifying the
 external table.


        Example: External Table

 //STEP1  EXEC  PGM=BESTOP,REGION=240K,PARM='I=R'
 //STEPLIB  DD  DISP=SHR,DSN=FEA.LINKLIB
 //FIELDUMP DD  SYSOUT=A
 //LISTING  DD  SYSOUT=A
 //TABLEQ   DD  DISP=OLD,DSN=CNaaaa.PRJ.BESTOP.TABLES(TABQ)
 //FILE1    DD  UNIT=SYSDA,DISP=(NEW,PASS),SPACE=(CYL,(5,5)),
 //             DCB=(LRECL=120,BLKSIZE=6000),DSN=&&CARDS
 //PROGRAM   DD   *
 ****** ADD COUNTY NAMES TO THE FILE *****
 M R.1.80 1.1.80
 L Q E
 W 1
 T Q  R.1.6  1.101.120  * COUNTY NAME LOOKUP
 $
 //READER  DD   *
         .
         .
         .
     data cards
         .


        Notes:

        The "TABLEQ" JCL statement establishes the linkage
        between   the   exteranl   table   and  the  table
        definition in the program.

        The record length of  the  external  must  be  80.
        Therefore  the  sum of the lengths of the argument
        and result cannot exceed 80.

        The  "$"  after  the  table  definition  statement
        indicates that this is a external table.






 ________________________________________________________________________

                                   -49-
1
                                  BESTOP
 ________________________________________________________________________


                  VII.__APPENDIX_B_-_MAXIMUM_FIELD_SIZES
+                 ____  ________ _ _ _______ _____ _____
0

      The widths of the fields or constants in the following instructions
 are limited to the specified number of characters.

             IF (Character Field Comparison          256
             IF (Numeric Field Comparison             16
             IF (Control Break)                      256
             MOVE                                   4096
             EDIT                                     16
             CLEAR                                  4096
             ADD                                      16
             SUBTRACT                                 16
             MULTIPLY
                  Multiplicand                        16
                  Multiplier                          15
                  Product + Rounding                  16
             DIVIDE
                  Dividend                            16
                  Divisor                             15
                  Quotient (extended)                 14
             KEYS                                    256



-
-
-
-
-
-
-
-

 ________________________________________________________________________

                                   -50-
1
                                  BESTOP
 ________________________________________________________________________


            VIII.__APPENDIX_C_-_EIA_IMPLEMENTATIONS_OF_BESTOP
+           _____  ________ _ _ ___ _______________ __ ______
0
      A.__BESTOP50,_BESTOPVL,_BEST400
+     __  _________ _________ _______

      These  are  the  original  versions  of  BESTOP  avalibale  at EIA.
 Basically they are all the same.  In the BEST400 version, 400K  of  work
 area  is  allocated  in order that the user may write larger programs or
 tables.

      B.__SUPERB
+     __  ______

      SUPERB  is a enhanced version of BESTOP the allows the user to call
 this  program  from  a  higher  level  language  like  PL/1  or   Cobol.
 Furthermore,  only  columns 1 thur 72 of the source program are scanned,
 and columns 73 thru 80 are ignored.  This means the user may enter  "RUN
 FETCH" instead of "RUN FET UNN" in Superwylbur.  In addition, the source
 program  gets  listed in the SYSPRINT file rather than the LISTING file.
 Also file counts are displayed in the SYSPRINT file.

      C.__BESTOP
+     __  ______

      BESTOP  is  actually  a  PL/1 program that calls SUPERB.  It offers
 several interesting features.  The user may code  instructions  to  copy
 source  code  from  a  library into his/her program.  Another feature of
 this program is that more than one instruction can be coded on one line,
 provided that the instructions are seperated by a semicolon.   When  the
 instructions are listed during exection, they will be listed on seperate
 lines.   As the code is being copied, it may simultaneously be modified.
 Another interesting feature is that BESTOP has several "canned"  program
 imbedded  within  it.   Most  notably is a update program.  All the user
 needs to code is the program invocation and suitable  parameters.   This
 update   program   can  handle  virtually  any  simple  sequential  file
 structure.  Other canned routines include a sequence checking routine, a
 dump and a file comparison routine.

        Example

  //UPD EXEC PGM=BESTOP,REGION=600K,PARM='T=1,A=1,B=3'
  //STEPLIB  DD  DISP=SHR,DSN=FEA.LINKLIB
  //SYSPRINT DD  SYSOUT=A
  //LISTING  DD  SYSOUT=V,FLASH=OUO
  //FILE1 DD DISP=(OLD,DELETE),DSN=&&UPD
  //FILE2 DD DSN=&&NEWM,UNIT=SYSDA,
  //  DISP=(NEW,PASS),SPACE=(CYL,(1,1),RLSE),
  //  DCB=(RECFM=FB,LRECL=80,BLKSIZE=6160)
  //FILE3 DD DISP=(OLD,DELETE),DSN=&&MSTR
  //PROGRAM  DD *
  @UPDATE K='1.1.22 3.1.22 1.30.36 3.30.36',               +
          T='23',S='37',E='80',L='80'


 ________________________________________________________________________

                                   -51-
1
                                  BESTOP
 ________________________________________________________________________


        Notes:

        FILE1  is  the transaction file.  FILE3 is the old
        master file.  FILE2 is the updated master file.

        The key fields are the first 22 positions in  each
        file.  Each file must therefore be sorted on these
        positions.

        The  transaction  code  is  in  position 23 of the
        transaction file.  Valid codes and there  function
        are as follows:

             A,I - add/insert a record into the file

             C,R - change/revise a record

             D   - delete a record

             U   - add a record if the transaction key is
                   less than the master key, otherwise
                   change a record if the keys match.

        The  plus  sign indicates that this instruction is
        continued.

        "S"  indicates  the  start  of  the   data.    "E"
        indicates  the  end of the data, and "L" shows the
        record length.  If E=L, then E may by omitted.

        Revisions are performed in  the  data  area  only.
        This updated program assumes no prior knowledge of
        the  demarcation  of  data  fields.  Revisions are
        performed  on  a  character  by  character   basis
        according to the following rules:

             1.   If a character on the transaction record
             is blank,then the corresponding character  on
             the master file record will remain unchanged.

             2.   If  the  character  on  the  transaction
             record is  not  blank,  then  this  character
             replaces  the  corresponding character on the
             master file record.

             3.  The exception to  the  previous  rule  is
             that  if the transaction record has the value
             of the "BLANK"  variable  (default  is  "_"),
             then   the  corresponding  character  on  the
             master file record becomes blank.
0
 ________________________________________________________________________

                                   -52-
1
                                  BESTOP
 ________________________________________________________________________


        Only  the  first 130 characters of the transaction
        record will be listed.  The type of transaction is
        indicated  in  column   one  of  the  listing   as
        follows:

              "+" - this record has been added to the file

              "-"  -  this  recods  has  been deleted from
              the file

              "  "  -   this    is    a    revision/change
              transaction record

              ">"  - this is the original master record to
              be changed

              "<" - this id the changed master file record

              "*"  -  this  transaction   record   has   a
              processing error  (i.e.  a  matching  record
              exist  if  an  insert  was  attempted, or no
              matching   record  exists  if  a  delete  or
              change was attempted)



        Example

        Obtain  the  documentation  for the various canned
        programs

             @HELP HELP

        Get the description of the syntax for the sequence
        checking program

             @HELP SEQCHK
-
-
-
-
-
 ________________________________________________________________________

                                   -53-
1
                                  BESTOP
 ________________________________________________________________________


        Example

        Copy  source  code  into a Bestop program prior to
        actual program execution.

 //DUMP   EXEC PGM=BESTOP,REGION=600K,PARM='I=1'
 //STEPLIB  DD DISP=SHR,DSN=FEA.LINKLIB
 //SYSPRINT DD SYSOUT=A
 //LISTING  DD SYSOUT=A
 //FILE1    DD DISP=OLD,DSN=CNaaaa.uuu.MASTER.FILE
 //MACROS   DD DISP=SHR,DSN=CNaaaa.uuu.BESTOP.SOURCE.LIB
 //PROGRAM  DD *

 *  LIST  STATES  ALABAMA  & ALASKA FROM THE MASTER FILE
 *  ALSO LIST STATE AND COUNTY NAMES
 *   1.3  =  STATE CODE, 1.6 = STATE & COUNTY CODE

 I  M  1.1.6  E  '010,020'
    M  1.1.80  L.1.80
    L S E       * LOOKUP STATE NAME
    L C E       * LOOKUP  CNTY  NAME
    W L 2

 T S 1.1.3  L.81.100       *  STATE  TABLE
 &STATES   SEL=(010),  SEL=(020)
 T  C  1.1.6 L.101.120     *  COUNTY NAMES
 &COUNTIES  SEL=(010), SEL=(020)


        Notes:

        The file defined by the DDName=MACROS  must  be  a
        partitioned dataset.  "STATES" and "COUNTIES"  are
        members of the PDS.


        To  include  data  from a member into the program,
        code an ampersand "&" in column 1 followed by  the
        member  name.   The included data may be qualified
        and/or modified during the copy operation. (For  a
        more   complete  description  of  this  mechanism,
        reference the documentation for the MACROS program
        written by Hans Becker (202-252-6874)).

-
-
0
 ________________________________________________________________________

                                   -54-