BFX

                      Copyright (c) 1992 Richard D. Fothergill



























                                                      Richard D. Fothergill
                                                           the Oak Hill BBS
                                                          141 Oak Hill Road
                                                      Pittsfield, MA  01201
                                                  Data/FAX - (413) 499-7245












          WHAT IS BFX?

          When  I purchased my ZyXEL  U-1496 Modem/Fax I wanted an easy way
          to  be able to accept fax and modem calls on the same line.  This
          would allow me to continue to operate my BBS software and be in a
          position  to receive  faxes.  I  tried BinkleyTerm and FrontDoor.
          Both  excellent programs, but  way more than  I needed or wanted,
          not  having a  need for  network mailers  or a  built in terminal
          program.   I wanted  something simple,  small, easy  to setup and
          maintain.  Thus the beginning of BFX.

          WHAT CAN I DO WITH BFX?

          You  run BFX instead  of your BBS  software.  BFX will answer the
          phone,  decide  what  the  incoming  call  is  and  exit  with an
          errorlevel  which you  can  use in  a  batch file  for subsequent
          operations.   A BBS  call will also  create a  batch file to call
          your  BBS software.  In addition  you can program up to 10 events
          with  a preset time  of execution and  exit errorlevel.  When BFX
          encounters  one of  these it  will  exit with  your predetermined
          errorlevel.   Again, you control further processing in your batch
          file.

          DISCLAIMER

          IN  NO EVENT WILL  I BE LIABLE  TO YOU FOR ANY DAMAGES, INCLUDING
          ANY   LOST  PROFITS,   LOST  SAVINGS   OR  OTHER   INCIDENTAL  OR
          CONSEQUENTIAL DAMAGES ARISING OUT OF YOUR USE OR INABILITY TO USE
          THE PROGRAM, OR FOR ANY CLAIM BY ANY OTHER PARTY.


























          BFX                                               -1-
          Copr (c) 1992 Richard D. Fothergill









          INSTALLATION

          There  are three files that you must create to run BFX.  They are
          BBS.BAT, BFX.CFG, BFX.EVT.  I will discuss these individually.

          BBS.BAT

          This batch file is the heart of your BBS/FAX system.  It controls
          all  activity and  execution.  You  do not  have to  use the name
          BBS.BAT,  it can be any  name of your choosing.  The following is
          the BBS.BAT file I use.

          @ECHO OFF
          :loop
            cls
            BFX
            if errorlevel 40 goto event
            if errorlevel 30 goto fax
            if errorlevel 20 goto spit
            if errorlevel 10 goto spitl
            if errorlevel  0 goto end
          :event
            sfmaint
            goto loop
          :fax
            rcvfax 1 f:\sf\fax
            goto loop
          :spit
            call bbsexe
            goto loop
          :spitl
            spitfire 0
            goto loop
          :end

          There are four hardcoded errorlevels.  They are:

               0 - Terminate
              10 - Local Logon
              20 - BBS/Modem Connection
              30 - FAX Connection

          The  loop: label is where execution of the batch file will return
          to  after any activity other  than a normal exit.  BFX is started
          and  awaits a caller.  If a call is received or a scheduled event
          occurs  BFX will exit with the corresponding errorlevel.  Control
          then returns to this batch file.








          BFX                                               -2-
          Copr (c) 1992 Richard D. Fothergill









          BFX.CFG

          This is the configuration file you setup to inform BFX of certain
          parameters  it  needs to  function.   The following  is  a sample
          configuration file.

          CM=2
          BA=38400
          PA=N
          DA=8
          SB=1
          MI=AT&FM0V1E0H0S2=1X7#B1+FCLASS=6
          AS=ATA
          HY=ATH0
          HN=ATH1
          MR=ATZ
          BB=SPITFIRE
          BP=
          CP=/C
          EC=/E
          ST=120
          RC=2
          LM=>> BFX >> logging on to...

          There  are no spaces  allowed in this  file between the parameter
          and  the = sign.  The items should appear in the sequence listed.
          The parameters and the meanings are a follows:

          CM  The communications port you have your modem on.

          BA  The baud rate to initialize your modem to.

          PA  Parity

          DA  Data length

          SB  Stop Bits

          MI  Your initialization string for modem/fax reception.

          AS  Modem answer string.

          HY  Modem onhook string.

          HN  Modem offhook string.

          MR  Modem reset string.

          BB  The name you would like placed in the BBSEXE.BAT file.

          BP  The text you would like to preceed the baud rate parameter in
              the BBSEXE.BAT file.



          BFX                                               -3-
          Copr (c) 1992 Richard D. Fothergill









          CP  The text you would like to proceed the com port parameter in
              the BBSEXE.BAT file.  Spitfire specifies that the parameter
              read /C<comport>.  Check your BBS software.

          EC  The text you would like in then BBSEXE.BAT file to notify
              your BBS software of an error correcting connection.

          ST  Sleep time out seconds.  This is the amount of time BFX
              will wait before blanking the screen.  A display of the
              program name and current time will appear at random locations
              to remind you of the program running.  If ST=0 then screen
              blanking is disabled.

          RC  The number of rings on which you would like BFX to answer
              the call.

          LM  Log on message.  This is sent to the caller just before BFX
              exits on a modem connection.

          BFX.EVT

          This file is used to define your events.  It is a comma delimited
          file consisting of three parameters.  The first is a 40 character
          description.  This will be written to the log file when the event
          is executed.  The second is the time you want the event to occur.
          The format is HH:MM and is in 24 hour time.  The last item is the
          errorlevel.   This can  be any  integer value  except one  of the
          hardcoded  errorlevels mentioned earlier.  Each event must appear
          on  a separate line in the file and you are limited to 10 events.
          A typical line in the event file is as follows:

              DAILY MAINTENANCE,01:00,40

          This  line would cause  BFX to  exit with an  errorlevel of 40 at
          1:00 am.

          FILES CREATED BY BFX

          There  are three  files  created by  BFX.   A discussion  of each
          follows.

          BFX.LOG

          If  this file  is not  found at  start-up BFX  creates a new one.
          Each  time an activity occurs,  an entry is written to this file.
          The entry will consist of the date, time, description of activity
          and  either the errorlevel for an event or the CONNECT string for
          a  modem connection.  Local logons  are not recorded in the file.
          This  file has  no interaction with  your BBS  log file.  A modem
          connection  may be made  and control passed  to your BBS software
          and  the user might  hang up with  out logging on.  In this case,
          there  would still be  a record of  the connection in the BFX.LOG
          but in all probability, not in your BBS log.


          BFX                                               -4-
          Copr (c) 1992 Richard D. Fothergill









          BFX.STS

          This  is a  file used  strictly by  BFX.  Each  time BFX releases
          control  back to DOS, BFX writes control data to this file.  When
          it  restarts it  reads this  information  back in.   Although not
          required,  it is suggested  that each time  you erase the BFX.LOG
          file  to  clear  that,  you  erase  BFX.STS  to  reset  the  call
          statistics.   You do not have  to recreate these files.  BFX will
          create new ones if existing files are not found.

          BBSEXE.BAT

          When  a BBS call is  received, BFX will create a batch file which
          contains  the name (BB),  followed by the  baud rate prefix (BP),
          baud  rate, com  port prefix  (CP), com  port (CM)  and the error
          correcting  string  (EC) .   The  parameters you  specify  in the
          configuration  file should allow  you to  construct an entry that
          will  allow you  to start your  BBS software.   The format of the
          line in BBSEXE using the configuration parameters is:

              [BB] [BP]<baud rate> [CP][CM] [EC]
              SPITFIRE 14400 /C2 /E


          GENERAL DISCUSSION

          As  you can  see  from my  sample  BBS.BAT file  I  am set  up as
          follows.

          Errorlevel                Action

              0         Normal program exit.  Modem reset.
             10         Local logon to BBS.  Spitfire requires that you
                        call it with a baud rate of 0 to let it know that
                        it is a local log on and not try to detect a
                        carrier.
             20         Remote call BBS logon.  Spitfire requires that you
                        call it with a baud rate and com port to notify it
                        that a connection has already been made and to
                        proceed to the user log on.
             30         Remote call FAX transmission.  The batch file
                        passes control to ZyXEL's RCVFAX program which also
                        assumes a connection has been established.
             40         User specified event.  I have this set to occur at
                        1:00 am.  This is routine BBS maintenance.  Please
                        remember, running in a system such a this, in all
                        probability events scheduled in your BBS software
                        will never occur.  Your BBS software is not the
                        program controlling the flow, BFX is, so events
                        should be schedule through BFX.





          BFX                                               -5-
          Copr (c) 1992 Richard D. Fothergill









          MENU AND HOT KEYS

          From  the Waiting  for Caller  screen you  have two  possible key
          strokes.   Alt-X will close BFX and execute a normal exit.  Alt-M
          will bring up a pop menu with the following selections available:

              View Activity Log
              Local Logon
              Drop to DOS
              Terminate BFX

          Within  this  menu  your  mouse  will  be  active  to  locate the
          highlight  bar or you  can use the  arrow keys.  Either press the
          left mouse button or the enter key to make a selection.  Pressing
          the  right mouse  button or  the Esc  key will  return you to the
          Waiting for Caller screen.

          View  Activity Log  - This  selection  will pop  up a  window and
          display  the BFX.LOG file.  All  the direction keys are active as
          well  as the mouse.  Press  the Esc key or the right mouse button
          to return to the menu.

          Local Logon - This will exit the system with an errorlevel of 10.
          This  does not  have to  be a  local log  on.  You  can have your
          BBS.BAT file execute any program you wish or none at all.

          Drop  to DOS  - Self explanatory.   The DOS  prompt is amended to
          remind you to EXIT back to the BFX menu.

          Terminate  BFX - Same as  the Alt-X key press.  Executes a normal
          exit back to dos.
























          BFX                                               -6-
          Copr (c) 1992 Richard D. Fothergill