ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
    ³      RemoteAccess Avatar Conversion Utility version 1.01     ³
    ³           copyright (c) S/e/m/a/j Communications.            ³
    ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

The RemoteAccess Avatar Conversion utility, or AVTCONV, will convert
your existing ansi (.ANS) screens into Avatar (.AVT) screens suitable
for use with RemoteAccess 1.10.

Conversion of screens into Avatar is always possible, but not always
easy. If ANVCONV says that a screen cannot be converted, then you should
load the screen into TheDraw, or similar ANSI drawing package, and
resave it with no line length limit.

Screens containing RemoteAccess control codes may need special care.


                           What AVTCONV does
                           ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

For the technically minded, AVTCONV directly translates the following
ANSI control codes:

        ESC [ ... H             direct cursor movement
        ESC [ ... f             direct cursor movement

        ESC [ 2 J               clear screen
        ESC [ K                 erase line
        ESC [ ... m             set graphics rendition.

AVTCONV handles the following control codes in a special way:

        ESC [ ... A             relative cursor movement
        ESC [ ... B             relative cursor movement
        ESC [ ... C             relative cursor movement
        ESC [ ... D             relative cursor movement

        ESC [ s                 save cursor position
        ESC [ u                 restore cursor position

Since the AVATAR control codes do not allow easy multiple cursor movements
in any direction, and for speed, AVTCONV replaces relative cursor movements
with a direct cursor movement. If AVTCONV is not sure of it's
position, or, there are less than two cursor movements in a row, it is
more efficient to use repeated relative cursor movements, so that's what
it does.

If AVTCONV knows where it is on the screen, it strips the save cursor
position command, and replaces the restore cursor position command with
a goto cursor position command. If it encounters these commands and it
doesn't know where you are on the screen, it reports that the file cannot
be converted.

Additionally, AVTCONV automatically scans for repeated characters and
reduces them to an Avatar "repeat character" sequence if this would be
more efficient (byte-wise). Lastly, if enabled, AVTCONV can compress
the file even further using advanced pattern recognition features.

Unfortuately, at the moment, hardly any comms packages support pattern
expansion which contains avatar codes, so, this compression is not selected
by default. Besides which, the scanning mechanism is slow!


                          How to use AVTCONV
                          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

With this release of AVTCONV, a number of switches have been provided to allow
greater flexibility, and speed.

Options should be specified on the command line.  They can be preceeded by
either a "/" or a "-".  Most of the options are "toggles". You should
append either a "+" or "-" to turn on or off the option respectively. If
you don't specify either, then the option is turned on.

eg.	AVTCONV /o- /c /a+ /x95

	Would turn off cursor optimisation, AVT/0+ compression on,
	animation delays on and sets the screen width to 95.
	
The default for each of the


	/o		Cursor optimisation.
	(active)	When on, AVTCONV will scan through your file removing
			redundant save/restore cursor position commands, to
			further decrease the size of the AVT file.
			
	/c		AVT/0+ compression.
	(off)		Although RemoteAccess supports AVT/0+ compression,
			many communications programs do not. Even FrontDoor
			v2.00 has problems with this compression, so its
			probably not a good idea to use this until more
			programs support AVT/0+.  Basically, this option
			enables a pattern recognition search, further
                        decreasing the size of your AVT file. Unfortunately,
			this is very slow, but I hope to speed it up in
			a future version.	

	/r		RLE compression.
	(on)		This is simple data compression supported by all
			Avatar compatible communications packages. There
			should be no reason to turn it off, but you can
			if you like...!
			
	/a		Animation delays.
	(off)		Normally, AVTCONV ignores the delays put into
			animation by programs such as TheDraw, but when
			this option is specified, these delays are
			included.
			
	/x		Screen width.
	(80)		Follow this command by width of your screen. There
			should be no reason to alter it from 80, but
			just in case..
			
	/y		Screen height.
	(25)		This option should be followed by the height of your
			screen. See screen width for more information.

To run AVTCONV, simply type..
			
   AvtConv [options] [path] [ext]

where,

  path is the path to the files you want to convert (eg \RA\TXT\*.ANS),
  the default is *.ANS

  ext is the extension to put on the new files, the default is AVT.

Examples of use:

   AVTCONV
   will convert *.ANS in the current directory to .AVT files.

   AVTCONV /c- C:\RA\TXTFILES\*.ANS AKK
   will convert *.ANS in the ra textfiles directory to .AKK files without
   cursor optimisation.

   AVTCONV \*.ANS /r-
   will convert *.ANS in the root directory to .AVT files, with RLE
   compression off.