Why use the Quick Basic HLLAPI

	Every multitasker that I have examined insists on managing INT
	14h.  The FOSSIL specification is basically an extension of the
	normal BIOS INT 14h functions.  However, in implementing a FOSSIL
	with features that are not supported by BIOS's INT 14h, additional
	registers were used to pass additional parameters.  Some
	multitaskers will intercept the INT 14h calls and will alter
	registers that are not normally used by BIOS.	 Quarterdeck's tech
	support confirmed to me that they may change the DS register when
	DESQview intercepts an INT 14h  (when released, version 2.26  of
	DESQview is supposed to correct this).  What this means is that
	some FOSSIL functions will work correctly with a multitasker and
	others will not.  Additionally, it means that if one application
	program uses a FOSSIL function that another application does not
	use, then one of the programs may work fine with a multitasker
	and the other may not.

	My first task in solving problems with multitaskers was to
	eliminate the need for X00 to be called using an INT 14h.  Starting
	with version 1.20  of X00, I have included quick and dirty HLLAPI
	routines for some high level languages.  More are yet to come.
	Applications programmers should replace references to library
	routines in their existing source with the replacement routine(s)
	included in the X00 distribution file. Then include the appropriate
	object module in the linking process.  At this writing, HLLAPIs are
	included for:

	   Microsoft C, all models
	   Borland's Turbo C
	   Borland's Turbo Pascal
	   Microsoft Quick Basic

        The first time the HLLAPI is called, it will determine if X00 is
        the active FOSSIL.  If X00 is the active FOSSIL, then it will be
        directly called instead of using INT 14h.  If X00 is not the
        active FOSSIL, or if there is no FOSSIL, the HLLAPI will issue an
        INT 14h.  After the first call to the HLLAPI, a maximum of only 4
        assembly instructions are added to the execution thread no matter
        what FOSSIL is installed.  The addition of 4 instructions to the
        execution thread should have no effect on execution speed of the
        application program.
 
	Using the HLLAPIs to access X00 with a multitasking system can
	result in significantly faster execution because the multitasker's
	management of INT 14h is avoided.  Thus, the multitasker has no
	opportunity to change the registers and all X00 functions should
	work correctly.

	Those using assembly language to access X00 should replace INT 14h
	instructions with a CALL BYPASS and include BYPASS.OBJ in the linked
	program.  BYPASS should be declared as a FAR external,
	i.e.	EXTRN	BYPASS:FAR











				QBHLLAPI

	I am not a Basic programmer, so please forgive any documentation
	blunders and/or syntax errors in the example Basic code fragments.

	Now included in the X00 distribution is an object module that allows
	access to all X00 functions from Quick Basic.  That module is:

		QBX00.OBJ

	Two routines are defined in this module, QBX00 and QBX00X.
	These routines are intended to be direct replacements for X00
	calls when using the Quick Basic statements CALL INTERRUPT,
	CALL INTERRUPTX, CALL INT86OLD and CALL INT86XOLD.  The only
	difference in the calling sequence(s) is that the interrupt number
	is not passed as a parameter.

	To use these interfacing routines, the programmer basically sets
	variables is a structure that corresponds to the processor's
	registers and passes the structure's address to QBX00 or QBX00X.
	When QBX00 or QBX00X is invoked, it copies the variables in the
	structure to the processor's registers and then calls X00.  Upon
	return from X00, all of the processor's registers are copied into
	the output structure.  The input structure and output structure
	may be the same.

	In order to provide convenient access to the QBX00 routines from
	the Quick Basic 4 environment, QBX00.OBJ should be converted
	into regular library (.LIB) and Quick Library (.QLB) formats.
	This can be accomplished by issuing the following DOS commands:

	           LIB QBX00 +QBX00;
	           LINK /Q QBX00,,,BQLB45

	For a more complete description of the structures and their uses,
	read the documentation about the library functions INTERRUPT,
	INTERRUPTX, INT86OLD and INT86XOLD in the appropriate Microsoft
	Quick Basic reference manual.  Also see the include file QB.BI
	which comes on your Quick Basic disks.

	The code fragments below are intended to provide examples of
	replacing INTERRUPT, INTERRUPTX, INT86OLD and INT86XOLD calls with
	QBX00 and QBX00X calls.

	My thanks to Scott Barnes for helping with documentation and testing
	the Quick Basic HLLAPI.


'** Sample QuickBasic 4.xx calls to X00.

'$INCLUDE: 'QB.BI'

DECLARE SUB QBX00 (inreg AS RegType,outreg AS RegType)
DECLARE SUB QBX00X (inreg AS RegTypeX, outreg AS RegTypeX)

COMMON SHARED INREG AS REGTYPE, OUTREG AS REGTYPE
COMMON SHARED INREGX AS REGTYPEX, OUTREGX AS REGTYPEX

    PORTNUM = 0                     'For COM1: operations

'** EXAMPLE 1: Initialize X00 driver and check initialization
    INREG.AX = &H400                        'FOSSIL function 04h
    INREG.DX = PORTNUM                      'Port number (0=COM1)
    INREG.FLAGS = 512                       'Keeps interrupts enabled
    CALL QBX00(INREG, OUTREG)               'Call X00
    IF OUTREG.AX <> &H1954 THEN             'If installed X00 returns &H1954
        PRINT "FOSSIL driver not found!"
        STOP
    ELSEIF (OUTREG.BX \ 256) < 5 THEN       'Is FOSSIL level 5 supported
        PRINT "FOSSIL driver does not support Level 5 commands."
        GOTO SHUTDOWN
    END IF

'** EXAMPLE 2: Transmit a string TXIT$ using FOSSIL's write block function
'** Note: The INREGX/OUTREGX structures and CALL INTERRUPTX statement must be
'         used since FOSSIL requires the ES register to be passed in the call.

    TXIT$ = "Sample data to be transmitted"
    TXSTART = 1                              'Try to xmit entire string
    MAXTX = LEN(TXIT$)                       'Total # of characters to xmit
    INREGX.AX = &H1900                       'Write block function code
    INREGX.DX = PORTNUM                      'Port number (0=COM1)
    INREGX.FLAGS = 512                       'Keeps interrupts enabled
    DO UNTIL TXSTART > MAXTX                 'Loop until entire string is sent
         TXNOW$ = MID$(TXIT$, TXSTART)       '
         INREGX.CX = LEN(TXNOW$)             'Length of to xmit
         INREGX.ES = VARSEG(TXNOW$)          'Segment of string
         INREGX.DI = SADD(TXNOW$)            'Offset of string
         CALL QBX00X(INREGX, OUTREGX)        'Call X00
         TXSTART = TXSTART + OUTREGX.AX      'Add chars actually sent
    LOOP