Point Calculator Ver 1.0
                                
                              By: Joe Thompson
                                  8-2-92
                              
                         Compuserve ID: 71321,1177
                         
                     EET BBS Fido-net address 1:116/24        
 
                              615-325-7800






                        Disclaimer and limit of liability

          Joe Thompson makes no warranty of any kind, either express 
          or implied, including but not limited to implied warranties
          of merchantability  and  fitness for a particular  purpose, 
          with respect to this software.
        
          In no event shall  Joe Thompson  be  liable for any damages
          (including damages for loss of business profits, business
          interruption, or loss of business information) arising out of
          the use of this software.



                                Summary

	  Point Calculator is a calculator program for Autocad that
 	  takes advantage of the release 12 dialog interface to pro
 	  vide a full function calculator plus the ability to get
   	  and manipulate points. These points are then returned to 
 	  the current command for use. The calculator can be called
 	  transparently so it is ideally suited to run inside the
	  line, circle, move or any other drawing command that 
	  requires a point coordinate or real number distance.


			      Requirements
		
          This program requires Autocad release 12+.

	      		      Installation


	  The Point Calculator is very easy to install simply copy
	  calc.exp and calc.dcl into your current Autocad path and
	  issue the following command at the Autocad command 
	  prompt:

		            (xload"calc")

	  This loads the program and assigns it to key <F10> by use
	  of ANSI escape sequences. This means that any time you hit
	  the <F10> key calc starts and runs transparently. Calc may
	  be incorperated into your existing menus or run from the 
	  command prompt by entering: 
		
				'calc

	 The Point Calculator may also be set to load every time 
	 Autocad runs by entering the line
		
				CALC
	
	 into your acad.ads file. 



			      Operation

	 The operation of Point Calculator is simply and straight
	 forward. the left side of the dialog contains a simply
	 scientific calculator with all basic functions including
         +, -, *, /, sin, cos, tan, square, square root, inverse
         sin , cos, tan, PI, sto in memory, rcl from memory, Ce
         clear entry, and  which deletes 1 character from the 
         end of an entry. The right bottom of the calulator also
         has two additional buttons IN and MM. These buttons 
         provide conversion between decimal systems. The Select
         button on the bottom right allows the selection of a 
         distance obtained from selecting two points on an Autocad
         drawing. The point selection osnap mode defaults to end
         and int so if you want something different you will have to
         enter it yourself.  The result obtained from the distance
	 between the two selected points is entered into the calcul
	 ators main register for manipulation. The INV button 
	 controls whether an sin or inverse sin is preformed.

	 The Right side of the calculator contains the point manipu
	 lation registers. There are three registers one for X, one
	 for Y and one for Z. When the program starts it reads the 
	 value of the LASTPOINT Autocad syatem variable and places
	 these coordinate values into the programs point registers.
	 These values may now be edited.  The buttons surrounding
	 the point registers are for transferring the value into
	 the calculator register and preforming simply addition and
	 subtraction on the point values. These buttons are defined
	 as follows.

	 X :
           This button transfers the contents of the calculator 
	 register into the X point register.

 	 X :
           This button transfers the contents of the X point 
	 register into the calculator register.

 	 X +:
           This button transfers takes the value in the calculator
	 register adds it to the X point register and places the
	 result in the X point register.

 	 X -:
           This button transfers takes the value in the calculator
	 register subtracts it from the X point register and places the
	 result in the X point register.
	 
	 Get Pt X:
	  This button allows the user to select a point on the screen 
         and places the X coordinate of the selected point in the X
	 point register.

	 Y :
           This button transfers the contents of the calculator 
	 register into the Y point register.

 	 Y :
           This button transfers the contents of the Y point 
	 register into the calculator register.

 	 Y +:
           This button transfers takes the value in the calculator
	 register adds it to the Y point register and places the
	 result in the Y point register.

 	 Y -:
           This button transfers takes the value in the calculator
	 register subtracts it from the Y point register and places the
	 result in the Y point register.
	 
	 Get Pt Y:
	  This button allows the user to select a point on the screen 
         and places the Y coordinate of the selected point in the Y
	 point register.

	 Z :
           This button transfers the contents of the calculator 
	 register into the Z point register.

 	 Z :
           This button transfers the contents of the Z point 
	 register into the calculator register.

 	 Z +:
           This button transfers takes the value in the calculator
	 register adds it to the Z point register and places the
	 result in the Z point register.

 	 Z -:
           This button transfers takes the value in the calculator
	 register subtracts it from the Z point register and places the
	 result in the Z point register.
	 
	 Get Pt Z:
	  This button allows the user to select a point on the screen 
         and places the Z coordinate of the selected point in the Z
	 point register.
	
	 Get Point:
	  This button allows the user to select a point on the screen
	and places all three coordinate values into the point register.

	The Return Point toggle at the bottom of the screen controls
	whether a point value is returned or a real number value. The
	toggle defaults to on so it will return a point value. To return
	a real value simply turn it off.