*.* Structures Unlimited *.*

                                   Presents

                                     D3RUN

           Copyright (C) 1991, Structures Unlimited, Brookfield, WI
                              All rights reserved





INTRODUCTION                                                           
============

     This limited version of D3RUN is offered to current and future users
of Finite  Element  Analysis,  free  of  charge.    The program has been
restricted to a maximum of 50 nodes for trial use and BBS distribution.         
To obtain the  full  3D  Frame Analysis program with over 6000 available
degrees of freedom, a  users manual, and future updates, simply complete
the registration form included.



HELPFUL HINTS
=============


1.  General
    All input must be unit consistant.


2.  Member Definition

    A.  Z reference node locates the XZ-plane of the element.
    B.  Pin codes:  enter one (1) to release the degree of freedom.  

             IPC1 - ABC
                    A - axial release        
                    B - Y rotation end one (1)
                    C - Z rotation end one (1)

             IPC2 - ABC
                    A - X rotation release (torsion)
                    B - Y rotation end two (2)
                    C - Z rotation end two (2)
                  
    C.  Rigid links are identified with a beam property of 99.
    D.  Rigid ended elements require an "A" and "B" dimension which are
        the length of the rigid section for end one (1) and end two (2),
        respectively.




 
3.  Restraints

    A.  The restraint code, numbers 1-6, are entered to selectively restrain 
        degrees of freedom.  
    B.  Rotational values for input are in radians.
        

4.  Load Input

    Nodal and gravity loads are input in the global coordinate system, while
member loads are input in the local (member) coordinate system.  


5.  Printing Output

    If  an  80 column printer  is  being  used,  set  your  printer  for
    condensed mode since the standard output is wider than 80 columns.
    

6.  Plotting

    When  plotting a sectional view, enter  the  node  number  and  axis
    reference to define the view direction.  For  example, a "2Z" would
    plot the members viewed from node 2 and looking in the Z direction.
    



        For further information and needed help please fax us at
                             1-414-784-7523.
                
                        !!!!!!  good luck !!!!!!
                





==============================================================================
[                           REGISTRATION FORM                                ]
[                                 D3RUN                                      ]
[                                                                            ]
[ Date:  ____/____/____                     TO:  Structures Unlimited        ]
[                                                P.O. Box 547                ]
[                                                Brookfield, WI 53008-0547   ]
[                                                                            ]
[  FROM:                                                                     ]
[        Name: __________________________________________________            ]
[                                                                            ]
[     Company:  _________________________________________________            ]
[                                                                            ]
[     Address: __________________________________________________            ]
[                                                                            ]
[        City: __________________________ State: ___ Zip: _______            ]
[                                                                            ]
[   Area Code: (______) Phone: __________________________________            ]
[                                                                            ]
[   Comments:  __________________________________________________            ]
[                                                                            ]
[              __________________________________________________            ]
[                                                                            ]
[              __________________________________________________            ]
[                                                                            ]
[                                                                            ]
[        ___ Enclosed is $350.00 for a single registration of D3RUN,         ]
[            and a users manual.                                             ]
[                                                                            ]
==============================================================================