=================================================================
                                           X
                                          X X
                                         X X X
                                        X  X  X
                                       X   X   X
                                      X    X    X
                                     X     X     X
                                    X      X      X
                                           X
                                           X
                                           X
                                           X
                                           X
                                           X
                                           X
                                           X
                                           X
                                           X
                                           X
                                           X
                                           X
                                           X
                                           X
                                          XXX
                                         XXXXX
                                        XXXXXXX

              THIS SHEET IS PROVIDED TO HELP YOU ALIGN YOUR PRINTER PAPER

                   ALIGN PAPER TO HAVE A SMALL MARGIN ABOVE THE TOP,

                     AND BELOW THE BOTTOM, ROW OF "=" CHARACTERS.

                                        XXXXXXX
                                         XXXXX
                                          XXX
                                           X
                                           X
                                           X
                                           X
                                           X
                                           X
                                           X
                                           X
                                           X
                                           X
                                           X
                                           X
                                           X
                                           X
                                           X
                                    X      X      X
                                     X     X     X
                                      X    X    X
                                       X   X   X
                                        X  X  X
                                         X X X
                                          XXX
                                           X
           =================================================================




    ==============  AUTORTTY - SAMPLE PROGRAM (AUTOSMPL.EXE)  ==============

         ======================= IMPORTANT NOTE =======================
    THIS PROGRAM DOES -NOT- SUPPORT INTELLIGENT TERMINALS SUCH AS THE PK-232

    ENCLOSED IS YOUR "AUTORTTY" SAMPLE PROGRAM (NAMED: "AUTOSMPL.EXE").  THE
    DOCUMENTATION  FILE  IS LOCATED IN THE SUB-DIRECTORY  CALLED,  DOC-FILE.
    THE  "SAMPLRTY.DOC"  FILE  CAN  BE PRINTED  USING  YOUR  MS-DOS  "PRINT"
    PROGRAM.   THE FIRST PAGE HAS TOP AND BOTTOM EQUAL SIGNS "=" TO HELP YOU
    ALIGN THE PAPER IN YOUR PRINTER.

    PLEASE  NOTE:
    A NUMBER OF FUNCTIONS HAVE BEEN DISABLED IN THE ENCLOSED SAMPLE PROGRAM.
    THE  RECEIVE  AND TRANSMIT BUFFERS ARE LIMITED TO 5K  EACH,  THE  NORMAL
    BUFFER  SIZE  IS  65,500 BYTE FOR EACH.  THE  INFO  SCREENS  WITHIN  THE
    PROGRAM HAVE NOT BEEN CHANGED, HENCE, IT WILL GIVE THE VALUE 65,500.

    YOU CAN -NOT- SAVE THE TRANSMIT BUFFER, WITHIN THE EDITOR, IN THE SAMPLE
    PROGRAM.  AUTO-PIX (THE "PIXBOX" MODULE) IS NOT INCLUDED IN THIS  SAMPLE
    VERSION.   AUTO-SAVE  (SENDING  RECEIVED TEXT TO  DISK)  HAS  ALSO  BEEN
    DISABLED.  YOU CAN SAVE THE "LIMITED" RECEIVE BUFFER TO DISK VIA F4 KEY.

    IMPORTANT MESSAGE:
    YOU CAN ACTUALLY RECEIVE AND TRANSMIT WITH THE ENCLOSED SAMPLE  PROGRAM,
    BE  AWARE THAT THE ENCODED CALLSIGN FOR "CWID" AND "OWNER  VERIFICATION"
    HAVE  THE  LETTERS "S-A-M-P-L-E" (WITHOUT THE HYPHENS) EMBEDDED  IN  THE
    PROGRAM.   WHAT THIS MEANS IS:  IF YOU PRESS CONTROL I TO SEND THE  CWID
    (OR  YOU ARE IN TRANSMIT MODE OVER 9 MINUTES), IT WILL SEND THE  LETTERS
    "S A M P L E".   IF  YOU TRANSMIT OVER  300  CHARACTERS AND  ATTEMPT  TO
    RETURN TO RECEIVE, IT WILL INFORM YOU TO SEND PROPER ID.  THE  ENCLOSED,
    SAMPLE,  PROGRAM  REQUIRES  YOU TO SEND THE LETTERS  "SAMPLE".   IN  THE
    ACTUAL  PROGRAM, YOU WOULD BE REQUIRED TO SEND, AT LEAST, YOUR  CALLSIGN
    BEFORE  YOU CAN EXIT TRANSMIT MODE (NORMALLY YOU WOULD SEND THE  STATION
    YOU'RE WORKING AND YOUR CALL IN THE ID) EITHER WAY, YOU COULD THEN ENTER
    THE <CTRL> E TO EXIT TRANSMIT MODE AND RETURN TO RECEIVE.

    REMEMBER,  THE  RECEIVE AND TRANSMIT (PIX) BUFFERS ARE LIMITED  TO  5000
    CHARACTERS IN THIS SAMPLE PROGRAM.

    IF  YOU ENCOUNTER SCREEN INTERFERENCE WHEN USING A "CGA" VIDEO  ADAPTER,
    YOU WILL HAVE TO USE THE /SNOW COMMAND LINE SWITCH WITH THE PROGRAM NAME
    WHEN  YOU  BRING-UP THE PROGRAM.  IF YOU HAVE A  MONOCHROME  (COMPOSITE)
    MONITOR  ON  YOUR  COLOR  VIDEO CARD, YOU WILL HAVE  TO  USE  THE  /COMP
    (COMPOSITE MONOCHROME)  COMMAND LINE SWITCH.  YOU CAN USE EITHER OR BOTH
    OF THESE SWITCHES IF NECESSARY.

    EXAMPLE:  AUTOSMPL /SNOW /COMP<RETURN>

    THE  ABOVE  EXAMPLE  INCLUDES  BOTH SWITCHES - USE  ONLY  THE  ONES  YOU
    ACTUALLY NEED.

    TO  PROPERLY  INSTALL  THE  PROGRAM  AND  SET  THE  PARAMETERS  IN   THE
    CONFIGURATION SCREENS, PRINT-OUT THE DOC FILE "SAMPLRTY.DOC" AND  FOLLOW
    THE INFORMATION UNDER INSTALLATION AND CONFIGURATION PAGES.  RS-232 PIN-
    OUT INFORMATION (THE PROGRAM USES) IS ALSO INCLUDED IN "SAMPLRTY.DOC".

    THE  OTHER PAGE, INCLUDED HERE, GIVES INFORMATION REGARDING  THE  SYSTEM
    REQUIREMENTS NECESSARY FOR RUNNING "AUTOSMPL.EXE" PROGRAM, AS WELL AS  A
    LIST OF MANY OF IT'S MAJOR FEATURES.

                  WALTER E. BESS, JR. (K8LC) -- PRECISION ELECTRONICS
                   1525 KARIN STREET -- IRONTON, OHIO   45638




    ** AUTORTTY/AUTO-PIX PROGRAM REQUIREMENTS AND ADDITIONAL INFORMATION **

    THIS PROGRAM DOES -NOT- SUPPORT INTELLIGENT TERMINALS SUCH AS THE PK-232

    REQUIREMENTS:  IBM OR COMPATIBLE COMPUTER - USING MS-DOS 2.1 OR HIGHER.
    FREE MEMORY REQUIRED TO RUN:  391K FOR AUTORTTY - 410K FOR AUTO-PIX
     === ABOVE REQUIREMENTS MAY CHANGE WITH LATER VERSIONS OF PROGRAM/S ===

    THIS  PROGRAM SUPPORTS MOST (BUT NOT ALL) OF THE POPULAR VIDEO  ADAPTERS
    USED  IN IBM, AND COMPATIBLE, COMPUTERS.  THE /SNOW COMMAND LINE  SWITCH
    IS PROVIDED TO HANDLE THE "SNOW" PROBLEM ENCOUNTERED WITH SOME CGA VIDEO
    ADAPTERS.  THE /COMP COMMAND LINE SWITCH MUST BE USED IF YOU ARE USING A
    COMPOSITE VIDEO MONITOR (MONOCHROME) ON YOUR COLOR VIDEO ADAPTER.

    SOME OF THE FEATURES OF AUTORTTY:
    * 45-75-110-135-300 BAUD - EITHER BAUDOT (5 LEVEL) OR ASCII (8/7 LEVEL)
    * FULL USER CONFIGURATION - WHICH IS SAVED TO DISK AND USED AT STARTUP.
    * RECEIVE BUFFER SIZE IS 65,500 BYTE - WHEN FULL WILL CONTAIN LAST 65.5K
    * ABILITY TO SAVE THE RECEIVE BUFFER TO DISK - AT ANY TIME.
    * AUTO-SAVE -ECHOES RECEIVED TEXT TO A DISKFILE, UP TO DISK CAPACITY.
    * PRINT ECHO - <CTRL> P - RECEIVE TEXT (AND XMIT PIX) ECHO TO PRINTER.
    * PROGRAM WILL -NOT- HANGUP IF PRINTER IS TAKEN OFF LINE FOR ANY REASON.
    * SUPPORTS PARALLEL PRINTERS:  LPT1-2-3 -AND- SERIAL PRINTERS:  COM1-2-3
    * USES A FULL 65,500 BYTE BUFFER TO:  LOAD - EDIT  AND TRANSMIT YOUR PIX
    * THE ABOVE BUFFER CAN ALSO BE LOADED FROM THE RECEIVE BUFFER (OR BLOCK)
    * THE "AUTOEDIT" MODULE, FOR EDITING THE XMIT (PIX) BUFFER, INCLUDES ALL
      THE FEATURES NECESSARY TO CREATE OR MAINTAIN YOUR PIX FILES.
    * THE ABILITY TO SEND PART (FILL) OF A PIX FROM THE XMIT (PIX) BUFFER.
    * LINE ONE WILL DISPLAY FILENAME LOADED IN BUFFER - AND FILL LINES SET.
    * 10 (1K BYTE) MESSAGE PORTS - 9 SAVABLE TO DISK - LOADED IN AT STARTUP.
    * ABILITY TO NEST MESSAGE PORT CALLS - MAKES IT EASY TO "BUILD" YOUR ID.
    * MESSAGE PORT #1 CAN BE MODIFIED WITHOUT ENTERING PORT EDIT MODE.
    * TERMINAL UNIT CAN USE EITHER COM1 OR COM2 SERIAL PORT.
    * 3000 BYTE TYPE AHEAD BUFFER - MUCH LARGER THAN ACTUALLY NEEDED.
    * TRANSMIT "BREAK" MODE - ALLOWS YOU TO ANSWER A QUERY WITHOUT  SENDING
      YOUR TYPE AHEAD BUFFER. (VERY HANDY)
    * VIEW BUFFERS MODE - TO ALLOW YOU TO QUICKLY LOOK THROUGH THE BUFFERS
    * BLOCK MODE - ALLOWS YOU TO "MARK" A BLOCK TO RESEND, SAVE OR DELETE IT
    * HELP SCREENS AVAILABLE FOR MOST MODES - GIVES BRIEF DESCRIPTIONS.
    * AUTOMATIC CW-ID - EVERY 9 MINUTES - OR CAN BE SENT WITH <CTRL> I.
    * DISPLAY A DISK DIRECTORY FROM WITHIN PROGRAM (USES YOUR PATH INPUT).
      YOU  WILL  STILL HAVE 6 LINES OF RECEIVE TEXT TO VIEW.  YOU  CAN  ALSO
      SELECT:   LOAD XMIT (PIX) BUFFER MODE -AND- DELETE A FILE  MODE  WHILE
      YOU VIEW THE DIRECTORY.
    * INPUT OF A SEPARATE PATH FOR EACH PROGRAM MODE (USING CONFIGURATION)
      YOU CAN ALWAYS CHANGE THE DEFAULT PATH WHEN NECESSARY.
    * ABILITY TO CLEAR:  TYPE AHEAD, RECEIVE AND XMIT (PIX) BUFFERS.
    * DELETE A DISKFILE FROM WITHIN THE PROGRAM.
    * PRINT MODE WHICH ALLOWS PRINTING FROM EITHER THE RECEIVE OR XMIT (PIX)
      BUFFERS.   YOU CAN PRINT ALL OR PART (FILL) OF EITHER BUFFER AND  HAVE
      THE OPTION TO "AUTO LINEFEED" WHICH WILL SPREAD OUT OVERLINES IN A PIX
    * AUTO-PIX  VERSION  OF AUTORTTY - THE  AUTO-PIX  MODE IS  A  COMPLETELY
      AUTOMATIC "PIXBOX" MODULE WITHIN  "AUTORTTY".  IT ALLOWS OTHERS (AFTER
      GIVING  YOUR  SYSTEM  CALLUP)  TO LOG ON YOUR  SYSTEM,  GET  DISK  AND
      PIXFILE  NUMBERS, READ YOUR PIX FILES, GET PART  (FILL) OF  A  PIXFILE
      (AFTER  GIVING   START  AND END LINE NUMBERS), LEAVE  (SAVE)  A  SHORT
      MESSAGE FOR YOU  -AND-  OTHER FUNCTIONS RELATED TO RTTY PIX GATHERING.
    * "AUTORTTY" ALWAYS SENDS THE PROPER END-OF-LINE SEQUENCE FOR RTTY PIX.
    * SEVERAL SPECIAL PIX FILE MAINTENANCE PROGRAMS INCLUDED WITH EACH PROG.

              WALTER E. BESS, JR. (K8LC) -- PRECISION ELECTRONICS
                   1525 KARIN STREET -- IRONTON, OHIO   45638





       ============== AUTORTTY/AUTO-PIX VERSION OF PROGRAM ==============

    THE  ENCLOSED  SAMPLE PROGRAM IS OF THE BASIC "AUTORTTY"  RTTY  PROGRAM,
    ALTHOUGH WRITTEN FROM THE GROUND UP FOR USE WITH RTTY (PIX) PICTURES, IT
    CONTAINS ABOUT ANY FUNCTION NECESSARY FOR YOUR AMATEUR RADIO,  STANDARD,
    RTTY COMMUNICATION NEEDS.  NOTE: THIS ISN'T A CONTEST PROGRAM.

    AS  MENTIONED  ON THE LAST PAGE, AUTORTTY/AUTO-PIX IS  A  "PIXBOX"  TYPE
    PROGRAM.  WHICH MEANS IT IS SIMILAR TO A "MAILBOX" PROGRAM (IN THAT  YOU
    LOG  ON AND SEND IT COMMANDS) BUT CAN'T BE DIRECTLY USED AS  A  MAILBOX.
    ALTHOUGH  IT DOES HAVE THE ABILITY TO HAVE SOMEONE SEND YOU  A  MESSAGE,
    AND  SAVE IT TO DISK, THERE ARE NO FUNCTIONS TO SEARCH FOR "MAIL".   THE
    MESSAGE SAVE, IN THIS PROGRAM, IS ONLY THERE SO YOUR "PIXBOX" USERS  CAN
    LEAVE YOU A MESSAGE.

    ONCE  CALLED  UP, BY SENDING THE REQUIRED CALL-UP CODE, A USER  WILL  BE
    PROMPTED TO GIVE THEIR CALLSIGN THREE TIMES, SEPARATE EACH WITH A  SPACE,
    AND  IF  EVERYTHING GOES OKAY, THEY WILL ENTER "AUTO-PIX"  MODE.   AFTER
    GETTING  LOGGED  ON,  THE USER CAN GIVE VARIOUS  COMMANDS  WHICH  ALLOWS
    HIM/HER TO RECEIVE PIX SENT FROM THE PIXFILE DISK DRIVE AS GIVEN IN  THE
    PROGRAM CONFIGURATION.

    THE  FULL  AUTORTTY/AUTO-PIX PROGRAM IS REALLY DESIGNED FOR  THOSE  THAT
    HAVE SIZABLE RTTY PIX LIBRARIES AND PLAN ON HAVING A SYSTEM THAT  OTHERS
    CAN  ACCESS AND RECEIVE PIX FROM THEIR PIX LIBRARY.  THIS  PROGRAM  ALSO
    ALLOWS USERS TO ISSUE A "//FILL" COMMAND AND RECEIVE PART OF A PIX FILE.
    THE USER ENTERS BOTH THE START AND END LINE NUMBERS FOR THE FILL.  THERE
    ARE MANY COMMANDS WITHIN AUTO-PIX, ALL DESIGNED WITH THE USER'S EASE  OF
    USE IN MIND.

    ========================================================================

        THE  "AUTORTTY/AUTO-PIX"  PROGRAMS  ARE NOW READY FOR SHIPMENT.

    THE  INTRODUCTORY PRICE OF "AUTORTTY" AND  "AUTORTTY/AUTO-PIX"  PROGRAMS
    WILL BE AS FOLLOWS (NOTE: THE PRICES ARE IN U.S FUNDS):

       AUTORTTY (COMPLETE RTTY WITHOUT AUTO-PIX "PIXBOX" MODULE) - $ 65.00
       AUTORTTY/AUTO-PIX (COMPLETE RTTY WITH "PIXBOX" PROG) ------ $125.00
         YOU MUST INCLUDE PRIORITY MAIL POSTAGE FOR THE ABOVE PROGRAMS

    POSTAGE PAYMENT REQUIRED:

    U.S.:
       AUTORTTY AND AUTO-PIX PROGRAMS ----------------------------- $ 3.50

    CANADA:
       AUTORTTY AND AUTO-PIX PROGRAMS ----------------------------- $ 4.00

    TO AVOID THE TWO TO THREE WEEK "PERSONAL CHECK" DELAY, IN SHIPPING  YOUR
    PROGRAM, SEND YOUR ORDER WITH FUNDS BY CASHIER'S CHECK OR MONEY ORDER.

    U.S. ORDERS:
    THE  U.S.  POSTAL  SERVICE OFFERS A "COD" OPTION, BUT IT HAS  A  FEE  OF
    $4.00,  THIS  IS  IN  ADDITION TO THE NORMAL  POSTAGE  FOR  SENDING  THE
    PROGRAM. THE POSTAL SERVICE ALSO CHANGES YOU FOR A MONEY ORDER FOR  YOUR
    RETURN.  I FEEL THIS IS JUST TOO HIGH AND WOULD PREFER NOT TO USE IT









           TO ORDER EITHER OF THE PROGRAMS, USE THE ORDER FORM BELOW.

    ------------------------------ CUT HERE --------------------------------

                             PRECISION ELECTRONICS
                        1525 KARIN STREET - P.O. BOX 764
                          IRONTON, OHIO   45638   USA
                             PHONE: 1-614-532-6111
    ========================================================================


    FULL NAME:
    ------------------------------------------------------------------------

    AMATEUR CALL:                                 DATE:
    ------------------------------------------------------------------------

    ADDRESS:
    ------------------------------------------------------------------------
    ADDITIONAL ADDRESS
    (IF NECESSARY):
    ------------------------------------------------------------------------

    CITY, STATE, ZIP:
    ------------------------------------------------------------------------

               =====  THE AMOUNTS BELOW ARE IN U.S. FUNDS  =====
      ===== NON U.S AMATEURS - MAKE APPROPIATE MONETARY CONVERSION =====

    MARK DISK SIZE YOU PREFER FOR PROGRAM DISK(S).

    ____ 5 1/4 360K  ____ 5 1/4 1.2M(HD)  ____ 3 1/2 720K  ____ 3 1/2 1.44M

    - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - 

    _____ AUTORTTY (BASIC RTTY PROGRAM WITHOUT AUTO-PIX) --- $______________

    ----- AUTORTTY/AUTO-PIX (FULL RTTY AND PIXBOX PROG.) --- $______________

    OHIO RESIDENTS -MUST- INCLUDE 6% SALES TAX ON ORDER ---- $_____________

    YOU -MUST- INCLUDE SHIPPING WITH YOUR ORDER.
    U.S. RATE: $ 3.50 PER PROGRAM
    CANADIAN RATE: 4.00 PER PROGRAM       POSTAGE INCLUDED:  $_____________


                                          TOTAL ENCLOSED:    $______________

                   AVOID THE 2 TO 3 WEEK PERSONAL CHECK DELAY
                      SEND CASHIER'S CHECK OR MONEY ORDER

    SORRY, NO COD'S AT PRESENT - U.S. POSTAL SERVICE COD JUST TO HIGH TO USE

    SEND YOUR REMITTANCE TO:
                               WALTER E. BESS, JR.  K8LC
                               PRECISION ELECTRONICS
                               1525 KARIN STREET - P.O. BOX 764
                               IRONTON, OHIO   45638   USA


    ------------------------------ CUT HERE --------------------------------































                SAMPLE PROGRAM OF "AUTORTTY" - RTTY PIX PROGRAM BY K8LC

           A NUMBER OF FUNCTIONS, OF THE FULL PROGRAM, HAVE BEEN DISABLED IN
                          THIS SAMPLE VERSION "AUTOSMPL.EXE"

           THE  FOLLOWING  MANUAL  IS  THE  COMPLETE  MANUAL  PROVIDED  WITH
                                      "AUTORTTY"

           THE MANUAL FOR THE "AUTO-PIX", AUTOMATED "PIXBOX" MODULE, HAS NOT
                          BEEN PROVIDED IN THIS DOCUMENTATION






























                        ==============  CONTENTS ==============

           INTRODUCTION ------------------------------------- SEC 1  P --- 1

           SERIAL PORT INFORMATION -------------------------- SEC 1  P --- 2

           PROGRAM INSTALLATION ----------------------------- SEC 1  P --- 3

           PROGRAM CONFIGURATION ---------------------------- SEC 1  P - 4-6

           CREATING AND EDITING MESSAGE PORTS --------------- SEC 1  P --- 7

           "FUNNY" CHARACTERS IN COL 80 --------------------- SEC 1  P --- 8

           RECEIVE MODE (INFO) ------------------------------ SEC 1  P --- 9

           TYPE AHEAD BUFFER USE ---------------------------- SEC 1  P --- 8

           "BREAK" TRANSMIT MODE OPERATION ------------------ SEC 1  P --- 8
                                                              SEC 2  P --- 1

           AUTO-SAVE (RECV TEXT TO DISK) MODE --------------- SEC 1  P -- 11

           BLOCK MODE OPERATION ----------------------------- SEC 1  P -- 11
                                                KEYS  ------- SEC 2  P - 6-7

           PRINT MODE USE ----------------------------------- SEC 1  P -- 12
           (TO HAVE INCOMING TEXT ECHO TO PRINTER - SEE PRINT ECHO PAGE III)

           RTTY BAUD RATE AND MODE (IN BAUD INSTEAD OF WPM) - SEC 1  P -- 12
                                                              SEC 2  P --- 5

           TOGGLING BETWEEN BAUDOT AND ASCII MODE ----------- SEC 1  P -- 12
                                                              SEC 2  P --- 5

           DATE/TIME INPUT FOR XMIT FROM TYPE AHEAD --------- SEC 1  P -- 12
                                                              SEC 2  P --- 6

           SENDING FILES ENTERED IN THE TYPE AHEAD BUFFER --- SEC 1  P -- 13
                              (BEST EXPLAINED IN SECTION 2)   SEC 2  P - 5-6

           LOADING AND SENDING THE PIX XMIT BUFFER ---------- SEC 1  P -- 13
                                                              SEC 2  P --- 2

           EDITING TRANSMIT (PIX) BUFFER -------------------- SEC 1  P 14-17

           PREPARING AND SENDING PART (FILL) OF A PIX FILE -- SEC 1  P -- 13
                                                              SEC 2  P --- 3

           USING "SHELL" MODE (TEMPORARY PRG EXIT TO "DOS") - SEC 1  P -- 12
                                                              SEC 2  P --- 4

           EXIT THE AUTORTTY PROGRAM ------------------------ SEC 1  P -- 13
                                                              SEC 2  P --- 5

           CORRECTING A MESSED UP SCREEN (SEC-1 P-9) -------- SEC 1  P --- 9
                       <ALT> F1 - SCREEN REDRAW)              SEC 2  P --- 1

           AUTO-PIX MODE - ALL INFO FOR THIS MODE IS IN SECTION 3 OF MANUALS
                           (SECTION 3 HAS ITS OWN CONTENTS)
                                          (I)





               ====== LIST OF FUNCTIONS AND THEIR KEY ASSIGNMENTS ======

           =================================================================
           FUNCTION --------------------- ASSIGNED KEY/S ---- LOCATION -----
           =================================================================

           HELP/INFO ------------------------- F1 ----------- SEC 2  P --- 1

           BREAK XMIT MODE -------------- <SHIFT> F1 -------- SEC 1  P --- 8
                                                              SEC 2  P --- 1

           PROGRAM CONFIGURATION -------- <CTRL> F1 --------- SEC 1  P --- 4
                                                              SEC 2  P --- 1

           REDRAW RECEIVE SCREEN -------- <ALT> F1 ---------- SEC 1  P --- 9
              (READ NOTES IN SEC 1 PAGE 9 ABOUT REDRAW)       SEC 2  P --- 1

           FORCE LETTERS IN BAUDOT RECV ---- F2 / <CTRL> R -- SEC 2  P - 1-2

           BREAK (IMMEDIATE) FROM XMIT TO RECV - F2/<CTRL>R - SEC 2  P - 1-2

           TYPE AHEAD TRANSMIT MODE ------ <SFT> F2/<CTL> T - SEC 1  P --- 8
                                                              SEC 2  P --- 2

           LOAD XMIT (PIX) BUFFER -------------- F3 --------- SEC 1  P -- 13
                                                              SEC 2  P --- 2

           SENDING PIX FROM LOADED BUFFER ----- <SHIFT> F3 -- SEC 1  P -- 13
                                                              SEC 2  P --- 2

           EDITING THE TRANSMIT (PIX) BUFFER --- <CTRL> F3 -- SEC 1  P 14-17
            ("AUTOEDIT" MODULE)                               SEC 2  P --- 2

           SENDING PIX ENTERED IN TYPE AHEAD ---- <CTRL> F -- SEC 1  P -- 12
                                                              SEC 2  P - 4-5

           FILL (PART PIX) LINE ENTRY ------------ F7 ------- SEC 1  P -- 13
                                                              SEC 2  P --- 3

           SENDING FILL ---------------------- <SHIFT> F7 --- SEC 1  P -- 13
                                                              SEC 2  P --- 3

           SAVING RECEIVE BUFFER TO DISK ---------- F4 ------ SEC 1  P --- 9
                                                              SEC 2  P --- 2

           CREATING AND EDITING MESSAGE PORTS - F5 (THEN "M") SEC 1  P --- 7
                                                              SEC 2  P - 2-3

           NESTING MESSAGE PORTS ------------ <ALT> 1 - 0 --- SEC 1  P --- 7
                                                              SEC 2  P --- 8

           DISPLAY OF DISK DIRECTORY ------- F5 (THEN "D") -- SEC 1  P -- 10

           EDIT/VIEW INFORMATION ------------------ F5 ------ SEC 1  P -- 10
                                                              SEC 2  P --- 2

           BLOCK MODE (MARKING AND OPTIONS) ------- F8 ------ SEC 1  P -- 11
                                                              SEC 2  P --- 3

                               (CONTINUED ON NEXT PAGE)
                                         (II)





           ===== LIST OF FUNCTIONS AND THEIR KEY ASSIGNMENTS (CONT.) ======

           =================================================================
           FUNCTION --------------------- ASSIGNED KEY/S ---- LOCATION -----
           =================================================================

           PRINTING MODE (NOT PRINT ECHO) --------- F9 ------ SEC 1  P -- 12
                                                              SEC 2  P --- 3

           PRINT ECHO (RX ALSO GOING TO PRN) ---- <CTRL> P -- SEC 1  P --- 9
                                                              SEC 2  P --- 5

           AUTO-SAVE (RX ALSO GOING TO DISK) ---- <CTRL> F9 - SEC 1  P -- 11
                                                              SEC 2  P --- 3

           CLOSING AUTO-SAVE --------------------- <ALT> F9 - SEC 1  P -- 11
                                                              SEC 2  P --- 4

           AUTO-PIX (AUTO-PIX VER. PROGRAM) ------- F10 ----- SEC 2  P --- 4
           (AUTO-PIX INFO IN SECTION 3 - HAS ITS OWN CONTENTS)SEC 3  ( ALL )

           AUTO-PIX (PRINT LOGFILE) (A-P ONLY) - <SHIFT> F10 -SEC 2  P --- 4
           (AUTO-PIX INFO IN SECTION 3 - HAS ITS OWN CONTENTS)SEC 3  ( ALL )

           EXIT PROGRAM (TEMPORARY) TO DOS ------ <ALT> F10 - SEC 1  P -- 12
                                                              SEC 2  P --- 4

           EXIT PROGRAM (FINAL) --------- <CTRL> O-<CTRL> U - SEC 1  P -- 13
                                                              SEC 2  P --- 5

           BAUD RATE (CHANGE) ------------------ <CTRL> B --- SEC 1  P -- 12
                                                              SEC 2  P --- 5

           RTTY MODE (CHANGE BAUDOT-ASCII) ----- <CTRL> V --- SEC 1  P -- 12
                                                              SEC 2  P --- 5

           ASCII (TOGGLE 8 BIT/7 BIT) ---------- <CTRL> A --- SEC 1  P -- 12
                                                              SEC 2  P --- 5

           PIX SENDING FROM TYPE AHEAD ENTRY --- <CTRL> F --- SEC 1  P -- 13
                               (BEST EXPLAINED IN SECTION 2)  SEC 2  P - 5-6

           "BELL" CHARACTER (SENDING) ---------- <CTRL> G --- SEC 2  P --- 6

           DATE/TIME (SENDING) ----------------- <CTRL> D --- SEC 2  P --- 6

           CWID (SENDING) ---------------------- <CTRL> I --- SEC 2  P --- 6

           CLEAR A LINE FROM TYPE AHEAD OR MSG - <CTRL> Y --- SEC 2  P --- 6

           MARKING THE END OF YOUR TYPE ENTRY -- <CTRL> E --- SEC 1  P --- 8
           (USE THIS AT THE VERY END OF YOUR CURRENT XMISSION)SEC 2  P --- 6

           ADDING A CALL TO MESSAGE PORT #1 ----- <ALT> A --- SEC 1  P --- 7
                                                              SEC 2  P --- 7

           REMOVING A CALL FROM MESSAGE PORT #1 - <ALT> R --- SEC 1  P --- 7
                                                              SEC 2  P --- 7

                               (CONTINUED ON NEXT PAGE)
                                         (III)





           ===== LIST OF FUNCTIONS AND THEIR KEY ASSIGNMENTS (CONT.) ======

           =================================================================
           FUNCTION --------------------- ASSIGNED KEY/S ---- LOCATION -----
           =================================================================

           CLEARING ALL CALLS FROM MSG PORT #1 --- <ALT> C -- SEC 1  P --- 7
                                                              SEC 2  P --- 7

           ==================================================================
           KEYS USED IN  "AUTOEDIT" ARE GIVEN ON PAGES 14 - 17 OF THIS MANUAL
           ==================================================================



           = THE FOLLOWING ARE KEYS USED WITHIN EDIT/VIEW AND BLOCK MODES =

           ^Q/HOME - ^Z/END - ^W/PAGEUP - ^X/PAGEDOWN ------- SEC 2  P - 6-7


            ======== THE FOLLOWING ARE KEYS USED WITHIN BLOCK MODE ========

           <CTRL> B - <CTRL> E - ALL <ARROW KEYS> ----------- SEC 2  P - 6-7





































                                      (IV)






























                                   AUTORTTY/AUTO-PIX

                                  INFORMATION  MANUAL

                                       SECTION 1




































            ============= INTRODUCTION TO AUTORTTY/AUTO-PIX ==============

           THIS  PROGRAM  WAS DEVELOPED, FROM THE GROUND UP,  FOR  RTTY  PIX
           ENTHUSIASTS.   MOST  PROGRAMS  WRITTEN IN THE  PAST  HAVE  EITHER
           IGNORED RTTY PIX ALTOGETHER, OR HAVE ONLY COVERED PART, OF  MANY,
           SPECIAL  DEMANDS  RTTY PIX SENDING, AND RECEIVING,  IMPOSE  ON  A
           PROGRAM.  AUTORTTY HANDLES THE SPECIAL NEEDS FOR OVERLINED PIX  -
           AND  THE  ABILITY TO "EXPLODE" THOSE LINES IN  A  PRINTOUT.   THE
           PROGRAM WILL NOT "HANG-UP" IF YOUR PRINTER RUNS OUT OF PAPER, YOU
           TAKE  IT  OFF LINE OR ANY ERROR CONDITION THAT MAY  OCCUR.   THIS
           PROGRAM NOT ONLY TAKES OUT ANY EXTRA CARRIAGE RETURNS SENT WITH A
           SINGLE LINEFEED, IT REMOVES ALL UNNECESSARY CARRIAGE RETURNS.  IF
           YOU  RECEIVE 10 CR/LF PAIRS - THIS PROGRAM WILL STORE ONE CR  AND
           10  LFS.  YOU DO HAVE THE AN OPTION WHICH WILL RETAIN  CR'S  SENT
           WITH  MULITPLE CR/LF PAIRS, IF THEY ARE TRANSMITTED.   WHEN  THIS
           PROGRAM  SENDS  A  PIX FILE - IT ALWAYS  SENDS  A  THREE  CONTROL
           CHARACTER  END-OF-LINE  SEQUENCE.   ON  A  FULL  "NEW-LINE"  THIS
           PROGRAM SENDS (1) CR/LF PAIR - THEN THE CONTROL CHARACTER OF  THE
           FIRST  PRINTABLE CHARACTER IN THE LINE (A LTRS FOR A  <SPACE>  OR
           OTHER "LETTER" CHARACTER  - A FIGS FOR A "FIGURE" CHARACTER).  ON
           AN  OVERLINE,  THIS PROGRAM SENDS TWO CARRIAGE  RETURNS  AND  THE
           CONTROL  CHARACTER OF THE FIRST PRINTABLE CHARACTER IN THE  LINE,
           AS  MENTIONED ABOVE.  THIS WILL KEEP THE OLD MECHANICAL  MACHINES
           FROM STAYING IN FIGS, IF THEY GET OUT OF STEP WITH THE PIX  BEING
           SENT,  WHICH CONTAIN  ONLY "LETTERS" CHARACTERS.  IF YOU  DO  GET
           OUT OF STEP, IT WILL ONLY BE FOR THE REMAINDER OF THAT LINE.

           TRANSMIT (PIX) BUFFER EDITING IS ALSO AVAILABLE IN BOTH  AUTORTTY
           AND THE AUTORTTY/AUTO-PIX COMBO PROGRAMS.  THE "AUTOEDIT"  MODULE
           CONTAINS  ALL OF THE FUNTIONS NECESSARY FOR EDITING AND  CREATING
           RTTY PIX - OR ANYTHING ELSE THAT REQUIRES AN ASCII TEXT EDITOR.

           THIS  PROGRAM IS NOT ONLY A FINE PROGRAM FOR RTTY PIX - IT  IS  A
           VERY NICE PROGRAM TO USE FOR GENERAL RAG-CHEWING QSO'S.  AUTORTTY
           CONTAINS  MOST OF THE MAJOR FEATURES OF OTHER RTTY  PROGRAMS  AND
           MANY THE OTHERS DON'T.  THERE ARE FUNCTIONS THIS PROGRAM  DOESN'T
           INCLUDE SUCH AS CW AND COMMANDS FOR A "SMART" INTERFACE (TU), BUT
           FOR THE AVID PIX LOVER THIS PROGRAM SHOULD FILL MANY VOIDS OTHERS
           LEAVE.   THERE ARE MANY OTHER FEATURES AVAILABLE  WITH  AUTORTTY,
           THOSE ARE BEST LEARNED BY ACTUALLY USING THE PROGRAM AND  READING
           ABOUT THEM IN THE REST OF THIS MANUAL.

           IF YOU PURCHASED THE FULL AUTORTTY/AUTO-PIX PROGRAM, YOU HAVE THE
           FINEST AUTOMATED "PIXBOX" PROGRAM AVAILABLE TODAY - BAR NONE...

           PLEASE NOTE:
           YOU DO NOT HAVE TO REGISTER YOUR NEW AUTORTTY (OR  AUTORTTY/AUTO-
           PIX  COMBO) PROGRAM.  I HAVE RETAINED ALL  INFORMATION  REGARDING
           YOUR NAME, AMATEUR CALL, FULL ADDRESS, VERSION NUMBER AND DATE OF
           YOUR PROGRAM.

                                          HAPPY PIX'N

                                          WALTER E. BESS, JR.,  K8LC
                                          PRECISION ELECTRONICS
                                          1525 KARIN STREET - P.O BOX 764
                                          IRONTON, OHIO   45638
                                          PHONE: 1-614-532-6111


                                       1





            ========= INTERFACE (SERIAL) PORT INFO FOR AUTORTTY ==========

           THIS   PROGRAM   SUPPORTS  EITHER  COM1 OR COM2 AS   THE   SERIAL
           PORT  FOR CONNECTION TO YOUR INTERFACE (TU).  (DEFAULT IS COM2)

           IMPORTANT NOTE:  THIS PROGRAM DOES -NOT- SUPPORT SPECIAL COMMANDS
           REQUIRED  BY MOST "SMART" TERMINALS.  UNLESS  YOUR  "INTELLIGENT"
           TERMINAL  UNIT  HAS  A  WAY  TO  PASS  DATA  BOTH  WAYS,  WITHOUT
           MODIFICATION,  AND  YOU CAN USE THE THE RS-232  LINES  AS  LISTED
           BELOW, THIS PROGRAM MAY GIVE UNSATISFACTORY RESULTS.

           PINOUTS FOR YOUR RS-232 ARE AS FOLLOWS:
                                                 DB-9 PLUG       DB-25 PLUG
           INPUT FROM RECEIVER -------------------    2    -------     3
           OUTPUT TO TRANSMITTER -----------------    3    -------     2
           SIGNAL GROUND -------------------------    5    -------     7
           PTT (PUSH TO TALK LINE) ---------------    7    -------     4
           CWID LINE -----------------------------    4    -------    20

           IF  YOU  ENCOUNTER PROBLEMS OF SIGNALS BEING  REVERSED  (SUCH  AS
           HAVING   THE XMITTER  KEYED WHEN THE PROGRAM IS SHOWING  RECEIVE)
           YOU  CAN   INVERT   THE SIGNAL  VOLTAGE BY ADDING  EITHER  AN  IC
           INVERTER OR A  SIMPLE  TRANSISTOR CIRCUIT.  IF YOU HAVE  PROBLEMS
           ALONG  THESE LINES - CONTACT ME -  I  HAVE SEVERAL  CIRCUITS  YOU
           MAY BE ABLE TO USE.  IF YOU ARE USING  A  COMPUTER WITH 2  SERIAL
           PORTS  THAT  USE THE DB-25 PIN CONNECTOR, YOU  MAY  EXPERIENCE  A
           PROBLEM OF THE INPUT AND OUTPUT LINES BEING REVERSED.  THEY   USE
           TWO  FORMATS   FOR  THIS PLUG (MAY ALSO EXIST WITH THE  9  PIN  -
           ALTHOUGH  I   HAVE  NOT ENCOUNTERED IT), THEY  USUALLY  HAVE  ONE
           FEMALE  AND  ONE MALE CONNECTOR FOR THEM.  THE  TWO  FORMATS  ARE
           "DCE"  (DATA COMMUNICATIONS EQUIPMENT) AND "DTE"  (DATA  TERMINAL
           EQUIPMENT).   THE  ONLY SOLUTION HERE IS TO OPEN YOUR  CABLE  (OR
           CONNECTOR) AND ACTUALLY SWITCH THE WIRES ON PINS 2 AND 3.

           IF YOUR TERMINAL UNIT DOES NOT SUPPORT "CW ID" YOU WILL  PROBABLY
           HAVE TO BUILD A SMALL (SIMPLE) CIRCUIT TO HAVE THE CWID LINE  KEY
           YOUR  SPACE TONE, OR SPACE SHIFT (IF YOU ARE USING FSK).   I  CAN
           SUPPLY  YOU  WITH SEVERAL CIRCUITS THAT SHOULD TAKE CARE  OF  THE
           PROBLEM, IF NECESSARY.





















                                       2





                      ============== INSTALLATION ==============

           FIRST,   MAKE  A  BACKUP COPY OF THE ORIGINAL PROGRAM  DISK   AND
           PUT  THE ORIGINAL IN A SAFE PLACE.  FOLLOW INSTRUCTIONS GIVEN  IN
           THE "DOS" MANUAL REGARDING YOUR COPY -OR- DISKCOPY COMMANDS.

           IMPORTANT NOTE:  IF YOU ARE USING A COMPOSITE VIDEO  (MONOCHROME)
           MONITOR  ON  YOU COLOR VIDEO ADAPTER, YOU -MUST- USE  THE   /COMP
           COMMAND  LINE  SWITCH WHEN YOU WANT TO BRING UP  AUTORTTY.   THIS
           WILL  ENABLE  THE  PROGRAM  TO SELECT  THE  PROPER  VIDEO  MEMORY
           ATTRIBUTES  FOR  A MONOCHROME MONITOR AND STILL USE  THE  "COLOR"
           VIDEO MEMORY AREA.  THIS SWITCH WILL BE IN ADDITION TO THE  /SNOW
           SWITCH (EXPLAINED BELOW).  IF YOU ONLY NEED THE COMPOSITE  SWITCH
           YOUR  COMMAND LINE IS:  AUTORTTY /COMP<RETURN>.  IF  YOU  REQUIRE
           BOTH:  AUTORTTY /SNOW /COMP<RETURN>.  THE SWITCHES NEED NOT BE IN
           THIS ORDER.

           TO   INSTALL,  JUST  COPY  THE  "AUTORTTY.EXE"  FILE   INTO   THE
           SUBDIRECTORY  YOU WANT  TO  RUN THE PROGRAM FROM.  THEN (WHEN  IN
           THE   AUTORTTY   DIRECTORY) ENTER:  AUTORTTY<RETURN>,  THIS  WILL
           BRING-UP YOUR NEW AUTORTTY  PROGRAM.  AUTORTTY COMES UP WITH CAPS
           LOCK = ON, YOU DON'T HAVE TO USE A UTILITY FOR THAT PURPOSE.  THE
           FIRST  TIME THE PROGRAM IS "BOOTED" IT CREATES TWO  DISKFILES  IN
           YOUR DEFAULT DIRECTORY PATH (THE PATH YOU SHOULD HAVE THE PROGRAM
           IN),  ONE  IS CALLED  "RTYCONFG.DAT"  AND THE  SECOND  IS  CALLED
           "MSG-PORTS.DAT".   THE  FIRST   FILE WILL  CONTAIN  A  NUMBER  OF
           DEFAULTS  FOR THE  PROGRAM  OPTIONS, THE  SECOND HAS ALL  OF  THE
           INFO FOR YOUR 9 (USER  CONFIGURABLE) MESSAGE PORTS.

           IF YOU HAVE AN EARLY CGA VIDEO ADAPTER AND ARE EXPERIENCING SNOW,
           OR OTHER INTERFERENCE, ON YOUR MONITOR - YOU WILL HAVE TO USE THE
           /SNOW   COMMAND LINE SWITCH WHENEVER YOU BRING-UP AUTORTTY.   USE
           THE  FOLLOWING,  IF  THE /SNOW  SWITCH  IS  NECESSARY:   AUTORTTY
           /SNOW<RETURN>.  SEE ABOVE REGARDING A COMPOSITE VIDEO MONITOR (IF
           IT APPLIES TO YOU).

           NOTE:  YOU  DO  NOT  HAVE  TO  REGISTER  YOUR  NEW  AUTORTTY   OR
           AUTORTTY/AUTO-PIX  PROGRAM.   I HAVE ALREADY FILED  ALL  OF  YOUR
           PROGRAM  INFORMATION, AS WELL AS YOUR NAME, FULL ADDRESS AND  HAM
           CALL.   IF  YOU  CHANGE YOUR AMATEUR CALL - I  WILL  UPDATE  YOUR
           PROGRAM  AT NO CHARGE (IF YOU HAVE THE CURRENT VERSION).  IF  YOU
           HAVE  A PREVIOUS VERSION, YOU WILL BE CHARGED THE  UPDATE  CHARGE
           AND RECEIVE THE LATEST VERSION WITH YOUR NEW CALL SIGN IN IT.

















                                       3





                      ============== CONFIGURATION ==============

           PRESS,   AND   HOLD,  THE  <CTRL> KEY  WHILE  YOU  PRESS  THE  F1
           FUNCTION   KEY,  THIS BRINGS UP THE FIRST OF  FIVE  CONFIGURATION
           SCREENS.

           NOTE: CONFIGURATION SCREENS #4 AND #5 ARE FOR USE WITH "AUTO-PIX"
           MODULE ONLY.  IF YOU PURCHASED THE BASIC "AUTORTTY" PROGRAM,  YOU
           DO NOT GIVE INPUT ON SCREENS 4 AND 5.

           YOU SHOULD RUN THROUGH ALL OF THE CONFIGURATION THAT PERTAINS  TO
           YOUR  PREFERENCE  AND HARDWARE.  YOU SHOULD GO THROUGH  ALL  FIVE
           SCREENS (USING PAGEUP OR PAGEDOWN) AND SELECT THE THE OPTIONS YOU
           WANT FROM  THE "TOGGLE"  OPTIONS ON THE FIRST TWO SCREENS.  INPUT
           YOUR   PREFERENCE  FOR THE VARIOUS "PATH" OPTIONS, ON  SCREENS  3
           AND  4.   SCREEN 5 HAS TWO INPUTS FOR  OPTIONAL  MESSAGES  TO  BE
           SENT  DURING WELCOME AND EXIT  ROUTINES  IN AUTO-PIX  MODE.    IF
           YOU DON'T WANT TO USE A MESSAGE,  JUST  LEAVE  THEM BLANK.

           THE FOLLOWING IS A LIST OF CONFIGURATION OPTIONS.

           1.   BAUD RATE USED FOR PROGRAM  STARTUP - SELECT THE  BAUD  RATE
           THAT  YOU WANT THE PROGRAM TO USE WHEN FIRST "BOOTED".

           2.   MODE USED FOR PROGRAM STARTUP - SELECT THE RTTY MODE  TO  BE
           USED WITH ABOVE BAUD RATE AT STARTUP.

           3.   YOUR TIME ZONE - SELECT THE TIME ZONE YOU LIVE IN,  THIS  IS
           USED   FOR SENDING  DATE/TIME  IN TYPE TRANSMIT AND WITH THE  LOG
           ON/OFF  INFO  FOR AUTO-PIX.

           4.  TYPE OF TIME - SELECT EITHER DAYLITE-SAVING OR STANDARD.

           5.  RETAIN  A CARRIAGE RETURN WITH EACH LINE-FEED  RECEIVED   (IF
           SENT).  THIS  PROGRAM  DEFAULTS TO  REMOVING  "ALL"  UN-NECESSARY
           CARRIAGE  RETURNS RECEIVED.  WHAT THIS MEANS IS:  IF YOU  RECEIVE
           CR/CR/CR/LF  -  THE PROGRAM SAVES  ONLY -ONE- CARRIAGE  RETURN  -
           CR/LF.    BY  THE  SAME TOKEN,  IF   THE  PROGRAM   RECEIVES  TEN
           CARRIAGE  RETURN   LINE-FEED PAIRS:  10 CR/LF'S, IT  DEFAULTS  TO
           SAVE ONLY THE FIRST CARRIAGE RETURN AND THEN  10 LINE-FEEDS.
           IF  YOU PREFER TO SAVE A CARRIAGE RETURN WITH EACH   LINE-FEED  -
           PRESS THE SPACE BAR TO TOGGLE YOUR SELECTION FROM "NO" TO "YES".

           6.   SERIAL  PORT USED FOR INTERFACE - SELECT THE  SERIAL   (COM)
           PORT   YOU ARE  USING WITH YOUR RTTY INTERFACE  (TERMINAL  UNIT).
           EITHER COM-1 OR COM-2 IS SUPPORTED.

           7.   PRINTER  PORT - SELECT THE PORT YOU WANT ANY PRINTER  OUTPUT
           TO   GO.  THIS  IS  USUALLY  LPT1  (FOR PARALLEL PRINTERS).    IF
           YOU  HAVE  OTHER PARALLEL PRINTERS AND WANT TO USE ONE OF THOSE -
           JUST  SELECT THE  PROPER PORT.   IF  YOU HAVE A  SERIAL  PRINTER,
           SELECT THE COM PORT YOU HAVE IT CONNECTED TO.

           IMPORTANT:   DO  -NOT-  HAVE THE SAME "SERIAL" PORT SELECTED  FOR
           BOTH  THE  RTTY INTERFACE (ITEM 6 ABOVE) AND A  "SERIAL"  PRINTER
           (ITEM 7 ABOVE).




                                       4





           8.  HAVE  BORDER AROUND DISPLAY SCREEN -  (FOR EGA AND VGA  ONLY)
           -   THE  PROGRAM FIRST BOOTS WITH A BORDER - FOR  THOSE  DISPLAYS
           THAT  WILL SUPPORT IT.  IF YOU PREFER NOT TO HAVE A BORDER,  JUST
           PRESS <SPACE> TO TOGGLE IT TO "NO".
           NOTE:    WHEN  USING BORDER ON - SOME  SCREEN  SAVERS  (BLANKERS)
           WILL  ONLY  REMOVE  THE  VISIBLE  PROGRAM FROM THE  DISPLAY   AND
           LEAVES THE SCREEN ENTIRELY A DIM WHITE (GRAY).  IF YOU HAVE  SUCH
           A SCREEN SAVER - YOU WILL HAVE TO SET THE BORDER TO OFF TO  BLANK
           THE  SCREEN.   SOME SCREEN SAVERS WILL  NOT  PERMIT  TRANSMITTING
           WHILE BLANKED.

           9.   DISPLAY OPTIONS MENU FOR SHIFT KEY - AS YOU  PROBABLY   HAVE
           NOTICED,  THIS  PROGRAM DISPLAYS THE OPTIONS ASSOCIATED WITH  THE
           UNSHIFTED  STATE, <SHIFT>, <CTRL> AND <ALT> KEYS.  IF YOU USE THE
           SHIFT  KEY A LOT AND ARE DISTRACTED  BY THE CHANGING STATUS  LINE
           (LINE  25),  YOU  CAN  CHANGE THIS OPTION TO  "NO"  -  THIS  WILL
           DISABLE THE CHANGE FOR THE <SHIFT> KEY.

           10.  ECHO  TYPED CHARACTERS  AND  MESSAGE PORTS TO RECV BUFFER  -
           MANY   PEOPLE  LIKE TO HAVE  WHAT THEY TYPE TO BE ECHOED  TO  THE
           RECEIVE BUFFER AND RECEIVE SCREEN.  IF YOU WANT THIS, TOGGLE  THE
           SELECTION TO "YES".

           THE   ABOVE OPTIONS ARE ALL "TOGGLE" SELECTIONS.  THIS MEANS  YOU
           SET  THE CURSOR  ON THE LINE YOU WANT TO CHANGE AND PRESS <SPACE>
           KEY TO TOGGLE THROUGH YOUR CHOICES.

           THE FOLLOWING ARE OPTIONS WHICH REQUIRE INPUT FROM YOU.

           11.   DISK  TO XMIT BUFF PATH - THIS WILL BE THE  "DEFAULT"  PATH
           USED   WHEN  YOU  WANT TO LOAD THE XMIT (PIX) BUFFER  FROM  DISK.
           YOU  ARE NOT  "BOUND" BY THIS SELECTION - AFTER PRESSING  F3  AND
           GETTING  THE  PROMPT ON LINE 17, YOU  CAN USE THE  BACKSPACE  (OR
           DELETE)  KEY TO BACKUP AND  ENTER  ANOTHER PATH, WHEN  NECESSARY,
           THEN THE DISKFILE NAME.
           NOTE: YOU CAN USE WILDCARDS WITHIN THE FILENAME YOU INPUT ABOVE.

           12.   RECV   BUFF  TO  DISK  PATH -  AGAIN,   THIS  WILL  BE  THE
           "DEFAULT"  PATH DISPLAYED WHEN YOU PRESS F4 TO SAVE  THE  RECEIVE
           BUFFER TO DISK.  YOU CAN BACKSPACE AND ENTER ANOTHER IF YOU WISH.
           NO WILDCARDS HERE - PLEASE.

           13.   AUTO_SAVE  DRIVE PATH - THIS WILL BE THE   "DEFAULT"   PATH
           DISPLAYED  WHEN  YOU PRESS <CTRL> F9 (AUTO_SAVE MODE) - TO  ENTER
           THE  FILENAME  USED TO SAVE ALL RECEIVED TEXT TO.  AGAIN YOU  CAN
           BACKUP AND CHANGE IT.

           14.   DIRECTORY  SEARCH PATH - THIS IS THE  "DEFAULT"  PATH  USED
           WHEN  YOU  ENTER F5 (EDIT/VIEW MODE) AND SELECT "D"  FOR  DISPLAY
           DIRECTORY.  IT CAN BE CHANGED TO.

           15.   DELETE  DISK  FILE PATH - THE "DEFAULT" PATH  USED  IN  THE
           PROMPT  WHEN  YOU SELECT <CTRL> F6 (DELETE FILE MODE).   THIS  IS
           CHANGEABLE ALSO.

           = THE FOLLOWING ARE FOR USE WITH  AUTO-PIX PROGRAM VERSION ONLY =

                          ====== STARTING ON NEXT PAGE ======

             = READ INFORMATION FOLLOWING THE AUTO-PIX CONFIGURE OPTIONS =
                                           5





           = THE FOLLOWING ARE FOR USE WITH  AUTO-PIX PROGRAM VERSION ONLY =

           16.   AUTO_PIX ON ERROR PATH - THIS  WILL BE THE PATH THAT   WILL
           CONTAIN FILES  THAT  FOR  SOME REASON COULDN'T BE SAVED IN  THEIR
           PROPER  PATH, DURING AUTO-PIX MODE.  THIS CAN BE CAUSED BY A DISK
           FULL  ERROR  OR  OTHER ERROR  CONDITION.  AT THIS TIME  ONLY  THE
           LOGFILE SAVE USES THIS PATH IN AN EMERGENCY.

           17.  AUTO_PIX LOGFILE PATH - THIS IS THE PATH USED WHEN  AUTO-PIX
           SAVES LOGGING  INFORMATION  TO DISK - FOR SYSTEM USERS.  ALL   OF
           THE  LOGFILE DISK FILENAMES WILL HAVE THE FORM:   MM-DD-YY     NO
           EXTENSION.

           18.   AUTO_PIX  USER_MSG  PATH  - THIS   IS  THE  PATH  ANY  USER
           MESSAGES, SENT TO YOU, WILL BE STORED UNDER.

           19.   AUTO_PIX  XMIT DRV PATH - THIS IS THE PATH  WHICH  AUTO-PIX
           WILL USE TO ACCESS THE "PIX" FILES SELECTED BY YOUR SYSTEM USERS.
           IT  CAN  BE JUST A FLOPPY  DRIVE  SUCH  AS   B:\ - OR  AN  ENTIRE
           PATH  TO  YOUR HARD DRIVE SUBDIRECTORY WHERE YOU  WANT  USERS  TO
           ACCESS LIKE  E:\XMAS-PIX\.

           20.   AUTO_PIX CALL-UP CODE - YOU ENTER THE SUFFIX YOU WANT  USED
           FOR  YOUR AUTO-PIX CALL-UP CODE - ALL - AUTO-PIX PROGRAM  CALL-UP
           CODES WILL BEGIN WITH "PIX" - LIKE MINE - PIX8LC.

           21.   SPECIAL OR HOLIDAY MESSAGE TO BE SENT DURING THE  "WELCOME"
           MESSAGE  IN AUTO-PIX.  LEAVE COMPLETELY BLANK IF YOU DO NOT  WANT
           ANYTHING SENT.

           22.   SPECIAL OR HOLIDAY MESSAGE TO BE SENT DURING THE   SIGN-OFF
           (EXIT) MESSAGE IN AUTO-PIX.  LEAVE COMPLETELY BLANK IF YOU DO NOT
           WANT ANYTHING SENT.

           ALL   OF   THE USER INPUT OPTIONS CAN BE CHANGED  BY  RE-ENTERING
           THEM  AND  EDITING  -  THEN PRESS <RETURN> TO  GO  BACK  TO  LINE
           SELECTION.

           WHEN   YOU ARE FINISHED WITH YOUR CONFIGURATION,  PRESS  <RETURN>
           AND   YOUR  SELECTIONS  WILL BE SAVED TO DISK.   YOU'LL  THEN  BE
           ASKED  IF  YOU  WANT TO USE THE OPTIONS YOU  JUST  SELECTED,  YOU
           PROBABLY  WILL WANT TO USE THEM - SO PRESS "Y" TO  INDICATE  YES.
           UNLESS  YOU CHANGE YOUR SYSTEM IN SOME WAY OR  YOUR TIME  CHANGES
           (DAYLITE/STANDARD)  - THIS SHOULD BE THE ONLY TIME YOU WILL  NEED
           TO  RUN  THE  "COMPLETE"  CONFIGURATION.   THE  VALUES  YOU  HAVE
           SELECTED  WERE  SAVED TO DISK AND WILL BE INPUT INTO  THE  PROPER
           VARIABLES  EACH  TIME THE PROGRAM STARTS-UP. YOU DO NOT  HAVE  TO
           CHANGE  EVERYTHING  WHEN  YOU  MODIFY  YOUR  CONFIGURATION,  JUST
           CHANGE THE ONE OR TWO ITEMS THAT  NEED TO BE CHANGED, THEN  PRESS
           <RETURN> AND THOSE CHANGES WILL BE SAVED  TO  DISK.   IF YOU WANT
           TO  HAVE  A CHANGE ONLY USED DURING THE  CURRENT  SESSION,  PRESS
           ESCAPE   KEY   <ESC>  INSTEAD  OF  <RETURN>,   THIS   EXITS   THE
           CONFIGURATION  SCREENS  AND  ASKS WHETHER YOU  WANT  TO  USE  THE
           CHANGES YOU  MADE DURING THE CURRENT SESSION - JUST PRESS "Y" AND
           YOU WILL USE THOSE CHANGES ONLY DURING THE CURRENT SESSION.





                                           6





              =========== CREATING AND EDITING MESSAGE PORTS ===========

           PRESS   F5,  THIS WILL BRING UP A MENU FOR THE  EDIT/VIEW   MODE.
           SELECT THE EDIT MESSAGE PORTS OPTION, BY PRESSING "M".  YOU  WILL
           THEN  BE PROMPTED FOR THE MESSAGE  PORT NUMBER.  YOU USE  ANY  OF
           THE  NUMBER KEYS LOCATED ABOVE THE NORMAL ALPHABET KEYS (NOT  THE
           ONES ON YOUR KEYPAD).  IT WILL DISPLAY A WINDOW FOR YOU TO  INPUT
           YOUR  INFO  INTO  THAT MESSAGE  PORT.   WHEN  YOU  FINISH  EITHER
           CREATING OR EDITING THAT MESSAGE PORT, PRESS <ESC> KEY, YOU  WILL
           BE  ASKED IF YOU WANT THOSE CHANGES SAVED TO DISK - YOU  PROBABLY
           WILL  - SO PRESS "Y" FOR YES.  FOLLOW THE SAME PROCESS TO  CREATE
           OR EDIT ANY MESSAGE PORTS YOU WILL BE USING.

           YOU   CAN   ALSO  NEST  A ANOTHER MESSAGE PORT CALL  WITHIN  YOUR
           INPUT  TO THE CURRENT MESSAGE PORT.  YOU  INPUT A NESTED  MESSAGE
           PORT BY PRESSING, AND HOLDING, THE  <ALT> KEY WHILE PRESSING  ANY
           OF THE MESSAGE PORT NUMBER KEYS. (ONES ABOVE THE NORMAL  "LETTER"
           KEYS - NOT THE KEYPAD)

           THIS VERSION  OF "AUTORTTY"  SUPPORTS ONLY A "BACKSPACE" TYPE  OF
           EDITING.   THE DELETE  KEY HAS THE SAME ACTION AS  THE  BACKSPACE
           WHEN EDITING YOUR TYPE AHEAD AND MESSAGE PORTS.

           PLEASE NOTE:  THE TRANSMIT (PIX) BUFFER EDITING SUPPORTS COMPLETE
           EDITING USING ALL EDITING AND ARROW KEYS.

           YOU CAN DELETE A WHOLE LINE BY PRESSING THE <CTRL> AND  "Y"   KEY
           COMBINATION.    TO   INPUT  A MESSAGE PORT  IN  THE  TYPE   AHEAD
           BUFFER,   YOU PRESS (AND HOLD) THE <ALT> KEY WHILE  PRESSING  THE
           NUMBER  KEY OF THE PORT YOU WANT TO INPUT.  (AGAIN - DO  NOT  USE
           KEYPAD KEYS)

           IMPORTANT:  NEVER HAVE A MESSAGE PORT CALL ITSELF - OR ANY  OTHER
           THAT  MAKES A CALL TO A MESSAGE PORT THAT WILL CREATE  A  "LOOP".
           THE MAXIMUM SIZE OF A MESSAGE PORT IS 1000 CHARACTERS.

           NOTE:   MESSAGE  PORT  ZERO (0) WILL  ALWAYS  BE  INITIALIZED  TO
           CONTAIN  40 RY'S AND A CR/LF PAIR.    AT PROGRAM  START-UP.   YOU
           CAN EDIT PORT 0 BUT IT WILL NEVER BE SAVED  TO     DISK,  AS  THE
           OTHERS ARE.

           NOTE:   MESSAGE PORT #1 IS A  SPECIAL PURPOSE MESSAGE PORT,  READ
           BELOW.

           NESTING   A  CALL TO MESSAGE PORT #1 MAKES IT EASY  TO  CONSTRUCT
           THE   SEQUENCE  OF  PORTS  CALLED  FOR  STATION  ID  SENT  DURING
           EXCHANGES IN A QSO.  MESSAGE PORT #1 SHOULD BE RESERVED FOR  THIS
           PURPOSE.   YOU CAN CLEAR MES-SAGE PORT  #1 BY PRESSING <ALT> C  -
           IT WILL PROMPT TO VERIFY YOU WANT TO CLEAR MESSAGE PORT  #1.   TO
           ADD A CALL TO MESSAGE PORT #1 - PRESS <ALT> A -  IT  WILL  PROMPT
           (ON LINE 17) FOR THE CALL SIGN TO ADD, DO NOT ADD A  LEADING   OR
           TRAILING   SPACE   -  ONE  TRAILING SPACE IS ADDED  BY   PROGRAM.
           YOU   CAN  REMOVE A CALL SIGN FROM MESSAGE PORT  #1  BY  PRESSING
           <ALT> R, YOU WILL BE PROMPTED  (AGAIN  ON  LINE 17) FOR THE  CALL
           SIGN  TO REMOVE -  IF  IT  IS UNABLE  TO FIND THE CALL - IT  WILL
           DISPLAY  A  MESSAGE  TO THAT  EFFECT  ON      LINE  17.   I  CALL
           MESSAGE  PORT #1 FROM WITHIN MESSAGE PORT #2 - THEN  ADD      "DE
           K8LC,  WALT,  IRONTON, OHIO"(CR/LF).

                               (CONTINUED ON NEXT PAGE)
                                           7





           THIS  WAY  YOU ONLY HAVE TO  GIVE     MESSAGE  PORT  #2   IN  THE
           TYPE  AHEAD BUFFER.  WHEN MESSAGE  PORT  #2  IS      CALLED,  THE
           FIRST  THING  IT DOES IS SEND MESSAGE PORT #1 -  THEN  SENDS  THE
           REMAINDER OF MESSAGE PORT #2.

           IMPORTANT  NOTE:  ALTHOUGH AUTORTTY SAVES, AND USES, THE  DEFAULT
           PATH DURING PROGRAM START-UP AND WHEN RETURNING FROM A "SHELL" TO
           YOUR  DOS, IT MAY BE SAFER TO RETURN TO THE RTTY PROGRAM  DEFAULT
           DIRECTORY  BEFORE  ENTERING:   EXIT<RETURN>   TO  RETURN  TO  THE
           PROGRAM.


             ======= WHAT ARE THOSE FUNNY CHARACTERS IN COLUMN 80? =======

           A   NOTE   ABOUT  THOSE  "FUNNY" CHARACTERS IN COLUMN   80:    AS
           YOU   HAVE PROBABLY NOTICED BY NOW, I DO NOT DISPLAY THE  END  OF
           LINE  SEQUENCE  RIGHT AFTER ANY TEXT YOU HAVE RECEIVED  OR  TYPED
           INTO  VARIOUS  BUFFERS.   I  HAVE  ALWAYS  USED,  AND  RECOMMEND,
           "WORDSTAR BY MICROPRO CORP." AS A FIRST RATE PIX FILE EDITOR, AND
           HAVE  TRIED  TO KEEP THE SCREEN LOOKING  THE  SAME, FOR  EASE  OF
           USE.    IT   ALSO  MAKES  FOR A  "CLEAN"   PIX   WHEN   YOU   ARE
           RECEIVING  ONE.  JUST REMEMBER A "-" INDICATES A CARRIAGE RETURN,
           A "J" INDICATES  A LINEFEED AND A "<" INDICATES A CARRIAGE RETURN
           / LINEFEED PAIR.


            =========== TYPING INTO THE XMIT TYPE AHEAD BUFFER ===========

           YOU   ENTER   TEXT  TO TRANSMIT IN THE SAME  FORM  YOU  USED   TO
           CREATE YOUR MESSAGE PORTS.  IT SUPPORTS THE SAME "BACKSPACE" TYPE
           EDITING AND WHOLE LINE DELETE WITH THE <CTRL> Y  KEY COMBINATION.
           THIS  TYPE  AHEAD  BUFFER  HAS   A   MAXIMUM  CAPACITY  OF   3000
           CHARACTERS.    THIS  SHOULD  BE  MORE  THAN  ENOUGH    FOR    ANY
           CONVERSATION  QSO.  IF  YOU  TRANSMIT  MORE  THAN  300 CHARACTERS
           WITHOUT  SENDING  YOUR CALL (FOR  IDENTIFICATION)   THE   PROGRAM
           PROMPTS   YOU  TO  INPUT PROPER  ID AND THEN TO  PRESS  <CTRL>  E
           KEY.   THE <CTRL>  E KEY SHOULD ALWAYS BE USED AT THE VERY END OF
           A  BUFFER YOU ARE PLANNING TO XMIT, (AFTER ANY MESSAGE PORT  INFO
           USED  FOR  ID AND THE  K'S WE USUALLY SEND).   WHEN  THE  PROGRAM
           ENCOUNTERS <CTRL> E, IT WILL SCROLL UP THE TYPE AHEAD WINDOW  AND
           PLACE  THE CURSOR IN COLUMN 1 - IT ALSO SENDS A  CARRIAGE  RETURN
           LINEFEED  PAIR, HOLDS FOR A SHORT DELAY AND THEN   SWITCHES  YOUR
           RIG  (AND  PROGRAM) BACK TO RECEIVE MODE.  TO  ACTUALLY  TRANSMIT
           THE  BUFFER  YOU JUST CREATED, PRESS <CTRL> T OR <SHIFT>  F2  KEY
           COMBINATIONS  THIS  WILL KEY YOUR TRANSMITTER AND  BEGIN  SENDING
           YOUR  TYPE AHEAD BUFFER.  WHEN  THE TRANSMIT CATCHES UP  TO  YOUR
           TYPING  -  YOU WILL STILL  HAVE  THE OPPORTUNITY  TO   CORRECT  A
           TYPO (IN THE WORD YOU ARE ENTERING)  BY  JUST PRESSING  BACKSPACE
           OR  DELETE TO GO BACK TO THE ERROR  THEN  ENTER  THE  CORRECTION.
           THIS IS CALLED "XMIT BY THE WORD" WHICH MEANS  THE  WORD YOU  ARE
           ENTERING  WILL NOT BE SENT UNTIL YOU PRESS THE <SPACE> AFTER  IT.
           MESSAGE  PORTS  ARE  ENTERED BY PRESSING AND  HOLDING  <ALT>  AND
           PRESSING  THE  NORMAL   NUMBER KEY (NOT KEYPAD  NUMBERS)  OF  THE
           MESSAGE PORT YOU WANT TO SEND.






                                           8





               ============== USING "BREAK" TRANSMIT MODE ==============

           THERE  WILL  BE TIMES, AFTER TYPING IN A LOT OF TEXT TO  USE  FOR
           YOUR  NEXT TRANSMISSION,  THAT  SOMEONE  WILL ASK YOU A  QUESTION
           THAT DEMANDS AN IMMEDIATE  ANSWER.  INSTEAD OF HAVING TO SEND THE
           WHOLE  BUFFER YOU HAVE TYPED, YOU CAN  ELECT TO USE  THE  "BREAK"
           TRANSMIT  MODE.   WHEN YOU  PRESS <SHIFT>  F1  THE   TYPE   AHEAD
           WINDOW  IS "SAVED" AND CLEARED.  THE TRANSMITTER  IS  KEYED ON  -
           AND  YOU ARE READY TO ENTER THE TEXT TO BE SENT.  AT THE END  YOU
           CAN  ENTER  YOUR ID INFO AND PRESS THE NORMAL <CTRL> E   KEY   TO
           RETURN TO RECEIVE - OR YOU MAY ELECT TO GO DIRECTLY TO THE NORMAL
           TYPE AHEAD MODE WITHOUT GOING BACK THROUGH RECEIVE - YOU CAN   DO
           THIS BY PRESSING <CTRL> T OR <SHIFT> F2.


                   ============== NORMAL RECEIVE MODE ==============

           WHEN  THE PROGRAM IS "BOOTED" IT COMES UP IN THE  NORMAL  RECEIVE
           MODE, AT WHATEVER  BAUD RATE AND MODE YOU SELECTED DURING PROGRAM
           CONFIGURATION.  WHILE  YOU  ARE IN QSO - MANY  TIMES YOU WILL  BE
           BUSY TYPING AHEAD FOR YOUR NEXT TRANSMISSION - SOMETHING IS  SENT
           AND  BY THE TIME YOU LOOK UP, ITS SCROLLING OFF THE  SCREEN.   IF
           THIS HAPPENS, YOU CAN PRESS THE F5 KEY TO  BRING-UP THE EDIT/VIEW
           MODE  MENU.  BY PRESSING "R" YOU WILL SELECT THE RECEIVE  BUFFER,
           THE  SCREEN THEN  DISPLAYS YOUR RECEIVE BUFFER STARTING  AT   THE
           BEGINNING.   YOU CAN PRESS PAGEDOWN OR PAGEUP  TO   MOVE  THROUGH
           THE  BUFFER, OR HOME/END KEYS TO JUMP TO THE BEGINNING  OR   END,
           RESPECTIVELY,   OF  THAT BUFFER.  IN THIS WAY YOU CAN  SEE   WHAT
           HAD   BEEN SENT.  WHEN YOU ARE FINISHED LOOKING  PRESS:  <ESCAPE>
           AND YOU WILL RETURN TO  THE  EDIT/VIEW MENU, THEN PRESS  <ESCAPE>
           AGAIN  TO RETURN  TO  NORMAL RECEIVE MODE.  YOU CAN ALSO USE  THE
           "BLOCK"  MODE  TO  LOOK  THRU THE BUFFER AND   MARK  A  BLOCK  TO
           TRANSMIT,  SAVE  TO DISK OR DELETE (FROM  THE   RECEIVE  BUFFER).
           YOU ALSO HAVE THE OPTION TO SAVE THE RECEIVE BUFFER TO  DISK,  TO
           DO  THIS  PRESS: F4 - A PROMPT IS DISPLAYED, ON LINE  17,  FOR  A
           FILENAME  TO  BE USED TO SAVE THE BUFFER UNDER.   ANOTHER  OPTION
           AVAILABLE  TO  YOU, IN  THE BLOCK MODE, IS THE ABILITY TO MARK  A
           "BLOCK"  OF RECEIVE  BUFFER, YOU  CAN THEN PRINT  (PRINT MODE  IS
           SELECTED  BY PRESSING F9 FROM  NORMAL RECEIVE  MODE),  DELETE  OR
           TRANSMIT  THAT BLOCK.  YOU  CAN  BEGIN  "PRINT ECHO"   MODE,   TO
           SEND RECEIVED CHARACTERS TO YOUR PRINTER,  BY  PRESSING <CTRL>  P
           - IT WILL DISPLAY THE PRINT ECHO MESSAGE ON 16.  IF YOU DON'T GET
           THE PRINT ECHO MESSAGE AND INSTEAD YOU HEAR A BEEP,  YOUR PRINTER
           IS  PROBABLY  OFF  LINE   -  NOT TURNED ON -  OR  IN  SOME  ERROR
           CONDITION.

           THERE'S  AN OPTION IN THE CONFIGURATION SCREENS THAT  WILL  ALLOW
           ALL TYPE AHEAD  CHARACTERS, MESSAGE PORTS AND BLOCK SENDING TO BE
           ECHOED  TO  THE RECEIVE  SCREEN AND, AT THE SAME TIME,  INTO  THE
           RECEIVE  BUFFER.   IF YOU DESIRE THIS - BE SURE  TO  SELECT  THAT
           OPTION IN THE CONFIGURATION.

           IMPORTANT NOTE:  THERE ARE, RARE, OCCASIONS THE PROGRAM MAY  MISS
           AN  INTERRUPT  OR SOME OTHER TIMED EVENT, WHEN THIS  HAPPENS  ANY
           NUMBER OF WEIRD THINGS CAN BEFALL THE PROGRAM.  ANYTIME SOMETHING
           HAPPENS THAT CAUSES THE SCREEN TO GET MESSED UP - ALWAYS TRY  THE
           <ALT> F1 REDRAW - MOST OF THE TIME THE NEW SCREEN WILL BE REDRAWN
           CORRECTLY.   IT MAKE TAKE SEVERAL TRYS TO ACCOMPLISH THE  CORRECT
           REDRAW.  IF THE REDRAW DOESN'T CORRECT YOUR SCREEN PROBLEM -  TRY
           GOING  INTO  OTHER  MODES AND  RETURNING,  BEFORE  REBOOTING.
                                       9





                  ============== USING EDIT/VIEW MODE ==============

           PRESSING F5 WILL BRING-UP THE EDIT/VIEW MENU IN THE UPPER AREA OF
           THE RECEIVE WINDOW.  YOU HAVE SEVERAL OPTIONS AVAILABLE TO YOU IN
           THIS  MODE.  THE FIRST IS "EDIT MESSAGE PORT", ENTERING "M"  WILL
           TAKE YOU INTO THIS MODE.  THE NEXT WINDOW WILL PROMPT YOU FOR THE
           MESSAGE  PORT  NUMBER YOU WISH TO EDIT (OR  CREATE).   USING  THE
           NORMAL  NUMBER  KEYS  (NOT THOSE ON THE KEYPAD)  ENTER  THE  PORT
           NUMBER  YOU NEED TO WORK WITH. AFTER MAKING YOUR SELECTION AS  TO
           PORT  NUMBER TO USE - YOUR DISPLAY WILL NOW HAVE A  WINDOW  WHICH
           YOU  WILL  USE  TO INPUT YOU MESSAGE.   ENTERING  CHARACTERS  AND
           EDITING  USES THE SAME -BACKSPACE ONLY- FORMAT AS YOU USE IN  THE
           TYPE  AHEAD AND BREAK MODES.  FULL EDITING WILL BE PROVIDED IN  A
           LATER VERSION OF AUTORTTY.  AFTER YOU HAVE COMPLETED YOU MESSAGE,
           PRESS <ESC> - YOU ARE THEN PROMPTED IF YOU WANT THE MESSAGE  PORT
           SAVED TO DISK - SELECT "Y" OTHERWISE PRESS "N" OR <ESC>.

           YOUR SECOND OPTION IN EDIT/VIEW IS TO VIEW EITHER THE RECEIVE  OR
           TRANSMIT  (PIX)  BUFFER.  USING EITHER "R" OR "T"  (FOR  RECEIVE,
           TRANSMIT  RESPECTIVELY)  YOU SELECT THE BUFFER YOU WANT  TO  USE.
           YOU CAN MOVE THROUGH THE BUFFER USING ANY OF THE FOLLOWING  KEYS:
           HOME  - TAKES YOU TO THE BEGINNING OF BUFFER, END - TAKES YOU  TO
           THE END OF BUFFER, PAGEUP - TAKES YOU UP A PAGE (SCREEN),  PAGEDN
           - TAKES YOU DOWN A PAGE (SCREEN).  WHEN YOU ARE FINISHED  LOOKING
           THROUGH  THE  BUFFER - PRESS <ESC>, THIS TAKES YOU  BACK  TO  THE
           EDIT/VIEW MENU.

           THE THIRD OPTION IS TO DISPLAY A DISK DIRECTORY.  PRESS "D"  WILL
           BRING  UP  A WINDOW WHICH PROMPTS FOR A  PATH  (DRIVE\SUB-DIRS\).
           AFTER  ENTERING  YOUR  DESIRED PATH (ENTERING  NOTHING  WILL  NOT
           DISPLAY  DEFAULT)  PRESS <RETURN> AND THE "SORTED"  DIRECTORY  IS
           DISPLAYED  IN  THE  SAME WINDOW YOU HAVE  BEEN  USING.   YOU  USE
           PAGEUP/PAGEDN TO MOVE THROUGH THE LIST OF FILES DISPLAYED, AGAIN,
           HOME/END KEYS ARE SUPPORTED.  PRESS <ESC> WILL RETURN YOU TO  THE
           EDIT/VIEW MENU.

           TO   RETURN  TO  NORMAL RECEIVE MODE - PRESS:  <ESC>   OR   SHIFT
           F5.  THE RECEIVE SCREEN IS COMPLETELY UPDATED.






















                                       10





               ============== USING THE BLOCK MODE OPTION ==============

           PRESSING  F8  BRINGS  UP BLOCK MODE MENU,  HERE  YOU  CAN  SELECT
           BETWEEN XMIT SENT  BUFFER (THIS BUFFER HAS THE LAST 1120 BYTE  OF
           TEXT  YOU  HAVE SENT FROM  THE KEYBOARD) OR  THE  RECEIVE  BUFFER
           (THIS BUFFER HAS A MAXIMUM OF 65,500  CHARACTERS). THE OTHER  TWO
           OPTIONS ON THIS MENU ARE THE DELETE BLOCK FROM RECEIVE BUFFER AND
           SAVING  THE  BLOCK TO DISK.  TO MARK A BLOCK TO BE USED  -  FIRST
           SELECT  THE  BUFFER YOU WANT TO USE USING EITHER THE "T"  OR  "R"
           KEY.   THE  XMIT  SENT  BUFFER IS  COMPLETELY  DISPLAYED  ON  ONE
           SCREEN,  THE   RECEIVE BUFFER CAN CONTAIN  MANY  DISPLAY  SCREENS
           (PAGES).   USE THE ARROW  KEYS  TO MOVE THE  CURSOR   AROUND  THE
           SCREEN  AS NEEDED.  TO MARK THE BEGINNING OF A BLOCK - PLACE  THE
           CURSOR  ON THE CHARACTER THAT WILL BE  THE  STARTING   POINT   OF
           THE BLOCK - THEN  PRESS  <CTRL>  B.  THAT CHARACTER  WILL THEN BE
           DISPLAYED IN REVERSE VIDEO.  MOVE THE CURSOR TO THE  VERY END  OF
           THE  BLOCK YOU WANT TO SELECT AND PRESS <CTRL> E IF YOU  ARE   IN
           THE XMIT SENT BUFFER - THE ENTIRE BLOCK IS DISPLAYED IN   REVERSE
           VIDEO,   OTHERWISE  THE END CHARACTER WILL ALSO BE DISPLAYED   IN
           REVERSE  VIDEO.   PRESSING EITHER <CTRL> B OR <CTRL>  E  ACTUALLY
           TOGGLES  THE  BLOCK  POINTER  ON AND OFF.   IF,  AFTER  YOU  HAVE
           SELECTED A BEGINNING OR END, YOU WANT  TO  CHANGE YOUR  SELECTION
           -  JUST  PRESS  THE KEY THAT SELECTS THE POINTER   YOU   WANT  TO
           CHANGE  (<CTRL>  B = START OR <CRTL> E  =  END) AND  PRESS   THAT
           KEY  AGAIN.  THE FIRST KEY PRESS WILL CLEAR THE ORIGINAL  POINTER
           (EVEN   IF YOU ARE NOT ON IT WITH THE CURSOR), PRESSING  IT   THE
           SECOND   TIME WILL SELECT THAT POINTER AGAIN AT  WHATEVER  CURSOR
           POSITION  YOU  MAY BE ON AT THE TIME.  YOU ARE NOW READY TO  EXIT
           TO THE MENU,  YOU MUST  PRESS THE F8 KEY (PRESSING <ESCAPE>  WILL
           RETURN  YOU TO THE MENU - BUT  CLEARS ANY BLOCK MARKERS THAT  YOU
           MAY  HAVE SELECTED).  USING F8 TO EXIT THE BUFFER WILL  SAVE  THE
           POINTERS  YOU HAVE SELECTED.  THIS BLOCK IS NOW READY FOR YOU  TO
           DO WITH AS YOU WISH (SAVE,DELETE,PRINT OR RE-SEND).

           NOTE:  ALL KEY ASSIGNMENTS FOR BLOCK MODE ARE GIVEN ON PAGES: 5 &
           6  OF:  SECTION 2 - PROGRAM KEY ASSIGNMENTS.


                  ============== USING AUTO-SAVE MODE ==============

           SINCE  THE  RECEIVE  BUFFER  IS  LIMITED  TO  HOLDING  THE   LAST
           65,500  CHARACTERS,   SAVING  EVERYTHING  THAT MAY  BE  SENT  FOR
           LONG PERIODS IS IMPOSSIBLE  USING IT.  THIS IS WHERE  "AUTO-SAVE"
           COMES  IN,  BY  SELECTING  THIS   MODE,  EVERYTHING  RECEIVED  IS
           "ECHOED"  TO  A DISKFILE.  BY  PRESSING <CTRL> F9 - YOU  WILL  BE
           PROMPTED  (ON  LINE  17)  FOR A FILENAME  TO  SAVE  THE  RECEIVED
           CHARACTERS  UNDER.  THE AMOUNT OF RECEIVED TEXT IS ONLY   LIMITED
           BY  THE  DISK SIZE.

           IMPORTANT  NOTE:  FILES SAVED USING AUTO-SAVE MAY BE MUCH  LARGER
           THAN CAN BE LOADED INTO PIX BUFFER TO EDIT.  IF THIS IS THE CASE,
           YOU WILL HAVE TO USE AN OUTSIDE WORD PROCESSOR TO EDIT THE FILE.

           NOTE:
           IF YOU HAVE A COLOR MONITOR, LINE 25 (THE OPTION/INFO LINE)  WILL
           HAVE  A  CYAN (AQUA) COLOR BACKGROUND.  MONO  USERS  SHOULD  HAVE
           "NORMAL"  VIDEO.  YOU CAN ALSO CHECK BY PRESSING  <CTRL>   F9  TO
           SEE  IF  YOU ARE IN "AUTO-SAVE" MODE -  BY  PRESSING  THOSE  KEYS
           (WHEN YOU ARE IN AUTO-SAVE) A MESSAGE IS DISPLAYED INDICATING YOU
           ARE ALREADY IN "AUTO-SAVE" MODE.  TO CLOSE FILE, PRESS <ALT> F9.
                                       11





                    ============== USING PRINT MODE ==============

           PRESSING   F9  - DISPLAYS THE PRINT MENU (IF YOUR PRINTER  IS  ON
           LINE   AND NOT  IN  SOME ERROR CONDITION).  HERE YOU  CAN  SELECT
           BETWEEN   PIX   XMIT BUFFER, RECEIVE BUFFER OR A  RECEIVE  BLOCK.
           AFTER  SELECTING  THE   BUFFER, YOU HAVE  THE  OPTION  OF  EITHER
           PRINTING THE WHOLE FILE OR PART OF A  FILE (FILL).   YOU CAN ALSO
           TOGGLE  BETWEEN AUTO-LINEFEED OR NORMAL  PRINTING.  USING   AUTO-
           LINEFEED WILL SPREAD OUT AN OVERLINE TO MAKE SEEING  "DINGS" IN A
           PIX  EASIER  TO  SPOT.  USING THIS PRINT MODE  YOU  CAN  PRINT  A
           DISKFILE  FROM  THE XMIT (PIX) BUFFER WHILE  VIEWING  THE  NORMAL
           RECEIVE  MODE SCREEN.  YOU WILL NOT LOSE ANY RECEIVE  OR  PRINTER
           CHARACTERS BY DOING THIS.

                   ============== USING "SHELL" MODE ==============

           BY  PRESSING <ALT> F10 YOU CAN SHELL OUT OF THE PROGRAM  TO  YOUR
           OPERATING  SYSTEM (THE FILE STORED UNDER THE COMSPEC  ENVIRONMENT
           VARIABLE).   IF  YOU  LIMIT  YOUR  "OUT OF PROGRAM  TIME"  TO  20
           MINUTES OR LESS, YOU  WILL NOT LOSE ANY RECEIVE CHARACTERS.  WHEN
           YOU ARE FINISHED USING THE SHELL JUST ENTER:  EXIT<RETURN>  - AND
           YOU  WILL BE RETURNED TO THE PROGRAM WITH THE  SCREEN  COMPLETELY
           UPDATED.   THIS SELECTION IS AVAILABLE IN EITHER  NORMAL  RECEIVE
           MODE, OR IN THE -TYPE AHEAD- XMIT MODE.

           IMPORTANT NOTE:  ALTHOUGH AUTORTTY SAVES THE DEFAULT PATH  DURING
           PROGRAM START-UP, FOR INTERNAL FILE SAVES (LIKE MSG PORTS, ETC.),
           IT  MAY BE SAFER HAVE THE PATH SET TO THE PROGRAM DEFAULT  BEFORE
           RETURNING   FROM  YOUR  "SHELL"  MODE,  ALTHOOGH  I  HAVE   NEVER
           ENCOUNTERED  A PROBLEM BY RETURNING TO THE PROGRAM  FROM  ANOTHER
           PATH.

           IMPORTANT  NOTE:   NEVER CALL-UP A PROGRAM FROM THIS  SHELL  THAT
           WILL MODIFY THE SERIAL PORT YOU ARE USING FOR YOUR INTERFACE.


             ============== BAUD RATE - RTTY MODE SELECTION ==============

           TO  TOGGLE BETWEEN FIXED BAUD RATES (45-75-110-135-300) YOU  JUST
           PRESS  <CTRL>  B.  TO TOGGLE BETWEEN ASCII AND BAUDOT JUST  PRESS
           <CTRL>  V.  IF YOU  ARE  IN ASCII MODE - YOU CAN  TOGGLE  BETWEEN
           ASCII8  (8  LEVEL)  AND ASCII  7 (7 LEVEL) BY PRESSING <CTRL>  A.
           THESE SELECTIONS WORK ONLY IN RECEIVE MODE.

               ============== SENDING DATE/TIME AND CWID ==============

           PRESS  <CTRL>  D  TO SEND THE CURRENT  DATE/TIME.   THIS  CAN  BE
           ENTERED  INTO THE  TYPE AHEAD BUFFER AS WELL - AND WILL  BE  SENT
           WHEN  THE  XMIT ROUTINE COMES TO IT.  PRESS <CTRL> I  TO  SEND  A
           CWID.   THIS  IS  NOT STORED IN THE TYPE AHEAD, SO  IT   IS  ONLY
           AVAILABLE WHEN THE TYPE AHEAD BUFFER IS EMPTY (CAUGHT UP  TO YOUR
           TYPING).    AUTORTTY  WILL AUTOMATICALLY SEND  YOUR  CWID   EVERY
           NINE MINUTES, WHETHER IN PIX OR FILL MODE OR JUST SENDING TEXT IN
           A QSO.  IT WILL  EVEN  ID IF YOU ARE ON THE PHONE AND THE RIG  IS
           SITTING  THERE  IN "MARK" TONE.





                                          12





            ======= SENDING FILES ENTERED IN THE TYPE AHEAD BUFFER =======

           WHEN  YOU  FIRST ENTER <CTRL> F  THE NEXT INPUT MUST BE  A  VALID
           FILENAME.  YOU CAN'T HAVE ANY  SPACES BETWEEN THE  CHARACTERS  IN
           THE    FILESPEC  (DRIVE/PATH/FILENAME).  YOU  END  YOUR  FILESPEC
           ENTRY  BY  PRESSING <CTRL> F - A  SECOND TIME. (NEVER  ALLOW  THE
           FILENAME  BETWEEN  THE CONTROL F CHARACTERS TO  WRAP  TO  ANOTHER
           LINE)    SEE  AN EXAMPLE OF THIS AND FURTHER INFORMATION  IN  THE
           PROGRAM  KEY  ASSIGNMENTS AREA OF THIS MANUAL, SECTION2.


           ========== LOADING AND TRAMSMITTING THE PIX XMIT BUFFER =========

           BY   PRESSING  F3 - YOU WILL BRING UP A MENU IN THE UPPER  WINDOW
           GIVING YOU THE OPTIONS AVAILABLE TO YOU FOR LOADING THE  TRANSMIT
           (PIX)  BUFFER.  THOSE OPTIONS ARE:  1. LOAD BUFFER FROM DISK,  2.
           LOAD  BUFFER FROM THE RECEIVE BUFFER (THE CURRENT  CONTENTS),  3.
           LOAD BUFFER FROM A "BLOCK" SELECTED FROM THE RECEIVE BUFFER.

           WHEN  LOADING  FROM DISK, YOU MUST INPUT  THE  COMPLETE  FILESPEC
           (DRIVE:\PATH\FILENAME)  OF   THE DISKFILE TO BE LOADED  INTO  THE
           PIX   XMIT BUFFER.  THE FILENAME WILL BE DISPLAYED ON  LINE  ONE.
           IF YOU NEED TO EDIT THE FILE BEFORE SENDING, PRESS <CTRL> F3  AND
           YOU WILL ENTER "AUTOEDIT", THE EDITOR MODULE.

           WHEN LOADING FROM EITHER OF THE RECEIVE BUFFER OPTIONS, THE  NAME
           DISPLAYED ON LINE ONE WILL REFLECT WHICH OPTION YOU USED.  IF YOU
           PLAN  ON SAVING AND/OR EDITING THE TRANSMIT BUFFER, PRESS  <CTRL>
           F3.  IF YOU PREVIOUSLY LOADED THE BUFFER FROM THE RECEIVE  BUFFER
           OR  BLOCK  -  YOU  WILL  BE  PROMPTED  FOR  A  COMPLETE  FILESPEC
           (DRIVE:\PATH\FILENAME)  YOU WANT THE BUFFER SAVED UNDER.    AFTER
           GIVING AN ACCEPTABLE FILESPEC, YOU WILL ENTER THE TRANSMIT  (PIX)
           BUFFER EDITOR "AUTOEDIT".

           NOTE:   FOR INFORMATION ON USING "AUTOEDIT", THE  TRANSMIT  (PIX)
           BUFFER EDITING MODULE, SEE NEXT PAGE.

           WHEN  YOU   ARE   IN  XMIT  MODE, YOU CAN  TRANSMIT  THE  PIX  BY
           PRESSING <SHIFT> F3,  THIS  WILL HALT  YOUR TYPE AHEAD SENDING  -
           SO  IT SHOULD ONLY BE SELECTED WHEN  YOUR TYPE  AHEAD  BUFFER  IS
           EMPTY (AS INDICATED BY THE TYPE BUFF SIZE ON  LINE 18).


           ========== PREPARING AND SENDING PART (FILL) OF A PIX ===========

           WHEN  THE XMIT BUFFER IS LOADED, PRESS F7 - YOU WILL BE  PROMPTED
           (ON  LINE 17)  FOR BOTH THE START AND END FILL LINES.  AFTER  YOU
           HAVE GIVEN YOUR INPUT, IT WILL BE DISPLAYED BESIDE THE PIX NUMBER
           ON  LINE ONE.  YOU  CAN TRANSMIT  THE  "FILL"  FROM  YOUR  NORMAL
           TYPE AHEAD  MODE  BY  PRESSING <SHIFT> F7.  AGAIN YOUR TYPE AHEAD
           BUFFER SHOULD BE EMPTY WHEN ENTERING THIS THIS MODE.


              ============== EXITING YOUR AUTORTTY PROGRAM ==============

           TO   EXIT  AUTORTTY, PRESS <CTRL> O - A MESSAGE WILL  APPEAR   ON
           LINE  25 INFORMING YOU TO PRESS <CTRL> U TO EXIT OR ANY OTHER  TO
           CONTINUE IN THE PROGRAM.


                                       13





           =======  USING  "AUTOEDIT" TRANSMIT (PIX) BUFFER EDITOR  =======

           AFTER  LOADING THE TRANSMIT (PIX) BUFFER, USING THE  F3  COMMAND,
           YOU CAN ENTER THE EDIT BUFFER MODE BY PRESSING <CTRL> F3.  IF YOU
           PREVIOUSLY  LOADED THE BUFFER FROM EITHER OF THE  RECEIVE  BUFFER
           OPTIONS,  YOU  WILL  FIRST BE PROMPTED FOR  A  COMPLETE  FILESPEC
           (DRIVE:\PATH\FILENAME) TO SAVE THE BUFFER UNDER.

           THE EDITOR WILL COMPLETELY FILL YOUR COMPUTER SCREEN.  NOTE:  ALL
           RECEIVED DATA IS STILL BEING SAVED IN THE RECEIVE BUFFER AND WILL
           BE DISPLAYED WHEN YOU EXIT (BY PRESSING <ESCAPE>) THE EDITOR.

           LINE  (1) HAS THE EDITOR NAME "AUTOEDIT" ALONG WITH THE  FILENAME
           OF  THE FILE WHICH IS DISPLAYED.  LINE (24) SHOWS THE  AMOUNT  OF
           "FREE" BUFFER SPACE - THE ACTUAL ROW OF THE FILE THE CURSOR IS ON
           (OVERLINES  ARE  NOT  COUNTED) - THE COLUMN WITHIN  THE  ROW  THE
           CURSOR IS ON (EACH ROW CAN BE AS LONG AS 225 CHARACTERS, ALTHOUGH
           NOT  RECOMMENDED, ITS THERE SO YOU CAN USE BACKSPACE AND  DELETE
           MODES WHICH APPEND LINES TOGETHER).  ADDITIONALLY, LINE (24) HAS
           AN  INDICATOR TO INFORM WHETHER YOU ARE IN INSERT (OPENS A  LINE
           UP  TO  "INSERT" CHARACTERS TYPED WITHIN IT) OR  OVERWRITE  (NEW
           CHARACTERS  ARE ENTERED "OVER" THE OLD TEXT) MODE.  THE  LETTERS
           "INS"  STAND FOR INSERT MODE - "OVR" INDICATES  OVERWRITE  MODE,
           THE  CURSOR ALSO INDICATES WHICH MODE YOU ARE IN.  AN  UNDERLINE
           CURSOR  INDICATES  "INSERT"  MODE -  A  BLOCK  CURSOR  INDICATES
           "OVERWRITE"  MODE.  YOU TOGGLE BETWEEN THESE MODES  BY  PRESSING
           <INSERT>  KEY.  LASTLY, LINE (24) DISPLAYS THE SIZE OF THE  FILE
           YOU ARE EDITING, THIS IS UPDATED (AS IS THE BUFFER FREE) -  WHEN
           YOU ENTER OR DELETE CHARACTERS.  LINE (25) DISPLAYS THE  OPTIONS
           AVAILABLE WITHIN THE EDITOR.

           HELP - PRESS F1 - WILL DISPLAY A SCREEN OF KEY ASSIGNMENTS USED.

           PRESSING  F3  (IN  NORMAL  EDIT MODE) - WILL  PROMPT  YOU  FOR  A
           COMPLETE FILESPEC (DRIVE:\PATH\FILENAME) OF THE DISKFILE YOU WANT
           TO "INSERT" AT THE CURRENT CURSOR POSITION.

           PRESSING F4 (IN NORMAL EDIT MODE) - WILL SAVE THE BUFFER TO DISK,
           USING   THE  FILESPEC  YOU  ENTERED  PREVIOUSLY.    THE   PROGRAM
           AUTOMATICALLY  RENAMES THE CURRENT FILE WITH A ".BAK"  EXTENSION,
           THEN SAVES THE CURRENT BUFFER CONTENTS USING THE NORMAL FILENAME.
           IF,  FOR  SOME REASON, IT CAN NOT SAVE THE FILE  AT  THE  CURRENT
           FILESPEC - YOU WILL BE PROMPTED FOR ANOTHER FILESPEC TO SAVE  THE
           BUFFER UNDER.

           PRESSING  F4  (IN BLOCK MODE) - WILL PROMPT YOU  FOR  A  COMPLETE
           FILESPEC  (DRIVE:\PATH\FILENAME) WHICH WILL BE USED  WHEN  SAVING
           THE "MARKED" BLOCK.

           PRESSING  F8 TOGGLES BLOCK MODE (ON/OFF).  WHEN ON, YOU CAN  MARK
           THE  BEGINNING AND END OF A "BLOCK" OF TEXT TO EITHER  DELETE  OR
           COPY TO ANOTHER LOCATION.  YOU SELECT THE "BLOCK START" BY  FIRST
           PLACING  THE  CURSOR AT THE POINT YOU WANT THE BLOCK TO  START  -
           THEN  PRESS  <CTRL> B. BY THE SAME TOKEN, YOU SELECT  THE  "BLOCK
           END" BY PLACING THE CURSOR AT THE POINT YOU WANT THE BLOCK TO END
           - THEN PRESS <CTRL> E.  WHEN YOU MAKE THESE SELECTIONS, RIGHT AND
           LEFT  POINTING  TRIANGLES  ARE  "INSERTED"  IN  THEIR  RESPECTIVE
           POSITIONS  (EVERYTHING  WITHIN  THESE  "TRIANGLES"  ARE  IN   THE
           SELECTED  BLOCK - INCLUDING ANY END-OF-LINE CHARACTERS).  IF  YOU
                            (CONTINUED ON NEXT PAGE)
                                       14





           ===  USING  "AUTOEDIT" TRANSMIT (PIX) BUFFER EDITOR (CONT.)  ===

           MAKE A MISTAKE IN SELECTING A BLOCK MARKER - JUST PRESS THAT  KEY
           SEQUENCE  AGAIN AND THE MARKER WILL BE CLEARED FROM  THE  SCREEN.
           YOU  DO NOT HAVE TO BE "ON" THE MARKER TO CLEAR IT - EVEN IF  THE
           MARKER  HAS SCROLLED OFF THE SCREEN, IT WILL BE CLEARED,  IF  YOU
           HAVE THE CURSOR AT THE NEW POSITION - JUST PRESS THE PROPER BLOCK
           SELECTING KEYS AGAIN AND IT WILL BE MARKED.  LINE 25 SHOWS IF YOU
           HAVE  A BLOCK MARKER SET OR CLEARED.  PRESSING F8 A  SECOND  TIME
           WILL EXIT BLOCK MODE.

           YOU ONLY HAVE THREE OPTIONS AVAILABLE IN BLOCK MODE:  1. <CTRL> D
           -  TO  DELETE  THE "MARKED" BLOCK,   2. <CTRL> O -  TO  COPY  THE
           "MARKED"  BLOCK,  STARTING AT THE CURRENT CURSOR  POSITION.   YOU
           CAN'T  HAVE THE CURSOR INSIDE THE BLOCK WHEN YOU  SELECT  "COPY".
           3. F4 - SAVES CURRENT MARKED BLOCK (PROMPTS FOR FILESPEC).

           IMPORTANT NOTE:
           IF  YOU ATTEMPT TO DELETE A BLOCK THAT IS LARGER THAN  10K  BYTE,
           YOU  WILL GET A MESSAGE WINDOW WHICH EXPLAINS THAT THE BLOCK  YOU
           HAVE SELECTED IS OVER 10K AND YOU WILL NOT BE ABLE TO  "UNDELETE"
           IT.   THE WINDOW THEN PROMPTS, ASKING IF YOU WANT TO  DELETE  THE
           BLOCK ANYWAY.

                     ----  KEYS SUPPORTED WITHIN "AUTOEDIT"  ----

           F1  -  HELP  - DISPLAYS A SCREEN WHICH CONTAINS ALL  OF  THE  KEY
           ASSIGNMENTS USED WITHIN THE EDITOR.

           F3  (NORMAL  EDIT  MODE)  -  PROMPTS  FOR  A  COMPLETE   FILESPEC
           (DRIVE:\PATH\FILENAME) OF THE FILE TO BE INSERTED AT THE  CURRENT
           CURSOR POSITION.

           F4 (NORMAL EDIT) - SAVES BUFFER - SEE PREVIOUS PAGE.

           F4 (BLOCK MODE) - PROMPTS FOR A COMPLETE FILESPEC (DRIVE:\PATH\
           FILENAME) FOR SAVING CURRENT BLOCK TO DISK.

           F8  - TOGGLES ENTER/EXIT OF BLOCK MODE (LINE 24 WILL SHOW  IF  IN
           BLOCK MODE OR NORMAL EDIT MODE).

           <CTRL>B - TOGGLES SET/CLEAR OF START OF BLOCK (IN BLOCK MODE).

           <CTRL>E - TOGGLES SET/CLEAR OF END OF BLOCK (IN BLOCK MODE).

           <BACKSPACE>  WILL "DELETE" AS THE CURSOR MOVES BACK TO THE  LEFT.
           IF  YOU  ARE IN COLUMN ONE - PRESSING BACKSPACE  WILL  CAUSE  THE
           CURRENT LINE TO BE APPENDED TO THE LINE ABOVE (AFTER REMOVING THE
           PREVIOUS LINE'S END-OF-LINE CHARACTER/S).

           <DELETE>  WILL "DELETE" CHARACTERS TO THE RIGHT OF THE CURSOR  AS
           THEY  ARE "PULLED" TO THE CURSOR.  IF YOU HAVE THE CURSOR AT  THE
           END OF A LINE - IT WILL "PULL" THE NEXT LINE UP AND APPEND IT  TO
           THE  CURRENT LINE (AFTER REMOVING THE CURRENT LINE'S  END-OF-LINE
           CHARACTER/S).

           <ARROW>  KEYS - ALL ARROW KEYS ARE SUPPORTED.  LINES LONGER  THAN
           THE  CURRENTLY DISPLAYED 79 CHARACTERS (AS INDICATED BY A "+"  IN
           COLUMN 80) WILL BE DISPLAYED, AS THE CURSOR REACHES COLUMN 80, BY
                            (CONTINUED ON NEXT PAGE)
                                       15





           ===  USING  "AUTOEDIT" TRANSMIT (PIX) BUFFER EDITOR (CONT.)  ===

           HAVING  THE  SCREEN "SCROLL" TO THE RIGHT.  IT WILL  JUMP  IN  20
           CHARACTER INCREMENTS AS YOU MOVE THE CURSOR FARTHER TO THE  RIGHT
           (OR  LEFT  - IF YOU ARE MOVING BACK TO THE BEGINNING).   YOU  CAN
           SCROLL THROUGH THE FILE BY HOLDING DOWN EITHER THE "UP" OR "DOWN"
           ARROW  KEYS.   THE  SCREEN WILL SHIFT RIGHT  AS  THE  CURSOR,  OR
           CHARACTERS, ARE ENTERED IN COLUMN 80 - IT WILL SHIFT LEFT AS  YOU
           MOVE THE CURSOR (OR BACKSPACE) LEFT FROM COLUMN 1 (UNLESS YOU ARE
           AT THE BEGINNING OF THAT LINE).

           <HOME> KEY - MOVES THE CURSOR TO THE BEGINNING OF ITS LINE.

           <CTRL><HOME>  MOVES THE CURSOR TO THE UPPER LEFT OF  THE  CURRENT
           SCREEN.

           <END> KEY - MOVES THE CURSOR TO THE END OF ITS LINE.

           <CTRL><END>  MOVES THE CURSOR TO THE END OF THE LAST LINE ON  THE
           CURRENT SCREEN.

           <PAGEUP> KEY - MOVES THE CURRENT DISPLAY SCREEN "UP" BY 20 LINES.

           <CTRL><PAGEUP> KEY - TAKES YOU TO THE BEGINNING OF THE FILE.

           <PAGEDOWN>  KEY - MOVES THE CURRENT DISPLAY SCREEN "DOWN"  BY  20
           LINES.

           <CTRL><PAGEDOWN> KEY - TAKES YOU TO THE END OF THE FILE.

           <RETURN>  -  WILL INSERT A CARRIAGE RETURN/LINEFEED PAIR  AS  THE
           END-OF-LINE CHARACTERS.

           <CTRL> M - WILL INSERT A CARRIAGE RETURN ONLY AS THE  END-OF-LINE
           CHARACTER.

           <CTRL>  J - WILL INSERT A LINE WHICH HAS ONLY A LINEFEED  AS  THE
           END-OF-LINE CHARACTER.

           <CTRL>  Y - DELETES THE "WHOLE" LINE THE CURSOR IS  ON.   HOLDING
           THESE  KEYS  DOWN WILL KEEP SCROLLING UP THE  FILE  AND  DELETING
           LINES  AS IT GOES.  IF YOU USE THIS FEATURE, YOU SHOULD HAVE  THE
           CURSOR ON LINE ONE - THIS WAY YOU HAVE THE REST OF THE SCREEN  TO
           VIEW AS IT DELETES.  ON FAST COMPUTERS, YOU CAN GET DELETE  LINES
           VERY QUICKLY - SO BE VARY CAREFUL.

           <CTRL>  R  - WILL RESTORE THE "LAST" LINE  WHICH  WAS  PREVIOUSLY
           DELETED WITH THE COMMAND ABOVE.

           <ALT>  R - WILL RESTORE THE LAST BLOCK DELETED (IF  THAT  DELETED
           BLOCK WAS LESS THAN 10K) AT THE CURRENT CURSOR POSITION.

           <CTRL> N - INSERTS A LINE AT THE CURRENT CURSOR POSITIONS - WITH
           A CARRIAGE RETURN/LINEFEED END-OF-LINE.

           <ESCAPE>  KEY  - WILL EXIT THE EDIT MODE AND RETURN  YOU  TO  THE
           NORMAL  RECEIVE RTTY SCREEN.  IF THE FILE HAS CHANGED  SINCE  YOU
           LAST  SAVED,  YOU  WILL BE PROMPTED WITH THE  OPTIONS  TO  EITHER
           "SAVE AND EXIT" OR "EXIT WITHOUT SAVE".
                            (CONTINUED ON NEXT PAGE)
                                       16





           THE DISPLAY OF EACH LINE'S END-OF-LINE CHARACTER/S IS THE SAME IN
           THE EDITOR AS IT IS IN THE REST OF THE PROGRAM.  A "<" IN  COLUMN
           80 INDICATES A CARRIAGE RETURN/LINEFEED PAIR.  A "-" IN COLUMN 80
           STANDS FOR A CARRIAGE RETURN ONLY.  A "J" IN COLUMN 80  INDICATES
           A LINEFEED ONLY.  A "+" INDICATES A LINE THAT IS LONGER THAN, THE
           DISPLAYED, 79 CHARACTERS.

           IF  YOU HAVE A COLOR MONITOR, THE LINE WHICH HAS THE CURSOR  WILL
           BE DISPLAYED IN "YELLOW".



















































                                       17






























                                   AUTORTTY/AUTO-PIX

                                    KEY ASSIGNMENTS

                                       SECTION 2




































           FUNCTION  KEY ASSIGNMENTS FOR K8LC AUTORTTY PROGRAM  VERSION 1.X
              ------  <CTRL> & <ALT> KEY ASSIGNMENTS ALSO INCLUDED ------

           F1 - - - - - HELP/INFO --- OFFERS MULTIPLE SCREENS WHICH  EXPLAIN
           HELP/KEYS    ALL KEY  ASSIGNMENTS USED BY THIS PROGRAM.  THE INFO
                        GIVEN IS JUST A BRIEF DESCRIPTION OF THEIR USE.

           <SHIFT> F1 - FROM RECEIVE MODE, THIS WILL ALLOW YOU TO GO INTO  A
           "BREAK"      BREAK-XMIT  TRANSMIT MODE.  YOUR NORMAL  TYPE  AHEAD
                        WINDOW WILL BE SAVED AND THEN CLEARED.  YOU ARE  NOW
                        IN  TRANSMIT BREAK MODE AS THE LINE ABOVE  THE  TYPE
                        BUFFER  WINDOW  WILL INDICATE. YOU CAN  GO  DIRECTLY
                        FROM  THIS  TRANSMIT MODE TO THE NORMAL  TYPE  AHEAD
                        XMIT  MODE BY PRESSING <SHIFT> F2 OR <CTRL> T.   THE
                        NORMAL  EXIT WILL BE BY USING THE CTRL E (AT END  OF
                        TEXT  YOU WANT SENT) OR WITH F2 OR <CTRL>  R  (PRESS
                        TWICE  FROM TYPE XMIT GOES TO RECEIVE - PRESS  THREE
                        TIMES TO ABORT PIX BUFFER SENDING - SUCH AS  SENDING
                        A PIX OR FILL - AND RETURNS TO TYPE XMIT MODE).

           <CTRL> F1 -- BRINGS UP THE  FIRST, OF FIVE, PROGRAM CONFIGURATION
                        OPTION SCREENS.  THIS FIRST SCREEN COVERS:  THE BAUD
                        RATE AND RTTY MODE THE PROGRAM WILL STARTUP IN. YOUR
                        TIME  ZONE, WHETHER ITS DAYLIGHT SAVING OR  STANDARD
                        TIME AND LASTLY IF YOU WANT TO RETAIN A CR SENT WITH
                        A  CR/LF PAIR (IF SENT).  THE NEXT  SCREEN  INCLUDES
                        INPUT  OFTHE  SERIAL PORT YOU  ARE  USING  FOR  YOUR
                        INTERFACE   AND OTHER  VARIABLES  NEEDED FOR  PROPER
                        PROGRAM  OPERATION.  THE NEXT TWO SCREENS  HAVE  THE
                        DEFAULT   "PATHS"  USED  BY  THE   VARIOUS   PROGRAM
                        FUNCTIONS.   SCREEN 5 HAS TWO INPUTS WHICH ARE  USED
                        TO  SEND   SPECIAL INFO OR HOLIDAY GREETINGS  -  THE
                        FIRST IS SENT DURING THE WELCOME MESSAGE, THE SECOND
                        IS SENT DURING LOG-OFF.

           IMPORTANT:   <CTRL>F1 SHOULD BE THE VERY FIRST THING YOU DO AFTER
                        INSTALLING "AUTORTTY" ON YOUR COMPUTER.

           <ALT> F1 - - REDRAWS  THE RECEIVE  WINDOW AND STATUS  LINES.  IF,
                        FOR SOME REASON, YOUR RECEIVE WINDOW OR STATUS LINES
                        BECOME  MESSED UP, PRESSING <ALT> F1 SHOULD  CORRECT
                        THE PROBLEM. EVEN IF THE SCREEN GETS MESSED UP, YOUR
                        RECEIVE BUFFER SHOULD CONTAIN THE CORRECT DATA.

                        ALWAYS TRY THIS FUNCTION, ALONG WITH TRYING TO GO TO
                        SOME  OTHER  MODE AND RETURN, BEFORE  REBOOTING  THE
                        PROGRAM.  MOST OF THE TIME THIS FUNCTION SHOULD GIVE
                        SATISFACTORY RESULTS.

           F2 - - - - - IN RECEIVE MODE,  THIS COMMAND PUTS THE  PROGRAM  IN
           (OR CTRL R)  "LTRS" RECEIVE, JUST IN-CASE YOUR "28" GETS STUCK IN
           IN  RECV IT  "FIGS".   IN  TRANSMIT MODE  (IF  CURRENTLY  SENDING
           FORCES LTRS  YOUR  TYPE  AHEAD  BUFFER,  SENDING A PIX  OR  FILL)
                        THIS SELECTION WILL GIVE YOU  IMMEDIATE  BREAKOUT OF
                        TRANSMIT MODE.

                           (F2 INFO CONTINUED ON NEXT PAGE)



                                           1





                           === F2 INFORMATION CONTINUED ===

           IN XMIT IT   NOTE:  YOU  WILL HAVE TO  PRESS F2  TWICE  TO  ABORT
           FORCES END   NORMAL TYPE TRANSMIT  AND THREE TIMES TO ABORT A PIX
           XMIT  AND    OR FILL.   (A SAFE GUARD AGAINST  ACCIDENTAL  ABORT)
           RETURNS TO   ANY CHARACTERS LEFT IN THE XMIT BUFFER WILL BE  SENT
           RECEIVE      THE NEXT TIME YOU USE  XMIT  MODE.  TO AVOID SENDING
                        THE  REMAINDER  OF  A BUFFER - YOU  SHOULD  USE  THE
                        NORMAL  RETURN TO RECEIVE <CTRL> E.   USING THIS  AT
                        THE  END  OF  "EVERYTHING"  YOU PLAN TO  XMIT,   THE
                        PROGRAM WILL AUTOMATICALLY  SEND  A CARRIAGE  RETURN
                        LINEFEED PAIR,  THEN SCROLL UP THE TYPE AHEAD SCREEN
                        AND  PLACES  CURSOR.  YOU ARE THEN  READY  TO  START
                        ENTERING YOUR TEXT AGAIN.

           <SHIFT> F2 - GOES FROM RECEIVE MODE TO TRANSMIT MODE  -  OR  FROM
           (OR CTRL T)  TRANSMIT BREAK MODE TO  NORMAL TYPE  AHEAD  TRANSMIT
           RX TO TX     MODE.  THERE IS A CONFIGURATION OPTION ALLOWING YOUR
                        TYPE & MESSAGE PORT XMIT TO BE ECHOED TO THE RECEIVE
                        SCREEN AND PUT IN THE RECV BUFF.

           F3 - - - - - DISPLAYS  A  MENU  (ON  UPPER  WINDOW)   GIVING  THE
           LOAD PIX     OPTIONS FOR LOADING THE TRANSMIT (PIX) BUFFER.    IF
           XMIT BUFFER  LOADING  FROM  A  DISK  FILE,  YOU  -MUST- ENTER THE
                        COMPLETE FILESPEC (DRIVE\PATH\FILENAME) OF THE  FILE
                        YOU WANT LOADED IN THE TRANSMIT BUFFER.  IF YOU WANT
                        TO USE SOMETHING OTHER THAN THE DISPLAYED   DEFAULT,
                        JUST  USE  EITHER   BACKSPACE OR  DELETE  (DELETE  =
                        BACKSPACE IN RTTY PRG) TO CLEAR THE DEFAULT AND TYPE
                        IN  YOUR  INPUT.  THIS FUNCTION IS  AVAILABLE  WHILE
                        VIEWING  A DIRECTORY BROUGHT UP BY F5 -  (EDIT  VIEW
                        MODE)  WITH  "D" SELECTED.  YOUR OTHER  OPTIONS  ARE
                        LOADING   THE  TRANSMIT  BUFFER  WITH  THE   CURRENT
                        CONTENTS  OF THE RECEIVE BUFFER, OR FROM A  SELECTED
                        "BLOCK" OF THE RECEIVE BUFFER.

           <SHIFT> F3 - WHEN IN TRANSMIT MODE, THIS WILL SEND THE  DISKFILE
           XMIT PIX     THAT WAS LOADED WITH THE ABOVE F3 COMMAND.

           <CTRL> F3 -- ENTERS "AUTOEDIT" MODULE -- FOR EDITING THE TRANSMIT
           AUTOEDIT     (PIX) BUFFER.   THIS FUNCTION ALLOWS "FULL"  EDITING
                        OF THE BUFFER.  FOR COMPLETE DETAILS, SEE SECTION  1
                        MANUAL - PAGES 14-16.

           F4 - - - - - PROMPTS (ON LINE 17) FOR A  FILESPEC  (DRIVE:\PATH\-
           SAVE RECV    FILENAME)  THAT  WILL  BE USED TO  SAVE THE  RECEIVE
           BUFFER TO    BUFFER UNDER.  IF THE FILE  EXISTS,  IT WILL  ASK IF
           DISK         YOU WANT TO OVER-WRITE THE EXISTING FILE.

           <SHIFT> F4 - USE THIS WHEN YOU HAVE FINISHED ENTERING ALL OF YOUR
           (OR CTRL E)  INPUT IN THE TYPE AHEAD (OR BREAK) BUFFER.
                        SEE <CTRL> E FOR COMPLETE INFORMATION ON THIS ENTRY.

           F5 - - - - - DISPLAYS  THE EDIT/VIEW  MENU IN A  WINDOW  THAT  IS
           EDIT OF MSG  OPENED  UP IN  THE UPPER RECEIVE WINDOW.   YOU  WILL
           PORTS AND    STILL HAVE 6 LINES OF RECEIVE TEXT DISPLAYED.    YOU
           VIEW TX &    HAVE  THE  OPTIONS OF  EDITING YOUR  MESSAGE  PORTS,
           RX BUFFERS   VIEWING  THE  RECEIVE  AND XMIT  (PIX)  BUFFERS  AND
           & DIR        DISPLAYING A DIRECTORY.

                                           2





           F6 - - - - - DISPLAYS  INFO  (ON  LINE  25)  ABOUT  CLEARING  THE
           CLRS RX,TX,  VARIOUS BUFFS.  PRESS: "R" TO CLEAR RECEIVE - "T" TO
           PIX BUFFS    CLEAR TYPE AHEAD - "P" TO CLEAR THE PIX BUFFER.

           <CTRL> F6 -- PROMPTS  (ON LINE 17) FOR A FILESPEC  (DRIVE:\PATH\-
           DELETES  A   FILENAME)  WHICH WILL BE DELETED - IT WILL  ASK  FOR
           DISKFILE     VERIFICATION  BEFORE  ACTUALLY  DELETING  THE  FILE.
                        THIS  FUNCTION IS AVAILABLE WHILE YOU ARE VIEWING  A
                        DIRECTORY BROUGHT UP BY F5 (EDIT/VIEW MODE) WITH "D"
                        SELECTED.

           F7 - - - - - PROMPTS (ON LINE 17) FOR  BOTH THE  START  LINE  AND
           INPUT  PIX   END LINE  NUMBERS  USED FOR SENDING PART OF  A  FILE
           FILL LINES   (FILL).  TRANSMIT BUFFER MUST BE LOADED BEFORE  THIS
                        FUNCTION WILL OPERATE.

           <SHIFT> F7 - TRANSMITS THE  "FILL"  SELECTED WITH THE F7 FUNCTION
           XMIT ABOVE   ABOVE.  YOU  MUST BE IN  TRANSMIT  MODE  BEFORE THIS
           PIX FILL     THIS SELECTION WILL WORK. IF YOU WANT TO SEND TO THE
                        END  OF A PIX - PICK A LINE NUMBER GREATER THAN  THE
                        NUMBER IN PIX - I USE 999.

           F8 - - - - - BRINGS UP THE MENU FOR "BLOCK" MODE.   YOU HAVE  THE
           BLOCK MODE   OPTIONS  TO  MARK  A BLOCK EITHER IN  YOUR  KEYBOARD
           MARK BLOCK   (TYPE SENT) BUFFER OR RECEIVE BUFFER.   YOU CAN XMIT
           IN  RECEIVE/ THE  "MARKED" BLOCK,  WHILE IN  NORMAL  XMIT   (TYPE
           TYPE AHEAD   AHEAD)  MODE BY PRESSING <SHIFT> F8.  THIS XMIT WILL
           BUFFERS      HALT  NORMAL TYPE AHEAD SENDING - SO USE  THIS  MODE
                        WHEN  YOUR  TYPE BUFFER  INDICATES  ZERO.    ANOTHER
                        OPTION  ALLOWS  YOU  TO DELETE THE  BLOCK  FROM  THE
                        RECEIVE  BUFFER - OR SAVE  THE BLOCK TO  DISK.   YOU
                        CAN  ALSO PRINT THE  BLOCK  BY CALLING UP THE  PRINT
                        MODE (F9) AND SELECT "PRINT BLOCK".

           <SHIFT> F8 - TRANSMITS  THE SELECTED BLOCK -- THIS FUNCTION  ONLY
           XMITS BLOCK  WORKS WHEN YOU ARE IN TRANSMIT (TYPE AHEAD) MODE.

           F9 - - - - - DISPLAYS  THE PRINTING OPTION MENU.  YOU CAN  PRINT
           PRINTING     ALL  OR PART OF EITHER THE XMIT (PIX) BUFFER OR  THE
           OPTION       RECEIVE BUFFER.  IT ALSO HAS THE OPTION  TO  ENABLE
           MENU         "AUTO LINEFEED" WHICH WILL SPREAD  OUT THE OVERLINES
                        SO  YOU  CAN BETTER SEE A PROBLEM THAT  MAY  REQUIRE
                        EDITING.   YOU  CAN ALSO PRINT THE   "MARKED"  BLOCK
                        FROM THE RECEIVE BUFFER.   PRINTER ERRORS SHOULD NOT
                        NOT "HANG-UP" THE PROGRAM.

           <CTRL> F9 -- PROMPTS  (ON LINE 17)  FOR  THE FILESPEC  TO  ACCEPT
           AUTO-SAVE,   THE  CHARACTERS RECEIVED.   IF  YOU ARE PLANNING  ON
           SAVES  ALL   BEING  AWAY FOR A NUMBER OF HOURS - YOU  CAN  SELECT
           CHARACTERS   THIS  MODE TO HAVE  "EVERYTHING" RECEIVED IN A  DISK
           RECEIVED TO  FILE.   YOU  CAN  LATER GO THIS FILE  WITH   A  WORD
           A  SELECTED  PROCESSOR  AND EXTRACT ANY TEXT,  OR PIX  FILE,  YOU
           DISKFILE     WANT  TO  KEEP.  YOU WILL STILL BE  ABLE   TO   VIEW
                        THE  RECEIVED  TEXT  AND  USE  MOST  OF  THE   OTHER
                        FUNCTIONS  OF THIS PROGRAM, SUCH AS TRANSMIT,  WHILE
                        YOU ARE IN AUTO-SAVE.  COLOR MONITOR USERS:  LINE 25
                        (OPTION/INFO  LINE)   WILL HAVE  A  CYAN  BACKGROUND
                        INSTEAD OF WHITE WHEN IN AUTO-SAVE MODE.
                        MONO USERS:  LINE 25 SHOULD BE IN REVERSE VIDEO.

                                           3





           <ALT> F9 - - THIS  CLOSES THE FILE OPENED BY THE  ABOVE   COMMAND
           CLOSES A-S   AND RETURNS TO THE NORMAL PROGRAM MODE.

           F10 - - - -  IF YOU HAVE THE FULL AUTORTTY/AUTO-PIX PROGRAM:
           AUTO-PIX     PRESSING THIS KEY THREE TIMES, YOU WILL ENTER "AUTO-
           MODE         PIX" MODE. PRESSING THIS KEY THREE TIMES FROM WITHIN
                        "AUTO-PIX" WILL EXIT THAT MODE AND RETURN YOU TO THE
                        NORMAL PROGRAM MODE.  THIS MODE WILL NOT FUNCTION IF
                        YOU ARE IN AUTO-SAVE.

           <SHIFT> F10 - IF YOU HAVE THE FULL AUTORTTY/AUTO-PIX PROGRAM:
           PRINTS  LOG-  THIS  SELECTION WILL  PRODUCE A  PRINT-OUT  OF  THE
           FILE FROM     LOGFILE CREATED BY THE "AUTO-PIX" MODE.  YOU SHOULD
           AUTO-PIX      RUN THIS ONCE A MONTH  TO  KEEP A RECORD OF  SYSTEM
           LOGFILES      USAGE.   COPY  THE  FILES TO  A   FLOPPY  FOR  SAFE
                         KEEPING,  THEN  DELETE THE FILES FROM THE   LOGFILE
                         DEFAULT  PATH.    THIS WILL SPEED-UP  THE  LOG  OFF
                         PROCESS,  ESPECIALLY IF YOU ARE USING  A FLOPPY FOR
                         THE DEFAULT LOGFILE PATH.

           <ALT> F10 -- SHELLS  OUT  TO  THE PROGRAM THAT IS  NAMED  IN  THE
           SHELL TO     ENVIRONMENT  VARIABLE  "COMSPEC" - THIS  IS  USUALLY
           "COMSPEC"    YOUR  VERSION  OF MS-DOS  UNLESS YOU  ARE  USING  AN
                        ALTERNATE  OPERATING  SYSTEM.   IF  YOU  KEEP   YOUR
                        "SHELL"  TIME LESS THAN 20 MINUTES -  YOU  SHOULDN'T
                        LOSE  ANY  RECEIVE  CHARACTERS  (BASED  ON  100  WPM
                        BAUDOT).   WHEN  IN  THE SHELL  YOU  CAN  RUN  OTHER
                        PROGRAMS  (IF  THEY  WILL FIT IN  MEMORY)  OR  OTHER
                        COMMAND LINE OPERATIONS.































                                       4





            <CTRL> & <ALT> KEY  ASSIGNMENTS FOR "AUTORTTY" PRG VERSION 1.X

           CTRL B - - - TOGGLES  THROUGH THE VARIOUS BAUD RATES   SUPPORTED
                        BY  THIS PROGRAM.  THOSE ARE 45 - 75 - 110 -  135  -
                        300.   YOU  MUST  BE IN RECEIVE  MODE  TO  USE  THIS
                        FUNCTION.

           CTRL V - - - TOGGLES  BETWEEN BAUDOT AND ASCII MODES.   THE  DEF-
                        AULT ASCII MODE USES THE  8 BIT  DATA FORMAT.    YOU
                        CAN  SWITCH BETWEEN ASCII8 AND ASCII7 BY  USING  THE
                        CTRL A SHOWN BELOW.

           CTRL A - - - IN  ASCII  MODE - THIS TOGGLES  BETWEEN  ASCII8  AND
                        ASCII7.

           CTRL O - - - PRESS TO EXIT PROGRAM -- YOU ARE PROMPTED  (ON  LINE
                        25) TO EITHER PRESS CONTROL U  (TO EXIT PROGRAM  AND
                        RETURN  TO DOS) OR TO PRESS ANY OTHER KEY TO  RETURN
                        TO PROGRAM.

           CTRL P - - - TOGGLES PRINTER ECHO ON/OFF.   THIS CAN BE SELECTED
                        DURING  NORMAL RECEIVE  MODE, AS WELL AS,  WHEN  YOU
                        ARE  IN ANY XMIT MODE.   WHEN ON, ALL RECEIVED  TEXT
                        IS ECHOED TO THE PRINTER (USING ANY PORT -SERIAL  OR
                        PARALLEL-    )   YOU   SELECTED    DURING    PROGRAM
                        CONFIGURATION.  IF YOU TAKE THE PRINTER OFF LINE  OR
                        IT RUNS OUT OF PAPER, OR ANY OTHER MALFUNCTION,  THE
                        PROGRAM WILL -AUTOMATICALLY- TURN OFF THE PRINT ECHO
                        FEATURE.  THIS KEEPS THE PROGRAM FROM "HANGING UP".

           NOTE:  IF  PRESSING  THIS KEY DOES  -NOT-  GIVE  THE  PRINT  ECHO
           MESSAGE  ON EITHER LINE 16 OR 18 (RECV OR XMIT) YOUR PRINTER  MAY
           BE OFF LINE (OR NOT TURNED ON) OR MAYBE OUT OF PAPER OR ANY OTHER
           ERROR THAT WILL NOT ALLOW PRINTING.  YOU WILL GET A "BEEP" TO LET
           YOU KNOW SOMETHING IS WRONG.

           CTRL F - - - ALLOWS LOADING AND SENDING OF A DISKFILE (PIX)  FROM
                        WITHIN  THE  NORMAL  TRANSMIT  TYPE  AHEAD   BUFFER.
                        TO USE THIS FUNCTION:  PRESS CTRL F  (THIS  DISPLAYS
                        Ÿ)  THEN ENTER  THE  FILESPEC  (DRIVE\PATH\FILENAME)
                        PRESS CTRL F  (THIS DISPLAYS ANOTHER Ÿ).   NOTE:  DO
                        -NOT- HAVE ANY SPACES BETWEEN THE CTRL F CHARACTERS.
                        YOU  MUST  INCLUDE DRIVE AND ANY  SUBDIRS.   IF  THE
                        TRANSMIT HAS CAUGHT UP TO YOU AND YOU BEGIN ENTERING
                        DATA AFTER THE FIRST CTRL F  --  THEN YOU DECIDE YOU
                        DO  NOT WANT TO SEND A FILE AFTER ALL - JUST  BACKUP
                        TO  THE  FIRST CTRL F AND ENTER THE SECOND  CTRL  F.
                        WHEN  THE PROGRAM ENCOUNTERS THE SECOND CTRL F -  IT
                        TRYS  TO OPEN THE FILE TO SEND - NOT FINDING  ONE  -
                        IT, HARMLESSLY, EXITS BACK TO THE NORMAL TYPE  AHEAD
                        MODE, JUST LIKE BEFORE YOU ENTERED THE FIRST CTRL F.

           IMPORTANT:   THEY MUST BE USED IN PAIRS.   DON'T WRAP A  FILENAME
           TO ANOTHER ROW, ENTER <RETURN> THEN THE COMPLETE ENTRY

           YOU CAN ENTER ANY NUMBER OF DISKFILES IN THIS MANNER,  EACH  WILL
           BE  LOADED AND SENT AS IT COMES UP IN THE TYPE  AHEAD BUFFER.

           EXAMPLE:  ŸB:1234-1P.PIXŸŸB:1235-1P.PIXŸ - SENDS TWO FILES.
                        (<CTRL> F INFO CONTINUED ON NEXT PAGE)
                                           5





           CTRL F - - - (CONTINUED):

           IF YOU ARE GETTING NEAR COLUMN 60,  ENTER <RETURN> TO GO TO
           NEXT ROW BEFORE ENTERING ANOTHER SELECTION.

           EXAMPLE:  THIS IS A TYPE AHEAD LINE BEFORE 1ST CRTL F<RETURN>
                     ŸC:\NEW-PIX\GUD-NUDE.PIXŸ

           NOTE:  NEVER ALLOW A LINE WRAP BETWEEN THE TWO CTRL F'S

           CTRL G - - - SENDS THE "BELL" - IT IS DISPLAYED WITH THE  "MUSIC
                        NOTE".

           CTRL D - - - SENDS THE DATE/TIME - IT IS DISPLAYED  WITH  "SUN"
                        CHARACTER.

           CTRL I - - - TRANSMITS A CWID - IN TRANSMIT MODE.

           CTRL R - - - SEE INFORMATION FOR F2.

           CTRL T - - - SEE INFORMATION FOR <SHIFT> F2

           CTRL Y - - - CLEARS A LINE FROM EITHER TYPE AHEAD OR MESSAGE PORT
                        EDIT.

           CTRL E - - - ENTER  THIS AT -END- OF  ALL TEXT YOU WANT  TO  SEND
           (OR<SFT>F4)  (INCLUDING  ANY  MESSAGE  PORTS, YOU  ARE  USING  TO
                        INDICATE  THE END OF THE CURRENT  XMISSION.    AFTER
                        THIS  CHARACTER  IS ENTERED THE  PROGRAM  WILL   NOT
                        ALLOW  ANYMORE  CHARACTERS  TO  BE  ENTERED  IN   HE
                        KEYBOARD  BUFFER.   YOU CAN USE THE  <BACKSPACE>  OR
                        <DELETE>   KEYS  TO REMOVE  THIS   "CHARACTER"   AND
                        AGAIN  INPUT MORE TEXT OR MESSAGE PORTS IN THE  TYPE
                        AHEAD BUFFER.  WHEN  THE  XMIT  ROUTINE   ENCOUNTERS
                        THIS CHARACTER, THE PROGRAM WILL SCROLL UP THE  TYPE
                        AHEAD BUFFER WINDOW, PLACE CURSOR  AT THE  BEGINNING
                        OF  THE LINE (READY FOR YOUR NEXT INPUT) AND  RETURN
                        TO THE RECEIVE MODE.

           CTRL M - - - ENTERING <CTRL> M  TRANSLATES TO A CARRIAGE RETURN/-
                        LINEFEED PAIR IN TYPE AHEAD, BREAK AND MESSAGE  PORT
                        BUFFER INPUT.

           CTRL J - - - ENTERING <CTRL> J  ALSO  TRANSLATES  TO  A  CARRIAGE
                        RETURN/LINEFEED  PAIR  IN  TYPE  AHEAD,  BREAK   AND
                        MESSAGE PORT BUFFER INPUT.


           ========== KEYS USED INSIDE EDIT/VIEW AND BLOCK MODES ==========

           HOME/CTRL Q --- TAKES YOU BACK TO THE  BEGINNING  OF THE  BUFFER
                           YOU ARE IN. THIS KEY HAS NO EFFECT WHEN IN  TYPE
                           SENT BUFFER IN BLOCK MODE.

           END/CTRL Z ---- TAKES YOU TO THE END OF THE BUFFER YOU  ARE  IN.
                           THIS  KEY HAS EFFECT WHEN IN TYPE SENT BUFFER  IN
                           BLOCK MODE.


                               (CONTINUED ON NEXT PAGE)
                                           6





           PAGEUP/CTRL W - MOVES UP ONE  SCREEN (PAGE) IN THE BUFFER.   THIS
                           KEY  HAS NO EFFECT IN TYPE SENT BUFFER  IN  BLOCK
                           MODE.

           PAGEDN/CTRL X - MOVES DOWN ONE SCREEN (PAGE)  IN  THE  BUFFER.
                           AGAIN, THIS KEY HAS NO EFFECT IN TYPE SENT BUFFER
                           IN BLOCK MODE.

           <ESC> ESCAPE -- PRESSING THIS KEY WILL EXIT YOU FROM THE  BUFFER
                           YOU ARE IN BACK TO EITHER EDIT/VIEW OR BLOCK MODE
                           MENU.
           NOTE:  USING THIS KEY TO LEAVE A BUFFER IN BLOCK MODE WILL  -NOT-
           CREATE A MARKED, GLOBAL, BLOCK YOU CAN USE.


           ============== KEYS USED EXCLUSIVELY IN BLOCK MODE ==============

           <ARROW KEYS> - USE THE ARROW KEYS  TO PLACE  THE  CURSOR  ON  THE
                          CHARACTER  THAT IS USED FOR THE START AND  END  OF
                          YOUR BLOCK.

           CTRL  B  --  TOGGLES  THE -BEGINNING-  (TEMPORARY)  BLOCK  MARKER
                         WITHIN A BUFFER.  IF THE MARKER IS CLEAR - IT  WILL
                         MARK  (SET)  THE BEGINNING OF THE BLOCK.    IF  THE
                         MARK  IS  SET - IT WILL BE CLEARED  (REGARDLESS  OF
                         ITS LOCATION IN THE BUFFER).

           CTRL  E - - TOGGLES THE -END- (TEMPORARY) BLOCK MARKER  WITHIN  A
                        BUFFER.   IF  THE  MARKER IS CLEAR -  IT  WILL  MARK
                        (SET)  THE  END OF A BLOCK.  A SET  MARKER  WILL  BE
                        CLEARED BY PRESSING IT.

           HAVING   THE  ABOVE KEYS TOGGLE IS HANDY IF YOU  WISH  TO  CHANGE
           A   MARKER  AND DON'T WANT TO HAVE TO MOVE OFF TO  ITS   LOCATION
           TO  CLEAR  IT.  IF YOU SEE A  PLACE THAT SHOULD BE  THE  USED  AS
           MARKER,  BUT  YOU  ALREADY   HAVE  ONE  SET,  JUST  PRESS   BLOCK
           MARKER  KEY  (EITHER  <CTRL> B OR <CTRL> E) THE  ORIGINAL  MARKER
           IS  CLEARED.    IF  THE CURSOR IS ON THE SPOT YOU  WANT  THE  NEW
           MARKER  SET  - JUST  PRESS WHICH-EVER MARKER KEY THAT HAS  TO  BE
           SET.  IF THE CURSOR ISN'T ON THE NEW LOCATION, MOVE IT THERE THEN
           PRESS THE TEMPORARY BLOCK MODE MARKER KEYS <CTRL> B  OR <CTRL> E.


            ============ SPECIAL COMMANDS FOR MESSAGE PORT #1 ============

           <ALT> C - - CLEARS   MESSAGE  PORT  #1 -  CONFIRMS  YOUR   CHOICE
                       BEFORE ACTUALLY CLEARING THE PORT.

           <ALT> A - - ADDS  A  CALL  SIGN  TO  MESSAGE  PORT #1 -  DO   NOT
                       HAVE   ANY SPACES  IN  YOUR INPUT.  (PROMPTS ON  LINE
                       17)  THE  PROGRAM ADDS A TRAILING SPACE.

           <ALT> R - - REMOVES  A  CALL FROM MESSAGE PORT #1 - AGAIN DO  NOT
                       HAVE  ANY SPACES IN YOUR INPUT. (PROMPTS ON LINE  17)
                       IF THE CALL SIGN CAN NOT BE FOUND, IT WILL INFORM YOU
                       ON LINE 17.


                        (MESSAGE PORT INFORMATION ON NEXT PAGE)

                                           7





                                 --- MESSAGE PORTS ---

           ALT 1  THRU  ALT 0 -- (DO NOT USE KEYS ON KEYPAD)  USE TO  SELECT
           MESSAGE  PORT,  TO  SEND, IN TYPE AHEAD OR  BREAK  BUFFER.   WHEN
           PROMPTED  FOR MESSAGE PORT NUMBER IN "EDIT MESSAGE PORT" MODE  --
           JUST  USE THE NORMAL 1 THRU 0.  AGAIN,  DO NOT USE <ALT>  OR  THE
           KEYPAD KEYS, FOR EDITING.  YOU  CAN  NOW GIVE,  AS  PART OF  YOUR
           INPUT,  ANOTHER MESSAGE PORT  NUMBER  (USING  THE <ALT> KEY  WITH
           THE NORMAL NUMBER KEYS (NOT KEYPAD KEYS).

                                 ---------------------

           AS YOU WILL SEE, I HANDLE END-OF-LINE DISPLAY A BIT  DIFFERENTLY.
           COLUMN  80  WILL HAVE:  "<" FOR A CR/LF, "-" FOR A CR  ONLY,  "J"
           FOR   A   LINEFEED AND  A "+" FOR AN EXTENDED LINE (ONE  THAT  IS
           LONGER THAN 79 COLUMNS.  I CHOSE THIS METHOD SO YOUR RECEIVED PIX
           WOULD BE AS CLEAN AS POSSIBLE, ON THE SCREEN.

                                           WALTER E. BESS, JR.  K8LC
                                           PRECISION ELECTRONICS
                                           1525 KARIN STREET
                                           IRONTON, OHIO   45638
                                           PHONE:  1-614-532-6111





































                                           8