COMMBAT
=======

Thank your for downloading COMMBAT.  COMMBAT provides communication
capabilities for batch files. Since environment variables are used
as input and output, the CONFIG.SYS file has to be changed to reserve
more space for them.  To do this, add the following line to CONFIG.SYS :

	      shell=c:\command e:640 /p

If you find it useful and decide to continuously use it, please send $10
to my address below.  If you want the source, please send $5 more for
shipping and handling.

		    Eddie Tang
		    128 Queen Street South
		    P.O. Box 42096
		    Mississauga, Ontario
		    Canada	L5M 4Z4



Invocation
==========

          commbat /Ox [/Cn] [/E] [/R]

             /O specifies type of operation
		where x = s : send a string only
			= r : receive a string only
			= b : send and then receive a string

             /C specifies COM port n to be used
		where n = 1 to 2

	     /E to suppress error message display

	     /R to convert some control characters to string
		e.g. convert [CR][LF] to "\r" and "\n"




Environment variables
=====================

1. _CONFIG : Port configurations.  COMMBAT will look at this environment
	     variable to determine the configuration of the port.

     _CONFIG=Timeout,Speed,Parity,Data,Stop,DTR,RTS

         Timeout : Receive timeout in sec (0-9999)
         Speed   : 192/96/48/24/12/6/3    (def : unchanged)
         Parity  : (o)dd/(e)ven/(n)one    (def : unchanged)
         Data    : 5/6/7/8                (def : unchanged)
         Stop    : 1/2                    (def : unchanged)
         DTR     : n to drop it after closing port
         RTS     : n to drop it after closing port

     0 timeout is the same as no timeout which is the default
     value.

     If DTR/RTS are not specified, they will be left ON
     after closing the COM port.

     Examples :

     a.  _CONFIG=10,96,n,8,1,n,n
	     10 seconds receive timeout
	     9600 baud, 8 data bits, no parity, 1 stop bit,
	     drop DTR and RTS after closing port

     b.  _CONFIG=,,n,8,1,n,y
	     No receive timeout
	     Speed unchanged, 8 data bits, no parity, 1 stop
	     bit, drop DTR but leave RTS on



2. _SEND : String to be transmitted.  COMMBAT will send this string to
	   the specified COM port.  The maximum length of the string is
	   128 characters.  Control characters may be embedded in the string.

             Control characters and meaning

             \r     : Carriage Return
             \n     : Line Feed
             \f     : Form Feed
             \b     : Back Space
             \a     : Bell
             \v     : Vertical TAB
             \t     : Horizontal TAB
             \g     : '>'
             \l     : '<'
	     \xyy   : Hex code

     Examples

       _SEND=test message \x41B\x43\r\n

       Actual message sent will be :

              test message ABC[CR][LF]
			   ||| |   |
		    \x41---||| |   |
		       B----|| |   |
		    \x43-----| |   |
		      \r-------|   |
		      \n-----------|

       The length of this string is 18.


3. _TRIGn  : Strings to trigger start/end of reception.  Up to 4 (1 to 4)
	     receive triggers may be specified

     _TRIGn=SS,ES,MAX

        where
            n   = 1 to 4
	    SS	= Start sequence. Sequence to start reception of data.
	    ES	= Ending sequence. Sequence to stop reception of data.
	    MAX = Maximum number of characters to be received after SS

     Start sequence is not mandatory. But either ES or MAX must be present
     to determine the terminate condition.  If both are present, ES takes
     the precedence.  The maximum length of each sequence is 10 characters.

     Examples

	Incoming message for all the following examples :

		    QQQABC1234XYZRRR


     a. _TRIG3=ABC,XYZ,6

	When COMMBAT returns :

	_RCV=ABC1234XYZ

	Note that Max count (6) is not applicable since ending sequence
	is specified.


     b. _TRIG3=,XYZ

	When COMMBAT returns :

	_RCV=QQQABC1234XYZ

	The ending sequence will be included in the receive string _RCV.


     c. _TRIG3=,,6

	When COMMBAT returns :

	_RCV=QQQABC

	COMMBAT gets the first 6 characters it receives from COM port and
	stores in _RCV since no start sequence is specified.


     d. _TRIG3=ABC,,6

	When COMMBAT returns :

	_RCV=ABC1234XY

	COMMBAT gets 6 more characters after start sequence is detected.


     e. _TRIG3=ABC,,3
	_TRIG4=ABC,XYZ

	When COMMBAT returns :

	_RCV=ABC123

	TRIG3 comes first.


     f. _TRIG3=ABC,,10
	_TRIG4=ABC,XYZ

	When COMMBAT returns :

	_RCV=ABC1234XYZ

	TRIG4 comes first.


     g. _TRIG3=,,15
	_TRIG4=ABC,XYZ

	When COMMBAT returns :

	_RCV=QQQABC1234XYZRR

	Start seq of TRIG3 comes first. Therefore ending sequence of
	TRIG3 is used.


     h. _TRIG3=BC,XYZ
	_TRIG4=ABC,XYZ

	When COMMBAT returns :

	_RCV=BC1234XYZ

	Ending sequence detected at the same time. Trigger with smaller
	number (TRIG3) is chosen.



4. _RCV    : The received string.  COMMBAT will put the string received
	     in this environment variable.  Both start and ending
	     sequence will be included.  The maximum length of the
	     received string is 128.  If /R is specified in the command
	     line, the following codes will be converted to the corresponding
	     2-character string on the received message :

             0x0d (Carriage Return) -> \r
             0x0a (Line Feed)       -> \n
             0x0c (Form Feed)       -> \f
             0x08 (Back Space)      -> \b
             0x07 (Bell)            -> \a
             0x0b (Vertical TAB)    -> \v
             0x09 (Horizontal TAB)  -> \t
             0x3c ('<')             -> \l
             0x3e ('>')             -> \g

     Example : If TEST MESSAGE[CR][LF] is received and /R is specified in
	       the command, _RCV will contain :

	       _RCV=TEST MESSAGE/r/n