This program is Shareware, and
may be distributed freely, so-
long as the original archive
is not tampered with.

I claim no responsibility for
any damages incured by these
programs.
                      - Author





























                               Lcom v1.05

                                    ù

                         Written by John Bushnell

































        I.      Overview of supplied files
       II.      Setting up Lcom for use
      III.      Using the program
       IV.      Author's Notes

                A.  Getting Help
                B.  The Terminal
                C.  Controlling The Modem
                D.  General Defaults (Controlling Variables Within the Program)       
                E.  Telephone (Dialing) Directory
                F.  Telephone Directory Special Terminal Service Keys
                G.  The ScrollBack Buffer
                H.  Macros (In General)
                I.  Macros (Incoming)
                J.  Translate Tables
                K.  Ascii Tables
                L.  Transfer Protocol Areas
                M.  Shelling To Dos
                N.  Changing Video Modes (screen length, width, color/b&w, etc)
                O.  Controlling the Lcom Menus (sizes, colors, positions, etc)
                P.  Zooming
                Q.  Viewing the DOS screen
                R.  Saving the screen (record screen)
                S.  Printing The Screen
                T.  Log to File (protocol:ascii download)
                U.  Log to Printer
                V.  Sending the modem init string manually
                W.  Hanging up the modem
                X.  Exiting the program

         v1.01+

                Y.  Split-Screen Chat-Mode (cooinsidentally alt-Y)
                Z.  The Notes feature

         v1.02+

                ** not yet added to documentation **

         v1.03+

                ** not yet added to documentation **

         v1.04+
                
                ** not yet added to documentation **

         v1.05+
        
                ** not yet added to documentation ** (terrible, i know)


 
      Appendix A - TroubleShooting
                










 



                       ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
                       ³OVERVIEW OF SUPPLIED FILES³
                       ÀÄÄÄÄÄÄÄÄÄÄÄÄÄIÄÄÄÄÄÄÄÄÄÄÄÄÙ


        Lcom comes with five executable files:

             INSTALL.BAT  - installs Lcom for use from the ground up.  This
                            batch file *must* be run first if this is not
                            an upgrade from a previous version.

             UPGRADE.BAT  - run this batch file instead of INSTALL.BAT if you
                            are upgrading from a previous version of Lcom.
                            after running UPGRADE.BAT, you will be prompted
                            with furthur instructions.



                LCC       - The Lcom Configuration program.  You use this to
                            install Lcom initially (this will be the first
                            program you run (after either the INSTALL.BAT or
                            UPGRADE.BAT files) and whenever you wish to change
                            an option within the Lcom.

                LC .EXE   - Lcom.  The main program.

                LCV.EXE   - The Lcom Video Configuration program.
                            Change your video mode to each video mode you
                            would ever want to run Lcom in, and run LCV in
                            each so that Lcom can know a little information
                            about the modes it will be used in.  Lcom will
                            run in any screen size, from 40x25 to 200x127.







                        ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
                        ³SETTING UP LCOM FOR USE³
                        ÀÄÄÄÄÄÄÄÄÄÄÄIIÄÄÄÄÄÄÄÄÄÄÙ


        To setup Lcom for use, refer to the INSTALL.DOC file for detailed
instructions on the most basic configuration to the most comprehensive.












                            ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
                            ³USING THE PROGRAM³
                            ÀÄÄÄÄÄÄÄIIIÄÄÄÄÄÄÄÙ





                              A. GETTING HELP





Help is available from any part of the program through the help key; defaulted
to be F1.  After pressing F1, help information specific to the area of the
program which you are in will be shown.  Pressing F1 again will give you help
on the help window.  In short, the arrow keys allow you to move up and down
through the help material (if more than one page exists) and the escape key
leaves.





                            B. THE TERMINAL





When you first run Lcom you enter the terminal window.  From here, all the 
other windows which you can access while using Lcom, such as the telephone
directory and macros, are available by pressing the appropriate keys.

The terminal has several options which you can select.  These include the
emulation which is being used to translate commands over the modem and
whether or not characters you type are echoed on the screen or not.  These
options can be set in two places.  The first is in the config program; Changes
made here are permanent.  The second is through the General Defaults window.
Most changes made from this window are lost when you rerun the Lcom.  You
would normally change the settings in the config program if you want them to
be still set every time you run Lcom.






                       C. CONTROLLING THE MODEM
   





The Line Settings window (ALT-L) is the window which shows you what your modem
is currently configured to, and, allows you to change that configuration.
Items that can be changed include the baud rate, parity, character length,
stop bits, com port, and com port base address.  You move to each of the
different items that can be changed by using the right and left arrow keys.
To change the value of the currently highlighted option, press the up or down
arrow keys.

All of the items in this window can also be changed in the config program;
however, be forewarned that if you change the com port in the config program,
you must (also) change the com port base address to correspond to your (new)
com port.





                          D. GENERAL DEFAULTS





The general defaults window is a window inside of the Lcom program which allows
you to temporarily change options which Lcom uses while it is running.
Examples include the terminal emulation, duplex, init string (this will be
changed permanently), and how long the dial waits for a connection before
giving up.





               E. TELEPHONE DIRECTORY (DIALING DIRECTORY)





The Lcom telephone directory (defaulted to be the ALT-D key) is the method by
which you store the phone numbers of people you wish to call, and, to call and
connect to those numbers.  Lcom supports up to 65,000 numbers (infinite for all
intents).  You can move throughout the different numbers using the up and down
arrow keys, as well as the page keys and the home and/or end keys.

The telephone directory operates off of a command line system; that is, where
you type in any command you wish to use in verbose; i.e. "sort".  There are
some 'givens', however.  These include:

      - Pressing return on a blank line issues the dial command.  If any
        numbers are marked (in the que) they are dialed, otherwise, the
        number you are currently on is dialed.

      - Pressing the space-bar issues the "mark" command; which adds the
        current entry into the que.

      - ALT-E issues the EDIT command; which edits the current number.

      - Typing in a word which is not a command, such as "whatever", is then
        assumed by Lcom to be a search string.  A search for that word is
        started, and if it is found, the highlighted bar is moved to that
        number.  This is useful for quickly finding certain number.  If you
        had a number which, for instance, you labeled as "John's BBS", you
        could just type in "john" and Lcom would go directly to that number.



Lcom has many commands available for your use in the telephone directory.  You
can type them out manually or simply type the RIGHT ARROW (or '/' key) and
thumb through the list of commands and choose the one you want; either with the
enter key which executes the command immediately, or the space bar which types
out the command for you up to the point where you would press enter, but does
not.

Here is a complete listing of the dialing directory commands:
-------------------------------------------------------------

        dial ù This dials a number or numbers which are specified after the
               command, in the que; or if neither of these exist, the currently       
               highlighted number.

        once ù This command is the same as the dial command, except that the
               dial command repeats after an unsuccessful attempt.  The once
               command dials the specified number(s) once, and then stops.

        edit ù (Also ALT-E) this command pulls you into the telephone edit
               window.  From there, you can enter in things such as the
               phone number's name, number, and baud rate.

        goto ù This allows you to immediately go to the number of your choice.
               You can either tell the telephone directory to go to a specific
               number (i.e. "goto 10") or a specific name.
               (i.e. "goto compuserve")  If you are going to use the second
               method, then you can (in almost all cases) drop the "goto".

        mark ù Marking a number "adds it to the que".  This means, that it
               labels that number such that when you dial, all other labeled
               numbers are dialed one after another until a connection.

      unmark ù After marking a number, you may wish to un-mark it.

        find ù This command is the same as the goto command; except that
               it searches for the number you want assuming the string you
               pass it is part of the name at all times.  With goto, if
               you were to say "goto 10", it would assume you meant the 10th
               number; whereas find assumes you wanted to find the number
               which had a 10 in the name.  i.e. "...10... bbs".
               format: "find <whatever>".

        copy ù This command allows you to duplicate a number.
               "copy 10" would copy the number you are currently highlighting
               to entry #10.

       clear ù Erases all information inside of the number indicated.

      delete ù This deletes the "slot" held by the number you deleted.
               see: insert.

      insert ù Lcom does not come with any "slots" for you to put your phone
               numbers in.  You have to create them as you need them.  This
               is done by the "insert" command.  Hypothetically, this should
               be the first command you ever type in the dialing directory.
               After inserting a number, you would then want to edit it with
               the edit command.

        swap ù If you ever want to swap one number with the place held by
               another, use the swap command.  "swap 10" will swap #10 with
               the currently highlighted number.

        sort ù You can sort your phone list by any of several methods.
               These include name, number, and activity.  If you don't specify
               a field, (i.e. sort 10-20) then Lcom sorts the entire list.  If
               you wish to sort in reverse order, then specify the field in 
               reverse. (i.e. sort 20-10).

        open ù You may have more than one telephone directory.  If so, you
               can load a new one or edit an old one by typing "open fname".
               "LC" is the standard dialing directory file.  Therefore, if you
               wish to open your original dialing directory, you would type
               "open lc"

        help ù Pulls up local help on the telephone directory.  This is
               also the help key (F1).

        zoom ù Expands or unexpands the telephone directory window.  This is
               also the zoom key (F5).  Sometimes even in Zoomed mode there
               is more information to be displayed.  This information can
               be displayed by moving over right using the ctrl-right-arrow
               key.  This key also works while not zoomed.

         out ù This command is purely for your own convenience.  If you ever
               wish to send a number or numbers over the modem, i.e. to tell
               a friend the number to a certain bbs, you can simply use the
               out command and Lcom types it for you.

       reset ù There is information stored in every number in the telephone
               directory.  Some of this information is visible to you, such
               as the number of times you've called a certain BBS; other
               information is not, such as the activity index.  All of these
               can be reset with the "reset" command.  This does *not*
               erase important information such as the number or name of that
               entry.  

        exit ù verbose equivalent to the escape key.


The format by which you use these commands follows these rules:

    "dial"        ù A command with no other information specified assumes that
                    you wish that command to apply to the currently highlighted
                    number.  If you were on entry #1, this command would dial
                    that entry.

    "dial 1"
    "dial 1,2,3"  ù Any numbers after a command represent the numbers that
                    the command is to apply to.

    "dial john"   ù If a non-number is specified, Lcom will attempt to figure
                    out which number you were referring to, and use the
                    appropriate number if found.

    "dial 1-20"   ù Specifying a field is done using a dash.  If you ever want
                    to perform the function in reverse, specify in the field
                    in reverse, i.e. "dial 20-1"

    "dial 100-"   ù (100 - end)    Dashes ( - ) signify a field. (as stated
    "dial -100"   ù (1 - 100)      above).  If you leave out the first part
    "dial - "     ù (1 - end)      of a dash statement, that piece is assumed
                                   to have been a '1'.  If you leave out the
                                   second part, that part is considered to be
                                   the end of the telephone directory, thus,
                                   the statement "dial 10-" will dial all
                                   numbers from #10 to the end of the telephone,
                                   dial "-10" from #1 to #10, and, "dial - "
                                   will dial all numbers.

                  

combinations are accepted for most commands:

    "dial 1,2,3,john,1-20"

*Note:  There are several commands which allow only specific types of entry
        specifications.  One such example is the sort command.  The only two
        possibilities for the sort command is just "sort", or "sort <field>",
        i.e. "sort 1-10", or "sort 10-1", but "sort 1,2,3" would be invalid.

Many times, it is not necessary to list the entire command.  If you list only
part of a command, such as "di" instead of "dial", or even "d", lcom will
assume you meant dial.  In the case of similar commands, such as "out" and
"once", if you say "o", lcom will assume the command you wanted was the first
one in the list.

If you are having trouble getting started with the telephone directory, try
these steps:  type "ins<ENTER>", then ALT-E.





THE EDIT WINDOW

        After invoking the edit command, a window will pop up which will
display all the information which you can change for the number you are
editing.  To edit a certain item, type the letter which corresponds to it.
For example in the case of the baud rate, the letter that corresponds to
it is a 'B'.  This is found directly below the baud.

        38400
         ^
         ³
         B

For most applications, you will need only to edit the name and phone number
of a new BBS, as the other information would most likely be the same as
it is defaulted.





WHEN DIALING, AND THE DIAL WINDOW

Lcom has a unique style of dialing.  You need not be *in* the dial window
to be dialing.  As Lcom is configured, when you start a dial the dial window
will not appear.  You will be in what is called "roam mode".  In roam mode,
you can move throughout Lcom while it is dialing.  If you type ALT-D to
go into the dialing directory, you will instead go into the "dial window".
Here you will find a list of various commands that you can type to do different
things while dialing.  Options include: going to the next number in the que
(n) redialing the previous number (p), and redialing the same number (r).
If you press ESCAPE from the dialing window, you abort the dial.  You can,
however, return back to the terminal (still dialing) and still be in roam mode.
This is done by pressing ENTER in the dialing window.  All of the commands
which are available in the dialing window are also available in the terminal.
Because of this, you can simply press ESCAPE in the terminal to stop the dial,
and in the same way you can press 'N' to go to the next number.

You can, if you wish, configure Lcom to automatically pull up the dialing
window when you first start to dial.  This is the format most communication
programs use, and in Lcom it is present simply as an aid you can use to view
your options.  Think of it as a help menu.






            F. TELEPHONE DIRECTORY SPECIAL TERMINAL SERVICE KEYS






There are two keys available from the terminal which perform several dialing
functions.  The first, which is defaulted to be the ALT-R key, is redial.
When you press this key, you start a redial of the last number you connected
to, or attempted to call.  If you had several numbers in the QUE, they will
be ignored in the "redial" option.

The second key is the "dial que" key. (defaulted to be ALT-Q).  Lets say you
had four numbers in your dial que when you connect to one of them.  After you
disconnect, you may want to start dialing the others again.  One way to do this
is to go into the dialing directory and press enter.  This starts the dial, and
since there are still the other three numbers in the que, those numbers are
dialed.  Another option, however, is to use the "dial que" key.  This key, for
all purposes, is exactly the same as going into the dialing directory and
restarting the dial process over again; except simplified into one key.  Also,
the ALT-Q key starts the dial in the que where you left off before, whereas
going into the dialing directory and pressing enter restarts the dial off of
the first marked number.




            

                       G. THE SCROLLBACK BUFFER





There will invariably be times when you wish to review over information you
had passed over before.  You can look over the information that had come in
earlier by going into the Scrollback Buffer. (defaulted to be the ctrl-left-
arrow key).  Lcom has what I have dubbed to be a non-volatile scrollback.
That is, when you quit Lcom you do not loose that information and so it is
still there when you rerun the program.  Lcom also, unlike many other programs
(all of the ones that I know of) does not store the entire scrollback buffer
in RAM.  Instead, Lcom has a service area (around 8k) where the information
goes to be put into the scrollback buffer, and once 8k is filled that
information is then passed on to a file on your hard disk and permanently 
stored.  By doing this, Lcom has a virtually limitless pool of storage for
the scrollback buffer.  The default size of the scrollback buffer is 1megabyte,
(or 1,000,000 bytes / 1,000 K ).  This could be considered large and you might
want to reduce the size of the backscroll in the config program.  You may even,
however, want to increase this size to be able to "go back" further.

The two key components of the scrollback storage is the UNIT SIZE, and the 
NUMBER OF UNITS.  If you have a UNIT SIZE of 8000bytes, and 128 units, then
your scrollback buffer will be 1,024,000 bytes on disk (as it is defaulted).
If you wanted to increase or decrease the size of the backscroll, the fastest
and best way would be to change the number of units.  If you cut the number of
units in half to 64, then you would cut the scrollback buffer size in half.
If you ever change the unit size, be aware of these facts:  Increasing the
unit size increases Lcom's size in RAM, and decreasing the unit size decreases
the program's efficiency on disk, since about Lcom must waste approximately
240bytes of each unit.





                              H. MACROS





Macros are the way by which you can set up a particular key to type out
a group of keys for you automatically.  You might, for instance, make a
key to type out your name, i.e. "John Bushnell", and your password "whatever",
separated by carriage returns.  You might also want to make a macro which
automatically starts a transfer using a specific protocol, or even make a
macro to dial a certain number.  Macros, put simply, simplify repetitive tasks.

Macros are present in several parts of the program.  There are, obviously, a
list of macros which you can define in the macro window.  There are also
two macros for each number in the dialing directory; one executed when you
first connect to a BBS, and the other just after you disconnect.  There's a
macro which is executed when you first run lcom (called the bootup macro)
and also one which is run just before Lcom quits.

The general rule for macros is that when the scrolllock light is off, you
are typing in regular words, like "hello".  When the scrolllock light is ON,
you are in what is called "direct type mode".  In this mode, anything and
everything which you type (other than shift, alt, ctrl, and keys like that)
are recorded into the macro.  Even ESCAPES and ENTERS are stored.  The only
key which is not recorded is the help key.  By going into direct type mode,
you can type in commands such as ALT-D to go into the dialing directory,
and the ENTER key to dial the current number.  By making such a macro, you
would have in effect duplicated the (DIAL QUE) key for the dialing directory.



IN THE MACROS WINDOW


        In the macros window, you have a list of "slots" where you can place
macros.  The process of making a macro is as follows:  First, you would most
likely want to give that macro its keystroke.  You can make a macro any key
you want, however you shouldn't make it the same key as something which is
already used.  Almost all of the ALT-Keys have been used by Lcom's different
windows, and the F1 and F5 key are also used.  When you try to define a macro
as a key already used by Lcom, a warning is displayed which says that "you
will be masking out another key".  I only allow you to mask out another key
since there may come a time when you would want to.  This might be so that you
could do a few other things before actually going into the window originally
occupied by the key you were masking over.

        You define the key for a macro by first pressing the CTRL-LEFT-ARROW
key.  After pressing that key, you will see a box appear on the left hand
side of the window prompting you to type the key you would like that macro to
be.  You would then type in your key, for instance, ALT-F10.  Then you can type
in your macro.  All letters, numbers, and symbols are accepted; and, once
again, if you want to type in keys like the ALT or F-Keys, turn on the scroll
lock light, type them in, and shut the scrolllock like off again.

        There are various commands which can be built into the macros to be
interpreted as the macro is executed.  These commands start with a tilde (~)
and are followed by a letter representing a specific corresponding command,
and may be followed by other letters to be used by that command.  An example
of this is the ~C command, which is substituted at run-time by the key which
executed the macro.  There is another command for producing sound (~S).  This
command requires that you follow the command by the frequency.  i.e. ~S± .
The ± that you see you may recognize as the ASCII character #177.  You
produce this character by pressing the ALT key, and while holding the ALT key
typing in 1 7 7 (ON THE KEYPAD) , and then releasing the ALT key.  By putting
that character in after the ~S command, you are telling lcom to create the
sound with the frequency 177, or more specifically, frequency 177*100.  But you
also need one more component with the sound command, you also need a "duration"
; that is, the length of the tone.  The duration comes directly after the
frequency and is represented the same way: by a symbolic character that you can
produce by pressing the ALT key, typing in the number into the keypad (1-255)
and releasing the ALT key.  A complete example of the sound command would be
~S±° . The first symbol is character #177, and the second is #176.  In this
example, you would be telling Lcom to produce the frequency 177 for 176 clock
ticks.  (there are roughly 18 (20) clock ticks in one second).

A more complete list of commands is available in the HELP menu for the macros.
In that help menu you will find commands listed in a "format".  The format
for the sound command would be found as   ~Sfd  .  The F stands for the
frequency, and the D the duration.






                        I. MACROS (INCOMING)





Probably the most powerful option in Lcom is the incoming macros.  These
are macros which are triggered by, instead of keys, words that come in over
the modem.  When you press the ctrl-left-arrow key, instead of prompting you
to type in the key that would trigger the macro (to the right), you are typing
in the string which will run that macro.  In this way you can automatically
log yourself onto bulletin boards or create an "auto-zmodem".

Auto-Zmodem is a feature which exists on a few communications programs.  This
is where a Zmodem transfer is initiated by the computer which that program
is connected to, and the communications program automatically starts the
same transfer.  Zmodem sends out the characteristic characters **B00 just
before it starts to send a file. (the  is character #24).  You could, for
instance, make an incoming macro which is triggered by **B00 and goes into
the Download window (PgDn) and goes to the External Zmodem protocol (which
you had added previously) and presses Enter.  You can go specifically to
any protocol by typing in the sequential letter that corresponds to that
protocol.  i.e. the first protocol would be "A", the second "B", and so on.

For a list of the commands and limitations of macros, read the previous
section on MACROS.






                        J. TRANSLATE TABLES





Lcom has three different types of translate tables.  The first is an "incoming
character" translate table, the second an "outgoing character" table, and the
third is a "color" translation table.  Translation tables take one 'thing' and
translate it to another.  For instance, in the case of the color table;  you
could change one color to be another.  You may want to do this because it is
hard to read that particular color combination on your monitor; who knows.
The outgoing translate table takes the letters you type and will translate them
into a different letter, and the incoming table takes the letters as they come
in and changes them before it displays them on the screen.

A couple notes about the character translate tables:

when you start changing characters around, you may experience some 'weird'
results.  The first of which is that characters are translated AFTER they
are checked by the incoming macros.  This means that your incoming macros
only apply to that which exactly comes in over the modem.  Secondly, if you
ever translate character #27 then the ANSI color and control process will
stop working (assuming you are using the ANSI emulation; which you probably
are.)


 

                          K. ASCII TABLES





An Ascii Table is a list of all the characters on your IBM computer.
In this table you will find a list of letters and symbols with their
corresponding numbers.  If you want to produce any of these symbols
(or letters) the procedure you use to do this is as follows:

First press and hold the ALT key, then while holding the ALT key, type in the
number of the symbol (ON YOUR KEYPAD, NOT ON THE NUMBERS ABOVE THE LETTERS)
and then, release the alt key.  <- That, is the process by which you can
create these symbols just about anywhere.  While you are in the ascii table,
if you wish to send one of these characters out over the modem, one easy way
is to simply move the highlighted bar over the symbol and then press and
release the enter key.

Most likely you will use this as a "reference" guide.





                      L. TRANSFER PROTOCOL AREAS





Lcom uses what are called "external protocols".  I've found through my OWN
experiences with communications programs that internal protocols are often
'behind the times'.  This means slow, buggie, and devoid of newer features
which have since been added.  External protocols, or protocols which are
separate programs, can be found on any protocol which you could ever want;
and they are almost always more current and easier to update (so you don't
have to keep getting newer versions of Lcom).
        If you are unfamiliar with the procedures associated with using
External protocols, here is a brief summary:  The most common external
protocol program is called "DSZ".  This program contains inside of it
the Xmodem, Ymodem-Batch, and Zmodem protocols.  Which protocol is being
used depends on what you tell it to use when you are setting it up.  You
would, for instance in the case of DSZ, use that program three different ways:
one for each protocol.  After you have created an external protocol definition
(see below), You will type in the filename and parameters for both uploading
and downloading.  For the Zmodem protocol, your filename and parameters for
Uploading would be, for example: "c:\path\dsz port 1 sz %f".  c:\path\dsz
would probably not be where you put your external protocol, but it happens to
be where mine is.  You would put in the path to your own external protocol
program.  Also, I put in "port 1" because I'm on Com 1... if you are on com 2
then you should put "port 2" for DSZ.  Or, you could even put "port %c" since
Lcom automatically translates "%c" into the current com port number.
        After you have entered in this "string" into the external protocol
edit menu (alt-e) for both upload and download, then you are ready to go.


Creating an External Protocol Definition
----------------------------------------

To create a new external protocol, press the insert key.  Then, to edit it,
(so as to enter in the upload and download strings, as well as the name) type
ALT-E (while on that protocol).

        




                          M. SHELLING TO DOS





After going into the SHELL window, you then have two options: either doing
a L:ocal shell or a R:emote (and local) shell.

The Local Shell is a normal dos shell.  The Remote Dos Shell is a unique shell
in which you, and your remote partner, can both shell to (your) dos at the
same time.

The Remote Shell
----------------

        A few notes about the remote shell,

        You shouldn't use this unless you are ONLINE.  If you do it while you
        are offline, you will most likely experience a "loop back" and the
        computer will (seem) to lock up.  If this occurs, turn the scrolllock
        light ON.

        Turning the scrolllock light ON makes it so that characters are not
        allowed from over the modem.  This means that your partner cannot
        type, and if he/she hangs up while you are in a remote shell (and
        a loopback occurs) you can simply turn the scrolllock light on and
        things will "flush" themselves out eventually.






      N. CHANGING VIDEO MODES (SCREEN LENGTH, WIDTH, COLOR/B&W, ETC.)





There are problems with changing the screen size on the IBM computer.  Going
to 80x43 or 80x50 is fairly generalized by all video cards, and so I *could*
make it so you could switch into these screen sizes, however, if I used that
system then you could never go into, lets say, 132 columns, or my favorite,
100x60.

Most video cards come with some sort of utility program to change the screen
size into 80x43, 80x50, 132x43 (whatever is supported).  For my video card
the program is called "ESU".  I type ESU /3 for 80x25 and ESU /40 for 80x43.

The idea behind Lcom is that for every video mode that you would ever wish to
go into, you would run LCV (the lcom video utility) and configure Lcom for that
screen size individually.  After you've done 80x25, you'd then run your
change-screen-size program that came with your video card and switch to the
next mode that you might want to use.  After you've changed, then you'd rerun
LCV and configure for that screen mode.  Configuring for a screen mode involves
simply going into LCV, into the Change-mode-parameter-area, and typing in the
command which would set your screen size to that mode at dos.  i.e. "ESU /3"
(goto 80x25 for Video7 video cards).

After you've configured all of the modes you would ever want to use, you can
then go into them from the ALT-V (defaulted to) window.

You can also change the video mode from a DOS SHELL and lcom will work fine
in the new mode when you return; whether you configured that mode or not.





      O. CONTROLLING THE LCOM MENUS (SIZES, COLORS, POSITIONS, ETC.)





The Lcom Video program (LCV) is the means by which you can change the sizes,
colors, and positions of each window.  Inside of the LCV program there are
several initial options, the first of which is "configure windows".
After going into that area, you will now be in a mockup of Lcom.  When you
type the dialing directory key you will pull up a fake dialing directory.
You can use the arrow keys to move the window around on the screen, or the
shift-arrow keys to resize the window.  Pressing ALT-C takes you into a
window whereby you can change the colors of that window.

There are several "default" color sets which you can load.  They are a window
which you can reach by typing CTRL-ENTER.  In that window you could also save
your favorite color set to one of the default slots in the lower section and
then load it back into a different screen size.





                              P. ZOOMING





There are currently, two places where you can "zoom" in.  The first of which
is the terminal window.  By pressing the (defaulted to) F5 key, you will switch
between three different terminal windows.  The telephone directory also has
the ability to zoom.  By pressing this same zoom key, you will expand the
telephone directory to be able to view more information at one time.
(see 'zoom' in telephone directory)





                      Q. VIEWING THE DOS SCREEN





You can view the dos screen, that is, the screen as it was before you ran
Lcom (or after you left a shell) by pressing the View Dos Screen key.  This
key is defaulted to be ALT-F5.  This key can be activated from almost all
areas of Lcom.




                  R. SAVING THE SCREEN (RECORD SCREEN)




In Lcom you can "snapshot" the screen by using the "record screen" key.  This
is defaulted to be ALT-S.  After you have told Lcom the name of the file you
wish to save the screen to, you will then be prompted for what emulation you
would like to use; TTY,ANSI, or LVI.  Basically, this means:

        TTY - No color
        ANSI - Ansi color
        LVI - LVI color

ANSI color is most likely the color coding system that you have when you type
files out from DOS with the "type" command, and so you would most likely want
to save to ANSI if you want to save in 'normal color'.  You may, however, wish
to save it in LVI color (lcom's compressed color format).

If you ever want to save a block of the screen, you can do that by poping into
the backscroll and using the backscroll block and save commands.




                       S. PRINTING THE SCREEN




ALT-P is defaulted to be the print screen key.  If ever you wish to send that
which is currently displayed on the screen to the printer, this is the key you
would want to use.  One again, if you ever want to only print a block, you
can do that by poping into the backscroll and using the backscroll block and
print commands.




                   T. LOG TO FILE (protocol:ascii download)




Log to file is the way by which you can save everything that comes in over the
modem to a file.  Log-To-File in Lcom *IS* ASCII DOWNLOAD.  After pressing the
Download key, you select the protocol as ASCII.  You will then be put into the
Ascii Download window.  From there, you type in the filename which you want to
log to <press enter>, and then you might <but don't have to> type in a format
file to use. (see format files)

There are several options in the ascii download (area) of options.  One of them
is, how you want to save the text.  In "Binary" format; everything you get goes
directly to a file.. no questions asked (other than conforming to the carriage
return and line feed translations).  Whereas, in text mode, if a character (for
instance) 26 comes in over the modem, I will not write it to the file.. I'll
change it to another symbol.  This is because character #26 symbolizes the end
of a text file, and would cause you to not be able to view the entire file
(without a smarter text editor).




                          U. LOG TO PRINTER




This is similar to the Log-To-File in that it records what comes in over the
modem; except to the printer.  When you're done with the Log to printer
feature, you press the same key that you started it with to stop it.  When
you press that key, Lcom is not necessarily done printing.  It may have yet
to finish off the current page, so do not shut the printer off until Lcom
says it has finished and all the printing has stopped.





                V. SENDING THE MODEM INIT STRING MANUALLY




The Modem Initialization string is sent automatically when the program first
boots up (unless it is configured otherwise) : as long as you are not online.
The time may come when you would want to re-send it.  This can be done with
the (send-modem-init-string-key). defaulted to ALT-O:utput init string.





                       W. HANGING UP THE MODEM




Lcom's key to hang up the modem is defaulted to ALT-H.  Lcom's method of
hanging up the modem is called "dropping the DTR".  This is the quickest method
that could be used.  You may want to switch to the old method of hanging up
the modem; which is for all intents and purposes, saying "hangup" to the modem
with three +'s and an ATH0 instruction.  You would most likely only want to
switch to this method (in the config program) if dropping the DTR did not work
with your modem.




     
                        X. EXITING THE PROGRAM




To exit the program, you first type the exit-lcom-key (defaulted to ALT-X) and
then (normally) just press ENTER (or Y).  You could, however, type the 'W' key
and exit without executing the terminate-lcom-macro (defined in the config
program).




ÄÄÄÄÄ
v1.01+
ÄÄÄÄÄ



                       Y. SPLIT-SCREEN CHAT-MODE




To enter in and out of split screen chat, press (defaulted) ALT-Y.  Once
inside the split-screen chat, you can use the shift-up-arrow and
shift-down-arrow to change the size of the split-screen windows.  The
shift-left-arrow command will clear the local buffer, and the shift-right-arrow
command will change the splitscreen type.

There are two possible types:  Normal and Holding.  The difference between the
two is that the holding mode does not send out what you have typed until you
press the ENTER key, whereas in normal mode each character is sent out
as you type them.  In holding mode, backspaces are not sent since they are
considered 'editing' commands for the text which you have typed.





                       Z. The NOTES FEATURE




The notes feature is a way by which you can store information about a bbs you
are on.  A, jotting place, as it were.  After you have connected to a bbs, you
can type (defaulted to) ALT-N and Lcom will run the text editor you have
specified in LCC with a unique filename for that entry in the dialing directory
list.  You can also, however, use the command (defaulted to) 'notes' in the
telephone directory after placing the highlighted bar on the entry you wish to
edit.




Appendix A - TroubleShooting
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

Error:                                                          Notes:



Fat table bad drive 'C message came up after quitting. (or something like that)

                        - this problem has occured on select systems.  so far,
                          it has not caused any damage.  After rebooting your
                          system, you should not see this message again.  If
                          you do, you might consider discontinuing use of this
                          program since I do not know the effects of this
                          message.  This is a very grave message though and
                          should not be taken lightly.

Modem does not respond.

                        - Make sure your com port is set correctly, and also,
                          make sure the modem base-address is set correctly.
                          Normally the base address would correspond to your
                          com port, but there may be an exception so I allow
                          you to change this.  If you do not set the base
                          address, it will appear your modem is not connected.

Connection locks up system.

                        - Occasionally a person has called up telling me that
                          they got lcom but it locks up when it connects
                          through the dialing directory.  Although I have not
                          found a cause for this, there is evidence that it
                          may be a bad copy of the program.  In other words,
                          someone may have tampered with it.  So if this occurs
                          on your system, I suggest trying to find a new copy
                          of this program.

Protocols don't work.

                        - Lcom has no internal protocols other than ascii,
                          currently, and as such Lcom must have an external
                          protocol program which it runs for its protocols.
                          This program will most likely be DSZ or GSZ.
                          Drop one of these programs into your Lcom root
                          directory (and if you're using gsz, change the
                          filename in the upload area to gsz by pressing
                          alt-e on each of the protocols and setting it there)
                          and everything should be fine.

                          Something may have happened to your copy of Lcom
                          causing there to be no defaulted protocols.  If this
                          is the case, you will have to add them yourself by
                          pressing the insert key (in the uploads area) and
                          then editing the new protocol (alt-e) and inserting
                          the proper command lines for upload and downloading.
                          Pressing the help key could be of some service here
                          since I list off the command lines for DSZ/GSZ.

Backscroll is Re-arranged 

                        - Lcom's backscroll has to do SO much, that to pull
                          every ounce of speed out of it possible it was
                          necessary to do some very 'hairy' things.  Due to
                          this, it is not uncommon for the backscroll to
                          mess itself up in terms of order or whatnot,
                          especially when you reboot your system right from
                          the terminal.  That is the worst thing you can do.
                          Whenever you think the backscroll may be messed up,
                          you *can* most likely fix it.  The (Z) command in
                          the backscroll will do this.



Something's suddenly stopped working and I don't know why.

                          Lcom runs heavily off of macros to do some of its
                          functions.  If you were to make a macro which
                          cancelled out a key (for instance) or set two keys
                          to the same function in the config program (masking
                          one out) this could cause certain portions of the
                          program to stop working.

                          Another culprit of the crippled com program could
                          be the backscroll.  The backscroll in lcom, because
                          it can be so large, can get corrupted.  Try using the
                          'Z' command in the backscroll which refreshes certain
                          variables the program uses.  This may solve the
                          problem.



                              ÚÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
                              ³AUTHORS NOTES³ 
                              ÀÄÄÄÄÄIVÄÄÄÄÄÄÙ



If you have any questions or comments, you can call my Bulletin Board in
San Clemente, CA. (714) 492-3804 (from Sept 4th to January 1st, 1992), (that
time frame given so that if I should take the BBS down that I don't continue to
get phone calls on that line).  If I should keep the BBS up longer, then the
range will change in future versions of Lcom; and there WILL be future
versions.

If you wish to contribute to the further versions of Lcom, you can send
a $20 donation to:  

        John Bushnell
             attn: Lcom
        401 Calle Robles
        San Clemente, Ca. 92672

Please include your name and mailing address so that I may know for future
reference that you have sent in your donation.  As the program becomes more
established, there may be benifits through the bulletin board for persons
who have sent in donations.

                                                           - John Bushnell

Furthur note:

        Some people have wanted to contact me through the bbs networks but
can hardly ever find my name because of the 'alias' system many bulletin boards
use.  My handle currently, and for the last three years, has been Nop.


.............................................................................
This program compiled using Borland C, v2.0 and Turbo Assembler, v2.5.