DVdevload     (c) Copyright 1991, 1992 Ralf Brown
v1.10	8/22/92

What is it?
-----------
DVdevload and its support program DVeop allow you to load device
drivers in a DESQview window.  Unlike Quarterdeck's DEVICE.COM through
version 2.34, DVdevload actually links the driver into the device
driver chain, thus permitting the use of drivers which do not hook any
interrupts.  With those versions of DEVICE.COM, if the driver does not
hook any interrupts, it is completely inactive because DEVICE.COM does
not hook it into the driver chain.  DEVICE.COM from DESQview v2.40 and
higher does hook the driver into the device chain, but uses much more
memory than DVdevload; the DEVICE.COM from v2.4x also does NOT
correctly unlink the driver when the window is closed, leading to
system instability.

What's New?
-----------
Changes since version 1.00:
	Fixed bug which caused unpredictable behavior if the driver
	   modified DS on installation.  


DISCLAIMER
----------
This product is distributed AS IS, with no warranties, express or implied.
The author disclaims all liability for any damages (incidental or
consequential) caused by the use or misuse of this product.  Sole
responsibility for determining its fitness for use rests with the user.


INSTALLATION
------------
DVdevload is quite simple to use.  Before starting DESQview, the DVeop
driver must have been installed, so you will need to add a line to
either AUTOEXEC.BAT or your DESQview startup batch file to run DVeop
without arguments, i.e.

	   DVEOP
or
	   DVEOP-S

DVeop will automatically load itself into high memory using either XMS
or DOS 5 upper memory blocks; LOADHIGH or its equivalent is completely
superfluous and would in fact *increase* DVeop's memory requirements.
DVEOP.COM and DVEOP-S.COM are the same except that DVEOP-S.COM only
supports 3 simultaneous windows using DVDEVLOD, while DVEOP.COM
supports 16.  This results in an 80-byte savings in the resident
portion (272 bytes versus 352 bytes when loaded high).

Once DVEOP has been run, you can now start DESQview.  Within each
window that requires a particular driver, you need to run DVDEVLOD.COM.
Thus, you would have a line like

	   DVDEVLOD C:\DOS\ANSI.SYS

in that window's startup batch file.  If the driver requires any parameters,
you simply place them after the driver's name, as in

	   DVDEVLOD C:\DOS\ANSI.SYS /L
or
	   DVDEVLOD C:\DOS\DISPLAY.SYS con=(ega,437,4)

You may run DVDEVLOD multiple times within a single window to load multiple
drivers.


REQUIREMENTS
------------
DVdevlod requires DOS 2.0 or higher and DESQview 2.26 or higher.  Once
installed, it uses 192 bytes in addition to the memory used by the driver
itself.


LIMITATIONS
-----------
This version of DVdevload is not able to load block devices inside a DESQview
window.  If the driver provides one or more drive letters, it must be loaded
in CONFIG.SYS.	While technically possible, loading block devices is far more
complex than character devices, because several DOS-internal data structures
must be modified on each task switch.  A future version will remove this
limitation.

Further, DVdevload can not be used in windows for which the protection level
(second "Change a Program" screen) has been set to either 2 or 3, as DESQview
will complain about a protection violation each time DVdevload tries to
patch the device chain.  There are no problems with protection levels 0 or 1.
I do not believe that a workaround for this problem exists, because DVdevload
must inherently mess with DOS's internals, which is considered outside the
program's address space at higher protection levels.


AVAILABILITY
------------
The newest version is available in the following places:

    On the Internet, for anonymous FTP from CS.CMU.EDU [128.2.222.173] in
    directory /afs/cs.cmu.edu/user/ralf/pub/DESQview.  You must change
    directory there with a single command before attempting to retrieve
    any files, due to the way the security mechanism works.  If your site
    is connected to AFS, you can simply change directory to the above
    directory and perform a normal Unix/VMS/whatever file copy.

    On FIDOnet, for download and File Request from SoundingBoard, 1:129/26,
    1-412-621-4604, 2400/9600 HST.  The file is kept in file area 8.


AUTHOR
------
	Ralf Brown			[valid until November 1, 1993]
	813 Copeland Way, Suite 26
	Pittsburgh, PA 15232

	Internet: ralf+@cs.cmu.edu
	CIS:	  >INTERNET:ralf+@cs.cmu.edu
	FIDO:	  Ralf Brown 1:129/26.1