NAME
     df - free and used disk space

SYNOPSIS
     df [/cn /r /p /?]

DESCRIPTION
     DF reports on the disk space available all hard drives.  Its
     output looks like this:

     Drive Label      Used  Available
     C:    SYSTEM      57%      2096K
     D:    OLDDRIVE    48%     10742K
     E:    APPLICATNS  90%      1646K
     F:    DATA        35%     13140K

     DF finds all drives, such as network drives, higher than C:
     and includes them in the list.  With the /c option, DF will
     dynamically watch the available drives.  If a SUBST command
     is used or a network drive is added, DF will update its list
     to include that drive.

OPTIONS
     Options are case sensitive and may be strung together: /c4/r

     /cn
     Continuously update the list every n seconds.  Normally, df
     lists the disk space and exits.  This option is most useful when
     df is used in its own window.  n must be an integer between
     0 and 65535.  Hitting any key will stop the listing and
     cause df to exit.

     /r
     Resize the window to fit exactly the number of drives in the
     system.  Useful with /c option.

     /p
     Print "Press any key to continue..." and wait for keystroke
     before exiting.

     /?
     Display a help screen.

BUGS
     If using /c and /r, the maximum size of the window must be
     as large as the (max # of drives+1) or strange things will happen.

Last Updated: August 11, 1991

----------------------------------------------------------------------------


NAME
     dvsixdi - External Device Interface for DVSI

SYNOPSIS
     In autoexec.bat:

     [loadhi] dvsixdi.com

DESCRIPTION
     DVSIXDI is the heart of DVSI.  It keeps track of the processes
     that DESQview starts and stops, as well as the CPU time of each
     process and other information.  Basically, whenever DESQview
     does something important, it calls DVSIXDI to record what is
     happening.

     DVSIXDI should be installed before DESQview is run.  It is
     best to put it in AUTOEXEC.BAT.  It will take up about
     1.2K of memory after it exits.  To minimize the memory it requires,
     load it (and any other TSRs) before you set your PATH and
     other environment variables.  Preferrably, it should be loaded
     in high memory, but this is not required.

     DVSIXDI may error out and not load.  The possible error messages
     are:

     Error: Already Installed
          You can only load DVSIXDI once.

     Error: No available slots
          You have too many TSRs loaded that use the Multiplex interrupt
          2F.  DVSIXDI cannot be loaded until an interrupt 2F slot is
          available.

     DVSIXDI requires at least version 2.26 of DESQview.

     Other programs can communicate with DVSIXDI.  Please read
     the distribution information in README.1ST; I retain the
     copyright for this material and I do not allow modification
     of the DVSI package.

     I do not guarantee anything about the future of the DVSIXDI
     interface except for the installation check and the version check.
     The interface for version 1.10 is

     AX=0de01h  BX=7575h  CX=function

     Function
     00h - Installation check
           Returns AL=ffh if installed

     01h - Notification on: not currently used

     02h - Notification off: not currently used

     03h - Get application records
           Return
             CX = number of application records
             ES:DI pointer to array of application records
             AX = 1 if OK, 0 if not OK
             BX = last instantaneous time slice in 1/100 secs

           ES:DI points to the data structure in use.  I recommend
           that you start a critical section, make this call, make
           a copy of the records, and end the critical section.  Only
           those records that have (flags & 0x80) true are valid, but
           there are 15 records total.

           Application record:
           app_rec_t struc
                   flags           db ?  ;See below
                   openkeys        dw ?  ;Keys on Open Window menu
                   appnum          dw ?  ;Switch windows #
                   handle          dw ?  ;Segment of handle of process
                   numtasks        dw ?  ;Number of tasks including self
                   mapcntx         dw ?  ;Mapping context of process
                   t_start         dd ?  ;DVSI clock value at process's start
                   t_getcpu        dd ?  ;DVSI clock when last got CPU
                   t_giveupcpu     dd ?  ;DVSI clock when last gave up CPU
                   t_cpu           dd ?  ;CPU time in 1/100 sec since start
                   t_cpu_last      dd ?  ;CPU time at instant. time start ago
                   t_cpu_inst      dd ?  ;CPU time in last instant. time secs
                   hook            dd ?  ;Hook for other programs
           app_rec_t ends

               The flags field can be an ORing of:
                   04h   ;This is DV system task
                   80h   ;Valid record (used internally by DVSIXDI)
               These flags are not currently used:
                   01h   ;This task swapped out
                   02h   ;This task has keyboard

               DVSI clock value of 0 is the time DESQview is started.
               Clock values are in 1/100 seconds.

               The Instantaneous Time is approximately 10 seconds.  The
               t_cpu_last field is the value of the t_cpu field before
               the current Instantaneous Time period started.  The
               t_cpu_inst field is the amount of cpu time in the last
               Instantaneous Time period (t_cpu - t_cpu_last).

     04h - Get Version
          Return AH=Major, AL=Minor (1.10 is 010Ah)

     05h - Get Time since DV started
          Return DX:AX = 1/100 seconds since DV started

     06h - Get Task Switches
          Return DX:AX = # of task switches since DV start
                    CX = # of task switches in last instantaneous time
BUGS
     DVSIXDI only keeps track of 15 processes at a time. Anything
     started after 15 is ignored completely, and never seen again
     by DVSIXDI except in the calculation of number of task switches.


Last updated: August 11, 1991

----------------------------------------------------------------------------

NAME
     kill - Kill a DESQview process

SYNOPSIS
     kill [/p /?] <process_id>

DESCRIPTION
     KILL "kills" a DESQview process.  It works just like "Close Window"
     except that it will kill the process even if the "Allow Close
     Window Command" is "N" in the DVP file.  This command is dangerous,
     because you could easily lose data if you don't save before
     using kill.  It is much better to exit a program (especially
     non-DESQview programs) from the program itself.

     The process to be killed is unswapped, brought to the top,
     and killed.  Kill then displays the handle of the killed process.

     KILL requires DVSIXDI 1.1 to be installed.

OPTIONS
     All options are case sensitive.

     /p
     When the process is killed, print "Press any key to
     continue..." and wait for a keystroke.

     /?
     Print a help message summarizing the options.

     <process_id>
     The process to be killed. If <process_id> is 4 digits, it is
     interpreted as a hex DESQview process handle from PS.  If it is
     less than 4 digits, it is interpreted as a Switch Windows number.

BUGS
     Some programs are determined not to die. They may require a
     keystroke to make them go.

Last Updated: August 1, 1991

----------------------------------------------------------------------------

NAME
     perf - DESQview CPU performance statistics

SYNOPSIS
     perf [/cn /p /?]

DESCRIPTION
     PERF displays DESQview's performance.  It requires DVSIXDI 1.1
     to be installed.

     PERF's output looks like this:

                        INSTANT      TOTAL
     CPU Utilization          5%        36%
     Task Switches           10        500
     Task Switches/s        1.0        1.5
     Time (1/100 s)        1011      75067

     Two columns of information are presented.  The statistics in the
     INSTANT column represent the performance averaged over approximately
     the last 10 seconds, while the TOTAL column represents the performance
     averaged over the entire time DESQview has been running.

     CPU Utilization
     The percentage of time spent running programs other than the
     DV System Task.

     Task Switches
     Number of times that DESQview has switched to a different task.

     Task Switches/s
     Number of task switches per second during the time period.

     Time
     The amount of time in 1/100 seconds that was used to calculate
     the statistics.  The INSTANT column may be at up to 10 seconds old.

OPTIONS
     All options are case sensitive.  Options may be strung together:
     /c4/p

     /cn
     Continuously update the statistics every n seconds.  Normally, perf
     lists the statistics and exits.  This option is most useful when
     perf is used in its own window.  n must be an integer between
     0 and 65535.  Hitting any key will stop the listing and
     cause perf to exit.  A good value for n is 10 seconds, since
     DVSIXDI updates the INSTANT information every 10 seconds.

     /p
     When the listing is complete, print "Press any key to
     continue..." and wait for a keystroke.  Helpful if you are
     not using /c and you want to use perf in its own window.  Will
     work with the /c option.

     /?
     Prints a help screen.  If any bad options are given, this
     screen will automatically be printed.

BUGS
     Integer math is used for the calculations; truncation rather than
     rounding occurs in the least significant digit.

     The INSTANT column gives strange numbers during the first 10 seconds
     after DESQview is started.

Last Updated: August 5, 1991

----------------------------------------------------------------------------

NAME
     ps - DESQview process status

SYNOPSIS
     ps [/cn /dpath /p /r /l /?] [<process_id>]

DESCRIPTION
     PS provides information on the current DESQview processes.
     It requires DVSIXDI 1.1 to be installed.  Without the /l option,
     PS's output looks like this:

     HNDL SW TK MAP  TTLMEM SYSMEM  L SYS  CPUTIME CPU UT KY NAME
     d662 ?   0 95f6 641680 278512  276144  433516  89.2%    DV System Task
     cf9b 1   1 0fe8  16464   1632    1088       0   0.0% CC Clock & Calendar
     d027 2   1 1c34 ?????? Swappds ??????    6764   5.1% WP WordPerfect 5
     cfe1 3   1 1b52 Swappd    592    1088     344   6.7% MF Quarterdeck Manifest

     The columns are described below:

     HNDL
     The hexadecimal segment of the process's handle, similar to UNIX's PID.

     SW
     The number appearing on the Switch Windows menu for this
     task.  Applications which are "orphaned" and do not appear
     on the Switch Windows menu, as well as the DV system task, will
     contain a "?" in this column.

     TK
     The number of separate tasks, including itself, that the
     application has started.  For most programs, this will show
     1, but some DESQview specific programs may use more than one
     task.

     MAP
     The hexadecimal mapping context of the application.  This number
     is used with a DESQview API call to guarantee that the program
     is in conventional memory.

     TTLMEM
     The total memory, in bytes, used by the application.  If
     "Swappd" appears in this column, the process's memory is
     swapped out.  If system memory is swapped out, a "??????"
     will appear in the field because the real value cannot be
     determined.

     SYSMEM
     The system memory, in bytes, used by the application. If
     "Swappd" appears in this column, the process's system memory is
     swapped out.  If an "s" is appended to the value, the system
     memory resides in shared memory (see Wordperfect, above).

     L SYS
     The largest block of system memory, in bytes, available to
     the application. A "??????" implies that the value cannot be
     determined.

     CPUTIME
     Approximate amount CPU Time in 1/100 seconds for the process.
     The time is actually only accurate to about 6/100 of a second.

     CPU UT
     Approximate percentage of CPU time that the process has used in
     the last approximately 10 seconds.  This column may be at most
     10 seconds old.  The percentage for the DV System Task is
     basically unused CPU time.

     KY
     The keys used to open the application.

     NAME
     The name of the application, as shown on the Open Window
     menu.

     If the /l option is used, the output looks a little messier:

     HNDL SW TK MAP  TTLMEM SYSMEM  L SYS  CPUTIME CPU UT KY NAME
     kbd  mbx  obq  cursor  positn  visible logcl dispd

     d3e2  ?  0 0249 654016 384752  354128  723011  97.2%    DV System Task
     014d d3e2 0197 ( 1,17) ( 0,56) ( 0, 0) 17x24 17x24

     ce55  ?  1 1044  16448   1632    1088       6   0.0% CC Clock & Calendar
     014d ce55 0197 ( 0,33) (58,15) ( 0, 0)  1x45  1x35

     cefe  2  1 1aca 589808    480     432   55865   0.0% BD Big DOS
     014d cefe 0197 (39, 6) ( 0, 0) ( 0, 0) 60x80 60x80

     cf4f  3  1 1fe0  32736    208     208   33714   2.8% PS DVSI ps
     014d cf4f 0197 (16,15) (11, 0) ( 0, 0) 50x80 28x80


     The additional columns in the second line for each process are:

     KBD MBX OBQ
     The hex offsets for the process's default keyboard, mailbox and
     objectq.  The segments are the same as the process's handle.

     CURSOR
     The position of the cursor relative to the window's origin,
     (row, column).

     POSITN
     The upper left corner of the window on the screen, (row, column).

     VISIBLE
     The coordinate of the upper left corner of the displayed window,
     (row, column).  This number can be changed by using "Rearrange -
     Scroll".

     LOGCL
     Logical, or maximum, size of the window, in rows x columns.

     DISPD
     Displayed size of the window, in rows x columns.

OPTIONS
     All options are case sensitive.  Options may be strung together:
     /c4/p/d\dv

     /cn
     Continuously update the list every n seconds.  Normally, ps
     lists the status and exits.  This option is most useful when
     ps is used in its own window.  n must be an integer between
     0 and 65535 (I don't know why you'd want to wait 18 hours,
     but you can!).  Hitting any key will stop the listing and
     cause ps to exit.

     /p
     When the listing is complete, print "Press any key to
     continue..." and wait for a keystroke.  Helpful if you are
     not using /c and you want to use ps in its own window.  Will
     work with the /c option.

     /dpath
     Find DESQVIEW.DVO in the directory specified by path.
     DESQVIEW.DVO is the file that the Open Window menu gets its
     info from, and where ps finds the NAME and KEY fields.  If
     this option is not specified, ps will first look in C:\DV, then
     search the PATH environment variable for the directory.
     This will usually work because the DESQview system directory
     name should be in the PATH.  However, I have noticed that
     the environment does  not get passed if ps is started from
     its own window, so I provided this option.

     /r
     Resize the window according to the number of processes in the list.
     The window is made 80 columns wide and high enough for all the
     processes to be displayed, and is moved left to column 0.
     If using /c and the number of processes changes, the window size
     is changed also.

     /l
     Long listing: more info than you really wanted to know about each
     process.

     /?
     Prints a help screen.  If any bad options are given, this
     screen will automatically be printed.

     <process_id>
     If <process_id> is specified, only display info for that process.
     Normally, PS displays all processes.  <process_id> is interpreted
     as a hexadecimal handle if it is 4 digits.  Otherwise, it
     is considered a switch windows number.

BUGS
     Any processes started after 15 have been started will be ignored.

     Running Add A Program or Delete A Program no longer confuses
     PS.  However, if you are using /c and you add or delete programs,
     and run them, PS may display "(not available)" in the NAME
     field.  This is because PS does not close and reopen DESQVIEW.DVO
     each iteration.  If the "(not available)" bothers you, exit
     PS and restart.


Last Updated: August 11, 1991


----------------------------------------------------------------------------

NAME
     memstat - DESQview memory status

SYNOPSIS
     memstat [/cn /p /?]

DESCRIPTION
     MEMSTAT is an alternative to DESQview's Memory Status program.
     It takes up much less CPU time, although it is larger than
     Memory Status.  It can also be used at the DOS command line,
     while Memory Status cannot.

     MEMSTAT displays the same information as memory status, and
     adds another column.  The output looks like this:

     TYPE  TOTAL LARGEST AVAILABLE USED
     Conv   590K    345K      375K  36%
     Exp   2912K    576K     1184K  59%
     Com  25600   10668     10804   58%

     The columns are:

     TYPE
     The type of memory described in this row.  "Conv" is conventional
     memory, or memory between 0 and 640K.  "Exp" is expanded
     (EMS or EEMS) memory.  "Com" is DESQview's common memory
     area.

     TOTAL
     The total amount of memory in the system.

     LARGEST
     The largest block of available memory.

     AVAILABLE
     The total amount of memory currently available.

     USED
     The percentage of memory that is currently being used.

OPTIONS
     All options are case sensitive.  Options may be strung together:
     /c4/p

     /cn
     Continuously update the statistics every n seconds.  Normally, memstat
     lists the statistics and exits.  This option is most useful when
     memstat is used in its own window.  n must be an integer between
     0 and 65535.  Hitting any key will stop the listing and
     cause memstat to exit.

     /p
     When the listing is complete, print "Press any key to
     continue..." and wait for a keystroke.  Helpful if you are
     not using /c and you want to use perf in its own window.  Will
     work with the /c option.

     /?
     Prints a help screen.  If any bad options are given, this
     screen will automatically be printed.

Last Updated: August 11, 1991

--------------------------------------------------------------------------

NAME
     uptime - Print amount of time DESQview has been running

SYNOPSIS
     uptime [/p /?]

DESCRIPTION
     UPTIME reports the amount of time that DESQview has been running
     in the following format:

     DESQview has been running for 2 days 1 hour 5 minutes and 21.34 seconds
     Since Fri Aug 02 18:23:45 1991

     UPTIME requires DVSIXDI 1.1 to be installed.

OPTIONS
     All options are case sensitive.

     /p
     After the time is displayed, print "Press any key to
     continue..." and wait for a keystroke.

     /?
     Print a help message summarizing the options.


Last Updated: August 2, 1991

--------------------------------------------------------------------------

NAME
     wn - Manipulate DESQview windows

SYNOPSIS
     wn [/?] <command> [<process_id>]

DESCRIPTION
     WN contains a set of commands for manipulating DESQview windows.
     Windows may be killed, raised, lowered, topped, hidden or
     suspended.

     Killing a window is just like the DVSI's KILL command.  Read
     KILL's man page for more information.

     Raising a window gives it the keyboard.  It is equivalent to
     using the "Switch Windows" menu.

     Lowering a window puts it at the bottom of the window stack,
     and takes away the keyboard.

     Topping a window brings it to the top of the window stack, but
     does not give it the keyboard.

     Hidding a window is works just like "Rearrange - Hide".

     Suspending a window hides it and doesn't give it any CPU time
     while hidden.

     A suspended or hidden window may be unhidden by raising or
     topping it.

OPTIONS

     /?
     Print a help message

     <command> may be one of the following.  The first letter of the
     command may be used as an abbreviation.  The command is
     case-insensitive.
     KILL
     RAISE
     LOWER
     TOP
     HIDE
     SUSPEND

     If <process_id> is specified, that process's window is manipulated.
     Otherwise, the current process's window is used.  If <process_id>
     is 4 hex digits, it is interpreted as a handle.  Otherwise,
     it is considered a Switch Windows number.

Last Updated: August 11, 1991