Installation instructions for the packet driver collection
          
          
          Document conventions
          
               All numbers in this document are given in C-style
          representation.  Decimal is expressed as 11, hexadecimal is
          expressed as 0x0B, octal is expressed as 013.  All reference to
          network hardware addresses (source, destination and multicast)
          and demultiplexing information for the packet headers assumes
          they are represented as they would be in a MAC-level packet
          header being passed to the send_pkt() function.
          
          
          Using the packet drivers
          
               The packet driver must be installed prior to use.  Since
          each packet driver takes only a few thousand bytes, this is best
          done in your autoexec.bat.  Since the Ethernet boards typically
          have jumpers on board, the packet driver must be informed of the
          values of these jumpers (auto-configure is possible, but can
          disturb other boards).  The first parameter is the software
          interrupt used to communicate with the packet driver.  And
          again, because each board is different, the rest of the
          parameters will be different.
          
          All parameters must be specified in C-style representation.
          Decimal is expressed as 11, hexadecimal is expressed as 0x0B,
          octal is expressed as 013.  Any numbers that the packet driver
          prints will be in the same notation.
          
          Before installing the packet driver, you must choose a software
          interrupt number in the range between 0x60 and 0x80.  Some of
          these interrupts are used for other purposes, so your first
          choice may not work.  See Appendix A for the section of Ralf
          Brown's interrupt list between 0x60 and 0x80.
          
          Running a packet driver with no specifications will give a
          usage message.  The parameters for each packet driver are
          documented below.
          
          Most drivers can also be used in a PROM boot environment, see
          PROMBOOT.NOT for how to use -d and -n options for that purpose.
          
          The -w switch is used for Windows.  Install the packet driver
          before running MS-Windows.  This switch does not prevent Windows
          from swapping your network application out of memory, it simply
          detects when that has happened, and drops the packets on the
          floor.
          
          3Com 3C501
          
               usage: 3C501 [-n] [-d] [-w] packet_int_no [int_no
          [io_addr]]
          
               The 3c501 driver requires two additional parameters -- the
          hardware interrupt number and the I/O address.  The defaults are
          3 and 0x300.
          
          







          3Com 3C503
          
               usage: 3C503 [-n] [-d] [-w] packet_int_no [int_level(2-5)
          [io_addr [cable_type]]]
          
               The 3c503 driver requires three additional parameters --
          the hardware interrupt number, the I/O address, and the cable
          type.  The 3c503 can be attached to thick or thin Ethernet
          cables, and the selection is made in software.  The cable type
          parameter should be zero for thick, and one for thin.  The
          defaults are 2, 0x300, and 1 (thin).  The 3c503 uses shared
          memory whose address is set by jumpers, but the software can ask
          the board what the address is.
          
          
          3Com 3c505
          
               usage: 3c505 [-n] [-d] [-w] packet_int_no [int_no [io_addr
          [base_addr]]]
          
               The 3c505 driver requires three additional parameters --
          the hardware interrupt number, the I/O address, and the memory
          base address.  The defaults are 2 and 0x300 and 0xd000.
          
          
          3Com 3c507
          
               usage: 3c507 [-n] [-d] [-w] packet_int_no [int_no [io_addr
          [base_addr]]]
          
               The 3c507 will determine its parameters by reading the
          board.  The only time you would need to specify the parameters
          is when you have multiple 3c507s in the same machine.
               The 3c507 driver will use three additional parameters --
          the hardware interrupt number, the I/O address, and the memory
          base address.
          
          3Com 3c523
          
               usage: 3c523 [-n] [-d] [-w] packet_int_no [int_no [io_addr
          [base_addr]]]
          
               The 3c523 driver requires three additional parameters --
          the hardware interrupt number, the I/O address, and the memory
          base address.  The defaults are 3 and 0x300 and 0xc000.
          
          
          ARCETHER
          
               usage: arcether [-n] [-d] [-w] packet_int_no [int_no
          [io_addr [base_addr]]]
          
               The ARCNET driver requires three additional parameters --
          the hardware interrupt number, the I/O address, and the memory
          base address.  The defaults are 5 and 0x2e0 and 0xd800.  Note
          that a packet driver client must specifically support ARCNET.
          The only known client is Phil Karn's (KA9Q) networking package,
          NOS.
          
          







          ARCNET
          
               usage: arcnet [-n] [-d] [-w] packet_int_no [int_no [io_addr
          [base_addr]]]
          
               The ARCNET driver requires three additional parameters --
          the hardware interrupt number, the I/O address, and the memory
          base address.  The defaults are 5 and 0x2e0 and 0xd800.  Note
          that a packet driver client must specifically support ARCNET.
          The only known client is Phil Karn's (KA9Q) networking package,
          NOS.
          
          
          AT&T
          
               usage: at&t [-n] [-d] [-w] packet_int_no [int_no [io_addr
          [base_addr]]]
          
               The AT&T driver requires three additional parameters --
          the hardware interrupt number, the I/O address, and the memory
          base address.  The defaults are 2 and 0x360 and 0xd000.  This
          driver supports the StarLAN 1, StarLAN 10 NAU, EN100 and StarLAN
          Fiber NAU.
          
          
          AT&TLP 0x62 2 0x360 0xd000 0 0
          
               usage: at&t_lp [-n] [-d] [-w] <packet_int_no> [<int_no>
          [<io_addr> [<base_addr> [<media_sel> [<li_enabl>]]]]]
          
               The AT&T_LP driver requires five additional parameters --
          the hardware interrupt number, the I/O address, the memory base
          address, media select, and link integrity.  The defaults are 2
          and 0x360 and 0xd000.  This driver supports the ATStarStation,
          ATStarLAN 10 LanPACER+ NAU, ATStarLAN 10 LanPACER NAU and AT
          Microelectronics T7231 evaluation board.
          
          The final two numbers are new attributes.
          
               0 0 --> This is for AUI setting
               0 1 --> This is also for AUI setting
               1 0 --> This is for TP setting, no link integrity
               1 1 --> This is for TP setting, link integrity enabled
          
          For the LP NAU only, "0 0" and "0 1" are invalid as there is no
          AUI port on that NIC.
          
          
          David Systems Inc (DSI)
          
               usage: davidsys [-n] [-d] [-w] <packet_int_no> <int_no>
          <io_addr> <delay_mult>
          
          The DSI driver requires three additional parameters, the
          hardware interrupt number, the I/O port and the delay
          multiplier.  Delaymult is a system dependent timing loop used
          for I/O to the card.  A reasonable value is calculated during
          initialization, but on some fast systems it may need to be
          somewhat larger.  The multipler is divided by ten, then
          multiplied by the calculated delay.  The default multiplier is







          10 (actually 1.0).
          
          
          D-Link DE-600
          
               usage: de600 [-n] [-d] [-w] packet_int_no
          
               The D-Link Pocket Lan Adapter packet driver requires no
          additional parameters.
          
          
          Digital Equipment Corporation DEPCA
          
               usage: depca [-n] [-d] [-w] <packet_int_no> [<int_no>
          [<io_addr> [<mem_addr>]]]
          
               The DEPCA packet driver requires three additional
          parameters -- the hardware interrupt number, the I/O address,
          and the memory base address.  The defaults are 5 and 0x300 and
          0xd000.  The packet driver will resolve the io_addr
          automatically if io_addr is set to '?', e.g.
          depca 0x7e 5 ? 0xd000.
          
          
          Multitech EN-301
          
               usage: en301 [-n] [-d] [-w] packet_int_no [int_no
          [io_addr]]
          
               The Multitech driver runs the EN-301 cards. The Multitech
          driver requires two additional parameters, the hardware
          interrupt number, and the I/O port.
          
          Intel EtherExpress
          
               usage: exp16 [-n] [-d] [-w] <packet_int_no> [<io_addr>]
          
          The Intel EtherExpress packet driver has one optional
          parameter.  The <io_addr> is only needed if there is more than
          one EtherExpress card in your system.  Otherwise, the driver
          will search for adapter and get its parameters from it.
          
          Mitel Express
          
               usage: express [-n] [-d] [-w] <packet_int_no> [-n]
          [<driver_class> [<int_no>]]
          
               The Mitel Express packet driver has one optional switch,
          and two optional parameters. The <driver_class> defaults to
          SLIP, and the <int_no> defaults to 7.  The -n switch instructs
          card to be an NT.  The <driver_class> should be SLIP or a
          number.
          
          
          












          HP Ethertwist
          
              usage: hppclan [-n] [-d] [-w] packet_int_no [int_no
          [io_addr]]
          
               The hppclan driver requires two additional parameters --
          the hardware interrupt number and the I/O address.  The defaults
          are 3 and 0x300.
          
          
          ICL EtherTeam16
          
               usage: ETHIIE [-n] [-d] [-w] packetintno [intlevel [ioaddr
          [cabletype]]]
          
               The ETHIIE driver requires three additional parameters --
          the hardware interrupt number, the I/O address, and the cable
          type.  The interrupt levels supported by the adapter are 5, 9
          (2), 12 and 15.  The Ethenet IIe can be attached to thick or
          thin Ethernet cables, and the selection is made in software. The
          cable type parameter should be zero for thick, and one for
          thin.  With the Twisted Pair (TP) version of the adapter, you
          must set interface to the value 1 (thin).
          
          The defaults are 9 (2), 0x300 and 1 (thin).
          
          Please note, that the adapter can be used only in a 16-bit slot
          of your computer.
          
          IBM Token Ring
          
               usage: ibmtoken [-n] [-d] [-w] packet_int_no [adapter_no]
          
               The IBM Token Ring packet driver requires one additional
          parameters -- the adapter number.  The default is zero.  See
          IBMTOKEN.DOC for more information.
          
          
          LocalTalk
          
               usage: localtlk [-n] [-d] [-w] <packetintno> [<IP address>]
          
               The LocalTalk packet driver requires atalk.sys to be
          installed.  Because it is not an Ethernet class driver, it
          requires special code in the client.  See LOCALTLK.NOT for more
          details.
          
          
          NCR ET-105
          
               usage: ncret105 [-n] [-d] [-w] <packet_int_no> <int_no>
          <base_addr> <Ethernet_address>
          
               The NCR ET-105 driver requires four additional parameters
          -- the hardware interrupt number, the I/O address, the memory
          base address, and the Ethernet address.  The Ethernet address
          assigned to any particular board is printed on sticky labels
          that come with the board.
          
          







          Novell IPX
          
               usage: ipxpkt [-n] [-d] [-w] packet_int_no [-n [no_bytes]]
          
               The ipxpkt packet driver simulates Ethernet on Novell IPX
          protocol.
          
          
          BICC Data Networks' ISOLAN 4110 ethernet
          
               usage: isolan [-n] [-d] [-w] packet_int_no [int_no
          [base_addr]]
          
               The BICC Isolan requires three additional parameters --
          the hardware interrupt number and the memory base address.  The
          defaults are 2 and 0xb800h.
          
          
          Netbios
          
               usage: nb [-n] [-d] [-w] packet_int_no ip.ad.dr.ess
          [receive queue size]
          
               The netbios packet driver transports IP packets over
          NetBIOS.
          
          
          Novell ne1000
          
               usage: ne1000 [-n] [-d] [-w] packet_int_no [int_no
          [io_addr]]
          
               The ne1000 driver requires two additional parameters --
          the hardware interrupt number and the I/O address.  The defaults
          are 3 and 0x300.
          
          
          Novell ne/2
          
               usage: ne2 [-n] [-d] [-w] <packet_int_no>
          
               The ne/2 driver requires no additional parameters.
          
          
          Novell ne2000
          
               usage: ne2000 [-n] [-d] [-w] packet_int_no [int_no
          [io_addr]]
          
               The ne2000 driver requires two additional parameters --
          the hardware interrupt number and the I/O address.  The defaults
          are 2 and 0x300.
          
          
          Racal-Interlan (Formerly Interlan) NI5010
          
               usage: NI5010 [-n] [-d] [-w] packet_int_no [int_no
          [io_addr]]
          
               The NI5010 driver requires two additional parameters --







          the hardware interrupt number and the I/O address.  The defaults
          are 3 and 0x300.
          
          
          Racal-Interlan (Formerly Micom-Interlan) NI5210
          
               usage: ni5210 [-n] [-d] [-w] packet_int_no [int_no [io_addr
          [base_addr]]]
          
               The NI5210 driver requires three additional parameters --
          the hardware interrupt number, the I/O address, and the memory
          base address.  The defaults are 2 and 0x360 and 0xd000.  Note
          that Interlan sets the default memory base to 0xa000, which is
          brain-damaged, because that area of memory is specifically
          reserved for video adapters, and in fact the EGA and VGA use
          it.
          
          
          Racal-Interlan NI6510
          
               usage: ni6510 [-n] [-d] [-w] packet_int_no [int_no
          [io_addr]]
          
               The ni6510 driver has two additional parameters -- the
          hardware interrupt number and the I/O address.  The defaults are
          2 and auto-sense.  These parameters do not need to be set unless
          the auto-sense routine fails, or otherwise disrupts operation of
          your PC.
          
          
          Racal-Interlan (Formerly Micom-Interlan) NI9210
          
               usage: ni9210 [-n] [-d] [-w] packet_int_no [int_no [io_addr
          [base_addr]]]
          
               The ni9210 driver requires three additional parameters --
          the hardware interrupt number, the I/O address, and the memory
          base address.  The defaults are 2 and 0x360 and 0xd000.
          
          
          NTI 16
          
               usage: nti16 [-n] [-d] [-w] packet_int_no [int_no [io_addr
          [base_addr]]]
          
               The nti16 driver requires three additional parameters --
          the hardware interrupt number, the I/O address, and the memory
          base address.  The defaults are 3 and 0x338 and 0xd000.
          
          
          SLIP8250
          
               usage: SLIP8250 [-n] [-d] [-w] packet_int_no [-h]
          [driver_class] [int_no]
                  [io_addr] [baud_rate] [recv_buf_size]
                  The driver_class should be SLIP, KISS, AX.25, or a
                  number.
          
               The SLIP8250 driver is not strictly an Ethernet adapter,
          however some software packages (such as KA9Q's NET and NCSA







          Telnet) support Serial Line IP (SLIP).  SLIP must be specially
          supported because it doesn't use ARP and has no hardware
          addresses prepended to its packets.  The PDS is not clear on
          this, but the packet driver does the SLIP encoding.
          
          The parameters are as follows.  The -h flag is included if you
          wish to use hardware handshaking (the packet driver will then
          suspend the transmission of characters while CTS is low).  The
          driver_class is the class that is returned to a client of the
          packet driver spec in the driver_info call.  The int_no is the
          hardware interrupt number, defaults to 4 (COM1).  The io_addr
          is the hardware I/O address, defaults to 0x3f8 (COM1).  The
          baud_rate defaults to 4800 baud.  The recv_buf_size defaults to
          3000.
          
          
          EtherSLIP
          
               usage: ethersl [-n] [-d] [-w] packet_int_no [-h] [int_no]
                  [io_addr] [baud_rate] [send_buf_size] [recv_buf_size]
          
               The EtherSLIP driver is a simulated Ethernet adapter.  It
          appears to the application software to be an Ethernet driver,
          but it transmits and receives SLIP packets on the serial line.
          
          The parameters are as follows. The -h flag is included if you
          wish to use hardware handshaking (the packet driver will then
          suspend the transmission of characters while CTS is low).  The
          int_no is the hardware interrupt number, defaults to 4 (COM1).
          The io_addr is the hardware I/O address, defaults to 0x3f8
          (COM1).  The baud_rate defaults to 4800 baud.  The
          send_buf_size and recv_buf_size default to 3000 each.
          
          
          Ungermann-Bass NIC-PC
          
               usage: ubnicpc [-n] [-d] [-w] <packet_int_no> <int_no>
          <base_addr>
          
          The UB NIC-PC driver requires two additional parameters, the
          hardware interrupt number, and the memory base address.
          
          
          Ungermann-Bass NIC-PS/2
          
               usage: ubnicps2 [-n] [-d] [-w] <packet_int_no> <int_no>
          <io_addr> <base_addr>
          
          The UB NIC-PS/2 requires three additional parameters -- the
          hardware interrupt number, the I/O address, and the memory base
          address.  The defaults are the contents of the POS registers, so
          the only time you would need to use the parameters is if you're
          using two NIC-PS/2 boards in one machine.
          
          
          











          Tiara Lancard
          
               usage: tiara [-n] [-d] [-w] packet_int_no [int_no
          [io_addr]]
          
               The Tiara driver runs the Tiara LANCARD/E cards, both
          eight and sixteen bit cards.  The Tiara driver requires two
          additional parameters, the hardware interrupt number, and the
          I/O port.
          
          Western Digital WD8003 E EBT EB ET/A and E/A
          
               usage: WD8003E [-n] [-d] [-w] packet_int_no [-o]
          [int_level [io_addr [mem_base]]]
          
               The WD8003E driver runs the Western Digital E, EBT, EB,
          ET/A, and E/A Ethernet cards.  The WD8003E requires three
          additional parameters -- the hardware interrupt number, the I/O
          address, and the memory base address.  The defaults are 2 and
          0x280 and 0xd000.  The wd8003 cards do not enable their memory
          until configuration time.  Some 386 memory mappers will map
          memory into the area that the card intends to use.  You should
          be able to configure your software to leave this area of memory
          alone.  Also driver will refuse to map memory into occupied
          memory.  The occupied memory test fails on some machines, so the
          optional switch -o allows you to disable the check for occupied
          memory.
          
          
          Errorlevels
          
               Some of the packet drivers return error codes.  Some of
          these error codes indicate fatal errors, and some are merely
          warnings.  For the moment, you must consult the source to see
          what the errorcodes mean.  For example, pktchk returns 0 if a
          packet driver exists at a given address, and 1 if not.  You
          might use it in a batch file that only installs a packet driver
          if one is not found.
          
                  rem only install the packet driver if there isn't one
                  rem already.
                  pktchk 0x7e
                  if errorlevel 0 goto gotit
                  ni5210 0x7e
          
          :gotit
          
               The "errorlevel" test is true if the errorlevel is less
          than or equal to the parameter.
          
          
          Utility Programs
          
               There are also several utility programs for packet
          drivers:
          
          
          









          PKTADDR
          
               usage: pktaddr packet_int_no [ethernet_addr]
          
               If the second argument is given, the Ethernet address of
          the given packet driver is set.  The Ethernet address is printed
          out.
          
          
          PKTALL
          
               usage: pktall packet_int_no
          
               All packets are received and discarded from the given
          packet driver.  This program is of most use with PKTMODE and
          TRACE.
          
          
          PKTCHK
          
               usage: pktchk packet_int_no [packet_int_no]
          
               Test for existance of a packet driver.  Returns with
          errorlevel 0 if the specified interrupt has a packet driver.  If
          the second argument is given, all interrupts in the range are
          checked for a packet driver.  If no packet driver is found at
          all, errorlevel 1 is returned.
          
          
          PKTMODE
          
               usage: pktmode packet_int_no [receive_mode]
          
               If the second argument is given, the receive mode of the
          given packet driver is set.  A decimal number from the list of
          modes should be used.  All the possible modes are printed out.
          Unimplemented modes are marked with "xx", and the current mode
          is marked with "->".
          
          
          PKTMULTI
          
               usage: pktmulti packet_int_no [-f filename | address ...]
          
               The specified addresses are set as allowed multicast
          addresses.  If no list of addresses is given, then the current
          list of addresses is printed.  The
          addresses may either be specified on the command line, or in a
          file using the -f option.  When a file is used, any whitespace
          in the file is ignored.
          
          
          PKTRING
          
               usage: pktring [-m] dest_packet_int_no src_packet_int_no
          
               Test two packet drivers loaded on two Ethernet cards in
          the same machine.  Sends packets of every possible length using
          the driver located at src_packet_int_no to the driver located at
          dest_packet_int_no.  If the -m switch is used, then the various







          receive modes are tested.  Note that the multicast tests (modes
          four and five) do not work properly yet.
          
          
          PKTSTAT
          
               usage: pktstat first_int_no [last_int_no]
          
               The statistics for all packet drivers in the given range
          are printed.  The default range is 0x60 through 0x80.  The
          meanings of the columns are given below.
          
                  
          pkt_in  is the number of packets ever received by this driver.
          pkt_out is the number of packets ever transmitted by this
                  driver.
          byt_in  is the number of bytes ever received by this driver.
          byt_out is the number of bytes ever transmitted by this driver.
          pk_drop Packets dropped because there was no handler for that
                  Ethernet packet type.
          err_in  Dependent upon the packet driver.
          err_out Dependent upon the packet driver.
          
          
          PKTSEND
          
               usage: pktsend packet_int_no [-r] [-f filename | packet]
          
               The specified packet is sent using the specified packet
          driver.  The -r option says to repeat sending as fast as
          possible.  You shouldn't use this option very often.  The packet
          may either be specified on the command line, or in a file using
          the -f option.  When a file is used, any whitespace in the file
          is ignored.
          
          PKTTRAF
          
               usage: pkttraf packet_int_no
          
               Graphically display traffic on an EGA or VGA screen.  The
          first twenty Ethernet addresses encountered are assigned a node
          number. The traffic between each pair of nodes is displayed as a
          line of varying intensity.  When any line reaches maximum
          intensity, the intensities of all lines are halved.
               A cursor highlights one of the nodes.  The Ethernet
          address of the highlighted node is printed in the lower-right
          corner.  The cursor is moved using space and backspace.
          
          TERMIN
          
               usage: termin [-s] packet_int_no
          
               The specified packet driver is terminated, and its memory
          recovered.
          
               The s-option (stop) is used to prepare for termination.
          The in-use flag for all handles are cleared. This prevents
          upcalls to handlers that are to be removed and also makes it
          possible to later terminate the packet driver even though
          handles are not released.  Actually, doing termin -s after prom







          boot is like cutting the branch you are sitting on.  Recipe for
          removing packet driver, IPX and NET:
          
                                          
                  pktdrvr 0x7c ....
                  MARKNET C:IPX&NET3.MRK
                  PDIPX
                  NET3
                  . . .
                  NET3 u                ; unload netx to avoid
                                          communication timeout
                  TERMIN -s 0x7c        ; pkt drvr no longer calls any
                                          nonexistent rcvrs
                  RELNET ipxet3.mrk     ; IPX is "removed"
                  TERMIN 0x7c           ; It is now safe to terminate the
                                          packet driver
          
          
          TRACE
          
               usage: trace packet_int_no [buffer_size]
          
               Trace is very useful for debugging packet driver
          troubles.  Trace lets you trace all transactions between a user
          program and the packet driver.  The transactions are stored in a
          memory buffer whose size is set with buffer_size.  The default
          size is 10,000 bytes.
          
               When you run trace, it sets itself up and then spawns
          COMMAND.COM so that you can run a network program that uses the
          packet driver.  After you quit your network session, you issue
          an "EXIT" command.  This returns you to trace, which writes the
          transaction log to "TRACE.OUT".  The following program, DUMP,
          interprets TRACE.OUT.
          
          
          DUMP
          
               usage: dump
          
               Interprets the contents of TRACE.OUT as written by TRACE.
          
          
          WINPKT
          
               usage: winpkt <new_packet_int_no> <old_packet_int_no>
          
          Provides a Packet Driver interface between Windows 3 Enhanced
          mode applications and a real Packet Driver.  This attempts to
          solve the problem of Windows moving applications around in
          memory willy nilly.  It replaces the -w flag hack.
          
          Install WINPKT after the Packet Driver and before starting
          Windows.
          
          
          










                                     Appendix A
          
          Interrupt usage in the range 0x60 through 0x80, from Ralf
          Brown's interrupt list.
          
                   
                   
          60 -- -- reserved for user interrupt 
          60 -- -- FTP Driver - PC/TCP Packet Driver Specification 
          60 01 FF FTP Driver - DRIVER INFO 
          60 02 -- FTP Driver - ACCESS TYPE 
          60 03 -- FTP Driver - RELEASE TYPE 
          60 04 -- FTP Driver - SEND PACKET 
          60 05 -- FTP Driver - TERMINATE DRIVER FOR HANDLE 
          60 06 -- FTP Driver - GET ADDRESS 
          60 07 -- FTP Driver - RESET INTERFACE 
          60 11 -- 10-NET - LOCK AND WAIT 
          60 12 -- 10-NET - LOCK 
          60 13 -- 10-NET - UNLOCK 
          60 20 -- FTP Driver - SET RECEIVE MODE 
          60 21 -- FTP Driver - GET RECEIVE MODE 
          60 24 -- FTP Driver - GET STATISTICS 
          61 -- -- reserved for user interrupt 
          62 -- -- reserved for user interrupt 
          63 -- -- reserved for user interrupt 
          64 -- -- reserved for user interrupt 
          65 -- -- reserved for user interrupt 
          66 -- -- reserved for user interrupt 
          67 -- -- LIM EMS 
                   ...  
          67 DE 00 Virtual Control Program Interface - INSTALLATION CHECK 
                   ...  
          68 01 -- APPC/PC 
                   ...  
          69 -- -- unused 
          6A -- -- unused 
          6B -- -- unused 
          6C -- -- system resume vector (CONVERTIBLE) 
          6C -- -- DOS 3.2 Realtime Clock update 
          6D -- -- VGA - internal 
          6E -- -- unused 
          6F -- -- Novell NetWare - PCOX API (3270 PC terminal interface) 
          6F 00 -- 10-NET - LOGIN 
                   ...  
          70 -- -- IRQ8 - AT/XT286/PS50+ - REAL-TIME CLOCK 
          71 -- -- IRQ9 - AT/XT286/PS50+ - LAN ADAPTER 1 
          72 -- -- IRQ10 - AT/XT286/PS50+ - RESERVED 
          73 -- -- IRQ11 - AT/XT286/PS50+ - RESERVED 
          74 -- -- IRQ12 - PS50+ - MOUSE INTERRUPT 
          75 -- -- IRQ13 - AT/XT286/PS50+ - 80287 ERROR 
          76 -- -- IRQ14 - AT/XT286/PS50+ - FIXED DISK 
          77 -- -- IRQ15 - AT/XT286/PS50+ - RESERVED 
          78 -- -- not used 
          79 -- -- not used 
          7A -- -- Novell NetWare - LOW-LEVEL API 
          7A -- -- AutoCAD Device Interface 
          7B -- -- not used 
          7C -- -- not used 
          7D -- -- not used 
          7E -- -- not used 







          7F -- -- HDILOAD.EXE - 8514/A VIDEO CONTROLLER INTERFACE 
          7F -- -- HLLAPI (High-Level Language API) 
          80 -- -- reserved for BASIC