Installation instructions for the packet driver collection


          Document conventions

               All numbers in this document are given in C-style
          representation.  Decimal is expressed as 11, hexadecimal is
          expressed as 0x0B, octal is expressed as 013.  All reference to
          network hardware addresses (source, destination and multicast)
          and demultiplexing information for the packet headers assumes
          they are represented as they would be in a MAC-level packet
          header being passed to the send_pkt() function.


          Using the packet drivers

               The packet driver must be installed prior to use.  Since
          each packet driver takes only a few thousand bytes, this is best
          done in your autoexec.bat.  Since the Ethernet boards typically
          have jumpers on board, the packet driver must be informed of the
          values of these jumpers (auto-configure is possible, but can
          disturb other boards).  The first parameter is the software
          interrupt used to communicate with the packet driver.  And
          again, because each board is different, the rest of the
          parameters will be different.

          All parameters must be specified in C-style representation.
          Decimal is expressed as 11, hexadecimal is expressed as 0x0B,
          octal is expressed as 013.  Any numbers that the packet driver
          prints will be in the same notation.

          Before installing the packet driver, you must choose a software
          interrupt number in the range between 0x60 and 0x80.  Some of
          these interrupts are used for other purposes, so your first
          choice may not work.  See Appendix A for the section of Ralf
          Brown's interrupt list between 0x60 and 0x80.

          Running a packet driver with no specifications will give a
          usage message.  The parameters for each packet driver are
          documented below.

          The -n option is used to convert IPX packets between the
          Ethernet II type 8137 encapsulation used by BYU's PDSHELL IPX
          interface code and the 802.3-style encapsulation normally used
          on Ethernet by Netware servers, shells and boot PROMs.  It will
          also convert incoming type 8137 packets to type 8138 so that
          Netware doesn't get confused.

          The -d option is used to delay the initialization of the
          Ethernet card until the packet driver is used for the first
          time.  See PROMBOOT.NOT for how to use -d and -n in a PROM boot
          environment.

          The -w switch is used for Windows.  Install the packet driver
          before running MS-Windows.  This switch does not prevent Windows







          from swapping your network application out of memory, it simply
          detects when that has happened, and drops the packets on the
          floor.

          3Com 3C501

               usage: 3C501 [-n] [-d] [-w] packet_int_no [int_no
          [io_addr]]

               The 3c501 driver requires two additional parameters -- the
          hardware interrupt number and the I/O address.  The defaults are
          3 and 0x300.


          3Com 3C503

               usage: 3C503 [-n] [-d] [-w] packet_int_no [int_level(2-5)
          [io_addr [cable_type]]]

               The 3c503 driver requires three additional parameters --
          the hardware interrupt number, the I/O address, and the cable
          type.  The 3c503 can be attached to thick or thin Ethernet
          cables, and the selection is made in software.  The cable type
          parameter should be zero for thick, and one for thin.  The
          defaults are 2, 0x300, and 1 (thin).  The 3c503 uses shared
          memory whose address is set by jumpers, but the software can ask
          the board what the address is.


          3Com 3c505

               usage: 3c505 [-n] [-d] [-w] packet_int_no [int_no [io_addr
          [base_addr]]]

               The 3c505 driver requires three additional parameters --
          the hardware interrupt number, the I/O address, and the memory
          base address.  The defaults are 2 and 0x300 and 0xd000.


          3Com 3c507

               usage: 3c507 [-n] [-d] [-w] packet_int_no [int_no [io_addr
          [base_addr]]]

               The 3c507 will determine its parameters by reading the
          board.  The only time you would need to specify the parameters
          is when you have multiple 3c507s in the same machine.
               The 3c507 driver will use three additional parameters --
          the hardware interrupt number, the I/O address, and the memory
          base address.







          3Com 3c523

               usage: 3c523 [-n] [-d] [-w] packet_int_no [int_no [io_addr
          [base_addr]]]

               The 3c523 driver requires three additional parameters --
          the hardware interrupt number, the I/O address, and the memory
          base address.  The defaults are 3 and 0x300 and 0xc000.


          ARCNET

               usage: arcnet [-n] [-d] [-w] packet_int_no [int_no [io_addr
          [base_addr]]]

               The ARCNET driver requires three additional parameters --
          the hardware interrupt number, the I/O address, and the memory
          base address.  The defaults are 5 and 0x2e0 and 0xd800.  Note
          that a packet driver client must specifically support ARCNET.
          The only known client is Phil Karn's (KA9Q) networking package,
          NOS.


          AT&T

               usage: at&t [-n] [-d] [-w] packet_int_no [int_no [io_addr
          [base_addr]]]

               The AT&T driver requires three additional parameters --
          the hardware interrupt number, the I/O address, and the memory
          base address.  The defaults are 2 and 0x360 and 0xd000.  This
          driver supports the StarLAN 1, StarLAN 10 NAU, EN100 and StarLAN
          Fiber NAU.


          D-Link DE-600

               usage: de600 [-n] [-d] [-w] packet_int_no

               The D-Link Pocket Lan Adapter packet driver requires no
          additional parameters.


          Digital Equipment Corporation DEPCA

               usage: depca [-n] [-d] [-w] <packet_int_no> [<int_no>
          [<io_addr> [<mem_addr>]]]

               The DEPCA packet driver requires three additional
          parameters -- the hardware interrupt number, the I/O address,
          and the memory base address.  The defaults are 5 and 0x300 and
          0xd000.  The packet driver will resolve the io_addr
          automatically if io_addr is set to '?', e.g.
          depca 0x7e 5 ? 0xd000.






          Mitel Express

               usage: express [-n] [-d] [-w] <packet_int_no> [-n]
          [<driver_class> [<int_no>]]

               The Mitel Express packet driver has one optional switch,
          and two optional parameters. The <driver_class> defaults to
          SLIP, and the <int_no> defaults to 7.  The -n switch instructs
          card to be an NT.  The <driver_class> should be SLIP or a
          number.

          HP EtherTwist/Starlan10/ThinLan

              usage: hppclan [-n] [-d] [-w] packet_int_no [int_no
          [io_addr]]

               The hppclan driver supports 8 and 16 bit HP LAN cards
          based on the National 8390 chip.  Earlier HP LAN cards should
          use the 3Com 3C501 driver.  The hppclan driver requires two
          additional parameters -- the hardware interrupt number and the
          I/O address.  The defaults are 3 and 0x300.  On IBM PS/2
          Microchannel machines, the defaults are read from the PS/2
          configuration NOVRAM and additional parameters are not
          normally required.


          IBM Token Ring

               usage: ibmtoken [-n] [-d] [-w] packet_int_no [adapter_no]

               The IBM Token Ring packet driver requires one additional
          parameters -- the adapter number.  The default is zero.  See
          IBMTOKEN.DOC for more information.


          LocalTalk

               usage: localtlk [-n] [-d] [-w] <packetintno> [<IP address>]

               The LocalTalk packet driver requires atalk.sys to be
          installed.  Because it is not an Ethernet class driver, it
          requires special code in the client.  See LOCALTLK.NOT for more
          details.


          NCR ET-105

               usage: ncret105 [-n] [-d] [-w] <packet_int_no> <int_no>
          <base_addr> <Ethernet_address>

               The NCR ET-105 driver requires four additional parameters
          -- the hardware interrupt number, the I/O address, the memory
          base address, and the Ethernet address.  The Ethernet address
          assigned to any particular board is printed on sticky labels
          that come with the board.







          Novell IPX

               usage: ipxpkt [-n] [-d] [-w] packet_int_no

               The ipxpkt packet driver simulates Ethernet on Novell IPX
          protocol.


          BICC Data Networks' ISOLAN 4110 ethernet

               usage: isolan [-n] [-d] [-w] packet_int_no [int_no
          [base_addr]]

               The BICC Isolan requires three additional parameters --
          the hardware interrupt number and the memory base address.  The
          defaults are 2 and 0xb800h.


          Netbios

               usage: nb [-n] [-d] [-w] packet_int_no ip.ad.dr.ess
          [receive queue size]

               The netbios packet driver transports IP packets over
          NetBIOS.


          Novell ne1000

               usage: ne1000 [-n] [-d] [-w] packet_int_no [int_no
          [io_addr]]

               The ne1000 driver requires two additional parameters --
          the hardware interrupt number and the I/O address.  The defaults
          are 3 and 0x300.


          Novell ne/2

               usage: ne2 [-n] [-d] [-w] <packet_int_no>

               The ne/2 driver requires no additional parameters.


          Novell ne2000

               usage: ne2000 [-n] [-d] [-w] packet_int_no [int_no
          [io_addr]]

               The ne2000 driver requires two additional parameters --
          the hardware interrupt number and the I/O address.  The defaults
          are 2 and 0x300.







          Racal-Interlan (Formerly Interlan) NI5010

               usage: NI5010 [-n] [-d] [-w] packet_int_no [int_no
          [io_addr]]

               The NI5010 driver requires two additional parameters --
          the hardware interrupt number and the I/O address.  The defaults
          are 3 and 0x300.


          Racal-Interlan (Formerly Micom-Interlan) NI5210

               usage: ni5210 [-n] [-d] [-w] packet_int_no [int_no [io_addr
          [base_addr]]]

               The NI5210 driver requires three additional parameters --
          the hardware interrupt number, the I/O address, and the memory
          base address.  The defaults are 2 and 0x360 and 0xd000.  Note
          that Interlan sets the default memory base to 0xa000, which is
          brain-damaged, because that area of memory is specifically
          reserved for video adapters, and in fact the EGA and VGA use
          it.


          Racal-Interlan NI6510

               usage: ni6510 [-n] [-d] [-w] packet_int_no [int_no
          [io_addr]]

               The ni6510 driver has two additional parameters -- the
          hardware interrupt number and the I/O address.  The defaults are
          2 and auto-sense.  These parameters do not need to be set unless
          the auto-sense routine fails, or otherwise disrupts operation of
          your PC.


          Racal-Interlan (Formerly Micom-Interlan) NI9210

               usage: ni9210 [-n] [-d] [-w] packet_int_no [int_no [io_addr
          [base_addr]]]

               The ni9210 driver requires three additional parameters --
          the hardware interrupt number, the I/O address, and the memory
          base address.  The defaults are 2 and 0x360 and 0xd000.


          NTI 16

               usage: nti16 [-n] [-d] [-w] packet_int_no [int_no [io_addr
          [base_addr]]]

               The nti16 driver requires three additional parameters --
          the hardware interrupt number, the I/O address, and the memory
          base address.  The defaults are 3 and 0x338 and 0xd000.







          SLIP8250

               usage: SLIP8250 [-n] [-d] [-w] packet_int_no [-h]
          [driver_class]
                  [int_no]
                  [io_addr] [baud_rate] [send_buf_size] [recv_buf_size]
                  The driver_class should be SLIP, KISS, AX.25, or a
                  number.

               The SLIP8250 driver is not strictly an Ethernet adapter,
          however some software packages (such as KA9Q's NET and NCSA
          Telnet) support Serial Line IP (SLIP).  SLIP must be specially
          supported because it doesn't use ARP and has no hardware
          addresses prepended to its packets.  The PDS is not clear on
          this, but the packet driver does the SLIP encoding.  The
          parameters are as follows.  The -h flag is included if you wish
          to use hardware handshaking (the packet driver will then suspend
          the transmission of characters while CTS is low).  The
          driver_class is the class that is returned to a client of the
          packet driver spec in the driver_info call.  The int_no is the
          hardware interrupt number, defaults to 4 (COM1).  The io_addr is
          the hardware I/O address, defaults to 0x3f8 (COM1).  The
          baud_rate defaults to 4800 baud.  The send_buf_size and
          recv_buf_size default to 3000 each.


          Ungermann-Bass NIC-PC

               usage: ubnicpc [-n] [-d] [-w] <packet_int_no> <int_no>
          <base_addr>

          The UB NIC-PC driver requires two additional parameters, the
          hardware interrupt number, and the memory base address.


          Ungermann-Bass NIC-PS/2

               usage: ubnicps2 [-n] [-d] [-w] <packet_int_no> <int_no>
          <io_addr> <base_addr>

          The UB NIC-PS/2 requires three additional parameters -- the
          hardware interrupt number, the I/O address, and the memory base
          address.  The defaults are the contents of the POS registers, so
          the only time you would need to use the parameters is if you're
          using two NIC-PS/2 boards in one machine.


          Tiara Lancard

               usage: tiara [-n] [-d] [-w] packet_int_no [int_no
          [io_addr]]

               The Tiara driver runs the Tiara LANCARD/E cards, both
          eight and sixteen bit cards.  The Tiara driver requires two
          additional parameters, the hardware interrupt number, and the







          I/O port.

          Western Digital WD8003 E EBT EB ET/A and E/A

               usage: WD8003E [-n] [-d] [-w] packet_int_no [-o]
          [int_level [io_addr [mem_base]]]

               The WD8003E driver runs the Western Digital E, EBT, EB,
          ET/A, and E/A Ethernet cards.  The WD8003E requires three
          additional parameters -- the hardware interrupt number, the I/O
          address, and the memory base address.  The defaults are 2 and
          0x280 and 0xd000.  The wd8003 cards do not enable their memory
          until configuration time.  Some 386 memory mappers will map
          memory into the area that the card intends to use.  You should
          be able to configure your software to leave this area of memory
          alone.  Also driver will refuse to map memory into occupied
          memory.  The occupied memory test fails on some machines, so the
          optional switch -o allows you to disable the check for occupied
          memory.


          Errorlevels

               Some of the packet drivers return error codes.  Some of
          these error codes indicate fatal errors, and some are merely
          warnings.  For the moment, you must consult the source to see
          what the errorcodes mean.  For example, pktchk returns 0 if a
          packet driver exists at a given address, and 1 if not.  You
          might use it in a batch file that only installs a packet driver
          if one is not found.

                  rem only install the packet driver if there isn't one
                  rem already.
                  pktchk 0x7e
                  if errorlevel 0 goto gotit
                  ni5210 0x7e
          :gotit

               The "errorlevel" test is true if the errorlevel is less
          than or equal to the parameter.


          Utility Programs

               There are also several utility programs for packet
          drivers:


          PKTADDR

               usage: pktaddr packet_int_no [ethernet_addr]

               If the second argument is given, the Ethernet address of
          the given packet driver is set.  The Ethernet address is printed
          out.







          PKTALL

               usage: pktall packet_int_no

               All packets are received and discarded from the given
          packet driver.  This program is of most use with PKTMODE and
          TRACE.


          PKTCHK

               usage: pktchk packet_int_no [packet_int_no]

               Test for existance of a packet driver.  Returns with
          errorlevel 0 if the specified interrupt has a packet driver.  If
          the second argument is given, all interrupts in the range are
          checked for a packet driver.  If no packet driver is found at
          all, errorlevel 1 is returned.


          PKTMODE

               usage: pktmode packet_int_no [receive_mode]

               If the second argument is given, the receive mode of the
          given packet driver is set.  A decimal number from the list of
          modes should be used.  All the possible modes are printed out.
          Unimplemented modes are marked with "xx", and the current mode
          is marked with "->".


          PKTMULTI

               usage: pktmulti packet_int_no [-f filename | address ...]

               The specified addresses are set as allowed multicast
          addresses.  If no list of addresses is given, then the current
          list of addresses is printed.  The
          addresses may either be specified on the command line, or in a
          file using the -f option.  When a file is used, any whitespace
          in the file is ignored.


          PKTSTAT

               usage: pktstat first_int_no [last_int_no]

               The statistics for all packet drivers in the given range
          are printed.  The default range is 0x60 through 0x80.  The
          meanings of the columns are given below.


          pkt_in  is the number of packets ever received by this driver.
          pkt_out is the number of packets ever transmitted by this
                  driver.







          byt_in  is the number of bytes ever received by this driver.
          byt_out is the number of bytes ever transmitted by this driver.
          pk_drop Packets dropped because there was no handler for that
                  Ethernet packet type.
          err_in  Dependent upon the packet driver.
          err_out Dependent upon the packet driver.


          PKTSEND

               usage: pktsend packet_int_no [-r] [-f filename | packet]

               The specified packet is sent using the specified packet
          driver.  The -r option says to repeat sending as fast as
          possible.  You shouldn't use this option very often.  The packet
          may either be specified on the command line, or in a file using
          the -f option.  When a file is used, any whitespace in the file
          is ignored.

          PKTRING

               usage: pktring [-m] dest_packet_int_no src_packet_int_no

               Test two packet drivers loaded on two Ethernet cards in
          the same machine.  Sends packets of every possible length using
          the driver located at src_packet_int_no to the driver located at
          dest_packet_int_no.  If the -m switch is used, then the various
          receive modes are tested.  Note that the multicast tests (modes
          four and five) do not work properly yet.


          TERMIN

               usage: termin [-s] packet_int_no

               The specified packet driver is terminated, and its memory
          recovered.

               The s-option (stop) is used to prepare for termination.
          The in-use flag for all handles are cleared. This prevents
          upcalls to handlers that are to be removed and also makes it
          possible to later terminate the packet driver even though
          handles are not released.  Actually, doing termin -s after prom
          boot is like cutting the branch you are sitting on.  Recipe for
          removing packet driver, IPX and NET:







                  pktdrvr 0x7c ....
                  MARKNET C:IPX&NET3.MRK
                  PDIPX
                  NET3
                  . . .
                  NET3 u                ; unload netx to avoid
                                          communication timeout
                  TERMIN -s 0x7c        ; pkt drvr no longer calls any
                                          nonexistent rcvrs
                  RELNET ipxet3.mrk     ; IPX is "removed"
                  TERMIN 0x7c           ; It is now safe to terminate the
                                          packet driver


          TRACE

               usage: trace packet_int_no [buffer_size]

               Trace is very useful for debugging packet driver
          troubles.  Trace lets you trace all transactions between a user
          program and the packet driver.  The transactions are stored in a
          memory buffer whose size is set with buffer_size.  The default
          size is 10,000 bytes.

               When you run trace, it sets itself up and then spawns
          COMMAND.COM so that you can run a network program that uses the
          packet driver.  After you quit your network session, you issue
          an "EXIT" command.  This returns you to trace, which writes the
          transaction log to "TRACE.OUT".  The following program, DUMP,
          interprets TRACE.OUT.


          DUMP

               usage: dump

               Interprets the contents of TRACE.OUT as written by TRACE.







                                     Appendix A

          Interrupt usage in the range 0x60 through 0x80, from Ralf
          Brown's interrupt list.



          60 -- -- reserved for user interrupt
          60 -- -- FTP Driver - PC/TCP Packet Driver Specification
          60 01 FF FTP Driver - DRIVER INFO
          60 02 -- FTP Driver - ACCESS TYPE
          60 03 -- FTP Driver - RELEASE TYPE
          60 04 -- FTP Driver - SEND PACKET
          60 05 -- FTP Driver - TERMINATE DRIVER FOR HANDLE
          60 06 -- FTP Driver - GET ADDRESS
          60 07 -- FTP Driver - RESET INTERFACE
          60 11 -- 10-NET - LOCK AND WAIT
          60 12 -- 10-NET - LOCK
          60 13 -- 10-NET - UNLOCK
          60 20 -- FTP Driver - SET RECEIVE MODE
          60 21 -- FTP Driver - GET RECEIVE MODE
          60 24 -- FTP Driver - GET STATISTICS
          61 -- -- reserved for user interrupt
          62 -- -- reserved for user interrupt
          63 -- -- reserved for user interrupt
          64 -- -- reserved for user interrupt
          65 -- -- reserved for user interrupt
          66 -- -- reserved for user interrupt
          67 -- -- LIM EMS
                   ...
          67 DE 00 Virtual Control Program Interface - INSTALLATION CHECK
                   ...
          68 01 -- APPC/PC
                   ...
          69 -- -- unused
          6A -- -- unused
          6B -- -- unused
          6C -- -- system resume vector (CONVERTIBLE)
          6C -- -- DOS 3.2 Realtime Clock update
          6D -- -- VGA - internal
          6E -- -- unused
          6F -- -- Novell NetWare - PCOX API (3270 PC terminal interface)
          6F 00 -- 10-NET - LOGIN
                   ...
          70 -- -- IRQ8 - AT/XT286/PS50+ - REAL-TIME CLOCK
          71 -- -- IRQ9 - AT/XT286/PS50+ - LAN ADAPTER 1
          72 -- -- IRQ10 - AT/XT286/PS50+ - RESERVED
          73 -- -- IRQ11 - AT/XT286/PS50+ - RESERVED
          74 -- -- IRQ12 - PS50+ - MOUSE INTERRUPT
          75 -- -- IRQ13 - AT/XT286/PS50+ - 80287 ERROR
          76 -- -- IRQ14 - AT/XT286/PS50+ - FIXED DISK
          77 -- -- IRQ15 - AT/XT286/PS50+ - RESERVED
          78 -- -- not used
          79 -- -- not used
          7A -- -- Novell NetWare - LOW-LEVEL API







          7A -- -- AutoCAD Device Interface
          7B -- -- not used
          7C -- -- not used
          7D -- -- not used
          7E -- -- not used
          7F -- -- HDILOAD.EXE - 8514/A VIDEO CONTROLLER INTERFACE
          7F -- -- HLLAPI (High-Level Language API)
          80 -- -- reserved for BASIC