43

NAME
     43  -  EGA 43 line emulator for Hercules.          (Version 1.0)


SYNOPSIS
     43 [options] <command>

     <command> is the usual command used to start a program in 25 line
     mode.


DESCRIPTION
     43 emulates the 43 line textmode of an EGA Card on a Hercules
     Graphic Card (HGC).

     43 is purposive for text editing with ascii-editors.

     This program uses the graphic mode of the Hercules Card to dis-
     play the text. Cause the bios is skipped by most programs, the
     solution is to copy the textscreen periodically to the graphic-
     screen. This slows down the computing speed much, but there is
     still enough efficiency to edit textfiles. With many programs,
     switching between 25 and 43 lines is possible. In 25 line mode
     the computing speed is not slowed down.


OPTIONS
     -i         Invert the screen. By default characters are displayed
                white on black. This option displays characters black
                on white.

     -f<name>   path to specify another fontfile. By default the font
                43.fnt from the program directory is used.

     -m1        support serial mouse at COM1.
                43 refreshes the graphicscreen in the timerinterrupts.
                During this periods, all interrupts are disabled and
                input from serial ports is lost. If you select this
                option, the program checks the serial port. If there
                is new data, repainting the screen is stopped and the
                serial line can be served. If you move your mouse lon-
                ger, screenrefresh only affects the line containing
                the mousecursor.

             !! This option requires an installed Microsoft compatible
                mousedriver, to determine the line of the mousecursor.
                If there is no mousedriver installed the computer will
                hang.

     -m2        same as -m1 except for COM2.

     -s<nn>     redraw nn lines per timertick (1<nn<43) (default:13)

                The default value 13 means 13 line are repainted per
                timertick. This affects a complete screenrefresh 5.4
                times a second. If you increase this value the screen
		is refreshed faster, but the computer slows down.

     -t         start in 25-line textmode. Whithout this option, the
                display starts in 43-line mode.


REQUIREMENTS
     An AT-286 or AT-386 (of course 200% compatible) with at least
     10 Mhz and a Hercules Graphics Card with 64 KB of memory (2 pages).
     This program wastes less than 30 KB of memory.


EXAMPLE
     43 C:\COMMAND   Load a secondary command.com.
     43 -m1 tc       Start Turbo-C in 43 line mode, support mouse at
                     COM1. If you want to use this program with Turbo-
                     C++ 1.0 you must explicit set 43-line mode with
                     TCINST. Switching between 25 and 43 line in TC is
                     not possible (I don't know, how tc recognizes the
                     EGA; any help appreciated).


USING 43 WITH A DOS SHELL
     If you start a DOS shell with 43, the screen will still scroll with
     only 25 lines of text. You can use 43 lines with ZANSI.SYS (a faster
     ansi.sys replacement, look at your BBS) which supports switching
     between 25 and 43 line mode. This switching will be done by the
     two batchfile SET43.BAT and SET25.BAT.


FILES
     43.exe          the emulator
     43.fnt          the default font (same directory as 43.exe)


SEE ALSO
     hmode.exe, egafont.exe


BUGS
     Changing cursorsize is not supported.

     Only normal and inverted text attributes can be displayed. If the
     color-attribute of the mouse cursor is not black on white, the
     cursor might be invisible.

     Mouse motion in vertical direction creates ghost cursors until
     motion is stopped.
     

TECHNICAL NOTES
     The program simulates parts of an EGA BIOS. Text is diplayed in
     monochrome mode 7 with video memory starting at Segment b000h.
     Most programs don't require that the video buffer of an EGA starts
     at segment b800h as used in video modes 2 and 3.
     This program uses the timer interrupt. Cause this, interrupts are
     disabled long times. To avoid problems with disk/harddisk access,
     interrupt 13h is watched to stop refreshing the screen during
     diskette operations.
     Programs which have time-critical routines should not be used
     with this program. For example communication programs will loose
     incoming data.

  !! Be carefull with software which direct accesses the floppy/hard-
     disk controller (might be some backup programs, disk utilities).
  !! Be carefull with cache programs that do staged write-cache. These
     programs also use the timerinterrupt.


COPYRIGHT
     Torsten Bachmann                                  Feb' 1991
     Dr. H. Kapfingerstr. 13 A213
     8390 Passau
     GERMANY

     Internet: bachmann@fmi.uni-passau.de