BETA RELEASE OF OS/2 COMMUNICATION DRIVERS


    COM.SYS          08-10-92
    VCOM.SYS       08-07-92
    COMM.DRV      06-11-92
    MODE.COM      08-06-92


    IBM DISCLAIMS ALL WARRANTIES, WHETHER EXPRESSED OR IMPLIED, INCLUDING
    WITHOUT LIMITATION, WARRANTIES OF FITNESS AND MERCHANTABILITY WITH
    RESPECT TO THE INFORMATION IN THIS DOCUMENT AND INCLUDED SOFTWARE
    PRODUCTS.  . BY FURNISHING THIS MATERIAL, IBM GRANTS NO LICENSES TO ANY
    RELATED PATENTS OR COPYRIGHTS.

    Copyright IBM Corporation, 1992, all rights reserved.


    1.0       INSTALLATION PROCEDURE

                    a.      The following files will be replaced:

                             x:\OS2\COM.SYS
                             x:\OS2\MODE.COM
                             x:\OS2\MDOS\VCOM.SYS
                             x:\OS2\MDOS\WINOS2\SYSTEM\COMM.DRV

                            These files will be backed up with the extension *.392.  If 
                            files with this extension already exist, then NO BACKUP will 
                            take place.  The installation utility is assuming that you are 
                            using IBM OS/2 2.0 GA release drivers.  

                     b.    Switch to the drive and directory where the BETA files are
                            located.

                     c.     Enter "cominst  x:" at the command line where
                             x: is the drive letter of the OS/2 Partition.

                     d.     To DE-Install the BETA drivers communication driver, Enter 
                             DEINSTL x: where x: is the drive letter of the OS/2 Partition.

    2.0      DESCRIPTION OF DRIVERS

                    The following is a brief description of the BETA
                    communication drivers for OS/2 2.0.  There are new
                    parameters for the COM.SYS which is located in the
                    CONFIG.SYS file.

    2.1      COM.SYS

                    COM.SYS now has new parameters to indicate the COM port
                    number, the I/O address, the UNIQUE IRQ level and  how to
                    handle spurious interrupts.   An example follows:

                    DEVICE=C:\OS2\COM.SYS (n,xxxx,ii,s) [(n,xxxx,ii,s)]...

                    where the last parameter is optional.







                    n         :   COM port number (usually 3 and 4 but it is
                                   possible to configure any communication port to a
                                   differrent IRQ or I/O Address

                     xxxx   :  COM port address

                     ii         :  IRQ level

                     s         :  Spurious interrupt handling switch
                                   values:

                                   D or d   to deinstall COM driver if
                                                 more than 1000 consecutive
                                                 spurious interrupts occur.

                                    I or i     to ignore spurious interrupt.

                                    P or p  to post error if more than 1000
                                                 consecutive interrupts occur.   When 
                                                 posting an  error, some DOS applications 
                                                 can hang.


                    COM.SYS also has the following fixes:

                    1. COM.SYS now uses a different algorithm to test for he presence of a 
                        communications port at the given address.  There were certain cases 
                        where a port was not recognized.

                    2. Change from DevHlp EOI to writing port 0x20 to
                         reduce interrupt pass.  (Possible performance
                         improvement).

                    3. Better checking of FIFO.

                    4. COM.SYS does not detect Hayes ESP card so that Hayes
                        ESP card can be used as a regular dual asynch card.

                    5. New DOS_SETTING Propertys :  COM_DIRECT_ACCESS removes the IO hook of 
                       VCOM.SYS after check the access control.  If the application only 
                       works  when  VCOM.SYS is not loaded, COM_DIRECT_ACCESS will help the
                       problem.  When COM_DIRECT_ACCESS is on, any application which 
                       requires the presence of VCOM.SYS will not work in the DOS session.  
                       This VCOM.SYS requires the new COM.SYS.  The COM_SELECT setting will 
                       "hide" communication ports from certain DOS applications which try to 
                       control all the communication ports (See Below).  


    2.2      VCOM.SYS

                        No parameters or settings required.  This version of VCOM.SYS should 
                        work better with X00.SYS (and other similar applications) when 
                        COM_DIRECT_ACCESS is ON.  COMDD.SYS (which is required by older DOS 
                        applications such as BASIC) should also perform better.  COMMDD.SYS 
                        is loaded into the DOS_DEVICE setting for a Virtual Dos Machine.  









    2.2.1    COM_DIRECT_ACCESS DOS property

                        When COM_DIRECT_ACCESS is ON, VCOM.SYS will allow a DOS application 
                        to access the communication ports directly.  This DOS property makes 
                        LapLink III, FaskLynx, FSDUAT, AS/400 Asynch Router, MS WORD work in 
                        VDM session.  However, since the buffers in COM.SYS cannot be used, 
                        characters may be lost and and some applications may suffer from the 
                        lack of buffering.  With most DOS applications, COM_DIRECT_ACCESS 
                        should be set to OFF as its default setting.  


    2.2.2    COM_SELECT DOS Property

                        COM_SELECT allows the DOS session to select only one communication 
                        port to be used by the session.  The communication ports which are 
                        not selected will be hidden from the DOS session.  There are some 
                        DOS applications which take over every available communication port.  
                        This DOS property is effective in preventing those DOS applications 
                        from taking over all the communication ports.  An example of a DOS 
                        application which attempts to control all the communcication ports 
                        is LapLink Pro.  If LapLink Pro and another application which 
                        accesses a communication port are executed at the same time, it is 
                        necessary to set COM_SELECT.  The default setting is ALL.


    2.3      COMM.DRV

                       COMM.DRV contains the support for COM3 and COM4 in WinOS2.  This 
                       COMM.DRV requires the new VCOM.SYS.