Documentation for IFC routines.
-------------------------------
Source file(s)	: ifc.c
Include file(s)	: ifc.h
Library			: tools.lib

The routines contained in IFC.C are designed to simplify reading from, and
writing to, the parallel ports in order to use them for simple interfacing
circuits.

===============================================================================

Function		int IFCset(int portnum)
Prototype in	ifc.h

	Sets the current port to portnum. Portnum can range from 0 to 3, with 0
	being LPT1, and 3 being LPT4.

Returns			FALSE if an invalid printer port is specified, TRUE otherwise.

-------------------------------------------------------------------------------

Function		int16 IFCout(uint8 val)
Prototype in	ifc.h

	Outputs the 8 bits of val to the current port.

Returns			the value ouput, or -1 if the current port is invalid.

-------------------------------------------------------------------------------

Function		int16 IFCin()
Prototype in	ifc.h

	Reads 8 bits of data from the current port.

Returns			the value read, or -1 if the current port is invalid.

===============================================================================

General notes :
---------------

Beginning at location 0040:0008 is a block of 8 bytes. These are arranged as
4 words, 1 for each of the ports LPT1 to LPT4. If this word is 0, the corres-
ponding port is invalid, otherwise the word contains the base I/O address of
the port. Starting from this base addresss are 3 locations of interest.

At [base+0] is an 8-bit latch leading to pins 2-9 on the connector. There is
also a tri-state buffer reverse-connected across this latch, so that reading
this address will return the current states of pins 2-9. Unfortunately, that
does not mean these pins can be used for input, as the latch is not open-
collector. However, this feature is useful for verifying that written data has
actually made it to the hardware.

At [base+1] is an I/O chip, of which bits 3-7 are useful. This chip can
only be used for inputting data. Bits 3-6 will read as 0 if the appropriate
pin is at GND relative to pin 25, or 1 if the pin is at +5v. However, bit 7
is inverted - It will read 0 if pin 11 is at +5v and 1 if it's at GND.

At [base+2] is another chip, of which bits 0-3 can be read or written. This
chip is a set of open-collector output transistors, with tri-state buffers
reverse-connected to enable reading. Bits 0, 1 and 3 are inverted. A 1 in the
bit position will produce GND on the appropriate pin, while a 0 will produce
a floating (+5v) value. Bit 2 will produce +5v if it's 1, or a floating GND
if it's 0.

This gives a total of 17 bits which can be played with, as follows :

Offset	bit		Pin		Direction
0		0		2		Output
0		1		3		Output
0		2		4		Output
0		3		5		Output
0		4		6		Output
0		5		7		Output
0		6		8		Output
0		7		9		Output
1		3		15		Input
1		4		13		Input
1		5		12		Input
1		6		10		Input
1		7		11		Input		Inverted
2		0		 1		Either		Inverted
2		1		14		Either		Inverted
2		2		16		Either
2		3		17		Either		Inverted

As written, my functions use the first 8 bits (Offset 1, 3-7 and Offset 2, 0-2)
as input pins. This gives us a total of 8 inputs and 8 outputs (from Offset 0).
I figured this was a good balance, and it shouldn't be too hard to write some
routines for any other configuration. Some possibly useful configurations
would be :

12 outputs, 5 inputs,
8 outputs,  9 inputs, or
9 outputs,  8 inputs.

WARNING : You should be careful not to change any bits in these locations
other than the necessary ones. I can't remember what they do. Also, Bits 0-3
of Offset 2 terminate at open-collector ouputs on the chip. If you're going
to use these for inputs, you need to make sure you don't short them to +5v
while they are latched at Gnd. However, the other way is quite okay. The safest
bet is to only connect up gear which shorts them to ground, or leaves them Open
circuit. They have pullup resistors internal to them, and if left floating will
quite happily show a '1'.This will prevent damage to the chip, then all you
have to remember is to write them correct value to each of these bits before
doing any reading from them. This makes sure the outputs are not S/C to ground
by the chip itself. If this doesn't make sense, the following suggested
connection diagram might help.

              PC               |                Your Gear
                               |
              +5v              |
               |               |
               Z resistor      |
               |---------------------- SWITCH
              |/               |         |
Bit 0-3   ----|                |         |
              |\               |        Gnd
               |               |
               |               |
              Gnd              |
                               |

Here's the pin to port/bit assignments.

Pin		IFCallout	IFCallin	IFCout	IFCin	Port/Bit	Direction
-----------------------------------------------------------------------------
 1		   8		   0				  0		   2/0		Both
 2		   0					  0				   0/0		Out
 3		   1					  1				   0/1		Out
 4		   2					  2				   0/2		Out
 5		   3					  3				   0/3		Out
 6		   4					  4				   0/4		Out
 7		   5					  5				   0/5		Out
 8		   6					  6				   0/6		Out
 9		   7					  7				   0/7		Out
10					   7				  6		   1/6		In
11					   8				  7		   1/7		In
12					   6				  5		   1/5		In
13					   5				  4		   1/4		In
14		   9		   1				  1		   2/1		Both
15					   4				  3		   1/3		In
16		  10		   2				  2		   2/2		Both
17		  11		   3						   2/3		Both
-----------------------------------------------------------------------------

Here's the normal pin functions for a printer port.

Pin		Function at PC					Pin		Function at PC
-----------------------------------------------------------------------------
 1		Strobe out						14		Auto LF out
 2		D0 out							15		Fault in
 3		D1 out							16		Init out
 4		D2 out							17		Select out
 5		D3 out							18		Gnd
 6		D4 out							19		Gnd
 7		D5 out							20		Gnd
 8		D6 out							21		Gnd
 9		D7 out							22		Gnd
10		ACK in							23		Gnd
11		Busy in							24		Gnd
12		Paper End in					25		Gnd
13		Select in
-----------------------------------------------------------------------------