Documentation for music routines
--------------------------------
Source file(s)	: music.c
Include file(s)	: music.h
Library			: tools.lib

The music routines enable sound to be played through the normal PC speaker.
The first routine emulates the standard BASIC "play" command, with single
note output, while the other two routines enable 3-voice polyphonic music
to be played from a file in a special format.

===============================================================================

Function		void play(char *s)
Prototype in	music.h

	Plays notes from the character string s. S should contain a sequence of
	commands, optionally followed by a single digit argument, as follows :

	Command		Argument	Function
	A-G			1-9			Play the note, set the length for this note only
							if the argument is present.
	T			0-9			Set the tempo from 0 (fastest) to 9 (slowest).
	L			1-9			Set the default note length from 1 (full note) to
							9 (1/256th note).
	O			1-9			Set the octave from 0 (lowest) to 9 (highest).
	@			filename	Continue getting commands from the specified file.
							Unless this is the last command in the string, the
							argument should be terminated by another '@'. The
							file can contain multiple lines, and can contain
							another '@' command. '@'s can be nested until you
							run out of memory.

Returns			Nothing

-------------------------------------------------------------------------------

Function		void tri(short tune)
Prototype in	music.h

	Takes an array of 'short', and plays it. Each element in the array must
	be at least 16 bits long. The highest 3 bits represent the Command, and
	the lowest 13 bits represent the Value. The commands are as follows :

	000		End-Of-Tune
	001		Delay for Value, then play Voices 1,2 & 3
	010		Change Tempo to Value
	011		Ignore this Value
	100		Set Pitch for Voice 1
	101		Set Pitch for Voice 2
	110		Set Pitch for Voice 3
	111		Set Pitch for Voice 3

	Note that this is only my best guess at how this thing really works.
	Take it with a pinch of salt.

Returns			Nothing

-------------------------------------------------------------------------------

Function		char *mplay(char *name)
Prototype in	music.h

	This function uses tri() to play a tune stored in a file. The file has a
	default extension of ".POL", and should contain a series of integers
	seperated by blanks or newlines. Each of the integers should be in the
	format specified for tri().

Returns			pointer to the name of the file played.

===============================================================================

General notes :
---------------

mplay() was written by Mike Talvola, of Agoura Hills CA, and placed in the
public domain. I used it here virtually unchanged.

tri() was written by A. Bogatyrev, of Moscow, and placed in the public domain.
Again, I used it here virtually unchanged.

play() was written by myself, and is placed in the public domain, although I
retain full copyrights.